# Installing and Starting the SPU HLSW (ANB on 31.08.04)

# (PACS-TW-TN-015)

#### EEPROM

To install and start the HLSW from SPU EEPROM, please follow these steps:

  - Use the TC packets loader tool (from IFSI-Gavazzi) to load SPU SW TC packets dedicated for EEPROM (Commands to SPU SUSW). These TC packets are uploaded, then, for both SPUs.

  - Running confidence check on EEPROM(Commands to SUSW) and comparing to checksums Table on SW User Manual.

  - Copy the program from EEPROM to RAM (3 Commands to SPU SUSW) as follows:

Command 1: startfunc command to copy runtime header segment from EEPROM to PRAM

Command ID (2 Bytes):	0x04

Spare (2 Bytes):	0x00

Activity ID (2 Bytes):	0x65   (Load SPU_ASW from EEPROM)

SID (2 Bytes):	0x05

Parameter1 (4 Bytes):	0x03   (Memory ID for EEPROM)

Parameter2 (4 Bytes):	0x100   (Start address of SPU_ASW in EEPROM)

Parameter3 (4 Bytes):	0x01   (Memory ID for PRAM)

Parameter4 (4 Bytes):	0x100   (Start address in target RAM)

Parameter5 (4 Bytes):	0x1E0   (Length of SAUs to transfer referred to target Memory)

Command 2: startfunc command to copy initialisation segment from EEPROM to PRAM

Command ID (2 Bytes):	0x04

Spare (2 Bytes):	0x00

Activity ID (2 Bytes):	0x65   (Load SPU_ASW from EEPROM)

SID (2 Bytes):	0x05

Parameter1 (4 Bytes):	0x03   (Memory ID for EEPROM)

Parameter2 (4 Bytes):	0x300   (Start address of SPU_ASW in EEPROM)

Parameter3 (4 Bytes):	0x01   (Memory ID for PRAM)

Parameter4 (4 Bytes):	0x300   (Start address in target RAM)

Parameter5 (4 Bytes):	0x700   (Length of SAUs to transfer referred to target Memory)

Command 3: startfunc command to copy program memory code from EEPROM to PRAM

Command ID (2 Bytes):	0x04

Spare (2 Bytes):	0x00

Activity ID (2 Bytes):	0x65   (Load SPU_ASW from EEPROM)

SID (2 Bytes):	0x05

Parameter1 (4 Bytes):	0x03   (Memory ID for EEPROM)

Parameter2 (4 Bytes):	0xA00   (Start address of SPU_ASW in EEPROM)

Parameter3 (4 Bytes):	0x01   (Memory ID for PRAM)

Parameter4 (4 Bytes):	0xA00   (Start address in target RAM)

Parameter5 (4 Bytes):	0xA600 (Length of SAUs to transfer referred to target Memory)

  - Running confidence check on RAM (Commands to SUSW) and comparing to checksums Table on SW User Manual.

  - Starting the HLSW

One command should be sent to the SPU SUSW

Command ID (2 Bytes):	0x04

Spare (2 Bytes):	0x00

Activity ID (2 Bytes):	0x66   (Give the control to SPU_ASW)

SID (2 Bytes):	0x02

Parameter1 (4 Bytes):	0x01   (Memory ID for PRAM)

Parameter2 (4 Bytes):	0xA02   (Start address in RAM of the SPU_ASW)

(	The SPU starts sending HK after establishing connection with DPU.

#### RAM

To install and start the HLSW from SPU RAM, please follow these steps:

- Use the TC packets loader tool (from IFSI-Gavazzi) to load SPU SW TC packets dedicated for RAM (Commands to SPU SUSW). These TC packets are uploaded, then, for both SPUs.

- Running confidence check on RAM (Commands to SUSW) and comparing to checksums Table on SW User Manual.

- Starting the HLSW

One command should be sent to the SPU SUSW

Command ID (2 Bytes):	0x04

Spare (2 Bytes):	0x00

Activity ID (2 Bytes):	0x66   (Give the control to SPU_ASW)

SID (2 Bytes):	0x02

Parameter1 (4 Bytes):	0x01   (Memory ID for PRAM)

Parameter2 (4 Bytes):	0xA02   (Start address in RAM of the SPU_ASW)

(	The SPU starts sending HK after establishing connection with DPU.

- Copying the HLSW from RAM to EEPROM (Command to HLSW: copy data from RAM to EEPROM)

Command ID (2 Bytes):	0x04

Spare (2 Bytes):	0x00

Activity ID (2 Bytes):	0x04  (CP_DATA_RAM_EEPROM)

SID (2 Bytes):	0x05

Parameter1 (4 Bytes):	spare

Parameter2 (4 Bytes):	0x01   (Memory ID for PRAM)

Parameter3 (4 Bytes):	0x100  (Start Address in PRAM)

Parameter4 (4 Bytes):	0xE0100  (Start address in EEPROM)

Parameter5 (4 Bytes):	0x16B00   (Data Length in 16bit words)

- It is recommended to send this copy command for SPU stopped mode (no compression).

- All modifications via write commands are not recorded in the EEPROM SW copy.

- Modifications via generic load commands in program memory might be recorded in the EEPROM SW copy. However, all HLSW versions do not load into program memory.

- Running the confidence check on EEPROM could only be performed while SUSW has handover SPU.