# HERSCHEL/PACS

# SPU High Level Software To DPU

# Interface Description

# Document Ref.: PACS-TW-ID-001

# Issue: 6.0

# Distribution Record

| Issue / Revision | Draft 0 | Draft 1 | Draft 2 | 1 | 1.1 | 1.2 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Distribution Date | 10.05.2000 | 06.07.2000 | 16.08.2000 | 19.01.2001 | 16.03.2001 | 23.05.2001 | 02.07.2001 |
| Issue / Revision | 2.1 | 3 | 3.1 | 3.2 | 3.3 | 3.4 | 4.0 |
| Distribution Date | 27.08.2001 | 07.09.2001 | 05.10.2001 | 23.10.2001 | 22.01.2002 | 03.04.2002 | 11.09.2002 |
| Issue / Revision | 4.1 | 4.2 | 4.3 | 4.4 | 4.5 | 4.6 | 5.0 |
| Distribution Date | 25.03.2003 | 30.04.2003 | 14.05.2003 | 28.05.2003 | 03.07.2003 | 29.07.2003 | 29.03.2004 |
| Issue / Revision | 5.1 | 6.0 |  |  |  |  |  |
| Distribution Date | 16.04.2004 | 14.12.2005 |  |  |  |  |  |

| INTERNAL | EXTERNAL |
| --- | --- |
| Department | Name | Qty | Company | Name | Qty |
| UVIE/ASTRO | F. Kerschbaum | 1 | MPE | H. Feuchtgruber | 1 |
| UVIE/ASTRO | R.Ottensamer | 1 |  |  |  |
|  |  |  | CSL |  | 0 |
|  |  |  | IAC |  | 0 |
|  |  |  | IFSI | R. Orfei, S. Pezzuto | 1 |
|  |  |  | MPE | PACS Project Office (pacs@mpe.mpg.de) PACS Warm Electronic (pacs-we@ster.kuleuven.ac.be) | 1 |
|  |  | Electronic Archives at Leuven http://pacs.ster.kuleuven.ac.be | 1 |

# Document Change Record

| Document Title HERSCHEL – PACS SPU HLSW to DPU Interface Description |
| --- |
| Issue | Date | Reason for Change |
| Draft 0 | 09/05/2000 | Initial issue |
| Draft 1 | 06/07/2000 | Discussions in PACS OBS#2 + Comments |
| Draft 2 | 16/08/2000 | Comments from IFSI CSL and Discussions in MPE |
| 1 | 16/01/2001 | Discussions with MPE and IFSI and document structure update |
| 1.1 | 16/03/2001 | Comments from OBS#4 |
| 1.2 | 22/05/2001 | Comments from HLSW meeting in Vienna |
| 2 | 28/06/2001 | Comments from OBS#5 |
| 2.1 | 15/08/2001 | Adapted to the new PS-ICD |
| 3 | 31/08/2001 | Comments from IFSI and MPE |
| 3.1 | 03/10/2001 | Comments from OBS#6 |
| 3.2 | 19/10/2001 | Comments from MPE and IFSI |
| 3.3 | 17/01/2002 | See ECPs N°: ECP-020101, ECP-020102, ECP-020103, ECP-020104, ECP-020105, ECP-020106, ECP-020107, ECP-020108, ECP-020109, ECP-020110, ECP-020111, ECP-020110, ECP-020112, ECP-020113 and ECP-020114 |
| 3.4 | 19/03/2002 | See ECPs N°: ECP-020301, ECP-020302, ECP-020303, ECP-020304, ECP-020305 and ECP-020306 |
| 4.0 | 11/09/2002 | See Attached ECPs |
| 4.1 | 25/03/2003 | See Attached ECPs |
| 4.2 | 30/04/2003 | See Attached ECPs |
| 4.3 | 14/05/2003 | See Attached ECP |
| 4.4 | 28/05/2003 | See Attached ECPs |
| 4.5 | 03/07/2003 | See Attached ECP |
| 4.6 | 28/07/2003 | See Attached ECP |
| 5.0 | 26/03/2004 | See Attached ECPs |
| 5.1 | 16/04/2004 | See Attached ECPs |
| 6.0 | 13/12/2005 | See Attached ECPs |

Contents

1.	Introduction	8

1.1.	Purpose of the Document	8

1.2.	Acronyms and Abbreviations	9

1.3.	References	10

1.3.1.	Applicable Documents	10

1.3.2.	Reference Documents	10

1.4.	Overview of the Document	10

1.5.	Interface Function	10

2.	General Description	11

3.	DPU Commands	12

4.	SPU – DPU Protocol	13

4.1.	Command Source Packet Structure	13

4.1.1.	Command ID	13

4.1.2.	Data	14

4.1.2.1.	LOAD	14

4.1.2.2.	DUMP	15

4.1.2.3.	CHECK	15

4.1.2.4.	Perform Activity	16

4.1.2.4.1.	CP_DATA_RAM_EEPROM	16

4.1.2.4.2.	RESET	17

4.1.2.4.3.	RAW_CHAN_TRAN_MODE	17

4.1.2.4.4.	STOP_REDUCT_COMPR	18

4.1.2.4.5.	START_REDUCT_COMPR	18

4.1.2.4.6.	PEAK_UP	19

4.1.2.4.7.	ACT_TEST_PHOT	19

4.1.2.4.8.	ACT_TEST_SPEC	19

4.1.2.4.9.	CONNECT_DMC	20

4.1.2.5.	Write	20

4.2.	Response Source Packet Structure	22

4.2.1.	Acknowledgement of the LOAD Command	22

4.2.2.	Acknowledgement of the DUMP Command	23

4.2.3.	Acknowledgement of the CHECK Command	24

4.2.4.	Acknowledgement of the Perform Activity Command	24

4.2.5.	Acknowledgement of the Write Command	25

4.2.6.	Response to an Invalid Command ID	26

4.3.	SPU HLSW HK	27

4.3.1.	Definition and Packet Structure	27

4.3.2.	SPU HLSW HK List	27

4.4.	Science Source Data	30

4.4.1.	Packet Structure	30

4.4.1.1.	Compressed Entity Header	31

4.4.1.2.	Compressed DEC/MEC Header	31

4.4.1.3.	Compressed Science Data	31

4.4.2.	Compressed Entity Transmission Protocol	31

4.4.2.1.	Block Header	31

4.4.2.1.1.	Header	32

4.4.2.1.2.	Counter	32

4.4.2.1.3.	Blocks	32

4.4.2.2.	Data	32

5.	Are You Alive SPU	33

# List of Figures

Figure 1. Communication between SPU HLSW and DPU	11

Figure 2. Command Packet Structure	13

Figure 3. Load Command Data Field Packet Structure	14

Figure 4. Organization of the Address1 Field	14

Figure 5. Dump Command Data Field Packet Structure	15

Figure 6. Check Command Data Field Packet Structure	15

Figure 7 Copy Data from RAM to EEPROM Command Data Field Packet Structure	16

Figure 8. Warm Reset Command Data Field Packet Structure	17

Figure 9. Raw Channel Selection Command Data Field Packet Structure	17

Figure 10. Stop Command Data Field Packet Structure	18

Figure 11. Start Command Data Field Packet Structure	18

Figure 12. Peak-up Command Data Field Packet Structure	19

Figure 13. SPU Test Command for Photometry Data Field Packet Structure	19

Figure 14. SPU Test Command for Spectroscopy Data Field Packet Structure	19

Figure 15. Connect to DEC/MEC Command Data Field Packet Structure	20

Figure 16. Write Command Data Field Packet Structure	20

Figure 17. Response Packet Structure	22

Figure 18. Packet Structure of the Positive Acknowledgement (PACK) of the Load Command	22

Figure 19. Packet Structure of the Negative Acknowledgement (NACK) of the Load Command	22

Figure 20. Packet Structure of the Positive Acknowledgement (PACK) of the Dump Command	23

Figure 21. Packet Structure of the Negative Acknowledgement (NACK) of the Dump Command	23

Figure 22. Packet Structure of the Positive Acknowledgement (PACK) of the Check Command	24

Figure 23. Packet Structure of the Negative Acknowledgement (NACK) of the Check Command	24

Figure 24. Packet Structure of the Positive Acknowledgement (PACK) of the Perform Activity Command	24

Figure 25. Packet Structure of the Negative Acknowledgement (NACK) of the Perform Activity Command	25

Figure 26. Packet Structure of the Positive Acknowledgement (PACK) of the Write Command	25

Figure 27. Packet Structure of the Negative Acknowledgement (NACK) of the Write Command	25

Figure 28. Packet Structure of the Negative Acknowledgement (NACK) of an Invalid Command ID	26

Figure 29. SPU HK Data Packet Structure for Blue SPU/Red SPU	27

Figure 30. Compressed Entity Packet Structure	30

Figure 31. Splitting of the Compressed Entity and the Resulting Science Data Blocks	30

Figure 32. Compressed Entity Header Structure	31

Figure 33. Structure of the Science Data Block sent from SPU to DPU	31

# List of Tables

Table 1. Description of the SPU HLSW Commands	12

Table 2. DPU Command IDs	13

Table 3. Identification of the Activities	16

Table 4. Parameter IDs for the Write Commands	21

Table 5. Error Codes and Attached Parameters for the Load Command	22

Table 6. Error Codes and Attached Parameters for the Dump Command	23

Table 7. Error Codes and Attached Parameters for the Check Command	24

Table 8. Error Codes and Attached Parameters for the Perform Activity Command	25

Table 9. Error Codes and Attached Parameters for the Write Command	26

Table 10. SPU HLSW HK List	29

Table 11. SPU HK Check by DPU	33

# Introduction

The reduction/compression SW of the ‘Photodetector Array Camera Spectrometer’ (PACS) Instrument is developed by (T)UVIE. The way the compression should be done for the science data is read from the DEC/MEC header and tables stored on board. The compressed data should be transferred to the DPU via one IEEE 1355/spacewire data link per board. AD003 describes the critical interfaces between separately developed sub-units of PACS while this document depicts the SPU to DPU interface.

## Purpose of the Document

This document defines the transmission protocol between SPU HLSW and DPU. The DPU is the slave (1355 link start-up protocol), which sends commands. The SPU HLSW, which is the master (1355 link start-up protocol), acknowledges and executes the commands. Compressed/uncompressed data are sent to DPU according to DEC/MEC header and tables stored on board. Additionally, the HLSW HK parameters are sent to the DPU at a data rate compatible with the overall PACS HK.

In its present form, the document contains the protocol of DPU-SPU HLSW interface.

## Acronyms and Abbreviations

| ADSP | Analog device DSP | OBCP | On-Board Control Procedure |
| --- | --- | --- | --- |
| AID | Activity ID | OBS | On-Board Software |
| AOCS | Attitude and Orbit Control Subsystem | PACS | Photodetector Array Camera and Spectrometer |
| ASW | Application SoftWare |  |  |
| BOL | BOLometers | PHC | PhotoConductors |
| CDMS | Command and Data Management System | PMA | Program Memory Address |
| CPU | Central Processing Unit | PMD | Program Memory Data |
| CRE | Cold Readout Electronics | PRIP | Pattern Recognition and Image Processing |
| CSL | Centre Spatial de Liège | PROM | Programmable Read Only Memory |
| DEC/MEC | Detector Controller/Mechanisms Controller | RAM | Random Access Memory |
| DPU | Digital Processing Unit | RCNB | Raw Channels NumBer |
| DRCU | Detector Readout and Control Unit | RCX | Raw Channel indeX |
| DSP | Digital Signal Processor | REAL | REduction ALgorithm |
| EEPROM | Electrically Erasable Programmable Read Only Memory | ROM | Read Only Memory |
|  |  | SAU | Smallest Addressable Unit |
| FCU | FPU Control Unit | SID | Structure ID |
| FIRST | Far Infrared and Sub-millimeter Telescope | SPIRE | Spectral and Photometric Imaging Receiver |
| FPU | Focal Plane Unit | SPU | Signal Processing Unit |
| HIFI | Heterodyne Instrument for HERSCHEL (HiFi instrument) | SW | SoftWare |
|  |  | SWL | Short WaveLength |
| HK | House-Keeping | TBC | To Be Confirmed |
| HLSW | High Level SW | TBD | To Be Defined |
| HS | High Speed | TBU | To Be Updated |
| HSO | Herschel Space Observatory | TBW | To Be Written |
| HW | HardWare | TC | TeleCommand |
| I/F | Interface | TM | TeleMetry |
| IAC | Instituto de Astrofísica de Canarias | TUVIE | Technical UVIE |
| ID | Identification | UR | User Requirement |
| IFSI | Istituto di Fisica dello Spazio Interplanetario | URD | User Requirements Document |
| LLSW | Low Level SW | UVIE | University of Vienna |
| LSB | Least Significant Byte | WE | Warm Electronics |
| LWL | Long WaveLength |  |  |
| MEM_STATUS_CNTS | MEMory STATUS CouNTerS |  |  |
| MFCU | Mechanisms and Focal plane electronics Control Unit |  |  |
| MSB | Most Significant Byte |  |  |

## References

### Applicable Documents

| AD001 AD002 AD003 | PACS-TW-GS-001 SCI-PT-ICD-07527 PACS-ME-ID-001 | HERSCHEL/PACS SPU High Level Software Specification Document Packet Structure Interface Control Document PACS Instrument Interface Requirement Document |
| --- | --- | --- |

### Reference Documents

| RD001 RD002 | BSSC(96)2 DIPSAPII-DAS-31-06 | Guide to applying the ESA software engineering standards to small Software projects SMCS332 user manual |
| --- | --- | --- |

## Overview of the Document

This document is structured as follows:

- From Section 1 and Section 2, an introduction showing the SPU HLSW environment is presented.

- Section 3 contains a list of the supported DPU commands

- The DPU-SPU protocol is presented in Section 4. It consists of the Data Packet Structure (Command, Response, HK and Science Data Packet Structure).

- In Section 5, the SPU responsibility is described.

## Interface Function

It consists of one 1355 data link per board running at nominal link speed (10 Mbps). The DPU-SPU HLSW communication is bi-directional.

# General Description

# The communication interface between DPU and SPU HLSW is depicted in Figure 1.

# Figure 1. Communication between SPU HLSW and DPU

The SPU unit consists of two CPU boards, which work independently. They are called SWL SPU and LWL SPU. The HLSW will be identically implemented in the CPU of each SPU sub-unit (SWL and LWL). As both CPUs have equivalent functionality, we only focus on the HLSW interface to DPU of one board. The SPU contains one data input from DPU:

- Commands from DPU

and three data outputs to DPU:

- Compressed data to DPU

- HK to DPU

- Command response to DPU

The SPU HLSW is the master of the DPU-SPU HLSW connection according to the link start-up protocol described in RD002.

# DPU Commands

# The list of DPU commands to the SPU HLSW is presented in Table 1. See document AD001 for more details.

| Command | Description | Comments |
| --- | --- | --- |
| LOAD | Load | write data on the SPU memory |
| DUMP | Dump | read data from the SPU memory |
| CHECK | Check | check specified SPU memory locations. |
| Perform Activity | CP_DATA_RAM_EEPROM | Copy Data from RAM to EEPROM | burn upgraded HLSW into EEPROM |
|  | RESET | Warm Reset | performs SPU sub-unit warm reset |
|  | RAW_CHAN_TRAN_MODE | Raw Channel Selection | selects the number and index of raw channel |
|  | STOP_REDUCT_COMPR | Stop | interrupts the application SW |
|  | START_REDUCT_COMPR | Start | runs the application SW |
|  | PEAK_UP | Peak-up | performs the Peak-up routine |
|  | ACT_TEST_PHOT | SPU Test Mode for Photometry | generate synthetic data in photometry, compress it and send it to DPU |
|  | ACT_TEST_SPEC | SPU Test Mode for Spectroscopy | generate synthetic data in spectroscopy, compress it and send it to DPU |
|  | CONNECT_DMC | Connect to DEC/MEC | start the SPU link to DEC/MEC as slave or master |
| Write | WRT_DXSx | Write Detectors Selection Table | write the tables of the selected detectors (x = 1 .. 7) |
|  | WRT_DET_CST_SPEC | Write Detectors Constants in Spectroscopy | write the table of the photoconductors constants |
|  | WRT_DET_CST_PHOT | Write Detectors Constants in Photometry | write the table of the bolometer constants |
|  | WRT_SIM_DATA | Write Simulated Data Parameters | write the table of parameters for data simulation (SPU Test Mode) |

Table 1. Description of the SPU HLSW Commands

# SPU – DPU Protocol

Four kinds of data packets are foreseen from/to SPU to/from DPU:

- Command data packets

- Response data packets (Acknowledgement of DPU commands)

- SPU HLSW HK data packets

- Science data packets (compressed/uncompressed science data + compressed DEC/MEC header)

The commands, listed in Section 3, are sent from DPU to SPU using five command packet structures (Load, Dump, Check, Perform Activity and Write), as represented below.

## Command Source Packet Structure

The commands are sent from DPU through IEEE 1355/spacewire data links according to the packet structure represented by Figure 2. The command size should fit into a TC packet.

# Figure 2. Command Packet Structure

### Command ID

This field (2 Bytes) will be used to identify the type of DPU command, which is sent to the SPU. The SPU HLSW execution of one of them will be performed after the identification of the requested command. The command IDs are represented by Table 2.

| Command | Command ID | Comments |
| --- | --- | --- |
| LOAD | 0x01 | This command is used to write data on the SPU memory |
| DUMP | 0x02 | This command is used to read data from the SPU memory |
| CHECK | 0x03 | This command is used to check specified SPU memory locations. |
| Perform Activity | 0x04 | This command is used for several activities: Peak-Up I/F (PEAK_UP), Copy Data from RAM to EEPROM (CP_DATA_RAM_EEPROM), Warm Reset (RESET), Stop (STOP_REDUCT_COMPR), Start (START_REDUCT_COMPR), SPU Test Mode for Photometry (ACT_TEST_PHOT) and for Spectroscopy (ACT_TEST_SPEC) and Connect to DEC/MEC (DMC_CONNECT). |
| Write | 0x06 | This command is used to upgrade the parameter tables in the SPU memory (WRT_DXSx (x = 1…7), WRD_DET_CST_SPEC, WRT_DET_CST_PHOT, WRT_SIM_DATA). |

Table 2. DPU Command IDs

### Data

This field (Nx2 Bytes) is used to attach the required fields to execute the commands. The attached fields are described in the following subsections.

#### LOAD

# Figure 3 depicts the load command data field packet structure.

# Figure 3. Load Command Data Field Packet Structure

- Address1: This field as described in Figure 4, contains the Memory ID (1 Byte) and the MSB of the start address.

# Figure 4. Organization of the Address1 Field

Subsystem ID: 	010b for the SWL SPU, 011b for the LWL SPU and 100b for both SPU.

Memory type: 	0b for the program RAM and 1b for the data RAM

Memory block: 	0001b … RAM

0010b … Extended RAM

0100b … SMCS DPRAM

The MSB of the Start Address is read from the LSB of the Address1 field.

- Address2: This field contains the 2 LSBs of the start address

- Length of the data to be loaded (2 Bytes).

Its unit is word (4 Bytes for the load to data memory (SAU = 32 bits) and 6 Bytes for the load to program memory (SAU = 48 bits)).

- Data to be loaded (<Length>SAUs)

The maximum length of data that can be written with a single TC is 204 Bytes (51/34 SAUs for DRAM/PRAM) as described in AD002.

- Checksum that is used to verify the integrity of the data to be loaded (2 Bytes)

#### DUMP

# Figure 5 depicts the dump command data field packet structure.

# Figure 5. Dump Command Data Field Packet Structure

- Address1:  This field as described in Figure 4, contains the Memory ID (1 Byte) and the MSB of the start address

- Address2: This field contains the 2 LSBs of the start address

- Length of the data to be dumped (2 Bytes)

Its unit is word (4 Bytes in case of data memory (SAU = 32 bits) and 6 Bytes for the program memory (SAU = 48 bits)). The maximum length of memory that can be dumped with a single TC is 65532 Bytes (16383/10922 SAUs for DRAM/PRAM) as written in AD002.

#### CHECK

# Figure 6 depicts the check command data field packet structure.

# Figure 6. Check Command Data Field Packet Structure

- Address1:  This field as described in Figure 4, contains the Memory ID (1 Byte) and the MSB of the start address

- Address2: This field contains the 2 LSBs of the start address

- Length of the data to be checked (2 Bytes)

Its unit is word (4 Bytes in case of data memory (SAU = 32 bits) and 6 Bytes for the program memory (SAU = 48 bits)). The maximum length of memory that can be checked with a single TC is 65532 Bytes (16383/10922 SAUs for DRAM/PRAM) as written in AD002.

#### Perform Activity

Several activities are executed via this command. The Perform Activity command data field packet structure follows the service TC (8,4) in AD002. The Structure ID field defines the presence and the number of attached parameters. The coding of the Activity IDs and Structure IDs for the Perform Activity command is listed in Table 3.

| Activity | Activity ID | Structure ID | Comments |
| --- | --- | --- | --- |
| CP_DATA_RAM_EEPROM | ‘00000100’ (0x04) | ‘00000101’ (0x05) | The SPU HLSW burns the upgraded HLSW into EEPROM. |
| RESET | ‘00000101’ (0x05) | ‘00000000’ (0x00) | The SPU HLSW will be reset whenever this command is received |
| RAW_CHAN_TRAN_MODE | ‘00000110’ (0x06) | ‘00000101’ (0x05) | This command is sent in SPU Stopped mode to select number and end index of detectors from which data are send in raw form |
| STOP_REDUCT_COMPR | ‘00000111’ (0x07) | ‘00000000’ (0x00) | This command is transmitted for the interruption of the application SW. |
| START_REDUCT_COMPR | ‘00001000’ (0x08) | ‘00000000’ (0x00) | The SPU HLSW will run the application SW after the reception of the start command |
| PEAK_UP | ‘00001001’ (0x09) | ‘00000000’ (0x00) | After the reception of this command the SPU HLSW will run the Peak-Up SW. |
| ACT_TEST_PHOT | ‘00001010’ (0x0A) | ‘00000000’ (0x00) | After the reception of this command the SPU HLSW will generate synthetic data (photometry), compress it and send it to DPU. |
| ACT_TEST_SPEC | ‘00001011’ (0x0B) | ‘00000000’ (0x00) | After the reception of this command the SPU HLSW will generate synthetic data (spectroscopy), compress it and send it to DPU. |
| CONNECT_DMC | ‘00010000’ (0x10) | ‘00000001’ (0x01) | This command is used to start the SPU link to DEC/MEC as slave or master. |

Table 3. Identification of the Activities

##### CP_DATA_RAM_EEPROM

Figure 9 represents the Perform Activity command data field packet structure for Copy Data from RAM to EEPROM.

# Figure 7 Copy Data from RAM to EEPROM Command Data Field Packet Structure

- Spare field (2 Bytes) included for the 4 bytes alignment.

- Activity ID field (2 Bytes) for the Copy Data from RAM to EEPROM command is ‘0000100’ (0x04)

- Structure ID field (2 Bytes) for the Copy Data from RAM to EEPROM command is ‘00000101’ (0x05)

- Parameter1: Spare (4 Bytes).

- Parameter2: Memory ID for RAM (0x01 for PRAM, 0x11 DRAM and 0x12 for Extended DRAM)

- Parameter3: Start Address in RAM (Start address) (4 Bytes).

- Parameter4: Start Address in Target Memory (Start address in EEPROM)(4 Bytes)

- Parameter5: Length  (length in 16bit words)(4 Bytes).

##### RESET

# Figure 8 represents the Perform Activity command data field packet structure for Warm Reset.

# Figure 8. Warm Reset Command Data Field Packet Structure

- Spare field (2 Bytes) included for the 4 bytes alignment.

- Activity ID field (2 Bytes) for the warm reset command is ‘00000101’ (0x05)

- Structure ID field (2 Bytes) for the warm reset command is ‘00000000’ (0x00)

##### RAW_CHAN_TRAN_MODE

# Figure 9 represents the Perform Activity command data field packet structure for the Raw Channel Selection.

# Figure 9. Raw Channel Selection Command Data Field Packet Structure

- Spare field (2 Bytes) included for the 4 bytes alignment.

- Activity ID field (2 Bytes) for the Raw Channel Selection command is ‘0000110’ (0x06)

- Structure ID field (2 Bytes) for the Raw Channel Selection command is ‘00000101’ (0x05)

- Parameter1: Spare field (4 Bytes).

- Parameter2: Observing Mode (0x01 Spectroscopy, 0x02: Photometry) (4 Bytes).

- Parameter3: RCNB Number of Raw Channels (Range:0-31) (4 Bytes).

- Parameter4: RCX: Index of Raw Channels until which RCNB pixels are transmitted (4 Bytes).

- Parameter5: Spare field (4 Bytes).

##### STOP_REDUCT_COMPR

# Figure 10 represents the Perform Activity command data field packet structure for the Stop.

# Figure 10. Stop Command Data Field Packet Structure

- Spare field (2 Bytes) included for the 4 bytes alignment.

- Activity ID field (2 Bytes) for the stop command is ‘00000111’ (0x07)

- Structure ID field (2 Bytes) for the stop command is ‘00000000’ (0x00)

##### START_REDUCT_COMPR

# Figure 11 represents the Perform Activity command data field packet structure for the Start.

# Figure 11. Start Command Data Field Packet Structure

- Spare field (2 Bytes) included for the 4 bytes alignment.

- Activity ID field (2 Bytes) for the start command is ‘00001000’ (0x08)

- Structure ID field (2 Bytes) for the start command is ‘00000000’ (0x00)

##### PEAK_UP

# Figure 12 represents the Perform Activity command data field packet structure for the Peak-up.

# Figure 12. Peak-up Command Data Field Packet Structure

- Spare field (2 Bytes) included for the 4 bytes alignment.

- Activity ID field (2 Bytes) for the peak-up command is ‘00001001’ (0x09)

- Structure ID field (2 Bytes) for the peak-up command is ‘00000000’ (0x00)

##### ACT_TEST_PHOT

# Figure 13 represents the Perform Activity command data field packet structure for the SPU Test for Photometry.

# Figure 13. SPU Test Command for Photometry Data Field Packet Structure

- Spare field (2 Bytes) included for the 4 bytes alignment.

- Activity ID field (2 Bytes) for the SPU test command for photometry is ‘00001010’ (0x0A)

- Structure ID field (2 Bytes) for the SPU test command for photometry is ‘00000000’ (0x00)

##### ACT_TEST_SPEC

Figure 14 represents the Perform Activity command data field packet structure for the SPU Test for Spectroscopy.

# Figure 14. SPU Test Command for Spectroscopy Data Field Packet Structure

- Spare field (2 Bytes) included for the 4 bytes alignment.

- Activity ID field (2 Bytes) for the SPU test command for spectroscopy is ‘00001011’ (0x0B)

Structure ID field (2 Bytes) for the SPU test command for spectroscopy is ‘00000000’ (0x00)

##### CONNECT_DMC

Error! Reference source not found. represents the Perform Activity command data field packet structure for the Connect to DEC/MEC command.

# Figure 15. Connect to DEC/MEC Command Data Field Packet Structure

- Spare field (2 Bytes) included for the 4 bytes alignment.

- Activity ID field (2 Bytes) for Connect to DEC/MEC command is ‘00010000(0x10)

- Structure ID field (2 Bytes) for Connect to DEC/MEC command is ‘00000001’ (0x01)

- Parameter1 field (4 Bytes) contains the SPU link start-up protocol to DEC/MEC (0x11: Master, 0x22: Slave).

#### Write

# Figure 16 represents the Write command data field packet structure.

# Figure 16. Write Command Data Field Packet Structure

- Spare field (2 Bytes) included for the 4 bytes alignment.

- Parameter ID field (2 Bytes) represents the Memory/Address identifier. The Parameter ID of the write commands is presented in Table 4.

| Write Command | Parameter ID | Description |
| --- | --- | --- |
| WRT_DXS1 | ‘10000001’ (0x81) | This command is used to write the tables of the selected detectors (from which data are requested) on the SPU memory. WRT_DXS1-5 are reserved for the bolometers while WRT_DXS6-7 are reserved for the photoconductors. |
| WRT_DXS2 | 0x82 |  |
| WRT_DXS3 | 0x83 |  |
| WRT_DXS4 | 0x84 |  |
| WRT_DXS5 | 0x85 |  |
| WRT_DXS6 | 0x86 |  |
| WRT_DXS7 | 0x87 |  |
| WRT_DET_CST_SPEC | ‘01000010’ (0x42) | This command is used to write the table of the photoconductors constants, which are relevant for the pre-processing step. |
| WRT_DET_CST_PHOT | ‘00100100’ (0x24) | This command is used to write the table of the bolometer constants, which are relevant for the pre-processing step. |
| WRT_SIM_DATA | ‘00011000’ (0x18) | This command is used to write the table of parameters, which will be used, for the SPU test mode. |

Table 4. Parameter IDs for the Write Commands

- Length of the data to be written (2 Bytes).

Its unit is 4 Bytes for the write to the SPU memory.

- Data to be written (<Length>4 Bytes).

The maximum length of data that can be written with a single TC is 204 Bytes as written in AD002.

- Checksum that is used to verify the integrity of the data to be written (2 Bytes)

- Spare field (2 Bytes) included for the 4 bytes alignment.

## Response Source Packet Structure

The SPU HLSW acknowledges the command reception and/or execution by sending the command response within a maximum timeout of 200 milliseconds. It should be conforming to the structure defined in Figure 17.

# Figure 17. Response Packet Structure

The data field (Nx2 Bytes) is used to acknowledge the DPU command. Its coding is proposed in the following subsections.

### Acknowledgement of the LOAD Command

Two kinds of acknowledgement are proposed: positive and negative. Their packet structures are represented respectively in Figure 18 and Figure 19.

# Figure 18. Packet Structure of the Positive Acknowledgement (PACK) of the Load Command

# PACK ID:	‘10000001’ (0x81)

# Figure 19. Packet Structure of the Negative Acknowledgement (NACK) of the Load Command

NACK ID:	‘11110001’ (0xF1)

| Error Code | Error Definition | Parameter Attached … |
| --- | --- | --- |
| 0x72 | invalid Memory ID | Spare (3 Bytes) and Memory ID (1 Byte) |
| 0x73 | invalid Address | Spare (1Byte) and Address (3 Bytes) |
| 0x75 | invalid Checksum | Spare (2 Bytes) and Checksum (2 Bytes) |
| 0x7B | invalid Checksum after re-reading | Spare (2 Bytes) and Checksum after re-reading (2 Bytes) |

# Table 5. Error Codes and Attached Parameters for the Load Command

### Acknowledgement of the DUMP Command

Two kinds of acknowledgement are proposed: positive and negative. Their packet structures are represented respectively in Figure 20 and Figure 21.

The dumped data packet will be split into blocks of 996 Bytes whenever it exceeds the telemetry packet size. Therefore, the last block will have a size less or equal to 996 Bytes.

# Figure 20. Packet Structure of the Positive Acknowledgement (PACK) of the Dump Command

PACK ID:	‘000110000010’ (0x182)	for the intermediate packets (packets previous to the last)

‘10000010’ (0x82)	for the last packet

Address1:	represents the memory ID and the MSB (1 byte) of the start address of the dumped data block.

Address2:	represents the LSB (2 bytes) of the start address of the dumped data block.

Length:	is the size of the dumped data block in words.

Data:	maximum 996 Bytes per dumped data block. SAU is 6 Bytes for program memory and 4 Bytes for data memory.

Checksum:	the resulting checksum of the dumped data block.

# Figure 21. Packet Structure of the Negative Acknowledgement (NACK) of the Dump Command

NACK ID:	‘11110010’ (0xF2)

| Error Code | Error Definition | Parameter Attached … |
| --- | --- | --- |
| 0x72 | invalid Memory ID | Memory ID (1 Byte) and Address (3 Bytes) |
| 0x73 | invalid Address field | Memory ID (1 Byte) and Address (3 Bytes) |

Table 6. Error Codes and Attached Parameters for the Dump Command

### Acknowledgement of the CHECK Command

Two kinds of acknowledgement are proposed: positive and negative. Their packet structures are represented respectively in Figure 22 and Figure 23.

# Figure 22. Packet Structure of the Positive Acknowledgement (PACK) of the Check Command

PACK ID:	‘10000011’ (0x83)

The Address1, the Address2 and the Length are represented as in the original command.

Checksum:	the resulting checksum of the data.

# Figure 23. Packet Structure of the Negative Acknowledgement (NACK) of the Check Command

NACK ID:	‘11110011’ (0xF3)

| Error Code | Error Definition | Parameter Attached … |
| --- | --- | --- |
| 0x72 | Invalid Memory ID | Memory ID (1 Byte) and Address (3 Bytes) |
| 0x73 | Invalid Address field | Memory ID (1 Byte) and Address (3 Bytes) |

Table 7. Error Codes and Attached Parameters for the Check Command

### Acknowledgement of the Perform Activity Command

Two kinds of acknowledgement are proposed: positive and negative. Their packet structures are represented respectively in Figure 24 and Figure 25.

# Figure 24. Packet Structure of the Positive Acknowledgement (PACK) of the Perform Activity Command

PACK ID:	‘10000100’ (0x84)

The positive acknowledgement informs that the SPU HLSW has received and understood the Perform Activity command (it is not sent after the execution of the command).

# Figure 25. Packet Structure of the Negative Acknowledgement (NACK) of the Perform Activity Command

NACK ID: 	‘11110100’ (0xF4)

| Error Code | Error Definition | Parameter Attached … |
| --- | --- | --- |
| 0x77 | Invalid Activity ID | Spare (2 Bytes) and Activity ID (2 Bytes) |
| 0x78 | Invalid Structure ID | Spare (2 Bytes) and Structure ID (2 Bytes) |
| 0x79 | Invalid SID Parameter | SID Parameter (4 Bytes) |

Table 8. Error Codes and Attached Parameters for the Perform Activity Command

### Acknowledgement of the Write Command

Two kinds of acknowledgement are proposed: positive and negative. Their packet structures are represented respectively in Figure 26 and Figure 27.

# Figure 26. Packet Structure of the Positive Acknowledgement (PACK) of the Write Command

# PACK ID:	‘10000110’ (0x86)

# Figure 27. Packet Structure of the Negative Acknowledgement (NACK) of the Write Command

# NACK ID:	‘11110110’ (0xF6)

| Error Code | Error Definition | Parameter Attached … |
| --- | --- | --- |
| 0x74 | Length not compatible to Parameter ID | Spare (2 Bytes) and Length (2 Bytes) |
| 0x75 | Invalid Checksum | Spare (2 Bytes) and Checksum (2 Bytes) |
| 0x76 | Invalid Parameter ID | Spare (2Byte) and Parameter ID (2 Bytes) |
| 0x79 | Invalid Data Parameter | Data Parameter (4 Bytes) |
| 0x7B | Invalid Checksum after re-reading | Spare (2 Bytes) and Checksum after re-reading (2 Bytes) |

Table 9. Error Codes and Attached Parameters for the Write Command

### Response to an Invalid Command ID

This acknowledgement is send in case of receiving an unknown command ID. Figure 28 represents the packet structure.

# Figure 28. Packet Structure of the Negative Acknowledgement (NACK) of an Invalid Command ID

NACK ID:	‘000111111111’ (0x1FF)

Error Code:	‘01110001’ (0x71) … invalid command ID: unknown command

Command ID	is represented as in the original command.

## SPU HLSW HK

### Definition and Packet Structure

The SPU HLSW HK packet is sent from the SPU to the DPU. It consists either of compression results and status of the HLSW whenever raw data are received from DEC/MEC, or the SPU HLSW status while no observation is performed. The SPU HK parameters are listed in Table 10. Their associated field is depicted in Figure 29. SPU HLSW HK are transmitted at a data rate compatible with the overall PACS HK (see AD001 for details).

The Size of SPU HK data field is 72 Bytes per sub-unit. Every HK parameter is put in a 4-byte Word. In SPU idle mode (stopped data compression), only PIX, CI, CPU_WORKLOAD, DMC_LINK_STATUS, MEM_STATUS_CNTS and PAR_MONITOR fields are filled. The other fields are set to default value.

# Figure 29. SPU HK Data Packet Structure for Blue SPU/Red SPU

### SPU HLSW HK List

The SPU HLSW HK are listed in Table 10.

| Parameter | Size (B) | Variable | Default Value | Description |
| --- | --- | --- | --- | --- |
| SPUS_HK_HEADER SPUL_HK_HEADER | 4 | HK Header | 0x00870000 | This field is added to the HK packet sent from SPU to DPU. It distinguishes the HK from the science packet and the response packet |
| SPUS_OBSID SPUL_OBSID | 4 | Observation Identification | 0 | This field is used to identify the observation the HK belongs to. It should be the same OBSID for the science data. |
| SPUS_PIX SPUL_PIX | 4 | Packet Index | 0xFFFFXXXX | The two MSB of the PIX are set to 0, when the HK packet contains the compression results (compression started). In this case, the two LSB are counting the number of downlinked compressed entities since the HLSW handover of the SPU or the last warm reset command. Moreover, the 2 LSB provide the relationship between the science packet and the related HK. The concordance is determined on ground. The two MSB of the PIX are set to: 0xFFFF for stopped compression, 0xDDDD for started compression or 0xAAAA for auto-stopped compression (Avoiding a SW crash). In all three cases, the two LSB are stalled to the last updated value |
| SPUS_CI SPUL_CI | 2 | Counter Increments | 0xXXXX | This field is used to attest that HLSW is not hanging. It is periodically incremented from 0 to 65535. |
| SPUS_REAL SPUL_REAL | 2 | Reduction Algorithm Used | 0xFF | LSB is used to signal the used reduction algorithm if compression started. It is set to 0xFF if on-board data reduction is not used. MSB is used to signal the number of samples per sub-ramp (range: 2-128 in started compression). It is set to 0 if on-board data reduction is not used. |
| SPUS_SATUR_FLAG SPUL_SATUR_FLAG | 1 | Saturation Flag | 0 | 0x11: Saturated, 0: Non-Saturated |
| SPUS_SAMP_CORR SPUL_SAMP_CORR | 3 | Glitch Counter Information | 0 | Number of samples affected by glitches for the blue SPU. |
| SPUS_MAINT_RAMPS SPUL_MAINT_RAMPS | 2 | Number of Maintained Ramps/ Averages | 0 | Number of maintained slopes or sub-slopes (Spectroscopy) or averages (Photometry). |
| SPUS_CPU_WORKLOAD SPUL_CPU_WORKLOAD | 2 | CPU Workload | 0xXXXX | CPU workload for the past second. |
| SPUS_DMC_LINK_STATUS SPUL_DMC_LINK_STATUS | 2 | DEC/MEC Link Status | 0xFF | DEC/MEC Link Status: 0x00: Link is OFF, 0xFF: Link is ON and 0xAA: Link connection is in progress. |
| SPUS_INTEG_RAMPS SPUL_INTEG_RAMPS | 1 | Number of Integrated Ramps/ Averages | 0 | Number of integrated ramps (Spectroscopy) or averages (Photometry). |
| SPUS_VID SPUL_VID | 1 | Version ID | 0xXX | This field is used to represent the software version |
| SPUS_RCX SPUL_RCX | 2 | Raw Channel Index | 0 | The most significant 6 bits contain the Nb. of selected raw channels (RCNB) The least significant 10 bits contains the Index of Raw Channels (RCX) until which RCNB pixels data are transmitted with the compressed science data. |
| SPUS_DMC_ERROR SPUL_DMC_ERROR | 1 | DEC/MEC Header Error | 0 | This field is set to 0xFF if an error is detected in the DEC/MEC header. |
| SPUS_MEM_STATUS_CNTS SPUL_MEM_STATUS_CNTS | 2 | Memory Status Counters | 0xXXXX | LSB: EDAC memory check counter for Single Error Failure MSB: EDAC memory check counter for Double Error Failure |
| SPUS_SPARE_1 SPUL_SPARE_1 | 2 | Spare | 0 | Spare HK field |
| SPUS_LLC_ERROR SPUL_LLC_ERROR | 2 | Invalid LLC Parameter | 0 | This HK parameter reports an invalid write parameter for LLC. Default = 0. See the actual HLSW user manual for more details |
| SPUS_PAR_MONITOR SPUL_PAR_MONITOR | 2 | Monitored Write Parameter | 0 | This HK parameter can be exploited by the user in monitoring a dedicated parameter in the SPU memory. The address of this parameter can be set via a write command. The default value is 0. See the actual HLSW user manual for more details. |

# Table 10. SPU HLSW HK List

## Science Source Data

SPU HLSW may transmit a maximum number of 75 science data packets to DPU in one buffer (in one go). The science data packet structure is represented in the following subsections.

### Packet Structure

# Figure 30 depicts the compressed entity packet structure.

| CEH 28 Bytes | CDH <CDHS> 4 Bytes | CSD <SCIS> 4 Bytes |
| --- | --- | --- |

# Figure 30. Compressed Entity Packet Structure

CEH:	Compressed Entity Header.

CDH:	Compressed DEC/MEC Header.

CSD:	Compressed Science Data.

The compressed entity is split by the SPU into blocks of 1000 Bytes (see AD002) to fit into the telemetry packets (

Figure 31). A header of 12 Bytes (Block Header) is added to each block before it is sent to the DPU. 8 Bytes of this header will be ignored in the DPU.

# Figure 31. Splitting of the Compressed Entity and the Resulting Science Data Blocks

#### Compressed Entity Header

# Figure 32 represents the compressed entity header structure received on ground.

# Figure 32. Compressed Entity Header Structure

Type:	Type of the observing Mode (0x01 for spectroscopy and 0x02 for photometry)

PIX:	The PIX field provides the relationship between the HK packet and the science packet using the same index.

DECID:	The DECID field (DEcompression Code ID) is analogous to the CMP/CMM (Compression Mode) fields in the DEC/MEC Header. This field is used to enter the proper decompression mode.

CRCS:	The CRCS field represents the size of the Compressed Raw Channel data Size (in 4 Byte words).

CDHS:	The CDHS field represents the size of the Compressed DEC/MEC Header (in 4 Byte words).

SCIS:	The SCIS field represents the size of the compressed science data (in 4 Byte words).

#### Compressed DEC/MEC Header

# This field contains the lossless compressed DEC/MEC header (see AD001).

#### Compressed Science Data

# This field contains the compressed science data (see AD001).

### Compressed Entity Transmission Protocol

#### Block Header

# Figure 33 represents the block header of the science source packet sent from SPU to DPU.

# Figure 33. Structure of the Science Data Block sent from SPU to DPU

##### Header

The header field (4 Bytes) will be used to identify the packet and data type. This field will not be transmitted to ground. It will be skipped in the DPU level after the collection of the whole blocks of one compressed entity.

Header for science data block is:

0x008A0000         in spectroscopy mode

0x008B0000         in photometry mode

##### Counter

The counter field (4 Bytes) specifies the index of the actual transmitted block. Its range is from 1 to ‘blocks’. The two upper bytes are not transmitted to ground. They are skipped by DPU.

##### Blocks

This field (4 Bytes) specifies the total number of blocks the compressed entity packet has been split into (a block unit is up to 1000 Bytes) to fit into one telemetry packet and sent to the DPU. The two upper bytes are not transmitted to ground. They are skipped by DPU.

#### Data

This field contains the telemetry data block of 1000 Bytes. The collection of these blocks constitutes the compressed entity packet.

# Are You Alive SPU

The functionality of the SPU HLSW is continuously checked by the DPU monitoring some SPU HLSW HK data. The “Are you alive SPU” could be tested by the DPU using the SPU parameter CI (Table 10) and a time out. Both SPU boards will independently produce HK at regular time interval compatible with the PACS overall HK rate. This time interval is described in AD001. The DPU will always store the HK packets, and checks the parameter CI of the latest received SPU HK packet, at rate of 0.5 Hz, whether they are updated or not, according to the logic described in Table 11. If no update of this entry happens within a maximum time of 8 sec, the DPU will change accordingly its internal HK status related to the corresponding SPU.

| CI | DPU Check Rate (Hz) |
| --- | --- |
| Incrementing | 0.5 |

Table 11. SPU HK Check by DPU

# Footnotes

In this case, the maximum data size, which could be dumped, is 10 Kbytes, while only 9 Kbytes could be checked.

# Text boxes

Spare

2 Bytes

RCX

2 B

OBSID4 B

PIX
4 B

Parameter ID

2 Bytes

Counter

4 Bytes

Blocks

4 Bytes

CI
2 B

CDHS

2 Bytes

CPU_WORKLOAD 2 B

INTEG_RAMPS

1 B

CRCS

2 Bytes

PACK ID

2 Bytes

Parameter

4 Bytes

Parameter

4 Bytes

Error Code

2 Bytes

Data

<Length>4 Bytes

NACK ID

2 Bytes

Length

2 Bytes

Length

2 Bytes

Address2

2 Bytes

Address1

2 Bytes

SPARE_1

2 B

PACK ID

2 Bytes

Checksum

2 Bytes

SATUR_FLAG
1 B

Checksum

2 Bytes

LLC_ERROR

2 B

DMC_LINK_STATUS 2B

Block

Header

Structure ID

(2 Bytes)

PAR_MONITOR 2 B

DMC_ERROR

1 B

Activity ID

(2 Bytes)

Parameter

4 Bytes

Spare

(2 Bytes)

Prepared by:	Ahmed Nabil BELBACHIR	 		           Date: 13 December 2005

Checked and Approved by: Helmut FEUCHTGRUBER

Approved by: Stefano PEZZUTO

Error Code

2 Bytes

NACK ID

2 Bytes

Data

<Length>SAUs

Length

2 Bytes

Address2

2 Bytes

Address1

2 Bytes

PACK ID

2 Bytes

1012 Bytes

Data

Block

Header

1012 Bytes

Data

Structure ID

(2 Bytes)

Checksum

2 Bytes

command/response / HK

Parameter1

4 Bytes

Parameter

4 Bytes

Error Code

2 Bytes

VID

1 B

MAINT_RAMPS
2 B

SAMP_CORR

3 B

NACK ID

2 Bytes

Activity ID

(2 Bytes)

REAL
2 B

Spare

(2 Bytes)

Error Code

2 Bytes

NACK ID

2 Bytes

Structure ID

(2 Bytes)

Header

4 Byte

PACK ID

2 Bytes

compressed data

compressed data

Parameter

4 Bytes

command/response / HK

SPU LWL

SPU SWL

DPU

Spare

2 Bytes

Spare

2 Bytes

Activity ID

2 Bytes

Structure ID

2 Bytes

Parameter1..5

5x4 Bytes

Spare

2 Bytes

Activity ID

2 Bytes

Parameter1..5

5x4 Bytes

Spare

2 Bytes

Activity ID

2 Bytes

Structure ID

2 Bytes

Error Code

2 Bytes

NACK ID

2 Bytes

Block

Header

SCIS

4 Bytes

PACK ID

2 Bytes

Data

Nx2 Bytes

MEM_STATUS_CNTS

2 B

Data

Nx2 Bytes

Command ID

2 Bytes

Activity ID

(2 Bytes)

Spare

(2 Bytes)

Structure ID

(2 Bytes)

Activity ID

(2 Bytes)

Spare

(2 Bytes)

Structure ID

(2 Bytes)

Activity ID

(2 Bytes)

Spare

(2 Bytes)

1012 Bytes

Data

Structure ID

(2 Bytes)

( ( ( ( ( (

( ( ( ( ( (

Data (1000 Bytes)

Data (1000 Bytes)

Data (1000Bytes)

Data (1000 Bytes)

CSD

Memory ID

Command ID

4 Bytes

Error Code

2 Bytes

NACK ID

2 Bytes

Structure ID

2 Bytes

CDH

Type

4 Byte

DECID

12 Bytes

CEH

Activity ID

(2 Bytes)

PIX

4 Bytes

Spare

(2 Bytes)

Length

(2 Bytes)

Address2

(2 Bytes)

Address1

(2 Bytes)

Address1

(2 Bytes)

MSB of the Address

(1 Byte)

Subsystem ID

(3 bits)

Block inside the Memory Type

(4 bits)

HK_HEADER
4 B

Memory Type

(1 bit)

Data

<Length>SAUs

Length

2 Bytes

Address2

2 Bytes

Address1

2 Bytes

Address2

(2 Bytes)

Checksum

2 Bytes

Length

(2 Bytes)