New mass estimate based on amalgam of Peter and Fraser’s spreadsheet and new structure concept:

First let’s get the masses of what we know about – i.e. mirrors; detectors; mechanisms etc.

| 15-K |  |
| --- | --- |
| M3 | 95 |
| Filter | 50 |
| Total 15-K hardware | 145 x1.2 = 175 |
| 4-K Photometer (common) |  |
| Chopper | 500 |
| M5 | 90 |
| filter | 50 |
| 4-K Strap | 300 |
| 4-K Spectrometer |  |
| P/O Mirror | 40 |
| R1 | 40 |
| R2+R3 | 120 |
| R3+R4 | 100 |
| R5 | 60 |
| 2xPolariser | 100 |
| RT1 | 100 |
| Mechanism+RT2 | 1000 (cf GSFC 400 g for structure; LAS give <500g for LWS type motor) |
| C1 | 100 |
| C2 | 60 |
| Total 4-K Hardware | 2660 x1.2=3200 |
| 2-K Photometer |  |
| 2xFilter | 100 |
| 2xDichroic | 100 |
| M6 | 75 |
| M7 | 175 |
| M8 | 90 |
| Fold 1+2 | 150 |
| 2-K Strap | 200 |
| 3x Arrays | 900 |
| Baffles(?) | 200 |
| 2-K Spectrometer |  |
| C3 | 50 |
| Polariser | 50 |
| Fold 1 | 60 |
| 2xArrays | 600 |
| Baffles(?) | 200 |
| 2-K Strap | 200 |
| 2-K Cooler |  |
| Cooler+structure | 500 |
| 2-0.3 K Straps | 500 |
| Total 2-K Hardware | 4150 x1.2=4980 |

Table 1:  “Hardware” to be supported at each temperature stage

O.k. Now for the covers:

If we estimate the 4-K plate as being 450x550 mm and the height of the cover above it as about 180, then the surface area on the photometer and spectrometer 4-K covers will be about 6075 cm2.  If we assume that they consist of 100 micron thick aluminium foil then the basic mass of each cover will be 164 g – add 20% for the stiffening structure gives 200 g for each 4-K cover.  Assume the same for the 2-K cover even though it’s a bit smaller.  The 15-K cover has an area of about 12000 cm2 under the same assumptions it will be about 400 g.

Structure:

Take the mean thickness of the 2-K plate as being 0.5 cm (this HAS to be enough even including the optics mounts).  This gives a nominal mass of 3340 g – lets take 40% margin for this as there may be some complicated bits to do with the inner enclosure and mounting of the cooler – so mass of structure “plate” is 4700 g.  Take the mass of each support as 200 g – 600 g total.  The total 2-K structure is then 5300 g (cf. supported hardware and covers total of 5180 g)

Again take a mean thickness of 0.5 cm for the 4-K plate; 20% margin and 1000 g for the supports – gives 5000 g for the 4-K structure.

The total mass at 2-K is thus 10500 g

The total mass at 4-K is thus 8400 g

The total mass supported from 15-K is 19475 g (including mirrors and filter)

With a 0.5 cm mean thickness for the base-plate; 1500 g for the support structure; 500 g for the filter support and a margin of 20% the mass of the 15-K structure is ~7000 g.

The total mass will then be around 26.5 Kg INCLUDING 20% margin.

Even if I’m way out on the cover masses it still looks do-able for under 30 kg.

Thermal Disspation:

The following table gives the thermal budgets for the different temperature stages for the various options and operating modes: