Figure 1 shows the previous design of telescope simulator as used on UKIRT (RAL tech note 42).

Fig.1. Previous design, after UKIRT simulator.

Here the pupil-plane mirror is gimballed in order to scan the beam across the detector array. This scheme has the disadvantage that the f-number and beam-shape vary with array position. To overcome this the alternative steering scheme, used on ISO-LWS is chosen, as shown in figure 2.

Fig.2. Proposed scheme, after ISO-LWS simulator.

Although not shown, this scheme too includes the filter wheel and monitor pick-off mirror. The beam steering is achieved by the final relay mirror. As well as a gimbal control this mirror must also be translated parallel to the array in a co-ordinated manner, to keep the beam angle-of-incidence at the array (& the exit pupil position ) representative of the real telescope. This feature is not included in the ray-trace. The roof-top mirror arrangement is to provide focus-control and is to be translated in one-axis (trombone arrangement).

Optics equipment:

| Items | Source | Cost estimated |
| --- | --- | --- |
| Optical bench 6’ x 3’ min. | RAL existing. | 0 |
| Sources |  |  |
| Calibration source, cryogenic Black body | NPL, cost as per GERB | £ 20 K |
| FTS monochromator | QMW existing | £ 0 K |
| Sub-mm source | QMW Existing equip’t | 0 |
| Optics |  |  |
| Filter wheel |  |  |
| “ filter holder plate |  | £ 1 K |
| “ filters x 6 |  | £ 6 K |
| “ “ Rotary stage | Aerotech ARS300 | £ 5 K |
| “ “ “ controller | U511x-2-A | £ 6 K |
| Pupil mirror & mask & mount | Planar, MG/Ealing | £ 2 K |
| Ellipsoidal collecting mirror, < 5um rms roughness | RAL technology, ( 2 weeks staff effort + £ 1K mat’ls ) | £ 5 K |
| Trombone relay, 2 mirrors 30cm | MG/Ealing | £ 4 k |
| Linear stage+ step motor | Aerotech ATS15-200-M-20P-1-99 | £ 4.5 K |
| Steering mirror |  | £ 2 K |
| “ “ gimbal mount, 292mm, 2-axis stepper | Aerotech AOM360D-30-5-RE30-DDVAC | £ 10 K |
| Linear stage+ step motor, x 2 | Aerotech ATS15-200-M-20P-1-99 | £ 9 K |
| “ “ controller | “ U511 / 12 | £ 6 K |
| Pick-off mirror/beamsplitter |  | £ 2 K |
| PC & software for control & data collection |  | £ 2 K |
| Total |  | £ 84.5 K |