# Change notes:

Version 1:  26-NOV-1997.  Total bandwidth limited to 200-400 m - two 16x16 arrays - oversample factor of 3.

Version 2:  15-JAN-1998.  Total bandwidth 200-667 m - one 16x16, one 12x12 array - oversample factor of 5.

Version 3: 3-MARCH-1999.  Update to the Mach-Zehnder intensity beam splitter design.

# iNtroduction

This note updates and supersedes all versions of BOL/RAL/N/0023.  Here the baseline SPIRE spectrometer design that is actively being studied is briefly described and its operating parameters laid out.

Figure 1: Outline layout for the Mach-Zehnder FTS

# Outline design

The baseline design for the spectroscopy channel of the FIRST bolometer instrument will employ an imaging FTS with two wavelength channels.  The instrument is based on a Mach-Zehnder design with broad-band intensity beam splitters – figure 1 shows the general layout.  The minimum requirements for the FTS performance are given in Table 2 of the Science Requirements document – they are repeated here for completeness

# Operating PArameters and System Requirements for the FTS

In this section the global operating parameters (scan range, wavelength coverage etc. etc.) are given for the baseline FTS.

Wavelength coverage				(  = 200 - 667 m  or  15  - 50  cm-1

Optimised for operation in 200-400 m band

Bands						Band 1 - 200-299 centred at 240 (33 - 50 cm-1)

Band 2 - 299-667 centred at 412 (15 - 33 cm-1)

Required resolution 				(/((  =  100 at 250 (m  (40 cm-1)

(((  =  0.4 cm-1

Goal for resolution				(/((  =  1000 at 250 (m  (40 cm-1)

(((  =  0.04 cm-1

To illustrate the maximum requirements on the systems design, the goal resolution of 0.04 cm-1 is used throughout the rest of the document.

Optical path difference			(  = 1/(2L)	  (	L = 12.5 cm

assume 14 cm for scan length to allow for 							measure of zero path difference

Linear travel 					(14 cm)/4  = 3.5 cm ( 1.75 cm)

Nyqvist sampling rate:				(xmax  =  1/(2(max)

( (xmax  = 1/(2 x 33) = 0.015 cm  for band 2

( (xmax  = 1/(2 x 50) = 0.010 cm  for band 1

Over-sampling factor 				5

( (x  = 30 (m band 2	
						( (x  = 20 (m band 1

No. of samples per interferogram		Nsamp  = (14 cm)/(30 (m) = 4667 band 2
						Nsamp  = (14 cm)/(20 (m) = 7000 band 1

Audio frequencies				f  = vopd(

where vopd is the rate of change of the optical path 						difference.

Max. allowed audio freq.			20 Hz	(from assumed detector response)

(  vopd = 20/50  = 0.4 cm s-1

(  vmirrors = vopd/4 = 0.1 cm s-1

Audio freq. band 				15 - 33 cm-1  ( 6 - 13 Hz

33 - 50 cm-1 ( 13 - 20 Hz

Time per scan 					tscan  = (14 cm)/(0.4 cm s-1)  = 35 s

Sampling rate					(4667 samples)/(35 s)  = 133 samples s-1 - band 2

(7000 samples)/(35 s)  = 200 samples s-1 - band 1

Number of detectors 	- filled arrays		400 (16x16 + 12x12)

- feed horns		32 (20 band 1 + 12 band 2)

Position measurement:  			OPD accuracy required

minimum = 20/50 = 0.4 m

Actual position measurement = 0.4/4 = 0.1 m

Sampling required = same as single detector in 						band 1

Max. internal read-out rate:			Band 2: 133 Hz x 144 dets = 19.152 kHz

Band 1: 200 Hz x 256 dets = 51.200 kHz

Position measurement = 0.2 kHz

Total = 70 kHz

No. bits required to sample signal	16 – needs justification – won’t need this if the telescope is fully compensated.

Max. bit rate per frame			1120 kbit/s

Max total bits per scan			39200 kbit

Digital filtering should give factor 5 (oversample 						factor?)

Integration time required to fit this into 	39200/(5x40) = 196 secs

telemetry					(6 scans)

For feedhorn option all this goes down by 32/400 – max readout rate is 90 kbit/s – can almost telemeter this directly to the ground.