# SPIRE

| SUBJECT: | ICD 1.1/1.2.1 Structure - FiltersICD 1.1/1.2.1 Structure - Filters |
| --- | --- |
| PREPARED BY: | P. Ade B. WinterP.Hargrave B.Winter |
| DOCUMENT No: | SPIRE-ICD-1.1/1.2.1SPIRE-ICD-1.1/1.2.1 |
| ISSUE: | 0.10.1 1.0 | Date: | 20th August 1999 13th June 2000 |
| CHECKED BY: | …………………………………. | Date: | …………………………. |
| APPROVED BY: | …………………………………. | Date: | …………………………. |

Distribution

| Berend Winter | MSSL |
| --- | --- |
| Kjetil Dohlen | LAS |
| Dominique Pouliquen | LAS |
| Peter Ade | QMW |
| Peter Hargrave | QMW |
| Matt Griffin | QMW |
| Colin Cunningham | ATC |
| Bruce Swinyard | RAL |
| Ken King | RAL |
| Judy Long (SPIRE project office) | RAL |

# Change Record

| ISSUE | DATE |  |
| --- | --- | --- |
| 0.1 | 20th August 1999 | New document |
| 1.0 | 13th June 2000 | Official issue – updated to include revised filter information |

Table of Contents

Applicable Documents	0

Reference Documents	0

1.	Introduction	0

1.1	Purpose of Document	0

1.2	SCOPE	0

2.	functional interface	0

2.1	Functional Description and Block Diagram	0

2.2	Inputs	0

2.3	Outputs	0

3.	Mechanical, Thermal and Optical Interfaces	0

3.1	Mechanical and thermal interface data sheets	0

3.1.1	Outer cover – CFIL-1 (11 K cold stop)	0

3.1.2	Common structure – CFIL-2 (4 K cold stop)	0

3.1.3	OBP – beam splitters (SBDI-1 and SBDI-2)	0

3.1.4	PDBX – PFIL-2 (2 K cold stop)	0

3.1.5	SDBX – SFIL (2 K cold stop)	0

3.2	Harness interface data sheets	0

3.3	Optical interface data sheets	0

4.	Electrical interfaces.	0

4.1	Electrical interface definition and characterisation	0

4.1.1	Power Interface	0

4.1.2	Synchronisation	0

4.1.3	Electromagnetic Compatibility	0

4.1.4	Science Data interface	0

4.1.5	TM Interface	0

4.1.6	TC Interface	0

4.2	Electrical interface data sheets	0

4.3	Pin allocation for interface connectors (cables)	0

5.	Data Interfaces	0

# Glossary

| BSM | Beam Steering Mechanism |
| --- | --- |
| C.G. | Centre of Gravity |
| FTS | Fourier Transform Spectrometer |
| OBP | Optical Bench Panel |
| NA | Not Applicable |
| PDBX | Photometer Detector Box |
| SDBX | Spectrometer Detector Box |
| SPIRE | Spectral and Photometric Imaging REceiver |

# References

# Applicable Documents

| AD1 | Instrument Requirements Document, issue 0.30, May 2000 (FIRST/SPIRE) |
| --- | --- |

# Reference Documents

| RD1 | SPIRE filters sub-system specification – Draft 1.0 – 16th May 2000 |
| --- | --- |

# Introduction

## Purpose of Document

The purpose of this document is to define the interface between the SPIRE structure and the filters. Within this document the mechanical, thermal and optical interfaces are described.

This issue is a draft issue. The purpose of this issue is to define the interface, such that an agreed baseline interface is available at the beginning of the final design process. During the final design process the definitions may be refined and possibly changed, however at the end of the final design process the interface definition is frozen.

## SCOPE

The interfaces considered are between the SPIRE Optical Bench Panel, the common structure, the Photometer Detector Box, the Spectrometer Detector Box and the filters. Throughout the whole document the SPIRE Optical Bench Panel will referred to as OBP, the Photometer Detector Box as PDBX and the Spectrometer Detector Box as SDBX.

The document is divided into 3 parts.

The first part gives the status and description of the document itself

The second part gives the functional description defining the function within the structure.

The third part deals with the mechanical, thermal and optical interfaces.

The following interfaces are considered:

Common structure – 4 K cold stop CFIL2 and CFIL2

OBP – beam splitters (SBS1 and SBS2)

PDBX – 2 K cold stop (PFIL)

SDBX – 2 K cold stop (SFIL)

PDBX - PDIC1 (Dichroic)

PDBX - PDIC2 (Dichroic)

See the topological figures on the next page for the relative positions of the filters with respect to the IR-beam. The beam is a dotted arrow, the mirrors are blue and the filters green. Structure is represented by a solid black line.

Figure 1-1 Topology of photometer part of SPIRE, filters are green

List of acronyms for figure 1-1

CFIL1	Common Filter 1

CFIL2	Common Filter 2

CM3-5	Common Mirror 3-5

FOB	First Optical Bench Panel

FOR	First Optical Reference

PCAL	Photometer CALibrationsource

PDBX	Photometer Detector BoX

PDIC1	Photometer DIChroic 1

PDIC2	Photometer DIChroic 2

PFIL3	Photometer FILter 3 (entrance PDBX)

PFIL4L/5L	Photometer FILter 4 and 5 at nose PLW

PFIL4M/5M	Photometer FILter 4 and 5 at nose PMW

PFIL4S/5S	Photometer FILter 4 and 5 at nose PSW

PLW	Photometer Long Wave detector

PM6-11	Photometer Mirror 6 to 11

PMW	Photometer Medium Wave detector

PSW	Photomter Short Wave detector

SOB	Spire Optical Bench Panel

SOR	Spire Optical Reference

Figure 1-2 Topology of spectrometer part of SPIRE, filters are green

List of acronyms for figure 1-2

FOB	First Optical Bench Panel

FOR	Firs Optical Reference

SBS1	Spectromter Beam Splitter 1

SBS2	Spectromter Beam Splitter 2

SCCA	Spectrometer Corner Cube +X

SCCB	Spectrometer Corner Cube –X

SCAL	Spectrometer CALibration source

SDBX	Spectrometer Detector BoX

SFIL3L	Spectrometer FILter 3 (long wave)

SFIL3S	Spectrometer FILter 3 (short wave)

SFIL4L/5L	Spectrometer FILter at nose SLW

SFIL4S/5S	Spectrometer FILter at nose SSW

SM6-7	Spectrometer Mirror6-7

SM8A-12A	Spectrometer Mirror 8-12 +X chain

SM8B-12B	Spectrometer Mirror 8-12 -X chain

SMEC	Spectrometer MEChanism

SOB	Spire Optical Bench Panel

SOR	Spire Optical Rerference

# functional interface

## Functional Description and Block Diagram

The first filters in the chain, situated on the 4-K box, should reflect back to the sky as much unwanted high frequency radiation as possible. Filters on lower temperature shields should then reject radiation from higher temperature boxes and shields.

Strategic placement of filters will enable us to:

- Define the spectral passbands.

- Minimise the thermal loading on the 3He fridge, 2-K,  and 4-K stages by rejecting short wavelength thermal energy.

- Minimise stray light getting to the detectors.

- Maximise the in-band spectral transmission.

The sequence of filters starts with the 2 common 4-K filters at the input to the instrument. They minimise radiation from T > 4-K entering the instrument. The filters at the entrance of the detector boxes minimise the transmission of radiation from T > 2-K. The 0.3 K filters at the nose of the detectors are not discussed in this document since they interface only with the detectors. The beam splitters in the FTS part of the instrument reflect 50% and pass 50% of the incident radiation virtually independently of frequency across the entire SPIRE band. The dichroics within the PDBX reflect high frequencies and pass low frequencies and hence aid definition of the SPIRE photometer channels.

The filters are clamped against the structure using a light tight clamp ring. The function of the OBP (reviewing the interface between the OBP and the filters) is to support the beam splitters and their mounts. The mechanical interface should provide for a precise defined and accurately machined mounting surface. The mechanical interface should provide for sufficient stiffness, such that the mechanical loads on the mirrors are minimised. The same holds for the interfaces with the detector boxes and the dichroics. The dichroics and beam splitters are sensitive to warping, and this is considered in the design of the mounts for these components.

There is no block diagram.

## Inputs

No inputs

## Outputs

No outputs

# Mechanical, Thermal and Optical Interfaces

## Mechanical and thermal interface data sheets

The following holds for all interfaces considered in section 3.1.1 up to 3.1.13.

Mechanical environment

The sine and random input at the interfaces considered in this document will be updated after the coupled analysis. The input spectra hold for all interfaces. (TBC)

Quasi-Static

The qualification levels are provisional, copied from the qualification loads of ISO.

| Quasi Static levels | Case 1 | Case 2 | Case 3 | Case 4 |
| --- | --- | --- | --- | --- |
| x-direction | 22.5 g (TBC) | 22.5 g (TBC) | - | - |
| y-direction | 3 g (TBC) | - | 6 (TBC) | - |
| z-direction | - | 3 g (TBC) | - | 6 (TBC) |

Table 3.1-1: Qualification levels for quasi static vibration

Sine

The qualification levels are provisional copied from the qualification loads of ISO.

| Sine vibration levels | Frequency range | Input at base (QUAL) |
| --- | --- | --- |
| X-direction | 5-18 Hz 18-100 Hz | 22 mm (peak-peak) 100 g |
| Y-direction | 5-18 Hz 18-100 Hz | 22 mm (peak-peak) 100 g |
| Z-direction | 5-18 Hz 18-100 Hz | 22 mm (peak-peak) 100 g |

Table 3.1-2: Qualification levels for sine vibration

Random

The qualification levels are provisional, copied from the qualification loads of ISO.

| Random vibration levels | Frequency range | Input at base (QUAL.) |
| --- | --- | --- |
| X-direction | 5 – 150 Hz 150-700 Hz 700 – 2000 Hz | +6 dB Hz 1.44 g²/Hz -3 dB |
| Y-direction | 5 – 150 Hz 150-700 Hz 700 – 2000 Hz | +6 dB Hz 1.44 g²/Hz -3 dB |
| Z-direction | 5 – 150 Hz 150-700 Hz 700 – 2000 Hz | +6 dB Hz 1.44 g²/Hz -3 dB |

Table 3.1-3: Qualification levels for random vibration (45 grms)

Alignment

The following requirements hold for the alignment of the I/F lane between the filter mounts and the structure.

Off centre 1 mm all directions simultaneously (TBC). The flatness of the mounting surface for the cold stops is TBD.

The maximum warping of the dichroics induced by the structure is TBD

Tilt 1 arcminute (TBC)

Allowable interface loads

TBD (by MSSL)

### Common structure – CFIL1 (4-K)

INTERFACE DATA SHEET

| SUBSYSTEM: Common structure – CFIL1 | UNIT CODE: 1.1/1.2.1 |  |
| --- | --- | --- |

| UNIT DESIGNATION TOTAL NUMBER: 1 IN OPERATION: 1 | IN REDUNDANCY: NA |
| --- | --- |

MECHANICAL CHARACTERISTICS DIMENSIONS [mm]: Circular – 100mm dia. TBC MASS (including fasteners) tbd + 20 % contingency C.G.LOCATION [mm] (wrt reference hole R) X: Y: Z: Uncertainty: Inertia (wrt C.G.) [m2kg]: Ixx: Iyy: Izz Uncertainty: MATERIAL OF HOUSING: NA SURFACE FINISH: TOTAL CONTACT AREA: SURFACE ROUGHNESS OF CONTACT AREA: EIGEN FREQUENCY: The first eigenfrequency of the filter shall be above TBD Hz FOOT THICKNESS:

THERMAL CHARACTERISTICS Common structure – CFIL1 FOOT MATERIAL AND THICKNESS: SURFACE PROPERTIES: Thermal capacity: J/(K Conductive coupling: W/(K

QUALIFICATION TEMPERATURE LIMIT ((C) Common Structure – CFIL1

| GROUND STORAGE &TRANS | OPERATING MODE | NON OPERATING MODE | START UP |
| --- | --- | --- | --- |
| MIN | MAX | MIN | MAX | MIN | MAX | MIN |
| 10 | 40 | -271 | 40 | -271 | 40 | -271 |

HEAT DISSIPATION (W) Common structure – CFIL1

| MODE | AVERAGE | MIN | MAX |
| --- | --- | --- | --- |
| OFF | NA | NA | NA |
| STAND-BY | NA | NA | NA |
| OPERATING | NA | NA | NA |

.

| SUBSYSTEM: | UNIT CODE: |
| --- | --- |

MECHANICAL INTERFACE CONTROL DRAWING Common structure– CFIL1

| Change control sheet |
| --- |
| Drawing Number |
| Issue | Date | Change |
| A |  |  |

| SUBSYSTEM: Common structure CFIL1 | UNIT CODE: 1.1/1.2.1 |
| --- | --- |

MECHANICAL INTERFACE CONTROL DRAWING Outer cover – CFIL1

Drawing …….  gives details of the Common structure – CFIL1  mechanical interface.

### Common structure – CFIL2 (4 K)

INTERFACE DATA SHEET

| SUBSYSTEM: Common structure – CFIL-2 | UNIT CODE: 1.1/1.2.1 |  |
| --- | --- | --- |

| UNIT DESIGNATION TOTAL NUMBER: 1 IN OPERATION: 1 | IN REDUNDANCY: NA |
| --- | --- |

MECHANICAL CHARACTERISTICS DIMENSIONS [mm]: Circular – TBD mm dia. MASS (including fasteners) tbd + 20 % contingency C.G.LOCATION [mm] (wrt reference hole R) X: Y: Z: Uncertainty: Inertia (wrt C.G.) [m2kg]: Ixx: Iyy: Izz Uncertainty: MATERIAL OF HOUSING: NA SURFACE FINISH: TOTAL CONTACT AREA: SURFACE ROUGHNESS OF CONTACT AREA: EIGEN FREQUENCY: The first eigenfrequency of the filter shall be above TBD Hz FOOT THICKNESS:

THERMAL CHARACTERISTICS Common structure – CFIL2 FOOT MATERIAL AND THICKNESS: SURFACE PROPERTIES: Thermal capacity: J/(K Conductive coupling: W/(K

QUALIFICATION TEMPERATURE LIMIT ((C) Common structure – CFIL2

| GROUND STORAGE &TRANS | OPERATING MODE | NON OPERATING MODE | START UP |
| --- | --- | --- | --- |
| MIN | MAX | MIN | MAX | MIN | MAX | MIN |
| 10 | 40 | -271 | 40 | -271 | 40 | -271 |

HEAT DISSIPATION (W) Common structure – CFIL2

| MODE | AVERAGE | MIN | MAX |
| --- | --- | --- | --- |
| OFF | NA | NA | NA |
| STAND-BY | NA | NA | NA |
| OPERATING | NA | NA | NA |

.

| SUBSYSTEM: | UNIT CODE: 1.1/1.2.1 |
| --- | --- |

MECHANICAL INTERFACE CONTROL DRAWING Common structure – CFIL2

| Change control sheet |
| --- |
| Drawing Number |
| Issue | Date | Change |
| A |  |  |

| SUBSYSTEM: Common structure – CFIL2 | UNIT CODE: |
| --- | --- |

MECHANICAL INTERFACE CONTROL DRAWING Common structure – CFIL2

Drawing …….  gives details of the Common structure – CFIL2 mechanical interface.

### OBP – beam splitters (SBS1 and SBS2)

INTERFACE DATA SHEET

| SUBSYSTEM: OBP – beam splitters | UNIT CODE: 1.1/1.2.1 |  |
| --- | --- | --- |

| UNIT DESIGNATION TOTAL NUMBER: 2 IN OPERATION: 2 | IN REDUNDANCY: NA |
| --- | --- |

MECHANICAL CHARACTERISTICS DIMENSIONS [mm]: Circular – 46 mm dia. MASS (including fasteners) tbd + 20 % contingency C.G.LOCATION [mm] (wrt reference hole R) SBS1 - X: Y: Z: Uncertainty: SBS2 - X: Y: Z: Uncertainty: Inertia (wrt C.G.) [m2kg]: SBS1 - Ixx: Iyy: Izz: Uncertainty: SBS2 - Ixx: Iyy: Izz : Uncertainty: MATERIAL OF HOUSING: NA SURFACE FINISH: TOTAL CONTACT AREA: SURFACE ROUGHNESS OF CONTACT AREA: EIGEN FREQUENCY: The first eigenfrequency of the filter shall be above TBD Hz FOOT THICKNESS:

THERMAL CHARACTERISTICS OBP – beam splitters FOOT MATERIAL AND THICKNESS: SURFACE PROPERTIES: Thermal capacity: J/(K Conductive coupling: W/(K

QUALIFICATION TEMPERATURE LIMIT ((C) OBP – beam splitters

| GROUND STORAGE &TRANS | OPERATING MODE | NON OPERATING MODE | START UP |
| --- | --- | --- | --- |
| MIN | MAX | MIN | MAX | MIN | MAX | MIN |
| 10 | 40 | -271 | 40 | -271 | 40 | -271 |

HEAT DISSIPATION (W) OBP – beam splitters

| MODE | AVERAGE | MIN | MAX |
| --- | --- | --- | --- |
| OFF | NA | NA | NA |
| STAND-BY | NA | NA | NA |
| OPERATING | NA | NA | NA |

.

| SUBSYSTEM: OBP – beam splitters | UNIT CODE: 1.1/1.2.1 |
| --- | --- |

MECHANICAL INTERFACE CONTROL DRAWING OBP – beam splitters

| Change control sheet |
| --- |
| Drawing Number |
| Issue | Date | Change |
| A |  |  |

| SUBSYSTEM: OBP – beam splitters | UNIT CODE: 1.1/1.2.1 |
| --- | --- |

MECHANICAL INTERFACE CONTROL DRAWING OBP – beam splitters

Drawing …….  gives details of the OBP – beam splitters  mechanical interface.

### PDBX – PFIL3 (2 K cold stop)

INTERFACE DATA SHEET

| SUBSYSTEM: PDBX – PFIL3 | UNIT CODE: 1.1/1.2.1 |  |
| --- | --- | --- |

| UNIT DESIGNATION TOTAL NUMBER: 1 IN OPERATION: 1 | IN REDUNDANCY: NA |
| --- | --- |

MECHANICAL CHARACTERISTICS DIMENSIONS [mm]: Circular – 54 mm dia. MASS (including fasteners) tbd + 20 % contingency C.G.LOCATION [mm] (wrt reference hole R) X: Y: Z: Uncertainty: Inertia (wrt C.G.) [m2kg]: Ixx: Iyy: Izz: Uncertainty: MATERIAL OF HOUSING: NA SURFACE FINISH: TOTAL CONTACT AREA: SURFACE ROUGHNESS OF CONTACT AREA: EIGEN FREQUENCY: The first eigenfrequency of the filter shall be above TBD Hz FOOT THICKNESS:

THERMAL CHARACTERISTICS PDBX – PFIL3 FOOT MATERIAL AND THICKNESS: SURFACE PROPERTIES: Thermal capacity: J/(K Conductive coupling: W/(K

QUALIFICATION TEMPERATURE LIMIT ((C) PDBX – PFIL3

| GROUND STORAGE &TRANS | OPERATING MODE | NON OPERATING MODE | START UP |
| --- | --- | --- | --- |
| MIN | MAX | MIN | MAX | MIN | MAX | MIN |
| 10 | 40 | -271 | 40 | -271 | 40 | -271 |

HEAT DISSIPATION (W) PDBX – PFIL3

| MODE | AVERAGE | MIN | MAX |
| --- | --- | --- | --- |
| OFF | NA | NA | NA |
| STAND-BY | NA | NA | NA |
| OPERATING | NA | NA | NA |

.

| SUBSYSTEM: PDBX – PFIL3 | UNIT CODE: 1.1/1.2.1 |
| --- | --- |

MECHANICAL INTERFACE CONTROL DRAWING PDBX – PFIL3

| Change control sheet |
| --- |
| Drawing Number |
| Issue | Date | Change |
| A |  |  |

| SUBSYSTEM: PDBX – PFIL3 | UNIT CODE: 1.1/1.2.1 |
| --- | --- |

MECHANICAL INTERFACE CONTROL DRAWING PDBX – PFIL3

Drawing …….  gives details of the PDBX – PFIL3 mechanical interface.

### SDBX – SFIL3L/S (Spectrometer 2 K cold stops)

INTERFACE DATA SHEET

| SUBSYSTEM: SDBX – SFIL3 | UNIT CODE: 1.1/1.2.1 |  |
| --- | --- | --- |

| UNIT DESIGNATION TOTAL NUMBER: 2 IN OPERATION: 2 | IN REDUNDANCY: NA |
| --- | --- |

MECHANICAL CHARACTERISTICS DIMENSIONS [mm]: Circular – 43 mm dia. (TBC) MASS (including fasteners) tbd + 20 % contingency C.G.LOCATION [mm] (wrt reference hole R) SFIL3L - X: Y: Z: Uncertainty: SFIL3S - X: Y: Z: Uncertainty: Inertia (wrt C.G.) [m2kg]: SFIL3L - Ixx: Iyy: Izz Uncertainty: SFIL3L - Ixx: Iyy: Izz Uncertainty: MATERIAL OF HOUSING: NA SURFACE FINISH: TOTAL CONTACT AREA: SURFACE ROUGHNESS OF CONTACT AREA: EIGEN FREQUENCY: The first eigenfrequency of the filter shall be above TBD Hz FOOT THICKNESS:

THERMAL CHARACTERISTICS SDBX – SFIL3 FOOT MATERIAL AND THICKNESS: SURFACE PROPERTIES: Thermal capacity: J/(K Conductive coupling: W/(K

QUALIFICATION TEMPERATURE LIMIT ((C) SDBX – SFIL3

| GROUND STORAGE &TRANS | OPERATING MODE | NON OPERATING MODE | START UP |
| --- | --- | --- | --- |
| MIN | MAX | MIN | MAX | MIN | MAX | MIN |
| 10 | 40 | -271 | 40 | -271 | 40 | -271 |

HEAT DISSIPATION (W) SDBX – SFIL3

| MODE | AVERAGE | MIN | MAX |
| --- | --- | --- | --- |
| OFF | NA | NA | NA |
| STAND-BY | NA | NA | NA |
| OPERATING | NA | NA | NA |

.

| SUBSYSTEM: SDBX – SFIL3 | UNIT CODE: 1.1/1.2.1 |
| --- | --- |

MECHANICAL INTERFACE CONTROL DRAWING SDBX – SFIL3

| Change control sheet |
| --- |
| Drawing Number |
| Issue | Date | Change |
| A |  |  |

| SUBSYSTEM: SDBX – SFIL3 | UNIT CODE: 1.1/1.2.1 |
| --- | --- |

MECHANICAL INTERFACE CONTROL DRAWING SDBX – SFIL3

Drawing …….  gives details of the SDBX – SFIL3 mechanical interface.

## Harness interface data sheets

NA

HARNESS LAYOUT

NA

HARNESS LAYOUT

NA

## Optical interface data sheets

INTERFACE DATA SHEET

| SUBSYSTEM: | UNIT CODE: |
| --- | --- |

OPTICAL CHARACTERISTICS

| SUBSYSTEM: | UNIT CODE: |
| --- | --- |

OPTICAL INTERFACE CONTROL DRAWING

| Change control sheet |
| --- |
| Drawing Number |
| Issue | Date | Change |
| A |  | New issue |

| SUBSYSTEM: | UNIT CODE: |
| --- | --- |

OPTICAL INTERFACE CONTROL DRAWING

Drawing ………….. gives details of the subsystem a to subsystem b  optical interface

# Appendix A – Proposed mounts for filter components

This appendix shows conceptual designs for the various filter components.

Figure 4-1 Proposed mount for spectrometer beam splitters (SBS1 & SBS2)

Figure 4-2 Proposed mount for photometer dichroics (PDIC1 shown)

Figure 4-3 Proposed mount for hot-pressed filters