FIRST/PLANK - EMC & POWER QUESTIONNAIRE FOR PAYLOADS

PAYLOAD NAME:

REFERENCE PERSON:

- Power Interface Requirement

Please describe the expected power interface of the experiment with the satellite bus through a table, (see example below) specifying the name and type of power line required and, possibly, the LCL class associated to them.

Example:

| Function | Number of main lines required | Number of redundant lines required | LCL class eg 1,2,4,7A |
| --- | --- | --- | --- |
| + 28 V primary power | 1 | 1 | (109W/4A Trip-off limit) |
| +28 V primary power (heaters) | 1 | 1 | (28W/1A Trip-off limit) |
| Keep alive supply 7 – 9V | 0 | 0 | 1W max per line |

Note

The inrush current of the instrument should be limited to <1.5 times the LCL peak value and of duration < 0.5 msec. The rate of change of the inrush current shall not exceed 1A/micro sec

- Instrument Power Distribution Block Diagram and Redundancy Approach

Please describe the expected instrument internal power distribution block diagram and the redundancy concept within the instrument.

- Instrument Power Requirements

Please provide the preliminary power requirements for the instrument for each operational mode specifying the power through a table or, if necessary through a current versus time diagram.

Example:

| Experiment interface | Operational mode …….. Average Power | Peak Power and duration |
| --- | --- | --- |
| +28 Pr. Power |  |  |

Furthermore, state whether DC/DC converter synchronisation is required and, in the affirmative case, provide the relevant rationale.

- Instrument Grounding Diagram

Please describe with suitable drawings the grounding diagram that you expect to implement in your experiment, including the grounding of the harness shielding.

- Interconnecting Harness Block Diagram

Please describe the interconnecting harness block diagram within the instrument’s subsystems, specifying the expected length and the type of the signals.

- Instrument Susceptibilities

Please specify the frequencies and the levels for which you expect your instrument, or its parts/components, to be susceptible (Voltage and Current ripple, Electric Fields, Magnetic Fields, etc.).

- Instrument Emissions

Please specify the frequencies and the levels you expect your instrument will emit (Voltage and Current ripple, Electric Fields, Magnetic Fields, etc.).

- Instrument Frequency Plan

Please establish a frequency plan for your instrument assembly, including switching frequencies of power supplies, clocks, IF amplifiers etc. Information on pulse width, amplitude, rise and fall times of clocks are highly desirable.

- Detailed questions on EMC

- Does your instrument require electrostatic or magneto-static cleanliness at spacecraft level?

- What is the topology of the electronic interfaces you are considering in the instrument design? (E.g. single ended-differential, balanced-differential, etc.). If available, please give an interface circuit diagram.

- Do you believe your experiment be compliant to the ISO EMC requirements, which are presently assumed as a reference? Please try to establish a compliance matrix with the ISO EMC requirements.

- Do you expect your experiment be vulnerable to Electrostatic Discharge (say 10 kV, 5.6 mJ)?

- Do you believe it is mandatory to use a static screen for the converters’ transformers in order to minimise the winding capacitance and enhance AC de-coupling between primary and secondary power?

- Do you expect your experiment be vulnerable to voltage common mode transients? Which peak value and time characteristics?

- What is the EMC verification concept you plan to implement in the development phases of your instrument?

- What are the major concerns of your instrument from the EMC discipline point of view?