FIRST/SPIRE

WE Subsystem Specification Template

PROPOSAL

|  | Reference: Issue: Date: Author: | SPIRE-SAp-xxxx-99 Draft 0.2 7 - April - 2000 J-L.Auguères |  |
| --- | --- | --- | --- |

TABLE OF CONTENT

FOREWORDS	4

Purpose of the template.	4

Scope.	4

Notification.	4

1	INTRODUCTION.	5

1.1	Purpose.	5

1.2	Scope.	5

2	Subsystem Analysis (Cryo-Cooler example)	6

2.1	Overall description.	6

2.2	Requirements.	6

2.3	WE Subsystem I/F.	6

2.4	Block Diagram.	7

2.5	Criticality Analysis.	7

2.6	Functional Diagrams.	7

2.7	Subsystem States.	8

2.7.1	Status Diagram.	8

2.7.2	State Definition.	8

2.8	Status / Event relationship.	8

2.8.1	Event Definition.	8

2.8.2	Status Table.	9

2.8.3	State Transition Actions.	9

2.9	States vs. Controls.	9

2.10	Internal control algorithms.	10

2.10.1	Cold Finger temperature regulation.	10

2.10.2	Cryo-Cooler Recycling.	11

2.11	Setting Parameter list.	12

2.12	H/K list.	12

2.13	WE Implementation.	12

2.13.1	Subsystem Telecommands.	12

2.13.2	Subsystem S/W	13

2.13.3	Subsystem Dedicated Electronics.	13

3	WE Subsystem Dedicated Electronics implementation	14

3.1	Overall description.	14

3.2	Main Specifications.	14

3.3	Electronics Block-Diagram.	14

3.4	External I/F and Connection.	14

3.5	Detailed description.	14

3.5.1	Block 1.	14

3.5.2	Block 2.	14

3.5.3	Block n.	14

3.6	Power Supply.	14

3.7	Grounding Scheme.	14

3.8	Mechanical implementation.	14

3.9	Budgets.	14

3.10	Use of Special Components.	14

DOCUMENTATION

Applicable Documents

Reference Documents

[R1]	SPIRE Warm Electronics Subsystem requirements - Draft - Sept. 19, 1999 -
L.Vigroux.

[R2]	FIRST/SPIRE Warm Electronics Requirement Document - Draft 0.2 - Aug. 10,1999

[R2]	FIRST/SPIRE WE Subsystem Analysis Plan and Guidelines for the WE review -
Draft 0.1 – 8 – October – 2000.

ACRONYM LIST

AIV	Acceptance, Integration and Validation

BSM	Beam Steering Mirror

CEA	Commissariat à l'Energie Atomique

DPU	Data Processing Unit

DRCU	Detector Readout Control Unit

FIRST	Far InfraRed Submillimetre Telescope

FTS	Fourier Transform Spectrometre

H/K	HouseKeeping

ICD	Interface Control Document

IID	Instrument Interface Document

IRD	Instrument Requirements Document

LAM	Laboratoire d'Astrophysique de Marseille

PDR	Preliminary Design Review

QMW	Queen Mary and Westfield College

RAL	Rutherford Appleton Laboratory

SADT	Structured Analysis Design Technique

SAp	Service d'Astrophysique

SMEC	Spectrometer MEChanism

SPIRE	Spectral and Photometric Imaging REceiver

TBC	To Be Confirmed

TBD	To Be Defined

TBW	To Be Written

WE	Warm Electronics

WERD	Warm Electronics Requirement Document

# FOREWORDS

## Purpose of the template.

The purpose of this template is to propose a standardised layout for the WE subsystem specification documents to be produced for each subsystems. This template is broadly identical to the one provided as viewgraph presentation guidelines for the Dec. 99 WE review. These documents are intended to be used as:

- presentation material for the SPIRE delta PDR.

- subsystem specification for the Warm Electronics.

- inputs for the specification of the DRCU simulator.

This template is applicable for the following SPIRE WE Subsystems:

Subsystems						Resp. Institute

- Beam Steering Mirror				ATC/LAM

- FTS						LAM

- Cryo-Cooler.					SBT/SAp

- Calibrators						GSFC

- House keeping					SAp

- Feed horn						JPL/SAp

## Scope.

The Scope of this document concerns only the Warm Electronics view of the considered SPIRE Subsystems. However the WE part of each Subsystem has to be presented along with its respective environment (as a part of a whole SPIRE Subsystem).

Two aspects are addressed in this document:

- the WE Subsystem Analysis which concern the Subsystem requirements and functionality.

- the WE Subsystem Architecture and Design.

## Notification.

In order to illustrate the application of the guidelines, an example using the Cryo-Cooler WE  Subsystem has been set. However the information given on this Subsystem are only to be considered as illustration of the principles and do not reflect the reality (in particular, the temperature regulation of the head of the cryo-cooler is no longer considered).

# INTRODUCTION.

## Purpose.

## Scope.

# Subsystem Analysis (Cryo-Cooler example)

This Section is intended to provide a comprehensive description for each WE Subsystem with regard to their respective WE requirements and functionality. It aims to allow the identification of all the parameters (Settings, H/K, Control Lines) as well as the Monitoring and Control actions. The implementation itself  is out of the scope of this section. However, the implementation sharing between the various implementation level is considered (Tele-Commands, S/W task, dedicated electronics). Finally this section should provide rather comprehensive specifications for the use of S/W implementation.

## Overall description.

Description of the subsystem and its functionality (Cf. Laurent's logical block diagrams in the SPIRE WE subsystem requirement document).

The cryo-cooler provide the appropriate temperature to the detector. Its equilibrium temperature is about 300 mK. The cooler is based on He3 sorption on charcoal. The system must be recycled every 48 hours. The recycling time duration is 2 hours, including cooling time after the recycling. The temperature of the detector is determined by fixed thermal impedance between the cryo-cooler and the detector base plate. The equilibrium temperature of the system is determined by changing the thermal conduction of the heat switches which connect the cryo-cooler to the LHe tank of FIRST. These Heat Switches are based on small tube filled with He3 and containing a small amount of coal. When heated, the charcoal outgas He3 and the conduction of the switch increases. Cooling the charcoal create vacuum inside the tube, making the thermal conduction very low.

## Requirements.

List of the requirements related to the WE Subsystem. They shall be consistent with the WE Subsystem requirements (see the WERD).

| 7 | Shall be able to monitor the Cryo-cooler system. |
| --- | --- |
| 7.1 | Shall be able to control the regeneration cycle |
| 7.2 | Shall be able to regulate the temperature stability better than TBD mK at 0.015 Hz at a maximum power dissipation. |

## WE Subsystem I/F.

List of the I/F requirements between the WE Electronics and the proper Subsystem. Only the logical and functional aspects  have to be considered here. Implementation details as number, type or impedance of wires and connector type and pin-out  will be considered in the respective ICDs.

| I/F | Type | Nb. | I/O | Min. | Max. | Constraints |
| --- | --- | --- | --- | --- | --- | --- |
| Sorption Pump Heater | Analog Current | 2 | Out | 0 mA | 20 mA | 400 ( load |
| Thermal Switch Control | Analog Current | 4 | Out | 0 mA | TBD | load? |
| Cold Finger Temperature | Temp. Sensor (TBD) | 2 | In |  |  |  |
| Pump Heater Current | Analog | 2 | In |  |  |  |

## Block Diagram.

Logical block diagram representing the subsystem considered together with its WE parts. (Cf. Laurent's logical block diagrams in the SPIRE WE subsystem requirement document).

## Criticality Analysis.

Demonstrate that the proposed subsystem design fulfil the reliability requirements mainly:

- No single point failure.

- No propagation failure.

## Functional Diagrams.

To illustrate the various functionality of the subsystem, a description by the mean of functional chart can be provided (e.g. SADT functional diagrams).

## Subsystem States.

### Status Diagram.

The behaviour of most of the subsystems can be described by the mean of Status Diagrams showing the various states in which the Subsystem could be and the relationship between these States. Transition between states are triggered by Events (or any combination of them).

### State Definition.

List of each state along with their respective definition.

| N° | States | Definition |
| --- | --- | --- |
| 0 | Init | C.Cooler elect. is Switched On, H/K Monitoring Active. |
| 1 | St-by/C.down | Waiting State or Cooling Down waiting State. |
| 2 | CF regulation | Cryo-Cooler Cold Finger Temp. within the regulation limit. Regulation algorithm Active. |
| 3 | Recycling | Pump Heater(s) Activated. |

## Status / Event relationship.

### Event Definition.

The Events which when arising could modify the State of the Subsystem have to be defined.

| Events | Definition | Origin |
| --- | --- | --- |
| Activate Subsystem | Electronics Power On / Active Subs. Control | TC |
| De-Activate Subsystem | Electronics Power Off / De-Active Subs. Control | TC |
| Pump Heater 1/2 On | Pump Heater 1/2 switch on | TC |
| Pump Heater 1/2 Off | Pump Heater 1/2 switch off | TC or Time-Out or Current Overload |
| Temp. Regul. On | Temperature regulation of the Cooler head activated | TC |
| Temp. Regul. Off | Temperature regulation of the Cooler head de-activated | TC |
| CC. T. Out of Limit | Temperature on the Cryo-Cooler Cold Finger cross the max. limit. | Self-diagnostic |
| Subs. Fault | Cryo-cooler subsystem fault detected on the Subsystem | Self-diagnostic |

### Status Table.

This table shows the various events which could arise and their impacts on the evolution of the Subsystem current State. The various possible States are those described in the previous section

| N° | States | Fault | Activ. | De-Activ | P.Heat. On | P.Heat Off | T.Reg. On | T.Reg. Off | CC T. Out |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | Init | 0 | 1 | 0 | Error | - | Error | - | - |  |
| 1 | Standby | 0 | 1/Error | 0 | 3 | - | 2/1 | - | 1 |  |
| 2 | FP regul. | 0 | 1/Error | 0 | 3 | - | - | 1 | 1 |  |
| 3 | Recycling | 0 | 1/Error | 0 | - | 1 | Error | - | - |  |

### State Transition Actions.

This section provides the list and the respective description of all the actions to be carried out when stepping from one State to another.

| N° | States | Fault | Activ. | De-Activ | P.Heat. On | P.Heat Off | T.Reg. On | T.Reg. Off | CC T. Out |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | Init | A | B | A | - | - | - | - | - |  |
| 1 | Standby | A | B/- | A | C | - | D/- | - | B |  |
| 2 | FP regul. | A | B/- | A | C | - | - | B | B |  |
| 3 | Recycling | A | B/- | A | - | B | - | - | - |  |

| Actions | Descriptions |
| --- | --- |
| A |  |
| B |  |
| C |  |
| D |  |

## States vs. Controls.

For each state, the status of the various internal or external Controls (WE output, internal flags,...) could be defined by a dedicated table.

| N° | States | CC head Th. Sw. | CC Pump Th. Sw. | Pump Heater Sw. |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | Init | Off | Off | Off |  |  |  |  |  |  |
| 1 | Standby | Off | On | Off |  |  |  |  |  |  |
| 2 | FP regul. | Regul. | On | Off |  |  |  |  |  |  |
| 3 | Recycling | Off | Off | On |  |  |  |  |  |  |

## Internal control algorithms.

Dedicated complex functionality have to be described independently from their possible implementation (Tele-commands, Pure S/W, Electronics or any combination of them.

For each of such functionality, it is proposed to describe them using the following Plan:

- List of the States in which the functionality is Active.

- List of the Input Parameter (H/K, Setting, Computed Value,...)

- List of the Output Parameters.

- Description of the Algorithm.

### Cold Finger temperature regulation.

| Activ. State(s) | 2 |
| --- | --- |

Input Parameters:

| Label | Parameter | Origin | Type | Unit. | Min | Max | Accur |
| --- | --- | --- | --- | --- | --- | --- | --- |
| T_CC-HEAD | Temp. on the head of the Cryo-Cooler | H/K | Real | mK |  |  |  |
| T_REGUL_CF | Regul. Temp. of the head of the CC | Setting | Real | mK | 290 | 350 | 10 |
| T_FING_MAX | Maximum temp. on the Cold Finger | Setting | Real | mK |  | 350 |  |
| D_CF_REGUL | Max. Regulation Gap | Setting | Real | mK |  | 2.5 |  |

Output Parameters:

| Label | Parameter | Type | Unit. | Min | Max | Accur |
| --- | --- | --- | --- | --- | --- | --- |
| CC_HD_T_SW_1 | Thermal Switch on Cryo-Cooler's Head n°1 | On/Off |  |  |  |  |
| CC_HD_T_SW_2 | Thermal Switch on Cryo-Cooler's Head n°2 | On/Off |  |  |  |  |

Algorithm Description:

The algorithms can be described by the means of either a Chart or Pseudo-language or by a simple formulae. Depending on the kind of "algorithm" to be considered, 3 sequences could have to be described:

- an "Init sequence" which is to be run when starting the "algorithm" activity (e.g. when the State transition to one of the active State occurs) (see 2.8.3).

- a Periodic sequence which is run at a determined rate.

- a Closing sequence which is run when leaving from one of the active State (see 2.8.3).

Init Sequence:

Begin;

End;

Periodic Sequence: Activation rate 1s.

Begin;

If the "Temp. on CC's Head" < "CF Max Limit"

Then

If the "Temp. on CC's Head" - "Regul. Temp" > 2 mK

Then Switch On the "Head Thermal Switch";

Else Switch Off the "Head Thermal Switch";

Else

Flag the CF "Out of Limit" event;

Switch Off the "Head Thermal Switch";

End If;

End;

Closing Sequence:

Begin;

End;

### Cryo-Cooler Recycling.

| Activ. State(s) | 3 |
| --- | --- |

Input Parameters:

| Label | Parameter | Origin | Type | Unit. | Min | Max | Accur |
| --- | --- | --- | --- | --- | --- | --- | --- |

Output Parameters:

| Label | Parameter | Type | Unit. | Min | Max | Accur |
| --- | --- | --- | --- | --- | --- | --- |

Algorithm Description:

Init Sequence:

Begin;

End;

Periodic Sequence: Activation rate 1s.

Begin;

If the "Pump Heater Current" > "Pump Heater Current limit" Then generate a "Fault" event;

If the recycling time is over Then generate a "Time-Out" event;

End;

Closing Sequence:

Begin;

End;

## Setting Parameter list.

List of all the Setting Parameters to be set up (basically by the means of Tele-commands).

| Label | Parameter | Unit | Comment |
| --- | --- | --- | --- |
| T_FING_MAX | Maximum temp. on the Cold Finger | mK | No temp. regul. above this temp. |
| T_REGUL_CF | Temp. regulation setting on Cold Finger | mK |  |
| CC-REC-TIME | Recycling Time | sec. |  |
| CF-REG-DELT | Max Regulation Gap for the Cold Finger | mK |  |
| HEAT_CUR-L | Current Limit in the Pump Heaters | mA |  |
| HEAT_CUR_P1 | Setting value for the Heater Current of Pump 1 | mA |  |
| HEAT_CUR_P2 | Setting value for the Heater Current of Pump 2 | mA |  |

## H/K list.

List of the H/K generated by the Subsystem apart from the Setting Values which should be systematically mirrored).

| Label | Parameter | Type | Unit. | Min | Max | Rate | Accur |
| --- | --- | --- | --- | --- | --- | --- | --- |
| C_COOL_STATE | Current State Number | Int. |  |  |  |  |  |
| C_COOL_FAULT | Fault Flag | Bin. |  |  |  |  |  |
| CF_TEMP | Temperature on the Cold Finger | Analog | mK |  |  | 1s. | 1mK |
| HEAT_CUR_1 | Current measured in the Pump Heater 1 | Analog | mA |  |  | 1s. | 1mA |
| HEAT_CUR_2 | Current measured in the Pump Heater 2 | Analog | mA |  |  | 1s. | 1mA |

## WE Implementation.

This section aims to describe the way, the WE functions of the Subsystem are likely to be implemented

.

### Subsystem Telecommands.

List of the Subsystem dedicated Tele-Commands (a part from the parameter setting commands which are handled independently).

| Tele-Command | Function and Parameters |
| --- | --- |
|  | Cryo-Cooler Subsystem Activation / De-activation (Flag setting) |
|  | Pump Heater 1 Activation / De-activation (Flag setting) |
|  | Pump Heater 2 Activation / De-activation (Flag setting) |
|  | Temp. Regulation Activation / De-activation (Flag setting) |

### Subsystem S/W

List of the functions to be implemented by S/W either at DPU or DRCU level.

S/W Functions

All overall Monitoring & Control functionality

Cold Finger Temperature Regulation algorithm.

Cryo-Cooler Recycling algorithm.

### Subsystem Dedicated Electronics.

List of the functions to be implemented by the means of dedicated electronics (H/W).

Electronics (H/W) Functions

Temperature Sensor measurement electronics.

Pump Heater Current generators.

Pump Heater Current measurement electronics.

# WE Subsystem Dedicated Electronics implementation

This Section is intended to describe the features and the architecture of the Subsystem dedicated electronics (i.e. electronics circuitry and interconnection including complex circuits like FPGAs and/or dedicated micro-controllers. This Section is referring to the electronics items given in 2.13.3

## Overall description.

## Main Specifications.

## Electronics Block-Diagram.

## External I/F and Connection.

## Detailed description.

### Block 1.

### Block 2.

.

.

.

.

### Block n.

## Power Supply.

## Grounding Scheme.

## Mechanical implementation.

## Budgets.

## Use of Special Components.

# Footnotes

SADT: Structured Analysis Design Technique.

# Text boxes

Recycling

CF regulation

3

2

Standby / C.Down

1

Init

0