Introduction:

The cryostat study team wishes to investigate the impact of instrument operations on the thermal stability of the three levels within the FIRST cryostat.  The SPIRE instrument will undergo several mode changes during its operations that might affect the thermal stability of the gas cooled temperature stages.  In this note two examples of mode changes are offered for analysis: going from a warm cooler to a cold (300 mK) one – Cooler Recycling – and changing from photometer to spectrometer operation.

SPIRE Cooler Recycling:

During the ground contact period, the SPIRE instrument will go from its observing state to the Cooler recycle mode and then back to its observing state.  During this time the cooler will be recycled leading to a large thermal load on the strap to the LHe tank.  Following recycling the detectors are switched on again and the mechanisms etc set to their operating points.  In the first transient analysis case the instrument is supposed to perform a calibration operation and then be set to observe a source using the beam steering mirror in full chop mode.  In the table below the thermal dissipation at the various levels is crudely represented as a timeline for the JFET detector option.  The other detector options can be substituted by reference to the input data presented by the SPIRE team to the Cryostat Study.

| Time (h:mm:ss) | Sub-system | Status | Temp Stage | Power Dissipation* |
| --- | --- | --- | --- | --- |
| 0:00:00 | Cold Read-out Electronics | OFF | L2 | 0 |
| 0:00:00 | Cold Mechanisms/calibrators | OFF | L1 | 0 |
| 0:00:00 | Cooler | OFF | L0 | 0 |
| 0:00:01 | Cooler evaporator HS Cooler pump HS | ON OFF | L0 L0 | 1 W (Transient) |
| 0:00:02 | Cooler heater | ON | L0 | 90 mW |
| 0:30:00 | Cooler heater | OFF | L0 | 0 |
| 0:30:01 | Cooler evaporator HS Cooler pump HS | OFF ON | L0 L0 | ? (Sorption pump heaters) |
| 0:30:00 to 2:00:00 | Cooler/detectors | Cryopumping to 300 mK | L0 | 0 |
| 2:00:00 | Cold Readout Electronics | ON | L2 | 33 mW |
| 2:10:00 | Calibrator | ON | L1 | 2 mW |
| 2:12:00 | Calibrator | OFF | L1 | 0 mW |
| 2:12:01 | Beam Steering Mirror | ON (Chop 5 Hz) | L1 | 4 mW |

Table 1: Timeline for cooler recycling.