05 FEB '99 15:25	FIRST/FLPr~CK PROJ.+31 71 5655244 	FA/1

TO RPL KIMG

FIRST/Planck Project Telefax

Fax No : (31) 71 565 5244

Tel. No : (31) 71 565 5962

Ref.	:	PT-06359	Date	4 February, 1999

From	:	T. Passvogel (SCI-PT)	Page	1 of 1

To		M. Griffin (OMWC/London)	Fax No:	44 181 980 0986

K. King (RAUOxfordshire)		44 1235 44 6667

A. Pogiltsch (MPE/Garching)		49 89 3299 3292

0. Bauer (MPE/Garching)		49 89 3299 3569

Th. de Graauw (SRON/Groningen)		0503634033

H. Aarts (SRON/Utrecht)		0302540860

Copy	SCI-PT F. Felici, M. Anderegg, H. Schaap, B, Guillaume, M. von Hoegen

SCI-SA G. Pilbratt

Subject:	FIRST Telescope Design

Dear all,

During the last quarterly progress meeting on the FIRST telescope we learned that the telescope consists of pie-shaped elements. The specific question 1 want to raise and ask for your support is related to the design.

Assume as a worst case that the front faces (pie segments) are not connected, but separated by a 2mm wide gap (c:zl).

Further assume that there will be gradient in temperature between the segment of order of 0.5 K.

Note that three of six "gaps" will be for the outer part "shadowed" by the tripod legs.

Could you confirm that even under the above worst case assumptions, the design would not impact the instrument performances (considering off-axis position of instruments and chopping). A quick answer would be appreciated.

Best regards,

T. Passvogel

ESTEC

Pastbus R99 - N1 2200 AG NoAwilk - Kaplaticon 1 . N1 2201 AZ Noorkik M

-- hilp~/itl.tgd.int/plun(k