| HERSCHEL - SPIRE Spectrometer Mirror Mechanism subsystem specifications File : lam.pjt.spi.spt.20000208_smec_specifications.doc |  |
| --- | --- |

| Prepared by : | Date : |
| --- | --- |
| Dominique Pouliquen | 12 Oct 2001 |
| Checked by : | Date : |

Distribution List

| RAL | Ken J. King | X | Bruce M. Swinyard | X |
| --- | --- | --- | --- | --- |
| ATC | Colin Cunningham | X | Ian Pain | X |
| CEA-Sap | Jean-Louis Auguères | X | Christohe Cara | X |
| CNES | Yvan Blanc | X | Martine Joubert | X |
| DESPA | Guy Michel | X |  |  |
| GSFC | Don. E. Jennings | X | David Walser |  |
| LAM | Bruno Travers | X | Jean-Paul Baluteau | X |
|  | Claude Colin | X | Pascal Dargent | X |
|  | Kjetil Dohlen | X | Didier Ferrand | X |
|  | Michel Jevaud | X | Patrick Levacher | X |
|  | Alain Origné | X | Dominique Pouliquen | X |

Document change record

| Date | Indice | Remarks |
| --- | --- | --- |
| 11 Feb 2000 | 1 | Creation of the document |
| 14 Apr 2000 | 2 | Update of performances specifications following an internal meeting at LAM with JP Baluteau. |
| 25 Apr 2000 | 3 | Design description added. |
| 9 May 2000 | 4 | Adjustements after LAM reading Mission profile added Product tree added |
| 26 June 2000 | 5 | Adjustements according to systems budgets, optical error budget and IID-A Subsystem description and product tree suppressed, see reference document |
| 20 Dec 2000 | 6 | Filtering bandwidth added to the P10 specification Number of cycles for the on ground lifetests added Specifications for SMECm and MCU separated |
| 12 Apr 2001 | 7 | FIRST replaced by HERSCHEL Reference of documents updated Adjustments on the on-ground lifetime Shocks suppressed. |
| 12 Oct 2001 | 8 | Most of TBD's suppressed |

Glossary

AD	Applicable Document

AVM	Avionic Model

BOL	Begin Of Life

BSM	Beam Steering Mirror

BSMm	BSM cryogenic mechanism

CEA	Commissariat à l'Energie Atomique

CDR	Critical Design Review

CNES	Centre National des Etudes Spatiales

CoG	Center of Gravity

CQM	Cryogenic Qualification Model

DDR	Detailed Design Review

DESPA	Département des Etudes SPAtiales

DM	Development Model

DPU	Digital Processing Unit

DRCU	Digital Read-out and Control Unit

DSP	Digital Signal Processor

EGSE	Electrical Ground Support Equipment

EM	Electrical Model

EOL	End Of Life

ESA	European Space Agency

FPU	Focal Plane Unit

FS	Flight Spare model

FTS	Fourier Transform Spectrometer

GSFC	Goddard Space and Flight Center

H/K	House Keeping

H/W	Hardware

I/F	Interface

JPL	Jet Propulsion Laboratory

LAM	  Laboratoire d'Astrophysique de     Marseille

MAC	Multi Axis Controller

MCU	Mechanism Control Unit

MGSE	Mechanical Ground Support Equipment

MM	Mechanical Model

MSSL	Mullard Space Science Laboratory

NA	Not Applicable

OGSE	Optical Ground Support Equipment

PDR	Preliminary Design Review

PFM	Prototype Flight Model

RAL	Rutherford Appleton Laboratory

RD	Reference Document

S/C	Spacecraft

S/W	Software

SMEC	Spectrometer mirror MEChanism

SMECm	SMEC cryogenic mechanism

SPIRE		Spectral and Photometric Imaging REceiver

TBC	To Be Confirmed

TBD	To Be Defined

TBU	To Be Updated

TBW	To Be Written

TC	TeleCommands

TM	TeleMetry

WE	Warm Electronics

Table of contents

1. Scope of the document	5

2. Documents	5

2.1. Applicable documents	5

2.2. Reference documents	5

3. The SMEC Subsystem	6

3.1. General overview	6

3.2. Description of the spectrometer mirror mechanism subsystem	6

3.3. Mission profile	6

3.3.1. SMECm mission profile	6

3.3.2. MCU Mission profile	7

3.4. Product trees	8

4. SMEC Performances Requirements	9

5. SMECm Requirements	10

5.1. Technical requirements	10

5.2. Operational requirements	10

5.2.1. Relialibility	10

5.2.2. Lifetime	11

5.2.3. Operating modes	11

5.2.4. Telemetry	11

5.2.5. Telecommands	11

5.3. Interface requirements	11

5.4. Design and manufacture requirements	11

5.4.1. Design requirements	11

5.4.2. Manufacture requirements	11

5.5. Logistic requirements	12

5.6. Environment requirements	12

5.6.1. Natural environement	12

5.6.2. Operating environment	12

5.7. Verification requirements	12

6. MCU Requirements	13

6.1. Technical requirements	13

6.2. Operational requirements	13

6.2.1. Relialibility (see AD1)	13

6.2.2. Lifetime	13

6.2.3. Operating modes	14

6.2.4. Telemetry	14

6.2.5. Telecommands	14

6.3. Interface requirements	15

6.4. Design and manufacture requirements	15

6.4.1. Design requirements	15

6.4.2. Design rules	15

6.4.3. Manufacture requirements	15

6.5. Logistic requirements	15

6.6. Environment requirements	16

6.6.1. Natural environement	16

6.6.2. Operating environment	16

6.7. Verification requirements	16

# Scope of the document

This specification defines the requirements applied to the performances, the design and the qualification of the SPIRE spectrometer mirror mechanism. It is applicable to the PFM and the FS.

# Documents

## Applicable documents

|  | Title | Author | Reference | Date |
| --- | --- | --- | --- | --- |
| AD1 | Instrument Requirements Document | B.M.Swinyard | SPIRE-RAL-PRJ-000034 Issue 1.0 | 23 Nov 2000 |
| AD2 | ICD Structure - Mechanical I/F | B.Winter | SPIRE/MSS/PRJ/000617 Issue 1.0 | Apr 2001 |
| AD3 | MCU / DPU Command list ICD | D.Ferrand & M.Jevaud | LAM/ELE/SPI/011011 Issue 1.0 | 20 Sep 2001 |
| AD4 | Optics / SMEC Interface |  | SPIRE 1.2/1.5.2 |  |
| AD5 | SMEC / DRCU Interface |  | SPIRE 1.5.2/2.2 |  |
| AD6 | Systems budgets | C.Cunningham | SPIRE/ATC/DOC/000450 1.0 | 11 Jun 2000 |
| AD7 | Optical error budgets | K.Dohlen | LOOM.KD.SPIRE.2000.002-DRAFT | 22 May 2000 |
| AD8 | FIRST/Planck IID-A | ESA | PT-IID-A-04624 Iss1 Rev0 | 1 Sep 2000 |
| AD9 | SPIRE Product assurance plan | RAL | SPIRE-RAL-PRJ-000017 Issue 1.0 | 11 Apr 2001 |
| AD10 | MCU Flight model Inter connections list | P.Levacher & B.Travers | LAM/ELE/FTS/NTT/010314 Issue 1.0 | 20 Sep 2001 |
| AD11 | Qualification Random vibrations Specification 01 October 2001 | B.Winter | Noref Issue 8 | 1 Oct 2001 |

## Reference documents

|  | Title | Author | Reference | Date |
| --- | --- | --- | --- | --- |
| RD1 | MCU Design description | D.Ferrand, M.Jevaud, P.Levacher | LAM.ELE.SPI.NOT.000619 Iss 2 Rev 0 | 12 Apr 2001 |
| RD2 | SMECm design description | D.Pouliquen | LAM.PJT.SPI.NOT.200008 Ind 4 | 16 Oct 2001 |
| RD3 | Product Breakdown Structure | P.Dargent | SPI.PFM.00.PB.01.A | 3 Oct 2001 |

# The SMEC Subsystem

## General overview

The Spectrometer mirror MEChanism subsystem (SMEC) is a major part of the SPIRE Spectrometer. It is in charge of the movement of the FTS corner cubes mirrors inside the SPIRE spectrometer.

The critical performances of SMEC [AD1] are the mirror velocity and its stability, the mirror movement around its travel axis and the required accuracy of the mirror position measurements.

## Description of the spectrometer mirror mechanism subsystem

The SMEC is made of 2 main parts :

- The cryogenic mechanism (SMECm)

- The Mechanisms Control Unit  (MCU)

See RD1 and RD2 for details

## Mission profile

Here are the successive phases of the subsystem life from the end of manufacturing to the end of life.

These are for information only. Discrepancies with actual AIV and operation plan are allowed.

Durations are TBC.

### SMECm mission profile

| Operation | Where | Duration | Note |
| --- | --- | --- | --- |
| Bakeout | LAM | 1 week |  |
| Control and integration | LAM | TBD |  |
| Warm Vibrations | LAM | 1 week | Including correlated controls |
| Transport | From LAM to RAL (TBC) | 2 days |  |
| Cold vibrations | RAL (TBC) | 3 weeks | Including correlated controls There will be no 4K vibrations test facility at LAM. |
| 4K control test | RAL (TBC) | 1 week | Including correlated controls There will be no 4K test facility at LAM. |
| Transport | Back to LAM | 2 days |  |
| Thermal cycles | LAM | 4 weeks | Including correlated controls |
| Characterisation | LAM | 4 weeks |  |
| Transport | From LAM to RAL | 2 days |  |
| Integration in the FPU | RAL | 1 week | Including correlated controls |
| FPU Bakeout | RAL | 1 week |  |
| FPU 300K vibrations | RAL | 1 week |  |
| FPU Transport | From RAL to ? | TBD |  |
| FPU Cold vibrations | ? | 3+ weeks | Including correlated controls |
| FPU Transport | Back to RAL | TBD |  |
| FPU Thermal cycles | RAL | TBD | Including correlated controls |
| FPU Transport | From RAL to ESA | TBD |  |
| SPIRE integration in HERSCHEL | ESA | TBD | Including correlated controls |
| Satellite tests | ESA | TBD | Including correlated controls |
| Lock of launch latch | ESA | TBD | Including correlated controls |
| Storage | ESA | 2 years (TBC) |  |
| Launch | CNES Kourou | TBD |  |
| Power on | Orbit |  | Including correlated controls |
| Unlock of launch latch | Orbit | 1/2 day | Including correlated controls |
| Beginning of operation | Orbit | TBD | Health assessement of the subsystem |
| Operations | Orbit | 4.25 years | The SMECm will not be operated along the complete 4.25 years of HERSCHEL on orbit but approximately 8.5 non contiguous months. The subsystem will be stored (power off) during TBD months and powered on but non operating during TBD months. |
| End of operations | Orbit | TBD |  |

### MCU Mission profile

| Operation | Where | Duration | Note |
| --- | --- | --- | --- |
| Bakeout | LAM | 1 week |  |
| Control and integration | LAM | TBD |  |
| Warm Vibrations | LAM | 1 week | Including correlated controls |
| Transport | Form LAM to CEA | 2 days |  |
| Integration in the DRCU | CEA | 1 week | Including correlated controls |
| DRCU transport | From CEA to INTESPACE | TBD |  |
| DRCU Warm vibrations | INTESPACE (TBC) | 1 week | Including correlated controls |
| DRCU Thermal cycles | INTESPACE (TBC) | TBD | Including correlated controls |
| DRCU EMI EMC | INTESPACE (TBC) | TBD | Including correlated controls |
| DRCU transport | Back to CEA | TBD |  |
| DRCU transport | From CEA to RAL | TBD |  |
| SPIRE Calibrations | RAL | TBD |  |
| SPIRE Transport | From RAL to ESA | TBD |  |
| SPIRE integration in HERSCHEL | ESA | TBD | Including correlated controls |
| Satellite tests | ESA | TBD | Including correlated controls |
| Lock of SMECm and BSMm launch latches | ESA | TBD | Including correlated controls |
| Storage | ESA | 2 years (TBC) |  |
| Launch | CNES Kourou | TBD |  |
| Power on | Orbit |  | Including correlated controls |
| Unlock of SMECm and BSMm launch latches | Orbit | 1/2 day | Including correlated controls |
| Beginning of operation | Orbit | TBD | Health assessement of the subsystem |
| Operations | Orbit | 4.25 years | The MCU will not operate during the complete 4.25 years of HERSCHEL on orbit but approximately 1.4 year (non contiguous). |
| End of operations | Orbit | TBD |  |

## Product trees

SMECm : Proto Flight Model (extracted from RD3)

10 : Base structure

20 : Linear guidance means

21 : Rocking frames

22 : Intermediate frames

23 : Flex-pivots

24 : Synchronization

30 : Carriage

40 : Mirrors

50 : Actuator

51 : Stator

52 : Coils

60 : Optical position Sensor

61 : Sensor head

62 : Sensor rule

70 : L.V.D.T.  position sensors

71 : Coils

72 : Core

80 : Launch Latch

81 : Coil

82 : Core

84 : Pin

85 : Switch

90 : Harness

# SMEC Performances Requirements

| # | Requirement | IRD [AD1] | Note |
| --- | --- | --- | --- |
| SMEC_P1 | Scientific Travel = -3.2 / +3.2 mm | SMEC-R01 | w.r.t. ZPD position goal : -3.2 to +32 mm |
| SMEC_P2 | Minimum movement sampling interval = 5µ | SMEC-R02 |  |
| SMEC_P3 | Sampling interval = 5 to 25µ | SMEC-R03 | 2 to 26µ with 2µ steps 13 values selectable in the range. |
| SMEC_P4 | Scan length = Start and stop anywhere in the travel range | SMEC-R04 |  |
| SMEC_P5 | Deadtime = Less than 10% of the useful time | SMEC-R05 | Allocation of the 10% will be made by technical team |
| SMEC_P6 | Velocity range = 0.2 to 1 mm/s | SMEC-R06 & 07 | any value selectable in the range 0 to 5 mm/s with a 1µ/s resolution |
| SMEC_P7 | Velocity stability = 10 µ/s RMS in the velocity range, filtering bandwidth = 0.03 to 25Hz | SMEC-R08 |  |
| SMEC_P8 | Velocity stability duration = 24 consecutive hours | SMEC-R08 |  |
| SMEC_P9 | Mirrors position measurement range = -3.2 / +3.2 mm |  | Goal : -3.2 to 32 mm (see SMEC-P1) |
| SMEC_P10 | Mirrors position measurement accuracy = 0.1µ in the +/- 3.2 mm travel range, +/- 0.3µ elsewhere, filtering bandwidth = 0.03 to 25Hz | SMEC-R09 | The postion is measured relatively to fiducial mark position |

# SMECm Requirements

## Technical requirements

| # | Requirement | Ref | Note |
| --- | --- | --- | --- |
| SMECm_Tm1 | Axis definition = X is the direction of the travel and of the launch direction Y is perpendicular to the interface SMECm fixation plane Z is the third direction | AD2 | The XZ plane is the interface plane between the structure and SMECm |
| SMECm_Tm2 | SMECm Alignment tolerances = <1° (TBC) all directions w.r.t. optical path | AD7 |  |
| SMECm_Tm3 | Dimensions = 140 mm x 140 mm x 165 mm | AD2 | Plus a 24 mm deep pocket under the XZ plane |
| SMECm_Tm4 | Center of gravity = Xm = -7,47mm, Ym = + 1mm, Zm = +0,54 mm |  |  |
| SMECm_Tm5 | Mass = 1650 g excluding margins, mirrors, harness | AD6 | The mass budget is 1300 g for SMECm excluding margins, mirrors. |
| SMECm_Tm6 | Inertia = TBD |  |  |
| SMECm_Tm7 | Emitted vibrations = TBD |  |  |
| SMECm_Tm8 | Power consumption =< 2.4 mW | AD6 | Required mean power consumption over the mission. |
| SMECm_Tm9 | EMC = TBD |  |  |
| SMECm_Tm10 | Fiducial mark position = inside the +/- 0.32 mm subtravel |  |  |
| SMECm_Tm11 | Fiducial mark position accuracy = +/- 50 µ w.r.t. ZPD theoretical position, goal +/- 25µ |  |  |
| SMECm_Tm12 | Operational position = SMECm must be in the specs only in 0g conditions or simulated 0g. with the travel axis within +/- 8 degrees from the horizontal plane. |  | Actuator power limits the inclination from horizontal. |
| SMECm_Tm13 | Stray light = Must be as IR light tight as possible |  |  |
| SMECm_Tm14 | Number of thermometers = 2 Nominal and one redundant | AD1 | Location to be agreed with system team. |
| SMECm_Tm15 | Movement = No friction allowed, no shocks allowed |  | For optimum movement control |
| SMECm_Tm16 | Resonance frequency = None in the 0.03 – 25 Hz that cannot be notched by the control |  |  |
| SMECm_Tm17 | Corner Cubes decenter < 0.5 mm Corner cubes tilts < 10 arcmin |  |  |

## Operational requirements

### Relialibility

Cold redundant hardware shall be provided wherever practicable within the SMECm design.

Every electrical components is duplicated. Two completely independant electric systems are implemented, one redundant, one nominal, without electrical crossing.

The mechanical system cannot be duplicated.

### Lifetime

| # | Requirement | Ref | Note |
| --- | --- | --- | --- |
| SMECm_OL1 | Ground Storage lifetime = 2 years cumulated time |  | A guess |
| SMECm_OL2 | Ground Integrated lifetime = 4 years cumulated time |  | About |
| SMECm_OL3 | Ground operational lifetime = 3 months cumulated time |  | 1 month for subsystem acceptance 1 month for SPIRE acceptance 1 month for HERSCHEL acceptance Under 1g conditions The distribution will be : 1 month : SMECm travel = -0.32 to +0.32 mm => 1.8E6 cycles 1 month : SMECm travel = -3.2 to +3.2 mm => 1.8E5 cycles 1 month : SMECm travel = -3.2 to +32 (goal) mm => 3.7E4 cycles Number of cycles calculated assuming a speed of 0.5 mm/s plus 10% deadtime (*) |
| SMECm_OL4 | On orbit operational lifetime = 8.5 months cumulated time |  | Operating during 1/6 of the mission duration (4.25 years). 1/6 comes from: 3 experiments on herschel (PACS, HIFI and SPIRE) 2 sub instruments on SPIRE : the photometer and the spectrometer. Distribution: 85 days : SMECm travel = -0.32 to +0.32 mm => 5.2E6 cycles 85 days : SMECm travel = -3.2 to +3.2 mm => 5.2E5 cycles 85 days : SMECm travel = -3.2 to +32(goal) mm => 1E5 cycles Number of cycles calculated assuming a speed of 0.5 mm/s plus 10% deadtime (**) |
| SMECm_OL5 | On orbit non operational lifetime = 3.5 years cumulated time |  |  |

(*) The qualification factor for on ground operational lifetime is 4

(**)As the number of on orbit cycles is always greater than 1E5, the qualification factor to be applied during lifetime tests is 1.25 (see AD8)

### Operating modes

The SMECm has only one operating mode which is moving along the trajectory and back.

### Telemetry

NA

### Telecommands

NA

## Interface requirements

The interfaces are defined in the relevant applicable documents.

| Interface | With | Document |
| --- | --- | --- |
| Mechanical | SPIRE Structure | [AD2] |
| Thermal | SPIRE Structure | [AD2] |
| Optics | SPIRE Optics | [AD4] SPIRE 1.2 / 1.5.2 |
| Electronic | MCU | [AD10] |

## Design and manufacture requirements

### Design requirements

LAM design procedures are adopted where applicable

### Manufacture requirements

These are requirements on accessibility, dismountability, testability and manufacturing processes.

As a general rule, the manufacture and cleaning processes will be compatible with class 100 specifications and with the SPIRE PA plan (AD9)

Materials and processes will be declared in the relevant Declared Materials List.

## Logistic requirements

The subsystem wil be transported to and from RAL and CEA.

The containers will have to guarantee that:

- no shocks are greater than those defined for the launch.

- no pollution sneaks to the subsystem

## Environment requirements

These requirements describe the environement in which the subsystem will live.

### Natural environement

This is the description of the natural environment around the subsystem.

| # | Requirement | Ref | Note |
| --- | --- | --- | --- |
| SMECm_EN1 | Vacuum = Less than 10-4 Pa |  | During tests, launch and in operation |
| SMECm_EN2 | Operating temperature during system qualif and on orbit = 4K during subsystem qualification = 300K and 20K, (4K for specific tests) during SPIRE bake out = +80°C (353K) |  | Components at 100K inside the preamplifier |
| SMECm_EN3 | Storage and handling temperature = -20 to +30 °C |  | Under atmospheric pressure, on ground |
|  | Humidity = Less than 45% |  | In clean room |
|  | Cleanliness = Class 100 |  | In clean room |
| SMECm_EN4 | Radiations = Less than 3.5 kRAD | AD8 | On orbit |

### Operating environment

This is the description of the environment imposed by the location of the subsystem in SPIRE and in HERSCHEL.

| # | Requirement | Ref | Note |
| --- | --- | --- | --- |
| SMECm_ON1 | Vibrations quasi static level : 25 g along X (launch direction), 14 g along Y and 14 g along Z sine vibrations level : 40 g along X, 25g along Y and 25 along Z random vibrations level = 10.2 g RMS along X (launch direction), 11.3g RMS along Y and 9.9 gRMS along Z | AD11 AD2 | At 4K. Same levels at 300K for preliminary tests. |
| SMECm_ON2 | Shocks = NA |  |  |
| SMECm_ON3 | Microvibrations = TBD |  | On orbit |
| SMECm_ON4 | Acoustic = NA | AD8 | launched under vacuum |
| SMECm_ON5 | Electrostatic = TBD |  |  |
| SMECm_ON6 | EMC = TBD |  |  |

## Verification requirements

The verification requirements is in AD1.

# MCU Requirements

## Technical requirements

| # | Requirement | Ref | Note |
| --- | --- | --- | --- |
| MCU_Tm1 | Axis definition = TBD |  |  |
| MCU_Tm2 | Dimensions = TBD |  | Cards fromat is eurodouble or a little more (220 x 223 mm²) |
| MCU_Tm3 | Center of gravity = TBD |  | Only for the boards |
| MCU_Tm4 | Mass = TBD |  | Only mass of the boards. Mechanical box in the DRCU mass budget. |
| MCU_Tm5 | Inertia = TBD |  | Only for the boards |
| MCU_Tm6 | Power consumption = 15.5W mean, 22.5W peak | RD1 |  |
| MCU_Tm7 | EMC = TBD |  |  |

## Operational requirements

### Relialibility (see AD1)

IRD-REL-03 : Cold redundant hardware shall be provided wherever practicable within the MCU design.

IRD-REL-04 : As far as possible, all control loops shall be implemented through the use of on board software

IRD-REL-05 : It shall be possible to break all control loops implemented in hardware..

### Lifetime

Based on AD8

| # | Requirement | Ref | Note |
| --- | --- | --- | --- |
| MCU_OL1 | Ground Storage lifetime = 2 years cumulated time |  | A guess |
| MCU_OL2 | Ground Integrated lifetime = 4 years cumulated time |  | About |
| MCU_OL3 | Ground operational lifetime = 1.5 years cumulated time |  | 6 months for subsystem acceptance 6 months for SPIRE acceptance 6 months for HERSCHEL acceptance Under 1g conditions |
| MCU_OL4 | On orbit operational lifetime = 8.5 months cumulated time |  | Operating during 1/6 of the mission duration (4.25 years) |
| MCU_OL5 | On orbit non operational lifetime = 3.5 years cumulated time |  |  |

### Operating modes

See RD1 for further explanations.

| Mode # | Mode Name | Action | Possible Next Mode | On Command |
| --- | --- | --- | --- | --- |
| 0 | Off | The set of boards is not powered. No function available | On | Power On |
| 1 | On | The set of boards (main or redundant) board is powered . | Off | Power Off |
| 1.0 | Booting | The software is initialised after reset. The software is downloaded from Prom memory to SRam memory | Downloaded | MAC Reset On |
| 1.1 | Downloaded | The communication is available. The status of the system is available. Waiting for commands Goes initially to Open loop mode | Booting | MACReset On ‘ResetMAC’ |
| 1.1.0 | Open Loop | Waiting for Advanced Configuration Commands (Control gains,etc ...) Goes initially to open loop standby | Close Loop | ‘CloseLoop’ |
| 1.1.1 | Close Loop | nominal control loop mode using a digital PID controller at 300 s sampling rate Goes initially to Stand By mode | Open Loop | ‘OpenLoop’ |
| 1.1.1.0 | CLoop Stand By | Waiting for motion configuration: (Scan Length, etc..) | Motion init | ‘Init Motion’ |
| 1.1.1.1 | CLoop Motion Init | Searching for limits and diagnostics | Ready | End of Motion initialization |
| 1.1.1.2 | CLoop Ready | Waiting for motion commands and configuration | Scan | ‘StartMotion’ |
| 1.1.1.3 | CLoop Scan | Motion underway: scan for the SMEC, chopping and jiggling for BSM | Ready | End of Motion ‘StopMotion’ ‘ResetMotion |

### Telemetry

The telemetry interface link has a rate of 1 Mbits/s, based on 16 bits words. Data may be provided in 32 bits format in two words.

### Telecommands

The MCU shall receive a 32 bits word for each command. The 32 bit word shall include (i) 2 or 3 bits for subsystem id (ii) 7/8 bits for command type (e.g. set scan_length), (iii) the rest for the parameter itself. There are 2 registers (for command receipt and command reply) in interface with MCU DSP.

There is a specific broadcast @ a dedicated address.

There are typically three types of commands :

- Set Command : the parameter is put in the DSP memory for immediate or delayed execution

- Get Command : the dedicated parameter in  memory can be read by the DPU

- Immediate Command: Reset Command or Start Datation Counter

The detailed commands list is in AD3.

## Interface requirements

The interfaces are defined in the relevant applicable documents.

| Interface | With | Document |
| --- | --- | --- |
| Mechanical | DRCU | [AD5] SPIRE 1.5.2 / 2.2 |
| Thermal | DRCU | [AD5] SPIRE 1.5.2 / 2.2 |
| Electronics | DRCU DPU SMECm BSMm | [AD10] [AD10] [AD10] [AD10] |
| TM/TC | DPU | [AD3] |

## Design and manufacture requirements

### Design requirements

All electronics will be mounted on double eurocards.

### Design rules

TBD

### Manufacture requirements

These are requirements on accessibility, dismountability, testability and manufacturing processes.

As a general rule, the manufacture and cleaning processes will be compatible with the SPIRE PA plan (AD9)

## Logistic requirements

The subsystem wil be transported to and from CEA-SAp under LAM responsibility.

The containers will have to guarantee that:

- no shocks are greater than those defined for the launch.

- no pollution sneaks to the subsystem

## Environment requirements

These requirements describe the environement in which the subsystem will live.

### Natural environement

This is the description of the natural environment around the subsystem.

| # | Requirement | Ref | Note |
| --- | --- | --- | --- |
| MCU_EN1 | Vacuum = Less than 10-4 Pa |  | During tests, launch and in operation |
| MCU_EN2 | Operating temperature = -55 to +55 °C | AD8 |  |
| MCU_EN3 | Storage and handling temperature = -20 to +30°C |  | Overall, on ground |
|  | Humidity = Less than 45% |  | In clean room |
|  | Cleanliness = Class 10 000 |  | In clean room |
| MCU_EN4 | Radiations = Less than 12 kRAD | AD8 | On orbit |

### Operating environment

This is the description of the environment imposed by the location of the subsystem in SPIRE and in HERSCHEL.

| # | Requirement | Ref | Note |
| --- | --- | --- | --- |
| MCU_ON1 | Vibrations = TBD |  | At 300K, atmospheric pressure |
| MCU_ON2 | Shocks = TBD |  | At 300K, atmospheric pressure |
| MCU_ON3 | Acoustic = TBD |  | At 300K, atmospheric pressure |
| MCU_ON4 | Electrostatic = TBD |  |  |
| MCU_ON5 | EMC = TBD |  |  |

## Verification requirements

The verification requirements is in AD1.