| L.A.M. FRE 2243 | FIRST SPIRE | Ref : LAM.PJT.SPI.SPT.200002 Ind 4 Author : D.Pouliquen | Page : 1 / 14 Date : 9 May 2000 |
| --- | --- | --- | --- |
| SPIRE Spectrometer Mirror Mechanism Subsystem Specification |  |

Distribution List :

| RAL | Colin Cunningham |  | Ken J. King |  |
| --- | --- | --- | --- | --- |
|  | Bruce Swinyard | X |  |  |
| CNES | Martine Joubert |  | Yvan Blanc |  |
| CEA-Sap | Jean-Louis Auguères |  |  |  |
| DESPA | Guy Michel | X |  |  |
| GSFC | Don.E. Jennings | X |  |  |
| LAM | Armand Artinian |  | Jean-Paul Baluteau |  |
|  | Claude Colin |  | Pascal Dargent | X |
|  | Kjetil Dohlen | X | Didier Ferrand | X |
|  | Michel Jevaud |  | Patrick Levacher | X |
|  | Alain Origné |  | Dominique Pouliquen | X |

_________________________________________________________________________________

LABORATOIRE d'ASTROPHYSIQUE de MARSEILLE-  CNRS    BP 8   13376  MARSEILLE Cedex 12 FRANCE

Tél : (33) +4 91 05 59 00   -   Fax : (33) +4 91 05 69 59

Update

| Date | Indice | Remarks |
| --- | --- | --- |
| 11 Feb 2000 | 1 | Creation of the document |
| 14 Apr 2000 | 2 | Update of performances specifications following an internal meeting at LAM with JP Baluteau. |
| 25 Apr 2000 | 3 | Design description added. |
| 9 May 2000 | 4 | Adjustements after LAM reading Mission profile added Product tree added |

| Host system | Windows 95 |
| --- | --- |
| Word Processor | Microsoft Word 97 |
| File | C:\Document\LAM_PJT\FIRST\SPIRE\Ss_Smec\Phase_B_Documentation\LAM.PJT.SPI.SPT.20000204.doc |

Table of contents

1.	Scope of the document	4

2.	Documents	4

2.1.	Applicable documents	4

2.2.	Glossary	4

3.	The SMEC Subsystem	5

3.1.	Subsystem description	5

3.2.	Mission profile	9

3.3.	Product tree	10

4.	Requirements	11

4.1.	Functional requirements	11

4.1.1.	Performance requirements	11

4.1.2.	Technical requirements	11

4.1.2.1.	SMECm	11

4.1.2.2.	SMECp	11

4.1.2.3.	SMECe	12

4.1.2.4.	MCU	12

4.2.	Operational requirements	12

4.2.1.	Relialibility	12

4.2.2.	Lifetime	12

4.2.3.	Operating modes	12

4.2.4.	Telemetry	12

4.2.5.	Telecommands	13

4.3.	Interface requirements	13

4.4.	Design and manufacture requirements	13

4.4.1.	Design requirements	13

4.4.2.	Design rules	13

4.4.3.	Manufacture requirements	13

4.5.	Logistic requirements	13

4.6.	Environment requirements	13

4.6.1.	Natural environement	13

4.6.2.	Operating environment	14

4.7.	Verification requirements	14

# Scope of the document

This specification defines the requirements applied to the performances, the design and the qualification of the SPIRE spectrometer mirror mechanism. It is applicable to the PFM and the FS.

# Documents

## Applicable documents

|  | Title | Author | Reference | Date |
| --- | --- | --- | --- | --- |
| AD1 | Instrument Requirements Document | B.M.Swinyard | SPIRE-RAL-PRJ-000034 Issue 0.21 | 30 nov 1999 |
| AD2 | Structure/SMEC Interface |  | SPIRE 1.1/1.5.2 |  |
| AD3 | Thermal / SMEC Interface |  | SPIRE 1.1.1/1.5.2 |  |
| AD4 | Optics / SMEC Interface |  | SPIRE 1.2/1.5.2 |  |
| AD5 | DMEC / DRCU Interface |  | SPIRE 1.5.2/2.2 |  |

## Glossary

| AD | Applicable Document | JPL | Jet Propulsion Laboratory |
| --- | --- | --- | --- |
| BSM | Beam Steering Mirror | LAM | Laboratoire d'Astrophysique de Marseille |
| BSMm | BSM cryogenic mechanism | MCU | Mechanism Control Unit |
| CEA | Commissariat à l'Energie Atomique | MGSE | Mechanical Ground Support Equipment |
| CDR | Critical Design Review | MM | Mechanical Model |
| CNES | Centre National des Etudes Spatiales | MSSL | Mullard Space Science Laboratory |
| CoG | Center of Gravity | NA | Not Applicable |
| CQM | Cryogenic Qualification Model | OGSE | Optical Ground Support Equipment |
| DDR | Detailed Design Review | PDR | Preliminary Design Review |
| DESPA | Département des Etudes SPAtiales | PFM | Prototype Flight Model |
| DM | Development Model | RAL | Rutherford Appleton Laboratory |
| DPU | Digital Processing Unit | RD | Reference Document |
| DRCU | Digital Read-out and Control Unit | SMEC | Spectrometer mirror MEChanism |
| DSP | Digital Signal Processor | SMECm | SMEC cryogenic mechanism |
| EGSE | Electrical Ground Support Equipment | SMECp | SMEC cold preamplifier |
| EM | Electrical Model | SPIRE | Spectral and Photometric Imaging REceiver |
| FIRST | Far InfraRed Submillimeter Telescope | TBC | To Be Confirmed |
| FPU | Focal Plane Unit | TBD | To Be Defined |
| FS | Flight Spare model | TBU | To Be Updated |
| FTS | Fourier Transform Spectrometer | TBW | To Be Written |
| GSFC | Goddard Space and Flight Center | WE | Warm Electronics |

# The SMEC Subsystem

## Subsystem description

The Spectrometer mirror MEChanism subsystem (SMEC) is a major part of the SPIRE Spectrometer. It is in charge of the movement of the rooftop mirrors inside the SPIRE spectrometer.

The critical performances of SMEC [AD1] are the mirror velocity and its stability, the mirror movement around its travel axis and the required accuracy of the mirror position measurements.

The SMEC is made of 3 main parts and is controlled by the MCU:

- The cryogenic mechanism (SMECm)

The SMECm is the mechanism which moves the mirrors, The mirrors are considered a part of SMECm.

Basically,  the movement of the mirrors is a translation only, obtained through the action of a linear actuator. The position of the mirrors along their travel is measured by an incremental optical sensor coupled to a rule. This sensor is coupled with three magentoresistive position sensors for the ZPD position and travel limits measurements.

The mechanical design is based on the GSFC design for a balloon project. A base plate supports the mechanism and is mounted on the SPIRE Optical Bench (Structure). On the baseplate are mounted the fixed part of the actuator and the optical encoder. A moving plate supports the rooftop mirrors and the rule for the optical encoder. The base plate and the mirror moving plate are linked by four "legs". Each leg has two arms, one arm linking the base plate and the intermediate moving plate, the other linking the intermediate moving plate and the mirror moving plate. The articulations at both extremities of the legs use Bendix pivots. A synchronisation device ensures that the mirror plate moves parallel to the base plate. The stiffness of the articulation is very low to keep the actuator power consumption within the specified limits. Consequently, for SPIRE, a launch latch item is added to allow the mechanism to sustain the launch vibrations without damage. The latch is placed between the baseplate and the mirror moving plate.

- The preamplifier (SMECp)

Due to the loss of current on the output signals of the optical encoders when they are cooled down to 4K,  a preamplifier is necessary (TBC). The electronic components (JF4s, etc..) are implemented on a card integrated in a  box mounted on the SPIRE optical bench (TBC). The temperature of the components is set around 100K.

- The warm electronic (SMECe)

The SMEC warm electronic comprises the SMEC analog electronic i.e. the power amplifier for the actuator, the position acquisition electronics and interface unit and the ZPD and limit position sensors conditioning. The main and redundant circuitry are implemented on one board.

This board is a part of the Mechanism Control Unit (MCU).

- The mechanism control unit (MCU)

The MCU comprises the SMEC board, the BSM board and the Multi Axis Controller (MAC) board which houses the interface electronics (FPGA) and the mechanism control electronics (DSP based). The MAC board takes charge of the commands sent by SPIRE Digital Processing Unit (DPU) via the Digital Read-out Control Unit (DRCU), controls the movement of the mechanisms via the relevant analog board, delivers the position measurements and transmits the housekeeping data to SPIRE DPU via the DRCU.

The power is provided by the DRCU in which the MCU is integrated.

SPIRE Block Diagram

This diagram shows the links between the SMEC, the BSM, the MCU, the DRCU and the DPU.

View of the GSFC mechanism

The optical path has been symbolized for show.

MCU schematics

The 21020 DSP is the heart of the control system. It controls both the SMEC and the BSM FPU subsystems.

It is integrated in the DRCU.

## Mission profile

Here are the successive phases of the subsystem life from the end of manufacturing to the end of life.

These are for information only. Discrepancies with actual AIV and operation plan are allowed.

Durations are TBC.

| Operation | Where | What | Duration | Note |
| --- | --- | --- | --- | --- |
| Bakeout | LAM | Everything | 1 week |  |
| Control and integration | LAM | Everything | 2 weeks |  |
| Warm Vibrations | LAM | SMECm and SMECp Ok SMECe and MCU : TBD | 1 week | Including correlated controls |
| Transport | From LAM to RAL (TBC) | SMECm and SMECp | 2 days |  |
| Cold vibrations | RAL (TBC) | SMECm and SMECp | 3 weeks | Including correlated controls There will be no 4K vibrations test facility at LAM. |
| 4K control test | RAL (TBC) | SMECm and SMECp | 1 week | Including correlated controls There will be no 4K test facility at LAM. |
| Transport | From RAL(TBC) to LAM | SMECm and SMECp | 2 days |  |
| Thermal cycles | LAM | Everything | 4 weeks | Including correlated controls |
| Characterisation | LAM | Everything | 4 weeks |  |
| Transport | From LAM to RAL and CEA | SMECm and SMECp | 2 days |  |
| Integration in the SPIRE Structure | RAL | SMECm and SMECp | 1 week | Including correlated controls |
| Integration in the DRCU | CEA | SMECe and MCU | 1 week | Including correlated controls |
| Bakeout | RAL | SMECm and SMECp integrated | 1 week |  |
| Warm vibrations | RAL and CEA | Everything integrated | 1 week | Including correlated controls |
| Transport | From RAL to ? | SMECm and SMECp integrated | TBD |  |
| Cold vibrations | ? | SMECm and SMECp integrated | 3+ weeks | Including correlated controls |
| Transport | From ? to RAL | SMECm and SMECp integrated | TBD |  |
| Thermal cycles | RAL | Everything integrated | TBD | Including correlated controls |
| Calibrations | RAL | Everything integrated | TBD |  |
| Transport | From RAL to ESA | Everything integrated | TBD |  |
| Satellite tests | ESA | Everything integrated | TBD | Including correlated controls |
| Lock of launch latch | ESA | SMECm integrated | 1/2 day | Including correlated controls |
| Storage | ESA | Everything integrated | 2 years (TBC) |  |
| Launch | Kourou | SMECm and SMECp integrated, at 4k under vacuum SMECe and MCU, integrated, at 300K at atm pressure | TBD |  |
| Power on | Orbit | Everything integrated |  | Including correlated controls |
| Unlock of launch latch | Orbit | SMECm integrated | 1/2 day | Including correlated controls |
| Beginning of operation | Orbit | Everything integrated | TBD | Health assessement of the subsystem |
| Operations | Orbit | Everything integrated | 4.25 years | The SMEC subsystem will not be operated along the complete 4.25 years of FIRST on orbit but approximately 8.5 non contiguous months. The subsystem will be stored (power off) during TBD months and powered on but non operating during TBD months. |
| End of operations | Orbit | Everything integrated | TBD |  |

## Product tree

This product tree is for information only.

# Requirements

## Functional requirements

### Performance requirements

The performance requirements are listed in [AD1]

| # | Parameter | Value | IRD | Note |
| --- | --- | --- | --- | --- |
| P1 | Scientific Travel | -3.2 / +3.2 mm | IRD-SMEC-R01 et R02 | w.r.t. ZPD position goal : -3.2 to +32 mm |
| P2 | Movement minimum sampling interval | 5µ | IRD-SMEC-R02 |  |
| P3 | Sampling interval | 5 to 25µ | IRD-SMEC-R03 | TBD values selectable in the range. |
| P4 | Scan length | Start and stop anywhere in the travel range | IRD-SMEC-R04 |  |
| P5 | Deadtime | Less than 10% of the useful time | IRD-SMEC-R05 | Allocation of the 10% will be made by technical team |
| P6 | Velocity range | 0.2 to 1 mm/s | IRD-SMEC-R06 & 07 | TBD values selectable in the range |
| P7 | Velocity stability | 0.01 mm/s RMS in the velocity range, filtering bandwidth = 0.03 to 25Hz, Filter shape TBD | IRD-SMEC-R08 |  |
| P8 | Velocity stability duration | 24 consecutive hours | IRD-SMEC-R08 |  |
| P9 | Position measurement range | -3.2 / +3.2 mm | TBD | Goal : -3.2 to 32 mm (see P1) |
| P10 | Position measurement accuracy | 0.1µ in the +/- 3.2 mm travel range, +/- 0.3µ elsewhere | IRD-SMEC-R09 | The postion is measured relatively to fiducial mark position |

### Technical requirements

#### SMECm

| # | Parameter | Value | IRD | Note |
| --- | --- | --- | --- | --- |
| Tm1 | Axis definition | TBD |  |  |
| Tm2 | Alignment tolerances |  |  |  |
| Tm3 | Dimensions | TBD |  |  |
| Tm4 | Center of gravity | TBD |  |  |
| Tm5 | Mass | 1 kg including margin |  | Excluding mirrors |
| Tm6 | Inertia | TBD |  |  |
| Tm7 | Stiffness along travel axis | TBD |  |  |
| Tm8 | Emitted vibrations | TBD |  |  |
| Tm9 | Power consumption | TBD |  |  |
| Tm10 | EMC | TBD |  |  |
| Tm11 | Fiducial mark position | TBD |  | As near as possible to ZPD |
| Tm12 | Fiducial mark position accuracy | +/- 32µ |  | To be refined according to P5 |
| Tm13 | Operational position | SMECm can operate only in 0g conditions or with the travel axis within TBD degrees from the horizontal plane. |  | To have it operate in any condition would lead to a non acceptable thermal leak and very bad nominal conditions. |

#### SMECp

| # | Parameter | Value | IRD | Note |
| --- | --- | --- | --- | --- |
| Tp1 | Axis definition | TBD |  |  |
| Tp2 | Dimensions | 60 x 60 x 60 mm3 (TBC) |  |  |
| Tp3 | Center of gravity | TBD |  |  |
| Tp4 | Mass | 0.2 kg |  | Including box |
| Tp5 | Inertia | TBD |  |  |
| Tp6 | Power consumption | TBD |  |  |
| Tp7 | EMC | TBD |  |  |
| Tp8 | Position | Less than 1m (TBC) from Optical Encoder |  |  |
| Tp9 | Stray light | TBD |  | Must be as IR light tight as possible if mounted inside SPIRE Structure. |

#### SMECe

TBD

#### MCU

TBD

## Operational requirements

### Relialibility

### Lifetime

| # | Parameter | Value | IRD | Note |
| --- | --- | --- | --- | --- |
| OL1 | Ground Storage lifetime | 2 years |  | A guess |
| OL2 | Ground Integrated lifetime | 4 years |  | About |
| OL3 | Ground operational lifetime | 1.5 years |  | 6 months for subsystem acceptance 6 months for SPIRE acceptance 6 months for FIRST acceptance Under 1g conditions |
| OL4 | On orbit operational lifetime | 8.5 months cumulated time |  | Operating during 1/6 of the mission duration (4.25 years) Distribution: 85 days : SMECm travel = -0.32 to +0.32 mm 85 days : SMECm travel = -3.2 to +3.2 mm 85 days : SMECm travel = -3.2 to +32(goal) mm |
| OL5 | On orbit non operational lifetime | 3.5 years cumulated time |  |  |

### Operating modes

### Telemetry

### Telecommands

## Interface requirements

The interfaces are defined in the relevant applicable documents.

| Part | Interface | With | Document |
| --- | --- | --- | --- |
| SMECm | Mechanical | SPIRE Structure | SPIRE 1.1/1.5.2 |
|  | Thermal | SPIRE Structure | SPIRE 1.1.1/1.5.2 |
|  | Optics | SPIRE Optics | SPIRE 1.2 / 1.5.2 |
| SMECp | Mechanical | SPIRE Structure | SPIRE 1.1/1.5.2 |
|  | Thermal | SPIRE Structure | SPIRE 1.1.1/1.5.2 |
| SMECe | Mechanical | DRCU | SPIRE 1.5.2 / 2.2 |
|  | Thermal | DRCU | SPIRE 1.5.2 / 2.2 |
|  | Electronic | DRCU | SPIRE 1.5.2 / 2.2 |
|  | Electronic | MCU | TBW |
| MCU | Mechanical | DRCU | SPIRE 1.5.2 / 2.2 |
|  | Thermal | DRCU | SPIRE 1.5.2 / 2.2 |
|  | Electronics | DRCU | SPIRE 1.5.2 / 2.2 |

## Design and manufacture requirements

### Design requirements

TBD

### Design rules

TBD

### Manufacture requirements

These are requirements on accessibility, dismountability, testability and manufacturing processes.

- TBD fluids to be forbidden during manufacture to avoid pollution.

- TO BE COMPLETED

## Logistic requirements

The subsystem wil be transported to and from RAL and CEA.

The containers will have to guarantee that:

- no shocks are greater than those defined for the launch.

- no pollution sneaks to the subsystem

- TO BE COMPLETED

## Environment requirements

These requirements describe the environement in which the subsystem will live.

### Natural environement

This is the description of the natural environment around the subsystem.

| # | Parameter | Value | IRD | Note |
| --- | --- | --- | --- | --- |
| EN1 | Vacuum | Less than 10-4 Pa |  | During tests, launch and in operation |
| EN2 | Operating temperature | SMECm : during system qualif and on orbit = 4K SMECm : during subsystem qualification = 300K and 20K, (4K for specific tests) |  |  |
|  |  | SMECp : 4K (TBC) |  | Components at 100K inside |
|  |  | SMECe and MCU : -55 to +45°C (TBC) |  |  |
| EN3 | Storage and handling temperature | -20 to +30 °C |  | Overall, on ground |
|  | Humidity | Less than 45% |  | In clean room |
|  | Cleanliness | Class TBD |  | In clean room |
| EN4 | Radiations | SMECm : Less than 3.5 kRAD |  | On orbit |
|  |  | SMECp : Less than 3.5 kRAD |  |  |
|  |  | SMECe and MCU : Less than 12 kRAD |  |  |

### Operating environment

This is the description of the environment imposed by the location of the subsystem in SPIRE and in FIRST.

| # | Parameter | Value | IRD | Note |
| --- | --- | --- | --- | --- |
| ON1 | Vibrations | SMECm : TBD |  | At 4K |
|  |  | SMECp : TBD |  | At 4K (TBC) |
|  |  | SMECe and MCU : TBD |  | At 300K |
| ON2 | Shocks | SMECm : TBD |  | At 4K |
|  |  | SMECp : TBD |  | At 100K (TBC) |
|  |  | SMECe and MCU : TBD |  | At 300K |
| ON3 | Microvibrations | SMECm : TBD |  | On orbit NA for SMECp, SMECe and MCU |
| ON4 | Acoustic | NA |  | SMECm and SMECp Launched under vacuum SMECe and MCU mounted inside the DRCU box provided by CEA. |
| ON5 | Electrostatic | SMECm : TBD |  |  |
|  |  | SMECp : TBD |  |  |
|  |  | SMECe and MCU : TBD |  |  |
| ON6 | EMC | SMECm : TBD |  |  |
|  |  | SMECp : TBD |  |  |
|  |  | SMECe and MCU : TBD |  |  |

## Verification requirements