SPIRE Beam Steering Mirror Subsystem Specification Document

v 3.2

Ian Pain

# DISTRIBUTION LIST

| SPIRE-Project | Ken J. King | x |
| --- | --- | --- |
|  | Bruce M. Swinyard | x |
|  | Matt Griffin | x |
| UK ATC | Colin Cunningham | x |
|  | Gillian Wright | x |
|  | Ian Pain | x |
|  | Tully Peacocke | x |
|  | Brian Stobie | x |
|  | Brenda Graham | x |
|  | Tom Paul | x |
|  | Ken Wilson | x |
| LAM | Didier Ferrand | x |
|  | Dominique Pouliquen | x |
|  | Patrick Levacher | x |

# Record of Issue

| Date | Index | Remarks |
| --- | --- | --- |
| 13.Jun.00 | 1.0 | Issue for PDR |
| 06.Nov.00 | 2.0 | Update following additional technical data. Reformatting. |
| 31.May.01 | 3.0 | revising stability specification. ; Updated cross references ; Updated TBC’s of mirror dimensions; Updated vibration environment; Added reliability and safety requirements; Expanded compliance matrix. Distributed internal to ATC for comment. |
| 19.Jun.01 | 3.1 | (working draft - internal to ATC ). Confirmed 20msec risetime. Minor tweaks . updated vibration load and interfaces, updated outline description. |
| 10.Jul.01 | 3.2 | Amended reflectivity/ emmisivity spec ( non measurable). Updated compliance & ICD tables. |

# Table of contents

DISTRIBUTION LIST	1

Record of Issue	1

Table of contents	3

Table of Figures	4

File Description	5

Highlighting notes:	5

1.	Scope	7

2.	Documents and Glossary	7

2.1	Applicable documents	7

2.2	Reference documents	8

2.3	Glossary	8

3.	Subsystem description	10

3.1	Outline Description of the Beam Steering mirror mechanism subsystem	10

3.2	Mission profile	11

3.3	BSM Block Diagram	12

3.4	Design Assumptions	13

3.4.1	Optical Scaling Factor	13

3.4.2	Definition of Axes	13

4.	Functional Requirements	15

4.1	Performance requirements	15

4.1.1	Angular Travel - Chop Axis	15

4.1.2	Angular Travel - Jiggle Axis	15

4.1.3	Minimum Step Size	15

4.1.4	Chop Frequency	15

4.1.5	Jiggle Frequency	15

4.1.6	Holding position/ Drift Constraint	15

4.1.7	Stability	16

4.1.8	Position Measurement	16

4.1.9	Settling Time	16

4.1.10	Chop repeatability	16

4.2	Technical Specifications	17

4.2.1	Mechanical Dimensions	17

4.2.2	Operating Temperature	17

4.2.3	Thermal Isolation	17

4.2.4	Cold Power Dissipation	17

4.2.5	Warm Electronics Power Dissipation	17

4.2.6	Mirror Surface Dimensions	17

4.2.7	Mirror Surface Finish	17

4.2.8	Mirror Surface Reflectivity	18

4.2.9	Mirror Surface Emissivity	18

4.2.10	Baffle	18

4.2.11	Position of Rotation Axes	18

4.2.12	Orthogonality of Rotation Axes	18

4.2.13	Fail Safe (No Drive Signal) Position	18

4.2.14	Fail Safe (Mechanical Failure) Position	18

4.2.15	Mass	19

4.2.16	Cool-down time	19

4.2.17	Reliability	19

4.2.18	Failure Modes	19

4.3	Operational Specification	20

4.3.1	Operational Safety	20

4.3.2	Lifetime	20

4.3.3	Operating modes	21

4.3.4	Jiggle Mode	21

4.3.5	Chopping Mode	21

4.3.6	Scan mapping	21

4.3.7	Stare or 'holding' mode	21

4.3.8	Combinations of Modes	21

4.4	Interface requirements	21

4.4.1	Data Outputs	21

4.4.2	Data Inputs	22

4.4.3	Exported vibration	22

4.4.4	Stray Magnetic fields	22

4.4.5	Electro-Magnetic Compatibility	22

4.4.6	ICD's	22

4.5	BSM interface reference table	23

4.6	Design, manufacture and test requirements	25

4.6.1	Design requirements	25

4.6.2	Electronics Card Format	25

4.6.3	Product Assurance Plan	25

4.6.3.1	Mirror Flatness	25

4.6.3.2	Mirror Reflectivity	25

4.6.3.3	Cleanliness	25

4.6.3.4	Material selection	25

4.6.3.5	Storage	25

4.7	Environmental requirements	27

4.7.1	Operating environment	27

4.7.1.1	Shock	27

4.7.1.2	Quasi Static Loads	27

4.7.1.3	Sine Vibration	27

4.7.1.4	Random Vibration	28

4.7.1.5	Vacuum Level	28

4.7.1.6	Vacuum Outgassing	28

4.7.1.7	Temperature	28

4.7.1.8	Magnetic Fields	28

4.7.1.9	Survival Temperature	28

4.7.1.10	Radiation environment	29

4.8	Verification requirements	31

4.8.1	Performance Requirements	32

4.8.2	System Requirements	33

4.8.3	Operational Specification	34

4.8.4	Interface requirements	35

4.8.5	Design, manufacture and test requirements	36

4.8.6	Environmental requirements	36

# Table of Figures

Figure 1 Photometer Layout, BSM in green, highlighted with yellow oval	10

Figure 2 SPIRE Block Diagram showing BSM, Mechanism Control Unit (MCU).	12

# File Description

Created with:	 	MS Word 97 SR-1

File: 			BSM Subsystem Specification Document v3_2.doc

# Highlighting notes:

Text highlighted in yellow needs checking or updating, or indicates a missing reference (e.g. ???) or a TBD/TBC/TBW

Text highlighted in green is a substantial change new since the last released issue

# Scope

This specification defines the requirements applied to the performance, design and qualification of the Beam Steering Mechanism for the SPIRE photometer.  It includes a brief description of the proposed design to meet these requirements. The complete design description is found in RD1.

The Beam Steering Mechanism forms a sub-system of the SPIRE instrument. This specification is applicable to the CQM, the PFM and the FS. Where relevant, it is also applicable to the STM (deliverable to SPIRE but not ESA).

# Documents and Glossary

## Applicable documents

| Ref | Title | Author | Reference | Date |
| --- | --- | --- | --- | --- |
| AD1 | Instrument Requirements Document (IRD) | B.M.Swinyard | SPIRE-RAL-PRJ-000034 v0.30 | May 2000 |
| AD2 | ICD Structure - Mechanical I/F | B.Winters | SPIRE-MSS-PRJ-000xxx v1.0 | April 2001 |
| AD3 | Deleted | N/A |  |  |
| AD4 | Optics - BSM ICD | T.Peacocke, I.Pain | SPIRE-ATC-PRJ-000587 Annex E | Jun.01 |
| AD5 | Baffles - BSM ICD | T.Peacocke, I.Pain | SPIRE-ATC-PRJ-000587 Annex E | Jun.01 |
| AD6 | Photometer Bolometer Arrays - BSM ICD | B.Winters | ICD Structure - Mechanical I/F SPIRE-MSS-PRJ-000xxx v1.0 | April 2001 |
| AD7 | Spectrometer Bolometer Arrays - BSM ICD | B.Winters | ICD Structure - Mechanical I/F SPIRE-MSS-PRJ-000xxx v1.0 | April 2001 |
| AD8 | Photometer Calibration Source - BSM ICD | I.Pain | SPIRE-ATC-PRJ-000587 Annex C | Jun.01 |
| AD9 | Deleted | N/A |  |  |
| AD10 | On Board Software - BSM ICD | B.Stobie | SPIRE-ATC-PRJ-000587 Annex G | TBW |
| AD11 | Analogue Simulator - BSM ICD | TBD | TBD |  |
| AD12 | Instrument Simulator - BSM ICD | TBD | TBD |  |
| AD13 | Current Optical Configuration | ??? | PHT 126 I | Check status |
| AD14 | Operating Modes for the SPIRE Instrument | B.M.Swinyard | SPIRE-RAL_PRJ 000320 issue 2.2 | Check status |
| AD15 | BSM Sub-system Development Plan | I.Pain | SPIRE-ATC-PRJ-000466 v4.0 | 08.Apr.01 |
| AD19 | MCU-BSM ICD | I.Pain | SPIRE-ATC-PRJ-000587 Annex G | Jun.01 |
| AD20 | SPIRE Product Assurance plan | D.Kelsh | SPIRE-RAL-PRJ-00017 v1.0 | 11.Apr.01 |
| AD21 | ATC Interface drawing | ATC | SPIRE-BSM-021-002-001 r.1 | 15.Jun.01 |
| AD22 | BSM Product Assurance Plan | Ian Pain | SPIRE-ATC-PRJ-000711 Internal Draft 0.4 | 26.Jun.01 |
| AD23 | Optical System Design Description | K.Dohlen, B.Swinyard | SPIRE-LAM-PRJ-000447 Draft 1 | 18.Dec.00 |

## Reference documents

| Ref | Title | Author | Reference | Date |
| --- | --- | --- | --- | --- |
| RD1 | SPIRE BSM Design Description Document | Ian Pain | SPIRE-ATC-PRJ-000587 v4.0 | Jun.01 |
| RD2 | HERSCHEL Telescope Specification |  | PT-RQ-04761 Issue 1/A SPIRE-ESA-DOC-000195 | Jan.98 |
| RD3 | SPIRE Systems Budgets | C.Cunningham | SPIRE-ATC-PRJ-000450 | latest |
| RD4 | Radiation environment memo: | J. Sørensen TOS-EMA , | réf. 00-010/JS, | 14 May 2001 |
| RD5 | SPIRE mirrors specification | K.Dohlen and D.Pouliquen | LAM.PJT.SPI.SPT.200007 Ind 1 | 6.Jun.00 |
| RD6 | IID-A | HERSCHEL/Planck Project Team | SCI-PT-IIDA-04624 rev 1/0 | latest |
| RD7 | IID-B | ESA HERSCHEL/Planck Project Team | SCI-PT-IIDB/SPIRE-02124 rev 1/0 | latest |

## Glossary

| Abbrev | Meaning | Abbrev | Meaning |
| --- | --- | --- | --- |
| AD | Applicable Document | LAT | Lot Acceptance Tests |
| ADP | Acceptance Data Package | MAC | Multi Axis Controller |
| ATC | United Kingdom Astronomy Technology Centre | MAPTIS | Materials and Processes Technical Information Service |
| BSM | Beam Steering Mirror | MSFC | Marshall Space Flight Center |
| BSM | Beam Steering Mirror dummy | MCU | Mechanism Control Unit |
| BSMe | Beam Steering Mirror electronics | MIP | Mandatory Inspection Point |
| BSMm | Beam Steering Mirror mechanism | MGSE | Mechanical Ground Support Equipment |
| BSMs | Beam Steering Mirror structure | MPIA | Max Planck Institute for Astronomy |
| CAE | Computer Aided Engineering | MSSL | Mullard Space Science Laboratory |
| CDR | Critical Design Review | NASA | National Aeronautical Space Agency |
| CoG | Centre of Gravity | NA | Not Applicable |
| CIL | Critical Items List | NCR | Non Conformance Report |
| CQM | Cryogenic Qualification Model | NCRP | Non Conformance Review Panel |
| CTD | Change to Drawing/Document | OGSE | Optical Ground Support Equipment |
| DCL | Declared Components List | PA | Product Assurance |
| DDR | Detailed Design Review | PAD | Part Approval Document |
| DM | Development Model | PFM | Proto Flight Model |
| DML | Declared Materials List | PPARC | Particle Physics and Astronomy Research Council |
| DPA | Destructive Physical Analysis | PI | Principal Investigator |
| DSP | Digital Signal Processor | PID | Proportional – Integral - Derivative |
| ECSS | European Cooperation for Space Standardization | QA | Quality Assurance |
| EGSE | Electrical Ground Support Equipment | RAL | Rutherford Appleton Laboratory |
| ESA | European Space Agency | RAL SSD | RAL Space Science Department |
| FMEA | Failure Modes and Effects Analysis | RD | Reference Document |
| FMECA | Failure Modes, Effects and Criticality Analysis | rms | Root mean square |
| FPGA | Field Programmable Gate Array | SDOF | Single Degree of Freedom |
| FPU | Focal Plane Unit | SMEC | Spectrometer Mechanism |
| FS | Flight Spare | SPIRE | Spectral and Photometric Imaging REceiver |
| FSM | Flight Spare model | TBC | To Be Confirmed |
| GDFC | Goddard Flight Center | TBD | To Be Defined |
| GSE | Ground Support Equipment | TBW | To Be Written |
| HoS | Head of Specialism | UK ATC | United Kingdom Astronomy Technology Centre |
| Herschel | ESA Mission name (formerly FIRST) | UK SPO | UK SPIRE Project Office |
| ICD | Interface Control Document | WE | Warm Electronics |
| IBDR | Instrument Baseline Design Review |  |  |
| KIP | Key Inspection Point |  |  |
| LAM | Laboratoire d'Astrophysique de Marseilles |  |  |

# Subsystem description

## Outline Description of the Beam Steering mirror mechanism subsystem

The Beam Steering Mirror mechanism subsystem (BSM) is a critical part of the SPIRE Instrument. It is used to steer the beam of the telescope on the photometer and spectrometer arrays in 2 orthogonal directions, for purposes of fully sampling the image, fine-pointing and signal modulation.

The BSM comprises 4 main deliverables:

- The cryogenic mechanism (BSMm).

- The structural interface (BSMs).

- The warm electronics (BSMe)

- Mass and optical alignment dummies as required for SPIRE system level integration, (BSMd)

The position of the BSMm & BSMs are indicated in Figure 1.

Figure 1 Photometer Layout, BSM in green, highlighted with yellow oval

The BSMm consists of an aluminium alloy mirror, nominal diameter 32mm, machined as part of the chop axis. This is mounted orthogonally within a gimbal-type frame which provides for jiggle axis motion. The axes are suspended by flex-pivot mounts. The BSMm is a cryogenic device with nominal temperature 4-6K. Nominally, the chop axis provides 2.4 ° of mirror motion at 2 Hz and the jiggle axis provides  0.6° of motion at 1 Hz. The mirror also provides an aperture through which the Photometer Calibration Source is directed towards the detector arrays

The BSMs provides location of the BSMm on the SPIRE optical bench, and will also provide for a light tight enclosure and structural support for harnessing and thermometry. The BSMs integrates to the SPIRE Photometer Calibration Source (PCAL), supplied by the University of Wales, Cardiff, a baffle (supplied by RAL or ATC…TBC) and the SPIRE optical bench (MSSL). The BSMs is a cryogenic structure with nominal temperature 4-6K.

The BSMe provides electrical actuators which are used to provide motion of the mirror. Electrical transducers are used to measure the mirror position to allow control of the mirror position. The BSMe baseline design makes use of cryogenic motors used in PACS and magneto-resistive sensors used in ISOPhot. Each axis houses a rare-earth (NdFeB VACODYM 344) permanent magnet moving pole piece and is driven by a motor coil fixed to the mechanism housing/structure.

The cryogenic electronics are connected to the analogue power and amplifier electronics on the Warm Electronics (WE) by a cryogenic harness which will also feed out signal cables from thermocouples on the BSMs. The BSM operates under control of the Detector Readout and Control (HSDRC) sub-system’s Mechanism Control Unit (MCU) supplied by LAM. The BSMe will be specified and designed by the UK ATC, then manufactured by LAM in conjunction with the SMEC electronics. Integration and test will be at LAM, with support from ATC.

The BSMd may comprise several actual dummies, with at least (1) an optical dummy for initial alignment work and (2) a mass-representative model for structural vibration tests. Designs for mass and optical alignment dummies will not be specified in detail until the BSMs/BSMm design is complete.

## Mission profile

The BSM is developed as a sub-system and then integrated to the SPIRE FPU. The SPIRE instrument is subsequently integrated to Herschel. The instrument is to be cryogenically cooled, and will be cold during launch. Launch is scheduled for 2007 to an L2 orbit. The mission duration is a minimum of 4.25 years.

Per AD1, in  normal operations the satellite is expected to have a 24-hour operational cycle with data being collected autonomously for 21 hours and a 3 hour ground contact period – the Data Transfer and Commanding Period (DTCP). During the DTCP the data will be telemetered to the ground and the commands for the next 24-hour period will be up-linked.

## BSM Block Diagram

The block diagram below is adopted from AD1 Fig 3.1-1 and shows the relationships between the sub-systems of the SPIRE instrument.

Figure 2 SPIRE Block Diagram showing BSM, Mechanism Control Unit (MCU).

## Design Assumptions

### Optical Scaling Factor

A scaling factor between the movement of the mirror and movement of the beam on the sky of 1° (at the mirror) per 50 arcsec (on the sky) is assumed; i.e. a scaling factor of 72:1. This value is derived from the SPIRE optical design (AD13).

### Definition of Axes

The HERSCHEL spacecraft axes are defined in AD1, as follows:

- The X axis is the spacecraft boresight

- The Y axis is away from the HIFI instrument

- The Z axis is towards the sun shield.

The BSM is positioned in the SPIRE optical system such that the two rotation axes of the mirror produce nominal movements of the beam in the XY plane (around the Z axis) and in the XZ plane (around the Y axis) respectively.

The rotation axes of the BSM mirror shall be referred to as follows:

- Rotation producing a movement of the beam around the spacecraft Z axis - Chop axis

- Rotation producing a movement of the beam around the spacecraft Y axis - Jiggle axis

The mirror orientation is defined by two angles - the chop angle and the jiggle angle (c,j). The nominal zero position ( (c,j) = (0,0) ) is defined as the orientation such that the centre of the photometer detector arrays are aligned along the nominal SPIRE boresight.

# Functional Requirements

## Performance requirements

These requirements are not dependent on the particular design of the BSM.

### Angular Travel - Chop Axis

| The BSM shall allow angular movement of the mirror surface through an angle of (2.4° in the mirror chop axis. (see assumption 3.4 for corresponding on-sky motion). | AD1 : IRD-BSMP-R01 IID-B SRD-R9 |
| --- | --- |
| The minimum available chop throw shall be +/- 0.1° (see assumption 3.4 for corresponding on-sky motion). | AD1 : IRD-B SRD-R9 |

### Angular Travel - Jiggle Axis

| The BSM shall allow angular movement of the mirror surface through an angle of (0.6° in the mirror jiggle axis. (see assumption 3.4 for corresponding on-sky motion). | AD1 : IRD-BSMP-R02 |
| --- | --- |

### Minimum Step Size

| The BSM shall allow movements of the mirror surface in both chop and jiggle axes in minimum increments of 0.04°. (see assumption 3.4 for corresponding on-sky motion). | AD1 : IRD-BSMP-R03 |
| --- | --- |

### Chop Frequency

| The BSM shall allow movements of the mirror in the chop axis at any frequency up to 2Hz Hz for nominal operation and power dissipation | AD1 : IRD-BSMP-R04 |
| --- | --- |
| As a goal, the BSM shall allow movements of the mirror in the chop axis at any frequency up to 5Hz. At frequencies above 2Hz, a degradation in power dissipation performance and settling time of the BSM is acceptable. | AD1 : IRD-BSMP-R04 |

### Jiggle Frequency

| The BSM shall allow movements of the mirror in the jiggle axis at any frequency up to 0.5Hz. | AD1 : IRD-B SMP-R05 |
| --- | --- |
| As a goal, the BSM shall allow movements of the mirror in the jiggle axis at any frequency up to 1Hz. At frequencies above 0.5Hz, a degradation in power dissipation performance and settling time of the BSM is acceptable. | AD1 : IRD-B SMP-R05 |

### Holding position/ Drift Constraint

| The BSM shall be capable of moving to, and holding at, any commanded position within its range of movement, to within 0.004 degrees rms, for periods of up to 4 hours | AD1 : IRD-BSMP-R05 |
| --- | --- |

### Stability

| After settling, the mirror position shall remain within 0.004° (rms) of the mean steady state position, in the frequency range 0.03 - 25Hz. | AD1 : IRD-BSMP-R06 |
| --- | --- |
| As a goal, after settling, the mirror position shall remain within 0.002° (rms) of the mean steady state position, in the frequency range 0.03 - 25Hz. | AD1 : IRD-BSMP-R06 |

### Position Measurement

| The BSM shall provide measurements of the angular orientation of the mirror surface in both chop and jiggle axes to a resolution of 1/8 of the requirement, 1/4 of the goal. i.e. a requirement of 0.0005°. The rate at which the position measurements need to be made is TBD. This requires modelling at instrument level of what is needed to deconvolve the signal. A "past experience estimate" would be 5 - 10 measurements per half chop cycle, i.e. a requirement of 40Hz, a goal of 80Hz. | AD1 : IRD-BSMP-R07 |
| --- | --- |

### Settling Time

| The angular position of the mirror surface shall be within 0.02° of the mean steady state position in less than 20 milliseconds from the application of a demand in the chop axis. | AD1 : IRD-BSMP-R08 |
| --- | --- |
| The angular position of the mirror surface shall be within 0.02° of the mean steady state position in less than 0.100 sec from the application of a demand in the jiggle axis. | ??? |
| As a goal, the angular position of the mirror surface shall be within 0.02° of the mean steady state position in less than 0.050 sec from the application of a demand in the jiggle axis. | ??? |

### Chop repeatability

| The steady state repeatability between successive chop cycles shall be less than 0.004° (rms) over 4 hours. | ??? |
| --- | --- |

## Technical Specifications

### Mechanical Dimensions

| The BSMm shall fit within a volume of 130x130x30 mm (excluding mounting structure). | AD1 : IRD-BSMP-R09 |
| --- | --- |
| The BSM, including mounting structure, shall fit within a volume of 132x95x20mm | AD21 |
| The BSM mounting structure footprint is as defined in MSSL Interface drg. A2-5264-907 And ATC Interface drawing SPIRE-BSM-021-002-001 r.1 | AD2 AD21 |

### Operating Temperature

| The operational temperature of the BSM shall be at Thermal Interface Level 1 per RD6: nominally 4K, but in the range 3.5-6.0K . | AD1 : IRD-BSMP-R10 RD6 (Table 5.7.7.1-1) |
| --- | --- |
| The BSM shall be capable of operation (with reduced performance) at temperatures up to 300K. | AD1 : IRD-BSMP-R10 |

### Thermal Isolation

| No part of the BSM visible to the optical path shall rise by no more than 1K from the nominal operating temperature of the surrounding structure after 1 hour of operation in any mode. | AD1 : IRD-BSMP-R11 |
| --- | --- |

### Cold Power Dissipation

| The average power dissipation of the BSM Cryogenic Mechanism (BSMm) and the BSM Support Structure (BSMs) shall be less than 4mW in any operating mode, when operating at the temperature defined in section 4.2.4 | AD1 : IRD-BSMP-R12 |
| --- | --- |

### Warm Electronics Power Dissipation

| The average power dissipation of the BSM Warm Electronics (BSMe) shall be less than TBD Watts when chopping at 2Hz in any operating mode. | AD1 : IRD-BSMP-R13 |
| --- | --- |

### Mirror Surface Dimensions

| The mirror clear diameter after allowing for any obscuration by the baffle shall be greater than 32mm.The clear diameter is the visible diameter (when viewed orthogonal to the mirror surface with the mirror held at the 0,0 position) . | AD13 |
| --- | --- |
| The mirror shall include a central hole of no less than 2.8mm diameter to allow the Photometer Calibrator to be seen by the detectors. | AD13 |

### Mirror Surface Finish

| The mirror surface of the BSM shall be flat to <1(m (rms) and shall have a surface roughness of <10nm (rms). | AD13, RD5 |
| --- | --- |

See also 4.6.3.1.

### Mirror Surface Reflectivity

| The reflectivity of the mirror surface of the BSM shall be ≥99% in the wavelength range 200 - 670 (m by design. This requirement will not be measurable. | AD13, RD5 |
| --- | --- |

See also 4.6.3.2.

### Mirror Surface Emissivity

| The emissivity of the mirror surface of the BSM shall be <1% in the wavelength range 200 - 670(m by design. This requirement is the complement of 4.2.8 and will not be measurable | AD13, RD5 |
| --- | --- |

### Baffle

| The presence of a Baffle is assumed, and will be of the hole-in-plate type if internal component temperatures can meet the requirement of 4.2.3 . The opening in the stray light baffle will be sufficient to allow the 20% oversized beam to cross it with a positive margin of no more than 0.5 mm. | AD2 (section 2.5.9) This document |
| --- | --- |

### Position of Rotation Axes

| The position of the Rotation Axes shall be established accurately within 0.5 mm (TBC) and 0.5° (TBC) of nominal design position. | This document |
| --- | --- |
| The BSM shall be designed such that it may be repositioned on the SPIRE optical bench within a repeatability of 0.1 mm (TBC)and 0.05° (TBC) | This document |
| Rotational motions of the axes shall produce a de-centre of the axis of rotation of less than (10 microns) (TBC) | This document |

### Orthogonality of Rotation Axes

| The orthogonality of the rotation axes shall be within 0.15° (TBC). | This document |
| --- | --- |

### Fail Safe (No Drive Signal) Position

| When no drive signals are applied to the BSM, the mirror shall take up a position such that the mirror surface is perpendicular to the nominal (0,0) mirror position to within (0.18°. For information, this is intended to place the BSM within 50% of the beam FWHM. | This document |
| --- | --- |

### Fail Safe (Mechanical Failure) Position

| In the event of mechanical failure on launch, the mirror shall take up a position such that the beam remains useable by the spectrometer instrument, i.e. That the mirror surface is perpendicular to the nominal (0,0) mirror position to within (1.0°. | This document |
| --- | --- |

### Mass

| The BSM cryogenic mechanism (BSMm) and the BSM support (BSMs) shall have a combined mass of less than 1100g; including harness but excluding contingency and PCAL | IRD-SUBS-R03 (SPIRE Sub-system Budget Allocations) |
| --- | --- |

### Cool-down time

| Upon integration to the SPIRE optical bench, the BSM shall reach a temperature of 4K within 15 hours of the commencement of cooldown. This assumes a maximum average cooldown rate of 20K/hour. | ??? |
| --- | --- |

### Reliability

| As far as possible the total failure of a single sub-system shall not lead to the total loss of instrument operations. | AD1 : IRD-REL-R01 |
| --- | --- |
| Backup modes of operation should be available for all nominal observing modes. These shall be designed to allow the continued use of that mode, albeit with degraded performance or efficiency. | AD1 : IRD-REL-R02 |
| Cold redundant hardware shall be provided wherever practicable within the instrument design. | AD1 : IRD-REL-R03 |

### Failure Modes

| Failure of any sub-system, or one of its components, shall not affect the health of any other subsystem, the instrument or the interface with the satellite. | AD1 : IRD-SAFE-R08 |
| --- | --- |
| Failure of any component in a subsystem shall not damage any redundant or backup component designed to replace that component in the subsystem | AD1 : IRD-SAFE-R09 |
| No electronics sub-unit shall be capable of affecting instrument operations until it is in a defined state. This state shall be confirmed in the housekeeping telemetry. | AD1 : IRD-SAFE-R10 |

## Operational Specification

### Operational Safety

| The BSM shall operate safely in any normal operating mode. | This document |
| --- | --- |

### Lifetime

| The BSM shall be capable of operation in any normal mode for periods in excess of 1/6 of the nominal mission lifetime. | AD1 |
| --- | --- |
| All sub-systems are required to demonstrate that they will operate successfully over the 4.25 years of expected mission operations. | AD1 : IRD-SUBS-R02 |
| Lifetime tests of items operating <100000 times will use factors as specified in RD 16; i.e. Lifetime tests of the chop/jiggle mode will use a multiplier of 1.25x for on-orbit cycles and 4x for ground test cycles. | RD16 |

| Life time breakdown |
| --- |
| # | Parameter | IRD | Value | Note |
| OL1 | Ground Storage lifetime |  | 2 years | A guess |
| OL2 | Ground Integrated lifetime |  | 4 years | A guess |
| OL3 | Ground operational lifetime |  | 1.5 years TBC | 6 months for subsystem acceptance 6 months for SPIRE acceptance 6 months for HERSCHEL acceptance Broken down, nominally (TBC): 1M cycles during BSM check out at ATC 1M cycles during BSM check out at RAL 1M cycles during system integration, e.g. checking for cross talk, vibration, EMC. 1M cycles during observing mode checkout. 1M cycles for ESA/Herschel integration. 0.3M cycles spare. |
| OL4 | On orbit operational (chop & jiggle mode) Lifetime |  | Minimum 8.5 months cumulative time | Operating during 1/6 of the mission duration (4.25 years) |
| OL5 | On orbit de-powered operational Lifetime |  | Up to 3.5 years cumulative time | TBD |
| OL6 | On Orbit powered but not chopping (servo control only) |  | Up to 3.5 years cumulative time | TBD May be required if self-damping inadequate in face of micro-vibration environment |

### Operating modes

AD14 defines the required modes of operation in detail.  There are 14 (TBC)  operational modes, but from the point of view of the BSM motion they fall into three categories :

| Jiggle | AD14 |
| --- | --- |
| Chopping | AD14 |
| Scan mapping | AD14 |

Additionally holding the 'stare' position may require active servo control.

### Jiggle Mode

Jiggle Mode is used to optimize the sampling of the detector arrays. In this mode, the mirror is stepped in small angular increments. Jiggling may be done in any angular orientation (i.e. jiggling is not confined to the jiggle axis, and will usually be a combination of movements in the chop and jiggle axes).

Jiggle movements may be demanded in both chop and jiggle axes simultaneously. The fine pointing mode is executed as a jiggle pattern, and the difference lies in the processing/use of the data.

Jiggle mode will be used with both the photometer and the FTS. When the FTS is in use no chop will be required. During a photometer jiggle operation the BSM is also required to chop.  i.e. at each jiggle position a number of chop cycles will be executed.

### Chopping Mode

Chopping Mode is used to provide removal of 1/f noise in the photometer detectors. The mirror is used to move the source of interest between two separate detectors.

Chopping is only required in one axis (the chop axis), and will only be used when the photometer is in use, not with the FTS

### Scan mapping

Scan mapping with chopping may be required.  The jiggle and chop axes are used to execute chopping either parallel to or perpendicular to the scan direction, with the frequency of chop set by the jiggle axis frequency limit.

### Stare or 'holding' mode

Dependent on spacecraft  vibration levels, the BSM may require active servo control in order to maintain the nominal 'power-off' hold position within adequate accuracy. This is TBD.

### Combinations of Modes

The following combinations of the basic modes are required.

- Chopping and Jiggling

- Removal of optical or mechanical cross coupling during Chop-only or Jiggle-only operations.

## Interface requirements

### Data Outputs

The following data is provided by the BSMe via the MCU.

| Data | Rate | Reference |
| --- | --- | --- |
| Chop axis position | requirement 40Hz, TBC goal 80Hz.TBC | This document |
| Jiggle axis position | requirement 40Hz, TBC goal 80Hz.TBC | This document |
| Thermometer data | 1Hz (TBC) | ??? email |
| Motor voltage (or current, TBD) at a low rate for house-keeping | <100Hz (TBC) | ATC/LAM meeting May.00 |
| Motor voltage (or current, TBD) at a high rate for trouble shooting of transient effects (e.g. control systems tuning) | TBD | ATC/LAM meeting May.00 |

### Data Inputs

The following inputs are required to operate the BSM.

| Data | Rate | Reference |
| --- | --- | --- |
| Chop axis demand position | On Demand, max. 5Hz | AD19 |
| Jiggle axis demand position | On Demand, max. 1Hz | AD19 |
| Control system parameters (PID terms) | TBD, but slow | AD19 |
| Trajectory parameters (3 for each axis) | TBD, but slow | AD19 |
| Unlatch signal, if required | One-off | AD19 |

### Exported vibration

The BSM will produce vibration in the region 0-5 Hz, with TBD harmonics and TBD amplitude.

| The BSM shall induce micro-vibration measured on the optical bench (TBC at the detector sub-system mounting position), of less than 10 micro-g ( 9.81 (m/s²). | This document |
| --- | --- |

### Stray Magnetic fields

| To prevent spurious signal generation, magnetic field strength at the BSM position sensors should not exceed TBD | This document |
| --- | --- |

### Electro-Magnetic Compatibility

TBD - Grounding, Radiated emissions, etc…

### ICD's

The BSM interfaces with the following other subsystems in the SPIRE instrument. The interface to each sub-system is specified in the relevant Interface Control Document.

## BSM interface reference table

The master reference table is located in RD1.

| ID | Sub-System | Organization responsible | External ICD document | Internal ATC ICD document | Internal ATC ICD drawing/ file |
| --- | --- | --- | --- | --- | --- |
| 1 | BSM-SPIRE | RAL | Instrument Requirements Document (IRD). SPIRE-RAL-PRJ-000034 v0.30 May.00 | SPIRE-ATC-PRJ-000587 Annex A | SPIRE-BSM-021-001-001 |
| 2.1 | Structure – BSM | MMSL | ICD Structure - Mechanical I/F SPIRE-MSS-PRJ-000xxx v1.0 April 2001 | SPIRE-ATC-PRJ-000587 Annex B | SPIRE-BSM-021-002-001 |
| 2.2 | Structure – BSM | MMSL |  |  | SPIRE-BSM-021-002-002 (IGES file) |
| 2.3 | Thermometry | RAL | TBD |  | SPIRE-BSM-021-002-003 |
| 3 | Photometer Calibration Source - BSM | UoW, Cardiff | TBD | SPIRE-ATC-PRJ-000587 Annex C | SPIRE-BSM-021-003-001 |
| 4 | Launch Latch – BSM | LAM (TBC) | Spectrometer mirror mechanism design description LAM.SPI.PJT.NOT.200008 Ind 3 | SPIRE-ATC-PRJ-000587 Annex D | SPIRE-BSM-021-004-001 |
| 5.1 | Optics – external finish | LAM | Optical System Design Description SPIRE-LAM-PRJ-000447 Draft 1 18.Dec.00 | SPIRE-ATC-PRJ-000587 Annex E | SPIRE-BSM-021-005-001 |
| 5.2 | Optics – BSM | RAL | ??? |  | SPIRE-BSM-021-005-002 |
| 5.3 | Baffles – BSM | RAL | ??? |  | SPIRE-BSM-021-005-003 |
| 6 | Cryo-Harness | RAL / MSSL | SPIRE Harness Definition. SPIRE-RAL-PRJ-000608 Issue: 0.3 30.May.01 Harness routing : TBD (MSSL) | SPIRE-ATC-PRJ-000587 Annex F | SPIRE-BSM-021-006-001 |
| 7.1 | MCU-BSM | LAM | ??? | SPIRE-ATC-PRJ-000587 Annex G | SPIRE-BSM-021-007-001 |
| 7.2 | On Board Software - BSM | LAM | ??? |  | SPIRE-BSM-021-007-002 |
| 8 | Photometer Bolometer Arrays - BSM | MSSL | ICD Structure - Mechanical I/F SPIRE-MSS-PRJ-000xxx v1.0 April 2001 | Sub-System Specification EMC/ exported vibration ??? |  |
| 9 | Spectrometer Bolometer Arrays - BSM | MSSL | ICD Structure - Mechanical I/F SPIRE-MSS-PRJ-000xxx v1.0 April 2001 | Sub-System Specification EMC/ exported vibration ??? |  |
| 10 | FPU Simulator - BSM | TBD | TBD | TBD |  |
| 11 | Instrument Simulator - BSM | TBD | TBD | TBD |  |

## Design, manufacture and test requirements

This section details additional requirements which are placed on the sub-system which are not necessary to meet the functional or operational requirements, but are necessary to enable the sub-system to be designed, manufactured or tested. These are encapsulated as Product Assurance requirements and are fully covered in the BSM Product Assurance Plan, AD22

### Design requirements

UK Astronomy Technology Centre design procedures shall be adopted as applicable.

### Electronics Card Format

All electronics associated with the BSMe shall be mounted on double eurocards [AD19].

### Product Assurance Plan

The BSM deliverables will comply with the Spire Product Assurance Plan, AD20, and the BSM Product Assurance Plan AD22 .

Specific requirements are noted below, otherwise AD22 will be adopted.

### Mirror Flatness

To facilitate optical  laboratory testing, the mirror surface shall have a flatness of <100nm (P-V) TBC and an rms of TBD.

### Mirror Reflectivity

To facilitate optical testing laboratory testing, the mirror surface shall have a reflectivity of >80% at 633nm by design.

### Cleanliness

The BSM shall be assembled to class 1000 cleanliness, but shall be class 100 compatible by design.

### Material selection

Structures will be a 6082 grade aluminium alloy to UK standards, and will be selected in consultation with the optical bench design body (MSSL). The BSM mirror may be specified in grade 6061-T6/T651 to ensure adequate thermal stability based on ATC practice.

Fasteners will be cryogenic grade stainless steel. Where practicable they will be of a self locking type. Fasteners may include UNS thread types where required on the grounds of availability in small sizes, or as required by ICD, otherwise will be metric thread. In cases where a self locking fastener is not available, Stycast or Scotchweld 1838 will be used in visible applications under fastener heads.

### Storage

The BSM shall not suffer any performance degradation following storage in a dry nitrogen atmosphere for a period of up to 5 years.

Storage temperatures shall be in the range +5°C to +30°C.

## Environmental requirements

These requirements describe the environment the subsystem will encounter during its life.

### Operating environment

This section defines the environment for the BSM during operation. The BSM must meet all of the functional and operational requirements specified in section 4 when operating under this environment.

| All subsystems are required to undergo an environmental test programme that demonstrates the design and build standard of the sub-system models will be compatible with the environmental test programme to be carried out on the appropriate integrated instrument model. | IRD-SUBS-R01 |
| --- | --- |

### Shock

| No Shock specification is applied (TBC). As a working figure 50g static acceleration loads in all three axes are assumed. | AD2 |
| --- | --- |

### Quasi Static Loads

| For the BSM sub-system these are derived from the random vibration specification (see 4.7.1.4) using the Miles SDOF approximation to estimate rms and peak acceleration. | AD2 |
| --- | --- |
| For the SPIRE instrument as a whole the following Quasi-Static flight limit load are given. Per AD22 “All subsystems will be subjected to the same environment as defined above. The in table 1.4-1 defined accelerations are very important for limiting interface loads for the various sub-systems subjected to either sine, random or shock loads”. | AD22, table 1.4-1 |
| Quasi Static levels | Case 1 | Case 2 | Case 3 |  |
| x-direction | 25 g | - | - |  |
| y-direction | - | 14 g | - |  |
| z-direction | - | - | 14 g |  |

### Sine Vibration

| The provisional Qualification sine input (2 oct/min) specification is (As specified in AD2, AD22 these include the qualification factor of 1.5) : | AD22 Table 2.9.6-1 |
| --- | --- |
| Sine vibration levels | Frequency range | Input at base (QUAL) |  |
| X-direction | 5-30 Hz 30-100 Hz | 11 mm (0-peak) 40 g |  |
| Y-direction | 5-30 Hz 30-100 Hz | 11 mm (0-peak) 25 g |  |
| Z-direction | 5-30 Hz 30-100 Hz | 11 mm (0-peak) 25 g |  |

### Random Vibration

| BSM random Specification | Ref. instrument co-ordinate system | Email B.Winters 26.Jun.01 |
| --- | --- | --- |
| X 60 sec | g^2/hz | g^2/hz |  | Y 60 sec | g^2/hz | g^2/hz |  | Z 60 sec | g^2/hz | g^2/hz |
| f | Accept | Qual |  | f | Accept | Qual |  | f | Accept | Qual |
| 20 | 0.004 | 0.008 |  | 20 | 0.006 | 0.011 |  | 20 | 0.005 | 0.010 |
| 40 | 0.016 | 0.032 |  | 40 | 0.022 | 0.044 |  | 40 | 0.020 | 0.039 |
| 60 | 0.036 | 0.072 |  | 60 | 0.050 | 0.100 |  | 60 | 0.044 | 0.089 |
| 80 | 0.064 | 0.128 |  | 80 | 0.089 | 0.177 |  | 80 | 0.079 | 0.158 |
| 100 | 0.100 | 0.200 |  | 85 | 0.100 | 0.200 |  | 90 | 0.100 | 0.200 |
| 150 | 0.100 | 0.200 |  | 100 | 0.700 | 1.399 |  | 200 | 0.100 | 0.200 |
| 155 | 0.100 | 0.200 |  | 150 | 0.700 | 1.399 |  | 210 | 0.100 | 0.200 |
| 230 | 0.100 | 0.200 |  | 160 | 0.150 | 0.300 |  | 250 | 0.100 | 0.200 |
| 235 | 0.100 | 0.200 |  | 165 | 0.150 | 0.300 |  | 255 | 0.100 | 0.200 |
| 350 | 0.100 | 0.200 |  | 300 | 0.150 | 0.300 |  | 300 | 0.100 | 0.200 |
| 800 | 0.019 | 0.038 |  | 800 | 0.021 | 0.042 |  | 800 | 0.014 | 0.028 |
| 1000 | 0.012 | 0.024 |  | 1000 | 0.013 | 0.027 |  | 1000 | 0.009 | 0.018 |
| 1500 | 0.005 | 0.011 |  | 1500 | 0.006 | 0.012 |  | 1500 | 0.004 | 0.008 |
| 2000 | 0.003 | 0.006 |  | 2000 | 0.003 | 0.007 |  | 2000 | 0.002 | 0.004 |
| g-rms | 8.1 | 11.4 |  | g-rms | 11.1 | 15.7 |  | g-rms | 7.7 | 10.9 |

### Vacuum Level

| Less than 10-4 Pa TBC | ??? |
| --- | --- |

### Vacuum Outgassing

| Materials shall have a low outgassing rate with Total Mass Loss (TML) <1% and Volatile Condensable Material (VCM) ≤ 0.1% | AD22 |
| --- | --- |

### Temperature

| The BSM shall perform within specification at the operational temperature cited in 4.2.2. In addition, the BSM will operate with reduced performance at temperatures from 4-300K. | RD1 |
| --- | --- |

### Magnetic Fields

| To prevent spurious position signal input, stray magnetic fields must not exceed TBD at the chop and jiggle position sensors. | TBD |
| --- | --- |

### Survival Temperature

| The BSM shall remain fully operational following exposure to temperatures of 80°C for periods of up to 72 hours. (bakeout) | AD1 |
| --- | --- |

### Radiation environment

| The integrated dose for silicon behind 2 mm of aluminium is estimated at 12 kRad and behind 5 mm of aluminium as 3.5 kRad. These figures will be taken as the radiation tolerance for components in the warm electronics boxes and inside the cryostat respectively (TBC). | RD2 |
| --- | --- |

| Non-ionizing energy loss [MeV/g(Si)] | RD4 |
| --- | --- |
| Shield thickness | 3 Years | 5 Years | 10 Years |  |
| 2mm Aluminium | 1.83E+08 | 1.86E+08 | 2.62E+08 |  |
| 5mm Aluminium | 7.57E+07 | 7.66E+07 | 1.03E+08 |  |

| Total ionizing radiation dose in Si [rad] | RD4 |
| --- | --- |
| Shield thickness | 3 Years | 5 Years | 10 Years |  |
| 2mm Aluminium | 1.01E+04 | 1.04E+04 | 1.46E+04 |  |
| 5mm Aluminium | 3.79E+03 | 3.88E+03 | 5.11E+03 |  |

## Verification requirements

The BSM Development Plan (AD15) contains more detail on the actual tests to be carried out on the BSM. The table below shows how each of the functional and operational requirements in this document is to be demonstrated, for each of the deliverable BSM models. The deliverable models include the STM (deliverable to RAL but not ESA), CQM, PFM, FS

Key:

Test  									T

Measurement								M

Analysis	, Reference to calculations and previous tests, assumption		A

Inspection								I

Not Applicable 								X

Notes:

- The STM model may be delivered as a fixed mass with no mirror or a fixed mirror (TBD) The minimum requirements verification is specified accordingly. In the event that a representative rotating mirror is provided, the CQM test requirements will apply  (TBC).

- Tests and measurements are distinguished in that measurements are simple procedures e.g. to measure dimensions, mass etc. A test will in most cases include some combination of measurement devices, set up procedures, inspection, calibration, calculation, etc in order to demonstrate a requirement.

### Performance Requirements

| Reference | Requirement | STM | CQM | PFM | FS | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| 4.1.1 | Angular Travel - Chop Axis | X | T | T | T |  |
| 4.1.2 | Angular Travel - Jiggle Axis | X | T | T | T |  |
| 4.1.3 | Minimum Step Size | X | T | T | T |  |
| 4.1.4 | Chop Frequency | X | T | T | T |  |
| 4.1.5 | Jiggle Frequency | X | T | T | T |  |
| 4.1.6 | Holding position | X | T | T | T |  |
| 4.1.7 | Stability | X | T | T | T |  |
| 4.1.8 | Position Measurement | X | T | T | T |  |
| 4.1.9 | Settling Time | X | T | T | T |  |
| 4.1.10 | Chop repeatability | X | T | T | T |  |

### System Requirements

| Reference | Requirement | STM | CQM | PFM | FS | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| 4.2.1 | Mechanical Dimensions | M | M | M | M |  |
| 4.2.2 | Operating Temperature | T | T | T | T |  |
| 4.2.3 | Thermal Isolation | T | T | T | T |  |
| 4.2.4 | Cold Power Dissipation | X | T (a) | T | T | (a) Cold power dissipation of the CQM may not be compliant if non-space rated components are used for motor coils |
| 4.2.5 | Warm Electronics Power Dissipation | X | T | T | T |  |
| 4.2.6 | Mirror Surface Dimensions | M (b) | M | M | M | (b) X if STM has no mirror |
| 4.2.7 | Mirror Surface Finish | I/M (c) | I/M | I/M | I/M | (c) X if STM has no mirror |
| 4.2.11 & 4.2.8 | Mirror Surface Reflectivity | A(d) | A | A | A | (d) X if STM has no mirror |
| 4.2.9 | Mirror Surface Emissivity | X | X | X | X | Complement of 4.2.11 & 4.2.8 |
| 4.2.10 | Baffle | X | M/T | M/T | M/T | Measurement will be against design drawings. Tests only performed on integration at RAL |
| 4.2.11 | Position of Rotation Axes | M/I (e) | M/I | M/I | M/I | (e) X if STM has no mirror |
| 4.2.12 | Orthogonality of Rotation Axes | X | T | T | T |  |
| 4.2.13 | Fail Safe (No Drive Signal) Position | X | T/A(f) | T/A(f) | T/A(f) | (f) May require supporting analysis of rest position in 1 g field is not (0,0) |
| 4.2.14 | Fail Safe (Mechanical Failure) Position | X | X | T/A(g) | T/A(g) | (g) Demonstrated on tests on QM or DM |
| 4.2.15 | Mass | M | M | M | M |  |
| 4.2.16 | Cool-down time | T | T | T | T | Cooldown times will be dependent on cryostat configuration. |
| 4.2.17 | Reliability | X | X | A(h) | A(h) | (h) demonstrated by QM programme and by design/analysis |
| 4.2.18 | Failure Modes | X | X | A(j) | A(j) | (j) demonstrated by QM programme and by design/analysis |

### Operational Specification

| Reference | Requirement | STM | CQM | PFM | FS | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| 4.3.1 | Operational Safety | A | A | A | A | Demonstrated by analysis/design/risk assessment |
| 4.3.2 | Lifetime | X | X | A(k) | A(k) | (k) demonstrated by QM programme |
| 4.3.3 | Operating modes | X | T(l) | T | T | (l) CQM will not have redundant modes |
| 4.3.4 | Jiggle Mode | X | T | T | T |  |
| 4.3.5 | Chopping Mode | X | T | T | T |  |
| 4.3.6 | Scan mapping | X | X | X | X | Only applicable on spacecraft |
| 4.3.7 | Stare or 'holding' mode | X | T | T | T |  |
| 4.3.8 | Combinations of Modes | X | T | T | T |  |

### Interface requirements

| Reference | Requirement | STM | CQM | PFM | FS | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| 4.4.1 | Data Outputs | X | T | T | T | Fully demonstrated only on integration at LAM/ RAL . ATC tests will demonstrate compliance to ICD |
| 0 | Data Inputs | X | T | T | T | Fully demonstrated only on integration at LAM/ RAL . ATC tests will demonstrate compliance to ICD |
| 4.4.3 | Exported vibration | X | T | T | T | On integration to SPIRE at RAL |
| 4.4.4 | Stray Magnetic fields | X | T | T | T | On integration to SPIRE at RAL |
| 4.4.5 | Electro-Magnetic Compatibility | X | A/T | T | T | On integration to SPIRE at RAL |
| 4.4.6 | ICD's | I/M/T | I/M/T | I/M/T | I/M/T |  |

### Design, manufacture and test requirements

| Reference | Requirement | STM | CQM | PFM | FS | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| 4.6.1 | Design requirements | A | A | A | A | Compliance indicated in ADP |
| 4.6.2 | Electronics Card Format | X | I | I | I | Inspection of LAM deliverables |
| 4.6.3.1 | Mirror Flatness | M(m) | M | M | M | (m) X if STM has no mirror |
| 4.6.3.2 | Mirror Reflectivity | A(n) | A | A | A | (n) X if STM has no mirror |
| 4.6.3.3 | Cleanliness | I | I | I | I | Compliance determined by TBC |
| 4.6.3.4 | Material selection | I | I | I | I | Compliance indicated in ADP |
| 4.6.3.5 | Storage | A | A | A | A | Compliance indicated in ADP |

### Environmental requirements

| Reference | Requirement | STM | CQM | PFM | FS | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| 4.7.1.1 | Shock | X | X | X | X | No requirement |
| 4.7.1.2 | Quasi Static Loads | T | X | A(o) | A(o) | (o) demonstrated by QM programme |
| 4.7.1.3 | Sine Vibration | T | X | A(p) | A(p) | (p) demonstrated by QM programme |
| 4.7.1.4 | Random Vibration | T | X | A(q) | A(q) | (q) demonstrated by QM programme |
| 4.7.1.5 | Vacuum Level | T | T | T | T |  |
| 4.7.1.6 | Vacuum Outgassing | A | A | A | A | Demonstrated via materials selection and Compliance indicated in ADP |
| 4.7.1.7 | Temperature | T | T | T | T |  |
| 4.7.1.8 | Magnetic Fields | X | TBD | TBD | TBD | EMC tests performed when integrated at RAL. Tests to be determined once specification exists |
| 4.7.1.9 | Survival Temperature | T | T | T | T |  |
| 4.7.1.10 | Radiation environment | X | X | TBD | TBD | EMC tests performed when integrated at RAL. Tests TBD |

This page left deliberately blank

# Footnotes

Note that the terminology in this figure is in need up an update, as the spacecraft has been re-named Herschel, formerly FIRST. Hence FIRST-SPIRE Focal Plane Unit, or FSDPU should now read HSDPU.

.i.e. responsible for feeding ICD info upwards to SPIRE system design