# FIRST SPIRE

# DPU  Subsystem Specification Document

# Document Ref.:  SPIRE-IFS-PRJ-000462

# Issue:	Issue 1.1

Prepared by:		Anna 	Maria Di Giorgio			Date:     26/03/2001

Riccardo Cerulli-Irelli

Renato Orfei

Distribution List :

| RAL | B.M.Swinyard |
| --- | --- |
|  | K.King |
| IFSI | S. Pezzuto |
|  | C. Codella |
| CEA-Sap | J.-L. Auguères |
|  | C. Cara |

1	Introduction	5

1.1	Purpose of the document	5

2	Document List	5

2.1	Applicable Documents	5

2.2	Reference Documents	5

2.3	Acronyms and Glossary	6

2.3.1	Acronyms	6

3	Subsystem Description	7

3.1	General Overview	7

3.2	Subsystem Design	9

3.3	Mission Profile	14

3.4	Product Tree	14

4	Specifications	15

4.1	Functional specifications	15

4.1.1	Performance specifications	15

4.1.2	Technical specifications	15

4.2	Operational specifications	16

4.2.1	Operational Safety	16

4.2.2	Lifetime	16

4.2.3	Telemetry	16

4.2.4	Telecommands	17

4.3	Interface Requirements	19

4.4	Design and Manufacturing Specifications	19

4.4.1	Design requirements	19

4.4.2	Design rules	21

4.4.3	Manufacture Requirements	22

4.5	Logistic Requirements	22

4.6	Environment Requirements	22

4.6.1	Natural environment	22

4.6.2	Operating Environment	22

4.7	Verification Requirements	22

4.7.1	DPU Acceptance And Qualification	22

APPENDIX 1: QUALIFICATION TESTS DESCRIPTION	24

Document Status Sheet:

| Document Title: FIRST SPIRE DPU Subsystem Specification Document |
| --- |
| Issue | Revision | Date | Reason for Change |
| Draft 1 |  | 23 May 2000 | First draft |
| Draft 2 |  | 13 June 2000 | Updated accordingly to new Issues of the Applicable Documents |
| Issue 1.0 |  | 24 Nov 2000 | First Issue, updated accordingly to new Issues of the Applicable Documents |
| Issue 1.0 | 0.1 | 26 Mar 2001 | Updated accordingly to new Issues of the Applicable Documents. Low speed interface protocol updated. |

Document Change Record:

| Document Title: FIRST SPIRE DPU Subsystem Specification Document |
| --- |
| Document Reference Number: SPIRE-IFS-PRJ-000462 |
| Section | Reason For Change |
| 3.2, page 13 | New Low Speed Interface Protocol Description |
| 3.2, fig. 3-10 | New Low Speed Interface Protocol graphical representation |
| 3.2, fig. 3-4 | New CPU memory organisation scheme |
| 4.4.1, DPU-DES-32 | New DPU mechanical dimensions. |

# Introduction

## Purpose of the document

The Istituto di Fisica per lo Spazio Interplanetario (IFSI) of the Italian Consiglio Nazionale delle Ricerche (CNR) is responsible for the design and manufacturing of the three Digital Processing Units/Instrument Control Units for the three instruments to be flown on board of the ESA satellite FIRST: HIFI, PACS and SPIRE.

This specification defines the requirements applied to the performances, the design and the qualification of the SPIRE Digital Processing Unit (FSDPU subsystem). It is applicable to the AVM, the QM, the PFM and the FS.

The DPU On Board Software specification is given in the DPU/ICU OBS User Requirements Document and DPU/ICU OBS Software Specification Document.

# Document List

## Applicable Documents

| Document Reference | Name | Number/version/date |
| --- | --- | --- |
| AD1 | SPIRE Instrument Requirements Document | SPIRE/RAL/N/0034 Issue 0.1 23 Nov 2000 |
| AD2 | FIRST/Planck Instrument Interface Document Part A | PT-IID-A-04624 Draft 0.3 15 May 2000 |
| AD3 | FIRST/Planck Instrument Interface Document Part B Instrument “SPIRE” | SCI-PT-IIDB/PT-SPIRE-02124 Issue 0.1 01 Sep 2000 |
| AD4 | Operating Modes for the SPIRE Instrument | SPIRE-RAL-DOC-000320 Issue 0.22 14 June 2000 |
| AD5 | FIRST L-2 Radiation Environment | SPIRE-ESA-DOC-000195 |
| AD6 | DPU Interface Control Document | SPIRE-IFS-DOC Issue 0.1 22 Nov 2000 |

## Reference Documents

| Document Reference | Name | Number/version |
| --- | --- | --- |
| RD1 | DPU/DRCU Interface Control Document | SPIRE-SAP-PRJ-000451 Issue 0.2 21 June 2000 |
| RD2 | Discussion Note on the DPU/DRCU Operations Protocols- B. Swinyard | 22 May 2000 |

## Acronyms and Glossary

### Acronyms

| AD | Architectural Design |
| --- | --- |
| ATP | Acceptance Test Plan |
| AVM | Avionic Model |
| CNR | Consiglio Nazionale delle Ricerche |
| CPU | Control Processing Unit |
| CDMS | Computer Data Management System |
| CPP | Common parts Procurement |
| CQM | Cryogenic Qualification Model |
| DDD | Detailed Design Document |
| DPU | Digital Processing Unit |
| DSP | Digital Signal Processor |
| EEPROM | Electrically Erasable Programmable Read Only Memory |
| EMC | ElectroMagnetic Compatibility |
| EMI | ElectroMagnetic Interference |
| ESA | European Space Agency |
| FIRST | Far InfraRed and Submillimeter Telescope |
| HIFI | Heterodyne Instrument for FIRST |
| HK | HouseKeeping |
| HW | HardWare |
| IBDR | Instrument Baseline Design Review |
| ICD | Interface Control Document |
| ICDR | Instrument Critical Design Review |
| ICU | Instrument Control Unit |
| IHDR | Instrument Hardware Design Review |
| IFSI | Istituto di Fisica dello Spazio Interplanetario |
| ISVR | Instrument Science Verification Review |
| NA | Not Applicable |
| OBS | On-Board Software |
| PA | Product Assurance |
| PACS | Photoconductor Array Camera and Spectrometer |
| PROM | Programmable Read Only Memory |
| RAM | Random Access Memory |
| SCC | SpaceCraft Components |
| SEU | Single Event Upset |
| SPIRE | Spectral and Photometric Imaging REceiver |
| SVM | Service Module |
| SW | Software |
| TBC | To Be Confirmed |
| TBD | To Be Defined |
| TBW | To Be Written |
| TVT | Thermal Vacuum Test |

# Subsystem Description

## General Overview

The DPU of the SPIRE Instrument (FSDPU) interfaces with the Detector readout and Control Unit subsystem (FSDRC) and with the S/C telemetry, telecommand (the on board CDMS, Command and Data Management system) and power systems. In  Figure 3-1 the block diagram showing the interfaces of the FSDPU  is presented, including the cryo-harness. Conceptually the FSDRC is a single unit. However for accomodation reasons it will be split into two physical units: Instrument Control Unit (FSICU) and Detector Readout Unit (FSDRU).

FSICU contains:

- the electronics for the power conversion and distribution to the DRCU, for the control and readout of the thermometers, the cooler and  the calibration sources (Subsystem Control Unit, SCU)

- the electronics for the control and readout of the cold mechanisms (Mechanisms Control Unit, MCU).

FSDRU contains the bias conditioning electronics for the bolometers arrays and JFET units and the lock in amplifiers and readout electronics for all the detector arrays.

The interface with FSDRC will be composed by three high speed data links for science data collection (two links with FSICU and one link with FSDRU) and one low speed serial bus with three output buffers, for command transmission and housekeeping data collection (two outputs to FSICU and one output to FSDRU). Refer to AD6 for a detailed description of the harness.

The interface with the spacecraft shall be able to handle a baseline data rate of 100 kbps, with burst mode transmission up to 300 kbps. The interface shall be compliant with the MIL-STD-1553B standard, with the FSDPU acting as a remote terminal and the CDMS as the bus controller.

In Figure 3-2 the SPIRE DPU high level block diagram is shown: the FSDPU box is fully hardware redundant, with one DPU ON and the other in cold redundance. Each of the two redunded computers has its own DC/DC converter, CPU, memory and interfaces both to spacecraft and to the subsystems. Only the Avionic Models (see section 3.4) will have no redundancy, neither for the DC/DC converter, nor for the on board computer.

The main blocks of each of the two redunded DPUs are the CPU, the Spacecraft and subsystems interface and the DC/DC Converter.

## Subsystem Design

The FSDPU subsystem will include a synchronised  DC/DC converter with a nominal input DC voltage of 28 V and the overall characteristics in agreement with AD2. In figure 3-3 a block diagram of the DC/DC converter is shown. Converter gets the redundant 131.072 kHz (TBC) synchronisation signal from the spacecraft. The synch signal is transformer coupled with the transformer located on the spacecraft. The receiver DPU interface shall have an impedance >05Kohm in parallel to <=2pF.

The adopted CPU is the TEMIC TSC21020, that is a Digital Signal Processor (DSP) unit developed by Analogue Devices and implemented for flight use by TEMIC.

The CPU board will be based on this chip (20 MHz clock), with:

- an appropriate timer for time management and synchronisation purposes

- a watch-dog system that can be hardware disabled through jumper;

- Rad Tolerant memories and components

In Figure 3-4 the main blocks of the CPU board are shown.

In Figure 3.4 the memory organisation of the CPU is shown with the dimensions of the various types of memories. The CPU board will carry (on the PROMs) some basic software containing at least:

- a driver for the interface circuit with the S/C;

- a programme loader through the S/C telemetry;

- a driver for writing the EEPROMs;

- a function to carry out the EEPROM checksum test.

The DPU interfaces mechanically with the S/C and electrically with the S/C and the various subsystems. The electrical hardware interface with the S/C consists in:

- interface with the S/C Power Distribution System and the 28 V lines;

- interface with the DC/DC synchronisation signal: 131.072 kHz (AD2, section 5.9.6.1) implemented through a transformer;

- interface with the telemetry and telecommand subsystems.

In figure 3-5 a block diagram of the S/C interface board is shown. The MIL-STD-1553B standard is implemented through one nominal and one redundant transformer in the long stub configuration.

The interface between DPU and DRCU is shown schematically in Figure 3-7; a detailed description of this interface is given in RD1.  For the science data link, three monodirectional fast (1 MHz clock) synchronous serial input interfaces, each of which with 8 KW 16 Bit FIFO, are foreseen: the data can be received by the DPU at the same time. The clock, gate and data signals, coming from the subsystems, are as in Figure 3-8.

A serial synchronous bus is foreseen to interface with the control electronics of the focal plane unit subsystems: the bus will be used to transmit commands and receive responses or to control and receive housekeeping information. The baseline clock speed is 0.2 MHz (TBC). In Figure 3-9 the signals are shown: CLK & TX_DAT are coming from DPU and go in parallel with three distinct hardware interfaces to the three DRCU electronics blocks; the three RX_DAT lines are coming each from each of the three blocks and are multiplexed inside the DPU (see RD1).

All data transactions with the addressed subsystem (addr. In TX_DAT),  are initiated by DPU. 
DPU will send data to all subsystems using one serial data line TX_DAT and can send both commands and HK requests via this line. 
Subsystems, if required, will send responses via RX_DAT line.

A command is made of 2 start bits, 2 address bits, 28 data bits and 1 stop bit.
A HK request is made by setting the second start bit.

A HK response will consist of 2 start bits, 2 address bits, 28 data bits and 1 stop bit

The sub-unit address field in the TX command is used to select the input channel RX. No command can be sent to a sub-unit until the echo/HK RX corresponding to the last command sent is received. Figure 3-10  shows the transmission-reception sequence.

Figure 3-10 Low speed Interface – transmission reception protocol

Clock and TX_DAT are generated by DPU and distributed to all subsystems

For internal reading of analogue signals an A/D converter (12 bit) plus MPX (8 Channels) will be provided in order to digitise the information of  an internally conditioned thermistor and of the DC/DC converter voltage and total current.

## Mission Profile

The DPU will be designed to be used for 2 years on the ground, 2 years (TBC) of storage and 4 years in orbit with a probability better than 90% for the single ICU section (prime or redundant).

## Product Tree

The following deliverables are foreseen:

- DPU-AVM (Avionic Model): no redundancy, neither for the DC/DC converter, nor for the on board computer; only commercial grade components. These are to be used for the spire BBM (breadboard model), see section 2.4 of AD1. It is anticipated that it will not be possible to comply with what requested in AD2, chapter-page 9-1, paragraph 9.2.2.1, i.e. the AVM components will not be purchased, in general, from the same supplier of the FM/FS parts. The AVM will be delivered to ESA.

- DPU-QM (Qualification Model): full redundancy, both for the DC/DC converter, and for the on board computer; only commercial grade components  as far as possible within the fit, form and function of the flight model. The printed boards artwork will be the same as for FM/FS. This unit will undergo qualification tests. It is not a deliverable to ESA.

- DPU-PFM (Proto-Flight Model ): full redundant box; SCC level B components for the spacecraft interface, SCC level C for all the other components is the baseline. If it is confirmed by ESA the decision to issue a Common Parts Procurement for which ESA will pay non recurring costs and surcharge costs, then in this case all components will be at SCC level B. This unit will undergo acceptance tests.

- DPU-FS (Flight Spare): only spare boards (CPU, S/C I/F, SubSytem I/F, DC/DC Conv., mother board): SCC level B components for the spacecraft interface, SCC/C level for all the other components is the baseline, but the same as for the PFM applies. These boards will undergo acceptance tests.

# Specifications

## Functional specifications

### Performance specifications

| Requirement ID | Description | Reference |
| --- | --- | --- |
| DPU-FUN-01 | The interfaces of FSDPU with FSDRC shall be designed in order to couple with the maximum output data rates of the subsystems in the Cold Focal Plane: FTS mechanism controller; Beam Steering Mirror; Detector Focal Planes units (3 Photometer arrays and 2 Spectrometer arrays); Sorption cooler; Temperature probes; DRU/ICU housekeeping; Calibration Sources. | RD2, AD4 Sect. TBD |
| DPU-FUN-02 | The DPU shall be able to acquire all Photometer detector pixels corresponding to a 4'x8' FOV (288 detectors) at a maximum readout frequency of 40 Hz per frame and 16 bits per sample. | RD2, AD4 Sect. TBD |
| DPU-FUN-03 | The DPU shall be able to acquire all Spectrometer detector pixels corresponding to a 2.6'x2.6' FOV (56 detectors) at a maximum readout frequency of 200 Hz per frame and 16 bits per sample. | RD2, AD4 Sect. TBD |
| DPU-FUN-04 | Photometer data: The instantaneous dynamic range of the readout of a pixel shall be 16 bits. | AD4 Sect. TBD |
| DPU-FUN-05 | Spectrometer data: The instantaneous dynamic range of the readout of a pixel shall be: 15 bits (with background nulling). | AD4 Sect. TBD |

### Technical specifications

| DPU-FUN-06 | The DPU shall be able to handle the adopted standard MIL-STD-1553B for the interface with the spacecraft, supporting an average telemetry rate of 96 kbps, when the instrument is in prime mode, and of 2 kbps otherwise. | AD2 sect. 5.11.1 AD3 sect. 5.11.1 |
| --- | --- | --- |
| DPU-FUN-07 | The DPU shall be able to handle the adopted standard MIL-STD-1553B for the interface with the spacecraft, supporting a maximum telecommand rate of 4 kbps. | AD2 sect. 5.11.4 |
| DPU-FUN-08 | Maximum DPU power consumption: 15W Note by IFSI: the actual estimate of the DPU HW manufacturer is 24(6W | AD3 Sect. 5.9.3 |

## Operational specifications

### Operational Safety

| Requirement ID | Description | Reference |
| --- | --- | --- |
| DPU-SAF-01 | Failure of the DPU, or one of its components, shall not affect the health of any other subsystem, the instrument or the interface with the satellite. | IRD-SAFE-R06 |
| DPU- SAF-02 | Failure of any component in the DPU shall not damage any redundant or backup component designed to replace that component in the subsystem | IRD-SAFE-R09 |
| DPU- SAF-03 | No ASICs or FPGAs shall be capable of affecting instrument operations until they are in a defined state. |  |
| DPU- SAF-04 | It shall be possible to break via software all electronic control loops implemented in hardware, provided that the relevant commands are implemented in the FSDRC in agreement with FSDPU. | IRD-REL-R05 |
| DPU- SAF-05 | The instrument shall monitor the operational status of the instrument on-board computer and take appropriate action in case of error. (a watchdog function will be implemented to identify if the on board computer has crashed ) TBC | IRD-AUT-R06 |
| DPU- SAF-06 | Cold redundant hardware shall be provided | IRD-REL-R03 |

### Lifetime

| Requirement ID | Description | Reference |
| --- | --- | --- |
| DPU-OPE-01 | The DPU PFM shall be designed to couple with an integrated lifetime of 2 years. | AD2 |
| DPU-OPE-02 | The DPU PFM shall be designed to couple with a ground storage lifetime of 2 years (TBC). | AD2 |
| DPU-OPE-03 | The DPU PFM shall be designed to couple with an in orbit lifetime of 4 years, with a probability better than 90% for the single DPU section (prime or redundant). | AD2 |

### Telemetry

The housekeeping parameters provided by the DPU are (list is TBC):

- DPU Voltage (2bytes)

- DPU Current (2bytes)

- DPU Temperature (2bytes)

### Telecommands

The DPU dedicated commands are (list is TBC):

- DPU reset

Command: DPU_N_Reset(); DPU_R_Reset()

Parameters: Input  --- None

Output --- None

Action: Warm reset of the DPU. A warm reset is similar to a reboot without neither a memory test nor a copy of EEPROM into RAM. In this way the following DPU status is like after a switch-on but with its memory content preserved. This is an immediate command.

- Measurement Reset (TBC)

- Execute a function onboard

Command: DPU_N_EXEC_FUNCT (8,3)

Parameters: Input  --- 	FunctionID	8bits

N		8bits

PArameters	NX16bits

Action: Executes a function already stored onboard

- Set the telemetry rate

Command: DPU_N_SET_TM_RATE (8,3)

Parameters: Input  --- 	mode	8bits

Action: Set the telemetry rate: prime, parallel.

- Memory check

Command: DPU_N_MEM_CHECK (6,9)

Parameters: Input  --- 	MemID	8bits

Address	24bits

Length		16bits

Action: A checksum is derived for the specified area in memory.

- Memory load

Command: DPU_N_MEMORY_LOAD (6,2)

Parameters: Input  --- 	MemID	8bits

Address	24bits

Length		16bits

Data		16Xlength bits

Action: RAM Memory load (TBC)

- Memory dump

Command: DPU_N_MEMORY_DUMP (6,5)

Parameters: Input  --- 	MemID	8bits

Address	24bits

Length		16bits

Action: Memory dump applicable to any one of the 3 types of memory, PM, PM, EEPROM (TBC)

- Subsystem Parameter Table Update

Command: DPU_N_TABLE_UPDATE (6,2)

Parameters: Input  Start 	16 bit

Length 	16bit

Data 	16Xlength

Output --- Return 	4 Bytes

Action: The content at addres Start is substituted for by the content at address Data. The pointers Start and Data are incremented by one an the operation is repeated until Length bytes have been transferred. This command updates (part of) the DPU parameters stored onboard in the s ubsystems parameters table.  DATA are stored in Data memory starting from ADDRESS for a total of LENGTH bytes

- Set the predefined HK packet to be provided

Command: DPU_N_SET_HK_LIST(8,3)

Parameters: Input  --- Mode	8bits

Output --- Return 6 Bytes

Result 1 Byte

Action: sets the predefined list of HK values for the HK packet (the total number of predefined packets depends on the number of operating modes).

- Enable packet transmission

Command: DPU_N_ENABLE_PACKET_TRANSMISSION(14,1)

Parameters: Input  --- 	N	8bits

Type	8bits

Sub-type	8bits

SID		8bits

Action: enables the transmission of telemetry source packets of the specified type and subtype.

- Disable packet transmission

Command: DPU_N_DISABLE_PACKET_TRANSMISSION(14,2)

Parameters: Input  --- 	N	8bits

Type	8bits

Sub-type	8bits

SID		8bits

Action: disables the transmission of telemetry source packets of the specified type and subtype.

- All commands related to the time synchronisation (TBC):

Command: DPU_N_TIME_SYNC(9,4)

Command: DPU_N_TIME_VER(9,7)

Command: DPU_N_TIME_SET(9,4)

- Test connection(TBC)

Command: DPU_N_TEST_CONN(17,1)

Action: Start the “Are You alive?” procedure.

## Interface Requirements

The required operating temperatures at the interface of the SVM with FSDPU shall be compliant with AD3, section 5.7.3:

| Operating | Start-up | Switch-off | Non-operating |
| --- | --- | --- | --- |
| Min. 0C | Max. 0C | 0C | 0C | Min. 0C | Max. 0C |
| -15 | +45 | -30 | +50 | -35 | +60 |

With acceptance temperature 5 0C below min. and 5 0C above max. operating temperatures.

Qualification temperature 10 0C below min. and 10 0C above max. operating temperatures.

For what concerns the interfaces with the other instrument subsystems, the following requirement is applicable:

| Requirement ID | Description | Reference |
| --- | --- | --- |
| DPU-IF-01 | The interface with FSICU and FSDRU shall be compliant with the description in AD6. | IFSI |

## Design and Manufacturing Specifications

### Design requirements

| Requirement ID | Description | Reference |
| --- | --- | --- |
|  | CPU board design |  |
| DPU-DES-01 | The CPU board shall be based on the DSP TEMIC TSC21020, at least 20 MHz clock, chip. | IFSI |
| DPU-DES-02 | The CPU board shall carry a watch-dog system (TBC). | IFSI |
| DPU-DES-03 | The CPU board shall include a programmable timer, with a precision of 1 (s and a max capacity of 100s. | IFSI |
| DPU-DES-04 | The CPU board shall have at least 32 kbytes of PROM memory with the bootstrap programme and software to face emergency situation and for maintenance. | IFSI |
| DPU-DES-05 | The CPU board shall have at least 512 Kbytes of EEPROM memory for the main programme. | IFSI |
| DPU-DES-06 | The CPU board should have at least 3 Mbytes of PROGRAMME static RAM. | IFSI |
| DPU-DES-07 | The CPU board should have at least 2 Mbytes of DATA static RAM. | IFSI |
| DPU-DES-08 | It shall be possible to modify the EEPROM’s content during flight through a maintenance programme resident in PROM and through a software programme coming from the telecommand system. | IRD-CMD-R13 IFSI |
| DPU-DES-09 | All RAM (DRAM) memory (both DATA and PROGRAMME memory) should be SEU free. | IFSI |
| DPU-DES-10 | The CPU board shall have a system bus interface working either in master or slave mode. In master mode the board can have access to other digital boards through the bus. In slave mode other master boards (for instance the S/C interface board) can have access to a Dual-Port RAM memory bank, accessible to CPU, to exchange with CPU messages and data blocks. | IFSI |
| DPU-DES-11 | The CPU board shall carry on PROM the following basic software: a loader of a programme from telecommands; a driver for the spacecraft I/F (MIL-STD-1553B) a driver for the EEPROM writing. a function to carry out the EEPROM checksum test Moreover the CPU board shall support the EONIC Virtuoso operating system. |  |
|  | Low speed interface design |  |
| DPU-DES-12 | All links use the RS 422 standard (balanced line drivers and receivers). | AD6 Sect. 4.1 |
| DPU-DES-13 | All the frequencies generated within the DPU shall come from the same oscillator, in order to limit the EMC problems. | AD1 Sect. 2.10 |
| DPU-DES-14 | All data transactions with any addressed subsystem (addr. In TX_DAT, see fig. 3-9), are initiated by DPU. DPU shall send data to all subsystems using one serial bus line TX_DAT with three output buffers and can send both commands and HK requests via this line. | AD6 Sect. 4.2 |
| DPU-DES-15 | DPU shall be able to accept the subsystems responses via the three RX_DAT lines (see figure 3.7). | AD6 Sect. 4.2 |
| DPU-DES-16 | The Clock rate shall be at least 0.2MHz (TBC). | IFSI |
| DPU-DES-17 | Clock and TX_DAT shall be generated by DPU and distributed to all subsystems. | AD6 Sect. 4.2, 4.5 |
| DPU-DES-18 | RX_DAT lines, coming from each subsystem, shall be multiplexed in the DPU. | AD6 Sect. 4.2 |
| DPU-DES-19 | For internal reading of analogue signals an A/D converter (12 bit) plus MPX (8 Channels) shall be provided in order to digitise the information of an internally conditioned thermistor and of the DC/DC converter voltages and total DPU current. | IFSI |
|  | High speed interface design |  |
| DPU-DES-20 | Three fast (1 MHz clock, TBC) synchronous serial input interfaces shall be provided, each of which with 8 KW 32 Bit FIFO. The clock, gate and data signals, coming from the subsystems, are as in Figure 2-8. All data can be received by the DPU at the same time. | AD6 Sect. 4.3 |
|  | DC/DC Converter design |  |
| DPU-DES-21 | The synchronised DC/DC converter board shall have the following main characteristics: - input DC voltage ranging from 26 to 30 V (TBC), nominal is 28 V within 1%(TBC); | AD2 sect. 5.9.5.2 |
| DPU-DES-22 | max power to the DPU: 15W Note by IFSI: the actual estimate of the DPU HW manufacturer is 24(6W | AD3 sect. 5.9.3 |
| DPU-DES-23 | - efficiency of 70% or better; | IFSI |
| DPU-DES-24 | - input filter with EMI-EMC properties (following ESA EMC/EMI specs); | IFSI |
| DPU-DES-25 | - overall characteristics in agreement with FIRST IID-A (inrush current etc.). | AD2 sect. 5.9.5.4 |
| DPU-DES-26 | - input impedance = 5kOhm in parallel to 200 pF. | AD2 sect. 5.9.6.2 |
| DPU-DES-27 | The DC/DC converter shall support a synchronisation signal (squarewave, 5.0 V +/- 20%, ground free, transformer coupled) with a frequency of 131.073 kHz. | AD2 sect. 5.9.6.1-2 |
| DPU-DES-28 | Each of the two DC/DC converters shall be connected to an individual synchronisation signal | AD2 sect. 5.9.6.1 |
| DPU-DES-29 | In absence of a synchronisation signal, the DC/DC converter shall be free running at the nominal frequency +/- 10% with nominal performance. | AD2 sect. 5.9.6.1 |
|  | Spacecraft interface design |  |
| DPU-DES-30 | The spacecraft interface board shall be compliant with the MIL-STD-1553B standard. | AD3 sect. 5.11.5 AD2 sect. 5.11.6 |
|  | Overall mechanical design |  |
| DPU-DES-31 | The total FSDPU mass shall be less than 10 Kg. | AD3 sect. 5.5 |
| DPU-DES-32 | The FSDPU dimensions shall be 240x218x194 mm3 Note by IFSI: the actual dimensions after a first design of the mechanical box are 274x258x194 mm3 | AD3 sect. 5.5 AD6 Sect. 3.1 |
| DPU-DES-33 | The maximum shock to be sustained in any direction is 5g (TBD). | AD3 sect. 5.15.3.1 |

### Design rules

| Requirement ID | Description | Reference |
| --- | --- | --- |
| DPU-DES-34 | The boards dimensions should preferably be of «double Europe» standard. |  |
| DPU-DES-35 | All DPU boards shall carry Rad Tolerant memories and components: AVM: commercial grade components required; QM: commercial components or better to match Fit, Form and Functions of the FM/FS units; printed boards artwork shall be the same as FM/FS. PFM and FS: SCC level B for the S/C I/F SCC level C for all other components (baseline: if CPP confirmed, all components at SCC/C level B). |  |
| DPU-DES-36 | External connectors characteristics and mounting shall be compliant with AD2 indications. | AD2 sect. 5.10.1 |

### Manufacture Requirements

| Requirement ID | Description | Reference |
| --- | --- | --- |
| DPU-DES-37 | All the pertinent ESA recommendations for boards manufacturing shall be applied. | IFSI |

## Logistic Requirements

Normal laboratory conditions will be suitable for the ICU as the FM unit will be enclosed in a plexiglass box with an aluminum plate and it will be possible to have access to the box connectors through appropriate windows. A clean room of at least class 100000 is the preferred environment ( see AD3 section 5.15.3.1). Precautions have to be taken in order to avoid ESD damages.

## Environment Requirements

See section 4.5.

### Natural environment

See section 4.3 for the in-orbit operating temperatures of the DPU.

See section 4.5 for the storage environment.

Radiation environment: described in AD5.

### Operating Environment

See sections 4.3 and 4.6.1 above.

## Verification Requirements

### DPU Acceptance And Qualification

According to AD1, section 2.5, the SPIRE instrument will be qualified at unit level (i.e. the Warm electronics units and  the cold FPU units).

Adopting the assumptions listed  in section 3.3 of AD1, the DPU will undergo the following tests:

| Test: | DPU AVM | DPU EQM | DPU PFM | DPU FS |
| --- | --- | --- | --- | --- |
| Functional Test | X | X | X | X (note2) |
| Performance Test | X | X | X | X (note2) |
| Interface Drawing Verification | X * | X | X | NA |
| Electrical Interface Tests | X | X | X | NA |
| Vibrations Tests | NA | Q | A | NA |
| Thermal-.Vacuum Test | NA | Q | A | NA |
| Radiation tolerance | NA | NA | note 1 | note 1 |
| EMI / EMC | NA | Q (note 3) | Partly (TBD) | NA |
| ESD | NA | X | NA | NA |

Table 4-1 : Test matrix for the FSDPU.  Q indicates a test carried out at qualification level for qualification times; A indicates a test carried out at acceptance level.  An X indicates that this test is carried out and is a characterisation type test or the level is irrelevant. NA indicates that no test will be done on this model/unit.  Instrument level Qualification

Items that will be in the Interface Drawing:

- Box dimensions and envelope.

- Mass; Moment of Inertia; Centre of Gravity		(*NA for AVM).

- Feet and connector positions..

- Flatness of the mounting surface.

- Box and connectors identification.

- Connector definition.

- Box surface treatment including ( and ( values	(*NA for AVM).

Note 1: Radiation is included in EEE component selection and S/C sector analysis.

Note 2: Tests on PCB level only.

Note 3: Meaningful EMI/EMC tests should be carried out with subsystems or subsystems simulators.

| Requirement ID | Description | Reference |
| --- | --- | --- |
| DPU-VER-01 | To carry out the tests on the FSDPU QM listed in . | IRD-VER-R02 |
| DPU-VER-02 | To carry out the tests on the FSDPU PFM listed in . | IRD-VER-R03 |
| DPU-VER-03 | To carry out the tests on the FSDPU FS listed in . | IRD-VER-R03 |

APPENDIX 1: QUALIFICATION TESTS DESCRIPTION

Vibration:	The QM DPU will be vibrated at levels appropriate to its location within the instrument, as defined in AD2.

Thermal-Vacuum

cycle:	The DPU will undergo thermal vacuum tests. The number of cycles and the temperatures are defined in AD2.

Lifetime:	NA.

Soak/cycle:	The soak test will be part of the TV test, soak times are defined in AD2.

Radiation tolerance:	All ICU components will be radiation tolerant. A suitable analysis will show that the total dose will not exceed 10 kRad end of life.

Thermal range:	The applicable thermal ranges will be reached during the TV test.

Thermal stability:	NA

Microphonics:	NA

Ionising radiation:	See radiation tolerance above.

EMI:	The sensitivity of the ICU  to electromagnetic interference will be characterised.

EMC:	The radiated and conducted electromagnetic emission of a the ICU will be characterised.

Materials conformance: All materials used in the manufacture of the ICU will be approved for space use by ESA

# Text boxes

Figure 3-2 FSDPU high level block diagram

To FSDRC

To FSDRC

FSDL

FSDL

PDU

DC/DC CONV.

REDUND.

DC/DC CONV.

MAIN

1553 I/F

Figure 3-10 FSDPU/FSDRCU Low Speed Interface protocol

Service

Module

Cryostat

Wall

ESA-supplied

Cold

Harness

FS FPU

Cold Focal Plane Unit

ESA-supplied

Spacecraft

Harness

FSHAR

Warm Interconnect Harness

FS DRC

(DRCU)

Spacecraft

3 S/S       Low Speed Serial I/F Bus

- Current mode control
(simple dynamic behaviour)

- Coupled inductor
(good AC cross regulation)

1553 I/F

REDUNDANT

MAIN

POWER SUPPLY

POWER SUPPLY

Parallel bus

S/C

p

o

w

e

r

b

u

s

S/C 1553 BUS

Parallel bus

REDUNDANT

MAIN

CPU

PL I/F

CPU

PL I/F

FSDPU

Digital

Processing

Unit

CDMS TM/TC

DC/DC

Converter

Figure 3-4 CPU Memory Organisation

PROM

Kernel Telemetry upload SW

3 S/S

High Speed Serial I/F

S/C

Program RAM

Instr. Program

From EEPROM

EEPROM

Inst. Program

Data

RAM

DPU

TSC 21020 DSP

Program

area
48 bit words

Data area
32 bit words

512 Kw
3 MB

Synchronization

signal

Secondary filter

Rectification and

Driver

Circuit

Start-up

Protection

Overcurrent

EMC Filter

28 V

5V (to CPU board)

La

TRa

TRb

3 S/S High Speed Serial I/F

S/C

Data RAM

Program RAM

Inst Program from EEPROM

EEPROM

Inst. Program

PROM

Kernel Telemetry upload SW

DPU

TSC 21020 DSP

Data area
32 bit words

Program area
48 bit words

512 Kw
2 MB

512 Kw
3 MB

170 Kw
1 MB

Figure 3-3 DC/DC Converter scheme.

5.3 Kw

(32 KB)

NOM

RED

1553B  S/C  Bus

Analog Inputs

Rx_Dat 1..3

Tx_Dat 1..3

5.4 Kw
32 KB

Data

Data

Data

Gate

1 MB

Gate

Gate

512  Kw
2 MB

Clock   1..7

Clock

Clock

Clock

8 bit-MUX

12 bit A/D

System connector

Long stub

(transformer coupled)

FIFO

memories

WR, RD, CS, IRQ, CK

Data bus

Data bus

Strobes

Data bus

BU 61582

RS422

Transceivers

3 S/S Low Speed Serial I/F Bus

FSDL3

FSDL2

LSL

FSDL1

1553 Control I/F

Parallel Bus &

Control I/F

A1280A FPGA

Figure 3-7 FSDPU/FSDRC Interface Block Diagram

High speed

data links

Serial TC and

slow data link

FS DRC

Spacecraft 28 V

Figure 3-5 CPU Board Block Diagram

FS DPU

DC/DC

Converter

Secondary

Power Distrib. Unit

Sub-system

Control Unit

Detectors Control

Electronics

Mechanisms Control

Electronics

(FTS - BSM)

Figure 3-6 Spacecraft Interface Block Diagram

Figure 3-8 High speed interface protocol

Figure 3-1 SPIRE block diagram

FPGA

State

Machinee