SPIRE ICC

User Requirements Documents

Calibration

| Written by: | S.J. Oliver |
| --- | --- |
| Comments | Marc Sauvage |

Issue 1

Monday, 18 June 2001

SPIRE ICC	1

User Requirements Documents	1

Calibration	1

1	Introduction	3

1.1	Purpose & Scope	3

1.2	Definitions of Terms and Acronyms	3

1.3	Related Documents	3

1.4	Overview	4

2	User Characteristics	4

2.1	The Calibration Scientist	4

2.1.1	Photometer Calibration Scientist	4

2.1.2	FTS Calibration Scientist	4

2.2	Interactive Analysis Developer	4

2.3	Consortium Astronomers	4

2.4	Non-Consortium Astronomers	4

3	Requirements	4

3.1	UR-CAL-001: Ultimate Accuracy Goal	4

3.2	UR-CAL-100: Calibration Files	4

UR-CAL-110: Defining Calibration Files	4

UR-CAL-120: Defining Calibration Procedures	5

UR-CAL-130: Maintaining Calibration files	5

UR-CAL-140: Improving calibration files	5

3.3	UR-CAL-200 Calibration observations & Analysis Pre-Launch	5

UR-CAL-210: Calibration plan	5

UR-CAL-220: Ground based Laboratory measurements	6

UR-CAL-230: Ground based preparatory observations	6

UR-CAL-240: Space based preparatory observations	6

UR-CAL-250: Calibration Analysis	6

3.4	UR-CAL-300: Calibration observations & Analysis Post-Launch	6

UR-CAL-310: Calibration plan	7

UR-CAL-320: SPIRE calibration observations	7

UR-CAL-330: Calibration Analysis	7

UR-CAL-340: Scientific Assessment of Calibration	7

UR-CAL-350: Repeat Observations (RD-4 2.1.1)	7

UR-CAL-360: Observation Timescales (RD-4 2.1.2)	8

UR-CAL-370: Observation Day (RD-4 2.1.3)	8

UR-CAL-380: Failed Observations (RD-4 2.1.4)	8

UR-CAL-390: Rejected Observations (RD-4 2.1.5)	8

UR-CAL-400: Removed Observations (RD-4 2.1.5)	8

# Introduction

## Purpose & Scope

Requirements put on the ICC by the need to calibrate all the astronomical data taken

by the instrument. This includes making calibration observations, producing calibration

products and preparatory calibration observations (at other telescopes). It also includes

calibration of the instrument itself.

## Definitions of Terms and Acronyms

Listing of acronyms that are “unusual” to this URD

FIRST		Far InfraRed and Submillimetre Telescope

SPIRE 	The Spectral and Photometric Imaging REceiver for FIRST

ICC		Instrument Control Centre

URD		User Requirement Document

ILT		Instrument Level Test

AVM		Avionics Model

CQM		Cryo Qualification Model

PFM		Proto-Flight Model

PV		Performance Verification

GST		Ground Segment Testing

SCUBA	Submm Common User Bolometer Array

Planck	Planck Surveyor

SOFIA	Stratospheric Observatory for Far Infrared Astronomy

SIRTF		Space InfraRed  Telescope Facility

In addition two web pages are available describing terms applicable to SPIRE

http://www.ssd.rl.ac.uk/spire/consortium/information/FIRSTacronyms.shtm

http://www.ssd.rl.ac.uk/spire/consortium/information/FIRSTdefinitions.asp

which are to be updated.

## Related Documents

RD-1		SPIRE ICC URD Scope Document

RD-2		FIRST-FSC URD

RD-3		ICC actor calibration scientist v 0.4

RD-4		SPIRE ICC URD-FSC-D2

RD-5		SPIRE ICC Calibration Files (Draft 1.0)

RD-6		SPIRE ICC Calibration Plan (Draft 1.0)

## Overview

# User Characteristics

## The Calibration Scientist

The calibration scientist has a strong astronomical background and an in-depth knowledge of the properties and operations of the instrument. She plans the necessary calibration observations to characterize the instrument, determines and verifies the calibration parameters of the instrument and specifies how these parameters have to be applied in the standard product generation. [ICC actor v0.4]

### Photometer Calibration Scientist

A calibration scientist with special responsibilities for the Photometer

### FTS Calibration Scientist

A calibration scientist with special responsibilities for the FTS

## Interactive Analysis Developer

The IA developer will need to be able to modify IA routines in response to proposed changes in calibration procedures.

## Consortium Astronomers

The calibration can only be properly assessed when applied to real scientific measurements.  Special scientific observations may require special calibration. Those involved with the calibration activity need to be closely corresponding with Astronomers, in particular Consortium Astronomers.

## Non-Consortium Astronomers

The calibration can only be properly assessed when applied to real scientific measurements.  Special scientific observations may require special calibration. Those involved with the calibration activity need to be closely corresponding with Astronomers, to a lesser extent with non-Consortium Astronomers via the FSC.

# Requirements

## UR-CAL-001: Ultimate Accuracy Goal

It is hoped that ultimately the accuracy of any reasonable scientific measurement will be limited by the statistics of the data, rather than uncertainties in the calibration.  There will be certain exceptions, e.g. very deep integrations may be limited by flat-field errors which would require an excessive amount of calibration time to accommodate.  The ultimate accuracy may not be achieved until sometime after the mission, the uppermost priority during the mission must be to ensure that all necessary calibration measurements are taken to meet the eventual goal.

- Source		here

- Importance		Essential

- Frequency		once/yearly

- Phase			PV

## UR-CAL-100: Calibration Files

### UR-CAL-110: Defining Calibration Files

The “files” (or objects or whatever) that will be required for complete calibration of instrument and scientific observations need to be defined.  The specifications of these files might be different for different observing modes, although it would be an aim to keep them as similar as possible.  It is hoped that most of necessary files will be specified at an early stage, although the contents of these files may not be known until much later).   However, as knowledge of the instrument improves it is inevitable that new calibration files will be required.   It should be possible to alter these files independently of any procedures that use them (I.e. calibration information should not be hard-wired into code).  The file specifications should describe the formats (or interfaces), the parameters that are to be included, whether errors are needed and an allowance a drift of parameters with time, unless there are good reasons to believe that these are immutable (e.g. filter numbers).   A rough draft of these files will be given in RD-5

- Source		here

SIRD-ICCF-140

- Importance		Essential

- Frequency		yearly

- Phase			AVM

### UR-CAL-120: Defining Calibration Procedures

Associated with the calibration files should be standard procedures  for applying these files (these might be IA routines or scripts).  It should be possible to modify these standard procedures independently of the content of the files themselves.  It should also be possible to test new calibration procedures within the IA. Procedures demonstrably offering improvements should be implemented, though it should always be possible to use earlier procedures.  It is the responsibility of the ICC to ensure that these procedures (and the associated files) represent the best achievable knowledge of the instrument at that time.

- Source		here

SIRD-ICCF-140

- Importance		Essential

- Frequency		monthly

- Phase			AVM

### UR-CAL-130: Maintaining Calibration files

Corrupted or missing calibration files should be replaced with very little delay.  The calibration files available at different sites should be the same, with a few minor exceptions that may be required e.g. while testing.

- Source		here

SIRD-ICCF-140

SIRD-ICCO-075

SIRD-ICCA-025

- Importance		Essential

- Frequency		daily

- Phase			AVM

### UR-CAL-140: Improving calibration files

Some calibration files will require modification as a result of instrument “drifts” or as the knowledge of the instrument improves.   It must be possible to make these changes either automatically e.g. as a result of a regular measurement or “interactively” perhaps in response to a one off measurement.  It should always be possible to use the calibration files as they would have been at any earlier epoch.

- Source		here

SIRD-ICCF-140

SIRD-ICCO-075

SIRD-ICCA-025

- Importance		Essential

- Frequency		yearly

- Phase			AVM

## UR-CAL-200 Calibration observations & Analysis Pre-Launch

### UR-CAL-210: Calibration plan

The ICC shall be responsible for producing a calibration plan.  That is a sequence of observations, measurements and analysis that are necessary to provide the data to populate all the required calibration files.  Before operations this plan needs to be updated rarely (yearly?) to account for changes in instrument knowledge or measurement/observing facilities. A rough draft of this plan will be given in RD-6

- Source		here

SIRD-ICCF-145

- Importance		Essential

- Frequency		yearly

- Phase			AVM

### UR-CAL-220: Ground based Laboratory measurements

The ICC needs to ensure that the necessary laboratory measurements of the instrument are made and that the analysis necessary to turn the laboratory data into calibration files is undertaken.

- Source		here

SIRD-ICCF-145

- Importance		Essential

- Frequency		hourly-weekly

- Phase			AVM

### UR-CAL-230: Ground based preparatory observations

The ICC needs to ensure that the necessary ground-based astronomical observations are made (or have been made) and need to undertake the analysis necessary to turn these data into calibration files.

- Source		here

SIRD-ICCF-145

- Importance		Essential

- Frequency		yearly

- Phase			AVM

### UR-CAL-240: Space based preparatory observations

The ICC needs to ensure that the necessary space-based astronomical observations are made (or have been made) and need to undertake the analysis necessary to turn these data into calibration files.

- Source		here

SIRD-ICCF-145

- Importance		Essential

- Frequency		yearly

- Phase			SIRTF (2002)/SOFIA(2002)/ASTRO-F(2004)/Planck(2007)

### UR-CAL-250: Calibration Analysis

Where astronomical or laboratory measurements exist the ICC need to perform the data reduction and analysis necessary to transform these data into calibration files.  Where these analysis are repetitive and/or laborious it may be convenient to have these analysis performed automatically.

- Source		here

- Importance		Essential

- Frequency		daily (automatic) weekly (manual)

- Phase			AVM

## UR-CAL-300: Calibration observations & Analysis Post-Launch

A number of requirements in this section come from the FSC and are described in more detail in RD-3

### UR-CAL-310: Calibration plan

The ICC shall be responsible for producing a calibration plan.  That is a sequence of observations, and analysis that are necessary to provide the data to (re)populate all the required calibration files. Under normal circumstances this plan will be updated monthly, it needs to be possible to change this plan more rapidly in response to rejected calibration observations, anomalies in the instrument or in the PV phase.

- Source		here

SIRD-ICCO-042

SIRD-ICCO-050

- Importance		Essential

- Frequency		daily/monthly

- Phase			PV/Operations

### UR-CAL-320: SPIRE calibration observations

The ICC needs to ensure that the necessary observations with SPIRE (and other FIRST instruments are and need to undertake the analysis necessary to turn these data into SPIRE calibration files.

- Source		here

SIRD-ICCO-042

SIRD-ICCO-050

- Importance		Essential

- Frequency		hourly

- Phase			PV/Operations

### UR-CAL-330: Calibration Analysis

Where astronomical or laboratory measurements exist the ICC need to perform the data reduction and analysis necessary to transform these data into calibration files.  Where these analysis are repetitive and/or laborious it may be convenient to have these analysis performed automatically.

- Source		here

SIRD-ICCF-145?

SIRD-ICCO-042

SIRD-ICCO-050

- Importance		Essential

- Frequency		daily (automatic) weekly (manual)

- Phase			AVM

### UR-CAL-340: Scientific Assessment of Calibration

The calibration activity needs to be assessed in the context of real scientific measurements. Is the calibration adequate for the main scientific goals? Is the calibration accuracy sufficient, over specified, or lacking?  Do new calibrations need to be made to address specific scientific goals?

What are the calibration priorities?

- Source		here

SIRD-ICCF-145?

SIRD-ICCO-042

SIRD-ICC0-050

- Importance		Essential

- Frequency		daily (automatic) weekly (manual)

- Phase			AVM

### UR-CAL-350: Repeat Observations (RD-4 2.1.1)

- Source 	SIRD-ICC0-050

RD-4 2.1.1

### UR-CAL-360: Observation Timescales (RD-4 2.1.2)

- Source 	SIRD-ICC0-050

RD-4 2.1.2

### UR-CAL-370: Observation Day (RD-4 2.1.3)

- Source 	SIRD-ICC0-050

RD-4 2.1.3

### UR-CAL-380: Failed Observations (RD-4 2.1.4)

- Source 	SIRD-ICC0-050

RD-4 2.1.4

### UR-CAL-390: Rejected Observations (RD-4 2.1.5)

- Source 	SIRD-ICC0-050

RD-4 2.1.5

### UR-CAL-400: Removed Observations (RD-4 2.1.5)

- Source 	SIRD-ICC0-050

RD-4 2.1.5