SUBJECT: 	THERMAL CONFIGURATION CONTROL DOCUMENT

PREPEARED BY: 	S. HEYS………………………………… 	Date:  ………………

APPROVED BY: 	J. DELDERFIELD……………………..        Date: ……………….

APPROVED BY: 	B.SWINYARD…………………………….	Date: ……………….

CHANGE RECORD

| issue | date | section | change |
| --- | --- | --- | --- |
| D1 | 03-11-00 | - | New Document |
| D2 | 22-11-00 | All Table 6.2.1 Table 6.1.3 Table 6.1.3 Table 6.2.1 Table 6.3.1 Table 6.3.3 8.5 Table 9.2 | Sections rearranged. Cone support dimensions updated JFET enclosures attached with 4 bolts not 8. L2 straps included 10K to 4K harness updated Detector harness changed from W/mm per wire to W/mm per 12ax. Cu-Au-Cu on L0 straps changed to Cu-Ap-Cu. Constant Helium Mass Flow Rate Mirror Drive OFF at 14:32 |

CONTENTS

1.	SCOPE	5

2.	APPLICABLE DOCUMENTS	5

2.1.	ESA Applicable Documents	5

2.2.	Dornier Applicable Documents	5

2.3.	RAL Applicable Documents	5

2.4.	MSSL Applicable Documents	5

2.5.	QMW Applicable Documents	6

2.6.	CEA Applicable Documents	6

2.7.	JPL Applicable Documents	6

2.8.	Miscellaneous Applicable Documents	7

3.	INTRODUCTION	8

4.	INSTRUMENT THERMAL REQUIREMENTS	9

5.	INSTRUMENT THERMAL DESIGN OVERVIEW	10

5.1.	Overview	10

5.2.	FPU 10K Stage	10

5.3.	FPU 4K Stage	10

5.4.	FPU 1.8K Stage	10

5.5.	FPU 300mK Assembly	11

5.5.1.	Detectors	11

5.5.2.	Cooler to Detector Thermal Straps	11

5.6.	Helium Cooler	11

5.7.	Mechanisms	11

6.	HEAT LOAD AND TEMPERATURE GRADIENT BUDGETS	13

6.1.	Level 2 Stage	13

6.1.1.	Level 2 Heat Load	13

6.1.2.	Level 2 Average Power Dissipation	13

6.1.3.	Level 2 Heat Sink	14

6.2.	Level 1 Stage	15

6.2.1.	Level 1 Heat Load	15

6.2.2.	Level 1 Average Power Dissipation	15

6.2.3.	Level 1 Heat Sink	16

6.3.	Level 0 Stage	17

6.3.1.	Level 0 Heat Load	17

6.3.2.	Level  0 Average Power Dissipation	18

6.3.3.	Level 0 Heat Sink	18

6.4.	300mK Stage	19

6.4.1.	300mK Heat Load	19

6.4.2.	300mK Average Power Dissipation	19

6.4.3.	300mK Heat Sink	20

6.5.	Cooler - Detectors Thermal Strap Temperature Gradients	21

6.5.1.	Photometer Strap	21

6.5.2.	Spectrometer Strap	22

6.6.	Sub-System Conductive Couplings	23

6.6.1.	Cooler Internal Conductive Couplings	23

6.6.2.	Detector Internal Conductive Couplings	24

6.6.3.	Mechanism Interface Couplings	24

7.	COMPONENT POWER DISSIPATION	25

8.	THERMAL MATHEMATICAL MODEL	26

8.1.	NODAL BREAKDOWN	26

8.1.1.	10K Enclosures	26

8.1.2.	4K FPU Structure	26

8.1.3.	Mechanisms and Calibration Sources	26

8.1.4.	Mirrors	26

8.1.5.	1.8K Enclosures	26

8.1.6.	300mK Assembly	26

8.1.7.	Detectors	26

8.1.8.	Cooler	26

8.1.9.	Straps	26

8.2.	Conductive Couplings	29

8.2.1.	Definitions	29

8.2.2.	Thermal Conductivity	29

8.2.3.	Joint Interface Conductance	29

8.3.	Radiative Couplings	29

8.4.	Heat Capacities	30

8.4.1.	Specific Heat Capacity	30

8.4.2.	Masses	30

8.5.	FIRST Interface Thermal Model	33

9.	ANALYSIS CASE DEFINITIONS	34

9.1.	Steady-State Cases	34

9.2.	Operational Mode Change – Spectrometer to Photometer	34

9.3.	Cooler Recycling	35

APPENDIX A: NODe LISTING	36

APPENDIX B: THERMAL CONDUCTIVITIES vs TEMPERATURE	40

References	46

APPENDIX C:  SPECIFIC HEAT CAPCITIES vs TEMPERTURE	48

References	50

Appendix D: Joint Contact Conductance	51

Apeizon Grease Interfaces	51

Gold Plated Interfaces	53

References	55

# SCOPE

This document describes the overall SPIRE thermal mathematical model, consisting of the FPU and its components, the JFET Boxes, and the FIRST Cryostat interface model. A breakdown of all the significant input parameters and assumptions is provided. This document should be updated regularly as the instrument design iterates. Any modifications made to the SPIRE TMM should be referenced to this document.

# APPLICABLE DOCUMENTS

## ESA Applicable Documents

| ID | Title | Number |
| --- | --- | --- |
| AD 2.1.1 | FIRST/Planck Instrument Interface Document Part B (IID-B) Instrument "SPIRE" | PT-SPIRE-02124. Issue-Rev. No. 0-4 15-MAY-00 |
| AD 2.1.2 | FIRST Simplified Optical Bench Thermal Model | Fax Ref: SCI-PT/FIN-08132 24-AUG-00 |
| AD2.1.3 | FIRST /Planck Instrument Interface Document IID-Part A | SCI-PT-IIDA-04624 Issue 1/0 01-SEPT-00 |

2.1: ESA Applicable Documents

## Dornier Applicable Documents

| ID | Title | Number |
| --- | --- | --- |
| AD 2.2.1 | FIRST Instrument I/F Study Final Report | FIRST-GR-B0000.009. Issue 1 02-FEB-00 |

Table 2.2: Dornier Applicable Documents

## RAL Applicable Documents

| ID | Title | Number |
| --- | --- | --- |
| AD 2.3.1 | SPIRE Thermal Transient Cases for Cryostat Study | SPIRE-RAL-NOT-xxx (14-DEC-99) |
| AD 2.3.2 | Change To Requirements on the Cooler and Thermal Strap | e-mail B.Swinyard 07-APR-00 |
| AD 2.3.3 | Conceptual Design For the 300mK Thermal Strap | SPIRE-RAL-MOM-xxx 25-APR-00 |
| AD 2.3.4 | SPIRE Inputs For Cryostat and Instrument Thermal Modeling | RAL 15-MAY-00 -update |
| AD 2.3.5 | SPIRE FPU TMM Specification | S.Heys 30-MAY-00 |
| AD 2.3.6 | SPIRE Radiative Heat Loads | e-mail, A.Richards, 09-JUN-00 |
| AD 2.3.7 | Change To Requirements/Spec on the Cooler and Thermal Strap | e-mail B.Swinyard 04-JUL-00 |
| AD2.3.8 | Thermal Summit QMW 25/26 Sept 00 | SPIRE-RAL-MOM-000516 |

Table 2.3: SPIRE Applicable Documents

## MSSL Applicable Documents

| ID | Title | Number |
| --- | --- | --- |
| AD 2.4.1 | PROVISIONAL SPIRE (FIRST) Interface Drawing | A1 5264 300 Issue 5 21-MAR-00 |
| AD 2.4.2 | Here It Is | e-mail B.Winter 13-JUN-00 |
| AD 2.4.3 | Structure-Optics ICD | Spire ICD 1.1/1.2 Issue 1 B.Winter 13-JUN-00 |
| AD2.4.4 | FIRST/SPIRE A Frame Analysis | e-mail B.Winter 12-JUL-00 |
| AD 2.4.5 | Thermal Conductance SP1 Analysis and 6082 Data | e-mail B.Winter 23-SEPT-00 |
| AD 2.4.6 | SPIRE Cold Strap Lengths | J.Coker 02-OCT-00 |
| AD2.4.7 | Re: SPIRE - Thermal Assumptions | e-mail B.Winter 11-OCT-00 |
| AD2.4.8 | Structure-Mass | Issue 0.11 B.Winter 14-JUN-00 |
| AD2.4.9 | Re: FPU Cone Support | e-mail B.Winter 22-NOV-00 |

Table 2.4: SPIRE MSSL Applicable Documents

## QMW Applicable Documents

| ID | Title | Number |
| --- | --- | --- |
| AD 2.5.1 | The SPIRE Instrument For FIRST | SPIRE Meeting Munich -vue graphs 29-MAR-00 |
| AD 2.5.2 | SPIRE A Bolometer Instrument For FIRST | Proposal Submitted to ESA FEB-98 |

Table 2.5: SPIRE QMW Applicable Documents

## CEA Applicable Documents

| ID | Title | Number |
| --- | --- | --- |
| AD 2.6.1 | Preliminary Comments | e-mail L.Duband 7-JUN-00 |
| AD 2.6.2 | Cryogenic Sorption Cooler – Detailed Design of Engineering Models – Test Plan | TN/SBT/SC/99-04 Iss 0 Rev 0 L.Duband 22-JUN-00 |
| AD 2.6.3 | Cryogenic Sorption Cooler –Technical Requirements for the Engineering Models and Related Preliminary Design | SBT/CT/99-02 |
| AD 2.6.4 | Cryogenic Sorption Cooler ESA Contract: 12942/98/NL/PA | Presentation 07-SEPT-00 |
| AD 2.6.5 | Straps | e-mail L.Duband 27-SEPT 00 |
| AD2.6.6 | Frigio 3 He - Ensemble | QM Drawing 29/04/99 |
| AD2.6.7 | A Thermal Switch For Use At Liquid Helium Temperatures In Space-Borne Cryogenic Systems | L.Duband Cryocoolers 8 1995 |

Table 2.6: SPIRE CEA Applicable Documents

## JPL Applicable Documents

| ID | Title | Number |
| --- | --- | --- |
| AD 2.7.1 | Array Design | SPIRE Technology Downselect Meeting JPL vue graphs 01-FEB-00 |
| AD 2.7.2 | Spire Thermal Model | e-mail T.Cafferty 13-JUN-00 |
| AD 2.7.3 | Thermal Properties | e-mail T.Cafferty 04-AUG-00 |
| AD 2.7.4 | Re:More FPU Thermal Information | e-mail T.Cafferty 12-AUG-00 |
| AD2.7.5 | FPU Thermal Properties Summary | T.Cafferty 11-JUL-00 |
| AD2.7.6 | Mass.xls | Sept-00 |

Table 2.7: SPIRE JPL Applicable Documents

## Miscellaneous Applicable Documents

| ID | Title | Number |
| --- | --- | --- |
| AD 2.8.1 | Properties of Aluminium and Aluminium Alloys | Touloukian Y.S. |
| AD 2.8.2 | Properties of Materials at Low Temperatures (Phase A). A compendium. | Johnson V.J. Pergamon 1961 |
| AD 2.8.3 | RAL Thermal Database |  |
| AD 2.8.4 | Planck TMM |  |
| AD2.8.5 | Thermal Conductance of Gold Plated Metallic Contacts At Liquid Helium Temperatures | Peter Kittel |
| AD2.8.6 | Thermal Conductance of Pressed Metallic Contacts Augmented With Indium Foil Or Apeizon Grease At Liquid Helium Temperatures | Salerno and Kittel |
| AD2.8.7 | Thermal Conductance of Augmented Pressed Metallic Contacts At Liquid Helium Temperatures | Salerno, Kittel and Spivak |

Table 2.8: Miscellaneous Applicable Documents

# INTRODUCTION

A detailed thermal mathematical model of the SPIRE instrument has been created in ESATAN v.8.4.2.  Input parameters for this model originate from various sources, as referenced in Section 2. The thermal model and all input parameters are to be maintained under configuration control, with this document and the TMM updated only as any design changes or material properties modifications are approved.

The primary aim of the TMM is to provide information on the thermal performance of the SPIRE FPU as follows:

- The steady-state temperatures of the various components within the FPU, when under nominal conditions for each mode of operation.

- Stabilisation time required after change of operating mode from Photometer to Spectrometer.

- The effect of transients (e.g. cooler recycling) on on the ultimate stability of the 300mK detector stage.

- The time required for the instrument parts to reach their nominal operating temperatures after launch.

- Provide input to thermal design through analysis of proposed design modifications.

- Provide information on FIRST interface temperatures and heat loads through incorporation of FIRST Cryostat reduced node model in SPIRE TMM.

- Hence demonstrate that SPIRE meets thermal interface requirements (max heat loads to L0, L1 and L2).

# INSTRUMENT THERMAL REQUIREMENTS

The thermal requirements of the SPIRE instrument are summarised below in Table 4.1.

| Parameter | Specification | Reference |
| --- | --- | --- |
| FPU Bulk Temperature | ~4K | - |
| Cooler Interface Temperature | ~4K | - |
| Detector Module Interface Temperature | ~1.8K | - |
| Detector temperature | T <310mK | AD 2.3.7 |
| Detector array stability | 150nK/(Hz between 0.03 and 25Hz. | - |
| Heat leak to FPU from FIRST Optical Bench | 6mW for delta T = 11-4.2 = 6.8K | AD 2.3.4 |
| Conductive heat leaks down 1.8K box supports | 1mW for delta T = 4.2 - 1.7 = 2.5K | AD 2.3.4 |
| Total heat leak down the Photometer and Spectrometer 300mK strap supports | 1.0(W | AD 2.3.3 |
| Parasitic heat leak on 300mK detector stage | <1.6(W per array <8(W total | AD 2.3.3 |
| Cooler heat lift | 10(W (at 290mK evaporator temperature) | AD 2.3.7 |
| Temperature difference between cooler cold tip and detector arrays | < 20mK | AD 2.3.7 |
| Temperature gradient along compliant links from bus bars to Cooler or detectors | 2mK/link | AD 2.3.7 |

Table 4.1: SPIRE Instrument Thermal Requirements

# INSTRUMENT THERMAL DESIGN OVERVIEW

## Overview

The SPIRE FPU and JFET Boxes are mounted off the FIRST Cryostat 10K Optical Bench, surrounded by the FIRST Instrument Shield at approximately 10K. The instrument has four temperature stages at approximately 10K, 4K, 1.8K and 300mK. Each stage is cooled via direct mounting to the FIRST Optical Bench, or thermal straps to the Cryostat Vent Pipes or LHe Tank. Stringent specifications are placed on the allowable heat loads between these stages in order to maximise mission life and to guarantee the interface temperatures as shown in Table 5.1. It is anticipated that the actual interface temperatures will be significantly lower than those shown.

| SPIRE Stage | SPIRE Components | Heat Sink | Heat Sink Temperature at SPIRE Interface | Maximum Average Heat Lift | Reference |
| --- | --- | --- | --- | --- | --- |
| 10K | JFET boxes | FIRST Optical Bench FIRST L2 Vent Pipes | <15K | 50mW | AD2.1.3 |
| 4K | SOB structure/ mechanisms / mirrors | FIRST L1 Vent Pipes | <6K | 25mW | AD2.1.3 |
| 1.8K | FPU detector boxes / dichroics / mirrors | FIRST L0 LHe Tank | <2K | 10mW | AD2.1.3 |
| 0.3K | FPU detectors / cooler thermal link | SPIRE 3He Sorption Cooler | <290mK | 10(W | AD2.3.7 |

Table 5.1: SPIRE Temperature Stages and Heat Sinks

## FPU 10K Stage

The Photometer and Spectrometer JFET chips are located in two separate enclosures. These boxes are hard mounted to the 10K FIRST Optical Bench, which acts as a heat sink for the dissipated electronics power. In addition a thermal strap to the FIRST L2 sink is attached to each enclosure. The enclosures are linked to the FIRST Shield 1 (at ~35K) via a harness.

## FPU 4K Stage

The SPIRE FPU 4K Structure consists of an Aluminium Alloy 6082 Optical Bench with the Spectrometer and Photometer Assemblies mounted on opposite sides.  Aluminium Alloy 6082 walls surround each assembly and are hard bolted to the Optical Bench. The 4K SOB is the mechanical interface for the mirrors, mechanisms and cooler. These components are hard bolted to the SOB. The key thermal design features of the 4K stage are as follows:

- FPU mounted off the 10K FOB using three stainless steel isolating mounts.

- SOB attached to the FIRST L1Vent Line (at approximately 4K) via a copper thermal strap.

- Low conductance stainless steel harness from 10K stage JFET boxes.

## FPU 1.8K Stage

The five detectors require conductive and radiative interfaces at approximately 1.8K. This is achieved by housing the detectors in enclosures mounted off the SOB and cooled to 1.8K via the L0 sink. Separate enclosures are used for the Photometer and Spectrometer detectors. The key thermal design features of these enclosures are as follows:

- Boxes mounted from the 4K SOB on three insulating stainless steel blades.

- Low conductance stainless steel harness from 4K Stage.

- Boxes cooled via a thermal strap from FIRST L0. This strap runs from the Cryostat through a light tight feed through in the FPU 4K wall to the Spectrometer 2K Box wall and then onto the Photometer 2K Box wall.

- Detectors hard mounted to enclosure walls via 1.8K flange.

## FPU 300mK Assembly

### Detectors

The detector feedhorns, bolometer arrays and filters require to be held at <310mK. The key thermal design features used to achieve this are as follows:

- 300mK stage supported off 1.8K detector flange using 3000denier Kevlar thread.

- Low conductance Kapton and Constantan harnessing between the 300mK and the 1.8K stages.

- Copper straps from detectors to cooler cold tip at 290mK.

### Cooler to Detector Thermal Straps

The Photometer and Spectrometer 300mK detector stages are coupled via two separate thermal straps to the cooler cold finger. These straps are manufactured from high purity copper and are supported on Kevlar threads from the 1.8K enclosure walls. The straps pass through light tight feedthrus at the point where they enter the 1.8K enclosure.

## Helium Cooler

- The Cooler structure is hard mounted to the FPU 4K SOB.

- Kevlar threads are used to isolate the evaporator, pump and shunt from the Cooler 4K Stage.

- The pump and evaporator are linked to the FIRST L0 sink via heat switches and copper straps.

- The pump heat switch is ON during normal operations.

- The evaporator heat switch is OFF during normal operations.

- Recycling is carried out every 48 hours and should be completed in less than 2 hours.

- During recycling the evaporator heat switch is ON and the pump heat switch is OFF. The pump is heated to 40K for approximately 1 hour before the pump heater is switched OFF and the heat switch states are reversed. The pump then cools back to 1.8K, whilst the evaporator cools to <290mK. Separate straps are therefore necessary to prevent large increases in evaporator temperature, as the hot pump is re-connected to the Cryostat after recycling.

## Mechanisms

TBD

# HEAT LOAD AND TEMPERATURE GRADIENT BUDGETS

## Level 2 Stage

### Level 2 Heat Load

| From | To | Description | XSection | Length | Material | Interface Type | Contact Area | Reference | Heat Load Budget |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| FIRST Shield 1 | Photometer JFET Box | Harness | 6.76E-6mm2 14.25E-6mm2 171E-6mm2 | 1.2m | Brass Stainless PTFE | - | - | AD2.2.1 | 2mW (TBC) |
| FIRST Shield 1 | Spectrometer JFET Box | Harness | 2.02E-6mm2 4.26E-6mm2 51.1E-6mm2 | 1.2m | Brass Stainless PTFE | - | - | AD2.2.1 | 2mW (TBC) |
| MAXIMUM AVERAGE HEAT LOAD TO SPIRE L2: | 4mW (TBC) |

### Level 2 Average Power Dissipation

| Component | Reference | Heat Load Budget |
| --- | --- | --- |
|  |  | Photometer Mode | Spectrometer Mode |
| Photometer JFET Box | AD2.3.8 | 49.5mW | 0.0mW (TBC) |
| Spectrometer JFET Box | AD2.3.8 | 0.0mW (TBC) | 14.1mW |
| MAXIMUM AVERAGE POWER DISSIPATION AT SPIRE L2: | 49.5mW (TBC) | 14.1mW (TBC) |

### Level 2 Heat Sink

| From | To | Description | XSection | Length | Material | Interface Type | Contact Area | Reference | IID-A Heat Load Budget |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Photometer JFET Enclosure | FIRST Optical Bench | Bolted | - | - | - | *Al-Al | 4 bolts | AD2.1.3 | (TBD) |
| Photometer JFET Enclosure | FIRST L2 Vent Pipes | 10K Strap | - | - | - | 0.07W/K @10K | - | * | (TBD) |
| Spectrometer JFET Enclosure | FIRST Optical Bench | Bolted | - | - | - | *Al-Al | 4 bolts | AD2.1.3 | (TBD |
| Spectrometer JFET Enclosure | FIRST L2 Vent Pipes | 10K Strap | - | - | - | 0.07W/K @10K - | - | * | (TBD) |
| MAXIMUM AVERAGE HEAT LOAD BUDGET TO FIRST L2: | 50mW |

*Assumed

## Level 1 Stage

### Level 1 Heat Load

| From | To | Description | XSection | Length | Material | Interface Type | Contact Area | Reference | Heat Load Budget |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| FIRST Optical Bench | FPU 4K Stage | Cone Foot | 2mmx2mm x 8 spokes = 32mm2 | 21mm | Stainless Steel | - | - | AD2.4.9 | 6mW (TBC) |
| FIRST Optical Bench | FPU 4K Stage | 2 A-Frame Feet | 2 x 22.5mm2 = 45mm2 | 35mm | Stainless Steel | - | - | AD2.4.4 |  |
| Photometer JFET Box | FPU 4K Stage | Harness | 58-off 12-ax cables** | 150mm | Stainless Steel | - | - | AD2.3.4 / AD2.3.8 | 0.5mW (TBC) |
| Spectrometer JFET Box | FPU 4K Stage | Harness | 17-off 12-ax cables** | 150mm | Stainless Steel | - | - | AD2.3.4 / AD2.3.8 | 0.5mW (TBC) |
| MAXIMUM AVERAGE HEAT LOAD TO SPIRE L1: | 7.0mW (TBC) |

**Heat Flow per 12ax (W/mm) = 3.1E-06 ( TH2.19-TC2.19)

### Level 1 Average Power Dissipation

| Component | Reference | Power Budget |
| --- | --- | --- |
|  |  | Photometer Mode | Spectrometer Mode |
| Photometer Calibrator | AD2.3.1 | 1.5mW | 0.0mW |
| Spectrometer Calibrator | AD2.3.1 | 0.0mW | 5.0mW |
| Beam Steering Mechanism | AD2.3.1 | 2.6mW | 0.0mW |
| Spectrometer Mirror Drive | AD2.3.1 | 0.0mW | 2.4mW |
| MAXIMUM AVERAGE POWER DISSIPATION AT SPIRE L1: | 4.1mW | 7.4mW |

### Level 1 Heat Sink

| From | To | Description | XSection | Length | Material | Interface Type | Contact Area | Reference | IID-A Heat Load Budget |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| FPU Wall | FIRST L1 Vent Pipes | 4K Strap | 20mm x 1mm = 20mm2 | 300mm | ‘ISO’ Copper | *Cu-Au-Cu (both ends) | 4.7x1.4 = 6.58cm2 | AD2.1.2 / AD2.2.1 | 25mW |
| MAXIMUM AVERAGE HEAT LOAD BUDGET TO FIRST L1: | 25mW |

*Assumed

## Level 0 Stage

### Level 0 Heat Load

| From | To | Description | XSection | Length | Material | Interface Type | Contact Area | Reference | Heat Load Budget |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 4K SOB | 2K Box Strap | 4K Feedthru | 8 threads x 0.3mm2 | 20mm | Kevlar 49 Thread | - | - | AD2.4.7 | 0.020mW |
| 4K SOB | Cooler Evaporator Strap | 4K Feedthru | 8 threads x 0.3mm2 | 20mm | Kevlar 49 Thread | - | - | AD2.4.7 | 0.020mW |
| 4K SOB | Cooler Pump Strap | 4K Feedthru | 8 threads x 0.3mm2 | 20mm | Kevlar 49 Thread | - | - | AD2.4.7 | 0.020mW |
| 4K SOB | Phot. 2K Box | 3 Blade Supports | 3 x 10mm2 = 30mm2 | 30mm | Stainless Steel | - | - | AD2.3.4 | 0.600mW |
| 4K SOB | Spec. 2K Box | 3 Blade Supports | 3 x 10mm2 = 30mm2 | 30mm | Stainless Steel | - | - | AD2.3.4 | 0.400mW |
| 4K SOB | Phot. LW Detector 1.8K | Detector Harness | **9-off 12-ax cables | 80mm | Stainless Steel | - | - | AD2.7.4 | 0.100mW |
| 4K SOB | Phot. MW Detector 1.8K | Detector Harness | **19-off 12-ax cables | 80mm | Stainless Steel | - | - | AD2.3.8 / AD2.7.4 |  |
| 4K SOB | Phot. SW Detector 1.8K | Detector Harness | **30-off 12-ax cables | 80mm | Stainless Steel | - | - | AD2.3.8 / AD2.7.4 |  |
| 4K SOB | Spec. LW Detector 1.8K | Detector Harness | **7-off 12-ax cables | 80mm | Stainless Steel | - | - | AD2.3.8 / AD2.7.4 |  |
| 4K SOB | Spec. SW Detector 1.8K | Detector Harness | **11-off 12-ax cables | 80mm | Stainless Steel | - | - | AD2.3.8 / AD2.7.4 |  |
| 4K Cooler | 1.8K Cooler | Cooler Heat Leaks |  |  |  |  |  |  | 0.150mW (TBC) |
| MAXIMUM AVERAGE HEAT LOAD TO SPIRE L0: | 1.310mW (TBC) |

**Heat Flow per 12ax (W/mm) = 3.1E-06 ( TH2.19-TC2.19)

### Level  0 Average Power Dissipation

| Component | Reference | Power Budget |
| --- | --- | --- |
| Cooler Heat Switch |  | 0.2mW |
| Cooler Pump Heater |  | 200mW for 30mins every 48 hours = 2.08mW 25mW for 30mins every 48 hours = 0.26mW |
| MAXIMUM AVERAGE POWER DISSIPATION AT SPIRE L0: | 2.54mW (TBC) |

### Level 0 Heat Sink

| From | To | Description | XSection | Length | Material | Interface Type | Contact Area | Reference | IID-A Heat Load Budget |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| FPU 4K Feedthru | FIRST L0 | 1.8K Enclosures Strap | 20mm x 1mm = 20mm2 | *350mm | UHP Copper | *Cu-Ap-Cu (both ends) | 4.7x1.4 = 6.58cm2 | AD2.2.1 | 5mW |
| FPU 4K Feedthru | FIRST L0 | Cooler Pump Strap | 20mm x 1mm = 20mm2 | *350mm | UHP Copper | *Cu-Ap-Cu (both ends) | 4.7x1.4 = 6.58cm2 | AD2.2.1/AD2.6.5 | 5mW |
| FPU 4K Feedthru | FIRST L0 | Cooler Evaporator Strap | 20mm x 2mm = 40mm2 | *350mm | UHP Copper | *Cu-Ap-Cu (both ends) | 4.7x1.4 = 6.58cm2 | AD2.2.1/AD2.6.5 |  |
| MAXIMUM AVERAGE HEAT LOAD BUDGET TO FIRST L0: | 10mW |

## 300mK Stage

### 300mK Heat Load

| From | To | Description | XSection | Length | Material | Interface Type | Contact Area | Reference | Heat Load Budget |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1.8K Box | 300mK Phot. Busbar | Busbar Support | 2 threads x 0.3mm2 x 4 attachment points = 2.4mm2 | 20mm | Kevlar 49 Thread | - | - | AD2.4.7 | 0.50(W (TBC) |
| 1.8K Box | 300mK Phot. Feedthru | 2K Feedthru Support | 8 threads x 0.015mm2 = 1.2mm2 | 20mm | Kevlar 49 Thread | - | - | AD2.4.7 | 0.25(W (TBC) |
| 1.8K Box | 300mK Spec. Feedthru | 2K Feedthru Support | 8 threads x 0.015mm2 = 1.2mm2 | 20mm | Kevlar 49 Thread | - | - | AD2.4.7 | 0.25(W (TBC) |
| 1.8K Detector | 300mK Detector | 5 Detector Supports | 5 x 16 threads x 0.3mm2 = 24mm2 | 25mm | Kevlar 49 Thread | - | - | AD2.7.2 | 4.0(W |
| 1.8K Detectors | 300mK Detectors | Harness | 14mm2 0.275mm2 | 30mm | Kapton Constantan | - | - | AD2.7.4 | 4.0(W |
| MAXIMUM AVERAGE HEAT LOAD TO SPIRE 300mK STAGE | 9.0(W (TBC) |

### 300mK Average Power Dissipation

| Component | Reference | Power Budget |
| --- | --- | --- |
| Temperature Control Heaters | * | 1.0(W (TBC) |
| MAXIMUM AVERAGE POWER DISSIPATION AT SPIRE 300mK STAGE | 1.0(W (TBC) |

*Assumption

### 300mK Heat Sink

| From | To | Description | XSection | Length | Material | Interface Type | Contact Area | Reference | Heat Load Budget |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 300mK Assembly | Cooler Cold Tip | See Tables 6.5.1 and 6.5.2 for breakdown of 300mK Thermal Strap Couplings | 10(W |
| MAXIMUM HEAT LOAD BUDGET TO SPIRE 3HeCOOLER | 10(W |

## Cooler - Detectors Thermal Strap Temperature Gradients

### Photometer Strap

| From | To | Description | XSection | Length | Material | Interface Type | Contact Area | Reference | Max Temperature Drop |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Cover | Feedhorn | Contact Interface | - | - | - | In-Ap-In | 0.4 cm2 | AD2.7.4 | 3.0mK |
| Feedhorn | 300mK Flange | Internal Strap | Diameter 1mm = 0.78mm2 | 60mm | UHP Copper | Cu-ap-In | 2.7 cm2 | AD2.7.4 | 3.0mK |
| LW Flange MW Flange SW Flange | Busbar | Detector Strap | Diameter 2.5mm = 4.91mm2 | 60mm 113mm 53mm | UHP Copper | *Cu-Ap-Cu | 2(R x 0.6 = 0.47cm2 | AD2.4.5 / AD2.7.4 | 2.5mK |
| Phot. Busbar | Phot. Feedthru | Busbar | Diameter 3mm = 12.57mm2 | 288mm | UHP Copper | *Cu-Ap-Cu | 2(R x 0.6 = 0.57cm2 | AD2.4.5 | 3.5mK |
| Phot. Feedthru | Phot. Feedthru Flange | 2K Box Feedthru | Diameter 5mm = 12.57mm2 | 50mm | UHP Copper | *Cu-Ap-Cu | *1cm2 | AD2.4.5 | 3.0mK |
| Phot. Feedthru Flange | Cooler Evaporator | Cooler Strap | Diameter 2mm = 3.14mm2 | 130mm | UHP Copper | *Cu-Ap-Cu | *1cm2 | AD2.4.5 / AD2.3.3 | 5.0mK |
| MAXIMUM TEMPERATURE DROP FROM COOLER TO DETECTOR | 20mK |

### Spectrometer Strap

| From | To | Description | XSection | Length | Material | Interface Type | Contact Area | Reference | Max Temperature Drop |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Cover | Feedhorn | Contact Interface | - | - | - | In-Ap-In | 0.4 cm2 | AD2.7.4 | 3.0mK |
| Feedhorn | 300mK Flange | Internal Strap | Diameter 1mm = 0.78mm2 | 60mm | UHP Copper | Cu-ap-In | 2.7 cm2 | AD2.7.4 | 3.0mK |
| LW Flange SW Flange | Busbar | Detector Strap | Diameter 2.5mm = 4.91mm2 | 54mm 54mm | UHP Copper | *Cu-Ap-Cu | 1cm2 | AD2.4.5 / AD2.7.4 | 1.0mK |
| Spec. Feedthru | Spec. Feedthru Flange | 2K Box Feedthru | Diameter 5mm = 12.57mm2 | 40mm | UHP Copper | *Cu-Ap-Cu | *1cm2 | AD2.4.5 | 1.5mK |
| Spec. Feedthru Flange | Cooler Evaporator | Cooler Strap | Diameter 2mm = 3.14mm2 | 210mm | UHP Copper | *Cu-Ap-Cu | *1cm2 | AD2.4.5 / AD2.3.3 | 3.5mK |
| MAXIMUM TEMPERATURE DROP FROM COOLER TO DETECTOR | 12mK |

*Assumption

## Sub-System Conductive Couplings

### Cooler Internal Conductive Couplings

| From | To | Description | XSection | Length | Material | Interface Type | Contact Area | Reference |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 4K Flange | Pump | Kevlar Supports | 2.4mm2 | 27mm | Kevlar Thread | - | - | * |
| 4K Flange | Evaporator | Kevlar Supports | 2.4mm2 | 54mm | Kevlar Thread | - | - | AD2.6.2 |
| Pump | Shunt | Pipe | OD = 10.4mm ID = 10mm | 45mm | Ti6Al4V | - | - | AD2.6.2 |
| Shunt | Evaporator | Pipe | OD = 10.4mm ID = 10mm | 110mm | Ti6Al4V | - | - | AD2.6.2 |
| 4K Flange | Pump HS | HS Support | OD = 7.2mm ID = 7.0mm | 50mm | Ti6Al4V | - | - | AD2.6.2 |
| 4K Flange | Evaporator HS | HS Support | OD = 7.2mm ID = 7.0mm | 50mm | Ti6Al4V | - | - | AD2.6.2 |
| Evaporator HS | Shunt | Strap | 10mm2 | 50mm | Cu | Cu-Ap-Cu | 2cm2 | * |
| Evaporator | Evaporator HS | HS ON HS OFF | -- | - | - | 3mW/K 0.28(W/K | - | AD2.6.2 |
| Pump | Pump HS | HS ON HS OFF | - | - | - | 16mW/K 6(W/K | - | AD2.6.2 |

*Assumption

### Detector Internal Conductive Couplings

| From | To | Description | XSection | Length | Material | Interface Type | Contact Area | Reference |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2K Flange | Top Ring | Kevlar Supports | 8 threads x 0.3 cm2 = 2.4 mm2 | 25mm | Kevlar 49 Thread | - | - | AD2.7.2 |
| 2K Flange | Bottom Ring | Kevlar Supports | 8 threads x 0.3 cm2 = 2.4 mm2 | 25mm | Kevlar 49 Thread | - | - | AD2.7.2 |
| Top Ring | Spacer | Spacer | 33mm2 | 15.25mm | Invar | In-Ap-In | 0.66cm2 | AD2.7.4 |
| Bottom Ring | Spacer | Spacer | 33mm2 | 15.25mm | Invar | In-Ap-In | 0.66cm2 | AD2.7.4 |
| Bottom Ring | Cover |  | - | - | - | In-Ap-In | 5.7 cm2 | AD2.7.4 |
| Feedhorn | Cover |  | - | - | - | In-Ap-In | 0.4 cm2 | AD2.7.4 |
| Feedhorn | Strap Flange | Internal Strap | 1mm dia | 60mm | UHP Copper | Cu-Ap-In | 2.7 cm2 | AD2.7.4 |
| Top Ring | Strap Flange | - | - | - | - | Cu-Ap-In | 1 cm2 | AD2.7.4 |

*Assumption

### Mechanism Interface Couplings

| From | To | Description | XSection | Length | Material | Interface Type | Contact Area | Reference |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Spectrometer Calibrator | 4K Optical Bench | Mounting | - | - | - | Al-Au-Al | 4 x1cm2 | * |
| Photometer Calibrator | 4K Optical Bench | Mounting | - | - | - | Al-Au-Al | 4 x1cm2 | * |
| Spectrometer Mechansim | 4K Optical Bench | Mounting | - | - | - | Al-Au-Al | 4 x1cm2 | * |
| Photometer Beam Steering Mechanism | 4K Optical Bench | Mounting | - | - | - | Al-Au-Al | 4 x1cm2 | * |

*Assumption

# COMPONENT POWER DISSIPATION

The power dissipations for the various components are given in Table 7.1 below.

| Component | Peak Power (mW) | Mean Power (mW) | Comments | Reference |
| --- | --- | --- | --- | --- |
| Photometer Cold Read-Out Electronics | 49.5 | 49.5 | ON constantly in Photometer Mode | AD2.3.8 |
| Spectrometer Cold Read-Out Electronics | 14.1 | 14.1 | ON constantly in Spectrometer Mode | AD2.3.8 |
| Cooler Pump Heat Switch | 0.2 | 0.2 | On constantly when cooler ON | AD2.3.8 |
| Cooler Heater | 200 25 | 200 25 | ON during cooler recycling: 0mins- 30mins 30mins-60mins | AD2.3.8 |
| Photometer Calibrator | 2.0* | 1.5** | ON for 10 minute intervals during Photometer Mode. | *AD2.3.1 |
| Spectrometer Calibrator | 5.0 | 5.0 | ON in Spectrometer Mode | AD2.3.1 |
| Beam Steering Mechanism | 4.0* | 2.6** | ON in Photometer Mode | *AD2.3.1 |
| Spectrometer Mirror Drive | 6.5 | 2.4 | ON (cycling) during Spectrometer Mode (see Figure 11) | AD2.3.1 |

**Values calculated to give total steady-state powers as stated in AD2.3.4

Table 7.1: Component Power Dissipation

Figure 7.1: Spectrometer Mode Power Dissipation (5mW calibration source + mirror drive power)

# THERMAL MATHEMATICAL MODEL

## NODAL BREAKDOWN

The SPIRE thermal model consists of 138 diffuse nodes representing the SPIRE FPU, a single diffuse node for each of the two JFET Boxes, a single boundary node to represent the Cooler Cold Tip and four boundary nodes to represent the FIRST Cryostat. A full nodal breakdown of the TMM can be found in Appendix A.

### 10K Enclosures

The two JFET boxes are each represented by single diffuse nodes, hard mounted to the FIRST Optical Bench. The harnesses between the JFET boxes and the Spacecraft are sunk to the FIRST Shield 1 temperature. Straps to the FIRST L2 sink have an assumed conductance of 0.07W/K at 10K.

### 4K FPU Structure

The FPU structure is discretised along all axes in order to show temperature gradients through the instrument. A total of 10 nodes are used to represent the walls of the Spectrometer and Photometer and 16 nodes for the Optical Bench.

The FPU structure is mounted from the FIRST Optical Bench node on a single cone foot and two A-frame feet. Due to the non-uniform cross sectional area of the Cone Foot and the variation in conductivity across the foot with temperature, the cone is discretised into 10 nodes to improve the accuracy of the TMM. The A-Frames have a constant cross section and are therefore modelled as a simple conductive coupling between the FIRST Optical Bench and the FPU.

### Mechanisms and Calibration Sources

The mechanisms and calibration sources are modelled very simply, due to lack of detailed information on their design. A single node is used to represent each component, with an associated power dissipation and heat capacity. The components are assumed to be hard mounted to the structure with gold coated aluminium to aluminium interfaces. The conductance across this interface is varied according to temperature.

### Mirrors

Each mirror is modelled as a single node with an associated heat capacity. The mirrors are hard mounted to the structure via gold-coated aluminium to aluminium interfaces. The conductances across these interfaces are varied according to temperature.

### 1.8K Enclosures

The photometer and spectrometer 1.8K enclosure walls are discretised into 3 nodes and 2 nodes respectively. Baffles and mirrors within the boxes are modelled as separate nodes, as are the detectors.

### 300mK Assembly

The photometer and spectrometer thermal links from the cooler cold tip to the detector 300mK stages are modelled in order to show the critical temperature drops along these link. Figure 6.6 shows the nodal breakdown of the complete 300mK system.

### Detectors

The detector model is a simplified version of the reduced node detector model provided by JPL (AD2.7.2). Each detector is discretised into 7 nodes as shown in Figure 6.6.

### Cooler

The Cooler model is based on the nodal breakdown provided by L.Duband (AD2.6.1). A total of 6 nodes are used to represent the cooler as shown in Figure 6.6.

### Straps

Straps to the L0,L1 and L2 sinks are modelled as shown in Figures 6.9.1 to 6.9.4.

Figure 8.1.6: 300mK System Nodal Breakdown

Figure 8.1.9.1: L1 Strap Node Breakdown

Figure 8.1.9.2:L0 2K Box Strap Node Breakdown

Figure 8.1.9.3: L0 Cooler Pump Strap Node Breakdown

Figure 8.1.9.4: L0 Cooler Evaporator Strap Node Breakdown

## Conductive Couplings

### Definitions

The assumptions used for the definition of all critical conductive couplings are given in Section 7.

### Thermal Conductivity

The thermal conductivity vs temperature relationships assumed for the various materials are given in Appendix B. The integrated thermal conductivity is used in couplings linking components at different temperature stages, in order that changes in conductivity with temperature are accounted for in the analysis.

The most critical conductivity value is for copper, since changes in purity and application can significantly alter the conductivity. Two grades of copper are therefore assumed:

-‘Ultra High Purity Copper’ for the L0 straps, the 300mK links and the detector internals. This material exhibits a conductivity of 767W/mK at 2K. This is in close agreement with the value of 800W/mK at 2K given in AD2.2.1 for the L0 strap copper.

-A lower purity copper is assumed for the L1 straps. The material used has a conductivity of 138W/mK at 2K, which is in close agreement with the value of 140W/mK given in AD2.2.1 for the L0 strap copper.

These values will be updated following conductivity tests on the actual copper grade and configurations specified in the final design.

### Joint Interface Conductance

All significant joint interface conductances are accounted for in the TMM. The conductance values assumed are varied with temperature and are dependant on the materials being joined and on the interface. All critical interfaces in the 300mK Assembly are assumed to have interface conductances similar to that shown in Appendix D for Apeizon Grease interfaces. This is also the assumption for the L0 Straps. All other joints are assumed to have conductances similar to those shown for gold coated surfaces.

## Radiative Couplings

Radiative couplings between the SPIRE instrument’s external walls and the FIRST Cryostat are calculated by hand. The assumed emissivities and view factors are given in Table 8.3 below. Internal radiative loads have been shown to be insignificant due to the low temperatures involved.

| Surface i | Surface j | Emissivity i | Emissivity j | View Factor | Reference |
| --- | --- | --- | --- | --- | --- |
| FPU external side walls | FIRST Instrument Shield | 0.10 | 0.10 | *0.5 | AD2.3.4 |
| FPU external side walls | FIRST Optical Bench | 0.10 | 0.10 | *0.5 | AD2.3.4 |
| FPU external base | FIRST Instrument Shield | 0.10 | 0.10 | *0.0 | AD2.3.4 |
| FPU external base | FIRST Optical Bench | 0.10 | 0.10 | *1.0 | AD2.3.4 |
| JFET Boxes | FIRST Optical Bench | 0.10 | 0.10 | *0.5 | AD2.3.4 |
| JFET Boxes | FIRST Instrument Shield | 0.10 | 0.10 | *0.5 | AD2.3.4 |

##### *Approximation

##### Table 8.3: Radiative Exchange Coupling Parameters

## Heat Capacities

### Specific Heat Capacity

The assumed specific heat capacity vs temperature relationships for the various materials used within the TMM are shown in Appendix C.

### Masses

The masses assumed for all SPIRE components are shown in Table 8.4.2. Nodes representing the FIRST ITMM have boundary nodes with zero associated thermal mass. Their rate of change of temperature is restricted within the TMM as described in Section 8.5.

| Sub-System | Component | Temp (K) | No. Off | Mass (kg) | Material | Reference |
| --- | --- | --- | --- | --- | --- | --- |
| 4K Structure | Optical Bench | 4 | 1 | 7.102 | Al 6082 | AD2.4.8 |
| 4K Structure Photometer Cover | back panel | 4 | 1 | 0.539 | Al 6082 | AD2.4.8 |
|  | base plate | 4 | 1 | 1.229 | Al 6082 | AD2.4.8 |
|  | front panel | 4 | 1 | 0.709 | Al 6082 | AD2.4.8 |
|  | top cover | 4 | 1 | 0.787 | Al 6082 | AD2.4.8 |
|  | top rear cove | 4 | 1 | 0.434 | Al 6082 | AD2.4.8 |
|  | outer panel | 4 | 1 | 3.597 | Al 6082 | AD2.4.8 |
| 4K Structure Spectrometer Cover | back panel | 4 | 1 | 0.407 | Al 6082 | AD2.4.8 |
|  | base plate | 4 | 1 | 1.000 | Al 6082 | AD2.4.8 |
|  | front panel | 4 | 1 | 0.577 | Al 6082 | AD2.4.8 |
|  | top cover | 4 | 1 | 0.638 | Al 6082 | AD2.4.8 |
|  | top rear cover | 4 | 1 | 0.409 | Al 6082 | AD2.4.8 |
|  | outer panel | 4 | 1 | 3.184 | Al 6082 | AD2.4.8 |
| 4K Structure Mounting | A-frame | 4 | 2 | 0.115 | Al 6082 | AD2.4.4 |
|  | Cone | 4 | 1 | 0.150 | Al 6082 | Assumption |
| 4K Structure Photometer mounts and clamps | CM3, CM5, CM7 – mount | 4 | 1 | 0.650 | Al 6082 | AD2.4.8 |
|  | PM6, SM6 – mount | 4 | 1 | 0.120 | Al 6082 | AD2.4.8 |
|  | PM9 – mount | 2 | 1 | 0.010 | Al 6082 | AD2.4.8 |
|  | PM10 – mount | 2 | 1 | 0.010 | Al 6082 | AD2.4.8 |
|  | PM11 –mount | 2 | 1 | 0.010 | Al 6082 | AD2.4.8 |
|  | dichroic clamp + mount | 2 | 2 | 0.100 | Al 6082 | AD2.4.8 |
| 4K Structure Spectrometer mounts and clamps | beam splitter mount + clamp | 4 | 2 | 0.100 | Al 6082 | AD2.4.8 |
|  | SM7 – mount | 4 | 1 | 0.115 | Al 6082 | AD2.4.8 |
|  | SM8/11 –mount | 4 | 4 | 0.096 | Al 6082 | AD2.4.8 |
|  | SM9/10 – mount | 4 | 2 | 0.144 | Al 6082 | AD2.4.8 |
|  | SM12 –mount | 2 | 2 | 0.010 | Al 6082 | AD2.4.8 |
| 4K Structure Bulkhead/mirror mounts/baffles | M6 bulkhead/baffle | 4 | 1 | 0.352 | Al 6082 | AD2.4.8 |
|  | PM8 bulkhead/baffle | 4 | 1 | 0.212 | Al 6082 | AD2.4.8 |
|  | intermediate bulkhead/baffle | 4 | 1 | 0.105 | Al 6082 | AD2.4.8 |
|  | lower bulkhead/baffle | 4 | 1 | 0.180 | Al 6082 | AD2.4.8 |
|  | entry baffle | 4 | 1 | 0.500 | Al 6082 | AD2.4.8 |
| Mirrors Photometer | CM3 |  | 1 | 0.183 | Al 6082 | AD2.4.3 |
|  | CM5 |  | 1 | 0.360 | Al 6082 | AD2.4.3 |
|  | PM6 |  | 1 | 0.027 | Al 6082 | AD2.4.3 |
|  | PM7 |  | 1 | 0.300 | Al 6082 | AD2.4.3 |
|  | PM8 |  | 1 | 0.056 | Al 6082 | AD2.4.3 |
|  | PM9 |  | 1 | 0.223 | Al 6082 | AD2.4.3 |
|  | PM10 |  | 1 | 0.065 | Al 6082 | AD2.4.3 |
|  | PM11 |  | 1 | 0.060 | Al 6082 | AD2.4.3 |
| Mirrors Spectrometer | SM6 |  | 1 | 0.029 | Al 6082 | AD2.4.3 |
|  | SM7 |  | 1 | 0.044 | Al 6082 | AD2.4.3 |
|  | SM8 |  | 2 | 0.056 | Al 6082 | AD2.4.3 |
|  | SM9 |  | 2 | 0.037 | Al 6082 | AD2.4.3 |
|  | SM10 |  | 2 | 0.056 | Al 6082 | AD2.4.3 |
|  | SM11 |  | 2 | 0.097 | Al 6082 | AD2.4.3 |
|  | SM12 |  | 2 | 0.025 | Al 6082 | AD2.4.3 |
| Mechanisms | Beam Steering Mechanism | 4 | 1 | 1.000 | Aluminium | Assumed |
|  | Spectrometer Mechanism | 4 | 1 | 0.500 | Aluminium | Assumed |
| Calibration Sources | Photometer | 4 | 1 | 0.100 | Aluminium | Assumed |
|  | Spectrometer | 4 | 1 | 0.500 | Aluminium | Assumed |
| 2K Structure | 2K Photometer Box | 2 | 1 | 1.575 | Al 6082 | AD2.4.8 |
|  | 2K Spectrometer Box | 2 | 1 | 1.096 | Al 6082 | AD2.4.8 |
| Detectors Common | 2K Structure | 2 | 5 5 5 5 | 0.044 0.038 0.064 0.016 | Al St. Steel Invar Silicon | AD2.7.6 |
|  | Top Ring | 0.3 | 5 | 0.049 | Invar | AD2.7.6 |
|  | Spacer | 0.3 | 5 | 0.0184 | Invar | AD2.7.6 |
|  | Bottom Ring | 0.3 | 5 | 0.029 | Invar | AD2.7.6 |
| Detectors Photometer LW | Detector Cover | 0.3 | 1 | 0.031 | Invar | AD2.7.6 |
|  | Detector Strap | 0.3 | 1 | 0.007 | Copper | AD2.7.6 |
|  | Feedhorn | 0.3 | 1 | 0.314 | Copper | AD2.7.6 |
| Detectors Photometer MW | Detector Cover | 0.3 | 1 | 0.058 | Invar | AD2.7.6 |
|  | Detector Strap | 0.3 | 1 | 0.005 | Copper | AD2.7.6 |
|  | Feedhorn | 0.3 | 1 | 0.247 | Copper | AD2.7.6 |
| Detectors Photometer SW | Detector Cover | 0.3 | 1 | 0.058 | Invar | AD2.7.6 |
|  | Detector Strap | 0.3 | 1 | 0.005 | Copper | AD2.7.6 |
|  | Feedhorn | 0.3 | 1 | 0.190 | Copper | AD2.7.6 |
| Detectors Spectrometer LW | Detector Cover | 0.3 | 1 | 0.031 | Invar | AD2.7.6 |
|  | Detector Strap | 0.3 | 1 | 0.007 | Copper | AD2.7.6 |
|  | Feedhorn | 0.3 | 1 | 0.165 | Copper | AD2.7.6 |
| Detectors Spectrometer SW | Detector Cover | 0.3 | 1 | 0.058 | Invar | AD2.7.6 |
|  | Detector Strap | 0.3 | 1 | 0.005 | Copper | AD2.7.6 |
|  | Feedhorn | 0.3 | 1 | 0.118 | Copper | AD2.7.6 |
| Cooler | 4K Structure | 4 | 1 | 0.151 | Titanium | AD2.6.6 |
|  | Pump | 2 | 1 | 0.254 | Titanium | AD2.6.6 |
|  | Shunt | 2 | 1 | 0.0085 | Stainless Steel | AD2.6.6 |
|  | Evaporator | 0.3 | 1 | 0.236 | Titanium | AD2.6.6 |
|  | Pump Heat Switch | 2 | 1 | 0.050 | Titanium | AD2.6.7 |
|  | Evaporator heat Switch | 2 | 1 | 0.050 | Titanium | AD2.6.7 |
| 300mK Link | Photometer Busbar | 0.3 | 1 | 0.018 | Copper | calculated |
|  | Photometer 2K Feedthru | 0.3 | 1 | 0.009 | Copper | calculated |
|  | Spectrometer 2K Feedthru | 0.3 | 1 | 0.007 | Copper | calculated |
| JFET Boxes | Photometer | 10 | 1 | 1.250 | Aluminium | AD2.1.6 |
|  | Spectrometer | 10 | 1 | 1.250 | Aluminium | AD2.1.6 |
| Straps | L1 | 4 | 1 | 0.054 | Copper | calculated |
|  | L0 – 2K Box | 2 | 1 | 0.104 | Copper | calculated |
|  | L0-Pump | 2 | 1 | 0.083 | Copper | calculated |
|  | L0-Evaporator | 2 | 1 | 0.187 | Copper | calculated |

Table 8.4.2: SPIRE - Assumed Mass Breakdown

## FIRST Interface Thermal Model

The FIRST interface nodes (L0, L1 and L2 sinks, FOB, FIRST Instrument Shield  and FIRST Shield 1) are set as boundary nodes, whose temperatures are varied according to the SPIRE loads. The functions which are used to calculate these interface temperatures are as given in AD2.1.2.

During transient analysis the rates of change of these boundary temperatures are restricted to prevent model instability, since the FIRST ITMM itself has no inherent thermal mass. This rate restriction is achieved by maintaining a constant Helium mass flow rate (as stated in AD2.1.3) and restricting the rate of change of boundary temperatures, as shown in Table 8.5.

| Parameter | Max Rate of Change |
| --- | --- |
| Helium Mass Flow Rate | 0 mg/s |
| FIRST Shield 1 Temperature | 0.1 K/s |
| L2 (Optical Bench) Temperature | 0.1 K/s |
| L1 (Vent Pipe)Temperature | 0.1 K/s |
| L0 (LHe Tank) Temperature | 1.7K - constant |
| FIRST Instrument Shield | 10K - constant |

Table 8.5: FIRST Cryostat Parameter Rate of Change Restrictions

# ANALYSIS CASE DEFINITIONS

## Steady-State Cases

| Component | Node No. | POWER (mW) | Reference |
| --- | --- | --- | --- |
|  |  | Photometer Operation | Spectrometer Operation |  |
| Photometer Cold Read-Out Electronics | 5000 | 49.5 | 0.0 | AD2.3.8 |
| Spectrometer Cold Read-Out Electronics | 5500 | 0.0 | 14.1 | AD2.3.8 |
| TOTAL L2 (JFET) Dissipation | - | 49.5 | 14.1 | - |
| Cooler Pump Heat Switch (mean) | 4400 | 0.2 | 0.2 | AD2.3.8 |
| Cooler Heater | 4200 | 0.0 | 0.0 | - |
| Photometer Calibrator | 2090 | 1.5 | 0.0 | *AD2.3.1 / AD2.3.4 |
| Spectrometer Calibrator | 3250 | 0.0 | 5.0 | AD2.3.1 |
| Beam Steering Mechanism | 2100 | 2.6 | 0.0 | *AD2.3.1 / AD2.3.4 |
| Spectrometer Mirror Drive | 3200 | 0.0 | 2.4 | AD2.3.1 |
| TOTAL L1 (FPU) Dissipation | - | 4.3 | 7.6 | - |

Table 9.1: Steady-State Case Definition

## Operational Mode Change – Spectrometer to Photometer

Analysis is performed to predict the time taken for the FPU temperature to stabilise after a change in the mode of operation.

| Time (mm:ss) | Sub-System | Node No. | Status | Power Dissipation (mW) |
| --- | --- | --- | --- | --- |
| 00:00 | Ph. Cold Read-Out Electronics | 5000 | ON | 49.5 |
| 00:01 | Photometer Calibrator | 2090 | ON | 2.0 |
| 10:00 | Photometer Calibrator | 2090 | OFF | 0.0 |
| 10:01 | Ph. Cold Read-Out Electronics | 5000 | OFF | 0.0 |
| 10:01 | Sp. Cold Read Out Electronics | 5500 | ON | 14.1 |
| 10:02 | Spectrometer Calibrator | 3250 | ON (stabilising) | 5.0 |
| 10:32 | Spectrometer Calibrator | 3250 | ON | 5.0 |
| 10:32 | Mirror Drive | 3200 | ON(scanning) | 2.4 |
| 14:32 | Mirror Drive | 3200 | OFF | 0.0 |
| 14:32 | Spectrometer Calibrator | 3250 | ON* | 5.0 |

Status and Powers: ref. AD2.3.1

*Spectrometer remains ON: ref. AD2.3.8

Table 9.2: Operational Mode Change Case Definition

## Cooler Recycling

Analysis is performed to predict the level of disturbance caused to FPU temperatures during Cooler Recycling, and the time taken to stabilise after re-cycling.

During this analysis the Cooler Cold Tip is changed from a diffuse to a boundary node as recycling starts. After 1 hour, when Cryopumping starts, the cooler is converted to a boundary node, whose temperature is reduced at a constant rate to 0.3K. The cooling rate assumed is based on cooler test results given in AD2.6.4.

| Time (h:mm:ss) | Sub-System | Node No. | Status | Power (mW) | Reference |
| --- | --- | --- | --- | --- | --- |
| 0:00:00 | Ph. Cold Read-Out Electronics | 5000 | OFF | 0 | AD2.3.1 |
| 0:00:00 | Mechanisms / Calibrators | - | OFF | 0 | AD2.3.1 |
| 0:00:00 | Cooler | 4300 | OFF | 0 | AD2.3.1 |
| 0:00:01 | Cooler Evap HS Cooler Pump HS | 4500 4400 | ON OFF | 0.2 0 | AD2.3.1 |
| 0:00:02 | Cooler Heater | 4200 | ON | 200 | AD2.3.8 |
| 0:25:00 | Cooler Heater | 4200 | ON | 25 | AD2.3.8 |
| 0:55:00 | Cooler Heater | 4200 | OFF | 0 | AD2.3.8 |
| 0:55:01 | Cooler Evap HS Cooler Pump HS | 4500 4200 | OFF ON | 0 0.2 | AD2.3.1 |
| 0:55:02 to 1:30:00 | Cooler / Detectors | 4300 | Cryopumping to 290mK @ constant rate | 0 | AD2.6.4 |
| 1:30:00 | Ph. Cold Read Out Electronics | 5000 | ON | 49.5 | AD2.3.1 |
| 1:40:00 | Photometer Calibrator | 2090 | ON | 2 | AD2.3.1 |
| 1:42:00 | Photometer Calibrator | 2090 | OFF | 0 | AD2.3.1 |
| 1:42:01 | Beam Steering Mechanism | 2100 | ON | 4 | AD2.3.1 |
| 2:12:00 | Beam Steering Mechanism | 2100 | OFF | 0 | AD2.3.1 |

###### Table 9.3: Cooler Recycling Case Definition

# APPENDIX A: NODe LISTING

| Node No. | Node Name | Node Type | Temperature Stage (K) | Material |
| --- | --- | --- | --- | --- |
| CONE FOOT |  |  |  |
| 1 | spire_cone_foot1 | D | 10 | Stainless Steel |
| 2 | spire_cone_foot2 | D | 0 | Stainless Steel |
| 3 | spire_cone_foot3 | D | 0 | Stainless Steel |
| 4 | spire_cone_foot4 | D | 0 | Stainless Steel |
| 5 | spire_cone_foot5 | D | 0 | Stainless Steel |
| 6 | spire_cone_foot6 | D | 0 | Stainless Steel |
| 7 | spire_cone_foot7 | D | 0 | Stainless Steel |
| 8 | spire_cone_foot8 | D | 0 | Stainless Steel |
| 9 | spire_cone_foot9 | D | 0 | Stainless Steel |
| 10 | spire_cone_foot10 | D | 4 | Stainless Steel |
| FPU OPTICAL BENCH |  |  |  |
| 1000 | spire_4k_optical_bench | D | 4 | Aluminium Alloy 6082 |
| 1010 | spire_4k_optical_bench | D | 4 | Aluminium Alloy 6082 |
| 1020 | spire_4k_optical_bench | D | 4 | Aluminium Alloy 6082 |
| 1030 | spire_4k_optical_bench | D | 4 | Aluminium Alloy 6082 |
| 1100 | spire_4k_optical_bench | D | 4 | Aluminium Alloy 6082 |
| 1110 | spire_4k_optical_bench | D | 4 | Aluminium Alloy 6082 |
| 1120 | spire_4k_optical_bench | D | 4 | Aluminium Alloy 6082 |
| 1130 | spire_4k_optical_bench | D | 4 | Aluminium Alloy 6082 |
| 1200 | spire_4k_optical_bench | D | 4 | Aluminium Alloy 6082 |
| 1210 | spire_4k_optical_bench | D | 4 | Aluminium Alloy 6082 |
| 1220 | spire_4k_optical_bench | D | 4 | Aluminium Alloy 6082 |
| 1230 | spire_4k_optical_bench | D | 4 | Aluminium Alloy 6082 |
| 1300 | spire_4k_optical_bench | D | 4 | Aluminium Alloy 6082 |
| 1310 | spire_4k_optical_bench | D | 4 | Aluminium Alloy 6082 |
| 1320 | spire_4k_optical_bench | D | 4 | Aluminium Alloy 6082 |
| 1330 | spire_4k_optical_bench | D | 4 | Aluminium Alloy 6082 |
| FPU 4K WALLS |  |  |  |
| 1500 | spire_4k_spect_base | D | 4 | Aluminium Alloy 6082 |
| 1510 | spire_4k_spect_top | D | 4 | Aluminium Alloy 6082 |
| 1520 | spire_4k_spect_+z | D | 4 | Aluminium Alloy 6082 |
| 1530 | spire_4k_spect_-z | D | 4 | Aluminium Alloy 6082 |
| 1540 | spire_4k_spect_+y | D | 4 | Aluminium Alloy 6082 |
| 1600 | spire_4k_photo_base | D | 4 | Aluminium Alloy 6082 |
| 1610 | spire_4k_photo_top | D | 4 | Aluminium Alloy 6082 |
| 1620 | spire_4k_photo_+z | D | 4 | Aluminium Alloy 6082 |
| 1630 | spire_4k_photo_-z | D | 4 | Aluminium Alloy 6082 |
| 1640 | spire_4k_photo_+y | D | 4 | Aluminium Alloy 6082 |
| 1700 | spire_4k_connector panel | D | 4 | Aluminium Alloy 6082 |
| 1800 | spire_4k_aperture_filter | D | 4 | - |
| PHOTOMETER 4K STAGE |  |  |  |
| 2000 | photo_3_mirror_mount | D | 4 | Aluminium Alloy 6082 |
| 2030 | photo_mirror3 | D | 4 | Aluminium Alloy 6082 |
| 2040 | photo_mirror4 | D | 4 | Aluminium Alloy 6082 |
| 2050 | photo_mirror5 | D | 4 | Aluminium Alloy 6082 |
| 2060 | photo_mirror6 | D | 4 | Aluminium Alloy 6082 |
| 2070 | photo_mirror7 | D | 4 | Aluminium Alloy 6082 |
| 2080 | photo_mirror8 | D | 4 | Aluminium Alloy 6082 |
| 2090 | photo_calibrator | D | 4 | Aluminium Alloy 6082 |
| 2100 | photo_beam_steering_ mechanism | D | 4 | Aluminium Alloy 6082 |
| 2150 | photo_4K_baffle | D | 4 | Aluminium Alloy 6082 |
| 2160 | photo_4K_baffle | D | 4 | Aluminium Alloy 6082 |
| 2170 | photo_4K_baffle | D | 4 | Aluminium Alloy 6082 |
| 2180 | photo_4K_baffle | D | 4 | Aluminium Alloy 6082 |
| PHOTOMETER 2K STAGE |  |  |  |
| 2400 | photo_2k_box_px | D | 2 | Aluminium Alloy 6082 |
| 2410 | photo_2k_box_mid | D | 2 | Aluminium Alloy 6082 |
| 2420 | photo_2k_box_mx | D | 2 | Aluminium Alloy 6082 |
| 2450 | photo_2k_baffle | D | 2 | Aluminium Alloy 6082 |
| 2500 | photo_2k_dichroic1 | D | 2 | Aluminium Alloy 6082 |
| 2510 | photo_2k_dichroic2 | D | 2 | Aluminium Alloy 6082 |
| 2520 | photo2k__mirror9 | D | 2 | Aluminium Alloy 6082 |
| 2530 | photo2k__mirror10 | D | 2 | Aluminium Alloy 6082 |
| 2540 | photo2k__mirror11 | D | 2 | Aluminium Alloy 6082 |
| PHOTOMETER 0.3K COLD LINK |  |  |  |
| 2600 | cooler_photo_strap | D | 0.3 | Copper (UHP) |
| 2620 | photo_spect_strap | D | 0.3 | Copper (UHP) |
| 2650 | photo_300mK_busbar_cold | D | 0.3 | Copper (UHP) |
| 2655 | photo_300mK_busbar | D | 0.3 | Copper (UHP) |
| 2660 | photo_300mK_busbar | D | 0.3 | Copper (UHP) |
| 2665 | photo_300mK_busbar | D | 0.3 | Copper (UHP) |
| 2670 | photo_300mK_busbar_warm | D | 0.3 | Copper (UHP) |
| PHOTOMETER DETECTORS |  |  |  |
| 2700 | photo_detector1_2k | D | 2 | Aluminium Alloy 6082 |
| 2710 | photo_detector1_strap | D | 0.3 | Copper (UHP) |
| 2720 | photo_detector1_top_ring | D | 0.3 | Invar |
| 2730 | photo_detector1_spacers | D | 0.3 | Invar |
| 2740 | photo_detector1_bot_ring | D | 0.3 | Invar |
| 2750 | photo_detector1_cover | D | 0.3 | Invar |
| 2770 | feedhorn1 | D | 0.3 | Copper |
| 2800 | photo_detector2_2k | D | 2 | Aluminium Alloy 6082 |
| 2810 | photo_detector2_strap | D | 0.3 | Copper (UHP) |
| 2820 | photo_detector2_top_ring | D | 0.3 | Invar |
| 2830 | photo_detector2_spacers | D | 0.3 | Invar |
| 2840 | photo_detector2_bot_ring | D | 0.3 | Invar |
| 2850 | photo_detector2_cover | D | 0.3 | Invar |
| 2870 | photo_feedhorn2 | D | 0.3 | Copper |
| 2900 | photo_detector3_2k | D | 2 | Aluminium Alloy 6082 |
| 2910 | photo_detector3_strap | D | 0.3 | Copper (UHP) |
| 2920 | photo_detector3_top_ring | D | 0.3 | Invar |
| 2930 | photo_detector3_spacers | D | 0.3 | Invar |
| 2940 | photo_detector3_bot_ring | D | 0.3 | Invar |
| 2950 | photo_detector3_cover | D | 0.3 | Invar |
| 2970 | photo_feedhorn3 | D | 0.3 | Copper |
| SPECTROMETER 4K STAGE |  |  |  |
| 3000 | spect_input_fold_mirrorA | D | 4 | Aluminium Alloy 6082 |
| 3010 | spect_collimatorA | D | 4 | Aluminium Alloy 6082 |
| 3020 | spect_collimatorB | D | 4 | Aluminium Alloy 6082 |
| 3030 | spect_beam_divider1 | D | 4 | Aluminium Alloy 6082 |
| 3040 | spect_fold_mirror1A | D | 4 | Aluminium Alloy 6082 |
| 3050 | spect_fold_mirror2A | D | 4 | Aluminium Alloy 6082 |
| 3060 | spect_fold_mirror1B | D | 4 | Aluminium Alloy 6082 |
| 3070 | spect_fold_mirror2B | D | 4 | Aluminium Alloy 6082 |
| 3080 | spect_rooftop_mirrorA | D | 4 | Aluminium Alloy 6082 |
| 3090 | spect_rooftop_mirrorB | D | 4 | Aluminium Alloy 6082 |
| 3100 | spect_beam_divider2 | D | 4 | Aluminium Alloy 6082 |
| 3110 | spect_camera_mirrorA | D | 4 | Aluminium Alloy 6082 |
| 3120 | spect_camera_mirrorB | D | 4 | Aluminium Alloy 6082 |
| 3200 | spect_mirror_mechanism | D | 4 | Aluminium Alloy 6082 |
| 3250 | spect_calibrator | D | 4 | Aluminium Alloy 6082 |
| SPECTROMETER 2K STAGE |  |  |  |
| 3400 | spect_2k_box_px | D | 2 | Aluminium Alloy 6082 |
| 3410 | spect_2k_box_mx | D | 2 | Aluminium Alloy 6082 |
| 3450 | spect_2k_baffle | D | 2 | Aluminium Alloy 6082 |
| 3460 | spect_mirror12A | D | 2 | Aluminium Alloy 6082 |
| 3470 | spect_mirror12B | D | 2 | Aluminium Alloy 6082 |
| SPECTROMETER 0.3K COLD LINK |  |  |  |
| 3650 | spect_300mK_busbar_cold | D | 0.3 | Copper (UHP) |
| 3655 | spect_300mK_busbar | D | 0.3 | Copper (UHP) |
| 3660 | spect_300mK_busbar | D | 0.3 | Copper (UHP) |
| 3665 | spect_300mK_busbar_warm | D | 0.3 | Copper (UHP) |
| SPECTROMETER DETECTORS |  |  |  |
| 3700 | spect_detector1_2k | D | 2 | Aluminium Alloy 6082 |
| 3710 | spect_detector1_strap | D | 0.3 | Copper (UHP) |
| 3720 | spect_detector1_top_ring | D | 0.3 | Invar |
| 3730 | spect_detector1_spacers | D | 0.3 | Invar |
| 3740 | spect_detector1_bot_ring | D | 0.3 | Invar |
| 3750 | spect_detector1_cover | D | 0.3 | Invar |
| 3770 | spect_feedhorn1 | D | 0.3 | Copper |
| 3800 | spect_detector2_2k | D | 2 | Aluminium Alloy 6082 |
| 3810 | spect_detector2_strap | D | 0.3 | Copper (UHP) |
| 3820 | spect_detector2_top_ring | D | 0.3 | Invar |
| 3830 | spect_detector2_spacers | D | 0.3 | Invar |
| 3840 | spect_detector2_bot_ring | D | 0.3 | Invar |
| 3850 | spect_detector2_cover | D | 0.3 | Invar |
| 3870 | spect_feedhorn1 | D | 0.3 | Copper |
| COOLER |  |  |  |
| 4000 | cooler_4k_structure | D | 4 | Aluminium Alloy 6082 |
| 4200 | cooler_2K_pump | D | 4 | Ti6Al4V |
| 4250 | cooler_shunt | D | 2 | Ti6Al4V |
| 4300 | cooler_300mK_evap | B | 0 | Ti6Al4V |
| 4400 | cooler_pump_HS | D | 4 | Ti6Al4V |
| 4500 | cooler_evap_HS | D | 2 | Ti6Al4V |
| JFET BOX |  |  |  |
| 5000 | photometer_JFET_box | D | 10 | Aluminium Alloy 6082 |
| 5500 | spectrometer_JFET_box | D | 10 | Aluminium Alloy 6082 |
| STRAPS TO FIRST CRYOSTAT |  |  |  |
| 6000 | L1_strap_main_structure | D | 4 | Copper (UHP) |
| 6100 | L0_strap_2k_boxes | D | 2 | Copper (UHP) |
| 6200 | L0_strap_cooler_pump | D | 2 | Copper (UHP) |
| 6300 | L0_strap_cooler_evap | D | 2 | Copper (UHP) |
| FIRST CRYOSTAT |  |  |  |
| 10000 | first_10k_optical_bench | B | 10 | - |
| 20000 | first_L0_helium_tank | B | 1.7 | - |
| 21000 | first_L1_cooling_pipes | B | 4 | - |
| 22000 | first_instrument_shield | B | 10 | - |
| 23000 | first_shield1 | B | 34 | - |

# APPENDIX B: THERMAL CONDUCTIVITIES vs TEMPERATURE

## References

| Material Name | Reference |
| --- | --- |
| Aluminium Alloy 6082 | AD2.4.5 |
| UHP Copper | AD2.7.5 |
| Copper | AD2.8.4 |
| Kevlar 49 Thread | AD2.7.2 / AD2.7.5 |
| Invar | AD2.7.5 |
| Kapton | AD2.7.5 |
| Constantan | AD2.7.5 |
| Manganin | AD2.8.4 |
| Brass | AD2.8.4 |
| Stainless Steel 304 | AD2.8.4 |
| Titanium Alloy Ti6Al4V | AD2.8.3 |
| PTFE | AD2.8.4 |

Table B.1: Thermal Conductivity References

# APPENDIX C:  SPECIFIC HEAT CAPCITIES vs TEMPERTURE

## References

| Material Name | Reference |
| --- | --- |
| Aluminium | AD2.8.1 |
| Copper | AD2.7.5 |
| Invar | AD2.7.5 |
| Titanium | AD2.8.2 |
| Stainless Steel | AD2.8.2 |

Table C1: Specific Heat Capacity References

# Appendix D: Joint Contact Conductance

## Apeizon Grease Interfaces

## Gold Plated Interfaces

## References

| Interface Name | Description | Assumed Contact Force | Reference |
| --- | --- | --- | --- |
| Cu-Ap-Cu | Uncoated Copper - Apeizon - Uncoated Copper | 670N | AD2.8.6 |
| Cu-Ap-In | Uncoated Copper – Apeizon - Uncoated Invar | 670N | *AD2.8.6 |
| In-Ap-In | Uncoated Indium – Apeizon - Uncoated Invar | 670N | *AD2.8.6 |
| Al-Ap-Al | Uncoated Aluminium – Apeizon - Uncoated Aluminium | 670N | AD2.8.6 |
| Cu-Au-Cu | Gold Plated Copper - Gold Plated Copper | 670N | AD2.8.5 |
| Al-Au-Al | Gold Plated Aluminium – Gold Plated Aluminium | 670N | AD2.8.5 |
| Al-Al | Aluminium-Aluminium | 670N | AD2.8.5 |

*Assumed that Invar behaves as Stainless Steel.

Table C1: Joint Interface Conductances

# Text boxes

Pump Heat Switch

4400

0.K

Photometer

Detector

Spectrometer

SW detector

2910

0.K

MW detector

2810

0.K

photometer 2K box

1.K

busbar feedthru

2650

0.K

busbar

2660

0.K

busbar

2670

0.K

busbar

2655

0.K

bottom ring

2740

0.K

busbar

2665

0.K

strap flange

2600

0.K

strap flange

3600

0.K

busbar feedthru

3650

0.K

spectrometer

2K box

1.K

SW detector

3810

0.K

LW detector

3710

0.K

LW Detector

Strap Flange

2710

0.K

FPU 4K Wall

FIRST L0 LHe Tank

20000

spacers

2730

0.K

1.8K structure

2700

1.K

top ring

2720

0.K

feedhorn

2770

0.K

detector

2760

0. K

cover plate

2750

0.K

FIRST L0 LHe Tank

20000

strap flange

6300

FPU 4K Wall

Evaporator Heat Switch

4500

Photometer Box

2400

Spectrometer Box

3410

strap flange

6000

FIRST L0 LHe Tank

20000

FPU 4K Wall

Cooler Pump Heat Switch

4400

strap flange

6200

FIRST L1 LHe Vent Pipes

21000

strap flange

6000

FPU 4K Wall

Cooler

FPU

4K

Structure

4.K

Shunt

4250

0.K

Evap Heat Switch

4500

0.K

Evaporator

4300

0.K

Evap L0 Strap

6300

0.K

Pump L0 Strap

6200

0.K

Pump

4200

0.K