Section 10: Appendix 11

Compliance & Outstanding issues

## Contents

2.1	Contents	1

2.2	General	1

2.3	Compliance matrix	2

2.4	Known Issues	6

## General

At the release date of this document (20.Jul.01) the following issues are known. Any remaining issues not resolved by the DDR date (30.Jul.01) will be folded together with DDR raised issues and appropriate design changes made.

The design will be placed under configuration control on 31.Jul.01 and all changes thereafter will be raised as discussed in the Product Assurance plan (Engineering Change Requests and CTD'S)

## Compliance matrix

The current design status is compared to the requirements (RD 5). A simple yes/TBC/TBD approach is taken at this stage to indicate whether the design is currently shown to meet the requirements. Where data from single-axis tests is relevant it has been noted. Two axis prototype and development model tests will complete the bulk of the table over the following 1-4 months.

| Requirement | Met by baseline design | Design description reference | Supporting test data | Notes |
| --- | --- | --- | --- | --- |
| Angular Travel - Chop Axis | Yes | Drawing SPIRE-BSM-020-001 |  | By design - no fouls at max travel |
| Angular Travel - Jiggle Axis | Yes | Drawing SPIRE-BSM-020-001 |  | By design - no fouls at max travel |
| Minimum Step Size | TBC | Not covered |  | By design - limit will in digitization & noise |
| Chop Frequency | Yes | 10.5.1, 7.2.2.3 | partial | Power dissipation modeled at specified frequency. 1-AP chops OK at 2 Hz sine and square wave. |
| Jiggle Frequency | Yes | 10.5.1, 7.2.2.3 |  | Power dissipation modeled at specified frequency. |
| Holding position | Yes | 10.5.3 | see appendix 9 |  |
| Stability | Yes | 10.5.3 | see appendix 9 |  |
| Position Measurement | TBC | 10.5.3 (partial) | see appendix 9 |  |
| Settling Time | Yes | 10.5.2 | see appendix 9 |  |
| Chop repeatability | TBC | Not covered |  | Hysterisis, backlash etc need to be considered |
| Mechanical Dimensions | Yes | Mech ICD | partial | 2 axis prototype does not have baffle |
| Operating Temperature | Yes | 8.1.2 | Single axis : see appendix 8 | Cooldown data supports modelling. Mechanism functions cold |
| Thermal Isolation | Yes | 8.1.2, 8.1.3 | Single axis : see appendix 8 | Cooldown data supports modelling. Mechanism functions cold |
| Cold Power Dissipation | Yes | 10.5.1 | TBC | Tests in hand on 1-AP |
| Warm Electronics Power Dissipation | TBD | N/A | N/A | LAM |
| Mirror Surface Dimensions | Yes | SPIRE-BSM-020-004-001 | Yes | 2 axis prototype mirror is correct size |
| Mirror Surface Finish | Yes | 9.2 |  |  |
| Mirror Surface Reflectivity | Yes | 9.2 |  |  |
| Mirror Surface Emissivity | N/A | N/A |  |  |
| Baffle | TBC | 9.3 |  | Beam profile currently has minor foul from motor & sensor (see 7.3.1, Fig 14) |
| Position of Rotation Axes | Yes | Drawing SPIRE-BSM-020-001 |  | Assembly jig designs required |
| Orthogonality of Rotation Axes | Yes | Drawing SPIRE-BSM-020-001 |  | Assembly jig designs required |
| Fail Safe (No Drive Signal) Position | Yes | 13.2, Drawing SPIRE-BSM-020-001 |  | Assembly jig designs required |
| Fail Safe (Mechanical Failure) Position | Yes | 7.2.4.2-4 |  |  |
| Mass | Yes | 8.5 |  |  |
| Cool-down time | Yes | 8.1.2, 8.1.3 | Single axis : see appendix 8 | Cooldown data supports modelling. Mechanism functions cold |
| Reliability | Yes | 11 |  | Non-quantitative spec |
| Failure Modes | Yes | 11 |  |  |
| Operational Safety | Yes | N/A |  | ATC safety risk assessment performed |
| Lifetime | Yes | 7.2.4.1 (flex pivots) |  | Motors & sensor life TBC, but as PACS, ISOPhot |
| Operating modes | Yes | 10.8.2, 10.8.3 |  |  |
| Jiggle Mode | Yes | 10.8.2, 10.8.3 |  |  |
| Chopping Mode | Yes | 10.8.2, 10.8.3 |  |  |
| Scan mapping | Yes | 10.8.2, 10.8.3 |  |  |
| Stare or 'holding' mode | Yes | 10.8.2, 10.8.3 |  |  |
| Combinations of Modes | Yes | 10.8.2, 10.8.3 |  |  |
| Data Outputs | TBC | 10.6.1 (overview only) |  | Spec is TBC with LAM |
| Data Inputs | TBC | 10.6.1 (overview only) |  | Spec is TBC with LAM |
| Exported vibration | Yes | 7.3.7 |  |  |
| Stray Magnetic fields | TBC | 8.1.4 |  | No externally imposed spec |
| Electro-Magnetic Compatibility | TBC | 8.1.4, 10.6.7 |  | No externally imposed spec |
| ICD's | Yes | 12 |  |  |
| Design requirements | Yes | AD3, 13.1 |  | PA Plan - configuration control etc |
| Electronics Card Format | Yes | Not covered |  |  |
| Mirror Flatness (optical alignment) | Yes | 9.2 |  |  |
| Mirror Reflectivity (optical alignment) | Yes | 9.2 |  |  |
| Cleanliness | Yes | AD3, 13.1 |  |  |
| Material selection | Yes | 7.4.4, AD3 |  |  |
| Storage | Yes | 13.5 |  |  |
| Shock | N/A | N/A |  | No shock spec. |
| Quasi Static Loads | Yes | 7.1, 7.2.4.1, 7.3.2 |  |  |
| Sine Vibration | Yes | 7.1, 7.2.4.1, 7.3.2 |  |  |
| Random Vibration | TBC | 7.1, 7.2.4.1, 7.3.2 |  | Margins lower than ideal |
| Vacuum Level | Yes | Not covered | partial | Lab book notes, material choice |
| Vacuum Outgassing | Yes | Not covered |  | Covered by material selection |
| Temperature | Yes | 8.1.2, 8.1.3 | Single axis : see appendix 8 | Cooldown data supports modelling. Mechanism functions cold |
| Magnetic Fields | TBC | TBC |  | No externally imposed spec |
| Survival Temperature | TBC | Not covered |  | Magnets limited to 80 deg C |
| Radiation environment | TBC | Not covered |  | Infineon sensor requires rating. LAM to rate BSMe |

## Known Issues

| ID | Issue | Plan to resolve |
| --- | --- | --- |
|  | Motor corners clip the 20% oversize optical beam | Chamfer corners and shields - work in hand as at 20.Jul.01 |
|  | Chop sensor assembly edge clip the 20% oversize optical beam | Chamfer corners, move sensor back slightly |
|  | Chop sensor is G10 and emisivity/cooling needs to be modelled | Consider material change. |
|  | Baffle design is TBC | Liaise with RAL, Confirm before IBDR |
|  | Random vibration regime remains a challenge | Liaise with MSSL. DM vibration test |
|  | Jiggle flex pivots inconel survivability data needs updating in discussions with TRW | Resolve with TRW |
|  | Harness cut-outs and securing to the BSM structure interface need to be determined | Mock up harness on 2 axis prototype and make design changes |
|  | Harness layout to be optimized to allow overlay of prime on redundant. |  |
|  | MPIA motor space envelope is TBC after Zeiss optimization | Liaise with MPIA/Zeiss |
|  | Parts list needs update after LAM finalize MCU parts list | Liaise with LAM. Update at SMEC/MCU DDR |
|  | Warm electronics do not have baseline motor coil damping |  |
|  | Minimum step size & position measurement need more depth in design description | work in hand as at 20.Jul.01 |
|  | Model damping due to redundant motors, and evaluate need for cross-switching | Liaise with LAM, MPIA |
|  | Plan & cost qualification of Infineon position sensors | Update by IBDR |
|  | Flex pivot costing requires programmatic solution | Solve by IBDR |
|  | Model harness & RF Filters for cross-talk & EMC |  |
|  | Show how connections are made to motors, particularly if aluminium wires are specified by Zeiss | Liaise with MPIA/Zeiss |
|  | EMC not specified - stray magnetic fields etc | Measure BSM magnetic fields and communicate to systems team. |
|  | Data I/O has TBC's | Liaise with LAM. Update at SMEC/MCU DDR |
|  | Warm power dissipation is TBD | Liaise with LAM. Update at MCU DDR |
|  | Bake out temperature is TBC | Perform bake out tests on 2 axis prototype |
|  | Hysterisis, backlash etc need to be considered | Analyze before IBDR |
|  | Chatter & impact on end-stops | Consider compliant end stops, possibly as part of motor design |
|  | Cryo-Harness mechanical layout is not included in ATC drawing pack | Incorporate backshells & cable harness in ICD to structure – ensure avoidance of optical beams |
|  | No detailed design for flexible wiring to chop axis position sensors | Outline design before IBDR |
|  | Drawing pack is incomplete | Complete by IBDR. |