# Section 10

Appendix 3B:  Structural Interface FEA Results

# Scope

This document records a Finite Element Analysis performed on the SPIRE Beam Steering Mirror structure component,

# Model

## Design

The model is based on Pro/Engineer drawing number BSM-02-001-001 dated Rev 1 (WIP) 29.May.01.

## FEA representation

The FEA was performed as a solid model in integrated Pro/Mechanica. Multi-pass adaptive meshing was used, with convergence set at 10%. Small fillets and holes were generally suppressed, with the exception of connector pin and base mounting features. Material was assigned as Aluminium 6082

## Software

- Pro/Engineer 2000i2

- Pro/MECHANICA STRUCTURE Version 22.3(305) (integrated mode)

# Results

## 50 G acceleration load case

### Deflection results

Maximum displacement is predicted at 43 microns under this load case, with prime deflections occuring in a twisting mode (from the side loading) and a pistoning mode around the front mounting hole (from vertical and fore-aft loads).

Figure 1 : displacement results (millimetres)

### Von Mises Stress results

stresses peak at 36 MPa.

Permissible is per BS8118 (IP's design log no 9, p57)

For fatigue with FoS of 1.0

- 67 MPa friction grip bolted zones (not strictly applicable here as loads are not construction level friction grip)

- 96MPa for re-entrant features

- 76MPa small holes (dia < 3t)

For parent plate

240 MPa with suggested load factor of 2.5, ie a target of 96 MPa in this case

# Figure 2 stress distribution around connector  cut out and mounting feet

Figure 3  stress distribution around rear mounting foot

### Analysis report (extracts)

------------------------------------------------------------

Pro/MECHANICA STRUCTURE Version 22.3(305)

Summary for Design Study "static_50g"

Mon Jun 04, 2001   19:10:01

------------------------------------------------------------

No errors were found in the model.

Pro/MECHANICA STRUCTURE Model Summary

Principal System of Units: millimeter Newton Second (mmNs)

Length:          mm

Force:           N

Time:            sec

Temperature:     C

Model Type: Three Dimensional

Points:       1146

Edges:        5435

Faces:        7465

Springs:         0

Masses:          0

Beams:           0

Shells:          0

Solids:       3189

Elements:     3189

------------------------------------------------------------

Standard Design Study

Description:

50G loads applied in x,y,z

Static Analysis "static_50g":

Convergence Method: Multiple-Pass Adaptive

Plotting Grid:      4

>> Pass  1 <<

Total Number of Equations:    3330

Maximum Edge Order:              1

Elements Not Converged:       3189

Edges Not Converged:          5435

Local Disp/Energy Index:    100.0%

Global RMS Stress Index:    100.0%

>> Pass  2 <<

Total Number of Equations:   19418

Maximum Edge Order:              2

Elements Not Converged:       1956

Edges Not Converged:          4627

Local Disp/Energy Index:    100.0%

Global RMS Stress Index:     84.8%

>> Pass  3 <<

Total Number of Equations:   63723

Maximum Edge Order:              4

Elements Not Converged:       1639

Edges Not Converged:          2628

Local Disp/Energy Index:    100.0%

Global RMS Stress Index:     80.9%

>> Pass  4 <<

Total Number of Equations:  117789

Maximum Edge Order:              5

Elements Not Converged:        815

Edges Not Converged:           207

Local Disp/Energy Index:    100.0%

Global RMS Stress Index:     36.4%

>> Pass  5 <<

Total Number of Equations:  174100

Maximum Edge Order:              6

Elements Not Converged:        146

Edges Not Converged:             0

Local Disp/Energy Index:     54.9%

Global RMS Stress Index:     13.1%

>> Pass  6 <<

Total Number of Equations:  199893

Maximum Edge Order:              6

Elements Not Converged:         22

Edges Not Converged:             0

Local Disp/Energy Index:     30.1%

Global RMS Stress Index:     12.0%

RMS Stress Error Estimates:

Load Set          Stress Error  % of Max Prin Str

----------------  ------------  -----------------

LoadSet1           4.56e-01       1.3% of  3.63e+01

** Warning: Convergence was not obtained because the maximum

polynomial order of 6 was reached.

The analysis did not converge to within 10% on

edge displacement and element strain energy.

Total Mass of Model:  2.943847e-04

Mass Moments of Inertia about WCS Origin:

Ixx:  1.41233e+00

Ixy: -2.35807e-01  Iyy:  3.84633e-01

Ixz: -4.52996e-03  Iyz:  1.01220e-03  Izz:  1.29888e+00

Principal MMOI and Principal Axes Relative to WCS Origin:

Max Prin           Mid Prin           Min Prin

1.46399e+00        1.29874e+00        3.33110e-01

WCS X:  9.76566e-01        2.74581e-02        2.13461e-01

WCS Y: -2.13377e-01       -5.97632e-03        9.76952e-01

WCS Z: -2.81010e-02        9.99605e-01       -2.26723e-05

Center of Mass Location Relative to WCS Origin:

( 1.02862e+01,  4.89316e+01, -5.38177e-02)

Mass Moments of Inertia about the Center of Mass:

Ixx:  7.07486e-01

Ixy: -8.76379e-02  Iyy:  3.53484e-01

Ixz: -4.69293e-03  Iyz:  2.36968e-04  Izz:  5.62882e-01

Principal MMOI and Principal Axes Relative to COM:

Max Prin           Mid Prin           Min Prin

7.28123e-01        5.62755e-01        3.32974e-01

WCS X:  9.73328e-01        2.64026e-02        2.27892e-01

WCS Y: -2.27705e-01       -9.92492e-03        9.73680e-01

WCS Z: -2.79695e-02        9.99602e-01        3.64820e-03

Constraint Set: ConstraintSet1

Load Set: LoadSet1

Resultant Load on Model:

in global X direction:  1.451317e+02

in global Y direction:  1.451317e+02

in global Z direction:  1.451317e+02

Measures:

Name              Value      Convergence

--------------     -------------  -----------

max_disp_mag:       4.301418e-02      0.8%

max_disp_x:         3.048651e-02      0.8%

max_disp_y:        -1.805561e-02      0.9%

max_disp_z:         2.839908e-02      0.8%

max_prin_mag:       3.626618e+01      3.8%

max_stress_prin:    3.626618e+01      3.8%

max_stress_vm:      3.586344e+01      0.2%

max_stress_xx:      2.019206e+01     15.5%

max_stress_xy:      1.101872e+01     15.7%

max_stress_xz:      7.227989e+00      0.5%

max_stress_yy:      3.609924e+01      2.9%

max_stress_yz:     -7.932948e+00      0.6%

max_stress_zz:     -1.609714e+01      0.5%

min_stress_prin:   -3.532419e+01      1.2%

strain_energy:      9.345811e-01      0.6%

### Verification

##### Reaction loads

- need checking

##### Manual verification

##### - required,

## Modal Analysis

### Modal Analysis Results

To limit run time, the maximum number of modes to sweep for was set to 12. The results were:

Mode   Frequency

1  	6.881738e+02

2  	8.638142e+02

3  	1.780816e+03

4  	2.715497e+03

5  	3.058290e+03

6 	 	3.283797e+03

7		  3.344646e+03

8  	3.614443e+03

9  	3.957047e+03

10 	 4.096691e+03

11  	4.676689e+03

12  	5.185199e+03

Figure 4 First resonant mode, twisting of entire structure, 688 Hz

Figure 5 mode 2 , 864Hz. Piston and twist of whole structure

Figure 6 Mode 3 , 1780- Hz, rocking forward of whole structure

Figure 7 Mode 4, 2716 Hz, local resonance of plates

### Model report (extracts)

------------------------------------------------------------

Pro/MECHANICA STRUCTURE Version 22.3(305)

Summary for Design Study "modal"

Tue Jun 05, 2001   08:32:47

------------------------------------------------------------

No errors were found in the model.

Pro/MECHANICA STRUCTURE Model Summary

Principal System of Units: millimeter Newton Second (mmNs)

Length:          mm

Force:           N

Time:            sec

Temperature:     C

Model Type: Three Dimensional

Points:       1146

Edges:        5435

Faces:        7465

Springs:         0

Masses:          0

Beams:           0

Shells:          0

Solids:       3189

Elements:     3189

------------------------------------------------------------

Standard Design Study

Description:

basic modal analysis

Modal Analysis "modal":

Convergence Method: Single-Pass Adaptive

Plotting Grid:      4

Convergence Loop Log:                         (08:33:15)

>> Pass  1 <<

Calculating Element Equations           (08:33:15)

Total Number of Equations:   57792

Maximum Edge Order:              3

>> Pass  2 <<

Calculating Element Equations           (08:36:33)

Total Number of Equations:   65469

Maximum Edge Order:              5

RMS Stress Error Estimates:

Mode   Stress Error  (% of Max Modal Stress)

----  --------------

1       0.8%

2       0.7%

3       2.4%

4       1.3%

5       1.1%

6       0.8%

7       0.9%

8       1.6%

9       4.3%

10       2.4%

11       2.0%

12       1.0%

Total Mass of Model:  2.943847e-04

Mass Moments of Inertia about WCS Origin:

Ixx:  1.41233e+00

Ixy: -2.35807e-01  Iyy:  3.84633e-01

Ixz: -4.52996e-03  Iyz:  1.01220e-03  Izz:  1.29888e+00

Principal MMOI and Principal Axes Relative to WCS Origin:

Max Prin           Mid Prin           Min Prin

1.46399e+00        1.29874e+00        3.33110e-01

WCS X:  9.76566e-01        2.74581e-02        2.13461e-01

WCS Y: -2.13377e-01       -5.97632e-03        9.76952e-01

WCS Z: -2.81010e-02        9.99605e-01       -2.26723e-05

Center of Mass Location Relative to WCS Origin:

( 1.02862e+01,  4.89316e+01, -5.38177e-02)

Mass Moments of Inertia about the Center of Mass:

Ixx:  7.07486e-01

Ixy: -8.76379e-02  Iyy:  3.53484e-01

Ixz: -4.69293e-03  Iyz:  2.36968e-04  Izz:  5.62882e-01

Principal MMOI and Principal Axes Relative to COM:

Max Prin           Mid Prin           Min Prin

7.28123e-01        5.62755e-01        3.32974e-01

WCS X:  9.73328e-01        2.64026e-02        2.27892e-01

WCS Y: -2.27705e-01       -9.92492e-03        9.73680e-01

WCS Z: -2.79695e-02        9.99602e-01        3.64820e-03

Constraint Set: ConstraintSet1

Number of Modes: 12

Mode   Frequency

----  ------------

1  6.881738e+02

2  8.638142e+02

3  1.780816e+03

4  2.715497e+03

5  3.058290e+03

6  3.283797e+03

7  3.344646e+03

8  3.614443e+03

9  3.957047e+03

10  4.096691e+03

11  4.676689e+03

12  5.185199e+03

### Verification

- need checking manually

This page has been left blank deliberately.