Section 10: Appendix 4

Mechanical Failure Modes Effect and Criticality Analysis

| EQUIPMENT / INSTRUMENT: |  |  |  | SPIRE | Subsystem / System: |  | BSM | Doc. Number: | Design Description appendix 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Operating Mode: |  |  |  | CHOP & JIGGLE MODE | Operating / Mission Phase: |  | Observing | Issue: | 1 |
| Functional Diagram / Drawings: |  |  |  |  |  |  |  | date | 24.JUN.01 |
| a |  | b | c | d | e | f | g | h | I |
| ID |  | Item and Function | Assumed Failure Mode | Resulting Performance of and Effects on Equipment / Subsystem / System | Observable Symptoms (Housekeeping, Test) | Criticality | Prevention or Compensation Methods (back-up, redundancy) | Recommendations | Remarks |
| RBD-1 | 1 | BSM STRUCT | Failure to cool down | degraded detector | high background | 2R | redundant thermal path |  | should complete a thermal path fmea? |
|  | 2 |  | Fails on launch | probable damage to SPIRE | lack of signal | 2R | three fasteners.(2/3 redundant) | sizing calc on structural fasteners | MSSL responsible for fastener sizing |
|  | 3 |  | Failure during operation (SCC OR FATIGUE CRACK) | erratic resonance effects | changes natural frequencies | 2 | back-up mode - drift map | perform FEA, use SCC OK material |
|  | 4 |  | Degraded operation (RESONATES) | longer settling time | longer settling time | 3 | reduce speed operation |  |  |
| RBD-2a | 1 | Jiggle axis flex pivot | Fails on launch | loss of definition of pointing Loss of restoring torque. Increased friction to drive. Jiggle mode probably unusable | -unstable pointing. -Cross coupling of chop with jiggle beyond normal parameters. Increase in drive currents. -Random noise on sensors | 2R | -prevention by flex pivot protecion sleeve. -redundant bearing surface (RBD-2B) - degraged operation. -Coarse control with motors to central position. -Scan-map back-up mode | increase test programme to cover failure modes if funds permit. | most likely to lose both flex pivots if one goes. |
|  | 2 |  | Failure during operation -icing | increase in friction & power usage (or stuck) after cooldown | thermal history . Cured by warm up | 2 | prevented by clean room procedures |  | only during AIV - not possible during on-orbit operations |
|  | 3 |  | Failure during operation - fatigue | as fails-on launch | deterioration in performance as crack progresses | 2 | prevented by design selection and by careful alignmnet | flex pivot alignment procedure is critical |
|  | 4 |  | Failure during operation - debris ingress | increase in friction & power usage | random sticking. Power consumption high | 2 | prevented by clean room procedures |  |  |
|  | 5 |  |  |  |  |  |  |  |  |
| RBD-2b | 1 | Jiggle axis flex pivot protection sleeve | Failure during operation -icing | increase in friction (or stuck) after cooldown | motors & sensors working OK but no motion results | 2 |  |  |  |
|  | 2 |  | Failure during operation - debris ingress | increase in friction & power usage |  | 2 |  |  |  |
|  | 3 |  | friction or end-stop caused by small clearance | increase in friction & power usage |  | 2 |  | flex pivot mounting is critical. End stops to be well characterised. |
|  | 4 |  | vacuum welds during launch rubbing contact | no jiggle mode. Fixed stare mode, not (0,0) | motors & sensors working OK but no motion results | 2 | dissimilar metals (aluminium, inconel) | tribology investigation if funds permit |
|  | 5 | redundant journal bearing function | fretting failure, possibly vacuum welding | increase in friction & power usage | erratic torque-position plot | 2 | dissimilar metals (aluminium, inconel) | tribology investigation if funds permit | consider tests of this mode. |
| RBD3 | 1 | Jiggle frame structure (includes fasteners) | Failure to cool down quickly | Flex pivot differential thermal stresses | nil | 3 | thermal end-stop. Controlled cooldown rate for instrument |  |
|  | 2 |  | Fails on launch: structure cracks | loss of chop axis position definition | erratic torque-position plot | 2 |  | perform FEA, use SCC OK material |
|  | 3 |  | Fails on launch: fastener loosens | loss of chop axis position definition | erratic torque-position plot | 2R | redundant fasteners (4/8) |  | locking fasteners, torque control |
|  | 4 |  | Failure during operation (SCC OR FATIGUE CRACK) | erratic resonance effects | changes natural frequencies | 2 | back-up mode - drift map | perform FEA, use SCC OK material |
|  | 5 |  | Degraded operation (RESONATES) | longer settling time | longer settling time | 3 | reduce speed operation |  | unlikely |
| RBD4 | 1 | Chop demand | no chop requested (eg due to error in ODF, telemetry, operator error) | delay to troubleshoot problem | no chopping | 3 | nil in BSM | ODF software needs to be robust handling chop requests | higher level system needs to provide protection |
|  | 2 |  | excessive chop angle or frequency requested | flex pivot overload or excess power dissipation | as RBD2a | 2 | nil in BSM | MCU needs voltage limiter, software needs sanity check | higher level system needs to provide protection |
|  | 3 |  | chop demand short circuits | excess power dissipation | excess power dissipation, fixed offset | 2 | reset higher level system |  |  |
| RBD5 | 1 | Chop Structure | Failure to cool down quickly | Flex pivot differential thermal stresses | nil | 3 | thermal end-stop. Controlled cooldown rate for instrument |  |
|  | 2 |  | Fails on launch: structure cracks | loss of chop axis position definition | erratic torque-position plot | 2 |  | perform FEA, use SCC OK material | unlikely |
|  | 3 |  | Fails on launch: fastener loosens | loss of chop axis position definition | erratic torque-position plot | 2R | flex pivots would act as journal bearing. | locking fasteners, torque control |
|  | 4 |  | Fails on launch: magnet loosens | chop axis jams anywhere in range of travel | chop jams or high friction load | 2 | try cycling prime and redundant motor coils and restore to zero position. Scan map. | good process control on magnet adhesive required |
|  | 5 |  | Failure during operation (SCC OR FATIGUE CRACK) | erratic resonance effects | changes natural frequencies | 2 | back-up mode - drift map | perform FEA, use SCC OK material | unlikely |
|  | 6 |  | Degraded operation (RESONATES) | longer settling time | longer settling time | 3 | reduce speed operation |  | unlikely |
|  | 7 | chop mirror | print throug of lightweighting on mirror surface | image degradation | waffle pattern | 2 |  | test mirror surface for print through |
|  | 8 |  | contamination on mirror | image degradation | loss of signal, spectrographic signature | 2 | clean room assembly |  | unlikely |
| RBD-6A | 1 | Chop axis flex pivot | Fails on launch | loss of definition of pointing Loss of restoring torque. Increased friction to drive. Chop mode probably unusable | -unstable pointing. - Increase in drive currents. -Random noise on sensors | 2R | -prevention by flex pivot protecion sleeve. -redundant bearing surface (RBD-2B) - degraged operation. -Coarse control with motors to central position. -use of jiggle for 1/f deconvolution -Scan-map back-up mode | increase test programme to cover failure modes if funds permit. | most likely to lose both flex pivots if one goes. |
|  | 2 |  | Failure during operation -icing | increase in friction & power usage (or stuck) after cooldown | thermal history . Cured by warm up | 2 | prevented by clean room procedures |  | only during AIV - not possible during on-orbit operations |
|  | 3 |  | Failure during operation - fatigue | as fails-on launch | deterioration in performance as crack progresses | 2 | prevented by design selection and by careful alignmnet | flex pivot alignment procedure is critical |
|  | 4 |  | Failure during operation - debris ingress | increase in friction & power usage | random sticking. Power consumption high | 2 | prevented by clean room procedures |  | unlikely |
| RBD-6b | 1 | Chop axis flex pivot protection sleeve | Failure during operation -icing | increase in friction (or stuck) after cooldown | motors & sensors working OK but no motion results | 2R | -scan map -use of jiggle for 1/f deconvolution |  |
|  | 2 |  | Failure during operation - debris ingress | increase in friction & power usage |  | 2R | -scan map -use of jiggle for 1/f deconvolution |  |
|  | 3 |  | friction or end-stop caused by small clearance | increase in friction & power usage |  | 2R |  | flex pivot mounting is critical. End stops to be well characterised. |
|  | 4 |  | vacuum welds during launch rubbing contact | no jiggle mode. Fixed stare mode, not (0,0) | motors & sensors working OK but no motion results | 2R | dissimilar metals (aluminium, inconel) | tribology investigation if funds permit |
|  | 5 | redundant journal bearing function | fretting failure, possibly vacuum welding | increase in friction & power usage | erratic torque-position plot | 2 | dissimilar metals (aluminium, inconel) | tribology investigation if funds permit | consider tests of this mode. |
| RDB 7A, 8A, 9A | 1 | DRCU - MAC - BSMe Primary boards | Premature operation | chop before unlatch or power surge? Could damage motors or pivots | unknown | 2 | nil in BSM | DRCU to perform FMECA |  |
|  | 2 |  | Failure to operate | no chop or jiggle mode. No unlatch command? | no chopping, jiggling. Latch and damping remain in place | 2R | scan map |  |  |
|  | 3 |  | Failure to cease operation | excess power dissipation | excess power dissipation, fixed offset | 2R | reset higher level system or switch to redundant unit |  |
|  | 4 |  | Failure during operation | motors fail in on condition | excess power dissipation, fixed offset | 2R | reset higher level system or switch to redundant unit |  |
|  | 5 |  | Failure during operation | loss of BSM control | no chopping, jiggling. Latch indeterminate? | 2R | scan map or switch to redundant unit |  | indetermoinate latch state should be avoided. |
|  | 6 |  | Degraded operation | degrraded BSM function | degrraded BSM function | 2R | scan map or switch to redundant unit |  |  |
|  | 7 |  | short circuit |  |  |  | nil in BSM |  |  |
|  | 8 |  | open circuit |  |  |  | nil in BSM |  |  |
|  | 9 |  | incorrect function |  |  |  | nil in BSM |  |  |
|  | 10 |  | Incorrect commands |  |  |  | nil in BSM |  |  |
|  | 11 |  | Incorrect software functions |  |  |  | nil in BSM |  |  |
| RBD 10A | 1 | Connectors and cryo-harness | short circuit | motor shorted | no motion | 2R | switch to redundant harness and operate against a damped motor |  |
|  | 2 |  | short circuit | sensor shorted | invalid sensor value | 2R | switch to redundant harness | set invalid sensor range flags in WE software | check - does de-power of WE primary open the circuit? |
|  | 3 |  | short circuit | PCAL shorted | nil in BSM | 3 | nil in BSM |  |  |
|  | 4 |  | short circuit | thermistor shorted | nil in BSM | 3 | switch to redundant harness |  |  |
|  | 5 |  | Degraded operation | intermittent short | as short, but more annoying | 2R | switch to redundant harness |  | diagnose by extended telemetry? |
|  | 6 |  | open circuit | motor open | degraded motion | 2R | switch to redundant harness |  |  |
|  | 7 |  | open circuit | sensor open | no position feedback | 2R | switch to redundant harness or operate open-loop |  |
|  | 8 |  | open circuit | PCAL open | nil in BSM | 3 | nil in BSM |  |  |
|  | 9 |  | open circuit | thermistor open | nil in BSM | 3 | switch to redundant harness |  |  |
| RBD 11A | 1 | Chop Axis sensor | Failure to operate | chop offset close to zero position | invalid sensor value | 2R | switch to redundant WE or operate open-loop | set invalid sensor flags in WE software | problem may be in WE or harness |
|  | 2 |  | Failure to cease operation | chop offset at end of travel. | no position feedback, excessive power dissipation | 2R | switch to redundant WE or operate open-loop |  |
|  | 3 |  | Failure during operation | erratic pointing performance or drift | unknown | 2R | switch to redundant WE |  |  |
|  | 4 |  | Degraded operation | erratic pointing performance or drift | unknown | 2R | switch to redundant WE |  |  |
|  | 5 |  | short circuit | chop offset close to zero position | invalid sensor value | 2R | switch to redundant WE |  |  |
|  | 6 |  | open circuit | chop offset at end of travel. | no position feedback, excessive power dissipation | 2R | switch to redundant WE or operate open-loop |  |  |
|  | 7 |  | Incorrect software functions | unexpected behaviour, please contact your systems administrator | nil in BSM | 2R | nil in BSM | test all modes in ground |  |
| RBD 11B | 1 | Chop Axis control mode with no feedback | Failure to operate | undamped motion | undamped motion | 3 | switch to redundant harness or operate open-loop | test this mode on ground | this is a back-up degarded operation mode |
|  | 2 |  | Incorrect software functions | unknown | nil in BSM | 3 | nil in BSM | ensure this operating mode included in software |  |
| RBD 11c | 1 | Chop Axis control mode with current feedback | Failure to operate | undamped motion | undamped motion | 3 | switch to redundant harness or operate open-loop | test this mode on ground | this is a back-up degarded operation mode |
|  | 2 |  | Incorrect software functions | unknown | nil in BSM | 3 | nil in BSM | ensure this operating mode included in software |  |
| RBD 12A | 1 | Chop Axis Motor | short circuit | no motion | no motion | 2R | switch to redundant WE and operate against a damped motor |  | is the shorted condidtion detectable in WE by telemetry? |
|  | 2 |  | open circuit (broken wires) | no motion | no motion | 2R | switch to redundant WE |  | housing damage can affect redundant motor so is SPF for chopping (but not SPIRE) |
|  | 3 |  | part-short circuit (motor windings reduced by short) | degraded motion | increased settling time, changed power dissipation | 2R | switch to redundant WE and operate against a partly damped motor |  |  |
|  | 4 |  | mechanical damage - housing | degraded motion or thermal hot spot | increase in friction & power usage (or stuck) | 2 | -switch to redundant WE -use jiggle for 1/f removal -revert to scanmap |  |  |
|  | 5 |  | mechanical damage - fasteners loose | degraded motion or thermal hot spot | increase in friction & power usage (or stuck) | 2 | -switch to redundant WE -use jiggle for 1/f removal -revert to scanmap |  |  |
|  | 6 |  | mechanical damage - shield | degraded motion or thermal hot spot | increase in friction & power usage (or stuck) | 2 | -switch to redundant WE -use jiggle for 1/f removal -revert to scanmap |  |  |
|  | 7 |  | loss of electrical isolation | unknown | noise or erratic motion | 2 | -switch to redundant WE -use jiggle for 1/f removal -revert to scanmap | investigate |  |
| RBD 12B | 1 | Chop Axis Motor (cold redundant) | short circuit (probably on launch) | damping of primary motor | damped motion, increase in power dissipation | 2 | operate against a damped motor | test this mode on ground. Test redundant circuits on establishing orbit | cold redundant component |
| RBD 13 | 1 | unlatch harness and connector | short circuit | latch shorted | no retract signal | 2R | switch to redundant harness and operate against a damped solenoid coil |  | launch latch is on BSMs so is fed by cryo harness. Motor damping would just be in WE. |
|  | 2 |  | short circuit | sensor shorted | sensor indicates closed, but chop motion restricted | 2R | switch to redundant harness |  |  |
|  | 3 |  | Degraded operation | intermittent short | as short, but more annoying | 2R | switch to redundant harness |  | repeat unlatch command several times. |
|  | 4 |  | open circuit | latch unpowered | no retract signal | 2R | switch to redundant harness |  |  |
|  | 5 |  | open circuit | sensor open | sensor indicates closed, but chop motion is OK | 2R | switch to redundant harness or operate open-loop | incorporate in checklists | false negative sensor reading. |
| RBD 14 | 1 | unlatch demand | no unlatch requested (software error) | delay to troubleshoot problem | no retract signal | 3 | nil in BSM | MCU software to be robust |  |
|  | 2 |  | latch command set high | delay to troubleshoot problem | no retract signal | 3 | nil in BSM | MCU software to be robust |  |
|  | 3 |  | latch demand short circuits | excess power dissipation | excess power dissipation, BSM pinned in chop | 2R | reset higher level system, operate BSM in limited range of travel. | must be able to turn off power to launch latch solenoid with redundant function | solenoid left on would boil cryogens off if no provisdion to turn it off. |
| RBD 15 A,B,C | 1 | chop axis damping unlatch | Premature operation (during launch) | no damping of coil during launch. Possible damage to flex pivots | none | 2R | redundant coils damped | test this mode on the ground | could incorporate feedback into MCU? |
|  | 2 |  | Failure to operate | no damping of coil during launch. Possible damage to flex pivots | detectable in MCU? | 3R | redundant coils damped | MCU feedback required on damping |  |
|  | 3 |  | Failure to cease operation | damping of primary motor | damped motion, increase in power dissipation | 2R | serial redundant switches, possible to operate against damped coil |  |  |
|  | 4 |  | Failure during operation | indeterminate state | unknown | 3R | serial redundant switches |  |  |
|  | 5 |  | short circuit | damping of primary motor | damped motion, increase in power dissipation | 2R | serial redundant switches, possible to operate against damped coil |  |  |
|  | 6 |  | Incorrect commands | unlatch when not required | detectable in MCU? | 2 | nil in BSM | software protection against premature unlatch demand required |  |
|  | 7 |  | Incorrect software functions | unlatch when not required | detectable in MCU? | 2 | nil in BSM | software protection against premature unlatch demand required |  |
| RBD 16A | 1 | chop axis deployable end-stop unlatch | Premature retratction (during launch) | no limit of travel during launch. Possible damage to flex pivots | none | 2R | motor coils damped, flex pivot sleeves, adequate reserve on pivots |  | could incorporate feedback into MCU? |
|  | 2 |  | Overconstrains pivots | induced flex pivot failure | as RDB2, 4 | 2R | flex pivot sleeves, use of jiggle to address 1/f noise, scan map | test for this during vibration campaingns |  |
|  | 3 |  | Failure to cease operation | locking of chop axis motion end stops at 1.5 degrees | no retract signal obtained, hard stops at end of travel | 3R | redundant coil on solenoid, redundant harness |  |  |
|  | 4 |  | Failure during operation | indeterminate state | unknown | 3 | unknown | test MCU / software for indeterminate state | unlikely as bi-stable magnet. |
|  | 5 |  | short circuit | damping of primary solenoid coil | no retract signal obtained, hard stops at end of travel | 3R | redundant coil on solenoid, redundant harness |  |  |
|  | 6 |  | Incorrect commands | unlatch when not required | detectable in MCU? | 2 | nil in BSM | software protection against premature unlatch demand required |  |
|  | 7 |  | Incorrect software functions | unlatch when not required | detectable in MCU? | 2 | nil in BSM | software protection against premature unlatch demand required |  |