Section 10 Appendix 6

Thermal Calculations

Contents

Calculation: thermal equilibrium of motor coils, materials G10 vs Aluminium	2

1.1	Variables:	2

1.2	Results	4

2	Mirror temperature estimate	6

2.1	Block Diagram	6

2.2	Calculation	7

2.3	Results	8

2.4	Check on limiting heat path	9

3	Cernox 1030 Thermometer data sheet	11

Figures

Figure 1 : Cooling with G10. At dissipations of 1mW the motor coils would radiate at 50-70K	4

Figure 2: Cooling with aluminium: at dissipations below 18mW the background temperature would remain in specification (<1K)	5

Figure 3: thermal block diagram	6

Figure 4 mirror temperature sensitivity	8

# Calculation: thermal equilibrium of motor coils, materials G10 vs Aluminium

## Variables:

| Motor Dissipation (W) | 0-1.5 | mW |
| --- | --- | --- |
| Surface area (coils) | 0.0005208 | m2 |
| Stephan-Boltzmann constant, σ | 5.67E-08 |  |
| BSM structure temperature (worst case) | 6.0 | K |

| Coil surface area based on dimensions (mm) |
| --- |
| L | B | W |
| 15.5 | 12 | 6.2 |

Heat loading from motors Q= A x σ x (T1^4-T2^4)

The temperature, T1 of the motor coil was then calculated assuming pure radiative cooling,

| The minimum section of the motro block (neglecting cooling from any thermal or magmetics shield) - dimensions |  |
| --- | --- |
| W | H |
| 2.1 | 4.5 |

| Conductive cooling via G10 |  |  |
| --- | --- | --- |
| c(6.2-4.0 K) | 0.2 | W/m |
| Conductive cooling via Aluminium |  |  |
| c(6.2-4.0 K) | 33.6 | W/m |
| Conductive cooling via aluminium bolted joint | 60 | W/ m2 K |
| Area of Aluminium (min restriction) | 0.0000378 | m2 |
| Area of aluminium bolted joint | 0.00028875 | m2 |
| length (to inner coil) | 0.0097 | m |
| length (to outer coil) | 0.0199 | m |

| However, the aluminium case thermal path has a limit on conduction - from the bolted joint interface |  |
| --- | --- |
| Based on a 1K differential (conservative), the limit is | 0.017325 W |

| Q = A.c/L |
| --- |
| Heat conduction then calculated for the inner or outer coil |
| Temperature of coil, with balance cooled radiatively plotted below |  |

## Results

Figure 1 : Cooling with G10. At dissipations of 1mW the motor coils would radiate at 50-70K

Figure 2: Cooling with aluminium: at dissipations below 18mW the background temperature would remain in specification (<1K)

# Mirror temperature estimate

## Block Diagram

Figure 3: thermal block diagram

## Calculation

| Ac | 8.30E-04 | m2 | Chop axis area sees sky |
| --- | --- | --- | --- |
| Am | 3.00E-04 | m2 | Chop axis area sees motor |
| Ap | 4.48E-07 | m2 | csa pivots |
| Cp | 0.6 | W/ m2 | conduction pivots (stainless steel) |
| Lp | 6.53E-03 | m | length pivots (approx) |
| Tj | 5 | K | bsm structure & jiggle frame temp |
| Ts | 4-150 | K | Temperature of sky |
| Tm | 4-180 | K | temperature of motors |

Steady state:

Q sky + Q motor = Q flex pivot (ignoring re-radiation by mirror)

Ac.σ.( Ts4- Tc4) + Am σ.( Tm4- Tc4) = Ap.cp/Lp (Tc - Tj)

(Ac-Am)Tc4	+(Ap.Cp/Lp. σ).Tc = (Ap.cp/Lp. σ).Tj + Ac.Ts4	+Am.Tm4

Solve for Tc, results below

## Results

Figure 4 mirror temperature sensitivity

## Check on limiting heat path

Note the above assumes the flex pivots are the limit on the heat path. This can be confirmed by  crude calculation, below.

Allowing a 0.1 deg K differential across each section or interface, the chop axis pivot clearly has the lowest conducted heat.

| Component | Conduction (4-6k) | conductance (W/m^2K) | Contact Area | min CSA | Length | max Conducted heat (W) | Delta-T | Notes |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Optical Bench |  |  |  |  |  |  | 0.1 |  |
| Bench-Shoe interface |  | 7.50E+02 | 4.10E-04 |  |  | 3.08E-02 | 0.1 | Al-Au-Al |
| Shoe minimum section | 33.600 |  |  | 4.00E-04 | 0.008 | 1.68E+00 | 0.1 | Al 6082 |
| shoe-BSMs interface |  | 7.50E+02 | 4.00E-04 |  |  | 3.00E-02 | 0.1 | Al-Au-Al |
| BSMs minimum section | 33.600 |  |  | 3.37E-04 | 0.093 | 1.22E-01 | 0.1 | Al 6082 |
| BSMs-flex pivot capture sleeve |  | 6.00E+01 | 1.30E-04 |  |  | 7.80E-04 | 0.1 | al-al. surface area of top pivot half factored by .75 to allow for joint conduction |
| Flex pivot capture sleeve x2 | 33.600 |  |  | 2.14E-02 | 0.006 | 2.40E+02 | 0.1 | Al 6082 |
| Flex pivot capture sleeve- flex pivot x2 |  | 4.00E+02 | 1.37E-04 |  |  | 5.48E-03 | 0.1 | Al-eccobon-inconel |
| Jiggle flex pivot minimum section x2 | 0.600 |  |  | 3.00E-06 | 0.008 | 4.50E-04 | 0.1 | Inconel (or stainless) |
| Jiggle flex pivot - jiggle frame |  | 4.00E+02 | 1.00E-02 |  |  | 4.00E-01 | 0.1 | inconel-al |
| Jiggle frame minimum section | 33.600 |  |  | 2.00E-05 | 0.040 | 1.68E-02 | 0.1 | Al 6082 |
| Jiggle frame - capture sleeve x2 |  | 6.00E+01 | 1.00E-02 |  |  | 6.00E-02 | 0.1 | al-al |
| capture sleeve - chop flex pivot x2 |  | 4.00E+02 | 1.00E-02 |  |  | 4.00E-01 | 0.1 | Al-eccobon-inconel |
| chop flex pivot min section x2 | 0.600 |  |  | 2.00E-06 | 0.008 | 3.00E-04 | 0.1 | Inconel (or stainless) |
| chop flex pivot - chop stage |  | 4.00E+02 | 1.00E-02 |  |  | 4.00E-01 | 0.1 | inconel-al |
| Chop stage (mirror) min section | 33.600 |  |  | 2.00E-05 | 0.025 | 2.69E-02 | 0.1 | Al 6061 |

Data:

| Aluminium thermal integral (AL 6082) | 33.6 | 6-4.2K | W/m | RAL doc gives ~14 W/mK |  | ATC has 85 for Al 6063 |
| --- | --- | --- | --- | --- | --- | --- |
| inconel (use stainless steel) | 0.6 | 6-4.2K | W/m | RAL & ATC agree |  |  |
| vespel sp-1 | 0.0125 | 6-4.2K | W/m | RAL |  |  |
| joints : |  |  |  |  |  |  |
| al-al |  | 6.00E+01 | W/m^2K |  |  |  |
| al-au-al |  | 7.50E+02 | W/m^2K |  |  |  |
| stainless-stainless |  | 1.00E+02 | W/m^2K |  |  |  |
| inconel-al |  | 4.00E+02 | W/m^2K | guess |  |  |
| Al-eccobon-inconel |  | 4.00E+02 | W/m^2K | guess |  |  |

# Cernox 1030 Thermometer data sheet