BSM Design Description, Annex B: Interface Control Document: BSM to SPIRE Structure

v 1.0

## Distribution List

| SPIRE-Project | Ken J. King |  |
| --- | --- | --- |
|  | Bruce M. Swinyard |  |
|  | Doug K.Griffin |  |
|  | Matt Griffin |  |
| UK ATC | Colin Cunningham |  |
|  | Gillian Wright |  |
|  | Ian Pain |  |
|  | Tully Peacocke |  |
|  | Brian Stobie |  |
|  | Tom Paul |  |
|  | Ken Wilson |  |
| MSSL | Berend Winter |  |

## Record of Issue

| Date | Index | Remarks |
| --- | --- | --- |
| 19.Jun.01 | 1.0 | First Issue |

## Table of contents

Distribution List	1

Record of Issue	1

Table of contents	2

File Description	2

1.	Scope	3

2.	Documents	3

2.1.	Applicable documents	3

2.2.	Reference documents	3

3.	Functional Description and Block Diagram	3

4.	Inputs	5

4.1.	Resonance	5

4.2.	Scale factor	5

1.3.	Assumptions	6

1.4.	Suspended Masses	6

5.	Outputs	7

6.	Interface drawing	8

7.	Mass Properties	13

7.1.	Assembly Inertia Properties : SPIRE-BSM-020-001	16

7.2.	Assembly: BSM CHOP AXIS : SPIRE-BSM-020-004	17

7.3.	Assembly: Gimbal Frame : SPIRE-BSM-020-003	18

8.	Mechanical Environment	19

9.	Thermal Interface	19

9.1.	Finish	19

9.2.	Surface Area	19

9.3.	Contact Force	19

10.	Harness Routing	20

## File Description

Created with:	 	MS Word 97 SR-1

File: 			BSM_DESIGN_DESCRIPTION_V4.0_ annex_B_v1_0.doc

# Scope

This document outlines the ICD between the BSM (ATC) and the SPIRE structure (MSSL).

The contents of this document are intended for incorporation in the MSSL Structure ICD document, AD4

# Documents

## Applicable documents

|  | Title | Author | Reference | Date |
| --- | --- | --- | --- | --- |
| AD2 | BSM ICD drawing | I.Pain | ATC drawing number: SPIRE-BSM-021-002-001 | 15.Jun.01 |
| AD3 | Structure ICD drawing | MSSL | MSSL drawing number: A2/5264/907 |  |
| AD4 | ICD Structure - Mechanical I/F | B.Winter | SPIRE-MSS-PRJ-000xxx v1.0 | Apr.01 |
| AD5 | SPIRE Harness Definition | D.K.Griffin | SPIRE-RAL-PRJ-000608 v0.3 | 30.May.01 |
| AD6 | TBD (harness run mechanical details) |  | TBD |  |

## Reference documents

|  | Title | Author | Reference | Date |
| --- | --- | --- | --- | --- |
| RD 1 | Thermal Configuration Control Document | S.Heys | SPIRE-RAL-PRJ-000560 | 18.Apr.01 |

# Functional Description and Block Diagram

See BSM Design Description, section 5, 6 for the functional description and general block diagram. The specific ICD block diagram is shown below.

The BSM interfaces directly to the SPIRE Optical Bench and the optical beam. Four elements of the BSM are of relevance to this ICD.

- The baseplate provides location and a thermal path.

- The structural interface locates the BSM mechanism in place.

- The mechanism comprises a nested gimbal mount with a jiggle and chop axis. The mirror is integral to the chop axis.

The Photometer Calibrator (PCAL) has a direct interface to the back of the BSM structural interface, and the PCAL wiring is carried via the BSM cryo-harness.

Thermometers are carried on board the BSM structure, and whilst these will be of use in diagnosis of the BSM thermal condition the thermometry wiring harness is not directly available to the BSM warm electronics.

The Baffle interface ownership is TBD. Whilst the baffle mounts to the BSM structure, its features with respect to the optical beam have not yet been fully defined.

Figure 1 : BSM-STRUCTURE ICD BLOCK DIAGRAM

# Inputs

The BSM receives input vibrations from the structure, at a high level during launch and at a low level during operation (spacecraft micro vibration environment). There is a feedback between the BSM and the structure due to the vibration response of the BSM.

## Resonance

The principal resonant modes of the structure and the two suspended masses are presented below. A full analysis of the combined system is to be completed.

The BSM structural interface forms a stiff body. The first twelve structural modes were determined by finite element analysis

| FEA prediction for Response of structural interface |  | Approximate assembly response (see scale factor) |
| --- | --- | --- |
| Mode | Frequency (Hz) | Frequency (Hz) |
| 1 | 688 | 433 |
| 2 | 864 | 544 |
| 3 | 1781 | 1121 |
| 4 | 2715 | 1710 |
| 5 | 3058 | 1926 |
| 6 | 3284 | 2068 |
| 7 | 3345 | 2106 |
| 8 | 3614 | 2276 |
| 9 | 3957 | 2492 |
| 10 | 4097 | 2579 |
| 11 | 4677 | 2945 |
| 12 | 5185 | 3265 |
|  | mass of structure | 291 |
|  | mass of assembly | 734 |
|  | scaling for resonance | 0.630 |

Table 1: Structural Interface Principal Modes

## Scale factor

Pending a full resonant modes analysis, we may note that since the stiffness of the structural interface design remains unchanged, the assembly natural frequency scales as:

fn = 	√ (k/m)

2 п

hence, fn(assy)/ fn(struct)  =  √( m struct/ m assy)

The mass of the structure used for the FEA modes search was calculated at 291gm, and the full assembly mass (excluding contingency, the baseplate and fasteners below the structure base) is predicted at 734 gm . This yields a scaling factor of ~ 0.63, used in Table 1.

## Assumptions

As the structural response remains above 250 Hz it may be assumed to be stiff for subsequent analysis of the SPIRE structure. The actual combined system modes will differ from those presented, due to contributory effects from:

- the effect of bolted joints,

- the contribution of point masses mounted to the structure as distinct from the distributed structural mass

- the resonances of components mounted to it (particularly the baffle, launch lock and motor mounts)

## Suspended Masses

The BSM suspended masses have first natural frequencies approximately as follow:

| Axis | Mode | Spring Stiffness (N-m/rad or N/m) | Inertia (kgm²) | Mass of suspended part (grammes) | 1st Resonant frequency (Hz) |
| --- | --- | --- | --- | --- | --- |
| Chop | Torsional | 0.05875 | 1.70E-06 |  | 29.6 |
|  | Radial Orthogonal | 1225887.6 |  | 16 | 1393.1 |
|  | Radial 45 degrees | 875634 |  | 16 | 1177.4 |
|  | Axial | 1751268 |  | 16 | 1665.1 |
| Jiggle | Torsional | 0.4625 | 4.65E-05 |  | 15.9 |
|  | Radial Orthogonal | 2101521.6 |  | 88 | 777.8 |
|  | Radial 45 degrees | 1576141.2 |  | 88 | 673.6 |
|  | Axial | 3152282.4 |  | 88 | 952.6 |

Table 2 : Suspended Mass Principal Modes

The radial orthogonal rate is where the load is z-x plane or in the plane formed by the optical bench y axis and the BSM gut ray.

The 45 degree radial rate is where the load is applied in line with the plane of a flexure (oriented at 45 degrees to the orthogonal planes).

# Outputs

The BSM will output a vibration to the Optical Bench during chopping and jiggling.  The primary output will be at the chop and jiggle frequencies : 2 Hz and 0.5 Hz respectively, with harmonics TBD. Local TBD resonances of the BSM (e.g. of the baffle) may modify the harmonics.

Neglecting harmonics and any structural amplification (which should be small anyway, as the structure is stiff) the output forces take the form of a torque reaction in the structure in response to the acceleration of the mirror and jiggle frame  in chop and jiggle.

An approximation to this torque reaction may be made by taking the inertia of the moving masses, and an average acceleration over the specified rise time.

| BSM reaction loads summary table | Chop (*) | Jiggle (**) | Units |
| --- | --- | --- | --- |
| Torque reaction about chop axis (average) | 7.12E-06 | 0 | Nm |
| Torque reaction about jiggle axis (average) | 0 | 9.74E-06 | Nm |
| reaction force at hole at (242.57, 117.2, 526.863) | 6.74E-05 | 1.43E-04 | N |
| reaction force at hole at (351.861, 117.2, 521.426) | -3.37E-05 | 3.70E-05 | N |
| reaction force at hole at (334.299,117.2, 467.198) | -3.37E-05 | 3.70E-05 | N |
| * Chop reaction forces in optical bench y-axis |
| ** Jiggle reaction forces in optical bench z-x plane (normal to BSM jiggle axis) |

Table 3: BSM Reaction Loads

Strictly, these forces are in matched pairs with no net effect. Thus an equivalent 'micro-g’ output cannot be attributed to the BSM, i.e., a 'micro-g'  input is only resolved at the interface  between the optical bench and another supported system.

As a working figure, at a BSM mass of ~0.938 kg, the 'g' loading required to provide this type of force input combining the chop and jiggle loads gives a nominal acceleration at the front hole of 1.69E-04 m/s², i.e. an  'equivalent g loading' of 17.2 micro-g. In reality, the relevant mass is that of the whole structure, which is an order of magnitude more massive than the BSM, this accelerations attributable to the BSM will be below 2 micro-g.

# Interface drawing

- MSSL drawing: A2/5264/907

- ATC drawing: SPIRE-BSM-021-002-001, 4 sheets attached below.

Note: Higher quality prints will be exchanged via DXF format and full size manufacturing prints (A2 or A3)

# Mass Properties

| MASS BREAKDOWN OF THE SPIRE BEAM STEERING MIRROR ASSEMBLY |  |  | v1.2 | dated 16.Jun.01 |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MODEL : SPIRE-BSM-020-001 |  |  |  |  |  |  |  |  |
|  |  |  | DENSITY (kg/mm^3) | COMPONENT MASS (kg) |  | ASSY. MASS (kg) | CONTINGENCY (%) | CONTINGENT MASS (kg) | MASS INCL CONTINGENCY (kg) |
| Part Number | DESCRIPTION | MATERIAL: |  |  | QUANTITY |  |  |  |  |
| SPIRE-BSM-020-001-001 | BSM STRUCTURAL INTERFACE | AL_TO_BS_1470_6082 | 2.78E-06 | 0.2910 | 1 | 0.2910 | 10% | 0.0291 | 0.3201 |
| SPIRE-BSM-020-001-002 | BASEPLATE | AL_TO_BS_1470_6082 | 2.71E-06 | 0.0838 | 1 | 0.0838 | 10% | 0.0084 | 0.0922 |
| SPIRE-BSM-020-001-003 | JIGGLE AXIS FLEX CLAMP (L) | AL_TO_BS_1470_6082 | 2.71E-06 | 0.0026 | 1 | 0.0026 | 10% | 0.0003 | 0.0029 |
| SPIRE-BSM-020-001-005 | JIGGLE AXIS FLEX CLAMP (U) | AL_TO_BS_1470_6082 | 2.71E-06 | 0.0023 | 1 | 0.0023 | 10% | 0.0002 | 0.0026 |
| SPIRE-BSM-020-001-004 | PCAL SPACE ENVELOPE | ASSEMBLY | 6.00E-06 | 0.0507 | 1 | 0.0507 | 25% | 0.0127 | 0.0633 |
| SPIRE-BSM-020-001-006 | BAFFLE (CONCEPT) | AL_TO_BS_1470_6082 | 2.72E-06 | 0.0337 | 1 | 0.0337 | 50% | 0.0169 | 0.0506 |
| SPIRE-BSM-020-001-007 | LAUNCH LATCH (ENVELOPE) | ASSEMBLY | 7.00E-06 | 0.0509 | 1 | 0.0509 | 25% | 0.0127 | 0.0636 |
| SPIRE-BSM-020-003 | GIMBAL ASSEMBLY | ASSEMBLY | 3.23E-06 | 0.0883 | 1 | 0.0883 | 10% | 0.0088 | 0.0971 |
| SPIRE-BSM-020-005 | COIL ASSEMBLY | ASSEMBLY | 2.06E-06 | 0.0133 | 4 | 0.0534 | 10% | 0.0053 | 0.0587 |
| SPIRE-BSM-020-006 | SENSOR ASSY JIGGLE | ASSEMBLY | 2.45E-07 | 0.0004 | 1 | 0.0004 | 10% | 0.0000 | 0.0004 |
| SPIRE-BSM-020-008 | SHIELDED FLEXURE ASSY | ASSEMBLY | 7.73E-06 | 0.0031 | 2 | 0.0063 | 15% | 0.0009 | 0.0072 |
| SPIRE-BSM-020-009 | HARNESS ASSY (CONCEPT) | ASSEMBLY | 2.71E-06 | 0.0046 | 2 | 0.0092 | 50% | 0.0046 | 0.0138 |
| DISC-SPRING-ID-3_2 | DISC SPRING | STAINLESS-STEEL | 7.91E-06 | 0.0000 | 4 | 0.0002 | 10% | 0.0000 | 0.0002 |
| CERNOX-THERMISTOR | CERNOX-THERMISTOR | COPPER-CANISTER | 8.90E-06 | 0.0048 | 2 | 0.0096 | 10% | 0.0010 | 0.0105 |
| CAP-HD-SCREW-SS-M4X10 | CAP-HD-SCREW-SS-M4X10 | STAINLESS-STEEL | 7.91E-06 | 0.0020 | 3 | 0.0061 | 10% | 0.0006 | 0.0067 |
| CAP-HD-SCREW-SS-M2X10 | CAP-HD-SCREW-SS-M2X10 | STAINLESS-STEEL | 7.91E-06 | 0.0004 | 4 | 0.0016 | 10% | 0.0002 | 0.0018 |
| CAP-HD-SCREW-SS-M2-5X7_75 | CAP-HD-SCREW-SS-M2-5X7_75 | STAINLESS-STEEL | 7.91E-06 | 0.0006 | 2 | 0.0011 | 10% | 0.0001 | 0.0013 |
| CAP-HD-SCREW-SS-M2-5X7 | CAP-HD-SCREW-SS-M2-5X7 | STAINLESS-STEEL | 7.91E-06 | 0.0005 | 15 | 0.0081 | 10% | 0.0008 | 0.0089 |
| CAP-HD-SCREW-SS-M2-5X6 | CAP-HD-SCREW-SS-M2-5X6 | STAINLESS-STEEL | 7.91E-06 | 0.0005 | 8 | 0.0040 | 10% | 0.0004 | 0.0044 |
| CAP-HD-SCREW-SS-M2-5X12 | CAP-HD-SCREW-SS-M2-5X12 | STAINLESS-STEEL | 7.91E-06 | 0.0007 | 4 | 0.0029 | 10% | 0.0003 | 0.0032 |
| 37WAY_CONN | 37 WAY MDM CONNECTOR | CONNECTOR | 2.10E-06 | 0.0063 | 2 | 0.0125 | 20% | 0.0025 | 0.0150 |
| UN-MODELLED PARTS | ADHESIVE | ADHESIVE | 2.00E-06 | 0.0010 | 10 | 0.0100 | 10% | 0.0010 | 0.0110 |
| (approx. mass only) | P-CLIPS | BRASS (TBC) | 8.45E-06 | 0.0003 | 16 | 0.0055 | 10% | 0.0006 | 0.0061 |
|  | P-CLIP FASTENERS | STAINLESS-STEEL | 7.91E-06 | 0.0004 | 16 | 0.0064 | 10% | 0.0006 | 0.0071 |
|  | MDM FASTENERS | STAINLESS-STEEL | 7.91E-06 | 0.0004 | 4 | 0.0016 | 10% | 0.0002 | 0.0018 |
|  | LOCKING INSERTS | STAINLESS-STEEL | 7.91E-06 | 0.0003 | 56 | 0.0168 | 20% | 0.0034 | 0.0202 |
|  | DOWELS | STAINLESS-STEEL | 7.91E-06 | 0.0001 | 8 | 0.0009 | 15% | 0.0001 | 0.0010 |
|  | COATING | Nickel (10um) & Gold (3 um) | 1.13E-05 | 0.0159 | 1 | 0.0159 | 15% | 0.0024 | 0.0183 |
|  | PAINT | QMW BLACK (40 um) | 3.00E-06 | 0.0130 | 1 | 0.0130 | 15% | 0.0019 | 0.0149 |
|  | LACING | TBD | 1.50E-06 | 0.0020 | 2 | 0.0040 | 15% | 0.0006 | 0.0046 |
|  |  |  |  |  | TOTAL | 0.7927 | TOTAL CONTINGENCY | 0.1166 |  |
|  |  |  |  |  | TOTAL INCLUDING CONTINGENCY |  |  |  | 0.9093 |
|  |  |  |  |  | NB: excludes cryo-harness x2 and shoulder bolts for mount to optical bench |  |  |  |  |

Table 4: BSM Mass Breakdown

## Assembly Inertia Properties : SPIRE-BSM-020-001

The analysis below is performed on the BSM assembly model. However, it neglects the un-modelled components discussed in Table 4 above.

VOLUME 		=  2.3301650e+05  MM^3

SURFACE AREA 	=  2.1612245e+05  MM^2

AVERAGE DENSITY 	=  3.0643866e-06 KILOGRAM / MM^3

MASS 			=  7.1405265e-01 KILOGRAM

CENTER OF GRAVITY with respect to CS0 coordinate frame:

X   Y   Z    -1.8016179e+00  4.0471565e+01  5.8857929e+01  MM

INERTIA with respect to CS0 coordinate frame:  (KILOGRAM * MM^2)

INERTIA TENSOR:

Ixx Ixy Ixz  5.1366739e+03  9.2292278e+01  3.4535460e+01

Iyx Iyy Iyz  9.2292278e+01  4.1046018e+03 -1.4494497e+03

Izx Izy Izz  3.4535460e+01 -1.4494497e+03  2.0149595e+03

INERTIA at CENTER OF GRAVITY with respect to CS0 coordinate frame:  (KILOGRAM * MM^2)

INERTIA TENSOR:

Ixx Ixy Ixz  1.4934320e+03  4.0227633e+01 -4.1182323e+01

Iyx Iyy Iyz  4.0227633e+01  1.6286230e+03  2.5147549e+02

Izx Izy Izz -4.1182323e+01  2.5147549e+02  8.4306099e+02

PRINCIPAL MOMENTS OF INERTIA:  (KILOGRAM * MM^2)

I1  I2  I3   7.6590064e+02  1.4934970e+03  1.7057184e+03

ROTATION MATRIX from CS0 orientation to PRINCIPAL AXES:

0.06976        0.98932        0.12798

-0.28216       -0.10349        0.95377

0.95683       -0.10265        0.27193

ROTATION ANGLES from CS0 orientation to PRINCIPAL AXES (degrees):

angles about x  y  z -74.087          7.353        -85.966

RADII OF GYRATION with respect to PRINCIPAL AXES:

R1  R2  R3 3.2750739e+01  4.5733776e+01  4.8875200e+01  MM

## Assembly: BSM CHOP AXIS : SPIRE-BSM-020-004

VOLUME 		=  5.0106321e+03  MM^3

SURFACE AREA 	=  7.3328141e+03  MM^2

AVERAGE DENSITY 	=  3.1950638e-06 KILOGRAM / MM^3

MASS 			=  1.6009289e-02 KILOGRAM

CENTER OF GRAVITY with respect to _SPIRE-BSM-02-004 coordinate frame:

X   Y   Z     0.0000000e+00  4.6417925e-01 -6.0681758e+00  MM

INERTIA with respect to SPIRE-BSM-02-004 coordinate frame:  (KILOGRAM * MM^2)

INERTIA TENSOR:

Ixx Ixy Ixz  6.1027583e+00  0.0000000e+00 -6.3660228e-02

Iyx Iyy Iyz  0.0000000e+00  7.4176717e+00  5.9492677e-06

Izx Izy Izz -6.3660228e-02  5.9492677e-06  1.7406695e+00

INERTIA at CENTER OF GRAVITY with respect to _SPIRE-BSM-02-004 coordinate frame:  (KILOGRAM * MM^2)

INERTIA TENSOR:

Ixx Ixy Ixz  5.5098027e+00  0.0000000e+00 -6.3660935e-02

Iyx Iyy Iyz  0.0000000e+00  6.8281655e+00 -4.5087757e-02

Izx Izy Izz -6.3660935e-02 -4.5087757e-02  1.7372201e+00

PRINCIPAL MOMENTS OF INERTIA:  (KILOGRAM * MM^2)

I1  I2  I3   1.7357470e+00  5.5108762e+00  6.8285650e+00

ROTATION MATRIX from _SPIRE-BSM-02-004 orientation to PRINCIPAL AXES:

0.01686        0.99986        0.00043

0.00885       -0.00058        0.99996

0.99982       -0.01686       -0.00886

ROTATION ANGLES from _SPIRE-BSM-02-004 orientation to PRINCIPAL AXES (degrees):

angles about x  y  z -90.508          0.000        -89.034

RADII OF GYRATION with respect to PRINCIPAL AXES:

R1  R2  R3 1.0412552e+01  1.8553434e+01  2.0652789e+01  MM

## Assembly: Gimbal Frame : SPIRE-BSM-020-003

(Note– includes chop axis)

VOLUME 		=  2.7324248e+04  MM^3

SURFACE AREA 	=  3.5418903e+04  MM^2

AVERAGE DENSITY 	=  3.2306362e-06 KILOGRAM / MM^3

MASS 			=  8.8274705e-02 KILOGRAM

CENTER OF GRAVITY with respect to ACS2 coordinate frame:

X   Y   Z     3.8892385e+00 -5.7432544e-02  4.9707259e-02  MM

INERTIA with respect to ACS2 coordinate frame:  (KILOGRAM * MM^2)

INERTIA TENSOR:

Ixx Ixy Ixz  4.6576925e+01  8.3785780e-01  9.1887627e-01

Iyx Iyy Iyz  8.3785780e-01  7.7344040e+01 -2.7094953e-01

Izx Izy Izz  9.1887627e-01 -2.7094953e-01  4.6274274e+01

INERTIA at CENTER OF GRAVITY with respect to ACS2 coordinate frame:  (KILOGRAM * MM^2)

INERTIA TENSOR:

Ixx Ixy Ixz  4.6576416e+01  8.1813998e-01  9.3594184e-01

Iyx Iyy Iyz  8.1813998e-01  7.6008563e+01 -2.7120153e-01

Izx Izy Izz  9.3594184e-01 -2.7120153e-01  4.4938724e+01

PRINCIPAL MOMENTS OF INERTIA:  (KILOGRAM * MM^2)

I1  I2  I3   4.4503068e+01  4.6987413e+01  7.6033222e+01

ROTATION MATRIX from ACS2 orientation to PRINCIPAL AXES:

-0.41747        0.90827        0.02751

0.01866       -0.02170        0.99959

0.90850        0.41782       -0.00789

ROTATION ANGLES from ACS2 orientation to PRINCIPAL AXES (degrees):

angles about x  y  z -90.452          1.577       -114.685

RADII OF GYRATION with respect to PRINCIPAL AXES:

R1  R2  R3 2.2453127e+01  2.3071330e+01  2.9348341e+01  MM

# Mechanical Environment

This section outlines the interaction with the SPIRE structure mechanical environment specified in AD4.

To Be Written

# Thermal Interface

Cooling of the BSM is provided by contact to the optical bench (per RD1) and also by a direct thermal strap, per AD4 (?).

## Finish

The BSM’s interface baseplate (drawing number SPIRE-BSM-020-001-002) will be aluminium alloy, grade 6082, coated with electroless nickel (nominally 10 microns) and gold (nominally 5 microns). The baseplate provides raised pads to allow the BSM to be aligned by one-off machining operations. Any such local machining may remove the gold plating and reduce the quality of thermal contact.

A thermal strap interface will also be provided directly on the BSM structural interface, (drawing number SPIRE-BSM-020-001-001) . This will comprise a tapped hole, sized M4x 4mm deep TBC. At the thermal strap interface the local area will be machined flat (TBD microns) and smooth (TBC 1.8 microns RA).

External finish requirements permitting ,the structure will be coated with electroless nickel (nominally 10 microns) and gold plated (nominally 15 microns) (TBC)

## Surface Area

The contact surface area of the baseplate is 410 mm²  (NB, RD1 assumes 400 mm², but does not include a thermal strap)

The contact surface area of the thermal strap is TBD mm²

## Contact Force

At each contact face an approximate contact force of 1 KN (TBC) will be developed at each joint by an 8-32 UNC shoulder bolt torqued to 1.5-3.0 N-m (TBD). (NB RD1 assumes 670N)

# Harness Routing

The BSM prime and redundant harness are separate.

Each harness includes the motor, sensor, thermometry and PCAL cables and interfaces via a fully populated 37 way MDM connector, as specified in AD5.

The harness is run to the BSM as described in AD6, with a total length of TBD mm and a mass of TBD kg.

# Footnotes

The baffle may be supplied by ATC or RAL to an agreed specification.