| CARLO GAVAZZI SPACE S.p.A. | FIRST DPU SPIRE-IFS-PRJ-000731 |
| --- | --- |
| DOCUMENT TYPE : SPECIFICATION | DRD : |
| TITLE: FIRST CPU BOARD SPECIFICATION |
| DOCUMENT No: DPU-SP-CGS-001 | PAGE: 1 OF 29 |
| ISSUE No: 1 | DATE: 11/12/2000 |
| PREPARED BY: L. TUNESI |
| APPROVED BY: |
| THIS DOCUMENT IS SUBJECT TO THE APPROVAL OF: |
|  | YES | NO |  |
| Product Assurance | X |  |  |  |  |  |
|  |  |  |  | Approval Signature |  | Date |
| Configuration Control | X |  |  |  |  |  |
|  |  |  |  | Approval Signature |  | Date |
| Project Control |  | X |  |  |  |  |
|  |  |  |  | Approval Signature |  | Date |
| Engineering | X |  |  |  |  |  |
|  |  |  |  | Approval Signature |  | Date |
| Managing Director |  | X |  |  |  |  |
|  |  |  |  | Approval Signature |  | Date |
| CGS Program Manager | X |  |  |  |  |  |
|  |  |  | Approval Signature |  | Date |
|  | YES | NO |  |  |
| Higher Level Contractor | X |  |  |  |  |  |
|  |  |  | Approval Signature |  | Date |
| Customer |  | X |  |  |  |  |
|  |  |  | Approval Signature |  | Date |
| Data Management |  |  |  |  |  |
|  |  |  | Signature |  | Date |

| DOCUMENT CHANGE RECORD |
| --- |
| ISSUE N° | DATE | CHANGE AUTHORITY | PAGES AFFECTED | REMARKS |
| 1 | 11/12/2000 |  |  |  |

| LIST OF VALID PAGES |
| --- |
| PAGE | ISSUE N° | PAGE | ISSUE N° | PAGE | ISSUE N° | PAGE | ISSUE N° | PAGE | ISSUE N° |
| 1-29 | 1 |  |  |  |  |  |  |  |  |

Table of contents

1	SCOPE	7

2	APPLICABLE DOCUMENTS	8

3	reference documents	9

4	board CHARACTERISTICS	10

5	MECHANICAL CONSTRAINTS	11

6	environmental constraints and power supply	12

7	functional description	13

7.1	Processor	13

7.1.1	Interrupts	14

7.2	Program Memory	14

7.2.1	Program Memory Map	14

7.2.2	Wait states	15

7.2.3	Program memory bench	15

7.3	Data Memory	16

7.3.1	Memory mapping	16

7.3.2	Wait states	16

7.3.3	Data memory bench	17

7.4	Control FPGA	17

7.4.1	Interrupt manager	18

7.4.2	Watchdog & Reset	19

7.4.3	Interval timer	21

7.5	EEPROM Block	21

7.6	Boot PROM	21

7.7	Bus Interface	22

7.8	IEEE 1355 Interface	24

7.8.1	Electrical Interface	25

7.9	Clocks Generation and Distribution	26

7.10	Latchup Protection	26

8	performances	27

9	Pin function	28

LIST OF ACRONYMS

| AD# | Applicable Document number # |
| --- | --- |
| ASI | Agenzia Spaziale Italiana |
| ATP | Authorization to proceed |
| CGS | Carlo Gavazzi Space SpA |
| CNR | Consiglio Nazionale delle Ricerche |
| CPP | Coordinated Part Procurement |
| DPU | Data Processing Unit |
| EDAC | Error Detector And Corrector |
| DPR | Dual Port Ram |
| EEPROM | Electrically Erasable Programmable Read Only Memory |
| EM | Engineering Model |
| EPROM | Erasable Programmable Read Only Memory |
| EQM | Engineering Qualification Model |
| FIRST | Far Infra-Red and Sub-millimeter Telescope |
| FM | Flight Model |
| FPGA | Field Programmable Gate Array |
| FS | Flight Spare |
| FSDL | Fast Science Data Link |
| HIFI | Heterodyne Instrument for First |
| IFSI | Istituto per la Fisica dello Spazio Interplanetario |
| I/F | Interface |
| LSL | Low Speed Link |
| OBDH | On Board Data Handling |
| PA | Product Assurance |
| PACS | Photoconductor Array Camera and Spectrometer |
| PCB | Printed Circuit Board |
| PROM | Programmable Read Only Memory |
| PL | Payload |
| RAM | Random Access Memory |
| RD# | Reference Document number # |
| SEU | Single Event Upset |
| S/C | Spacecraft |
| SPIRE | Spectral and Photometric Imaging Receiver |

# SCOPE

The aim of the present document is to define the specifications of the CPU board to be used in the Data Processing Units, developed in the framework of the First program.

# APPLICABLE DOCUMENTS

[AD1]:	CNR.IFSI.2000TR01 "Documento di Specifiche Tecniche per il Contratto delle Data Processing Units del Satellite First dell'ESA"    IFSI (Issue: 1 - 15/09/2000)

[AD2]:	Technical proposal CGS (Ref. S9-030 November 99)

[AD3]:	"Allegato Tecnico al Contratto ASI"

# reference documents

[RD1]:	Radiation Tolerant 32/40-BIT IEEE Floating Point DSP Microprocessor Data Book 	Temic REV E October 05, 1998

# board CHARACTERISTICS

The CPU board is based on the TEMIC TSC21020 DSP. The main characteristics of the board are the following:

- DSP TSC21020 clocked @20MHz, 50ns instruction cycle time

- 20 MIPS 66MFlops (peak) of instruction rate

- 512K x 48bit (3MByte) program memory (0 Wait States operation)

- 512K x 32bit (2MByte) data memory (0 Wait States operation)

- 256K x 32bit (1MByte) EEPROM memory

- 32K x 8bit PROM based bootloader that automatically stores the boot program in program memory

- Internal watchdog for monitoring of software execution (disabled via jumper)

- Custom parallel data bus with 24 bit address and 32bit data

- Interrupt manager, totally configurable, with 6 available interrupt lines

- 32bit programmable interval timer (1(s of resolution)

- Three IEEE1355 interfaces up to 100MHz, (50% of the time machine for the transferring) with 1K x 32bit DPR buffer and RS422 standard outputs

- JTAG plug for the on board software debugging (EM version only)

- AMP connector for test purpose (EM version only)

# MECHANICAL CONSTRAINTS

The CPU function is implemented through two Printed Circuit Boards named:

- Main board

- STD Mezzanine board

- an additional I/F mezzanine can be mounted for custom interface applications

The mechanical constraints of the two boards are shown in the Table 1 and Table 2 while the weight of the overall CPU function is specified in the Table 3

| Main board size: | Double Euro (160mm x 233.35mm) |
| --- | --- |
| Overall thickness: | 28 mm (6mm solder side, 20mm comp. side, 2 mm PCB max) |
| Card retainers: | Calmark series 260 |
| Board connectors (connection to back plane): | 90°, male, DIN41612 type |
| Board connectors (connection to mezzanines): | AMP 536280-2 |

Table 1 Main board constraints

| STD Mezzanine size: | TBD |
| --- | --- |
| STD Mezzanine connectors: | AMP 536279-2 |
| STD Mechanical fastening: | Fixation on main board and stiffening bar with six screws |

Table 2 STD mezzanine board constraints

| Overall weight (max): | 600g (TBC) |
| --- | --- |

Table 3 CPU board weight

Due to critical allocation of the components on the board, components are mounted on both sides of the PCB.

# environmental constraints and power supply

The constraints are summarised in the following tables:

| Operating temperature: | -30 ( +55 °C |
| --- | --- |
| Non operating temperature: | -50 ( +85 °C |
| Total dose: | ( 10 Krad |
| SEU rate: | ( 1 error/year |

Table 4 Environmental constraints

| Power supply: | 5V +/- 0.5V |
| --- | --- |
| Maximum continuous supply current | 1.5A |
| Peak current: | 2A |

Table 5 Power supply

# functional description

The block diagram of the CPU board is shown in the Picture 1

Picture 1 CPU board block diagram

In the next paragraphs each block will be described in detail.

## Processor

The CPU is a Temic TSC21020F clocked @20MHz. The clock is generated by an integrated oscillator and distributed through low skew clock distributors. The other clocks (showed in the Picture 7) are obtained by successive divisions from 20 MHz.

The processor works as 32-bit fixed point format.

### Interrupts

| DSP IRQ # | Peripheral |
| --- | --- |
| 0 | Interrupt manager (see paragraph 7.4.1) |
| 1 | IEEE1355 dual port ram |
| 2 | Not Used |
| 3 | Not used (highest priority) |

Table 6 DSP interrupt table

The interrupt 0 must be configured as level in any case. The four interrupts can be read in the IRPTL register (1=asserted).

The ISR are 8-instruction wide and are mapped in memory according to the following table:

| IRQ# | PM Address |
| --- | --- |
| 0 | 0x000040 |
| 1 | 0x000038 |
| 2 | 0x000030 |
| 3 | 0x000028 |

Table 7 Addresses of the interrupt service routines

In order to avoid that high level interrupts are not detected during the execution of an ISR related to a lower level IRQ, the interrupt-nesting mode of the DSP should be activated setting the bit 11 of the MODE1 register.

## Program Memory

A description of the DSP program memory mapping and characteristics of the data memory bench are presented in the next three paragraphs.

### Program Memory Map

In the program memory only the SRAM is present, mapped according to the following table:

| Range | Bank | Peripheral |
| --- | --- | --- |
| 0x000000-0x07FFFF | 0 | Program Memory (512KWord 48-bit wide) |

Table 8 Program Memory map

The most significant digits are not decoded by hardware. Their value is set in the bank registers. The table reflects the default configuration:

- PMBANK=0x800000.

Changing the values of this register will reflect on the memory map. Consequently if there isn’t any particular reason to have different bank sizes these registers should be left as they are at power-up.

### Wait states

The wait states for the Program Memory must be set by software when the program starts execution. The PMWAIT register must be set as follows:

|  | Number of WS | Bits to set | WS Mode | Bits to set |
| --- | --- | --- | --- | --- |
| Bank0 | 0x0 | 4-2 | Both int & ext (0x02) | 1-0 |
| Bank1 | 0x0 | 9-7 | Both int & ext (0x02) | 6-5 |
|  | PMWAIT=0x00000042 |

Table 9 Program memory: setting of wait state numbers and modes

### Program memory bench

The program memory is formed by six 512Kx8bit SRAM memory chips. The access time of such chips shall be (35ns to allow 0 wait states operation. For the program memory bench the global capacity is given by 512x1024x48bit=25.165.824 bit. The SEU requirement is a probability ( 1 error/year in RAM; taking into account the manufacturer data of 10-11 errors/(bit day) for geosynchronous orbit, the probability of a SEU event (due to a heavy ion impact), is equal to 0.1 error/year. Since this figure is less than the maximum requested no EDACs are foreseen.

## Data Memory

A description of the DSP data memory mapping and characteristics of the data memory bench are presented in the next three paragraphs.

### Memory mapping

In the data memory are mapped all the peripherals connected to the CPU, according to the following table

| Range | Bank | Peripheral |
| --- | --- | --- |
| 0x00000000-0x0007FFFF | 0 | Data Memory (512KWord 32-bit wide) |
| 0x20000000-0x3FFFFFFF | 1 | IF Mezzanine (not used) |
| 0x40000000-0x400003FF | 2 | IEEE1355 interface ( 1K X32-bit wide) |
| 0x80000000-0x8003FFFF | 3 | EEPROM (256Kx32-bit wide) |
| 0x81000000-0x81FFFFFF | 3 | Interval timer |
| 0x82000000-0x82FFFFFF | 3 | Watchdog |
| 0x83000000-0x83FFFFFF | 3 | Interrupt manager |
| 0x84000000-0x84FFFFFF | 3 | SMCS332 configuration registers |
| 0x88000000-0x8FFFFFFF | 3 | 32-bit Bus Interface |

Table 10 Data Memory map

The most significant digit is not decoded by hardware. Its value is set in the bank registers. The table reflects the default configuration:

- DMBANK1=0x20000000

- DMBANK2=0x40000000

- DMBANK3=0x80000000.

Changing the values of these registers will reflect on the memory map. Consequently if there isn’t any particular reason to have different bank sizes these registers should be left as they are at power-up.

### Wait states

The wait states for the Data Memory must be set by software when the program starts execution. The DMWAIT register must be set as follows:

|  | Number of WS | Bits to set | WS Mode | Bits to set |
| --- | --- | --- | --- | --- |
| Bank0 | 0x00 | 4-2 | Internal SW (0x01) | 1-0 |
| Bank1 | 0x02 | 9-7 | Both int & ext (0x02) | 6-5 |
| Bank2 | 0x00 | 14-12 | Internal SW (0x01) | 11-10 |
| Bank3 | 0x01 | 19-17 | Both int & ext (0x02) | 16-15 |
|  | DMWAIT=0x00030541 |

Table 11 Data Memory: setting of wait state numbers and modes

### Data memory bench

Since the processor works at 32-bit fixed point mode-operation, the lowest 8-bits of the data bus won't be used; the memory bench shall be mapped in D8-D39 data bus space.

The data memory is formed by four 512Kx8bit SRAM memory chips (32 bit parallelism), mapped on the lowest memory space of the address bus. The access time of such chips shall be (35ns to allow 0 wait states operation. For what concern the SEU rate, the same program memory concept can be applied and no EDACs are necessary.

## Control FPGA

The control FPGA is implemented with a rad-hard Actel RH1280 (TBC).

The block performs the following functions:

- bus control and bus management

- local peripheral timing adjustment

- mezzanine interface

- boot logic

- interrupt manager

- watchdog

- interval timer

In the next paragraphs the main sections will be discussed.

### Interrupt manager

The interrupt manager expands the overall number of interrupts adding 8 more interrupt lines to the 4 native of the DSP. The dashed interrupts IRQ2, IRQ3 IRQM0, IRQM1 are reserved!

This peripheral is mapped as a set of registers starting at the base address specified in the DM map and is connected to the interrupt 0 of the CPU.

The interrupts are connected to this peripheral as follows in the Picture 2 and in the Table 12:

Picture 2 Interrupts distribution

| IRQM# | Peripheral |
| --- | --- |
| 0 | IF Mezzanine (not used, kept low) |
| 1 | IF Mezzanine (not used, kept low) |
| 2 | Interval timer |
| 3 | Bus interface (FSDL 0) |
| 4 | Bus interface (FSDL 1) |
| 5 | Bus interface (FSDL 2) |
| 6 | Bus interface (FSDL 3) |
| 7 | Bus interface (MIL-STD 1553) |

Table 12 Meaning of the eight added interrupts

The programmer must set the interface at startup so that each interrupt is configured with the correct polarity.

The meaning of the registers is explained in the following table along with the corresponding location in memory (*=default).

| DM Address | Register | Type |
| --- | --- | --- |
| BASE+0x00 | IRQ level register (0=high*, 1=low) | R/W |
| BASE+0x01 | IRQ type register (0=edge*, 1=level) | R/W |
| BASE+0x02 | IRQ mask register (0=masked*, 1=active) | R/W |
| BASE+0x03 | IRQ acknowledge register (0=ignored, 1=acknowledge) | W |
| BASE+0x03 | IRQ vector register (0=no interrupt, 1=interrupt pending) | R |

Table 13 Interrupt manager registers

The interrupt service routine related to DSP IRQ0 must read the vector register to know which peripheral requested an interrupt, then perform the operations related to the interrupt and write the acknowledge register setting at 1 the bits corresponding to the interrupts to acknowledge.

The registers are 8-bit wide, mapped on the bits 15-8 of the data memory. For each register the link between the interrupt number and the bit number is shown in the following table:

| IRQM# | Bit |
| --- | --- |
| 0 | 0 |
| 1 | 1 |
| 2 | 2 |
| 3 | 3 |
| 4 | 4 |
| 5 | 5 |
| 6 | 6 |
| 7 | 7 |

Table 14 Correspondence bit position-irqm#

All the bits of the registers are set to 0 at power-up.

### Watchdog & Reset

The watchdog timer is mapped on the data memory starting from the base address specified in the data memory map. The unit is visible by software as two registers, whose meaning is shown in the following table:

| DM Address | Register | Type |
| --- | --- | --- |
| BASE+0x00 | Watchdog delay register | R/W |
| BASE+0x01 | Watchdog trigger register | W |

Table 15 Watchdog registers

Both registers are 16-bit wide, mapped on bits D23-D8 of the data memory bus. The delay between two triggers can be programmed writing the first 3 bits (w0, w1, w2) in the delay register, according to the table hereafter. The programmer must keep in mind that, after each power on reset, only one writing is allowed in this register to prevent unwanted watchdog interval reprogramming due to software failures! Further writings shall have no effect.

The fourth bit of the watchdog delay register causes the reset of the remote peripherals, connected to the parallel bus. By asserting (high) this flag, the \SYSRESETOUT output line of the board shall be asserted, to propagate the reset on the bus; a successive de-asserting (low) of the flag causes the de-asserting of the output line. Pay attention that the CPU board will not be reset by this flag, nevertheless a software reset of the board will be possible simply avoiding the trigger of the watchdog.

| Value | Delay |
| --- | --- |
| 0 | 13.36s (default) |
| 1 | 208.75ms |
| 2 | 417.5ms |
| 3 | 835ms |
| 4 | 1.67s |
| 5 | 3.34s |
| 6 | 6.68s |
| 7 | Watchdog disabled (test only) |

Table 16: Watchdog delays

Hereafter the semantic of the watchdog delay register is presented:

| D15 | D14 | D13 | D12 | D11 | D10 | D9 | D8 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Not used | Not used | Not used | Not used | Not used | Not used | Not used | Not used | Not used | Not used | Not used | Not used | RESET | W2 | W1 | W0 |

Table 17: watchdog delay register

The watchdog is triggered writing the value 0x5A6C (hex) on the trigger register. If the programmed time expires without triggering the Watchdog, the CPU is reset.

An hardware jumper shall disable the watchdog circuit.

### Interval timer

A programmable 32 bit binary interval timer is implemented in the FPGA and it is visible in the data memory space as a set of three registers:

- control register with a start stop/stop bit and IRQ enable/disable bit

- loading register for the setting of the programmable value

- read-back register for the counting monitoring

The counter is clocked @1MHz allowing 1(s of timing resolution.

An edge-mode interrupt is generated whenever the programmed time is elapsed (see Table 12).

## EEPROM Block

The EEPROM block contains the program to execute. It is formed by a single 256Kx32bit (32-bit parallelism) EEPROM. The 32 bits shall be mapped in the bits D8-D39 of the DSP data bus. For unwanted writings on the EEPROM, it can be software protected in single frames (JEDEC standard algorithm).

The transfer of the program from this module to the program memory and the reconstruction of the 48-bit words from the 8-bit code, shall be performed by software resident in PROM and loaded in program memory after the power-on.

## Boot PROM

The boot PROM contains the primary bootloader. It is made by a single 32Kx8bit PROM. Jumpers make possible to insert a differently sized PROM (up to 32Kx8bit). This PROM is fully controlled by the boot section of the control FPGA and is not visible to the software during normal operation. Other drivers contained in PROM are described in the "Software Architectural Design".

## Bus Interface

The internal bus is directly derived from the DSP data bus (see [RD1]); it is composed by the following lines:

- 24 address lines

- 32 data lines

- 5 interrupt lines (programmable)

- 8 chip select lines (actives low)

- 1 read line (active low)

- 1 write line (active low)

- 1 system clock (20MHz)

- 1 asynchronous reset line (active low)

On this bus are mapped all the external peripherals. The DSP decodes eight chip select, agree with the following table:

| \CS | Address range |
| --- | --- |
| 0 | 0x88000000-0x88FFFFFF |
| 1 | 0x89000000-0x89FFFFFF |
| 2 | 0x8A000000-0x8AFFFFFF |
| 3 | 0x8B000000-0x8BFFFFFF |
| 4 | 0x8C000000-0x8CFFFFFF |
| 5 | 0x8D000000-0x8DFFFFFF |
| 6 | 0x8E000000-0x8EFFFFFF |
| 7 | 0x8F000000-0x8FFFFFFF |

Table 18: chip select address range

The timing of the bus is compliant to the 21020 read and write timing with 1 W/S (TBC) for the devices addressed by CS0(CS6; the last one has 6 hardware W/S (TBC) to address slow peripherals. The 32 bits shall be mapped in the bits D8-D39 of the DSP data bus.

The Picture 3 and Picture 4 show respectively, the write and read cycles for the peripherals on the bus space whereas the Table 19 reports the timing values.

Picture 3 Bus write cycle

Picture 4 Bus read cycle

| Parameter | Min | Max | Unit |
| --- | --- | --- | --- |
| tdawl | 14 (TBC) |  | ns |
| twlcl |  | 17 (TBC) | ns |
| tdckwl | 20 (TBC) | 30 (TBC) | ns |
| twde | 0 (TBC) |  | ns |
| tww | 26 (TBC) |  | ns |
| tddwh | 19 (TBC) |  | ns |
| thdwh | 50 (TBC) |  | ns |
| tahch |  | 17 (TBC) | ns |
| twwr | 17 (TBC) |  | ns |
| tdarl | 11 (TBC) |  | ns |
| trlcl |  | 17 (TBC) | ns |
| tdckrl | 20 (TBC) | 30 (TBC) | ns |
| tdrld |  | 21(TBC) | ns |
| trw | 76 (TBC) |  | ns |
| thdrh | -4 (TBC) |  | ns |
| trwr | 17 (TBC) |  | ns |

Table 19 Bus timings

In case of successive accesses to the same memory area (same chip select), the \CS lines remain asserted until a different memory area is addressed; this means that is not mandatory to have chip select signal edges on a bus cycle.

## IEEE 1355 Interface

The STD mezzanine contains three IEEE1355 serial links; they are realised with a single chip named SMCS332. Each link is composed by four signals: data-in, strobe-in, data-out, strobe-out; the signals are in RS422 electrical standard format. A dual port ram (4Kx32-bit) is foreseen to minimise the CPU intervention.

To optimise the data exchange between the DSP and the SMCS, the data are 32-bit deep, consequently the SMCS data bus, must be configured via software in 32 bit-parallelism mode.

The configuration registers of the SMCS are mapped in the bank 3 of the data memory space; to adapt the timing cycle of the SMCS, the DSP uses the acknowledge line to add hardware W/S.

The DPR is addressed directly by the bank 2 to maximise the transfer speed.

Picture 5 IEEE1355 interface stage

### Electrical Interface

As mentioned above, the IEEE1355 links shall be in RS422 electrical standard format. The interfaces employ balanced differential line drivers and receivers, type 26C31, 26C32 to provide good common mode rejection and reasonable isolation characteristics. In the Picture 6 are shown the driving and receiving networks:

Picture 6: RS422 electrical interface

The parasitic capacitance of the 26C32 input lines (to ground) shall be <20pF, this restricts the length of the PCB traces between the input resistors and the 26C32 inputs.

## Clocks Generation and Distribution

Picture 7 Clock generation and distribution

An oscillator generates the 20MHz clock (maximum frequency clock) for the DSP and the bus interface; the other clocks are generated by some FPGA blocks by successive divisions. In particular, the 10MHz and 1 MHz clocks, are obtained dividing the original clock respectively by 2 and by 20. The clocks are distributed by means of clock buffers.

## Latchup Protection

Due to the high level of latchup immunity of the selected components (>100MeV/mg cm2), no latchup protection is implemented on CPU board. Anyway, different supply sections are foreseen on the board itself to increase flexibility of the current protection philosophy of the system. Actually, all the power supply sections are joined on the motherboard to supply the CPU board with a single power line.

# performances

The CPU board performances are the following:

- computational machine at 20 MIPS 66MFlops (peak)

- 20MHz system clock

- automatic HW bootloader for boot program storing in program memory

- 32-bit interval timer, 1(s resolution

- 32-bit parallel system bus <110ns transfer time (TBC)

- eight CS lines (active low) for the addressing of the other peripherals of the bus

- three IEEE1355 serial interfaces up to 100Mbit/s (50% of the time machine for the transferring) in RS422 electrical standard interfaces

- programmable watchdog with settable intervals from 417.5ms to 13.36s

- interrupt manager, totally configurable, with 6 available interrupt lines

# Pin function

The pin function of the CPU board is shown in the Table 20 and Table 21.

| Pin # | Signal | Pin # | Signal | Pin # | Signal |
| --- | --- | --- | --- | --- | --- |
| 1 | +5VD | 33 | +5VD | 65 | +5VD |
| 2 | +VEEPROM | 34 | +VFPGA (RTC) | 66 | +VDSP |
| 3 | D0 | 35 | D1 | 67 | D2 |
| 4 | D3 | 36 | D4 | 68 | D5 |
| 5 | D6 | 37 | D7 | 69 | D8 |
| 6 | D9 | 38 | D10 | 70 | D11 |
| 7 | D12 | 39 | D13 | 71 | D14 |
| 8 | D15 | 40 | D16 | 72 | D17 |
| 9 | D18 | 41 | D19 | 73 | D20 |
| 10 | D21 | 42 | D22 | 74 | D23 |
| 11 | D24 | 43 | D25 | 75 | D26 |
| 12 | D27 | 44 | D28 | 76 | D29 |
| 13 | D30 | 45 | D31 | 77 | \WR |
| 14 | A0 | 46 | A1 | 78 | A2 |
| 15 | A3 | 47 | A4 | 79 | A5 |
| 16 | A6 | 48 | A7 | 80 | A8 |
| 17 | DGND | 49 | SACK | 81 | DGND |
| 18 | A9 | 50 | A10 | 82 | A11 |
| 19 | A12 | 51 | A13 | 83 | A14 |
| 20 | A15 | 52 | A16 | 84 | A17 |
| 21 | A18 | 53 | A19 | 85 | A20 |
| 22 | A21 | 54 | A22 | 86 | A23 |
| 23 | \CS0 | 55 | \CS1 | 87 | \CS2 |
| 24 | \CS3 | 56 | \CS4 | 88 | \CS5 |
| 25 | \CS6 | 57 | \CS7 | 89 | \RD |
| 26 | IRQM3 | 58 | IRQM4 | 90 | IRQM5 |
| 27 | IRQM6 | 59 | IRQM7 | 91 | SYSCLK |
| 28 | RESERVED | 60 | \SYSRESETOUT | 92 | SYSCLK |
| 29 | RESERVED | 61 | RESERVED | 93 | RESERVED |
| 30 | AGND | 62 | AGND | 94 | AGND |
| 31 | RESERVED | 63 | RESERVED | 95 | RESERVED |
| 32 | DGND | 64 | DGND | 96 | DGND |

Table 20 CPU board: P1 pin function

| Pin # | Signal | Pin # | Signal | Pin # | Signal |
| --- | --- | --- | --- | --- | --- |
| 1 | +5VD | 33 | +VIFMEZZ | 65 | +5VD |
| 2 | L0DI+ | 34 | L1DI+ | 66 | L2DI+ |
| 3 | L0DI- | 35 | L1DI- | 67 | L2DI- |
| 4 | L0SI+ | 36 | L1SI+ | 68 | L2SI+ |
| 5 | L0SI- | 37 | L1SI- | 69 | L2SI- |
| 6 | L0DO+ | 38 | L1DO+ | 70 | L2DO+ |
| 7 | L0DO- | 39 | L1DO- | 71 | L2DO- |
| 8 | L0SO+ | 40 | L1SO+ | 72 | L2SO+ |
| 9 | L0SO- | 41 | L1SO- | 73 | L2SO- |
| 10 | RESERVED | 42 | RESERVED | 74 | RESERVED |
| 11 | RESERVED | 43 | RESERVED | 75 | RESERVED |
| 12 | RESERVED | 44 | RESERVED | 76 | RESERVED |
| 13 | RESERVED | 45 | RESERVED | 77 | RESERVED |
| 14 | RESERVED | 46 | RESERVED | 78 | RESERVED |
| 15 | RESERVED | 47 | RESERVED | 79 | RESERVED |
| 16 | RESERVED | 48 | RESERVED | 80 | RESERVED |
| 17 | RESERVED | 49 | RESERVED | 81 | RESERVED |
| 18 | RESERVED | 50 | RESERVED | 82 | RESERVED |
| 19 | RESERVED | 51 | RESERVED | 83 | RESERVED |
| 20 | RESERVED | 52 | RESERVED | 84 | RESERVED |
| 21 | RESERVED | 53 | RESERVED | 85 | RESERVED |
| 22 | RESERVED | 54 | RESERVED | 86 | RESERVED |
| 23 | RESERVED | 52 | RESERVED | 84 | RESERVED |
| 24 | RESERVED | 53 | RESERVED | 85 | RESERVED |
| 25 | RESERVED | 54 | RESERVED | 86 | RESERVED |
| 26 | RESERVED | 58 | RESERVED | 90 | RESERVED |
| 27 | RESERVED | 59 | RESERVED | 91 | RESERVED |
| 28 | RESERVED | 60 | RESERVED | 92 | NOT USED |
| 29 | NOT USED | 61 | NOT USED | 93 | NOT USED |
| 30 | RESERVED | 62 | RESERVED | 94 | RESERVED |
| 31 | RESERVED | 63 | FLAG0 | 95 | FLAG1 |
| 32 | DGND | 64 | DGND | 96 | DGND |

Table 21 Cpu board: P2 pin function