| CARLO GAVAZZI SPACE S.p.A. | FIRST DPU SPIRE-IFS-PRJ-OOO732 |
| --- | --- |
| DOCUMENT TYPE : SPECIFICATION | DRD : |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD SPECIFICATION |  |  |  |  |
| DOCUMENT No: DPU-SP-CGS-002 |  |  | PAGE: 1 OF 33 |  |
| ISSUE No: 1 |  |  | DATE: 11/12/2000 |  |
| PREPARED BY: L. TUNESI |  |  |  |  |
| APPROVED BY: |  |  |  |  |
| THIS DOCUMENT IS SUBJECT TO THE APPROVAL OF: |  |  |  |  |
|  | YES | NO |  |
| Product Assurance | X |  |  |  |  |  |
|  |  |  |  | Approval Signature |  | Date |
| Configuration Control | X |  |  |  |  |  |
|  |  |  |  | Approval Signature |  | Date |
| Project Control |  | X |  |  |  |  |
|  |  |  |  | Approval Signature |  | Date |
| Engineering | X |  |  |  |  |  |
|  |  |  |  | Approval Signature |  | Date |
| Managing Director |  | X |  |  |  |  |
|  |  |  |  | Approval Signature |  | Date |
| CGS Program Manager | X |  |  |  |  |  |
|  |  |  | Approval Signature |  | Date |
|  | YES | NO |  |  |
| Higher Level Contractor | X |  |  |  |  |  |
|  |  |  | Approval Signature |  | Date |
| Customer |  | X |  |  |  |  |
|  |  |  | Approval Signature |  | Date |
| Data Management |  |  |  |  |  |
|  |  |  | Signature |  | Date |

| DOCUMENT CHANGE RECORD |  |  |  |  |
| --- | --- | --- | --- | --- |
| ISSUE N° | DATE | CHANGE AUTHORITY | PAGES AFFECTED | REMARKS |
| 1 | 11/12/2000 |  |  |  |

| LIST OF VALID PAGES |
| --- |
| PAGE | ISSUE N° | PAGE | ISSUE N° | PAGE | ISSUE N° | PAGE | ISSUE N° | PAGE | ISSUE N° |
| 1-33 | 1 |  |  |  |  |  |  |  |  |

Table of contents

1	SCOPE	7

2	APPLICABLE DOCUMENTS	8

3	reference documents	9

4	board CHARACTERISTICS	10

5	MECHANICAL CONSTRAINTS	11

6	environmental constraints and power supply	12

7	functional description	13

7.1	Spacecraft Interface	14

7.1.1	Clock generation	15

7.1.2	Software interface	15

7.1.3	Hardware Interface	16

7.1.4	Interface to MIL-STD-1553 bus	17

7.2	Fast Science Data Link Interfaces	17

7.2.1	Interrupt generation	18

7.2.2	Fifo flags	19

7.2.3	Software interface	19

7.3	Low Speed Link Interface	20

7.3.1	Interface for HIFI	21

7.3.2	Interface for SPIRE	22

7.3.3	Software interface	23

7.4	32-bit bus Interface	24

7.5	Analog Inputs	27

7.5.1	Analog input interfaces	27

7.5.2	Software interface	27

7.6	Control Logic	28

7.6.1	Board registers	28

7.7	Board Reset	29

7.7.1	Power-on Reset	29

7.8	Latchup Protection	30

8	Electrical interfaces	31

9	Pin function	32

LIST OF ACRONYMS

| AD# | Applicable Document number # |
| --- | --- |
| ASI | Agenzia Spaziale Italiana |
| ATP | Authorization to proceed |
| CGS | Carlo Gavazzi Space SpA |
| CNR | Consiglio Nazionale delle Ricerche |
| CPP | Coordinated Part Procurement |
| DPU | Data Processing Unit |
| DDC | Data Device Corporation |
| DPR | Dual Port Ram |
| EDAC | Error Detector And Corrector |
| EEPROM | Electrically Erasable Programmable Read Only Memory |
| EF | Empty FIFO |
| EM | Engineering Model |
| EPROM | Erasable Programmable Read Only Memory |
| EQM | Engineering Qualification Model |
| FIRST | Far Infra-Red and Sub-millimeter Telescope |
| FF | Full FIFO |
| FM | Flight Model |
| FPGA | Field Programmable Gate Array |
| FS | Flight Spare |
| FSDL | Fast Science Data Link |
| HF | Half Full FIFO |
| HIFI | Heterodyne Instrument for First |
| IFSI | Istituto per la Fisica dello Spazio Interplanetario |
| I/F | Interface |
| LSL | Low Speed Link |
| OBDH | On Board Data Handling |
| PA | Product Assurance |
| PACS | Photoconductor Array Camera and Spectrometer |
| PCB | Printed Circuit Board |
| PROM | Programmable Read Only Memory |
| PL | Payload |
| RAM | Random Access Memory |
| RD# | Reference Document number # |
| SEU | Single Event Upset |
| S/C | Spacecraft |
| SPIRE | Spectral and Photometric Imaging Receiver |

# SCOPE

The aim of the present document is to define the specifications of the PL I/F board to be used in the Data Processing Units, developed in the framework of the First program.

This document shall be the basis on which the PL I/F board will be designed.

# APPLICABLE DOCUMENTS

[AD1]:	CNR.IFSI.2000TR01 "Documento di Specifiche Tecniche per il Contratto delle Data Processing Units del Satellite First dell'ESA"    IFSI (Issue: 1 - 15/09/2000)

[AD2]:	Technical proposal CGS (Ref. S9-030 November 99)

[AD3]:	"Allegato Tecnico al Contratto ASI"

# reference documents

[RD1]:	Radiation Tolerant 32/40-BIT IEEE Floating Point DSP Microprocessor Data Book 	Temic REV E October 05, 1998

[RD2]:	First CPU Board Specification	DPU-SP-CGS-001, Carlo Gavazzi Space Issue 1 date 12/10/2000

[RD3]:	Space Level MIL-STD-1553 BC/RT/MT Advanced Communication Engine Terminal BU-61582 Data Book 	ILC Data Device Corporation 1995

[RD4]:	MIL-STD-1553 BC/RT/MT Advance Communication Engine (ACE) Data Book  ILC Data Device Corporation

[RD5]:	ACE/Mini-ACE Series BC/RT/MT Advanced Communication Engine Integrated 1553 Terminal… User's Guide  ILC Data Device Corporation, june 1999, REV J-2

# board CHARACTERISTICS

The PL I/F board is based on the Actel 8000 gates RH1280 FPGA (TBC). The main characteristics of the board are the following:

- MIL-STD-1553 RT-mode serial interface up to 400KHz (burst mode) for the connection to the spacecraft

- 16MHz square wave oscillator onto the board (for the 1553 terminal unit)

- Four Fast Science Data Link (FSDL) ports up to 2.5MHz for the HIFI and SPIRE payloads interfacing

- Low Speed Link at 312.5KHz towards 7 sub-systems, for commands sending

- eight, not conditioned, 0-5V, single ended, analog inputs

- 32-bit parallel system bus

- Software interface implemented by registers mapped on the parallel bus address space

- AMP connector for test purpose (EM version only)

# MECHANICAL CONSTRAINTS

The PL I/F function is implemented through two Printed Circuit Boards (TBC) named:

- Main board

- Mezzanine board (TBC)

The mechanical constraints of the two boards are shown in the Table 1 and Table 2 while the weight of the overall PL I/F function is specified in the Table 3

| Main board size: | Double Euro (160mm x 233.35mm) |
| --- | --- |
| Overall thickness: | 28 mm (6mm solder side, 20mm comp. side, 2 mm PCB max) |
| Card retainers: | Calmark series 260 |
| Board connectors (connection to back plane): | 90°, male, DIN41612 type |
| Board connectors (connection to mezzanine): | AMP 536280-2 |

Table 1 Main board constraints

| Mezzanine size: | TBD |
| --- | --- |
| Mezzanine connectors: | AMP 536279-2 |
| Mechanical fastening: | Fixation on main board and stiffening bar with six screws |

Table 2 Mezzanine board constraints

| Overall weight (max): | 480g (TBC) |
| --- | --- |

Table 3 PL I/F board weight

Due to critical allocation of the components on the board, components are mounted on both sides of the PCB.

# environmental constraints and power supply

The constraints are summarised in the following tables:

| Operating temperature: | -30 ( +55 °C |
| --- | --- |
| Non operating temperature: | -50 ( +85 °C |
| Total dose: | ( 10 Krad |
| SEU rate: | ( 1 error/year |

Table 4 Environmental constraints

| Power supply: | 5V ( 0.5V +15V ( 1.5V -15V ( 1.5V |
| --- | --- |
| Maximum continuous supply current | 1.5A |
| Peak current: | 2A |

Table 5 Power supply

# functional description

The block diagram of the PL I/F board is shown in the Picture 1

Picture 1 PL I/F board block diagram

The dashed parts of the block diagram (third FIFO in the FSDL interface) are mounted only for HIFI configuration.

In the next paragraphs each block will be described in detail.

## Spacecraft Interface

The spacecraft interface is the MIL-STD-1553B standard serial link at 100Kbit/s up to 400Kbit/s (burst mode). This interface is realised with a dedicated hybrid circuit, made by DDC.

Picture 2: MIL-STD-1553 interface

For the EM and EQM models shall be mounted the commercial version, named BU-61580. For the flight models (FM, FS) the BU-61582, the radiation hardened version of the BU-61580 terminal, shall be mounted.

This very useful terminal integrates dual transceivers, protocol, memory management and processor interface logic, 16Kx16-bit (4Kx16-bit for the commercial version) of Dual Port RAM and a Time Tag Register used to allow the software to manage the "on board time". The timer rollover generates an interrupt to be used to increment the software time registers. The clock of the Time Tag Register implies the time resolution. The programmable resolution is 2, 4, 8, 16, 32 or 64(s per LSB.

The terminal unit is used in 16-bit buffered mode [RD5].

### Clock generation

The DDC chip needs a square wave clock @16MHz; in order to easily generate this signal, a VECTRON qualified oscillator shall be used. All the other peripherals shall work with dedicated clocks generated by the 20MHz system clock.

### Software interface

In two different system bus spaces are mapped the S/C interface registers and the interface memory (see Table 15). The registers are the following:

| Address | Register | Size [bit] | Direction |
| --- | --- | --- | --- |
| 0x4000 | Interrupt mask register | 16 | read/write |
| 0x4001 | Configuration register #1 | 16 | read/write |
| 0x4002 | Configuration register #2 | 16 | read/write |
| 0x4003 | Start/Reset register | 16 | write |
| 0x4003 | BC/RT Command Stack Pointer register | 16 | read |
| 0x4004 | BC Control Word/RT Subaddress Control Word register | 16 | read/write |
| 0x4005 | Time Tag register | 16 | read/write |
| 0x4006 | Interrupt Status register | 16 | read |
| 0x4007 | Configuration register #3 | 16 | read/write |
| 0x4008 | Configuration register #4 | 16 | read/write |
| 0x4009 | Configuration register #5 | 16 | read/write |
| 0x400A | Data Stack Address register | 16 | read/write |
| 0x400B | BC Frame Time Remaining register | 16 | read/write |
| 0x400C | BC Time Remaining to Next Message register | 16 | read/write |
| 0x400D | BC Frame Time/RT Last Command/MT Trigger Word register | 16 | read/write |
| 0x400E | RT Status Word register | 16 | read |
| 0x400F | RT BIT Word register | 16 | read |
| 0x4010 | Test Mode register 0 | 16 |  |
| 0x4011 | Test Mode register 0 | 16 |  |
| 0x4012 | Test Mode register 0 | 16 |  |
| 0x4013 | Test Mode register 0 | 16 |  |
| 0x4014 | Test Mode register 0 | 16 |  |
| 0x4015 | Test Mode register 0 | 16 |  |
| 0x4016 | Test Mode register 0 | 16 |  |
| 0x4017 | Test Mode register 0 | 16 |  |
| 0x4018 | Reserved | 16 | -- |
| 0x4019 | Reserved | 16 | -- |
| 0x401A | Reserved | 16 | -- |
| 0x401B | Reserved | 16 | -- |
| 0x401C | Reserved | 16 | -- |
| 0x401D | Reserved | 16 | -- |
| 0x401E | Reserved | 16 | -- |
| 0x401F | Reserved | 16 | -- |

Table 6: MIL-STD-1553 registers

The registers are described in detail in [RD3].

For the data exchange, a 16Kx16-bit (4Kx16-bit for EM and EQM version) internal Dual Port RAM is used and it is mapped according to Table 7.

| Address | Peripheral | Size [bit] | Direction |
| --- | --- | --- | --- |
| 0x0000 ( 0x3FFF | Buffer RAM | 16 | read write |

Table 7: S/C interface buffer memory

The \INCMD hardware flag is mapped on the board status register (see Table 19) whereas the \SSFLAG pin is not connected.

### Hardware Interface

A hardware reset, acting on the MSTCLR pin of the terminal, shall be mapped in the reset register of the board.

This terminal unit is mapped as slow peripheral (\CS7) of the system bus; in order to adjust the timing, an acknowledge management mode is foreseen [RD5]. Two configurations (settable via jumper) are possible to manage this timing:

- non zero wait state mode

- zero wait state mode

The non zero wait state mode allows direct interface to the system bus: the terminal stops the DSP until the data are available on the output bus of the unit. In the zero wait state mode, the processor can clear its strobe before the completion of access to the unit internal RAM or registers. In this case it is necessary to connect and polling the \READYD line to FLAG1, for the completion of the transfer [RD3]. The suggested configuration is the first one.

### Interface to MIL-STD-1553 bus

The interface to MIL-STD-1553 bus is the transformer coupled configuration (long stub). Two isolation transformers (one per section) are present on the board. Since the terminal unit is powered at (15V, the transformers have a turns ratio of 2:1.

## Fast Science Data Link Interfaces

The four Fast Science Data Links are implemented to receive data from HIFI and SPIRE; the conceptual scheme is presented in the following picture:

Picture 3: Fast Science Data Link diagram

HIFI interfaces the DPU with four FSDL links (connection with HRS-V/H and WBS-V/H) only three links are necessary for the SPIRE (connection with DRE, MCE, SCE).

All the signals (FDATA, FCK, FGATE) are generated on the sub-unit side. The interface can receive data with clock frequencies up to 2.5MHz and the size of the data is dependent to the payload. HIFI uses 24-bit and the total FIFO configuration is necessary (up to 32-bit); on the contrary SPIRE uses 16-bit and two FIFO banks per link are mounted.

The timings are shown in Picture 4

Picture 4: FSDL timings

The gate signal is active (high) during the transmission of each data word. The gate signal shall be inactive (low) for, at least, one clock cycle between successive data word transfers. The gate and data signals change state on the falling edge of the clock signal.

### Interrupt generation

When the FIFO reaches the half quantity of data, an edge mode (150ns) interrupt is generated; each FSDL provides a dedicated interrupt line (see Table 8).

| IRQM# | Peripheral |
| --- | --- |
| 3 | Bus interface (FSDL 0) |
| 4 | Bus interface (FSDL 1) |
| 5 | Bus interface (FSDL 2) |
| 6 | Bus interface (FSDL 3) |

Table 8: FSDL interrupts

### Fifo flags

In the status register (see paragraph 7.6.1) the empty FIFO (EF), half full FIFO (HF) and full FIFO (FF) of each link are mapped; an echo of the gate signals (ACQ) are present in the status register to inform the system about the receiving data from the payload. An echo of the empty and full FIFO flags is directly in the SRX registers of each FSDL interface (see Picture 3).

Four fifo error flags (one per link) are mapped in the status register to inform that a misalignment is occurred. The hardware implementation is shown in Picture 5

Picture 5 FIFO error flag generation

In the reset register (see paragraph 7.6.1) four FIFO resets are mapped to clear the memories.

### Software interface

| Address | Register name | Size [bit] | Direction |
| --- | --- | --- | --- |
| 0x0 | FRX_register | 32 | read |

Table 9: FSDL registers

The 24 bit (16 for SPIRE) shall be mapped on the lowest space of the system data bus.

If the software accesses the registers when the FIFO are empty (EF flag asserted on the status register), the loaded value is not significant.

## Low Speed Link Interface

This command/housekeeping interface is applicable to both HIFI and SPIRE payloads; in particular it has to interface the LSU, LCU, FCU, HR-H, HR-V, WBE-H and WBE-V sub-units of HIFI, whereas DRE, MCE, SCE are the sub-units of SPIRE connected to this link.

The signals constituting the links are: clock line (LCK), transmitter line (LTX) and receiver line (LRX). LCK and LTX have to be generated by the board and LRX arrives from the sub-units. The LTX and LRX signals change state on the falling edge of the clock signal.

The clock is fixed at 312.5KHz and it is generated dividing the system clock by 64 (with a FPGA divider block).

Only three LRX lines are present, both for HIFI (LSU, LCU, FCU) and SPIRE; they have dedicates RS422 receivers and are selected, for the acquisition, by a MUX.

A schematic view of the board-side interface is the following:

Picture 6: Low Speed Link Interface

By this interface it is possible to send commands or housekeeping requests; some differences between the two payloads will be discussed: two different FPGA projects allow the implementation of the two configurations.

All the data formats shall be performed by software. In particular, for what concern the HIFI housekeeping request, the programmer must adds 16 high bits LSB to normalise the word in 32-bit format.

### Interface for HIFI

The command protocol and timing diagram is shown in Picture 7. Each command consists of: one start bit (high), one mode bit (high), four subsystem address bits and 26 data bits. The subsystem addresses are hamming coded, according to Table 10. No answers from the sub-units are foreseen in command protocol.

| AS0-AS3 | Unit |
| --- | --- |
| 0000 | LSU |
| 0011 | FCU |
| 0101 | HRH |
| 0110 | HRV |
| 1001 | WBE-H |
| 1010 | WBE-V |
| 1100 | LCU |
| 1111 | Broadcast command |

Table 10: Subsystem addresses

Picture 7: HIFI command protocol

A housekeeping request consist of: one start bit (high), one mode bit (low), four subsystem address bits, and an envelope. The address bits identify the requested housekeeping parameter. The envelope shall be active (high) until the full housekeeping response has been received, in any case it goes inactive (low) after 400 clock-cycles (hardware timeout). If the DPU has to transmit a command, when the housekeeping envelope is still active, the housekeeping request shall be aborted by setting the envelope into the inactive state.

Picture 8: HIFI housekeeping request command protocol

A command or housekeeping request shall not start within one clock-cycle after the previous command has terminated or the housekeeping envelope has gone to the inactive state.

### Interface for SPIRE

The command and acknowledge (echo or parameters) protocol is shown in Picture 9

Picture 9: SPIRE command protocol

Each command or acknowledge word is composed by: one start bit (high), one mode bit (low for echo request, high for command sending without answers), two subsystem address bits, 28 data bits.

| Mode bit | Ack |
| --- | --- |
| 0 | yes |
| 1 | no |

Table 11: Mode bit pattern definition

| A1 | A0 | Subsystem |
| --- | --- | --- |
| 0 | 0 | DRE |
| 0 | 1 | MCE |
| 1 | 0 | SCE |
| 1 | 1 | Broadcast command |

Table 12: subsystem addresses

Each command shall not start within one clock-cycle after the previous command has terminated (stop bit).

When a command with acknowledge request is received, the subsystem responds by transferring a command acknowledge word (echo or parameter) on the LRX interface line. The DPU receives then the answer, from the selected sub-unit. Successive answers, generated by other commands, will be overwritten on the same register.

### Software interface

The software interface is realised with three registers, as mentioned in Table 13

| Address | Register name | Size [bit] | Direction |
| --- | --- | --- | --- |
| 0x0 | LTX_register | 32 | read/write |
| 0x1 | LRX_ register | 32 | read |
| 0x2 | Lstatus_register | 32 | read |

Table 13: LSL registers

The command a/o the housekeeping request have to be written in the LTX register in 32-bit format, only when the "TX busy" flag of the Lstatus register (see Table 14) is not asserted. The "TX busy flag" is asserted when the interface is engaged in a command sending.

When a write cycle starts (only for HIFI), a previous housekeeping request, not terminated, shall be aborted and a new transmission will start. In this case the "HK aborted" flag of the Lstatus register will assert.

The echo/housekeeping datum (when the mode-bit of the TX command is low) is latched in the LRX register, then the "data ready" flag is asserted. The LRX register (and the "data ready" flag) shall be HW reset after a CPU read-access of this register.

| D15 | D14 | D13 | D12 | D11 | D10 | D9 | D8 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Not used | Not used | Not used | Not used | Not used | Not used | Not used | Not used | Not used | Not used | Not used | HK aborted (HIFI only) | Timeout (HIFI only) | HK pending (HIFI only) | Data ready | TX Busy |

Table 14: Lstatus register

The D3, D4 bits of the Lstatus register will be reset after a Lstatus reading cycle; in any case a new writing of the LTX register will reset the D1, D2, D3 of the same register.

In the board reset register a LSL reset flag clears whole the interface aborting every command sending, parameter waiting and clearing all the Lregisters.

## 32-bit bus Interface

The bus interface is implemented with buffer and transceiver devices, to match the bus electrical specifications and to be able to receive the following lines:

- 24 address lines

- 32 data lines

- 7 chip select lines (actives low)

- 1 read line (active low)

- 1 write line (active low)

- 1 system clock (20MHz)

- 1 asynchronous reset line (active low)

The bus interface has to drive:

- 5 interrupt lines

- 32 data lines

- 1 acknowledge line (active high)

The timing of the bus is derived from the ADSP21020 data bus; the number of wait states, associated to each chip select, is reported in the [RD2]. The 32 bits shall be mapped in the bits D8-D39 of the DSP data bus.

The Picture 10 and Picture 11 show respectively, the write and read cycles for the peripherals on the bus space.

Picture 10: Bus write cycle

Picture 11: Bus read cycle

The timing values are reported in the [RD2].

For what concern the internal peripherals, the chip select lines, coming from the bus, manage them according to the following table:

| \Chip select | Peripheral |
| --- | --- |
| 0 | FSDL 0 |
| 1 | FSDL 1 |
| 2 | FSDL 2 |
| 3 | FSDL 3 |
| 4 | Low Speed Link |
| 5 | Board Registers |
| 6 | Not used |
| 7 | MIL-STD-1553 Dual Port Ram (16KW) |
| 7 | MIL-STD-1553 Registers (see Table 6) |
| 7 | Analog Inputs (see Table 16) |

Table 15: map of the board into the system bus space

In case of successive accesses to the same memory area (same chip select), the \CS lines remain asserted until a different memory area is addressed; this means that is not mandatory to have chip select signal edges on a bus cycle.

## Analog Inputs

This section provides 8 single-ended, 0(5V, not conditioned analog inputs, each one having 10K( 100pF RC filter.

### Analog input interfaces

The analog input interface is implemented with an ADC chain, composed by the following stages:

- 8 analog input channels, each one with a 10K( 100pF RC filter

- a 8-channel analog multiplexer (HS508) that selects the channel

- an amplifier implemented with a OP27 operational amplifier that adapts the signal to the ADC span

- an AD584 voltage reference that provides a high precision voltage reference to the ADC chain, allowing a reference for possible software compensation of errors (thermal drift, gain variations, ageing, offset and so on) and for calibration verification purposes

- an AD574, 12-bit, 35(s ADC that receives the start conversion signal from the control stage of the FPGA and, after about 35(s, provides a data ready signal to the FPGA

- a 12-bit latch, implemented on the FPGA, that stores the converted value until the CPU reading

### Software interface

The analog input stage is addressed by a dedicated chip select line of the system bus. The set of registers are showed in the following table:

| Address | Register name | Size [bit] | Direction |
| --- | --- | --- | --- |
| 0x8000 | MSEL_reg | 3 | read/write |
| 0x8001 | MDATA_reg | 13 | read |

Table 16: analog input registers

The MDATA_reg contains the 12-bit converted data and a "ready" flag (MSB) that indicates when the data is ready (active high).

By writing a multiplexer selection in the MSEL_reg, the multiplexer shall select the line to be converted and the control block shall manage the conversion, after a delay of about 15(s, for the stabilisation of the signal. When the conversion will finished (about 35(s conversion time), the "ready" bit of the MDATA_reg will assert and the converted value will be present in this register. After the reading, the MDATA_reg shall be reset by the control block of the FPGA.

The analog input #7 is reserved: a half scale voltage reference is connected to this input to provide a reference for the calibration phase.

## Control Logic

The control logic is implemented with an Actel RH 1280 FPGA (TBC); it manages all the peripherals and realises the interface between the system bus and the peripherals.

### Board registers

| Address | Register name | Size [bit] | Direction |
| --- | --- | --- | --- |
| 0x0 | Reset register | 32 | read/write |
| 0x1 | Status register | 32 | read |

Table 17: board registers

The reset register allows single peripheral resets (except for the control logic) and the global software reset (see paragraph 7.7). Each flag must be asserted (high) to generate a reset and it must be de-asserted (low) by another writing.

These flags are mapped, according to the following table:

| D15 | D14 | D13 | D12 | D11 | D10 | D9 | D8 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SW reset | Not Used | Not Used | Not Used | Not Used | Not Used | Not Used | Not Used | Not Used | Not Used | LSL reset | MIL1553 reset | FSDL3 reset | FSDL2 reset | FSDL1 reset | FSDL0 reset |

Table 18: Reset register

The Status register reports all the status of the peripherals, the following table shows the map of the register:

| D15 | D14 | D13 | D12 | D11 | D10 | D9 | D8 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ACQ3 | FF3 | HF3 | EF3 | ACQ2 | FF2 | HF2 | EF2 | ACQ1 | FF1 | HF1 | EF1 | ACQ0 | FF0 | HF0 | EF0 |

| D31 | D30 | D29 | D28 | D27 | D26 | D25 | D24 | D23 | D22 | D21 | D20 | D19 | D18 | D17 | D16 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Not Used | Not Used | Not Used | Not Used | Not Used | Not Used | Not Used | Not Used | Not Used | Not Used | Not Used | 1553 \INCMD | Ferr3 | Ferr2 | Ferr1 | Ferr0 |

Table 19: Status register

## Board Reset

Three possible actions can globally reset the board:

- power-on reset

- hardware reset  with the system reset line (\SYSRESETIN ) driven by the CPU board

- software reset, asserting the global reset bit in the reset register

When the CPU asserts the reset line (hardware reset) the whole board is reset (also the blocks of the FPGA control logic) whereas a software reset causes the reset of all the devices except for the control logic block.

### Power-on Reset

The board is equipped with a power-on reset network to clear all the circuits at power-on.

Picture 12: power-on reset network

## Latchup Protection

Due to the high level of latchup immunity of the selected components (>100MeV/mg cm2), no latchup protection is implemented on PL I/F board. Anyway, different supply sections are foreseen on the board itself, to increase flexibility of the current protection philosophy of the system. Actually, all the power supply sections are joined on the motherboard to supply the PL I/F board with single 5V, +15V -15V power lines.

# Electrical interfaces

All the interfaces FSDL, and LSL are in RS422 electrical standard format. The interfaces employ balanced differential line drivers and receivers, type 26C31, 26C32, to provide good common mode rejection and reasonable isolation characteristics. In the Picture 13 are shown the driving and receiving networks:

Picture 13: RS422 electrical interface

The parasitic capacitance of the 26C32 input lines (to ground) shall be <20pF, this restricts the length of the PCB traces between the input resistors and the 26C32 inputs.

All the data have to be transferred with the MSB first.

# Pin function

The pin function of the PL I/F board is shown in the Table 20 and Table 21.

| Pin # | Signal | Pin # | Signal | Pin # | Signal |
| --- | --- | --- | --- | --- | --- |
| 1 | +5VD | 33 | +5VD | 65 | +5VD |
| 2 | +VFIFO | 34 | +5VBU61582 | 66 | +VFPGA |
| 3 | D0 | 35 | D1 | 67 | D2 |
| 4 | D3 | 36 | D4 | 68 | D5 |
| 5 | D6 | 37 | D7 | 69 | D8 |
| 6 | D9 | 38 | D10 | 70 | D11 |
| 7 | D12 | 39 | D13 | 71 | D14 |
| 8 | D15 | 40 | D16 | 72 | D17 |
| 9 | D18 | 41 | D19 | 73 | D20 |
| 10 | D21 | 42 | D22 | 74 | D23 |
| 11 | D24 | 43 | D25 | 75 | D26 |
| 12 | D27 | 44 | D28 | 76 | D29 |
| 13 | D30 | 45 | D31 | 77 | \WR |
| 14 | A0 | 46 | A1 | 78 | A2 |
| 15 | A3 | 47 | A4 | 79 | A5 |
| 16 | A6 | 48 | A7 | 80 | A8 |
| 17 | DGND | 49 | SACK | 81 | DGND |
| 18 | A9 | 50 | A10 | 82 | A11 |
| 19 | A12 | 51 | A13 | 83 | A14 |
| 20 | A15 | 52 | A16 | 84 | A17 |
| 21 | A18 | 53 | A19 | 85 | A20 |
| 22 | A21 | 54 | A22 | 86 | A23 |
| 23 | \CS0 | 55 | \CS1 | 87 | \CS2 |
| 24 | \CS3 | 56 | \CS4 | 88 | \CS5 |
| 25 | RESERVED | 57 | \CS7 | 89 | \RD |
| 26 | IRQM3 | 58 | IRQM4 | 90 | IRQM5 |
| 27 | IRQM6 | 59 | IRQM7 | 91 | SYSCLK |
| 28 | \SYSRESETIN | 60 | RESERVED | 92 | SYSCLK |
| 29 | -15VA | 61 | -15VA | 93 | -15VA |
| 30 | AGND | 62 | AGND | 94 | AGND |
| 31 | +15VA | 63 | +15VA | 95 | +15VA |
| 32 | DGND | 64 | DGND | 96 | DGND |

Table 20 PL I/F board: P1 pin function

| Pin # | Signal | Pin # | Signal | Pin # | Signal |
| --- | --- | --- | --- | --- | --- |
| 1 | +5VD | 33 | RESERVED | 65 | +5VD |
| 2 | FCK0+ | 34 | FGATE0+ | 66 | FDATA0+ |
| 3 | FCK0- | 35 | FGATE0- | 67 | FDATA0- |
| 4 | FCK1+ | 36 | FGATE1+ | 68 | FDATA1+ |
| 5 | FCK1- | 37 | FGATE1- | 69 | FDATA1- |
| 6 | FCK2+ | 38 | FGATE2+ | 70 | FDATA2+ |
| 7 | FCK2- | 39 | FGATE2- | 71 | FDATA2- |
| 8 | FCK3+ | 40 | FGATE3+ | 72 | FDATA3+ |
| 9 | FCK3- | 41 | FGATE3- | 73 | FDATA3- |
| 10 | AINP0 | 42 | AINP1 | 74 | AINP2 |
| 11 | AGND | 43 | AGND | 75 | AGND |
| 12 | AINP3 | 44 | AINP4 | 76 | AINP5 |
| 13 | AGND | 45 | AGND | 77 | AGND |
| 14 | AINP6 | 46 | NOT USED | 78 | NOT USED |
| 15 | AGND | 47 | AGND | 79 | AGND |
| 16 | RTAD0 | 48 | RTAD2 | 80 | RTAD4 |
| 17 | RTAD1 | 49 | RTAD3 | 81 | RTADP |
| 18 | LCK0+ | 50 | LTX0+ | 82 | LRX0+ |
| 19 | LCK0- | 51 | LTX0- | 83 | LRX0- |
| 20 | LCK1+ | 52 | LTX1+ | 84 | LRX1+ |
| 21 | LCK1- | 53 | LTX1- | 85 | LRX1- |
| 22 | LCK2+ | 54 | LTX2+ | 86 | LRX2+ |
| 23 | LCK2- | 52 | LTX2- | 84 | LRX2- |
| 24 | LCK3+ | 53 | LTX3+ | 85 | NOT USED |
| 25 | LCK3- | 54 | LTX3- | 86 | NOT USED |
| 26 | LCK4+ | 58 | LTX4+ | 90 | SCTX/RXA+ |
| 27 | LCK4- | 59 | LTX4- | 91 | SCTX/RXA- |
| 28 | LCK5+ | 60 | LTX5+ | 92 | SCTX/RXB+ |
| 29 | LCK5- | 61 | LTX5- | 93 | SCTX/RXB- |
| 30 | LCK6+ | 62 | LTX6+ | 94 | NOT USED |
| 31 | LCK6- | 63 | LTX6- | 95 | FLAG1 |
| 32 | DGND | 64 | DGND | 96 | DGND |

Table 21 PL I/F board: P2 pin function

# Text boxes

LTX

LCK

LCK

LRx

LTx