| FAILURE MODES EFFECTS AND CRITICALITY ANALYSIS (FMECA) |
| --- |
| Product: SPIRE Instrument Project/Phase: Herschel System/Subsystem/Equipment: DPU Mission phase/Operational Mode: Space Flight | Prepared by: R. Orfei Approved by: Date: 11-07-‘01 | Document reference: SPIRE-IFS-DOC-000785 Issue: Page of |
| Id number | Item/ block | Function | Failure mode | Failure cause | Failure effects a. Local effects b. End effects | Severity | Failure detection method/ observable symptoms | Compensation provisions | Correction actions | Remarks |
| 1.001 | DPU |  | Input Power 28V short to Gnd | Connector failure | a. Loss of DPU b. Loss of nominal side, propagation of short to the source | 1R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE | Further analysis required. LCLs at the power source |
| 1.002 |  |  | No function | Manufacturing error, part failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.1.001 | DC/DC conv. Main |  | Shorted | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.1.002 |  |  | Open | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.1.003 |  |  | Erratic output | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.1.004 |  |  | No output | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.2.001 | CPU |  | Shorted | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.2.002 |  |  | Open | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.2.003 |  |  | Output stuck low | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.2.004 |  |  | Output stuck high | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.2.005 |  |  | Output open | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.2.006 |  |  | Input open | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.3.001 | 2 Serial I/F to/from DRU |  | Shorted | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | Corrupted HK data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.3.002 |  |  | Output stuck low | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | Corrupted HK data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.3.003 |  |  | Output stuck high | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | Corrupted HK data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.3.004 |  |  | Output open | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | Corrupted HK data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.3.005 |  |  | Input stuck low | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | Corrupted HK data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.3.006 |  |  | Input stuck high | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | Corrupted HK data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.3.007 |  |  | Input open | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | Corrupted HK data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.4.001 | Serial I/F to/from MCU |  | Shorted | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | Corrupted HK data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.4.002 |  |  | Output stuck low | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | Corrupted HK data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.4.003 |  |  | Output stuck high | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | Corrupted HK data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.4.004 |  |  | Output open | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | Corrupted HK data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.4.005 |  |  | Input stuck low | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | Corrupted HK data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.4.006 |  |  | Input stuck high | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | Corrupted HK data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.4.007 |  |  | Input open | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | Corrupted HK data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.5.001 | S/C I/F |  | Shorted | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.5.002 |  |  | Output stuck low | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.5.003 |  |  | Output stuck high | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.5.004 |  |  | Output open | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.5.005 |  |  | Input stuck low | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.5.006 |  |  | Input stuck high | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.5.007 |  |  | Input open | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.6.001 | Data RAM 2MB |  | Shorted | Internal failure | a. Loss of DPU b. Likely loss of nominal side | 2R | No housekeeping data from SPIRE | Depending on page failure remedial actions are possible | None in SPIRE |  |
| 1.6.002 |  |  | Open | Internal failure | a. Loss of DPU b. Likely loss of nominal side | 2R | No housekeeping data from SPIRE | Depending on page failure remedial actions are possible | None in SPIRE |  |
| 1.6.003 |  |  | Slow transfer of data | Internal failure | a. Loss of DPU b. Likely loss of nominal side | 2R | No housekeeping data from SPIRE | Depending on page failure remedial actions are possible | None in SPIRE |  |
| 1.6.004 |  |  | Bit loss | Internal failure | a. Loss of DPU b. Likely loss of nominal side | 2R | Corrupted data from SPIRE | Depending on page failure remedial actions are possible | None in SPIRE |  |
| 1.7.001 | Data EEPROM 1MB |  | Shorted | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.7.002 |  |  | Open | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.7.003 |  |  | Slow transfer of data | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.7.004 |  |  | Bit loss | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | Corrupted data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.8.001 | Program PROM 32kB |  | Shorted | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.8.002 |  |  | Open | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.8.003 |  |  | Slow transfer of data | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Switch to redundant side | None in SPIRE |  |
| 1.8.004 |  |  | Bit loss | Internal failure | a. Loss of DPU b. Loss of nominal side | 2R | No housekeeping data from SPIRE | Depending on Bit address the instrument could still perform nominally | None in SPIRE |  |
| 1.9.001 | Program RAM 3MB |  | Shorted | Internal failure | a. Loss of DPU b. Likely loss of nominal side | 2R | No housekeeping data from SPIRE | Depending on page failure remedial actions are possible | None in SPIRE |  |
| 1.9.002 |  |  | Open | Internal failure | a. Loss of DPU b. Likely loss of nominal side | 2R | No housekeeping data from SPIRE | Depending on page failure remedial actions are possible | None in SPIRE |  |
| 1.9.003 |  |  | Slow transfer of data | Internal failure | a. Loss of DPU b. Likely loss of nominal side | 2R | No housekeeping data from SPIRE | Depending on page failure remedial actions are possible | None in SPIRE |  |
| 1.9.004 |  |  | Bit loss | Internal failure | a. Loss of DPU b. Likely loss of nominal side | 2R | No housekeeping data from SPIRE | Depending on page failure remedial actions are possible | None in SPIRE |  |