SPIRE-IFS-NOT-001130

Note on SPIRE-DPU architecture

Prepared by:	Riccardo Cerulli-Irelli

Distribution List :

| K. King | SPIRE |  |
| --- | --- | --- |
| S.D. Sidher | SPIRE |  |
| J.L. Auguères | SPIRE |  |
| C. Cara | SPIRE |  |
| D. Ferrand | SPIRE |  |
| G. Olofsson | SPIRE |  |
| L. Seno | Audionica |  |
| M. Giordano | Audionica |  |
| R. Orfei | IFSI |  |
| A. Di Giorgio | IFSI |  |
| S. Molinari | IFSI |  |
| S. Pezzuto | IFSI |  |
| S. Codella | IFSI |  |
| S. J. Liu | IFSI |  |

Document Status Sheet:

| Document Title: |
| --- |
| Issue | Revision | Date | Reason for Change |
| Draft 3 |  | 26/09/01 | Added Tuning task. Added generalized table uploading protocol |
| Draft 3.1 |  | 7/10/01 | VM code updated Added in Appendix an example on VM code |
| Draft 3.2 |  |  | Chapter formatting Chapter 3.1 expanded Chapter 3.4 initiated Chapter 3.4 – introduced minimum time between SS commands Chapter 3.5 expanded Appendix – Reason for a Virtual Machine |
| Draft 3.3 |  | 21/01/02 | Chapter 3.4 Introduction of a VM optimising compiler and simulator. |
| Draft 3.4 |  | 23/01/02 | Paragraph 3.4.1 Corrected VM code Introduced paragraph 3.4.2 and3.4.3 for Compiler/Simulator |

# Reference documents

| Document Reference | Title |
| --- | --- |

Acronyms

| CDMS | Central Data Management System |
| --- | --- |
| CNR | Consiglio Nazionale delle Ricerche |
| CPU | Control Processing Unit |
| DCU | Detector Control Unit |
| DPU | Digital Processing Unit |
| DRU | Detector Readout Unit |
| FIFO | First In First Out storage element |
| FIRST | Far InfraRed and Submillimeter Telescope |
| HK | HouseKeeping |
| HW | HardWare |
| I/F | Interface |
| IFSI | Istituto di Fisica dello Spazio Interplanetario |
| ISR | Interrupt Service Routine |
| LSB | Least Significant Bit(s) |
| MCU | Mechanism Control Unit |
| MSB | Most Significant Bit(s) |
| mutex | Mutual Exclusive flag |
| NA | Not Applicable |
| OBS | On-Board Software |
| OS | Operating System |
| PC | Program Counter |
| PDU | Power Distribution Unit |
| S/C | Spacecraft |
| SPIRE | Spectral and Photometric Imaging REceiver |
| SS | Subsystem |
| SW | SoftWare |
| TBC | To Be Confirmed |
| TBD | To Be Defined |
| TBW | To Be Written |
| TC | Telecommand |
| TM | Telemetry |
| VM | Virtual Machine |

# Table of contents

Reference documents	3

Table of contents	5

1	Introduction	6

2	Subsystem commanding description	6

2.1	CMD_SEQ_Task	7

2.2	HK_REQ_Task	7

2.3	LS_Task	7

2.4	ISR_3_Task	8

2.5	HS_Task	8

2.6	TMTC_Task	10

2.7	IDLE_Task	10

3	Detailed tasks description	11

3.1	CMD_SEQ_Task	11

3.1.1	On Board Tables	11

3.1.2	DPU Internal Commands	12

3.2	HK_REQ_Task	13

3.3	LS_Task	14

3.4	ISR_3_Task	15

3.4.1	Virtual Machine instructions	15

3.4.2	VM Compiler	18

3.4.3	VM Simulator	19

3.5	HS_Task	20

3.6	TMTC_Task	23

3.7	IDLE_Task	23

Appendix	24

Reason for a Virtual Machine	24

Sample VM code	26

# Introduction

This note tries to present in an informal format the status of SPIRE DPU OBS architecture.

The note will eventually be translate in the right format and included in the SSD as the “DPU Architecture Description”.

# Subsystem commanding description

With reference to the following figure, here is a description of the identified tasks.

As far as this note is concerned, a task is an infinite repeating program scheduled by some kind of signal, which suspends itself at the end. A new signal will re-schedule the task.

## CMD_SEQ_Task

This task is scheduled in the run queue by a semaphore set by the TMTC_Task, signalling the presence of telecommands. When the task gets the CPU attention, the incoming telecommands are controlled (a TC verification report is generated), exploded in elementary commands and executed/stored. The task, after that, suspends itself until the next semaphore signal.

At this stage there are two are main cathegories of commands:

- CPU internal commands.

- S/S commands.

The DPU internal commands are immediately executed inside the task.

S/S commands are stored in the Low Speed I/F command buffer, a semaphore signal is generated in order to put in the run queue the LS_Task  which is in charge of the actual transmission.

Optionally a second highest priority Low Speed I/F command buffer2 can be added in order to cope with immediate commands.

## HK_REQ_Task

The HK_Req_Task handles the periodic HK request. The OS periodically schedules the task in the running queue. This task just reads a table of SS elementary commands, writes the commands on the Low Speed I/F command buffer and sends a signal (increments semaphore counts) to the LS_Task .

The scheduling period of the task is set, enabled/disabled by DPU internal commands.

HK received from the SS on the low speed I/F together with those received via the high speed I/F, are stored and packetized in a circular data buffer as shown for the HS_Task

## LS_Task

The LS_Task  (together with the ISR_3_Task) is in charge of transmitting and possibly receiving commands/housekeeping to/from the subsystems. The actual timing of the commands transmission with this task is not predicable due to the multitasking nature of the OS; a jitter of few milliseconds must be taken in account.

The task, scheduled by HK_REQ_Task and CMD_SEQ_Task, checks the command against a fixed table for special cases (flush FIFO/sync etc), checks for the availability (mutex lock) of the low speed I/F port (might be used by ISR_3_Task) and if not available suspends itself until the port is no more busy. The task then writes on the output port the SS command and suspend itself for 1 ms (HIFI 2 ms if it’s an HK request) to allow the 100 us transmission time and possibly the HK response word with allowed time-out. If an HK is expected/received, the HK is stored in the TM HK buffer and formatted for TM transmission.

## ISR_3_Task

This task allows the transmission of commands to the SS at a fixed time with a maximum jitter of 10us (TBC). The task, interrupt driven, is started (and possibly terminated) by an DPU internal command which enable/disable the highest priority interrupt (Irq 3) driven by a 1 MHz clocked HW timer.

The tasks read from a preloaded table (exec_table) the time to the next command and the command to transmit, it then set the timer and transmits the command to the SS.

In order to avoid collision on the low speed I/F with the LS_Task, a special (internal) command is foreseen to lock/unlock (via a mutex) the low speed I/F. The locking command will precede the SS commands of at least 100 us in order to allow the possible contemporary (just started) transmission of a command via the LS_Task.

## HS_Task

This task collects science and HK data on the high speed I/F, format the data in “packet transmission ready” and stores the data in the right buffer.

The data on the high speed I/F are temporary stored on four 8Kword deep FIFOs, the “half FIFO full” signal associated to each FIFO generates an interrupt (IRQ 0) which in turn schedules the HS_Task on the run queue.

The main point here is that, due to the asynchronous operation of the FIFOs, the actual timing of the incoming data is lost, in other words no cause/effect between commands (on low speed I/F) and received data (on high speed I/F) is possible, at least in a simple efficient and reliable way.

## TMTC_Task

This task checks on the 3 record descriptor buffers if any Event/Report, HK or science TM packet (in this sequence) is ready for transmission, and transmit the packets at S/C generated (64 per seconds) interrupts. The same task signals to the CMD_SEQ_Task the possible presence of a TC.

## IDLE_Task

This low priority task is executed when no other task is active. The time spent inside this task is an indication of the load charge of the DPU/SPU.

# Detailed tasks description

## CMD_SEQ_Task

This task begins the execution on arrival of a TC packet signalled by the TMTC_Task. The first operation is the TC verification (RD1 3.1) with the generation of the acceptance report TM packet stored in the highest priority (Event/Report) buffer.

The received TC packets can be subdivided in 2 categories:

- DPU commands to update on board tables

- DPU internal commands

### On Board Tables

The SPIRE instrument will be completely controlled by a set of preloaded and TC modifiable 32 bit words tables. The tables fully control the SS configuration and observation modes, and are stored in data memory in contiguous locations in order to simplify a possible relocation.

A preliminary list of tables include:

- SS configuration tables

- VM programs

As a general rule, consecutive selected data (commands) from the configuration tables will be sent to the SS via the LS_Task, VM programs will be transmitted/interpreted in a timely ordered sequence by means of the ISR3_Task. The DPU uses observation parameters internally.

A unified generalized protocol to update the various tables is foreseen.

Each updating block of data will contain a 4-byte header followed by the relevant data

| Len | Field | Description |
| --- | --- | --- |
| 8 | Table number (ID) | Configuration, observation, VM prog….. etc |
| 8 | N. of data items which follows |  |
| 4 | Type of data | 0=8 bit , 1=16, 2=24, 3=32 bit |
| 12 | Offset from beginning of the table | 0=8 bit , 1=16, 2=24, 3=32 bit |
| 8..32 | Data | 8,16,24 or 32 bit words as defined above |
|  | … |  |
|  | Data |  |

If data type is 0 (8 bit items) an even number of data must follow.

Depending on the table number some different block header or implicit rule might be used, an example is an implied 16 bit left shift for HK request commands (stored on DPU as 32 bit words with the 16 LSB all ‘1’).

A type 8 “function management” is foreseen with one or more data blocks as above.

This generalized method has the advantage to permit whatever reconfiguration might be needed from the ground, besides being extremely simple as OBS implementation. The TC bandwidth should be reduced due to the possibility to upload only part of the relevant tables.

### DPU Internal Commands

This set of commands, fixes the operating mode of the DPU and are in general responsible for setting the SS configuration and executing the observation.

The internal commands may be divided in three categories:

- Instrument specific commands

- Observation parameters (# of data blocks to transmit etc)

- System commands

A preliminary set of DPU internal instrument specific commands follows:

| Mnemonic | Parameters | Description |
| --- | --- | --- |
| Run | Addr | Runs VM program beginning at address (index) Addr. (ISR_3_Task) |
| Stop |  | Halt the current running VM program |
| TblLoad | Tbl#, Addr, N | Transmits to SS via the LS_Task the N 32 bit words (commands) of table Tbl#, beginning at address (index) Addr |
| TblDump | Tbl#, Addr, N | Transmits in TM the N 32 bit words of table Tbl#, beginning at address (index) Addr |
| FifoFlush | N | Flushs FIFO number N [1 … 3]. If N=0 flush all |
| Sync |  | Sends broadcast DPU time to SS |
| Exec | P1,P2 … Pn | Executes some specialized function/Task, which need an “hard coded” function as for the tuning procedure. (TUNING_Task) |

The preliminary lists of DPU internal system commands follows:

- Time sync commands: The time received by the S/C is compared with the DPU internal clock and a constant offset is generated. The deviation of ICT time from the S/C time will be of the order of a ms.

- Housekeeping transmission rate: The rate sets the execution period of the HK_REQ_Task

- HK enable/disable

## HK_REQ_Task

## LS_Task

This task sends commands and HK requests to the SS via the low speed serial I/F.

Commands and HK requests written to the out buffer (Tx) are sent to all the SS, the address field of an HK request set the multiplexer (Mux) to the addressed SS in order to receive the requested HK on the input buffer (Rx).

## ISR_3_Task

The ISR_3_Task is actually a Virtual Machine executing one group of instructions (coded in the Exec_table) per each INT3 request. The Exec_Table is actually a one column 32 bit word vector containing commands to SS, timer setting (int3), mutex, loop and other Virtual Machine “assembler” instruction, operating as an absolute program.

A number of baseline VM programs, with functionality for the foreseen observation modes, will be stored on the DPU/DPU. These programs, stored in a fixed memory location, will be modified/reloaded via TC, thus easing the need for OBS patching. A program can be as simple as a loop calling a preloaded subroutine.

VM Program

For each INT3 request, the block of instructions from the current VM program counter (PC - index vector value) up to (excluding) the next SS command or mutex or NOP instruction, are executed. A set of VM internal registers R[32] TBC, are foreseen in order to execute loop, to pass parameters with subroutine etc. Each register is a 32 bit unsigned integer.

### Virtual Machine instructions

A preliminary set of  “VM assembler” instructions follows:

| Instr. code (hex) | VM asm Mnemonic | Description | Code type |
| --- | --- | --- | --- |
| (7) | CMD | Send_Command(addr, code, val) Send command code/val to SS addr |  |
| 0 | RCMD | Send_Command_Reg(addr, code, reg)1 Send command code/R[reg] to SS addr | 3 |
| 1 | MTX | Mutex(OnOff) Lock/Unlock low speed I/F port | 1 |
| 2 | NOP | NOP() No operation | 1 |
| 8 | TIM | Set_Timer(val) Set counter value (us) for next IRQ3 | 1 |
| A | READ | Read_HK_Reg(reg) Store received HK in R[reg] |  |
| 10 | RINC | Increment_Register(reg) R[reg] = R[reg] + 1 | 1 |
| 11 | RDEC | Decrement_Register(reg) R[reg] = R[reg] - 1 | 1 |
| 12 | RSET | Set_Register(reg, val32) R[reg] = val32 | 14 |
| 13 | RADD | Add_To_Reg(reg, va32l)4 R[reg] = R[reg] + val32 | 14 |
| 14 | RSUB | Sub_To_Reg(reg, val32)4 R[reg] = R[reg] – val32 | 14 |
| 15 | RAND | And(reg, val32)4 R[reg] = R[reg] & val32 | 14 |
| 16 | ROR | OR(reg, val32)4 R[reg] = R[reg] ¦ val32 | 14 |
| 17 | RREQ | Reg_Equate(reg1,reg2) R[reg1] = R[reg2] | 2 |
| 21 | JMPR | Jmp_Relative(vmAddr) PC = PC + vmAddr | 1 |
| 23 | RJPR | Jmp_Relative_Reg(reg) PC = PC + R[reg] | 1 |
| 25 | JPNZ | JumpNZ(reg, vmAddr) If (R[reg] !=0) PC = PC + vmAddr | 2 |
| 26 | RSZ | Skip_Reg_Zero(reg) If (R[reg] ==0) PC = PC + 1 | 1 |
| 27 | RSGT | Skip_Reg_GT(reg1,reg2) If (R[reg1] > R[reg2]) PC = PC + 1 | 2 |
| 28 | RSLT | Skip_Reg_LT(reg1,reg2) If (R[reg1] < R[reg2]) PC = PC + 1 | 2 |
| 30 | CALL | Call_Subr(vmAddr) PC = vmAddr (remember the present PC) | 1 |
| 31 | RET | Return() Return from subroutine | 1 |
| 41 | WRT | Write(reg) Write R[reg] to ICU frame | 1 |
| 50 | END | End End current VM program | 1 |
|  | DEF | Set constants |  |
|  | ORG | Address of code |  |
|  | _Label | Label referred by loop/jmp |  |
|  | COM | COM textstring Comment printed during the simulation |  |

It has to be noted that in order to make the VM program as relocable as possible, all jump instructions, with the exclusion of the Call Sub, are relative to the PC.

The table notation is:

Val	16 or 24 bit numeric constant possibly defined in a DEF statement.

Reg	VM internal registers index. Numeric constant between 0 and 31 possibly defined in a DEF statement.

VmAddr	Signed 16 bit numeric constant indicating the relative address displacement in a Jump instruction. It may be coded as a _label mnemonic, in this case the relative address displacement is computed by the compiler.

The preliminary instruction coding is as follows:

- First (MSB) bit=1 then it is a plain command to the SS, as the first bit (start bit) is always set.
Here we assume that the data content of the command can be splitted in two fields (code and value). The MSBit of addr field indicate cmd/hk request.

- First (MSB) bit=0 then it is a coded 32 bit instruction with:

Type 1

Type 2

Type 3

A VM assembler compiler/simulator program is provided in order to simplify the on ground coding of the observation programs.

### VM Compiler

The compiler resolve all the mnemonic labels and constant in a VM program and produce the absolute VM code. The compiler optimiser try also to take care of the MTX instructions which enable/disable the low speed I/F usage by the LS_Task.

The compiler run time arguments are:

| Switch | Description | Default value |
| --- | --- | --- |
| o0, o1, o2 | Different levels of optimisation | o0 = No optimisation |
| v0, v1, v2, v3 | Verbose level for terminal display | v0 = minimum display |
| prg filename | VM program input file | prg spire.vm |
| lst filename | Compiler/Simulator output filename | lst list.txt |
| t1 n | Start time for the simulation display [us] | t1 0 |
| t2 n | End time for the simulation display [us] | t2 100000000 |
| pc n | Address (program counter) of the program entry point | pc 0 |

The compiler optimisation level 1, check for a TIM instruction and, based on a threshold value (10 ms), test/insert a correct MTX instruction using the following criteria:

If TIM > threshold and last MTX=1

Then check/insert MTX=0

If TIM < threshold and last MTX=0

Then check/insert MTX=1

The compiler optimisation level 2, add to the level 1 optimisation a check for any “unprotected” (MTX=0) CMD/RCMD instruction, and protect the command with a double TIM-MTX couple using the following criteria:

If exist a CMD/RCMD instruction while MTX=0 and TIM=oldtim

Then modify to:

TIM 2000	(1 ms is chosen as the minimum TIM value)

MTX 1

CMD/RCMD xxx  (original instruction)

TIM oldtim

MTX 0

The TIM-MTX instructions inserted by the optimiser are prefixed by A_

Example:

| No optimisation | Optimisation level 1 | Optimisation level 2 |
| --- | --- | --- |
| MTX 0 | MTX 0 | MTX 0 |
| … | … | … |
| TIM 1000 | TIM 1000 | TIM 1000 |
| CMD aaa | A_MTX 1 | A_MTX 1 |
| CMD bbb | CMD aaa | CMD aaa |
| CMD ccc | CMD bbb | CMD bbb |
| TIM 100000 | CMD ccc | CMD ccc |
| TIM 1000 | TIM 100000 | TIM 100000 |
| CMD ddd | A_MTX 0 | A_MTX 0 |
| … | TIM 1000 | TIM 1000 |
| … | A_MTX 1 | A_MTX 1 |
| … | CMD ddd | CMD ddd |
| … | … | … |
| MTX 1 | MTX 1 | MTX 1 |
| … | … | … |
| TIM 110000 | TIM 110000 | TIM 110000 |
| CMD xxx | A_MTX 0 | A_MTX 0 |
| TIM 1000 | CMD xxx | A_TIM 2000 |
| CMD aaa | TIM 1000 | A_MTX 1 |
| CMD bbb | A_MTX 1 | CMD xxx |
| … |  | A_TIM 110000 |
|  |  | A_MTX 0 |
|  |  | TIM 1000 |
|  |  | MTX 1 |

### VM Simulator

The simulator section of the compiler program, is a modified version of the OBS VM section, the simulator control any “unprotected” CMD/RCMD instruction and output (on the out list file) a timeline of the SS commands. Comment instructions:

COM comment string

inserted in the input program, are listed by the simulator as:

COM comment string [addr,n]

with addr = address of the next istruction

n = auto incrementing number counting # of comment occurrence.

In the appendix a test program compilation/simulation is provided.

## HS_Task

This task collect science and HK data on the high speed I/F, format the data in “packet transmission ready” and store the data on the right buffer.

In order to allow asynchronous collection of science, the 16 bit data words on the high speed I/F are temporary stored on four 8Kword deep FIFOs, at a rate of 16 us per word.

The “half FIFO full” signal associated to each FIFO generate an interrupt (IRQ 0) which in turn schedule the HS_Task (through a Virtuoso event) on the run queue.

Data coming from FIFOs must be organized in frames, each frame consisting of a header (stripped before transmission) followed by data.

The header must contains at least the number of words which follows and the ID of the frame.

Each frame is stored in a separate circular buffer depending on the frame ID.

Some frames might contain HK data, the HK will overwrite the appropriate locations of the SPIRE common HK current buffer.

The presence of a TM data packet ready for transmission is signalled by a new entry (of type RecDesStru) in the science record descriptor buffer.

## TMTC_Task

## IDLE_Task

# Appendix

## Reason for a Virtual Machine

The driving requirement for the VM is the time sequence constraint between SS commands during an observation. The time sequence jitter on the SS commands (LS I/F) goes from seconds down to 10us.

Consider the following example:

Cmd1		@ T

Cmd2		@ T + t1 +-5ms = T2

Cmd3		@ T2 + t2 +- 100ms = T3

Cmd4		@ T3 + t3 +- 5us = T4

It is clear that, in a multi-task OS as Virtuoso, the only way to achieve the 10us and probably the 10 ms constraint is via an Interrupt Serviced Routine (with a high priority interrupt). It is also evident that once it has been decided to implement the interrupt environment, every command in the sequence should be sent via interrupt, so that all the commands will have the same (10 us) jitter in the time sequence.

The HW problem to generate the sequence of different period interrupts, is solved by using the DPU programmable 32 bit (1 MHz clock) down counter. This down counter starts decrementing its content from the last preset initial value, and generates an interrupt on zero value. Then the counter restarts again the cycle, beginning from the last preset initial value loaded before the zero count.

Now we have a mechanism, which forces the execution of a routine (ISR_3) at pre-defined time intervals. Entering the routine, the relevant SS command must be sent. In order to preserve the time jitter constraint, this command must be already prepared (in a table).

After the command is sent (written in the low speed serial output I/F), we might want to change the down counter initial count for the next interrupt, the only time constraint now is to exit from the ISR before the present terminal count. This new “initial count” value will be stored in some table, let’s say we store this value in the same table with the command sequence.

We can build a table as a sequence of two words: command and initial count, and perform always the same two operations inside the ISR:

- Increment the table pointer and send the command stored at the current table location

- Increment the table pointer and preset the initial count stored at the current table location

This scheme is not the most efficient in the case when a series of commands can be equally spaced in time and use the same initial count with no need to rewrite it. Moreover we have to disable/enable the LS_Task, depending on the interval time between the SS observation commands (HK are collected via LS_Task), as an example we might decide that every time the delay between two commands is grater than 10ms we want to enable LS_Task. So we have to build a table that is interpreted inside the ISR: every time an interrupt occurs a number of actions (table instructions beginning at the current pointer) is performed, the first one (time critical) being a command to SS and the following being some type of DPU internal commands.

Now we have come to a long table containing all the SS and DPU observation commands already somehow interpreted by an OBS routine (ISR_3). The first thing to note is that the commands are repeated in block as in a computer loop, so why not to add an DPU internal loop command to the table? Well to do so we must also define some local variable (register R[32]), then we could add other simple features like subroutine etc.

Ok we have come to a Virtual Machine implemented inside the ISR_3 routine.

## Sample VM code

The following VM program (file name spire.vm)  has been compiled with the command:

compiler o2  v1

;------------------------------------

; Case insensitive

; Comments begin with a ;

; Labels begin with a _ and are alone in a line

;------------------------------------

def timF 2000		; Fast command sequence (2 ms)

def timS 100000		; Slow command sequence (100 ms)

def CmdDCU 4		; Address for DCU commands

def CmdMCU 5		; Address for MCU commands

def CmdSCU 6		; Address for SCU commands

def CmdBRC 7		; Address for Broadcast commands

def HkDCU  0		; Address for DCU commands

def HkMCU  1		; Address for MCU commands

def HkSCU  2		; Address for SCU commands

def r0val 0xa		; constants in dec or hex

TIM	timS			; the optimiser 01 switch insert a MXT

RSET	0,r0val		; R[0]=0xa

; here the optimiser o2 switch take care of

; the TIM/MTX for the next two commands

rcmd 4,0xfff,0		; command to addr 0 (MSbit of addr is cmd/hk)

cmd  5,0x55,0xffff	; command to addr 1 (MSbit of addr is cmd/hk)

RSET 0,5

RSET 1, 10

TIM timF

COM Calling _hksum with R[0]=5 and R[1]=10 ; comment line for the simulator

call _hksub			; in the sub loop 6 times

RSET 0, 15

COM Calling _hksum with R[0]=15 and R[1]=10

call _hksub			; in the sub loop 10 times (R[1] limit reached)

END

;--------------------------------------------------------------------

; This loop is executed until the received hk (in the simulator

; is equal to R[31]) is greater than R[0], up to a maximum of R[1]

; times. The received hk in the simulator is R[31], this value is

; simply incremented.

; Local variable R[3] and R[2]

;--------------------------------------------------------------------

ORG 100

_hkSub

Com This is a comment for the simulator

RSET 31,0			; Simulator specific

RREQ 3,1			; save max loop count in local var R[3]

_hkloop

rcmd  HkSCU,0x123,31	; HK req to addr SCU

;(MSbit of addr is cmd/hk)

nop				; must wait at least 2 ms (timF)

; to have the hk reply

TIM	timS			; the optimiser insert a MXT

rinc 31			; increment R[31]: simulator specific

read 2			; HK (R[31] in the simulator) in R[2]

TIM	timF			; the optimiser insert a MXT

RDEC	3			; check for max loop

JPNZ	3, 2			; skip if R[3] !=0

RET

rsgt 2,0			; loop untill hk (R[2]=R[31]) <= R[0]

jmpr _hkloop		; next loop

RET

Here follows the Compiler /Simulator output stored in the default list file “list.txt”.

Note the A_TIM and A_MTX instructions inserted by the optimizer.

VM program file spire.vm

Optimisation level= 2

Start address (PC)= 0

Addr   opCode     Instruction

----  --------  ---------------------

0            def    timF 2000

0            def    timS 100000

0            def    CmdDCU 4

0            def    CmdMCU 5

0            def    CmdSCU 6

0            def    CmdBRC 7

0            def    HkDCU 0

0            def    HkMCU 1

0            def    HkSCU 2

0            def    r0val 0xa

0   80186a0  TIM    timS

1  12000000  RSET   0    r0val

2         a         r0val

3   80007d0  A_TIM  2000

4   1000001  A_MTX  1

5    4fff00  rcmd   4    0xfff 0

6   80186a0  A_TIM  100000

7   1000000  A_MTX  0

8   80007d0  A_TIM  2000

9   1000001  A_MTX  1

10  d055ffff  cmd    5    0x55 0xffff

11   80186a0  A_TIM  100000

12   1000000  A_MTX  0

13  12000000  RSET   0    5

14         5         5

15  12000001  RSET   1    10

16         a         10

17   80007d0  TIM    timF

18   1000001  A_MTX  1

19            Calling _hksum with R[0]=5 and R[1]=10

19  30000064  call   _hksub

20  12000000  RSET   0    15

21         f         15

22            Calling _hksum with R[0]=15 and R[1]=10

22  30000064  call   _hksub

23  50000000  END

100            ORG    100

100            _hkSub

100            This is a comment for the simulator

100  1200001f  RSET   31   0

101         0         0

102  17030001  RREQ   3    1

103            _hkloop

103    21231f  rcmd   HkSCU 0x123 31

104   2000000  nop

105   80186a0  TIM    timS

106   1000000  A_MTX  0

107  1000001f  rinc   31

108   a000002  read   2

109   80007d0  TIM    timF

110   1000001  A_MTX  1

111  11000003  RDEC   3

112  25030002  JPNZ   3    2

113  31000000  RET

114  27020000  rsgt   2    0

115  21fffff4  jmpr   _hkloop

116  31000000  RET

Begin simulation from t1= 0  up to t2= 100000000

Time    PC   Command

2000     5  cfff000a

106000    10  d055ffff

Calling _hksum with R[0]=5 and R[1]=10  [19, 1]

This is a comment for the simulator [100, 1]

210000   103  a1230000

316000   103  a1230001

422000   103  a1230002

528000   103  a1230003

634000   103  a1230004

740000   103  a1230005

Calling _hksum with R[0]=15 and R[1]=10  [22, 1]

This is a comment for the simulator [100, 2]

846000   103  a1230000

952000   103  a1230001

1058000   103  a1230002

1164000   103  a1230003

1270000   103  a1230004

1376000   103  a1230005

1482000   103  a1230006

1588000   103  a1230007

1694000   103  a1230008

1800000   103  a1230009

Found END. Normal end of execution

Simulation: total No of errors: 0

# Footnotes

Assuming all commands can be divided in 3 fields. If this is not the case “code” disappears.

May be forced in the program, but the compiler insert automatically this instruction whenever is needed based on the optimisation level.

This time is the interrupt period valid after the next instruction. The minimum interrupt period is the maximum value between the time used by the I/F to transmit a command (100 us) and the actual duration of the ISR3. For the time being let’s fix it to 1 ms. This period is the minimum period between two SS commands

These instructions are coded as two consecutive 32 bit words, the second containing the plain value of “val32”.

# Text boxes

TM
Event/report buffer

…

Telemetry HK buffer

Interrupt Manager

Half Full FIFO # 2

Half Full FIFO # 1

not used)

High

Interrupt Priority

Irq 3

Irq 2

Irq 0

DSP

Half Full FIFO # 3

TC - TM

1553 SC I/F

1 MHz clk

Timer
(32bit)

…

…

100

Send_Command_Reg(addr,cod,reg)

101

….

102

…

Low

TM HK buffer

Irq 1

Telemetry data buffers

CircBfStru

TM event/report buffer

Min               PRIORITY             Max

TM
Science buffer

HK monitoring for autonomous functions

IDLE_Task

TC buffer

Signal 
CMD-SEQ_Task

Check TM buffers for ready to send packets

Fill TC buffer, and signal CMD-SEQ_Task (to command Seq,)

TMTC_Task

IRQ2

Sub-frame interrupt

A tasks is a program scheduled by some kind of signal, which suspend itself at the end

IRQ3

Timer

TM science buffer

HS_Task

Move data to TM & HK buffers

LS_Task 
Signal

LS_Task

Tx
suspend
Rx

Signal LS_Task or TUNING_Task

Signal LS_Task

Execute VM code:

Set next INT delay
Tx-Rx cmd
Enable/Disable LS_Task]
Loop

Low Speed I/F command buffer

1 sec OS event

CMD-SEQ_Task

Signal

IRQ0

FIFO half full

ISR_3_Task

Timely commands
(Virtual Machine)

HK_REQ_Task

Periodic HK request

CMD-SEQ_Task

Command Sequencer
&
Controller

Record descriptor buffer

N words

Frame ID1

Data

Data

…

Data

n

1

Telemetry data buffers

N words

Frame ID n

Data

Data

…

Data

TM
HK buffer

103

Return

…

…

…

…

4

Call_Subr(100)

3

…

2

Mutex(1)

1

Set_Timer(1)

0

Instructions

PC

Subroutine 100