# Flex Pivot Options

### SPIRE BSM Discussion document - Ian Pain. 22.Aug.01

The Baseline flex pivot choice identified at DDR is technically acceptable but costs exceed the original budget estimate.

From Lucas TRW the baseline price for 18 pivots x two types, the total order cost would be ~£94.5k Adding in minimum spares (for a total buy of 20 of each type) would bring the total to £97k. This represents an over-run of £84k on the £13k budgeted for flex pivots.  Because of other savings in the BSM programme, the available budget for flex pivots is however, now £30k. i.e Costs above £30k will require savings elsewhere to stay within total cost.

Note that there is a complication between ability to run at higher power dissipation and motor choice. If MPIA/PACS/Zeiss select a Copper winding rather than the originally baselined Aluminium, the increase in dissipation is significant (about a factor of 5). Based on discussions with MPIA and UK motor winders, we should consider Copper the baseline until confirmed by Zeiss (late-mid'02). Thus motor availability constrains flex pivot choice.

## Description of Options

Greyed out areas are not favoured/possible. Notes referenced in roman numerals.

| Flex Pivot Option | Description | Cost | Power - Aluminium coil | Power - Copper coil | Comments |
| --- | --- | --- | --- | --- | --- |
| Budget | Original assumption. | £13k | 4mW | Assumption of £13k was optimistic. |
| Baseline | Inconel flex pivots. Two types (chop and jiggle). | £97k (*) | 1.3mW (iv) | 3.2mW (iii) | Based on Lucas TRW quote (ii). VAT & import duty not included - waiver would be required |
| Joint procurement of baseline design | As 2, but joint procurement with another agency such as SRON, | £53-63k | 1.3mW (iv) | 3.2mW (iii) | Unlikely £17-22k saving per pivot type by sharing tooling and material price pro-rata. But SRON only interested in jiggle type: maybe ask LAM to procure back-ups too? (unlikely) |
| 304 stainless | As 2, but use austenitic stainless steel. | £91.7k | 1.3mW (iv) | 3.2mW (iii) | Saves £1.4k per type of flex pivot. Possible better fatigue life but reduced strength (TBC). Not favoured, as if having specials made may as well get the best. |
| 429 stainless | Uses off the shelf pivots but need to upscreen, and schedule extra vibration tests | £34.2k | 1.3mW (iv) | 3.2mW (iii) | risk of failure on cold vibration Assume upscreen by buying 4 x requirements (20 pivots x 3 @ £70) and doing 2 x extra warm vibration tests (@£2k); 2 x extra cold vibration tests (@£10k/test) with 20 extra days work (@£300/day). |
| Material brokerage | As 2 but assume we Could sell material to a third party broker, the original supplier or e.g. RAL | £68.9k | 1.3mW (iv) | 3.2mW (iii) | Unlikely £12.8k saving per pivot type. Sell on of material may not work (or run into tax and duty issues) |
| ESA procurement? | Ask ESA procure the pivots for us | Nominal £13k | 1.3mW (iv) | 3.2mW (iii) | Assumed impossible would be ideal if we could do it. |
| Common Jiggle Pivot | switch to a single pivot type, 7010-600 | £58.8k | 11.8mW (v) | 55mW (v) | Cannot use this as baseline as requires Al. Windings Saves £35.7k on material & tooling. Risetime may be compromised if motor saturates |
| Common Chop Pivot | switch to a single pivot type, 7010-800 | £73.8k | 1.0mW (vi) | 1.7mW (vi) | Requires major lightweight of jiggle frame or waiver on load (by >65%) Saves £35k less say £20k for re-engineering & increased manufacture costs |
| Hybrid soultion | Procure Inconel Jiggle pivot in common with SRON 7010-600. But use a stainless steel pivot for chop axis. | £41.5k | 1.1mW (ix) | 2.0mW (ix) | Risk of problems with stainless steel chop pivot. Late stage de-scope to option 11 Saves £17k on shared material for inconel pivot. Cost of stainless is half of option 5. |
| Baseline chop, shared procurement on jiggle | Procure Inconel Jiggle pivot in common with SRON 7010-600. Buy our own inconel chop pivot | £75-80k | 1.1mW (ix) | 2.0mW (ix) | Requires 85% lightweight of jiggle frame Saves £17-22k on shared material |
| Common intermediate pivot | intermediate stiffness pivot to BSM specification compromise between the two. (eg Use SRON 7010-600 as example) | £72.8k | 3.6mW (vii) | 14.5mW (vii) | Would make any light-weighting or power budget problems a trade-off. The 7010-600 needs a lightweighting of the jiggle frame of 85% (possible). Saves $35k less £10k for engineering costs. Risetime may be compromised if motor saturates |
| BE Systems Pivot. 0.15mm blade | identical to SMEC pivots or a slightly lighter flexure | £55k | 1.4mW (viii) | 3.9mW (viii) | Cost approx. £1k per pivot x 40 . As unit is 2mm bigger, need to re-engineer chop & jiggle stage, motor mounts and BSMs (say £15k including redesign & new prototype m/c). |
| Spark Eroded Pivot | Special pivot, maybe developed by Zeiss | ? |  | ? | Cost as option 13, plus 'Zeiss' factor |
| Smiths Industries Pivots | Maraging Steel Pivot per Smiths Industries | ? | ~4mW | ~2mW | Would be a aerospace rated part. Cost and power budget assumed same as 11. Maraging should be OK cold (but is SCC 'C' rated) |

## Comparison of favoured options

Ideal cost target is £30k.

| Flex Pivot Option | Description | Cost | Power - Aluminium coil | Power - Copper coil | Risks |
| --- | --- | --- | --- | --- | --- |
| Baseline | Inconel flex pivots. Two types (chop and jiggle). | £97k (*) | 1.3mW | 3.2mW | VAT & import duty |
| Baseline chop, shared procurement on jiggle | Procure Inconel Jiggle pivot in common with SRON 7010-600. Buy our own inconel chop pivot | £75-80k | 1.1mW | 2.0mW | Requires 85% lightweight of jiggle frame Saves £17-22k on shared material |
| Hybrid soultion | Procure Inconel Jiggle pivot in common with SRON 7010-600. But use a stainless steel pivot for chop axis. | £41-48k | 1.1mW | 2.0mW | Risk of failure of stainless steel chop pivot. Needs 85% lightweight of jiggle frame Late stage de-scope to option 12 |
| BE Systems Pivot. 0.15mm blade | identical to SMEC pivots | £55k | 1.4mW | 3.9mW | delay to re-engineer (1-2 months) mass growth BE systems QA Not flown before No margin on power |
| 429 stainless | Uses off the shelf pivots but need to upscreen, and schedule extra vibration tests | £34.2k (+80k for cold vibration?) | 1.3mW | 3.2mW | risk of failure on cold vibration if need to re-qualify. 3-6 months late Need extra £97k to buy inconel if fails Need £50k? for catch-up costs Assumes 2 extra cold vibrations @£10k (real cost £50k TBC??) |
| Common intermediate pivot | intermediate stiffness pivot to BSM specification compromise between the two. (eg Use SRON 7010-600 as example) | £72.8k | 3.6mW | 14.5mW | Needs 85% lightweighting of the jiggle frame (possible) Copper motor coils don't meet spec |

## Notes

### Costs:

- all costs based on $1.40:£1.00, and 10.00FF:£1.00

- The Lucas flex pivots includes $28k of minimum material quantity charges and $22k of tooling charges, per type of pivot (we have two types, hence $100k). We get 18 of each type but buy enough material for 50. Assuming an exchange of 1.4 and that we do NOT pay import of VAT, this translates as ~£71k, for material and a unit cost  of approx £640 per pivot

### Power budget calcs:

- baseline pivot, copper coil:

0.80mW sensor

0.84mW chop (2.4degrees, 2 Hz, 47 Nmm/rad. stiffness)

1.54mW jiggle (0.6 degrees, 0.5Hz, 367 Nmm/rad stiffness)

total: 3.2 mW

- baseline pivot, aluminium coils

0.80mW sensor

0.17mW chop (2.4degrees, 2 Hz, 47 Nmm/rad. stiffness)

0.31mW jiggle (0.6 degrees, 0.5Hz, 367 Nmm/rad stiffness)

total: 1.28 mW

- using a baseline jiggle pivot in the chop and jiggle axis:

chop stiffness goes up by 7.94x. Chop power goes up by 63x. thus total power = 55mW (Cu); 11.8mW (Al),

- using a baseline chop  pivot in the chop and jiggle axis:

jiggle  stiffness goes down by 7.94x. Jiggle power goes down by 63x. thus total power = 1.7mW (Cu); 1.0mW (Al),

- Common intermediate SRON 7010-600 (187Nmm/rad) as example

chop stiffness goes up by 3.98x. Chop power goes up by 15.8x.

jiggle  stiffness goes down by 1.96x. Jiggle power goes down by 3.85x.

thus total power = 14.5mW (Cu); 3.6mW (Al),

- BE systems 0.15mm

0.15mm flexure for jiggle & chop

Stiffness: 89.1Nmm/Rad (dominique's note)

- jiggle stiffness down by 4.11x, power down by 16.89x

- chop stiffness up by 1.90x, power up by 3.6x

thus total power: 3.9mW (Cu) ; 1.4mW (Al)

- Hybrid solution

SRON 7010-600 pivot for jiggle. jiggle  stiffness goes down by 1.96x. Jiggle power goes down by 3.85x.

Baseline 5010-800 for chop.

Power: 2.0mW (Cu); 1.05mW (Al)