Subject: HERSCHEL SPIRE INTERFACE DOCUMENT REQUIREMENTS

APPROVED BY: 	J. DELDERFIELD……………………..	Date: ……………….

APPROVED BY: 	K. KING………………………………..	Date: ……………….

AS  ISSUED FOR SPIRE INTERFACE REVIEW, November 2000

To: SPIRE Project

From: John Delderfield

INTERFACE DOCUMENTS

I recently had a SPIRE CONFIGURABLE DOCUMENTS' TREE: SPIRE-RAL-PRJ-000033, Issue 0.4   J.D.  17/10/00 posted on DMS.   People will recall that I noted at our recent meetings that the ICDs needed to be re-sequenced to better reflect instrument hierarchy.  Rather than re-issue the whole tree right now, knowing that some people have already promised comments on it, let me just note the re-ordered ICD section, splitting the DRCU to be as it now is, two units.  This limb of the tree now looks like:

As noted above, ICDs shall reference higher docs. for I/Fs if appropriate, not repeat details.  The whole instrument harness between units is pulled out in the above scheme and so lower ICDs shall only call up connector ID and short functional description.  Some of the subsystem ICDs may be small enough to be incorporated into their subsystem requirements documents, e.g "Filters, beam splitters and dichroics" may be a case in point although even in this instance the bare optical component needs to be mounted with flight absorber around its periphery to permit its proper sub-system level characterisation.

Bruce is considering the project progress and setting documents in place + reviewing them.  He will probably attach this note to a document aimed at progressing this process, and mentioning names!

Let me specify items for contents lists of the ICDs, based on Colin's previous big VISIO diagram:

| Unit | Document number | At least I/Fs to |
| --- | --- | --- |
| Digital Processing Unit (DPU) | SPIRE-IFS-DOC-TBD | IIDB +Instrument Requirements on I/Fs Harness Definition Operating Modes ICU DRU |
| Instrument Control Unit (ICU) | SPIRE-SAP-DOC-TBD | IIDB + Instrument Requirements on I/Fs Harness Definition Operating Modes DPU DRU BSM Spectrometer Mechanism Stimuli/Calibrators HE3 Cooler |
| Detector Readout Unit (DRU) | SPIRE-SAP-DOC-TBD | IIDB + Instrument Requirements on I/Fs Harness Definition Operating Modes DPU ICU Detectors/JFETS modules |
| Structure incl. baffles, straps, thermometry & harness routing; | SPIRE-MSS-DOC-TBD | IIDB + Instrument Requirements on I/Fs Harness Definition Optics Config Control Mirrors/Stops BSM Spectrometer Mechanism Stimuli/Calibrators Filters,etc. HE3 Cooler Detectors/JFETS modules |
| Mirrors and optical stops | SPIRE-LAM-DOC-TBD | IIDB + Instrument Requirements on I/Fs Optics Config Control Operating Modes Structure etc. Spectrometer Mechanism Stimuli/Calibrators Filters,etc. Detectors/JFETS modules? |
| Beam Steering (Chopping) Mirror Assembly (BSM) | SPIRE-ATC-DOC-TBD | IIDB + Instrument Requirements on I/Fs Harness Definition Optics Config Control Operating Modes ICU Structure etc. |
| Spectrometer Mechanisms; | SPIRE-LAM-DOC-TBD | IIDB + Instrument Requirements on I/Fs Harness Definition Optics Config Control Operating Modes ICU Structure etc. |
| Photometer & Spectrometer Stimuli/Calibrators | SPIRE-QMW-DOC-TBD | IIDB + Instrument Requirements on I/Fs Harness Definition Optics Config Control Operating Modes ICU Structure etc. Mirrors/Stops |
| Filters, beam splitters and dichroics | SPIRE-QMW-DOC-TBD | IIDB + Instrument Requirements on I/Fs Harness Definition Optics Config Control Structure etc. Mirrors/Stops |
| Helium3 Cooler | SPIRE-JPL-DOC-TBD | IIDB + Instrument Requirements on I/Fs Harness Definition Operating Modes ICU |
| Detector Subsystems+ JFET modules | SPIRE-SBT-DOC-TBD | IIDB + Instrument Requirements on I/Fs Harness Definition Optics Config Control Operating Modes DRU Structure etc. Mirrors/Stops HE3 Cooler |

I'm sure people working on the project will quickly bring me up to speed where things need amending above!

The emboldened I/Fs in the r.h. column above are interfaces “looking up” the system and only need to be referenced for compliance.  This means that the I/Fs for some of the lower sub-systems may be put as a section in their requirements documents…unless people like generating paper.

Note that there are standard build requirements that have I/F implications, such as thermal, power, EMC and these should be put in the I/F documents IF they have not been covered elsewhere.