FIRST / SPIRE / FTS / MCU

EEE PART LIST

User code : FSFTSL

DCL code L 058

| Prepared by : | Date : |
| --- | --- |
| P. Levacher | 26-09-2001 |
| Approved by : | Date : |
| D. Pouliquen |  |

Document change record

________

| Révision |  |
| --- | --- |
| Issue - rev. | Date | Approved by | Modifications |
| 01 - 00 | 29-03-00 | D. P. | All : first issue |
| 02 - 00 | 27-04-00 | D. P. | document reference has changed, LAM/ELE/FTS/QUA/000201 is obsolete. scope paragraph is updated. acronyms added. connectors list added to this document in specific paragraphs. SRAM (65656) reference completed. EEPROM (28C010) reference completed. FIFO (67204) reference completed. qty of 26C31 increased. reference and package of FPGA changed. qty of DAC (7846) increased. qty of decoder (54HC138) increased. qty of transceiver (54HC245) increased. qty of HS-508 increased. reference of analog switch HS-302RH changed to HS-303RH. transistors 2N2222 & 2N2907 suppressed. LED for position encoder added photodiodes for position encoder added connector backshells added |
| 03 - 00 | 12-12-00 | D. P. | lot of parts changed according to First PPL dated 07-06-2000 Actel A1280 FPGA changed to RT14100, ADC AD574A changed to SEI 9220LPRP (speed and power consumption), voltage regulator diodes added, instrumentation amplifier AMP01 added, Jfet transistor (encoder preamplifier) changed by TIA hybrid module, relays added, crystal added, voltage regulator added. |
| 04 - 00 | 01-02-01 | D.P. | new component / previous issue are noted "N" in the family column cryo connector list added in § 6 LLI components are also listed in § 7 |
| 04 - 01 | 08-02-01 | D.P. | correction of an error in the quantities in the LLI components list. Mosfet added : 3N 163 Type of Jfet transistor added : 2N 4341 |
| 05 - 00 | 09-02-01 | D.P. | line driver and receiver changed to Intersil types (HS9-26C31RH & C32RH) to be conform with the DPU interface type of transistor added for launch latch drivers: 2N 5153 |
| 06 - 00 | 20-04-01 | D.P. | definitive choice of RAM : HX 6228 (SMDP65656 & UT9Q512 suppressed) qty of 54HC386 increased to 30 HS1-303RH confirmed (qty = 10), qty of 1N5712 increased, diode 1N4148 added qty of 1N3595 increased, 54HC04 changed to 54AC04 precision on zener diode : 1N6312 & 1N6317 |
| 07 - 00 | 23-07-01 | D.P. | changes and adds in cryo canon list, 2N2222A, 2N5154 added,1N4569 added, ATP on components identified, some change in quantities for analog parts, |
| 07 - 01 | 26-07-01 | D.P. | components in cryogenic temperature identified, self procurement components identified, correction of some writing errors. |
| 08 - 00 | 26-09-01 | D.P. | Quantities of analog components updated, Type of Jfet transistor changed to : 2N 4392 Connector FRB 65 pins added, male, female, saver, Types and quantities of connectors modified, Precision added for the type of relay, ATP for component identified, |

Acronyms

________

AD		Applicable Document

AIV		Acceptance, Integration and Validation

AVM		Avionics Model

BOL		Beginning  Of Life

BSM		Beam Steering Mirror

CEA		Commissariat à l'Energie Atomique

CQM		Cryogenic Qualification Model

EGSE		Electrical Ground Support Equipment

EOL		End of Life

ESA		European Space Agency

FIRST		Far InfraRed ans Submillimetre Telescope

FM		Flight Model

FPU		Focal Plane Unit

FTS		Fourrier Transform Spectrometer

FTSE		FTS warm Electronics

FTSP		FTS Preamplifier for the position encoder signals

H/K		HouseKeeping

H/W		Hardware

ICD		Interface Control Document

I/F		Interface

LAM		Laboratoire d'Astrophysique de Marseille

MAC		Multi Axes Controller

MCE		Mechanism Control Electronics

N/A		Not Applicable

RAL		Rutherford Appleton Laboratory

RD		Reference Document

ROE		Royal Observatory of Edinburgh

SAp		Service d'Astrophysique

S/C		Spacecraft

SM		Spare Model

SMEC		Spectrograph MEChanism

S/W		Software

TBC		To Be Confirmed

TBD		To Be Define

TBW		To Be Written

TC		Tele-Command

TM		TeleMetry

WE		Warm Electronics

…

Table of contents

________

document change records

Distribution List

acronysms

table of contents

1.	SCOPE	6

2.	REFERENCE DOCUMENTS	6

3.	ABBREVIATIONS	6

4.	LEGENDE OF LIST COLUMNES	6

5.	MANUFACTURERS	7

6.	LIST OF CRYO CONNECTORS AND CABLES	8

7.	LIST OF IDENTIFIED LLI COMPONENTS	10

8.	LIST OF EEE PARTS	11

# SCOPE

This document provide a preliminary list of EEE components which would be used in the flight model of the MCU system (warm electronics + SMEC encoder preamplifier + SMEC position encoders).

The cryo harness connectors are included in this list, with savers and accessories.

# REFERENCE DOCUMENTS

[RD1]		ESA/SCC QUALIFIED PARTS LIST (15-01-00)

[RD2]		EUROPEAN PREFERRED PARTS LIST (15-02-00)

[RD3]		CNES / QFT / IN0500 Liste préférentielle des composants

[RD4]		FIRST/Planck Prefered Part List ref. : FP-TLG-LI-0001 (07-06-2000)

# ABBREVIATIONS

EPPL		European Preferred Parts List

QPL		Qualified Parts List

TD		Total Dose effects

SEL		Single Event Latch up

SEU 		Single Event Upset

# LEGENDE OF LIST COLUMNES

F				ESA component family

GENERIC NAME		part number

MAN.				manufacturer

PACKAGE			mechanical package or housing

FUNCTION			features of the component

QTY				total quantity needed, including attrition

PROC-SPEC			QPL or PPL, procurement specification

LEVEL				Quality level

Q				space qualified

L				LLI component

# MANUFACTURERS

| Code | Manufacturer | Country | Remarks |
| --- | --- | --- | --- |
| AND | Analog Devices | USA |  |
| ACT | Actel Corporation | USA |  |
| ATM | ATMEL | USA / F |  |
| BBR | Burr Brown | USA |  |
| CAN | ITT Cannon | USA |  |
| CDI | Compensted Devices Inc. | USA |  |
| DAL | Dale | USA |  |
| DEU | Compagnie Deutsch | F |  |
| ELT | Eltec | USA |  |
| FCI | Framatome Connectors Int. | F |  |
| FRB | FRB Connectron | USA |  |
| GLN | Glenair | USA |  |
| HAM | Hamamatsu | J |  |
| HAR | Harris | USA | Intersil |
| HON | Honeywell | USA |  |
| INT | Intersil | USA |  |
| ITF | Interfet | USA |  |
| IRL | Infrared Laboratories Inc. | USA |  |
| TEK | Tekelec | F |  |
| LTC | Linear Technology Corp. | USA |  |
| MAX | Maxim | USA |  |
| MSC | Microsemi Corporation | USA |  |
| NSC | National Semiconductor | USA |  |
| OPD | Opto Diode | USA |  |
| SEI | Space Electronic Inc. | USA |  |
| SEM | Semicoa | USA |  |
| SFR | Vishay Sfernice | F |  |
| SIL | Siliconix | USA |  |
| SPR | Sprague | F |  |
| STM | STMicro | F |  |
| TEM | Temic (Atmel) | F |  |
| VIT | Vitramon | D |  |

# LIST OF CRYO CONNECTORS AND CABLES

| F | Generic Name | FLT Part Type | Pack. | Man / C | Function | Proc-Spec | Level | Qty | Q | LLI | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 02 N | MDM-37P FR123 | 3401 029 01B 37PFR123 |  | CAN/F | 37 cts MDM type connector, pin, + 4000mm AWG26 wires | SCC 3401/029 | SCC B | 8 | Y | N | cryo @ 4K |
| 02 N | MDM-37S FR114 | 3401 029 01B 37P FR114 |  | CAN/F | 37 cts MDM type connector, socket, with 508 mm AWG28 wires | SCC 3401/029 | SCC B | 13 | Y | N | cryo @ 4K |
| 02 N | MDM-37S FR*** | 3401 029 01B 37PFR*** |  | CAN/F | 37 cts MDM type connector, socket, with 500mm length of cable supplied by LAM | SCC 3401/029 | SCC B | 13 | Y | N | cable type is TBD, cryo @ 4K |
| 02 | MDM-25S FR116 | 3401 029 01B 25SFR116 |  | CAN/F | 25 cts MDM type connector, socket, uninsulated wire | SCC 3401/029 | SCC B | 5 | Y | N | cryo @ 4K |
| 02 | MDM- 25P FR136 (MDM-25PCBR) | 3401 029 01B 25PFR136 |  | CAN/F | 25 cts MDM type connector, pin, 90° PCB | SCC 3401/029 | SCC B | 5 | Y | N | cryo @ 4K |
| 2 | MDM-37 PS (SAVER) | 3401 041 06B 37PS |  | CAN/F | MDM connector saver, 37 cts | SCC 3401/041 | SCC B | 35 | Y | N | cryo @ 4K |
| 2 | MDM-25 PS (SAVER) | 3401 041 04B 25PS |  | CAN/F | MDM type connector saver, 25 cts | SCC 3401/041 | SCC B | 7 | Y | N | cryo @ 4K |
| 2 | MDM male & female screwlock (set of 2) | 3401 032 01 |  | CAN/F | set of 2 MDM male & female screwlock for front panel mounting | SCC 3401/032 | SCC B | 28 | Y | N | cryo @ 4K |
| 2 | MDM male & female screwlock (set of 2) | 3401 032 02 |  | CAN/F | set of 2 MDM male & female screwlock for rear panel mounting | SCC 3401/032 | SCC B | 28 | Y | N | cryo @ 4K |
| 2 | MDM 90° angle mounting braket | 3401 032 03 |  | CAN/F | set of 2 MDM 90° angle mounting braket | SCC 3401/032 | SCC B | 5 | Y | N | cryo @ 4K |
| 2 | MDM male screwlock for savers (set of 2) | 3401 032 05 |  | CAN/F | set of 2 MDM male screwlock assembly for saver | SCC 3401/032 | SCC B | 22 (tbc) | Y | N | cryo @ 4K |
| 2 | MDM female screwlock for PCB connectors | 3401 032 06 |  | CAN/F | set of 2 MDM female screwlock for PCB connectors | SCC 3401/032 | SCC B | 5 | Y | N | cryo @ 4K |
| 2 | MDM-accessories |  |  | GLN/ US | backshell for 37 cts MDM connector | TBD | TBD | TBD |  |  | cryo @ 4K |

|  | CABLES |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | cable with 11 shielded twisted pairs + general shield |  |  | TBD | AWG 30 (TBC) | TBD | TBD | 100m |  |  | cryo @ 4K self procurement |

# LIST OF IDENTIFIED LLI COMPONENTS

| F | Generic Name | FLT Part Type | Package | Man / C | Function | Proc-Spec | Level | Qty | Q | LLI | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 08 | 7805ALPRP | 7805ALPRPFK | 28-FP | SEI/ US | 16 bits analog digital converter, 10 µs | 7805ALPRP0319.99 | E | 10 | N | Y | prefered type / ATP 09-04 |
| 08 | 7846RP | 7846RPFS | 28-FP | SEI/ US | 16 bits Digital Analog converter, 10 µs | 7846RP0728.99 | S | 15 | N | Y | prefered type / ATP 09-04 |
| 08 | 27C1512RP | 27C1512RPDK | 40-DIL | SEi/ US | 32k x 16 PROM, 200ns | TL-DS-007 | K | 18 | N | Y | prefered type / ATP 09-04 |
| 08 | AD630SE/883 | 5962-89807012A | 20-LCC | AND/ US | modulator/ demodulator | 5962-89807 | B | 10 | N | Y | obsolete type, ATP 09-04 |

# LIST OF EEE PARTS

New component / previous issue are noted "N" in the Family column.

| F | Generic Name | FLT Part Type | Package | Man / C | Function | Proc-Spec | Level | Qty | Q | LLI | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | CAPACITORS |  |  |  |  |  |  |  |  |  |  |
| 01 | 805 TI 47 p ( C ( 1.5 n |  | chip 0805 | VIT/D | ceramic chip capacitor, type I, 50 V | SCC 3009/003 | SCC C | TBD | Y | N |  |
| 01 | 805 TII 1n ( C ( 27 n |  | chip 0805 | VIT/D | ceramic chip capacitor, type II, 50 V | SCC 3009/008 | SCC C | TBD | Y | N |  |
| 01 | 1812 TI 3.3 n ( C ( 18 n |  | chip 1812 | VIT/D | ceramic chip capacitor, type I, 50 V | SCC 3009/005 | SCC C | TBD | Y | N |  |
| 01 | 1812 TII 22 n ( C ( 270 n |  | chip 1812 | VIT/D | ceramic chip capacitor, type II, 50 V | SCC 3009/010 | SCC C | TBD | Y | N |  |
| 01 | CLR 79 15µ(C(1200µ 8µ(C(560µ |  |  | SPR/F | tantalum capacitor 15V 30V | SCC 3003/005 | SCC C | TBD | Y | N |  |
|  | CONNECTORS |  |  |  |  |  |  |  |  |  |  |
| 02 | DEMA 9S NMB FO | 3401 002 01 B DEMA9SNMBFO |  | CAN/F | 9 socket, subm. connector w/o cts | SCC 3401/001 | SCC B | 7 | Y | N |  |
| 02 | DBMA 25S NMB FO | 3401 002 01 B DBMA25SNMBFO |  | CAN/F | 25 socket, subm. connector w/o cts | SCC 3401/001 | SCC B | 7 | Y | N |  |
| 02 N | DBMA 25P NMB FO | 3401 002 01 B DBMA25PNMBFO |  | CAN/F | 25 pin, subm. connector w/o cts | SCC 3401/001 | SCC B | 7 | Y | N |  |
| 02 | DCMA 37S NMB FO | 3401 002 01 B DCMA37SNMBFO |  | CAN/F | 37 socket, subm. connector w/o cts | SCC 3401/001 | SCC B | 17 | Y | N |  |

| F | Generic Name | FLT Part Type | Package | Man / C | Function | Proc-Spec | Level | Qty | Q | LLI | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 02 N | Contacts male (crimp #20/24) | 3401 005 01 B |  | CAN/F | socket contacts for D*MA connector | SCC 3401/005 | SCC B | 1000 | Y | N |  |
| 02 | Contacts female (crimp #20/24) | 3401 005 02 B |  | CAN/F | socket contacts for D*MA connector | SCC 3401/005 | SCC B | 1100 | Y | N |  |
| 02 N | Contacts male (crimp #26/28) | 3401 005 03 B |  | CAN/F | socket contacts for D*MA connector | SCC 3401/005 | SCC B | 1000 | Y | N |  |
| 02 N | Contacts female (crimp #26/28) | 3401 005 04 B |  | CAN/F | socket contacts for D*MA connector | SCC 3401/005 | SCC B | 1000 | Y | N |  |
| 02 | DEBMA 9 PS NMB FO (saver) | 3401 020 01 B BDEBMA 9 PS NMB FO |  | CAN/F | subm. 9 p connector saver w/o contacts | SCC 3401/020 | SCC B | 14 | Y | N |  |
| 02 | DBBMA 25 PS NMB FO (saver) | 3401 020 01 B DBBM 25 PS NMB FO |  | CAN/F | subm. 25 p connector saver w/o contacts | SCC 3401/020 | SCC B | 24 | Y | N |  |
| 02 | DCBMA 37 PS NMB FO (saver) | 3401 020 01 B DCBM 37 PS NMB FO |  | CAN/F | subm. 37 p connector saver w/o contacts | SCC 3401/020 | SCC B | 34 | Y | N |  |
| 02 | Saver contacts | 3401 021 01 B |  | CAN/F | contacts for D*MA saver connector | SCC 3401/021 | SCC B | 2000 | Y | N |  |
| 02 | DE-60-20 | 3401 022 07 B |  | CAN/F | dust cap for DEBMA 9S (red) | SCC 3401/022 | SCC B | 7 | Y | N |  |
| 02 | DB-60-20 | 3401 022 11 B |  | CAN/F | dust cap for DBBMA 25S (red) | SCC 3401/022 | SCC B | 17 | Y | N |  |
| 02 N | DB-59-20 | 3401 022 12 B |  | CAN/F | dust cap for DBBMA 25P (red) | SCC 3401/022 | SCC B | 7 | Y | N |  |

| F | Generic Name | FLT Part Type | Package | Man / C | Function | Proc-Spec | Level | Qty | Q | LLI | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 02 | DC-60-20 | 3401 022 13 B |  | CAN/F | dust cap for DCBMA 37S (red) | SCC 3401/022 | SCC B | 17 | Y | N |  |
| 02 | screw-lock assembbly (female) | 3401 022 01 B NMB variant 01 |  | CAN/F | screw-lock assembbly (female) for D*MA connectors | SCC 3401/022 | SCC B | 27 | Y | N |  |
| 02 | screw-lock assembbly (female) | 3401 022 01 B NMB variant 06 |  | CAN/F | screw-lock assembbly (female) for D*MA connectors saver | SCC 3401/022 | SCC B | 72 | Y | N |  |
| 02 N | KNB 065 13 10 110 | 3401 016 01B 05 MC 33 33 33 |  | FRB/F | KNB type, right angle PCB 65 contacts pins connector | SCC 3401/016 | SCC B | 7 | Y | N |  |
| 02 | KNB 084 13 10 110 | 3401 016 01B 07 MC 33 33 33 |  | FRB/F | KNB type, right angle PCB 84 contacts pins connector | SCC 3401/016 | SCC B | 7 | Y | N |  |
| 02 | KNB 120 13 10 111 | 3401 016 01B 10 MC 35 35 35 |  | FRB/F | KNB type, right angle PCB 120 contacts pins connector | SCC 3401/016 | SCC B | 7 | Y | N |  |
| 02 N | KNB 065 26 30 121 | 3401 016 01B 17 FD 36 36 36 |  | FRB/F | KNB type, PCB, 65 contacts recept. connector | SCC 3401/016 | SCC B | 7 | Y | N |  |

| F | Generic Name | FLT Part Type | Package | Man / C | Function | Proc-Spec | Level | Qty | Q | LLI | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 02 | KNB 084 26 30 121 | 3401 016 01B 19 FD 36 36 36 |  | FRB/F | KNB type, PCB, 84 contacts recept. connector | SCC 3401/016 | SCC B | 7 | Y | N |  |
| 02 | KNB 120 26 30 121 | 3401 016 01B 22 FD 36 36 36 |  | FRB/F | KNB type, PCB, 120 contacts recept. connector | SCC 3401/016 | SCC B | 7 | Y | N |  |
| 02 N | KNB 065 SAVER | 3401 016 01B 17 FM 00 00 00 |  | FRB/F | KNB type, 65 contacts saver | SCC 3401/016 | SCC B | 13 | Y | N |  |
| 02 | KNB 084 SAVER | 3401 016 01B 19 FM 00 00 00 |  | FRB/F | KNB type, 84 contacts saver | SCC 3401/016 | SCC B | 13 | Y | N |  |
| 02 | KNB 120 SAVER | 3401 016 01B 22 FM 00 00 00 |  | FRB/F | KNB type, 120 contacts saver | SCC 3401/016 | SCC B | 13 | Y | N |  |

| F | Generic Name | FLT Part Type | Package | Man / C | Function | Proc-Spec | Level | Qty | Q | LLI | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | CRYSTAL |  |  |  |  |  |  |  |  |  |  |
| 03 | T807 | 3501011XXB | TO-5 | CMA/F | crystal 40 MHz | SCC-3501-011 | SCC B | 6 | Y | N | PPL / ATP11-07 |
|  | DIODES |  |  |  |  |  |  |  |  |  |  |
| 04 | 1N3595US-1 | JAN S 1N3595US-1 Hrd Glass | SMD | MSC/ US | switching diode, 225mA, 125V | MIL-PRF-19500/241 | JAN S | 196 | Y | N | PPL / ATP 24-09 |
| 04 | 1N4148-1 | 510102302B | DO-35 | MSC/ US | switching diode, | SCC 5101/023 | JAN S | 12 | Y | N | PPL / ATP 24-09 |
| 04 | 1N6312/US | JAN S 1N6312/US | B-SQ-Melf | MSC/ US | voltage regulator diode, 0.5W, 3.3V | MIL-PRF-19500/533 | JAN S | 6 | Y | N | PPL / ATP 08-10 |
| 04 | 1N6317/US | JAN S 1N6317/US | B-SQ-Melf | MSC/ US | voltage regulator diode, 0.5W, 5.1V | MIL-PRF-19500/533 | JAN S | 6 | Y | N | PPL / ATP 08-10 |
| 04 | 1N4569A-1 | JANS1N4569AUR-1 | DO-213AA | CDI/ US | voltage regulator, temp comp., 0.4W, 6.4V | MIL-PRF-19500/452 | JAN S | 7 | Y | N | PPL / ATP 08-10 |
| 04 | 1N5712-1 | CDS5712-1 | DO-35 | CDI/ US | Schottky diode, 20V, 35mA | MIL-PRF-19500/445 | Class S | 91 | N | N | PPL / ATP 24-09 |
| 04 | OD-880W |  | die | OPD/ US | LED (position encoder) | TBD | TBD | 7 | N |  | only for comments, self procurement (in mechanism @ 4K) |
| 04 | S2386-18K |  | die | HAM/J | photodiode (pos. encoder) | TBD | TBD | 17 | N |  | only for comments, self procurement (in mechanism @ 4K) |

| F | Generic Name | FLT Part Type | Package | Man / C | Function | Proc-Spec | Level | Qty | Q | LLI | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | CONVERTERS |  |  |  |  |  |  |  |  |  |  |
| 08 | 7805ALPRP | 7805ALPRPFE | 28-FP | SEI/ US | 16 bits analog digital converter, 10 µs | 7805ALPRP0319.99 | E | 10 | N | Y | prefered type / ATP 09-04 |
| 08 | 7846RP | 7846RPFS | 28-FP | SEI/ US | 16 bits Digital Analog converter, 10 µs | 7846RP0728.99 | S | 15 | N | Y | prefered type / ATP 09-04 |
|  | INSTR; AMPLIFIER |  |  |  |  |  |  |  |  |  |  |
| 08 | AD524SD | 5962-8853901VEA | 16-DIL | AND/ US | instrumentation amplifier | 5962-88539 | QML-V | 44 | Y | N | prefered type / ATP 24-09 |
|  | OPERATIONAL AMPLIFIER |  |  |  |  |  |  |  |  |  |  |
| 08 | OP27AJ | M38510/13503 SGA | TO-99 | AND/ US | operational amplifier | MIL-M-38510/135 | Class S | 17 | Y | N | prefered type / ATP 24-09 |
| 08 | OP400ATC | 5962-8777101V3A | 28-LCC | AND/ US | operational amplifier (quad) | 5962-87771 | Class V | 54 | Y | N | prefered type / ATP 24-09 |
| 08 | OP467AY | 5982-9325801VCA | 14-DIL | AND/ US | operational amplifier (quad) | 5962-93258 | Class S | 44 | Y | N | prefered type / ATP 24-09 |
|  | VOLTAGE REGULATOR |  |  |  |  |  |  |  |  |  |  |
| 08 | LM117H | 5962-R9951703VXA | TO-39 | AGI/ US | voltage regulator | SMD-5962-99517 B | Class S | 17 | Y | N | PPL / ATP 24-09 + ATP 08-10 |

| F | Generic Name | FLT Part Type | Package | Man / C | Function | Proc-Spec | Level | Qty | Q | LLI | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | VOLTAGE COMPARATOR |  |  |  |  |  |  |  |  |  |  |
| 08 | HS9-139HR | 5962F9861301VXC | 14-FP | NSC/ US | voltage comparator (quad) | SMD-5962-986301 | V | 58 | Y | N |  |
|  | LINE DRIVER RECEIVER |  |  |  |  |  |  |  |  |  |  |
| 08 | HS9-26C31RH-QS9000 | 5962F9666301 VEC | 16-FP | SIL/ US | line driver, 3 state output | 5962-96663 | QML-V | 7 | Y | N | PPL /ATP 11-07 |
| 08 | HS9-26C32RH-QS9000 | 5962F9568901 VEC | 16-FP | SIL/ US | line receiver | 5962-95689 | QML-V | 7 | Y | N | PPL /ATP 11-07 |
|  | MEMORY |  |  |  |  |  |  |  |  |  |  |
| 08 | HX 6228/TVHC | 6962H9853701 VXC | 32-FP | HON/US | 128k x 8 SRAM, 25 ns | 5962-98537 | QML-V | 54 |  | N | ATP 11-07 |
| 08 | 27C1512RP | 27C1512RPDK | 40-DIL | SEi/ US | 32k x 16 PROM, 200ns | TL-DS-007 | K | 18 | N | Y | ATP 09-04 |

| F | Generic Name | FLT Part Type | Package | Man / C | Function | Proc-Spec | Level | Qty | Q | LLI | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | DSP |  |  |  |  |  |  |  |  |  |  |
| 08 | TSC21020F | 5962-9953901VXC | MFP-256 | ATM-F | 32/40 bit Floating Point DSP | 5962-99539 | SCC B | 6 | N | N | PPL / ATP 11-07 |
|  | MODEM & SWITCHES |  |  |  |  |  |  |  |  |  |  |
| 08 | AD630SE/883 | 5962-89807012A | 20-LCC | AND/ US | modulator/ demodulator | 5962-89807 | B | 10 | N | Y | obsolete, ATP 09-04 |
| 08 | HS9-508BRH-QS9000 | 5962F9674202 VEC | 16-FP | INT/ US | 8 channel analog multiplexer | 5962-96742 | QML V | 27 | Y | N | prefered type / ATP 24-09 |
| 08 | HS9-303RH | 5962R9581301 VCC | 14-FP | INT/ US | analog switch | 5962-95813 | QML V | 38 | Y | N | ATP 24-09 |
|  | VOLTAGE REFERENCE |  |  |  |  |  |  |  |  |  |  |
| 08 | AD584TH | 5962-3812802 VGA | TO-99 (H8) | AND/ US | programmable voltage reference | 5962-38128 | QML-V | 17 |  | N | prefered type / ATP 24-09 |
|  | FPGA & GATES |  |  |  |  |  |  |  |  |  |  |
| 08 | RT54SX32S | SA/032003EYC | 208- CQFP | ACT/ US | 16k gates Antifuse FPGA | SMD-5962-01508 | Class S | 12 | N | N | prefered type / ATP 11-07 |
| 08 | 54AC04 | 5962-8760901VXA | FP | STM/F | inverter gate | SMD-5962-87609 | SCC B | 7 | Y | N | PPL / ATP 11-07 |
| 08 | 54HC386 | 920112102BF | FP | STM/F | exclusive or gate | SCC-9201-121 | SCC B | 0 (TBC) | Y | N | PPL / ATP 11-07 |

| F | Generic Name | FLT Part Type | Package | Man / C | Function | Proc-Spec | Level | Qty | Q | LLI | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | RELAYS |  |  |  |  |  |  |  |  |  |  |
| 09 | ETD2G 26 (TBC) | 3601 012 … |  | LEA/US | relay, 2 PDT, 26 V | SCC-3601-012 | SCC B | 0 TBC | Y | N | PPL |
| 09 | DFIC 26 | 3602 019 02 B 26V |  | LEA/US | latching relay, 2PDT, 26 V | SCC-3602-019 | SCC B | 16 | Y | N | PPL |
|  | RESISTORS |  |  |  |  |  |  |  |  |  |  |
| 10 | model 104, 5% 10 Mohms |  |  | ELT/ US | tubular resistor with leads, 5 % |  |  | 40 |  | N | T = 4K |
| 10 | model 104, 5% 20 Mohms |  |  | ELT/ US | tubular resistor with leads, 5 % |  |  | 60 |  | N | T = 4K |
| 10 | PHR 1206 | PHR 1206 … | 1206 SMD | DAL/ US | chip resistor, 0.1 %, 25 ppm/°C, 250 mW | MIL-R-55342/7 | FRL R | TBD | Y | N |  |
| 10 | RM1206 5.6 < R < 1M |  | 1206 SMD | DAL/ US | chip resistor, 1 %, 50 ppm/°C, 250 mW | MIL-R-55342/7 | FRL R | TBD | Y | N |  |
| 10 | RNC 50 1 < R < 1M (TBC) |  |  | SFR/F | film resistor, 0.5%, 50 ppm/°C | SCC 4001/009 | SCC C | TBD | Y | N |  |
| 10 | SIL 47 < R < 1M (TBC) |  | SIL- ? | SFR/F | film resistor, 2%, E48 | SCC 4005/003 | SCC C | TBD | Y | N |  |
|  | TRANSISTORS |  |  |  |  |  |  |  |  |  |  |
| 12 | 2N2219A |  | TO-39 | STM/F | NPN transistor, 800 mW | SCC-5201-003 | SCC B | 7 | Y | N | PPL / ATP 24-09 |
| 12 | 2N2905A (TBC) |  | TO-39 | STM/F | PNP transistor, 600 mW | SCC-5202-002 | SCC B | 0 | Y | N | PPL, qty =TBC |

| F | Generic Name | FLT Part Type | Package | Man / C | Function | Proc-Spec | Level | Qty | Q | LLI | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 12 | 2N2222A | 520100204B | TO-18 | STM/F | NPN transistor, 400 mW | SCC-5201-002 | SCC B | 34 | Y | N | PPL / ATP 24-09 |
| 12 | 2N2907A | 520200102B | TO-18 | STM/F | PNP transistor, 400 mW | SCC-5202-001 | SCC B | 34 | Y | N | PPL / ATP 24-09 |
| 12 | 2N5153 | 520400202B | TO-39 | STM/F | PNP transistor, 1000 mW | SCC-5204-002 | SCC B | 71 | Y | N | PPL / ATP 24-09 |
| 12 | 2N5154 | 520301002B | TO-39 | STM/F | NPN transistor, 1000 mW | SCC-5203-010 | SCC B | 71 | Y | N | PPL / ATP 24-09 |
| 12 | 3N163 |  | TO-72 | SIL/US | Mosfet transistor |  |  | 30 |  |  | in cryo mechanism @ 4K |
| 12 | 2N4392 |  | TO-18 | SIL/US | FET transistor |  | class S | 14 |  |  |  |
| 12 | TIA front end (TBC) |  | TO-5 | IRL/ US | preamplifier hybrid module |  | TBD | 0 TBC | N |  | only for comments, self procurement if used in mechanism @ 4K |
| 12 | MB-1 bracket (TBC) |  |  | IRL/ US | bracket for TIA preamplifier |  | TBD | 0 TBC | N |  | only for comments, self procurement if used in mechanism @ 4K |