Mechanism Control Unit

Grounding Scheme

| Prepared by : | Date : |
| --- | --- |
| Patrick Levacher | 11/10/2001 |
| Checked by : | Date : |
| Dominique Pouliquen | 11/10/2001 |

Document change record

________

| Issue - rev. | Date | Modifications |
| --- | --- | --- |
| 0 - 0 | 25-04-00 | All : draft issue |
| 1 - 0 | 19-06-00 | First issue |

Distribution list

________

| Jean Louis Auguères | CEA | X |  |
| --- | --- | --- | --- |
| Christophe Cara | CEA | X |  |
| Colin Cunningham | ROE | X |  |
| Brian Stobie | ROE | X |  |
| Ian Pain | ROE | X |  |
| Didier Ferrand | LAM | X |  |
| Michel Jevaud | LAM | X |  |
| Patrick Levacher | LAM | X |  |
| Dominique Pouliquen | LAM | X |  |
| Bruce Swinyard | RAL | X |  |
| Ken King | RAL | X |  |

Acronyms

________

AD			Applicable Document

AVM		Avionics Model

BOL		Begin Of Life

BSM		Beam Steering Mirror

CQM		Cryogenic Qualification Model

EGSE		Electrical Ground Support Equipment

EOL		End of Life

ESA		European Space Agency

FIRST		Far Infra Red and Sub-millimeter Telescope

FM			Flight Model

FPU		Focal Plane Unit

FTS		Fourier Transform Spectrometer

FTSE		FTS warm Electronics

FTSP		FTS Preamplifier for the position encoder signals

H/K			House Keeping

H/W		Hardware

I/F			Interface

LAM		Laboratoire Astrophysique de Marseille

MAC		Multi Axes Controller

MCU		Mechanism Control Unit

N/A			Not Applicable

RAL		Rutherford Appleton Laboratory

RD			Reference Document

ROE		Royal Observatory of Edinburgh

S/C			Spacecraft

SM			Spare Model

SMEC		Spectrograph MEChanism

S/W		Software

TBC		To Be Confirmed

TBD		To Be Define

TBW		To Be Written

TC			Tele-Command

TM			TeleMetry

WE			Warm Electronics

Table of contents

________

1	Introduction	5

1.1	Purpose and Scope	5

1.2	Applicable and reference documents	5

1.2.1	Applicable documents	5

2	SYSTEM OVERVIew	6

3	Grounding Scheme.	7

# Introduction

## Purpose and Scope

The purpose of this document is to describe the electronics design grounding of the MCU.

The MCU includes the control electronics unit of the 2 SPIRE mechanical subsystems (SMEC and BSM).

The MCU is part of the DRCU and has electrical  (Main Power Supplies) and mechanical (Electronics Cabinet) interfaces with it.

## Applicable and reference documents

### Applicable documents

| AD1 | Operating Modes for the SPIRE Instrument (SPIRE-RAL-DOC-000320) |
| --- | --- |
| AD2 | FIRST/Planck Packet Structure Interface Control Document (SCI-PT-IF-07527) |
| AD3 | Spire Spectrometer Mirror Mechanism Subsystem Specification (SPIRE-LAM-PRJ-000460) |
| AD4 | FIRST / Planck Instrument Interface Document Part B (SCI-PT-IIDB/SPIRE-02124) |
| AD5 | DRCU Electrical Interface Control Document (SAp-SPIRE-CCa-24-00) |
| AD6 | SPIRE Instrument Requirements Specification (IRD) (SPIRE-RAL-PRJ-000034) |
| AD7 | DPU Interface Control Document SPIRE-IFS-PRJ-000650 2 April 2001 Issue 1.0 |

# SYSTEM OVERVIew

The MCU is dedicated to the control and monitoring of the following 3 axis of the SPIRE instrument:

- the Spectrometer Mechanism (SMEC). The control is typically based on a scan at a configurable speed, but can be set-up on the basis of a step position control in case of the step and integrate mode of the instrument.

- the Chopper and Jiggle axis of the Beam Steering Mirror subsystem . The control is a position step control pattern.

The MCU control electronics includes:

- 2 MAC Boards (prime and redundant): common digital control board including:

- a 21020 DSP in charge of the control loop tasks and signal acquisitions

- 3 DACs for SMECm and BSMm motor control,

- 1 multiplexed (16 channels) 16 bits ADC for SMEC and BSM analogue signal acquisitions,

- 8 logical inputs

- 12 logical outputs.

- A 54SX32S ACTEL FPGA for:

- the bus control for interface with DACs, multiplexed ADC, digital inputs and outputs, and the optical encoder counting and logic. The encoder pulses generated by the encoder electronics are entering an Encoder Unit Interface (Bus control FPGA function) for pulses counting and crude position determination. The incremental position count is done in the FPGA for in order to verify the trajectory controlled by the DSP and acts the role of a watchdog. Furthermore, the Encoder Unit Interface includes error signals generation for whatever problem occurs during the trajectory (limits reached, etc...). If one on the logical signal is high, the DSP is interrupted and put in safe configuration.

- the communication with DPU high and low rate serial links.

- 2 SMEC Boards (prime and redundant): analogue electronics for the power amplification of the actuators and acquisition electronics for sensors pre-amplification and conditioning of the SMEC subsystem

- 1 BSM Board: analogue electronics for the power amplification of the actuators  and acquisition electronics for sensors pre-amplification and conditioning of both prime and redundant  BSM subsystems.

# Grounding Scheme.

- Motor PWR Analog ground to be added on the schematics

- The analog grounds not connected @ MCU level

- Analog/Digital grounds connected @ ADC level

- Analog ground not connected to mechanics