Qualification Random Vibration Specification 01 October 2001.

Draft spec, for comments only. Is to be implemented in next issue of Mechanical-ICD.

The hereafter listed tables specify the qualification input levels for the subsystems. Flight levels are a factor 2.25 lower in PSD, which is a factor of 1.5 lower in g-rms. There are jumps of ( dB/oct, if your shaker can't handle that, try 24 dB/oct. Even it out over frequency range. to both sides of jump.

Duration of qualification run 120 seconds. Sorry about that, but it is specified by ESA.

S-Mec

| Axis (S/C) | ramp up | plateau | ramp down | g-rms |
| --- | --- | --- | --- | --- |
| X | +6 dB/oct 20-100 Hz | 0.2 g2/Hz 100 - 300 Hz | -6 dB/oct 300-2000 Hz | (10.2 |
| Y | +6 dB/oct 20-100 Hz | 0.4 g2/Hz 100 - 200 Hz 0.1 g2/Hz 200 - 400 Hz | -6 dB/oct 400-2000 Hz | (11.3 |
| Z | +6 dB/oct 20-100 Hz | 0.3 g2/Hz 100 - 200 Hz | -6 dB/oct 200-2000 Hz | (9.9 |

Mirrors

| Axis (S/C) | ramp up | plateau | ramp down | g-rms |
| --- | --- | --- | --- | --- |
| X/Y/Z | +6 dB/oct 20-100 Hz | 0.35 g2/Hz 100 - 400 Hz | -6 dB/oct 300-2000 Hz | (16 |

BSM as for S-Mec except

| Axis (S/C) | ramp up | plateau | ramp down | g-rms |
| --- | --- | --- | --- | --- |
| Y | +6 dB/oct 20-100 Hz | 0.7 g2/Hz 100 - 200 Hz 0.1 g2/Hz 200 - 400 Hz | -6 dB/oct 400-2000 Hz | (11.3 |