| SUBJECT: | OOL Data Interface Control Document |
| --- | --- |
| PREPARED BY: | M. J. Graham |
| DOCUMENT No: | SPIRE-ICS-DOC-000974 |
| ISSUE: | 1.0 | Date: | 30th October 2002 |
| APPROVED BY: | …………………………………. | Date: | …………………………. |

| Agreed By | Date |
| --- | --- |
| HIFI EGSE Manager | L. Dubbeldam |  |
| HIFI ICC Manager | P. Roelfsema |  |
| PACS EGSE Manager | E. Wiezorrek |  |
| PACS ICC Manager | O. Bauer |  |
| SPIRE EGSE Manager | J. Payne |  |
| SPIRE ICC Manager | K. King |  |
| ESA HSC Manager | J. Riedinger |  |
| ESA AIV Manager | TBS |  |

Distribution

Otto H. Bauer

Milena Benedettini

Jon Brumfit

Odile Couer-Joly

Albrech de Jonge

Wim De Meester

Matt Fox

Kevin Galloway

Matthew Graham

Steve Guest

Ana Heras

Rik Huygen

Do Kester

Ken King

Tanya Lim

Jean-Jacques Mathieu

Seb Oliver

Sabine Osterhage

Goran Pilbratt

Craig Porrett

Rafael Prades

Timo Prusti

Johannes Riedinger

Peter Roelfsema

Hassan Siddiqui

Sunil Sidher

Eckhard Sturm

Bart Vandenbussche

Stephane Veillat

Ekkehard Wieprecht

Erich Wiezorrek

Peer Zaal

Rob Zondag

# Change Record

| ISSUE | DATE |  |
| --- | --- | --- |
| 0.1 draft | 24 November 2001 | Original version |
| 0.2 draft | 25 January 2002 | Incorporated comments from SPIRE, HIFI, PACS and ESTEC regarding: IST generation, time formats, offline delivery, XML, file naming. |
| 0.3 draft | 26 February 2002 | Slight changes to lengths of fields for compatibility with Logica development |
| 1.0 | 30 October 2002 | First official release |

# Table of Contents

1.	Introduction	7

1.1	Purpose	7

1.2	Scope	7

1.3	Applicable Documents	7

1.4	Reference Documents	7

1.5	List of Acronyms	8

2.	Operational Assumptions and Constraints	9

2.1	Communications	9

2.2	Hardware	9

2.3	Software	9

2.4	User	9

2.5	Timing	9

3.	Requirements	10

3.1	Functional Requirements	10

3.2	On-Line Delivery Requirements	10

3.3	Off-Line Delivery Requirements	10

4.	Interface Characteristics	11

4.1	Interface Location and Medium	11

4.2	Hardware Characteristics and Limitations	11

4.3	Data Source, Destination and Transfer Mechanism	11

4.4	Node and Device Addressing	11

4.5	Relationship with other interfaces	11

5.	Access	12

5.1	Programs generating or using the Interface Data	12

5.2	Failure Protection, Detection and Recovery Procedures	12

5.3	File Naming Conventions	12

5.4	Storage and File Deletion Requirements	12

5.5	Security Requirements	12

5.6	Data Integrity Checks	12

5.7	Backup Requirements	13

5.8	Input / Output Protocols, Calling Sequence	13

5.9	Synchronisation Requirements	13

5.10	Error Handling	13

6.	Detailed Interface Specification	14

6.1	Data Structure	14

6.2	Generation Method	14

6.3	Data passed across the interface – direction of transfer	14

6.4	Size and Frequency of Transfers	14

7.	Data Definition	15

7.1	File characteristics	15

7.2	Header Record	15

7.2.1	Time Format	15

7.3	OOL Packet	15

7.3.1	Limit record	16

7.3.2	Status Consistency record	17

7.3.3	State record	17

7.3.4	Value format	18

# Glossary

# Introduction

## Purpose

This document specifies the structure and contents of Out Of Limits (OOL) record file (ORF) as expected by the Herschel Common Science System (HCSS) in all mission phases: ILT, IST and Ops.

## Scope

This document corresponds to ICD#3 in the list of ICDs [RD3].

This ICD is applicable to all phases of the Herschel missions: all of ILT, IST and Ops.

This ICD defines the ORF file format only and does not cover the control aspects related to the file generation or ingestion into the HCSS: file generation in ILT is covered by [RD7].

## Applicable Documents

| AD1 | Herschel Ground Segment Design Description Document | FIRST/FSC/DOC/0146 | 1.1 | 10 December 2001 |
| --- | --- | --- | --- | --- |
| AD2 | Herschel Ground Segment IRD | FIRST/FSC/DOC/0117 | 2.0 | 6 December 2001 |

## Reference Documents

| RD1 | HCSS User Requirements Document | FIRST/FSC/DOC/0115 | 2.0 | 3 May 2001 |
| --- | --- | --- | --- | --- |
| RD2 | FIRST Common Science System: Use Case Definitions | FIRST/FSC/DOC/0158 | 1.0 | 7 November 2000 |
| RD3 | Ground Segment List of ICDs | FIRST/FSC/DOC/0150 | 1.0 | 24 November 2000 |
| RD4 | SCOS-2000 Out of Limits Display Operator User Manual | S2K-MCS-SUM-2220 -TOS-GCI | 1.1 | 17 July 2000 |
| RD5 | IMCS MADDS-A/MADDS-B Interface Control Document | IMCS-MADDSA- MADDSB-ICD-001 | Draft | 10 May 2000 |
| RD6 | MIB Format Interface Control Document | SPIRE-MCS-ICD-0001 -TOS-GCI | 4.2 | 1 December 2000 |
| RD7 | HCSS-RTA Interface Interface Control Document | SPIRE-ICS-DOC-000975 | 1.0 | 30 October 2002 |

## List of Acronyms

| AD | Applicable Document |
| --- | --- |
| CCS | Central Checkout System |
| DDID | Data Delivery System ICD |
| EGSE | Electrical Ground Segment Engineering |
| HCSS | Herschel Common Science System |
| IA | Interactive Analysis |
| ICD | Interface Control Document |
| ILT | Instrument Level Test |
| IST | Instrument System Test |
| MIB | Mission Information Base |
| MOC | Mission Operations Centre |
| OOL | Out Of Limits |
| ORF | OOL Record File |
| QLA | Quick Look Analysis |
| RD | Reference Document |
| RTA | Real-Time Assessment |
| SCOS | Spacecraft Operating System |
| TBC | To be confirmed |
| TBW | To be written |
| TC | Telecommand |
| TM | Telemetry |

# Operational Assumptions and Constraints

## Communications

N/A

## Hardware

N/A

## Software

The expected introduction of XML in 2002/03 is not anticipated to have any impact on binary format data such as that covered in this ICD.

## User

N/A

## Timing

N/A

# Requirements

## Functional Requirements

These requirements have been extracted from the Ground Segment IRD (see [AD1]).

IR-3.1-470: The MOC shall make available the instruments parameters OOL information for a given operation period. The HSC may be using this data for the purpose of observation quality control. It will make it available to the ICCs. An ICC will use OOL information for monitoring their instruments. The MOC will make available the list of instrument parameters out of limits (soft & hard) for a given operation period. OOL data are only relevant for HK TM parameters including derived parameters.

IR-3.1-475: The HSC shall pull OOL data from the MOC. The OOL data will be delivered with the flow of consolidated TM as separate packets.

IR-3.1-480: The MOC shall make available to the HSC the instrument parameters OOL for a given operational period at the same time as the instrument consolidated HK TM for this period.

IR-4.4-40: The RTA shall make available to the HCSS its logs for any given testing period.

IR-4.4-50: The HCSS shall pull the RTA logs data from the RTA.

## On-Line Delivery Requirements

### In ILT and IST, the ORF will be delivered from SCOS-2000.

In Ops, the ORF will be retrieved from the DDS by HSC.

## Off-Line Delivery Requirements

N/A

# Interface Characteristics

## Interface Location and Medium

This interface is applicable to the ORF, which is generated by the EGSE-ILT/MOC and delivered to the HCSS. In all cases, the ORF will be transferred as a file over a communication line (LAN for EGSE-ILT, WAN for Ops).

## Hardware Characteristics and Limitations

N/A

## Data Source, Destination and Transfer Mechanism

The data sources for the three mission phases are EGSE-ILT for ILT and IST (in the latter phase, the data will be produced by replaying the TM data to RTA/SCOS-2000 [AD1, AD2 4.4.2]) and MOC for Ops. The way in which the ORF is retrieved from the relevant data source is outside the scope of this ICD but is covered in [RD7] for ILT, TBD ICD for IST and DDID for Ops. An ORF will be exported to the HCSS from the data source when requested.

## Node and Device Addressing

For ILT, see [RD7].

## Relationship with other interfaces

For ILT, see [RD7].

# Access

## Programs generating or using the Interface Data

The main program using the ORF is the HCSS OOLIngestor; however, there are no restrictions on other programs using it.

## Failure Protection, Detection and Recovery Procedures

Any failure in transferring the ORF between the EGSE-ILT/MOC and the HCSS, e.g. timeout, will be detected when the ORF is processed by the HCSS (ingested). This will terminate the current processing including database transactions (rollback might be necessary) and reinitiate a for the ORF from the EGSE-ILT/MOC (see [RD7]).

## File Naming Conventions

Although the ORF is a transient file, a naming convention is required to ensure that ORFs are not overwritten on the data source side by successive ORFs before they have been transferred to the HCSS (this applies primarily to ILT using HCSS v0.1). The following file naming convention will be applied to the ORF:

ORF_yymmdd_cccc.DAT

- yy	is the year in which the data in the file start

- mm 	is the month in which the data in the file start

- dd	is the day of the month on which the data in the file start

- cccc	is a cyclic counter relating to files generated on the same day

## Storage and File Deletion Requirements

The HCSS database should be sufficient space to contain all OOL data, i.e. for the entire mission.

## Security Requirements

Servers must be kept up-to-date with the latest security patches, especially if not protected by a firewall. An unauthorised user must not be able to modify the ORF in any way (checksumming could aid in detecting this). Note that ftp is not a secure method of data transfer.

## Data Integrity Checks

As mentioned in section 5.2, processing of the ORF by the HCSS will detect any data integrity problems.

## Backup Requirements

Once ingested, OOL data are backed up as part of the HCSS database nominal back-up.

An ORF can be reconstructed from EGSE-ILT/CCS/MOC but this will certainly be limited in time. This constrains the HCSS to ingest all OOL data.

## Input / Output Protocols, Calling Sequence

### For ILT, this will be defined in [RD7]; for IST, this is defined as part of a TBD ICD; and for Ops, this will be defined as part of the DDID.

## Synchronisation Requirements

- A locking mechanism must be used to prevent data being extracted from the database whilst it is in the process of being written or modified to prevent a partially written ORF being transferred to the HCSS (see [RD7]).

## Error Handling

See section 5.2.

# Detailed Interface Specification

## Data Structure

### The data passed via the ORF interface is all file-based.

## Generation Method

### The ORF is generated by a specific application running in the EGSE-ILT/MOC following a request from the HCSS. Each file covers a specific time window reported in the file header in terms of both its start and end timestamps.

## Data passed across the interface – direction of transfer

This ICD deals solely with the data passed from the EGSE-ILT/MOC to the HCSS. The data passed is made up of the ORFs.

## Size and Frequency of Transfers

### It is envisaged that one ORF per operation period will be produced Ops; during ILT and IST, this might not be the case.

# Data Definition

This section defines the characteristics of the ORF.

The ORF shall be a collection of OOL event packets generated for each state transition during a time defined in the ORF header.

The MIB version used to generate a particular OOL event packet can be retrieved from the HCSS based on the release time in the ORF header record.

## File characteristics

The ORF is a binary file consisting of a header record and a variable number of OOL event packets, each of which consists of a list of records, arranged in time ascending order. Network-order byte ordering (MSB first) is to be used.

## Header Record

The header record reports general information about the contents of the file and is stored at the beginning of the file. The header has the following structure and information:

### Table 1 – ORF Header Record Structure

| No. | Field Title | Octet | Type | Description |
| --- | --- | --- | --- | --- |
| 0 | 1st OOL packet time | 0-7 | Time format | Release time of the first OOL event packet included in the file |
| 1 | Last OOL packet time | 8-15 | Time format | Release time of the last OOL event packet included in the file |
| 2 | Number of OOL packets | 16-19 | 32 bit integer | Number of OOL event packets in the ORF |
| Total Length | 20 |  |  |

### Time Format

The time format used is the Sun MJT, as standard on Sun Solaris UNIX platforms. The format is two 32 bit integers. The first contains the number of seconds since 00:00, 1st January 1970 and the second integer the number of microseconds:

| Octet | Type | Description |
| --- | --- | --- |
| 0-3 | 32 bit integer | Seconds since epoch (00:00, 1st January 1970) |
| 4-7 | 32 bit integer | Additional microseconds from seconds in first field |

## OOL Packet

OOL event packets are generated for each state transition within the time window covered by the file. If the limit checker is configured to generate an updated OOL packet, when any of the parameters have a value changed, then there are additional OOL packets generated with a minimum time of difference.

An OOL packet contains a list of records and has the following structure:

Table 3 – OOL Packet Structure

| No. | Field Title | Octet | Type | Description |
| --- | --- | --- | --- | --- |
| 0 | Number of records | 0-1 | 16 bit integer | The number of records in the OOL packet |
| 1 | Spacecraft | 2-3 | Characters | Spacecraft |
| 2 | Record 1 | 4-? | Record | 1st record |
| 3 | Record 2 | ? | Record | 2nd record |
| … | Record … | ? | Record | …th record |
| n+1 | Record n | ? | Record | nth record |
| Total Length |  |  |  |

Each record can be a:

- Limit record

- Status Consistency record (the parameter has not changed unless as a result of a TC)

- State record (the parameter is constant all the time)

### Limit record

This record is built for the parameters with parameter limit values and has the following structure:

Table 4 – Limit Record Structure

| No. | Field Title | Octet | Type | Description |
| --- | --- | --- | --- | --- |
| 0 | Type | 0 | 8 bit integer | Record type (0) |
| 1 | OOL time | 1-8 | Time format | The time when the parameter was found to be out of limits |
| 2 | Value time | 9-16 | Time format | Time of value |
| 3 | Name | 17-24 | Characters | Name of the parameter as appearing in the MIB |
| 4 | Behaviour number | 25-28 | 32 bit integer | Behaviour in BEHV subsystem |
| 5 | Parameter state | 29-30 | 16 bit integer | Parameter state in BEHV subsystem (0 = nominal, 1 = warning, 2 = out of limits, 3 = SCC) |
| 6 | String state | 31-32 | 16 bit integer | String state in BEHV subsystem |
| 7 | State | 33-41 | Characters | Description of parameter state (“LOW LOW”, “LOW”, “HIGH”, “HIGH HIGH”) |
| 8 | Value | 42-55 | Value | Parameter value |
| 9 | Low limit | 56-69 | Value | Low limit of parameter |
| 10 | Upper limit | 70-83 | Value | Upper limit of parameter |
| Total Length | 84 |  |  |

The reference file is BEHVoolLimitRecord in the BEHV subsystem (from [RD5]).

### Status Consistency record

This record is built for the parameters where the status consistency checking is defined and has the following structure:

Table 4 – Status Consistency Record Structure

| No. | Field Title | Octet | Type | Description |
| --- | --- | --- | --- | --- |
| 0 | Type | 0 | 8 bit integer | Record type (1) |
| 1 | OOL time | 1-8 | Time format | The time when the parameter was found to be out of limits |
| 2 | Value time | 9-16 | Time format | Time of value |
| 3 | Name | 17-24 | Characters | Name of the parameter as appearing in the MIB |
| 4 | Behaviour number | 25-28 | 32 bit integer | Behaviour in BEHV subsystem |
| 5 | Parameter state | 29-30 | 16 bit integer | Parameter state in BEHV subsystem (0 = nominal, 1 = warning, 2 = OOL, 3 = SCC) |
| 6 | String state | 31-32 | 16 bit integer | String state in BEHV subsystem |
| 7 | State | 33-41 | Characters | Description of parameter state (“LOW LOW”, “LOW”, “HIGH”, “HIGH HIGH”) |
| 8 | Value engineer | 42-55 | Value | Parameter engineering value |
| 9 | Low limit engineer | 56-69 | Value | Low limit of parameter (engineering value) |
| 10 | Upper limit engineer | 70-83 | Value | Upper limit of parameter (engineering value) |
| Total Length | 84 |  |  |

The reference file is BEHVoolLimitRecord in the BEHV subsystem (taken from [RD5]).

### State record

This record is built for the parameters with a list of defined states and has the following structure:

Table 5 – State Record Structure

| No. | Field Title | Octet | Type | Description |
| --- | --- | --- | --- | --- |
| 0 | Type | 0 | 8 bit integer | Record type (2) |
| 1 | OOL time | 1-8 | Time format | The time when the parameter was found to be out of limits |
| 2 | Value time | 9-16 | Time format | Time of value |
| 3 | Name | 17-24 | Characters | Name of the parameter as appearing in the MIB |
| 4 | Behaviour number | 25-28 | 32 bit integer | Behaviour in BEHV subsystem |
| 5 | Number of values | 29-30 | 16 bit integer | Number of values |
| 6 | Parameter state | 31-32 | 16 bit integer | Parameter state in BEHV subsystem (0 = nominal, 1 = warning, 2 = OOL, 3 = SCC) |
| 7 | Value | 33-46 | Value | Parameter value |
| Total Length | 47 |  |  |

The reference file is BEHVoolStatusRecord in the BEHV subsystem (taken from [RD5]).

### Value format

Values are specified as Char(14) [RD6] as they can be raw integer, engineering values, or strings depending on context.