The following tables define the form and capability of the SPIRE instrument to be delivered for EQM testing.

Updated 19/2/2002 to reflect expected form of QM1 HSFCU

Unit:  HSFPU

| Subsystem /component | Delivered CQM Form/Capability |
| --- | --- |
| Structure/baffles/wiring standoffs etc | Flight Representative |
| Mirrors | Flight Representative |
| Filters | Flight representative |
| Beam steering mirror | Form and fit compliant Functionally representative in at least one axis No redundancy Electrical interfaces compliant Thermal conduction flight representative Thermal dissipation may not be flight representative |
| 3He Fridge/thermal straps | Form and fit compliant Functionally fully flight representative All parts flight build standard except thermometers and heaters will be commercial/industrial grade |
| 300 mK Thermal control system | None |
| Photometer LW array | Flight representative |
| Photometer MW array | Form and fit compliant Resistors used to represent detectors. Temperature monitors functionally representative (TBC) |
| Photometer SW array | Ditto |
| SMEC | Form and fit compliant Functionally representative – mirror travel TBD Electrical interfaces must be compliant Thermal conduction flight representative Thermal dissipation may not be flight representative |
| Spectrometer SW array | As P/MW and P/SW arrays |
| Photometer LW array | Flight representative |
| Photometer Calibrator | Form and fit compliant Functionally representative Electrical interfaces compliant Thermal interfaces compliant No redundancy (TBC) |
| Spectrometer Calibrator | Form and fit compliant Functionally representative Electrical interfaces compliant Thermal interfaces compliant No redundancy (TBC) |
| Shutter | Form and fit compliant Functionally representative Electrical interfaces compliant |
| JFET Enclosures | Flight Representative |
| JFET Modules and JFET box RF filter modules | Form and fit compliant Functionally representative Electrical interfaces compliant Thermal interfaces compliant Only JFETs for “live” detector channels will be provided Resistors for thermal dissipation in other channels will be provided (TBC) |
| FPU RF Filters | Flight representative |
| Thermometry | Flight representative |
| FPU internal harnesses | Flight representative |

Unit: HSDCU

| Subsystem /component | Delivered CQM Form/Capability |
| --- | --- |
| External structure/mechanical interfaces | Flight representative |
| Electrical Interfaces | Prime interfaces flight representative No redundant interfaces implemented |
| Functionality | Near flight performance on prime side No redundant side implemented |
| Electrical Component Level | Commercial/industrial level parts with near flight performance |

Unit: HSFCU

| Subsystem /component | Delivered CQM Form/Capability |
| --- | --- |
| External structure/mechanical interfaces | Not form and fit compliant - some of the sub-units will not be housed within the FCU flight envelope |
| Electrical Interfaces | Interfaces to S/C not flight representative – EGSE replaces power supply unit Prime instrument interfaces flight representative No redundant interfaces implemented |
| Functionality | Near flight performance on prime side No redundant side implemented |
| Electrical Component Level | Commercial/industrial level parts with near flight performance |

Unit: HSDPU (this unit will also be used for the AVM)

| Subsystem /component | Delivered CQM Form/Capability |
| --- | --- |
| External structure/mechanical interfaces | Flight Representative |
| Electrical Interfaces | Prime interfaces flight representative No redundant interfaces implemented |
| Functionality | Near flight performance on prime side No redundant side implemented |
| Electrical Component Level | Commercial/industrial level parts with near flight performance |

Unit: HSWIH (Warm interconnect harness)

| Subsystem /component | Delivered CQM Form/Capability |
| --- | --- |
| External structure/mechanical interfaces | Flight representative |
| Electrical Interfaces | Flight representative |
| Functionality | Near flight performance |
| Electrical Component Level | Commercial/industrial level parts with near flight performance |