Herschel/SPIRE                                           SPIRE-MSS-PRJ-001023

MULLARD SPACE SCIENCE LABORATORY

| UNIVERSITY COLLEGE LONDON | Author: C BROCKLEY-BLATT |
| --- | --- |

SPIRE – MAIV FLOW CHART

Document Number:  MSSL/SPIRE/SP002.1   29 November 2001

Distribution:

| Spire Project Office | B Winter |  |
| --- | --- | --- |
| ESA PX | A Heske |  |
|  | J Bruston |  |
|  | J Rautakoski |  |
| RAL | B Swinyard |  |
|  | K King |  |
|  | J Delderfield |  |
|  | J Long (Project Office) |  |
| Mullard Space Science Laboratory | A Smith |  |
|  | J Coker |  |
|  | C Brockley-Blatt |  |
|  | A Dibbens |  |
| ATC | C Cunningham |  |
|  | I Pain |  |
|  | T Paul |  |
| Cardiff | M Griffin |  |
|  | P Hargrave |  |
| JPL | J Bock |  |
|  | J Lilienthal |  |
| CEA | L Duband |  |
| Herschel Project | Herschel.Planck@esa.int |  |
| Author: | C Brockley-Blatt | Date: |  |
| Checked: | B Winter | Date: |  |
| Approved: | T Dibbens | Date: |  |

# Change Record

| ISSUE | DATE |  |
| --- | --- | --- |
| 0.1 | September 2001 | New document |
| 1.0 | November 2001 | Issued |

Table of Contents

- Scope of Document

- Documents

  - Glossary

- MAIV Flow Chart

  - Explanation of Symbols

  - Structure Flowchart

## Scope of Document

This document presents the Manufacturing, Assembly, Integration and Test (MAIV) flowchart for the Spire Structure CQM, PFM and FS units.  The manufacture of the STM model should also be derived from this flow chart, although some tasks will not be performed (reduced functionality).  These tasks will be described in detail in the AIV plan.

According to AD1 the following models have to be manufactured:

STM 	- Structural Thermal Model

CQM 	- Cryogenic Qualification Model

PFM 	- Proto Flight Model

FS 	- Flight Spare

AD30 gives the overall view of the use of the different models and lists the various tests and test requirement references for each model. It stipulates that the STM model and the STM testing encompasses the qualification of the structure. The various subsystems mounted within and on the structure will have their own separate qualification tests.  The STM test focuses primarily on the structure, thermal hardware and the qualification test serves as a reference for the subsystem qualification tests.

The CQM model and test serves as a reference for the qualification of the various subsystems. The structure CQM model is the same as the STM structure model. The CQM model will be used in conjunction with the other two instruments (HIFI and PACS) at ESTEC for further verification.

## Documents

All documents are listed in the Figure 3.2 of the CIDL.

# 2.1	Glossary

All terms are listed in the CIDL.

## MAIV Flow Chart

3.1	Explanation of Symbols

## Structure MAIV Flow Chart

## 4.	Integration Notes

The SPIRE instrument consists of a monocoque shell holding a bending stiff optical bench. This optical bench supports a photometer and a spectrometer. All parts of these two measurement devices are mounted on the optical bench. The instrument is mounted on the FIRST optical bench via three interfaces. Two A-frames and a conical fixed point. These interfaces ensure a controlled contraction of the instrument when it is cooled down. The optical bench panel is on one side mounted on the fixed point, the side closest to the optical axis of the telescope. The two A-frames are mounted on the two corners the furthest away from the fixed point. The bending flexible direction of the A-frames is pointing towards the fixed point. Thus making the whole suspension kinematic.

The integration of the Spire structure is a very delicate operation. During the whole process great care has to be taken not to compromise the (future) alignment of the optical components. For this, during the manufacturing of the different parts and especially the optical bench, stress relaxation is required. In between various stages of machining the parts need to be heat treated. This to release as far as possible residual stress left behind after cutting the metal. The machining stages of the parts can be split between the first rough cutting and the final fine cutting. Before the final cutting, where the part is machined within its final tolerances, it is essential to have it heat treated.

The inaccuracy of machining of the various parts will lead to a build up of alignment errors of the structural interfaces upon which the various optical components will be mounted. The build up of this misalignment runs through the whole structure. It starts with the mounting of the instrument, continues through the covers and the optical bench. It is therefore of paramount importance that during integration the build-up of misalignment is minimised and moreover, to ensure that the construction and integration is done such that what ever the misalignment is, it will not change significantly after dismounting and re-mounting the covers.

The total allowable misalignment (error budget) of the optical components is given in AD24. The development plan, giving a listing of the various models required, is AD28. A more detailed description of the structure can be found in AD27.

# Text boxes

Mount Mirrors (See AD3)

Low Level Vibration Test

Rework or remount if needed

Rework or remount if needed

HOB Simulator from RAL

Transport Container

Assemble CSTR4

Bolt RF filter boxes on outer spectrometer panel

Bolt connector panels on outer panels

Mount stray light baffles on CSTR1, CSTR2 and CSTR3

Bolt down CSTR1 and CSTR2 to cooler

External Equipment/GSE

Next Step

Single Item

MIP/KIP

Document/Report

Transport

Process/Action

Test

Test Readiness Review

Post Test Review

Mount covers

Final mounting of outer covers

6

Major Review

Manufacturing Files

Review of Manufacturing Files

Machining of Parts

Minutes of Meeting

Certificate of Conformity

Inspection

Report

Parts Metrology

Plate parts if needed (Allu-chrome by Default)

Bake out parts – 5 days at 80(C

Mount optical bench on MGSE on the HOB simulator

Mount photometer panels – one by one bolting down on optical bench

Bolt panels together

1

1

Integrate stray-light baffles

Check flatness of interface with outer panel

Rework or remount if needed

Bolt down outer panel

Dowel position of photometer cover on optical bench

# Photometer Cover

# Spectrometer Cover

2

Bolt panels together

Mount spectrometer panels – one by one bolting down on optical bench

Dowel position of spectrometer cover on optical bench

Bolt down outer panel

Rework or remount if needed

Check flatness of interface with outer panel

Integrate stray-light baffles

2

Second stage SOB mounted components

Remove spectrometer outer cover

Assemble spectrometer mirror mounts and beam splitters

Check Alignment

1

3

3

Mount RF Filter box

Check relative positions and orientation of interface points

Assemble thermal straps

Remount spectrometer outer cover

Remove photometer outer cover

Assemble photometer mirror mounts

Mount photometer detector box

4

Check relative positions and orientation of interface points

4

Assemble thermal

straps

Remount photometer outer cover

MGSE

Photometer Outer Cover

Spectrometer Outer Cover

Mirror Mounts and Beam Splitters

Mount stray light baffle on thermal busbar

Mount fixed cone on base plate

Mount A-frames on base plate

Lower structure on mounts

Put base plate in transport container

Mount dichroics mounts

Mount Filter mounts

Mount Mirror mounts

Assemble thermal busbar

Mount detectors or D-tool for STM  to thermal busbar

Close detector box

Mount stray light baffle on thermal busbar

Close detector box

Mount detectors to thermal busbar

Mount dichroics mounts

Mount Filters mounts

Mount Mirrors mounts

Assemble thermal busbar

Mount RF Filter box interface frame with SOB edge

Mount RF Filter box into frame

To RAL

Bolt the cooler down on the SOB

Bolt thermal busbars on to the cold finger of the cooler

5

5

Mount BSM on SOB

Route Harness to RF filter boxes

Mount shutter on SOB/stray light baffle

Route Harness to RF filter boxes

Mount SCAL on stray light baffle

Route Harness to RF filter boxes

Mount SMECH in SOB

Route Harness to RF filter boxes

Cleaning and cleaniness monitoring

Packing

Delivery Review Board

ADP

Route Harness to RF filter boxes

6

Optical Alignment Checks (see AD3)

3D Alignment Checks of interfaces

7

7

Mount spectrometer detector box

Check Alignment

8

8