Herschel/SPIRE

MULLARD SPACE SCIENCE LABORATORY

| UNIVERSITY COLLEGE LONDON | Author: C BROCKLEY-BLATT |
| --- | --- |

SPIRE STRUCTURE– FMECA

Document Number:  MSSL/SPIRE/PA005.02    2 December 2002

Distribution:

| Spire Project Office | J Long |  |
| --- | --- | --- |
| ESA PX | A Heske |  |
|  | J Bruston |  |
|  | J Rautakoski |  |
| RAL | B Swinyard |  |
|  | K King |  |
|  | J Delderfield |  |
| Mullard Space Science Laboratory | A Smith |  |
|  | J Coker |  |
|  | C Brockley-Blatt |  |
|  | A Dibbens |  |
|  | B Winter |  |
| Cardiff | M Griffin |  |
|  | P Hargrave |  |
| Herschel Project | Herschel.Planck@esa.int |  |
| Author: | C Brockley-Blatt | Date: |  |
| Checked: | B Winter | Date: |  |
| Approved: | T Dibbens | Date: |  |

# Change Record

| ISSUE | DATE |  |
| --- | --- | --- |
| 0.1 | September 2001 | New document |
| 1.0 | November 2001 | Issued |
| 1.1 | December 2001 | Updated to ESA ECSS-Q-30-02A Standard, functional diagram added, Critical Items List added |
| 1.2 | July 2002 | Updated to reflect the detailed design of the thermal busbar |
| 2.0 | December 2002 | Up issued inline with other documents |

Table of Contents

1.	Scope of Document	4

2.	Documents	4

3.	FMECA	5

4.	Critical Items List	17

# Glossary

All terms are listed in the CIDL.

## Scope of Document

This document presents the results of the FMECA carried out on the SPIRE Structure.

## Documents

All documents are listed in Figure 3.2 of the CIDL.

## FMECA

A failure mode effects and criticality analysis has been performed on all functional elements of the structure which can cause failure effects within the experimentor cause damage to or interfere with, the proper functioning of the SPIRE instrument or HERSCHEL spacecraft.

Most of the pheomena can be captured by structural failure which can be detected by qualification

Each failure effect identified has been given a criticality category according to the definition below:

- Category 1:	Catastrophic - The failure results in loss of the instrument’s function or loss of missions or damage to another instrument (SN = 4)

- Category 2:	Critical - The failure results in loss of the subsystem’s function but the effect is confined to the subsystem. (SN = 3)

- Category 3:	Major - Degradation of subsystem functionality. (SN = 2)

- Category 4:	Negligible - Any other effect (SN = 1)

The following failure modes have been considered:

- Total

- Collapes

- Breaks

- Intermittent

- Distortion

- Thermal or light leak

- Partial

- Plastic deformation

- Misalignment

- Degration

- Degradation

The probability figures are:

- Probable			PN = 4

- Ocassional		PN = 3

- Remote			PN = 2

- Extremely remote		PN = 1

Design specifications, descriptions, functional diagrams etc, used in the preparation of the FMECA shall be attached or referenced.

3.1 Functional Diagram

3.2.	Column Descriptions

The following data elements are shown in the FMECA analysis sheet:

- Identification Number – Each failure mode and effect will have an unique number for treaceability purposes.

- Item – The name of the item of the subsystem being analysed.

- Function – A statement of the function performed by the item.

- Failure mode – All potential failure modes of the item under analysis are identified and described.

- Failure  Cause – The most probable cause associated with the failure mode.

- Mission Phase – The phase of the mission in which the failure is most likely to occur, be it testing or flight for example.

- Failure Effects – The consequences of each assumed failure, be it local or end effects.

- Severity Classification – The severity category.

- Failure Detection Method – A description by which occurrence of the failure mode is detected or observed, be it warning devices, sensing or none.

- Compensating Provisions – The actions that reduce or nullify the effects of the failure

- Severity Number, SN – The number assigned which is consistent with the severity category

- Probability Number, PN – The number assigned to the probability of the occurrence of the failure.

- Criticality Number, CN – The multiplication of the severity and probability numbers.

- Corrective actions – Corrective actions to prevent failure.

- Remarks – Any pertinent remarks relevant to and clarifying any other column.

| ID | Item | Function | Failure Mode | Failure Cause | Mission Phase | Failure Effect a) Local Effects b)End Effects | Severity | Failure Detection Method/Observable symptoms | Provisions | Severity Number SN | Probability PN | Criticality Number CN | Actions | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SS001 | Suspension | Supports Instrument on HOB | Collapses or breaks | Launch | Flight | Loss of instrument | 1 | Thermal performance | None | 4 | 2 | 8 | Sufficient design margin Replace Suspension |  |
| SS002 |  |  |  | Another instrument hitting SPIRE | Flight/Test | Thermal short, misalignment | 1 | Thermal performance | None | 4 | 2 | 8 | Sufficient design margin, non contact constraint |  |
| SS003 |  |  |  | Pre-flight handling and integration | Flight | Thermal short, misalignment | 1 | Thermal performance | None | 4 | 3 | 12 | Visual check before launch |  |
| SS004 |  |  | Plastic deformation | Launch | Flight | Loss of instrument | 1 | Alignment | None | 4 | 2 | 8 | Sufficient design margin |  |
| SS005 |  |  |  | Another instrument hitting SPIRE | Flight/Test | Thermal short, misalignment | 1 | Thermal performance | None | 4 | 2 | 8 | Sufficient design margin, non contact constraint |  |
| SS006 |  |  |  | Pre-flight handling and integration | Flight | Thermal short, misalignment | 1 | Alignment, using the optical cube | None | 4 | 3 | 12 | Replace suspension |  |

| ID | Item | Function | Failure Mode | Failure Cause | Mission Phase | Failure Effect a) Local Effects b)End Effects | Severity | Failure Detection Method /Observable symptoms | Provisions | Severity Number SN | Probability PN | Criticality Number CN | Actions | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SS007 | Cover panels | Stiffness and stray light and RF shielding | Stray light or RF leak | Dent | Test | Minor misalignment of instrument internally | 2 | Identify a misalignment or thermal short | None | 3 | 3 | 9 | Visual inspection before launch |  |
| SS008 | Spire Optical Bench | Stiffness and mounting provision for all other subsystems | Distortion | Prestress due to mishandling | Integration | Misalignment | 2 | Misalignment | None | 3 | 2 | 6 | Prelaunch check Training in integration procedure |  |
| SS009 | Thermal Straps | Provide conduction path | Breaks | Fatigue | Test/Flight | Loss of thermal conductance | 1 | Thermal performance, instrument performance | None | 4 | 3 | 12 | Sufficient margin Design for non fatigue critical |  |
| SS010 |  |  | Deformation | Mishandling | Test/Flight | Thermal short | 1 | Thermal performance, instrument performance | None | 4 | 2 | 8 | Visual inspection before launch |  |
| SS011 |  |  | Degradation of contact | Thermal or mechanical cycling | Flight | Loss of thermal conductance | 1 | Thermal performance, instrument performance | None | 4 | 1 | 4 | Instrument health check. sufficient design margin & qualification testing with regard to fatigue |  |

| ID | Item | Function | Failure Mode | Failure Cause | Mission Phase | Failure Effect a) Local Effects b)End Effects | Severity | Failure Detection Method/ Observable symptoms | Provisions | Severity Number SN | Probability PN | Criticality Number CN | Actions | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SS012 | Thermal Busbar | Provide 0.3K thermal path to detectors | Loss of suspension | Mechanical overload | Test/Flight | Loss of one detector | 2 | Thermal performance, detector performance | None | 3 | 2 | 6 | Sufficient design margin Engineering tests |  |
| SS013 |  |  |  |  | Test/Flight | Loss of all detectors | 1 | Thermal performance, detector performance | None | 4 | 2 | 8 | Sufficient design margin Engineering tests |  |
| SS014 |  |  | Work hardening | Repeated integrations | Test/Flight | Degradation of performance | 2 | Thermal performance, detector performance | None | 3 | 3 | 9 | Engineering tests, CQM and FM Tests | Sufficient design margin |
| SS015 |  |  | Breaking | Repeated integrations or mechanical loading | Test/Flight | Loss of one detector | 2 | Thermal performance, detector performance | None | 3 | 2 | 6 | Engineering tests, CQM and FM Tests | Sufficient design margin |
| SS016 |  |  |  |  | Test/Flight | Loss of all detectors | 1 | Thermal performance, detector performance | None | 4 | 2 | 8 | Engineering tests | Sufficient design margin |
| SS017 |  |  | Loss of electrical isolation | Breakage of insulation | Test/Flight | Loss of one detector | 2 | Thermal performance, detector performance | None | 3 | 2 | 6 | Engineering tests, CQM and FM Tests | Sufficient design margin |
| SS018 |  |  |  |  | Test/Flight | Loss of all detectors | 1 | Thermal performance, detector performance | None | 4 | 2 | 8 | Engineering tests, CQM and FM Tests | Sufficient design margin |

| ID | Item | Function | Failure Mode | Failure Cause | Mission Phase | Failure Effect a) Local Effects b)End Effects | Severity | Failure Detection Method/ Observable symptoms | Provisions | Severity Number SN | Probability PN | Criticality Number CN | Actions | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SS019 | Thermal Busbar | As above | Misalignment | Vibration testing | Test | Loss of one detector | 2 | Detector performance | None | 3 | 2 | 6 | Engineering tests | Sufficient design margin |
| SS020 | Mirror Mounts | Supports mirrors | Misalignment | Mishandling during integration | Test | Misalignment | 1 | Instrument performance | None | 4 | 2 | 8 |  | Alignment verification |
| SS021 |  |  | Break | Launch | Flight | Loss of alignment - common mirror | 1 | Instrument failure | None | 4 | 2 | 8 |  | Sufficient design margin |
| SS022 |  |  |  |  | Test/Flight | Loss of alignment -a mirror in spectrometer or photometer | 2 | Instrument performance | None | 3 | 2 | 6 | Q-Test | Sufficient design margin |
| SS023 | Photometer 2K Detector box and supports | Supports photometer detectors, stray light | Breakage | Launch | Flight | Loss of instrument | 1 | Measuring thermal performance | None | 4 | 2 | 8 | Qualification testing | Sufficient design margin |
| SS024 |  |  |  | Pre-flight handling or integration | Flight | Thermal short or misalignment | 1 | Measuring thermal performance | None | 4 | 2 | 8 | Qualification testing | Sufficient design margin |
| SS025 |  |  | Plastic deformation | Launch | Flight | Misalignment | 1 | Instrument performance | None | 4 | 2 | 8 | Visual inspection and Protoflight testing | Sufficient design margin Qualification testing |

| ID | Item | Function | Failure Mode | Failure Cause | Mission Phase | Failure Effect a) Local Effects b)End Effects | Severity | Failure Detection Method/ Observable symptoms | Provisions | Severity Number SN | Probability PN | Criticality Number CN | Actions | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SS026 |  |  |  | Pre-flight handling or integration | Flight | Thermal short or misalignment | 1 | Alignment | None | 4 | 2 | 8 | Visual inspection and Protoflight testing | Sufficient design margin |
| SS027 | Spectrometer 2K detector box and supports | Supports spectrometer detectors, stray light and RF baffle | Breakage | Launch | Flight | Loss of instrument | 1 | Measuring thermal performance | None | 4 | 2 | 8 | Qual-ification testing | Sufficient design margin |
| SS028 |  |  |  | Pre-flight handling or integration | Flight | Thermal short or misalignment | 1 | Measuring thermal performance | None | 4 | 2 | 8 | Visual inspection and protoflight testing | Sufficient design margin |
| SS029 |  |  | Plastic deformation | Launch | Flight | Misalignment | 1 |  | None | 4 | 2 | 8 |  |  |
| SS030 |  |  |  | Pre-flight handling or integration | Flight | Thermal short or misalignment | 1 | Alignment | none | 4 | 2 | 8 | Visual inspection and protoflight testing | Sufficient design margin |

| ID | Item | Function | Failure Mode | Failure Cause | Mission Phase | Failure Effect a) Local Effects b)End Effects | Severity | Failure Detection Method/ Observable symptoms | Provisions | Severity Number SN | Probability PN | Criticality Number CN | Actions | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SS031 | Stray light Baffles :General | Stray light shielding | Bent | Mishandling during integration | Test/Flight | Increase in background noise for detectors | 3 | Instrument performance | None | 2 | 3 | 6 | Visual check | Careful handling |
| SS032 |  |  |  |  | Test/Flight | Loss of field of view | 2 | Instrument performance | None | 3 | 3 | 9 | Visual check | Careful handling |
| SS033 |  |  |  |  | Test/Flight | Obscures common beam | 1 | Instrument performance | None | 4 | 3 | 12 | Visual check | Careful handling |
| SS034 | Feed thorough | Stray light shielding at thermal strap entry to different thermal zones | 4K- thermal short | Misalignment | Test/Flight | Degradation of thermal performance | 2 | Thermal performance | None | 3 | 2 | 6 | Visual check and measure | Tolerance on alignment |

| ID | Item | Function | Failure Mode | Failure Cause | Mission Phase | Failure Effect a) Local Effects b)End Effects | Severity | Failure Detection Method/ Observable symptoms | Provisions | Severity Number SN | Probability PN | Criticality Number CN | Actions | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SS035 | Feed Through |  | 2K- thermal short | Misalignment | Test/Flight | Degradation of thermal performance | 1 | Thermal performance | None | 4 | 2 | 8 | Visual check and measure | Tolerance on alignment |
| SS036 | Filters | Supports of the filters | Popping out its frame | Differential in pressure | Test | Damage to filters | 2 |  | None | 3 | 2 | 6 |  | Ensure adequate venting/control pump down |
| SS037 | Beam Spilitters/ Dichroics | Supports the beam and splitters and dichroics | Distortion | Asymmetric stressing | Test/Flight | Misalignment | 2 | Instrument performance | None | 3 | 2 | 6 |  | Mounts design symmetrical - 3 point mount |
| SS038 |  |  | Break | Launch | Flight | Loss of alignment - common mirror | 1 | Instrument failure | None | 4 | 1 | 4 |  |  |
| SS039 |  |  |  |  | Flight | Loss of alignment -a mirror in spectrometer or photometer | 2 | Instrument performance | None | 3 | 2 | 6 | Qualification testing | Sufficient design margin |

| ID | Item | Function | Failure Mode | Failure Cause | Mission Phase | Failure Effect a) Local Effects b)End Effects | Severity | Failure Detection Method/ Observable symptoms | Provisions | Severity Number SN | Probability PN | Criticality Number CN | Actions | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SS040 | Alignment cubes | Tool for alignment of instrument | Misalignment | Wrong reference for alignment of instrument | Test | Delay in test schedule | 3 | ?????? |  | 2 | 3 | 6 | Careful handling |  |
| SS041 | Thermistors | Measure the temperature of a part | Failure to operate | Broken or disconnected | Test/Flight | wrong temperature reading | 3 | Thermal testing | Redundancy | 2 | 3 | 6 |  |  |
| SS042 |  |  |  |  | Test/Flight | no temperature | 3 | Thermal testing | Redundancy | 2 | 3 | 6 |  |  |
| SS043 | Assembly jig | Support instrument during integration | Damage to instrument | Over constrained or lack of stiffness | Integration | misalignment | 2 | Visual inspection |  | 3 | 2 | 6 | No hypostatic mounting (no more than 6 degrees of freedom) |  |
| SS044 |  |  | Misalignment | Over constrained or lack of stiffness | Integration | Misalignment | 3 | Visual inspection |  | 2 | 2 | 4 | no hypostatic mounting adherence to integration alignment requirements (the way the alignment) |  |

## Critical Items List

| Item | Action |
| --- | --- |
| Suspension | Sufficient design margin, non contact constraint, Replace suspension between models |
| Thermal Busbar | Instrument health check. sufficient design margin & qualification testing with regard to fatigue |
| Mirror Mounts | Alignment verification, Sufficient design margin |
| Photometer 2K Detector box and supports | Sufficient design margin, Qualification testing |
| Sprctrometer 2K Detector box and supports | Sufficient design margin, Qualification testing |
| Straylight Baffle | Visual check |
| Feed through | Visual check and measure, Tolerance on alignment |
| Beam Splitters | Sufficient design margin, Qualification testing |

Page left intentionally blank

# Text boxes

Assembly Jig

Thermistors

Alignment Cubes

SBS/Dichroic Mounts

Filter Mounts

Stray Light Baffles

Spectrometer 2K Detector Box

Photometer 2K Detector Box

Mirror Mounts

Thermal Busbar

Thermal Straps

Spire Optical Bench

Cover Panels

Suspension

Structure