Herschel/SPIRE                                           SPIRE-MSS-PRJ-001024

MULLARD SPACE SCIENCE LABORATORY

| UNIVERSITY COLLEGE LONDON | Author: C BROCKLEY-BLATT |
| --- | --- |

SPIRE – FMECA

Document Number:  MSSL/SPIRE/PA005.1   29 November 2001

Distribution:

| Spire Project Office | B Winter |  |
| --- | --- | --- |
| ESA PX | A Heske |  |
|  | J Bruston |  |
|  | J Rautakoski |  |
| RAL | B Swinyard |  |
|  | K King |  |
|  | J Delderfield |  |
|  | J Long (Project Office) |  |
| Mullard Space Science Laboratory | A Smith |  |
|  | J Coker |  |
|  | C Brockley-Blatt |  |
|  | A Dibbens |  |
| ATC | C Cunningham |  |
|  | I Pain |  |
|  | T Paul |  |
| Cardiff | M Griffin |  |
|  | P Hargrave |  |
| JPL | J Bock |  |
|  | J Lilienthal |  |
| CEA | L Duband |  |
| Herschel Project | Herschel.Planck@esa.int |  |
| Author: | C Brockley-Blatt | Date: |  |
| Checked: | B Winter | Date: |  |
| Approved: | T Dibbens | Date: |  |

# Change Record

| ISSUE | DATE |  |
| --- | --- | --- |
| 0.1 | September 2001 | New document |
| 1.0 | November 2001 | Issued |

Table of Contents

- Scope of Document

- Documents

- FMECA

# Glossary

All terms are listed in the CIDL.

## Scope of Document

This document presents the results of the FMECA carried out on the SPIRE Structure.

## Documents

## All documents are listed in Figure 3.2 of the CIDL.

## FMECA

A failure mode effects and criticality analysis has been performed on all functional elements of the structure which can cause failure effects within the experimentor cause damage to or interfere with, the proper functioning of the SPIRE instrument or HERSCHEL spacecraft.

Most of the pheomena can be captured by structural failure which can be detected by qualification

Each failure effect identified has been given a criticality category according to the definition below:

- Category 1:	The failure effect is not confined to the subsystem.  When this failure also results in loss or degradation of the instrument’s function, this shall be stated.

- Category 2:	The failure results in loss or degradation of the subsystem’s function but the effect is confined to the subsystem.

- Category 3:	Minor internal subsystem failures.

The following attributes have been added to the criticality category as appropriate:

- “R”, if the design contains a redundant item which can perform the same function

- “SH”, if the failure effect causes a safety hazard

- “SPF”, if the failure is caused by a single point failure

The following failure modes have been considered:

- Total

-	Premature operation

-	Failure to operate (at the prescribed time)

-	Failure to cease operation (at the prescribed time)

- Failure during operation

- Mechanical failure

- Intermittent

-	For failure at component level e.g. hardware interface

- Short circuit

- Open circuit

- Incorrect function e.g. from single event upset – ex:latch ups

-	Incorrect commands or sequence of commands

- Partial

-	Incorrect software functions

- Degradation

-	Degradation or out of tolerance operation

Design specifications, descriptions, functional diagrams etc, used in the preparation of the FMECA shall be attached or referenced.

| ID | Item | Function | Failure Mode | Failure Cause | Failure Effect | Severity | Detection | Provisions | Actions |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Suspension | Supports Instrument on HOB | Collapses or breaks | Launch | Loss of instrument | 1SPF | Thermal performance | Sufficient design margin |  |
|  |  |  |  | Another instrument hitting SPIRE | Thermal short, misalignment | 1SPF | Thermal performance | Sufficient design margin, non contact constraint |  |
|  |  |  |  | Pre-flight handling and integration | Thermal short, misalignment | 1SPF | Thermal performance | Visual check before launch |  |
|  |  |  | Plastic deformation | Launch | Loss of instrument | 1 | Alignment | Sufficient design margin |  |
|  |  |  |  | Another instrument hitting SPIRE | Thermal short, misalignment | 1 | Thermal performance | Sufficient design margin, non contact constraint |  |
|  |  |  |  | Pre-flight handling and integration | Thermal short, misalignment | 1 | Alignment, using the optical cube | Replace suspension |  |

| ID | Item | Function | Failure Mode | Failure Cause | Failure Effect | Severity | Detection | Provisions | Actions |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2 | Cover panels | Stiffness and stray light and RF shielding | Stray light or RF leak | Dent | Minor misalignment of instrument internally | 2 | Identify a misalignment or thermal short | Visual inspection before launch |  |
| 3 | Spire Optical Bench | Stiffness and mounting provision for all other subsystems | Distortion | Prestress due to mishandling | Misalignment | 2 | Misalignment | Prelaunch check | Training in integration procedure |
| 4 | Thermal Straps | Provide conduction path | Breaks | Fatigue | Loss of thermal conductance | 1SFP | Thermal performance, instrument performance | Sufficient margin | Design for non fatigue critical |
|  |  |  | Deformation | Mishandling | Thermal short | 1SFP | Thermal performance, instrument performance | Visual inspection before launch |  |
|  |  |  | Degradation of contact | Thermal or mechanical cycling | Loss of thermal conductance | 1 | Thermal performance, instrument performance | Instrument health check and sufficient design margin and qualification testing | Qualification testing with regard to fatigue |
| ID | Item | Function | Failure Mode | Failure Cause | Failure Effect | Severity | Detection | Provisions | Actions |
| 5 | Thermal busbar | Provide 0.3K thermal path to detectors | Loss of suspension | Mechanical overload | Loss of one detector | 2 | Thermal performance, detector performance | Sufficient design margin | Engineering tests |
|  |  |  |  |  | Loss of all detectors | 1 | Thermal performance, detector performance | Sufficient design margin | Engineering tests |
|  |  |  | Work hardening | Repeated integrations | Degradation of performance | 2 | Thermal performance, detector performance | Sufficient design margin | Engineering tests, CQM and FM Tests |
|  |  |  | Breaking | Repeated integrations or mechanical loading | Loss of one detector | 2 | Thermal performance, detector performance | Sufficient design margin | Engineering tests, CQM and FM Tests |
|  |  |  |  |  | Loss of all detectors | 1 | Thermal performance, detector performance | Sufficient design margin | Engineering tests |

| ID | Item | Function | Failure Mode | Failure Cause | Failure Effect | Severity | Detection | Provisions | Actions |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 6 | Mirror Mounts | Supports mirrors | Misalignment | Mishandling during integration | Misalignment | 1 | Instrument performance | Alignment verification |  |
|  |  |  | Break | Launch | Loss of alignment - common mirror | 1 | Instrument failure | Sufficient design margin | Q-Test |
|  |  |  |  |  | Loss of alignment -a mirror in spectrometer or photometer | 2 | Instrument performance | Sufficient design margin | Qualification testing |
| 7 | Photometer 2K Detector box and supports | Supports photometer detectors, stray light | Breakage | Launch | Loss of instrument | 1SPF | Measuring thermal performance | Sufficient design margin | Qualification testing |
|  |  |  |  | Pre-flight handling or integration | Thermal short or misalignment | 1 | Measuring thermal performance | Sufficient design margin | Visual inspection and Protoflight testing |
|  |  |  | Plastic deformation | Launch | Misalignment | 1SPF | Instrument performance | Sufficient design margin | Qualification testing |
|  |  |  |  | Pre-flight handling or integration | Thermal short or misalignment | 1 | Alignment | Sufficient design margin | Visual inspection and Protoflight testing |
| ID | Item | Function | Failure Mode | Failure Cause | Failure Effect | Severity | Detection | Provisions | Actions |
| 8 | Spectrometer 2K detector box and supports | Supports spectrometer detectors, stray light and RF baffle | Breakage | Launch | Loss of instrument | 1SPF | Measuring thermal performance | Sufficient design margin | Qualification testing |
|  |  |  |  | Pre-flight handling or integration | Thermal short or misalignment | 1 | Measuring thermal performance | Sufficient design margin | Visual inspection and protoflight testing |
|  |  |  | Plastic deformation | Launch | Misalignment | 1SPF |  |  |  |
|  |  |  |  | Pre-flight handling or integration | Thermal short or misalignment | 1 | Alignment | Sufficient design margin | Visual inspection and protoflight testing |
| 9 | Stray light Baffles |  |  |  |  |  |  |  |  |
| 9a | General | Stray light shielding | Bent | Mishandling during integration | Increase in background noise for detectors | 3 | Instrument performance | Careful handling | Visual check |
|  |  |  |  |  | Loss of field of view | 2 | Instrument performance | Careful handling | Visual check |
|  |  |  |  |  | Obscures common beam | 1 | Instrument performance | Careful handling | Visual check |

| ID | Item | Function | Failure Mode | Failure Cause | Failure Effect | Severity | Detection | Provisions | Actions |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 9b | Feed thorough | Stray light shielding at thermal strap entry to different thermal zones | 4K- thermal short | Misalignment | Degradation of thermal performance | 2 | Thermal performance | Tolerance on alignment | Visual check and measure |
|  |  |  | 2K- thermal short | Misalignment | Degradation of thermal performance | 1 | Thermal performance | Tolerance on alignment | Visual check and measure |
| 10 | Non Mirror Optics mounts |  |  |  |  |  |  |  |  |
| 10a | Filters | Supports of the filters | Popping out its frame | Differential in pressure | Damage to filters | 2 |  | Ensure adequate venting/control pump down |  |
| 10b | Beam Spilitters/Dichroics | Supports the beam and splitters and dichroics | Distortion | Asymmetric stressing | Misalignment | 2 | Instrument performance | Mounts design symmetrical - 3 point mount |  |
|  |  |  | Break | Launch | Loss of alignment - common mirror | 1 | Instrument failure |  |  |
|  |  |  |  |  | Loss of alignment -a mirror in spectrometer or photometer | 2 | Instrument performance | Sufficient design margin | Qualification testing |
| ID | Item | Function | Failure Mode | Failure Cause | Failure Effect | Severity | Detection | Provisions | Actions |
| 11 | Alignment cubes | Tool for alignment of instrument | Misalignment | Wrong reference for alignment of instrument | Delay in test schedule | 3 | ?????? | Careful handling |  |
| 12 | Thermistors | Measure the temperature of a part | Failure to operate | Broken or disconnected | wrong temperature reading | 3R | Thermal testing |  |  |
|  |  |  |  |  | no temperature | 3R | Thermal testing |  |  |
| 13 | Assembly jig | Support instrument during integration | Damage to instrument | Over constrained or lack of stiffness | misalignment | 2 | Visual inspection | No hypostatic mounting (no more than 6 degrees of freedom) | Sound engineering practice |
|  |  |  | Misalignment | Over constrained or lack of stiffness | Misalignment | 3 | Visual inspection | no hypostatic mounting (no more than 6 degrees of freedom), adherence to integration alignment requirements (the way the alignment) | Sound engineering practice |

## Page left intentionally blank