| IID CHANGE REQUEST | HERSCHEL / PLANCK | REF. H-P-ASPI-CR-0021 Page 1/3 |
| --- | --- | --- |
| Instrument | Subsystem/Unit | Title of change: all clerical errors Alcatel comments 2, 8 10 |
| AFFECTED DOCUMENTATION: IID-A Document No:SCI-PT-IIDA 04624. Issue 2.0 Chapter/Requirement: |
| REASON / JUSTIFICATION OF CHANGE (incl. impact of no-change, if appropriate): Correct clerical errors. |

DESCRIPTION OF REQUESTED CHANGE (OR NEW TEXT):

==================================

1: Consistency mass allocation IID A-B

(Alcatel comments 2)

Modify Herschel Instrument mass distribution between Optical bench, Cryostat and SVM to reflect updates of IID-B's (consistency between IID-A and IID-B) (Alcatel comment 2)

5.5.4.1

| Interface | Max. allocated Mass [kg] | Remarks |
| --- | --- | --- |
| Optical Bench | 179 (175.5 | All FPU’s (including SPIRE JFET and RF filter module) |
| Cryostat | 35(39.6 | Includes a Bolometer Amplifier Unit and the HIFI Local Oscillator Unit (with radiator) |
| SVM | 201(199.9 | Warm units of all three instruments and Local Oscillator Unit wave-guides |
| Total | 415 |  |

===========================================

Alcatel comment 8

5.11.3. Timing

Replace

A unique on-board time, the TAI (Temps Atomique International – ref. 1958 January epoch), is maintained at spacecraft level and distributed to the instruments in order to time-tag their data, which will be embedded in their telemetry packets.

By

A unique on-board time, the Central Time Reference ( CTR ) is maintained at spacecraft level and distributed to the instruments in order to time-tag their data, which will be embedded in their telemetry packets.

=============================================

Alcatel comment 10

5.12.7: Planck Reference Star Pulse

Replace

For the Planck mission, the ACMS will provide the reference star signal.

For the Planck mission, the ACMS will provide the precise instant (+/- 1.5 msec) at which the field of  view of the star mapper moved across the reference star and transmit it to ground.

The reference star pulse and precise instant as above described will be distributed to he Planck instruments with maximum delay of 5 msec.

By

For the Planck mission, the ACMS will provide the spin reference message.

For the Planck mission, the ACMS will provide the precise instant (+/- 1.5 msec) at which the the spin reference message is generated and transmit it to ground.

The spin reference message and precise instant as above described will be distributed to he Planck instruments with maximum delay of 1sec.

==============================================

Comments from Meeting HP-ASPI-MN-581: AI 10

5.7.1.5: remove existing text, replace by TBD

5.7.1.6: Remove text and table, replace by NA

5.7.2.3.5: Remove text and table, replace by NA

5.6.1.1 Replace the number of fixation points for FPU.

Replace:

"The number of fixation points is different for each experiment: PACS 6, HIFI 3 and SPIRE 3 or 4."

by

"The number of fixation points is different for each experiment: PACS 3, HIFI 4 and SPIRE 3."

Rem: Astrium shall prepare a new section 5.6.1, according to the current OB & FPU accomodation design for further issue

| ORIGINATOR | DATE |
| --- | --- |
| APPROVED BY |
| Project Manager Date | Project Controller Date |
| PA Manager Date | Configuration Manager Date |

| ASSESSMENT / IMPACT OF CHANGE |
| --- |
| System Design: None |
| Schedule: none |
| Cost: |
| Analyst: Approved by: | Date: |

| IID CHANGE REQUEST | HERSCHEL / PLANCK | REF. H-P-ASPI-CR-0022 Page 1/3 |
| --- | --- | --- |
| Instrument All | Subsystem/Unit | Title of change: Riples & inrush current (Alcatel comment # 5 and 6) |
| AFFECTED DOCUMENTATION: IID-A Document No:SCI-PT-IIDA 04624. Issue 2.0 Chapter/Requirement:5.11.3 & 5.11.5.1 |
| REASON / JUSTIFICATION OF CHANGE (incl. impact of no-change, if appropriate): Change amplitude of ripples to ensure compatibility with the spacecraft (consistency between IID-A and GDIR) |

DESCRIPTION OF REQUESTED CHANGE (OR NEW TEXT):

5.9.5.3.2. Ripple and Spikes

replace

"The equipment shall operate with nominal performance when subject to the following main bus conditions:

140 mVpp Main Bus ripple

240mVpp Commutation spikes."

By

"The ripple and spikes shall be less than (at Distribution Unit output connectors):

• 300 mV peak to peak on 28 V lines.

This peak to peak value is defined in a 50 MHz bandwidth."

==============================================================================

5.9.5.6.4. Inrush Current

replace:

"Inrush current is limited by the spacecraft PDU LCL to a maximum of 1.5 times the short peak value. At LCL switch-on the inrush current is limited by the PDU LCL as well as the inductance in the user input circuit.

Inrush current is limited by the PDU LCL to a value between the instantaneous peak value and 1.5 times the instantaneous short peak value.

Inrush current duration duration is set the PDU LCL. To prevent LCL trip-off users shall limit the inrush current duration to a maximum change of 5A*msec (tbc). LCL users shall limit the rate of change of inrush current to 1A/microsec."

By

At power ON of the Distribution Unit power line via the LCL, the inrush current is limited to a value comprised between 1.2 Imax (TBC) and 1.5 Imax (TBC) during a duration t (minimum value guaranteed: 10 ms)

If the inrush current demand from the user is not under limitation value at t tripoff the equipment will be switched off.

Figure 5.9.5.6.4.1 gives the nominal current envelope.

The instantaneous rate of change of current (dI/dt) variation shall not exceed

10-6 A/s either positive or negative.

| ORIGINATOR | DATE |
| --- | --- |
| APPROVED BY |
| Project Manager Date | Project Controller Date |
| PA Manager Date | Configuration Manager Date |

| ASSESSMENT / IMPACT OF CHANGE |
| --- |
| System Design: |
| Schedule: |
| Cost: |
| Analyst: Approved by: | Date: |

| IID CHANGE REQUEST | HERSCHEL / PLANCK | REF. H-P-ASPI-CR-0023 Page 1/2 |
| --- | --- | --- |
| Instrument All | Subsystem/Unit | Title of change: Timing requirements (alcatel comment 9) |
| AFFECTED DOCUMENTATION: IID-A Document No:SCI-PT-IIDA 04624. Issue 2.0 Chapter/Requirement: 5.5.4.1 |
| REASON / JUSTIFICATION OF CHANGE (incl. impact of no-change, if appropriate): Modify timing stability requirement to be consistent with System Requirement and CDMU specification |

DESCRIPTION OF REQUESTED CHANGE (OR NEW TEXT):

5.11.5.1. Synchronisation Signal

replace

"A redundant, electrically isolated synchronisation signal with a frequency of

131072Hz and an overall stability of better than 1*10 -8 over 30 days will be delivered

to each instrument."

By

"A redundant, electrically isolated synchronisation signal with a frequency of

131072Hz and an overall stability of better than 1*10 -6 will be delivered to each instrument."

| ORIGINATOR | DATE |
| --- | --- |
| APPROVED BY |
| Project Manager Date | Project Controller Date |
| PA Manager Date | Configuration Manager Date |

| ASSESSMENT / IMPACT OF CHANGE |
| --- |
| System Design: The system performances are not consistent with requests from LFI IID-B (6E-9) |
| Schedule: none |
| Cost: |
| Analyst: Approved by: | Date: |

| IID CHANGE REQUEST | HERSCHEL / PLANCK | REF. H-P-ASPI-CR-0024 Page 1/4 |
| --- | --- | --- |
| Instrument Herschel | Subsystem/Unit HPLM | Title of change: EMC changes (Alcatel comments 7,11,12,13) |
| AFFECTED DOCUMENTATION: IID-A Document No:SCI-PT-IIDA 04624. Issue 2.0 Chapter/Requirement: |
| REASON / JUSTIFICATION OF CHANGE (incl. impact of no-change, if appropriate): (Alcatel comments to IID-A ) |

DESCRIPTION OF REQUESTED CHANGE (OR NEW TEXT):

| Pages Affected | Text to the change |  |
| --- | --- | --- |
| 5-61 (alcatel comment 7 | § 5.10.3.5 Correction : “Commentary : In case DC-to-DC converters are manufactured « ad hoc » for specific applications, it is recommended to use static shields between primary and secondary windings of the transformer. It would reduce the capacitive coupling between primary and secondary side. This static shield should be connected to the primary power return line chassis via a low inductance strap.” Rationale : the connection of the static shield to the primary power return line would provide only HF differential mode rejection, but no common mode rejection at all, unlike the connection of the static shield to chassis. |  |
| 5-86 (alcatel comment 11 | § 5.14.3.9 Figure 5.14.3-6 replaced by the following one : Rationale : the notch corresponds to the S/C TC band. |  |
| 5-87 (alcatel comment 12) | § 5.14.3.13 Correction : “No malfunction, degradation of performance or deviation beyond the tolerance indicated in its individual specification shall occur when the subsystem equipment and its interface lines are exposed to a repetitive electrostatic arc discharge of at least 5.6 15 mJ energy/ 15 kV. The current rise time shall be less than 10 ns. For conducted test only, if damage risks are envisaged for interface circuits, the voltage can be reduced down to 4 kV but the energy shall remain 5.6mJ.” Rationale : energy level changed from 5.6 mJ to 15 mJ to be consistent with SRS. Rise time specified, as critically affects the ESD current coupling to circuits. |  |
| 5-88 (alcatel comment 13 | Paragraphs 5.14.4 through 5.14.6 cancelled Rationale : agreed in EMC/Power WG meeting #9, the detailed information being in the IID-B's. |  |

| ORIGINATOR | DATE |
| --- | --- |
| APPROVED BY |
| Project Manager Date | Project Controller Date |
| PA Manager Date | Configuration Manager Date |

| INDUSTRY ASSESSMENT / IMPACT OF CHANGE |
| --- |
| System Design: |
| Schedule: none |
| Cost: |
| Analyst: Approved by: | Date: |

| IID CHANGE REQUEST | HERSCHEL / PLANCK | REF. H-P-ASPI-CR-0025 Page 1/5 |
| --- | --- | --- |
|  |  | Originator: B.Collaudin/P.Rideau |
| Instrument | Subsystem/Unit | Title of change: Tests requirements Alcatel comments 14, 15, 16 |
| AFFECTED DOCUMENTATION: IID-A Document No:SCI-PT-IIDA 04624. Issue 2.0 Chapter/Requirement: |
| REASON / JUSTIFICATION OF CHANGE (incl. impact of no-change, if appropriate): Consistency with EVTR. (Environment and test requirements) |

DESCRIPTION OF REQUESTED CHANGE (OR NEW TEXT):

==================================

(Alcatel comment 14)

9.5.2:  test level tolerances

change table  (old)

| Parameter | Remark | Tolerances |
| --- | --- | --- |
| Temperature (ambient) | Tmax and Tmin are the max. and min. nominal temperatures for a specific test | Tmax: + 0(C … + 3(C Tmin: - 0(C … - 3(C |
| Temperature (cryogenic) |  | To be tailored to test and temperature range |
| Pressure | Equal or above 0.1 mbar: Below 0.1 mbar: | 10% 50% |
| Relative Humidity |  | ± 5% |
| Sinusoidal Vibrations | Acceleration Frequency above 50 Hz | +/- 10% ± 2% |
| Random Vibrations | Power spectrum density (50 Hz or narrower): 20 to 500 Hz 500 to 2000 Hz Overall g RMS | ±1.5 dB ± 3 dB ± 1.5 dB |
| Static Force |  | ± 5% |
| Acoustic | see tolerances in |  |
| Mechanical Shock | ±0.05xA where A is peak response from semi-sinusoidal shock pulse |  |
| For the mass properties measurements, the following tolerances apply: |  |  |
| Weight |  | ( 1% |
| Centre of Gravity |  | ( 1% |
| Moments of Inertia |  | ( 5% |
| For the electromagnetic compatibility, the following tolerances apply : |  |  |
| Voltage Amplitude |  | 5% of the peak value |
| Current Amplitude |  | 5% of the peak value |
| RF Amplitude |  | tbd |
| Frequency |  | tbd |
| Distance |  | tbd |
| For the magnetic properties, the following tolerances apply : |  |  |
| Mapping distance measurement: |  | tbd |
| Displacement of assembly Centre of Gravity (COG) from rotation axis: |  | ± 5 cm |
| Vertical displacement of single probe centre line from COG assembly: |  | ± 5 cm |
| Mapping turntable angular displacement: |  | tbd |
| Magnetic field strength: |  | tbd |
| Repeatability of magnetic measurements (short term): |  | tbd |
| De-magnetising and magnetising field level: |  | tbd |

TO (new table)

| Parameter | Measurement Range | Tolerances |
| --- | --- | --- |
| Temperature | -55°C to +180°C - maximum temperature - minimum temperature below –55°C and above 10 K - maximum temperature - minimum temperature below 10 K - maximum temperature - minimum temperature | 0°C/+ 3°C - 3°C/0°C 0K/+1 K -1 K/0 K 0K/+0.1 K -0.1 K/0 K |
| Pressure | - p > 0,1 mbar - p < 0,1 mbar | < ( 1 % ( 10 % |
| Solar intensity |  | ( 3 % |
| Relative Humidity |  | + 5 % RH |
| Static test | Force | 0 % / 5 % |
| Sinusoidal Vibration | Acceleration/amplitude Frequency below 50 Hz Frequency above 50 Hz | 0 % / +5 % ( 0.5 Hz ( 2 % |
| Random Vibration | Power Spectral Density (g2/Hz) Overall g RMS | -1 dB/ +1.5 dB ( 10% |
| Acoustic Vibration | 1/3 octave band overall | -1.0 dB/3.0 dB (63 to 2000 Hz) -2.0 dB/4.0 dB (31.5 Hz) -1.0 dB/3.0 dB |
| Shock response | (Q=10) 1/6 octave band | ( 3.0 dB |
| Test Duration |  | 0 %/ 5 % |
| RF Power Level |  | < ( 0.3 dB |
| Spurious level | < -20 dBc and up to 80 dBc | < ( 0.5 dB |
| Frequencies | Audio < 20 kHz Video > 10 MHz Video < 10 Mz | 10 ppm 1 ppm 0.01 ppm |
| Voltage | < 5 Volt > 5 Volt | ( 0.2 % ( 0.5 % |
| Current | < 1 A > 1 A | ( 0.5 % ( 0.1 % |
| DC Power |  | ( 1.0 % |
| VSWR |  | 0.2 dB |
| Leak Rate |  | (10-5 Pa m3s-1 of Helium at 1013 hPa pressure differential |

===========================

(Alcatel comments 15)

9.5.3.3.2 Sine Vibration Test Levels and Duration

change

Acceptance levels are to be derived by dividing the qualification levels by a factor 1.5.

by

Acceptance levels are to be derived by dividing the qualification levels by a factor 1.25.

======================================

(Alcatel comments 16)

9.5.3.4: Random Vibration Tests

change

Acceptance levels are to be derived by dividing the qualification levels by a factor 2.25.

by

Acceptance levels are to be derived by dividing the qualification levels by a factor 1.5625.

| ORIGINATOR | DATE |
| --- | --- |
| APPROVED BY |
| Project Manager Date | Project Controller Date |
| PA Manager Date | Configuration Manager Date |

| INDUSTRY ASSESSMENT / IMPACT OF CHANGE |
| --- |
| System Design: None |
| Schedule: none |
| Cost: |
| Analyst: Approved by: | Date: |