| SUBJECT: | SPIRE Data ICDSPIRE Data ICD |
| --- | --- |
| PREPARED BY: | K.J. KingK.J. King |
| DOCUMENT No: | SPIRE-RAL-PRJ-001078SPIRE-RAL-PRJ-001078 |
| ISSUE: | Issue 2.0Issue 2.0 | Date: | 15th November 200415th November 2004 |
| APPROVED BY: |  |  |  |

| Checking Engineer (IFSI) R. Cerulli |  |
| --- | --- |
| OBS Engineer (IFSI) S. Molinari |  |
| Project Manager (IFSI) R. Orfei |  |
| Operations Scientist S. Sidher |  |
| Instrument Scientist B.M. Swinyard |  |
| Instrument Development Manager E.C. Sawyer |  |

Distribution

| R. Orfei | IFSI |
| --- | --- |
| R Cerulli | IFSI |
| S. Molinari | IFSI |
| J-L Augerres | CEA, Saclay |
| C. Cara | CEA, Saclay |
| S. D. Sidher | RAL |
| B. M. Swinyard | RAL |
| K. J. King | RAL |
| J.A. Long | RAL |

# Change Record

| ISSUE | DATE |  |
| --- | --- | --- |
| Issue 1.0 Draft 1 | 15th January 2002 | Original Draft |
| Issue 1.0 Draft 2 | 15th January 2003 | Updated Draft for DPU AVM Acceptance Test Section 1.1: Updated Scope description Section 1.3.2: Updated document references and added RD08 Section 2.1.3: Added note about TIME contents Section 2.2: Renamed APID5 Section 2.3: included details of which parts of the 1553 interface protocol are used Section 3.1: Updated Telecommand service usage Section 3.2.3: Defined both Housekeeping and Diagnostic reports. There are now 4 of each with 2 housekeeping and 1 diagnostic report pre-defined in the OBS Section 3.2.3.1: Updated definition of service (3,1) to send Table_ID as a parameter. This allows different SIDs for the same Table_ID Section 3.2.3.2: Service (3,2) set to Not Used Section 3.2.3.3: Service (3,3) now defined Section 3.2.3.4: Service (3,4) set to Not Used Section 3.2.3.5:Service (3,9) now defined Section 3.2.3.6: Service (3,11) set to Not Used Section 3.2.6.1: Memory addressing changed to use 8 bit Memory ID and 24 bit address Section 3.2.6.2: Memory addressing changed to use 8 bit Memory ID and 24 bit address Section 3.2.6.3: Memory addressing changed to use 8 bit Memory ID and 24 bit address Section 3.2.8.1.2-4: Deleted Cooler, SCAL and 300mk control commands – they are now implemented in software-driven VMs Section 3.2.8.2.2-4: Deleted Cooler, SCAL and 300mk control commands – they are now implemented in software-driven VMs Section 3.2.8.3.1: Changed Load_Table command to Set_Table, with consequent changes to parameters Section 3.2.8.3.2: Changed parameters Section 3.2.8.3.3: Changed parameters Section 3.2.8.3.6: Inserted commands to start and stop software-driven VMs Section 3.2.8.3.20: Deleted data packing command – data frames are packed into science packets until they are full (unless a flush command is received) Section 3.2.9.1: Change to packet definition to all Ack field to be changed Section 3.2.14.1: Service (14,1) now defined Section 3.2.14.2: Service (14,2) now defined Section 3.2.14.3: Service (14,3) now defined Section 3.2.17.1: Updated command description Section 3.2.20.4: This telecommand is no longer used – OTF and TSF provided by ground processing Section 3.2.22: Context Service not used Section 4.1: table updated to reflect changes to services Section 4.2.1.6: Updates Error code table Section 4.2.3.2: Added Critical Housekeeping Report definition Section 4.2.3.3: Updated Nominal Housekeeping Report definition Section 4.2.3.4: Added Detector Housekeeping Report definition Section 4.2.5.1: Removed OTF and TSF reports and added definition of report identified so far Section 4.2.5.2: Added definition of reports Section 4.3.5.3: Removed Error/Alarm report definition – they are not used as the ground does not remain in contact with the spacecraft Section 4.2.6: Defined Memory Dump reports Section 4.2.8: defined Function Activity Report Section 4.2.14: Defined Packet Generation Status Report Section 4.2.17: Defined Link connection Report Section 4.2.21: Science Data packet definition updated Section 4.2.22: Context Saving Service not used Section 5.1.1: Updated TC Parameter List Section 5.1.3: Updated TC Parameter Constraints Added commands to select science data Added Appendix D - description of science data processing |
| Issue1.1 Draft 1 | 31st July 2003 | Version issued for CQM Testing. This Version corresponds to the version 1.0 of the DRCU ICD. Section 1.3.1: Added IID-Part A to Applicable Documents Section 3.2.8.1: Added Launch Latch function to follow required implementation of arm-fire procedure for critical commands Added Booting Function Section 3.2.8.2: Added Launch Latch function to follow required implementation of arm-fire procedure for critical commands Added Booting Function Section 3.2.8.3: Added commands to engage/release Launch Latch Added Load_TC_and_Boot command Modified Force_Boot command Function and Activity IDs Defined Selection commands Section 3.2.20: Removed use of Information Distributiuon Service, 20 Section 4.1: Removed Diagnostic Housekeeping packets from table Section 4.2.1.2.1: Updated TM(1,2) error message format to conform to new PS_ICD Section 4.2.1.2.2: Added Packet Content Error code for Illegal Functio and Activity IDs Section 4.2.1.6: Removed Illegal Function and Activity ID errors from the TC Failure report – they ar enow reported as TC Acceptance Failures Section 4.2.3.1: Removed Detector Housekeeping report from table Section 4.2.3.2: Updated Critical Housekeeping Report table to reflect Issue 1.0 of DRCU ICD Section 4.2.3.3: Updated Nominal Housekeeping Report table to reflect Issue 1.0 of the DRCU ICD Section 4.2.3.4: Deleted Detector Housekeeping Report – offsets are no longer able to be read as housekeeping parameters and can be obtained via a science data report Section 4.2.5.1: Updated event report format to conform to AD01 Updated DPU error packets to conform to User Manual description Section 4.2.5.1.2: Updated Peak-up Report format to comply with agreed interface (to be included in IID-A) Section 4.2.5.2: Updated to reflect new format for event packets in AD01 and consolidated TM(5,2) event packets into one format Added Boot ROM Telemetry event packet Section 4.2.5.3: updated to include all BOOT SW generated telemetry packets (ref RD10) Section 4.2.7: Defined Function Activity Reports Section 4.2.14: Modified format to conform to AD01 Section 4.2.16: Added Time to test service TM(17,2) packet Section 4.2.20: Removed use of Information Distribution Service, 20 Section 4.2.21.1.3: Updated contents of SMEC Block Section 4.2.21.1.4: Updated contents of BSM Block Section 4.2.21.1.5: Defined contents of SCU Block Section 4.2.21.3: Defined New Test Pattern Blocks Defined MCU Engineering Block Appendix D: Replaced with Pixel Maps |
| Issue 1.1 Draft 2 | 10th August 2003 | Section 3.1: Removed HSK packet definition commands from Table Section 3.2.3: Removed HSK packet definition commands from Service 3 (moved to Service 8) Section 3.2.8.1.11: Added HSK Function Section 3.2.8.1.11: Added HSK Function Section 3.2.8.3: Added HSK packet definition commands Section 3.2.8.3.31 & 32: updated Selection commands to use SELECTID Section 4.2.1.6: modified TM(1,8) error codes for housekeeping packet definition commands Section 4.1.5.1.6: Updated Frame ID Error event packet –removed spare parameter Section 4.1.5.1.7: Updated Frame Length Error event packet Section 4.2.5.1.16: Added new event for TC counter error Section 4.2.21.1.3: Modified SMEC Block to contain full frame. This Is doen to be consistant with the use of selected data for SMEC operations Section 4.2.21.1.6: Defined DPU Blocks Section 4.2.21.2.6: Defined Selected Data Block, including adding normal SMEC data block Section 4.2.21.3.11: Added Transparent Data Block definition Section 4.2.21.4: Added Housekeeping Packet Definition Report Section 4.2.21.4.3: Added Housekeeping Packet Definition Report Parameters Section 4.2.21.4.4: Added Table Report Parameters |
| Issue 1.1 Draft 3 | 13th August 2003 | Updated TM(8,4) section to conform to AD01 – added SID to commands |
| Issue 1.1 Draft 4 |  | All TC Sections: Changed commands names to be identical to the short description in the MIB Section 3.1: Removed all service 12 TCs from table – this is handled with TC(8,4) commands Section 3.2.6: Added Boot S/W Memory ID = 4 for dumping and checking memory Section 3.2.6.1: noted maximum rate of sending Memory Load commands Section 3.2.8.3.4: added Garbage Collection command Section 3.2.8.3.7: corrected length field Section 3.2.8.3.9: corrected length field Section 3.2.8.3.11: corrected length field Section 3.2.8.3.13: corrected length field Section 3.2.8.3.14: corrected length field Section 3.2.8.3.15: corrected length field Section 3.2.8.3.16: Added possible Peak-up Mode definition Section 3.2.8.3.17: corrected length field Section 3.2.8.3.18: corrected length field Section 3.2.8.3.19: corrected length field Section 3.2.8.3.20: corrected length field Section 3.2.8.3.21: corrected length field Section 3.2.8.3.22: corrected length field Section 3.2.8.3.23: corrected length field Section 3.2.8.3.24: corrected length field Section 3.2.8.3.25: corrected length field Section 3.2.8.3.26: corrected length field Section 3.2.8.3.27: corrected length field Section 3.2.8.3.28: corrected length field Section 3.2.8.3.29: corrected length field Section 3.2.8.3.30: corrected length field Section 3.2.8.3.31: Corrected length field Modified explanatory text, removed SELECTID from input parameters Section 3.2.8.3.32: Corrected length field Replaced SELECTID by FRAMEID in input parameters Section 3.2.8.3.33: corrected length field Section 3.2.8.3.34: corrected length field Section 3.2.8.3.35: corrected length field Section 3.2.8.3.36: corrected length field Section 3.2.12: Defined Service 12 as Not Used Section 3.2.14.1: Defined Packet ID as the parameter to select which packets are to be enabled Section 3.2.14.2: Defined Packet ID as the parameter to select which packets are to be disabled Section 4.1: Updated table to show TM(5,4) is used, TM(12, 9) is not used and TM(22,*) is not used Section 4.2.1.6: Deleted illegal Packet error from table as it referred to Service 20 , which is no longer used Section 4.2.3.1: Updated APID for Critical Housekeeping Packet Section 4.2.3.2: Added DPUSTAT to Critical HSK Section 4.2.3.3: Added SCU25V, SCUREF and SCUGND to HSK TM packet Increased LSLOAD length to 32 bits – compensated by removing DPU Spare Renumbered table entries Various further name changes Section 4.2.5.1.5: Modified TM packet to include full response from DRCU Section 4.2.5.1.9: Modified TM packet to include full response from DRCU plus the interface status Section 4.2.5.1.10: Modified TM packet to include the interface status Section 4.2.5.1.11: Modified TM packet SID Section 4.2.5.1.19: Added Out of Limits Event Packet Section 4.2.5.3: Updated Boot SW error Packets definitions Section 4.2.8.1: Added SID to TM Packet Section 4.2.8.1: Corrected Parameter Table Section 4.2.21.4: Added DPU Science Data Packet |
| Issue 1.2j |  | Section 2.2: Updated APIDs Section 3.2.3: Changed Housekeeping Packet IDs Section 3.2.8.3.32:Changed description of selection command, updated command error list Section 3.2.8.3.34: Added Error codes 0x0817 – 0x0819 Section 3.2.8.3.35: Added Error code 0x0829 Section 3.2.8.3.36: Added Error code 0x0829 Section 4.2.1.2.2: Deleted Failure code 5 (not sent in TM(1,2) but in TM(1,8) Section 4.2.1.6: Updated Error codes Section 4.2.3.2: Changed OBSVER parameter Section 4.2.3.3: Updated Parameters Section 4.2.5.1: Made SIDs unique Updated parameter names Section 4.2.5.2.1:Changed SID from 0x0520 to 0x5200 Section 4.2.8.3: Introduced SELSID parameter and indicated that the parameters are repeated for each Frame type |
| Issue 1.2k |  | Section 3.2.8.3.37: Added FORCE_WRONG_CRC command Section 4.2.3.3: Added 5 lost TC/TM packets counters to nominal housekeeping packet |
| Issue 2.0 |  | Section 3.2.8.3.34: Removed Monitor Table ID Section 4.2.3.2: Updated table according to new version of RD07 Section 4.2.3.2: Updated table according to new version of RD07 Section 4.2.21.1: Removed DPU Scienec Packet - now defined as a VM science packet (see 4.2.21.4) Section 4.2.21.1: Added Selected Data packets to table and defined them in 4.2.21.1.6-8 Section 4.2.21.2: Removed selected data packets (now in section 4.2.21.1) Section 4.2.21.1.3: Updated SMEC Science Packet contents Section 4.2.21.1.4: Updated BSM Science Packet contents Section 4.2.21.2.6.1: Updated SMEC Selected Science Packet Contents Section 4.2.21.3.8: Updated MCU Engineering TM Packet contents Section 4.2.21.3.9: Updated MCU Test Pattern TM Packet Contents |

# Table of Contents

1.	Introduction	13

1.1	Scope	13

1.2	Structure of the Document	13

1.3	Documents	14

1.3.1	Applicable Documents	14

1.3.2	Reference Documents	14

2.	The Packet Interface	15

2.1	Packet Structures	15

2.1.1	Fields	15

2.1.2	Telecommand Packets	15

2.1.3	Telemetry Packets	16

2.2	APIDs	16

2.3	Packet Transfer Protocol	16

3.	SPIRE Telecommand Packets	18

3.1	Telecommand Packet Types	18

3.2	Telecommand Packet Definition	19

3.2.1	Telecommand Verification Service	19

3.2.2	Device Command Distribution	19

3.2.3	Housekeeping and Diagnostic Data Reporting	19

3.2.3.1	Define New Housekeeping Parameter Report (Service 3,1)	19

3.2.3.2	Define New Diagnostic Parameter Report (Service 3,2)	19

3.2.3.3	Clear Housekeeping Parameter Report Definitions (Service 3,3)	19

3.2.3.4	Clear Diagnostic Parameter Report Definitions (Service 3,4)	19

3.2.3.5	Report Housekeeping Parameter Report Definitions (Service 3,9)	19

3.2.3.6	Report Diagnostic Parameter Report Definitions (Service 3,11)	19

3.2.4	20

3.2.5	Event Reporting	20

3.2.6	Memory Management	21

3.2.6.1	Load Memory Using Absolute Addresses (Service 6,2): LOAD_MEMORY	21

3.2.6.2	Dump Memory Using Absolute Addresses (Service 6,5): DUMP_MEMORY	22

3.2.6.3	Check Memory Using Absolute Addresses (Service 6,9): CHECK_MEMORY	22

3.2.7	23

3.2.8	Function Management	24

3.2.8.1	Start Function (Service 8,1)	24

3.2.8.2	Stop Function (Service 8,2)	26

3.2.8.3	Perform Activity of a Function (Service 8,4)	28

3.2.8.4	ReportFunction Status (Service 8,5) REPORT_FUNCTION	50

3.2.9	Time Management	51

3.2.9.1	Enable Time Verification (Service 9,7) ENABLE_TIME_VERIFICATION	51

3.2.10	Unused Service	52

3.2.11	On-Board Scheduling	52

3.2.12	On-Board Monitoring	52

3.2.13	Unused Service	52

3.2.14	Packet Transmission Control	53

3.2.14.1	Enable Generation of Telemetry Packets (Service 14,1) ENABLE_TM_GENERATION	53

3.2.14.2	Disable Generation of Telemetry Packets (Service 14,2) DISABLE_TM_GENERATION	54

3.2.14.3	Report Enabled Telemetry Packets (Service 14,3) REPORT_ENABLED_TM	54

3.2.15	On-Board Storage and Retrieval	55

3.2.16	On-Board Traffic Management	55

3.2.17	Test Service	56

3.2.17.1	Perform Connection Test (Service 17,1) TEST_CONNECTION	56

3.2.18	On-Board Control Procedures	56

3.2.19	Action/Event Service	56

3.2.20	Information Distribution Service	57

3.2.21	Science Data	57

3.2.22	Context Saving Service	57

4.	SPIRE Telemetry Packets	58

4.1	Telemetry Packet Types	58

4.2	Telemetry Packet definitions	59

4.2.1	TC Verification Service	59

4.2.1.1	Telecommand Acceptance Report - Success (1,1)	59

4.2.1.2	Telecommand Acceptance Report - Failure (1,2)	59

4.2.1.3	Telecommand Execution Report - Started (1,3)	61

4.2.1.4	Telecommand Execution Report - Progress (1,5)	61

4.2.1.5	Telecommand Execution Report - Completion (1,7)	61

4.2.1.6	Telecommand Execution Report - Failure (1,8)	62

4.2.2	Device Command Distribution	63

4.2.3	Housekeeping and Diagnostic Data Reporting	64

4.2.3.1	Housekeeping Parameter Report  (Service 3,25)	64

4.2.3.2	Critical Housekeeping Report (SID=0x0300)	65

4.2.3.3	Nominal Housekeeping Report (SID=0x0301)	67

4.2.4	Unused Service	77

4.2.5	Event Reporting	77

4.2.5.1	Event Report (5,1)	77

4.2.5.2	Exception Report (5,2)	90

4.2.5.3	Error/Alarm Report (5,4)	92

4.2.6	Memory Management	96

4.2.6.1	Memory Dump, Absolute Addresses	96

4.2.6.2	Memory Check Report, Absolute Addresses	96

4.2.7	96

4.2.8	Function Management	97

4.2.8.1	Normal Functions Report	97

4.2.8.2	VM Functions Report	97

4.2.8.3	DPU Functions Report	98

4.2.9	Time Management	99

4.2.9.1	Time Verification Report	99

4.2.10	99

4.2.11	On Board Scheduling	99

4.2.12	On Board Monitoring	99

4.2.13	99

4.2.14	Packet Transmission Control	99

4.2.15	On Board Storage and Retrieval	100

4.2.16	On Board Traffic Management	100

4.2.17	Test Service	100

4.2.18	On Board Control Procedures	100

4.2.19	Action/Event Service	100

4.2.20	Information Distribution Service	100

4.2.21	Science Data	101

4.2.21.1	Nominal Science Data Report (21,1)	101

4.2.21.2	Science Type B Data Report (21,2)	107

4.2.21.3	Diagnostic Science Report (21,3)	111

4.2.21.4	Auxiliary Science Data Report (21,4)	117

5.	Parameters	120

5.1	TC Parameters	120

5.1.1	Parameter Definition	120

5.1.2	Conversion Curves	123

5.1.3	Constraints	123

5.2	TM  Parameters	124

5.2.1	Parameter Definition	124

5.2.2	Conversion Curves	134

5.2.3	Constraints	136

6.	Tables	137

7.	Control Loops	138

7.1	Control Loop Parameters	138

8.	Command List	139

9.	Detector Pixel Mapping	140

9.1	Phtometer SW	140

9.2	Photometer MW	141

9.3	Photometer LW	142

9.4	Spectrometer SW	143

9.5	Spectrometer LW	144

Figures

Tables

Glossary

| APID | Application ID |
| --- | --- |
| CDMS | Command and Data Management System |
| DPU | Digital Processing Unit |
| OBS | On-Board Software |
| SID | Structure ID |
| SPIRE | Spectral and Photometric Imaging REceiver |
| SVM | Service Module |
| VM | Virtual Machine |

# Introduction

Control of the SPIRE instrument is handled by the Digital Processing Unit (DPU) part of the instrument electronics, which contains the On-Board Software (OBS). This unit is mounted on the spacecraft Service Module (SVM) and interfaces directly to the CDMS bus of the Herschel spacecraft for the purpose of transferring commands to, and collection of telemetry data from the instrument.

All data passing between the instrument and the spacecraft is transferred in the form of telemetry and telecommand packets conforming to the ESA packet standards (RD01 and RD02).  The ESA Packet Utilisation Standard (RD03) defines the types of service that may be provided by units on board ESA spacecraft, but the set of supported packet types within the Herschel project is restricted. This restricted set is defined in the Herschel Packet Structure ICD (AD01) and is the minimum set necessary to meet the satellite operational requirements given in AD02.

Note: Items which are unclear from the documentation or are likely to be updated in the future are marked in blue text.

## Scope

This document defines the packet types and their contents that will be accepted and generated by the SPIRE instrument during all operations.  These packets conform to the formats given in the Packet Structure ICD (AD01) and the Ground Segment to Instruments ICD (AD03). They also provide for the instrument functionality described  in the instrument Operating Modes document (RD04) and elaborated in the instrument operating document (RD04).

The document does not describe the use of the commands (to be given in the OBS User Manual) or the way in which the commands are handled by the OBS (to be found in the OBS Architectural Design document).

## Structure of the Document

Section 2 describes the packet interface between the instrument and the spacecraft. This includes the general format of the packets used by the SPIRE instrument for telecommanding and telemetry  (from AD01), the allocation of Application IDs used by the instrument and the functionality of the packet  transfer protocol of the instrument/spacecraft interface (from AD01, appendix 9) that is used by the instrument.

Section 3 defines the format and content of each of the telecommand packets accepted by the instrument. Section 4 defines the corresponding information for the telemetry packets generated by the instrument. A description of how these packets are handled by the instrument is given in RD05.

Section 5 defines, in detail, the parameters used in the telecommand and telemetry packets.

## Documents

### Applicable Documents

| AD01 | Herschel/Planck Packet Structure Interface Control Document. (SCI-PT-ICD-07527) Issue 3.0 |
| --- | --- |
| AD02 | Herschel/Planck Operations Interface Requirements Document (SCI-PT-RS-07360), Issue 2.0 (draft3) |
| AD03 | Herschel Science Ground Segment to Instruments Interface Control Document (FIRST-FSC-DOC-0200), Issue 1.0 |
| AD04 | Herschel/Planck Instrument Interface Document Part A (SCI-PT-IIDA-04624), Issue 3.0 |

### Reference Documents

| RD01 | Packet Telemetry Standard (ESA PSS-04-106), Issue 1, 1998 |
| --- | --- |
| RD02 | Packet Telecommand Standard (ESA PSS-04-107), Issue 2, 1992 |
| RD03 | Telemetry and Telecommand Packet Utilisation Standard (ECSS-E-70/41) Draft 04, April 1999 |
| RD04 | Operating Modes of the SPIRE Instrument (SPIRE-RAL-PRJ-000320), Issue 3.0, 4th January 2002 |
| RD05 | Operating the SPIRE Instrument (SPIRE-RAL-DOC-000768), Issue 0.4, 29th January 2002 |
| RD06 | DRCU/DPU Interface Control Document (SAp-SPIRE-CCa-076-02) Issue 1.0, 14th February 2003 |
| RD07 | MCU/DPU Command List Interface Control Document and User Manual (LAM/ELE/SPI/011011), Issue 4.0, 30th September 2004 |
| RD08 | SPIRE On-Board Software User Manual (SPIRE-IFS-PRJ-001391) |
| RD09 | Herschel SPIRE DPU Hardware User Manual (SPIRE-IFS-PRJ-001390), Issue 1, 7th October 2002 |
| RD10 | DPU Switch-On Procedure Telemetry Packets User Manual (DPU-MA-CGS-004), Issue: draft, 5th February 2003 |

# The Packet Interface

## Packet Structures

The following packet structures are shown as a set of 16 bit words, contained in two consecutive octets in the packet structure (all packets are composed of an even number of octets). The most significant octet of each word comes before the least significant in the packet. The least significant bit of each word is on right of each field:

|  | MS Octet | LS Octet |  |
| --- | --- | --- | --- |
| Most Significant Bit | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Least Significant Bit |

### Fields

Within a field (of any length) the most significant bit is designated bit (0), the least significant bit is bit (length-1).

### Telecommand Packets

The following figure gives the general structure of a SPIRE TC Packet (after AD01)

| Packet Header | Packet ID | 0 | 0 | 0 | 1 | 1 | APID |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | Sequence Control | 1 | 1 | Src | Count |
|  | Length | Length |
| Data Field | Data Field Header | 0 | 0 | 0 | 0 | Ack | 1 | Type |
|  |  | Sub-Type | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | Source Data |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  | D | A | T | A |  |  |  |  |  |  |
|  | Error Control | Checksum |

Src,Count, Length, TIME and Checksum are defined in AD01

Ack is the most significant 3 bits of Ack as defined in AD01

Type and Sub-Type define the packet type and are also defined in AD01

### Telemetry Packets

The following figure gives the general structure of a SPIRE TM Packet (after AD01)

| Packet Header | Packet ID | 0 | 0 | 0 | 0 | 1 | APID |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | Sequence Control | 1 | 1 | Count |
|  | Length | Length |
| Data Field | Data Field Header | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Type |
|  |  | Sub-Type | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | TIME |
|  | Source Data |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  | D | A | T | A |  |  |  |  |  |  |
|  | Error Control | Checksum |

Count, Length, TIME and Checksum are defined in AD01

Type and Sub-Type define the packet type and are also defined in AD01

Note: the TIME field contains the DPU time of the construction of the packet, not the time of collection of the data.

## APIDs

The Application ID is used to identify the source or destination of a telemetry packet. Herschel uses different APIDs for different types of packet (see AD1) as well as for different instruments. The APIDS to be used by SPIRE are given in the following table:

| ID | Telemetry types | APID (hex) |
| --- | --- | --- |
| APID1 | SPIRE Telecommands, Telecommand Verification and Events | 500 |
| APID2 | SPIRE Periodic Housekeeping | 502 |
| APID3 | SPIRE Photometer Science Data | 504 |
| APID4 | SPIRE Spectrometer Science Data | 506 |
| APID5 | SPIRE Subsystem Science Data | 508 |

## Packet Transfer Protocol

At the low-level the Packet Transfer Protocol provides a series of sub-address messages to control and transfer data between subsystems. Some of these implement the packet transfer itself, others provide alternative methods of transferring data and controlling the transfer. This section identifies the sub-addresses used/accepted by the SPIRE instrument.

| Description | Sub-address(es) | Comments |
| --- | --- | --- |
| Mode Command | SA 0R | Used to identify the RT addressed in this subframe. The instrument responds only to its own address. For burst mode this is only set when the instrument has indicated that it has data to transfer |
|  | SA 0T, 31T, 31R | Not Used |
| Unit Control | SA 1R | Not Used |
|  | SA 1T | Contains Subframe counter and BIT word of 1553 i/f |
| Data Send | SA 2T, 3T, 4T, 7T, 9T, 29T | Not Used |
| Data Receive | SA 2R, 7R, 9R, 15R-26R, 29R | Not Used |
| Asynchronous Short Commands | SA 3R, 4R | Not used |
| Event Messages | SA 5R, 5T, 6R, 6T | Not Used |
| Time Messages | SA 8T | Not used |
|  | SA 8R | Used to transfer spacecraft time from CDMU to instrument (in subframe 33) rather than use packet service (9,5) |
| Packet Transfer TM Transfer Request | SA 10T | Used by instrument to indicate to CDMU that a TM packet is ready to transfer |
| TM Transfer Confirmation | SA 10R | Used to implement retry at packet level |
| TC Transfer Confirmation | SA 27T | Instrument sends a copy of TC Transfer Descriptor to indicate reception of TC |
| TC Transfer Descriptor | SA 27R | Used by the instrument to prepare for TC transfer |
| TM Data Send | SA 11T-26T | Used to transfer TM packets from instrument to CDMU |
| TC Data Receive | SA 11R-14R | Used to transfer TC packets from CDMU to instrument |
| Low-level Commands | SA 28T, 28R | Not Used |
| Data Wrap | SA 30T, 30R | Not Used by instrument, but made available for future use |

# SPIRE Telecommand Packets

This section defines all the telecommand packets accepted by the SPIRE instrument

## Telecommand Packet Types

The Packet Structure ICD (AD1) defines many types of service that can be provided by an Application. The following table shows the telecommand packet types that will be accepted by the SPIRE instrument.

| Description | Service Type | Service Sub-Type | Comments |
| --- | --- | --- | --- |
| Telecommand Verification Service | 1 |  | N/A |
| Device Command Distribution | 2 |  | Not Used |
| Housekeeping and Diagnostic Data Reporting | 3 |  | Not Used |
| Event Reporting | 5 |  | N/A |
| Memory Management |  |  |  |
| Load Memory Using Absolute Addresses | 6 | 2 |  |
| Dump Memory Using Absolute Addresses | 6 | 5 |  |
| Check Memory Using Absolute Addresses | 6 | 9 |  |
| Function Management |  |  |  |
| Start Function | 8 | 1 |  |
| Stop Function | 8 | 2 |  |
| Perform Activity of Function | 8 | 4 |  |
| Report Function Status | 8 | 5 |  |
| Time Management |  |  |  |
| Synchronise User | 9 | 3 | Not Used |
| Enable Time Synchronisation | 9 | 4 | Not Used |
| Time Code | 9 | 5 | Not Used |
| Verify User Time | 9 | 6 | Not Used |
| Enable Time Verification | 9 | 7 |  |
| Synchronise Central Time Reference | 9 | 10 | Not Used |
| On-Board Scheduling | 11 |  | Not Used |
| On-Board Monitoring | 12 |  | Not Used |
| Packet Transmission Control |  |  |  |
| Enable Generation of Telemetry Packets | 14 | 1 |  |
| Disable Generation of Telemetry Packets | 14 | 2 |  |
| Report Enabled Telemetry Packets | 14 | 3 |  |
| On-Board Storage and Retrieval | 15 |  | Not Used |
| On-Board Traffic Management | 16 |  | Not Used |
| Test Service |  |  |  |
| Perform Connection Test | 17 | 1 |  |
| On-Board Control procedures | 18 |  | Not Used |
| Action/Event Service | 19 |  | Not Used |
| Information Distribution Service | 20 |  | Not Used |
| Science Data | 21 |  | N/A |
| Context Saving Service | 22 |  | TBD |

## Telecommand Packet Definition

### Telecommand Verification Service

Not Applicable

### Device Command Distribution

Not Used

### Housekeeping and Diagnostic Data Reporting

The periodic Housekeeping and Diagnostic Data is reported, at fixed time intervals, in packets with a fixed format.  A maximum of 4 different reports are available for use at the same time, each allocated a different HK_Packet_ID, in the range 0 to 3. Associated with each HK_Packet_ID is a sampling interval and an on-board table, which contains the definition of the contents of the report.

The 4 reports are defined in the following way in the OBS by default:

| HK_Packet_ID | Report | Table_ID | Sampling Interval | HKSID |
| --- | --- | --- | --- | --- |
| 0x300 | Critical Housekeeping Report | 0 | 2000m sec | 0x0300 |
| 0x301 | Nominal Housekeeping Report | 1 | 1000 msec | 0x0301 |
| 0x302 | --- Undefined ---- | 2 | ---- Not sampled ---- | --- Undefined ---- |
| 0x303 | --- Undefined ---- | 3 | ---- Not sampled ---- | --- Undefined--- |

The contents of each report are described in the Housekeeping Parameter Report (Services 3,25).

Maintenance of the housekeeping report is made using TM(8,4)

#### Define New Housekeeping Parameter Report (Service 3,1)

Not Used

#### Define New Diagnostic Parameter Report (Service 3,2)

Not Used

#### Clear Housekeeping Parameter Report Definitions (Service 3,3)

Not Used

#### Clear Diagnostic Parameter Report Definitions (Service 3,4)

Not Used

#### Report Housekeeping Parameter Report Definitions (Service 3,9)

Not Used

#### Report Diagnostic Parameter Report Definitions (Service 3,11)

Not Used

Not Available

### Event Reporting

Not Applicable

### Memory Management

These commands allow access to the contents of memory locations.  Five areas of memory have been identified, with the following MEMORYID:

- Program Memory (RAM)

- Data memory  (RAM)

- 1553 I/F DPRAM

- EEPROM

- Boot S/W PROM

When accessing memory the address is specified in terms of the number of Single Addressable Units (SAUs)  from the start of the memory area. The SPIRE SAU is always 16bit words.

Note: This packet format does not strictly follow AD01 – The MEMORYID field is 8bits and the STARTADDR field is 24 bits.

#### Load Memory Using Absolute Addresses (Service 6,2): LOAD_MEMORY

This command should be sent at a maximum rate of 2 per second (unless TC verification is disabled).

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length |
| 0 | 0 | 0 | 0 | Ack | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| MEMORYID |  |
| STARTADDR |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | NSAU |
| Data |
| CRC |
| Checksum |

Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Illegal_Memory_ID | (1,8) | 0x0601 | Not a valid memory ID |
| Illegal_Start_Address | (1,8) | 0x0602 | Start address outside valid range |
| Illegal_Nsau | (1,8) | 0x0603 | Length will place data outside valid address range |
| Bad_Nsau | (1,8) | 0x0604 | Length does not agree with size of data field |
| Bad_CRC | (1,8) | 0x0605 | CRC in command does not agree with calculated checksum over data in command |
| Bad_Load | (1,8) | 0x0606 | CRC in command does not agree with calculated checksum over data in memory |

Note: currently there are restrictions on which memory areas can be directly loaded. These are to be clarified

#### Dump Memory Using Absolute Addresses (Service 6,5): DUMP_MEMORY

Note: This packet format does not strictly follow AD01 – The MEMORYID field is 8bits and the STARTADDR field is 24 bits.

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 11 |
| 0 | 0 | 0 | 0 | Ack | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| MEMORYID |  |
| STARTADDR |
| NSAU |
| Checksum |

Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Illegal_Memory_ID | (1,8) | 0x0601 | Not a valid memory ID |
| Illegal_Start_Address | (1,8) | 0x0602 | Start address outside valid range |
| Illegal_Nsau | (1,8) | 0x0603 | Length will read data outside valid address range |

Note: currently there are restrictions on which memory areas can be directly dumped (for example the PROM cannot be dunmped – only a copy of the PROM held in RAM). These are to be clarified

#### Check Memory Using Absolute Addresses (Service 6,9): CHECK_MEMORY

Note: This packet format does not strictly follow AD01 – The MEMORYID field is 8bits and the STARTADDR field is 24 bits.

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 11 |
| 0 | 0 | 0 | 0 | Ack | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 |
| 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| MEMORYID |  |
| STARTADDR |
| NSAU |
| Checksum |

Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Illegal_Memory_ID | (1,8) | 0x0601 | Not a valid memory ID |
| Illegal_Start_Address | (1,8) | 0x0602 | Start address outside valid range |
| Illegal_Nsau | (1,8) | 0x0603 | Length will read data outside valid address range |

Not Available

### Function Management

All command packets of this type may give rise to the following Errors:

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Illegal_Function_ID | (1,2) | 0x0801 | Function_ID not known |

#### Start Function (Service 8,1)

These commands allow functions that are not started automatically when the OBS runs to be started.

Possible Errors

In the event of being unable to complete the command the following reports shall be issued:

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Function_Active | (1,8) | 0x0830 | The function is already active – command ignored |

##### Function 0x01: Table Management

Always available - cannot be started

##### Function 0x02: Interrupt-driven VM

Always Available - cannot be started

##### Function 0x03: Software-driven VM1

Always Available - cannot be started

##### Function 0x04: Software-driven VM2

Always Available - cannot be started

##### Function 0x05: Software-driven VM3

Always Available - cannot be started

##### Function 0x10:  ENABLE_SMEC_LATCH

This telecommand enables execution of the SMEC Launch Latch movement commands. If this function is not activated then commands to the SMEC launch latch will be rejected by the OBS.

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length =9 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| SID=0x0000 |
| Checksum |

##### Function 0x70: Booting

Always Available - cannot be started

##### Function 0xC0: Operations

Always Available - cannot be started

##### Function 0xC1: Observations

Always Available - cannot be started

##### Function 0xCA: DPU

Always Available - cannot be started

##### Function 0xCC: HSK

Always Available - cannot be started

#### Stop Function (Service 8,2)

These commands allow functions that are not started automatically when the OBS runs to be stopped

Possible Errors

In the event of being unable to complete the command the following reports shall be issued:

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Function_Stopped | (1,8) | 0x0831 | The function is stopped – the command cannot be executed |

##### Function 0x01: Table Management

Always available - cannot be stopped

##### Function 0x02: Interrupt-driven VM

Always Available - cannot be stopped

##### Function 0x03: Software-driven VM1

Always Available - cannot be stopped

##### Function 0x04: Software-driven VM2

Always Available - cannot be stopped

##### Function 0x05: Software-driven VM3

Always Available - cannot be stopped

##### Function 0x10:  DISABLE_SMEC_LATCH

This telecommand disables execution of the SMEC Launch Latch movement commands. If this function is not activated then commands to the SMEC launch latch will be rejected by the OBS.

Note: normally this function is stopped automatically by execution of a Launch Latch command

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length =7 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Checksum |

##### Function 0x70: Booting

Always Available - cannot be stopped

##### Function 0xC0: Operations

Always Available - cannot be stopped

##### Function 0xC1: Observations

Always Available - cannot be stopped

##### Function 0xCA: DPU

Always Available - cannot be stopped

##### Function 0xCC: HSK

Always Available - cannot be stopped

#### Perform Activity of a Function (Service 8,4)

All command packets of this type and subtype may give rise to the following Errors:

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Illegal_Function_ID | (1,2) | 0x0801 | Function_ID not known |
| Illegal_Activity_ID | (1,2) | 0x0802 | Activity_ID not known |

##### Function 0x01 Table Management, Activity 0x01: SET_TABLE

This telecommand allocates space for a table. The previous space allocated to the table is lost.

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length =11 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0001 |
| TABLEID |
| TABLESIZE |
| Checksum |

Possible Errors

This telecommand shall be expected to issue a Telecommand Execution Report  - Completed, TM(1,7) on successful completion. In the event of being unable to complete the command the following reports shall be issued:

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Illegal_Table_ID | (1,8) | 0x0805 | Not a valid table ID |
| Table_Space_Full | (1,8) | 0x0809 | Not enough space available in DPU memory to create new table |

##### Function 0x01 Table Management, Activity 0x02: REPORT_TABLE

Requests telemetry packets reporting the content s of a table starting with the word at offset INDEX (32 bit words) from the start of the table and reporting COUNT words. The contents are reported in as many TM(21,4) packets as necessary to complete the request.

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 13 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | AC TIVITYID |
| SID=0x0002 |
| TABLEID |
| INDEX |
| COUNT |
| Checksum |

Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Illegal_Table_ID | (1,8) | 0x0805 | Not a valid table ID |
| Illegal_Table_Index | (1,8) | 0x0806 | Index outside valid range |
| Table_Bounds_Error | (1,8) | 0x080d | Not enough data available in the table to report COUNT words |
| Undefined_Table_Error | (1,8) | 0x0811 | Table is not defined |

##### Function 0x01 Table Management, Activity 0x03: UPDATE_TABLE

This command is used to load data into a table. The table should have had sufficient space allocated previously using the Set_Table command

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0003 |
| TABLEID |
| INDEX |
| N |
| Data |
| Checksum |

Possible Errors

This telecommand shall be expected to issue a Telecommand Execution Report  - Completed, TM(1,7) on successful completion. In the event of being unable to complete the command the following reports shall be issued:

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Illegal_Table_ID | (1,8) | 0x0805 | Not a valid table ID |
| Illegal_Table_Index | (1,8) | 0x0806 | Index outside valid range |
| Table_Bounds_error | (1,8) | 0x080d | Not enough space available in table to write new data |
| Bad_Data | (1,8) | 0x0808 | N does not agree with length of data field |
| Undefined_Table_Error | (1,8) | 0x0811 | Table is not defined |

##### Function 0x01 Table Management, Activity 0x04: COLLECT_GARBAGE

This command is used to run the garbage collector.

Note: the garbage collector also runs automatically if the free contiguous space available for tables is less than 20% of the total available (To be Clarified)

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length=9 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0004 |
| Checksum |

Possible Errors

This telecommand shall be expected to issue a Telecommand Execution Report  - Completed, TM(1,7) on successful completion. In the event of being unable to complete the command the following reports shall be issued:

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |

##### Function 0x02 Interrupt-driven VM, Activity 0x01: EXECUTE_COMMAND_LIST

Execute the command list held in the telecommand packet.

The Command list being executed is responsible for issuing all the necessary telecommand execution reports

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0004 |
| N |
| Data |
| Checksum |

Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Bad_Data | (1,8) | 0x0808 | N does not agree with length of data field |
| VM_Active | (1,8) | 0x080c | The VM is already executing a command list |

##### Function 0x02 Interrupt-driven VM, Activity 0x02: RUN_VM

Execute a command list held in a table by the Interrupt-driven VM. If the VM is already active the telecommand is rejected with an error packet (see below).

The Command list being executed is responsible for issuing all the necessary telecommand execution reports

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0005 |
| TABLEID |
| INDEX |
| N |
| Data |
| Checksum |

Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Illegal_Table_ID | (1,8) | 0x0805 | Not a valid table ID |
| Illegal_Table_Index | (1,8) | 0x0806 | Index outside valid range |
| Bad_Data | (1,8) | 0x0808 | N does not agree with length of data field |
| VM_Active | (1,8) | 0x080c | The VM is already executing a command list |
| VM_Undefined_Table_Error | (1,8) | 0x0810 | Table is not defined |

##### Function 0x02 Interrupt-driven VM, Activity 0x03: HALT_VM

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 9 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0000 |
| Checksum |

Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| VM_Inactive | (1,8) | 0x080a | Command List Not Running |

##### Function 0x03 Software-driven VM1, Activity 0x02: RUN_VM1

Start execution of a command list held in a table by the software-driven VM1. If the VM is already active the telecommand is rejected with an error packet (see below).

The Command list being executed is responsible for issuing all the necessary telecommand execution reports

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0007 |
| TABLEID |
| INDEX |
| N |
| Data |
| Checksum |

Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Illegal_Table_ID | (1,8) | 0x0805 | Not a valid table ID |
| Illegal_Table_Index | (1,8) | 0x0806 | Index outside valid range |
| Bad_Data | (1,8) | 0x0808 | N does not agree with length of data field |
| VM_Active | (1,8) | 0x080b | The VM is already executing a command list |
| Undefined_Table_Error | (1,8) | 0x080d | Table is not defined |

##### Function 0x03 Software-driven VM1, Activity 0x03: HALT_VM1

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 7 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0000 |
| Checksum |

Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| VM_Inactive | (1,8) | 0x080a | VM Not Running |

##### Function 0x04 Software-driven VM2, Activity 0x02: RUN_VM2

Start execution of a command list held in a table by the software-driven VM2. If the VM is already active the telecommand is rejected with an error packet (see below).

The Command list being executed is responsible for issuing all the necessary telecommand execution reports

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0009 |
| TABLEID |
| INDEX |
| N |
| Data |
| Checksum |

Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Illegal_Table_ID | (1,8) | 0x0805 | Not a valid table ID |
| Illegal_Table_Index | (1,8) | 0x0806 | Index outside valid range |
| Bad_Data | (1,8) | 0x0808 | N does not agree with length of data field |
| VM_Active | (1,8) | 0x080b | The VM is already executing a command list |
| Undefined_Table_Error | (1,8) | 0x080d | Table is not defined |

##### Function 0x04 Software-driven VM2, Activity 0x03: HALT_VM2

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 9 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0000 |
| Checksum |

Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| VM_Inactive | (1,8) | 0x080a | VM Not Running |

##### Function 0x05 Software-driven VM3, Activity 0x02: RUN_VM3

Start execution of a command list held in a table by the software-driven VM3. If the VM is already active the telecommand is rejected with an error packet (see below).

The Command list being executed is responsible for issuing all the necessary telecommand execution reports

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x000B |
| TABLEID |
| INDEX |
| N |
| Data |
| Checksum |

Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Illegal_Table_ID | (1,8) | 0x0805 | Not a valid table ID |
| Illegal_Table_Index | (1,8) | 0x0806 | Index outside valid range |
| Bad_Data | (1,8) | 0x0808 | N does not agree with length of data field |
| VM_Active | (1,8) | 0x080b | The VM is already executing a command list |
| Undefined_Table_Error | (1,8) | 0x080d | Table is not defined |

##### Function 0x05 Software-driven VM3, Activity 0x03: HALT_VM3

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 9 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0000 |
| Checksum |

Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| VM_Inactive | (1,8) | 0x080a | VM Not Running |

##### Function 0x10 SMEC Launch Latch, Activity 0x01: ENGAGE_LATCH

This telecommand sends the SetSLaunchLatch (engage) command (0x90430001) to the DRCU, provided the function is active. The function is then stopped.

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 9 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0000 |
| Checksum |

Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Function_Stopped | (1,8) | 0x0831 | The function is stopped – the command cannot be executed. An event TM(5,2) is also generated |
| Function_Unarmed | (5,2) | 0x0832 | The function has not been started prior to issuing this command |

##### Function 0x10 SMEC Launch Latch, Activity 0xFF: RELEASE_LATCH

This telecommand sends the SetSLaunchLatch (disengage) command (0x90430002) to the DRCU, provided the function is active. The function is then stopped.

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 9 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0000 |
| Checksum |

Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Function_Stopped | (1,8) | 0x0831 | The function is stopped – the command cannot be executed. An event TM(5,2) is also generated |
| Function_Unarmed | (5,2) | 0x0832 | The function has not been started prior to issuing this command |

##### Function 0xC0 Operations, Activity 0x40: PERFORM_PEAKUP

A Peak-up Report TM(5,1) is generated as a result of this command

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 41 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x000F |
| DCUDATAMODE PIXEL STARTCHOPPOSN CHOPPOSNINCR NCHOPPOSNS STARTJIGGPOSN JIGGPOSNINCR NJIGGPOSNS CHOPOFFSET NCHOPCYCLES CHOPCYCLEPERIOD NBSMFRAMES BSMFRAMESTIME NDCUFRAMES DCUFRAMESTIME DCUFRAMESDELAY |
| Checksum |

Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| No_Peak | (1,8) | 0x080c | Unable to find Peak |

##### Function 0xC1 Observations, Activity 0x01: SET_OBSID

Set the observation ID, and set the Building Block ID to zero. The value of these two parameters is reported in the instrument housekeeping packets and all science data packets.

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 13 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0010 |
| OBSID |
| Checksum |

##### Function 0xC1 Observations, Activity 0x02: SET_BBID

Set the Building Block ID. This is reported in the instrument housekeeping packets and all science data packets.

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 13 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0011 |
| BBID |
| Checksum |

##### Function 0xC1 Observations, Activity 0x03: SET_OBS_MODE

This value may be set by the command system in order to notify processing software of the observing mode. It is reported in the housekeeping packets. A New Step Report event packet TM(5,1)  is issued as a result of this command.

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 11 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0012 |
| MODE |
| Checksum |

##### Function 0xC1 Observations, Activity 0x04: SET_OBS_STEP

This value may be set by the command system in order to notify processing software of the current step in the  observing mode. It is reported in the housekeeping packets. A New Step Report event packet TM(5,1)  is issued as a result of this command.

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 11 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0013 |
| STEP |
| Checksum |

##### Function 0xCA DPU, Activity 0x01: RESET_DRCU_COUNTERS

This telecommand sends a broadcast command to the DRCU to reset the time counters in the DCU, SCU and MCU interfaces

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 9 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0000 |
| Checksum |

This telecommand shall be expected to issue a Telecommand Execution Report  - Completed, TM(1,7) on successful completion.

##### Function 0xCA DPU, Activity 0x02: FLUSH_FIFO

This telecommand forces the DPU to read any remaining  science data from the FIFOs place them into science data packets and transmit the packets. I.e. it completely  empties the DPU of science data.

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 11 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0015 |
| FIFOFLAGS |
| Checksum |

Note: This command must not be sent if the DRCU is generating science data

This telecommand shall be expected to issue a Telecommand Execution Report  - Completed, TM(1,7) on successful completion.

Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Invalid_FIFOFLAGS | (1,8) | 0x080f | Incorrect FIFOFLAGS (TBD) |

##### Function 0xCA DPU, Activity 0x03: SET_TM_NOMINAL_MODE

This telecommand sets the telemetry interface to the CDMS to operate in Nominal Mode.

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 9 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0000 |
| Checksum |

This telecommand shall be expected to issue a Telecommand Execution Report  - Completed, TM(1,7) on successful completion.

##### Function 0xCA DPU, Activity 0x04: SET_TM_BURST_MODE

This telecommand sets the telemetry interface to the CDMS to operate in Burst Mode.

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 9 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0000 |
| Checksum |

This telecommand shall be expected to issue a Telecommand Execution Report  - Completed, TM(1,7) on successful completion.

##### Function 0xCA DPU, Activity 0x05: SEND_DRCU_COMMAND

This telecommand allows sending a single command to the DRCU.

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 13 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0018 |
| DRCU Command MSW |
| DRCU Command LSW |
| Checksum |

Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| LS_Transmit_Error | (1,8) | 0x080e | Command was not correctly received by DRCU |

##### Function 0xCA DPU, Activity 0x06: RESET_FIFOS

This telecommand is used to reset all FIFOs. All data currently in the FIFOs is lost.

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 9 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0000 |
| Checksum |

##### Function 0xCA DPU, Activity 0x07: WRITE2EEPROM

This telecommand is used to copy PM into EEPROM.

This copies the block of Program Memory to the start of the EEPROM and formats it such that the boot software can copy it back to Program Memory and start execution of it. (Confirm)

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 17 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x001A |
| Start_Address MSW |
| Start_Address LSW |
| End_Address MSW |
| End_Address LSW |
| Checksum |

Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| EEPROM_Failed | (1,8) | 0x0812 | PM to EEPROM copy failed |

##### Function 0x70 DPU, Activity 0x02: LOAD_TC_AND_BOOT

After upload of a new OBS image into Data Memory using TC(6,2) commands, it is necessary to send this command to copy the full image from DM to Program Memory and start the OBS.

How does the program know where the image resides??????

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 9 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0000 |
| Checksum |

##### Function 0x70 DPU, Activity 0x03: FORCE_BOOT

This telecommand is used   to copy the OBS image from EEPROM to Program Memory and jumps to the start location of the OBS causing it to start running.

Need to be able to copy to a different address on Program Memory?

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 9 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0000 |
| Checksum |

##### Function 0x70 DPU, Activity 0x02: LOAD_TC_AND_WAIT

After upload of part of a new OBS image into Data Memory using TC(6,2) commands, it is necessary to send this command to copy the image from DM to Program Memory.  Further uplink of OBS code may then be made in order to complete the image upload.

How does the program know where the image resides??????

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 7 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0000 |
| Checksum |

##### Function 0xCA DPU, Activity 0x09: RESET_DPU

This telecommand  performs a warm reset of the DPU by executing the Boot software resident in Program memory

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 9 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0000 |
| Checksum |

##### Function 0xCA DPU, Activity 0x10: ENABLE_SELECTION

It may be necessary to reduce the instrument TM data rate (for example during parallel mode). To do this each possible science data frame can have a single associated selection (TBC).

Enable data selection from a science data frame. The DPU will use the contents of a table to define which words are extracted from the data frame into the telemetry packet (the table contains set of flags indicating the data required – 0 = not selected, 1= selected). The data is transmitted in a Selected Data Packet, TM(21,2) with the SID identifying the data structure.

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 15 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x001F |
| FRAMEID |
| SELECTEDSID |
| TABLEID |
| Checksum |

Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Illegal_Frame_ID | (1,8) | 0x0815 | Not a valid frame ID |
| Illegal_Table_ID | (1,8) | 0x0823 | Not a valid table ID |

##### Function 0xCA DPU, Activity 0x11: DISABLE_SELECTION

Disable selection for a science data frame. The complete data frame will now be placed into the science telemetry packets

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 11 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0020 |
| FRAMEID |
| Checksum |

Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Illegal_Selection_ID | (1,8) | 0x0816 | Not a valid Selection ID |
| Illegal_Frame_ID | (1,8) | 0x0815 | Not a valid frame ID |
| Undefined_Sel_Table | (1,8) | 0x0817 | Table ID is not defined |
| Invalid_Len_Sel_Table | (1,8) | 0x0818 | Length of Table does not match the selected Frame ID’s Length |
| Invalid_Content_Sel_Table | (1,8) | 0x819 | Content of Table doesn’t contain a valid Boolean value |

##### Function 0xCC HSK, Activity 0x01: DEFINE_NEW_HK_REPORT

This command is used to define/redefine housekeeping reports. The following procedure is used

- An on-board table is loaded with the definition of the report using one or more 'Update_Table' commands. The format of the table contents is given in RD08.

- An on-board table is loaded with monitoring information

- A 'Define New Housekeeping Parameter Report' is used to associate the table containing the report definition and the corresponding monitoring table with a HK_Packet_ID, a sampling interval (in msec) and a structure ID (SID). In this case:

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 21 |
| 0 | 0 | 0 | 0 | Ack | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0021 |
| HKPCKTID |
| HKSID |
| HKINTERVAL |
| HKREPEAT |
| TABLEID |
| Checksum |

Notes:

In order to redefine a report, the report must first be ‘cleared’ using a ‘Clear Housekeeping Parameter Report’ command, which has the effect of stopping report generation in order that the table containing the definition of the report and the corresponding monitor table contents may be modified. Report generation restarts with the execution of this service.

Currently we assume that only one housekeeping report (frame) will be sent in each packet. In the event that we need more than one (e.g. to increase the efficiency of reporting critical housekeeping) HKREPEAT will be increased to specify the number of hsk frames per packet.

An on board table will contain in TBD format the information about parameters to be monitored; since monitoring is performed on parameters sampled as part of the nominal HK packet, a monitoring table_ID must be communicated to the OBS each time the HK table ID is updated. The details are TBD.

##### Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Illegal_HK_Packet_ID | (1,8) | 0x0821 | HK_Packet_ID Out of Range |
| Illegal_HK_SID | (1,8) | 0x0822 | HK_SID MSB not 0x03 |
| Illegal_Table_ID | (1,8) | 0x0823 | TABLEID is out of range of possible table numbers |
| Illegal_HK_Sampling Interval | (1,8) | 0x0824 | HK_Sampling Interval is less than the absolute limit (10, TBC) |
| Undefined_HK_Table | (1,8) | 0x0825 | Table given by TABLEID is not defined |
| Report_in_Use | (1,8) | 0x0827 | An attempt is being made to modify a report without first ‘clearing’ it. |

##### Function 0xCC HSK, Activity 0x02: CLEAR_HK_REPORT

This command is used to clear the definition of a housekeeping report. It is usually used prior to redefining the report with TM(8,4):Funct-Act CC-01 and has the affect of stopping report generation within the OBS.

This command should not be used for disabling reporting (use service (14,2) for this) as the definition of the report contents and sampling interval is lost.

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 11 |
| 0 | 0 | 0 | 0 | Ack | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0022 |
| HKPCKTID |
| Checksum |

##### Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Illegal_HK_Packet_ID | (1,8) | 0x0821 | HK_Packet_ID Out of Range |
| Undefined_HK_Packet_ID | (1,8) | 0x829 | HK Packet ID not associated with a table |

##### Function 0xCC HSK, Activity 0x03: REPORT_HK_REPORT

This command is used to report the definition of a housekeeping report.

The information requested by this command is reported in TM service (21,4).  This contains only the information provided in the report definition telecommand. The actual definition of the report contents may be obtained by dumping the appropriate table.

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 11 |
| 0 | 0 | 0 | 0 | Ack | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0023 |
| HKPCKTID |
| Checksum |

##### Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Illegal_HK_Packet_ID | (1,8) | 0x0821 | HK_Packet_ID Out of Range |
| Undefined_HK_Packet_ID | (1,8) | 0x829 | HK Packet ID not associated with a table |

##### Function 0xCB HSK, Activity 0x01: FORCE_WRONG_CRC

This command is used to force the OBS to generate the wrong CRC for the next TM packet

This is used for diagnostic purposes only.

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 11 |
| 0 | 0 | 0 | 0 | Ack | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| SID=0x0001 |
| Checksum |

##### Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |

#### ReportFunction Status (Service 8,5) REPORT_FUNCTION

This telecommand requests a report on the status of a function. The instrument should respond with a TM(8,6) report.

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 7 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Checksum |

### Time Management

#### Enable Time Verification (Service 9,7) ENABLE_TIME_VERIFICATION

On receipt of this telecommand the instrument shall issue a Time Verification Report, TM(9,9).

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | 0 | 0 | 0 | Count |
| Length = 5 |
| 0 | 0 | 0 | 0 | Ack | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Checksum |

### Unused Service

Not Available

### On-Board Scheduling

Not Used

### On-Board Monitoring

Not Used

### Unused Service

Not Available

### Packet Transmission Control

#### Enable Generation of Telemetry Packets (Service 14,1) ENABLE_TM_GENERATION

This telecommand enables the transmission of instrument telemetry packets. By default all packets are enabled for transmission when the OBS starts. This telecommand is therefore only needed to restart transmission after transmission has been disabled.

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length |
| 0 | 0 | 0 | 0 | Ack | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| NPCKTS |
| TYPE | SUBTYPE |
| PACKETID |
| Repeat Type, Subtype and SID NPCKTS-1 times |
| Checksum |

Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Illegal_Type | (1,8) | 0x0e01 | Not a valid packet type for this APID |
| Illegal_Subtype | (1,8) | 0x0e02 | Not a valid subtype for packet with type TYPE |
| Illegal_PacketID | (1,8) | 0x0e03 | Not a valid Packet ID for packet with type TYPE and subtype SUBTYPE |
| Bad_NPCKTS | (1.8) | 0x0e04 | Number of packets to be enabled is not correct for telecommand length |

#### Disable Generation of Telemetry Packets (Service 14,2) DISABLE_TM_GENERATION

This telecommand disables the transmission of instrument telemetry packets. By default all packets are enabled for transmission when the OBS starts.

Note: Disabling TM generation does not stop generation of the TM packets within the OBS. These are created and processed as normal, but the packet is not passed to the 1553 interface to be sent to the CDMU. This is necessary to ensure that Housekeeping Monitoring continues to function even if the housekeeping TM is disabled, for example.

To be Confirmed

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length |
| 0 | 0 | 0 | 0 | Ack | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| NPCKTS |
| TYPE | SUBTYPE |
| PACKETID |
| Repeat Type, Subtype and Packet ID NPCKTS-1 times |
| Checksum |

Possible Errors

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Illegal_Type | (1,8) | 0x0E01 | Not a valid packet type for this APID |
| Illegal_Subtype | (1,8) | 0x0E02 | Not a valid subtype for packet with type TYPE |
| Illegal_PacketID | (1,8) | 0x0E03 | Not a valid Packet ID for packet with type TYPE and subtype SUBTYPE |
| Bad_NPCKTS | (1.8) | 0x0E04 | Number of packets to be enabled is not correct for telecommand length |

#### Report Enabled Telemetry Packets (Service 14,3) REPORT_ENABLED_TM

This telecommand requests a list of telemetry packet types and subtypes that are enabled for transmission

The list is reported in TM service  (14,4)

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 5 |
| 0 | 0 | 0 | 0 | Ack | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Checksum |

### On-Board Storage and Retrieval

Not Used

### On-Board Traffic Management

Not Used

### Test Service

#### Perform Connection Test (Service 17,1) TEST_CONNECTION

This test is used to check the End-to-End connection to the instrument. The instrument shall respond with a Successful Command Acceptance Report, TM(1,1),  followed by a Link Connection Report, TM(17,2).

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | 0 | 0 | 0 | Count |
| Length = 5 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Checksum |

### On-Board Control Procedures

Not Used

### Action/Event Service

Not Used

### Information Distribution Service

Not Used

### Science Data

Not Applicable

### Context Saving Service

Not Used

# SPIRE Telemetry Packets

This section defines all the TM packets that will be produced by SPIRE.

## Telemetry Packet Types

The Packet Structure ICD (AD1) defines many types of service that can be provided by an Application. The following table shows the telemetry packet types that will be produced by the SPIRE.

| Description | Service Type | Service Sub-Type | Comments |
| --- | --- | --- | --- |
| Telecommand Verification Service |  |  |  |
| Telecommand Acceptance Report - Success | 1 | 1 |  |
| Telecommand Acceptance Report - Failure | 1 | 2 |  |
| Telecommand Execution Report - Started | 1 | 3 |  |
| Telecommand Execution Report - Progress | 1 | 5 |  |
| Telecommand Execution Report - Completed | 1 | 7 |  |
| Telecommand Execution Report - Failure | 1 | 8 |  |
| Telecommand Contents Report | 1 | 9 | Not Used |
| Device Command Distribution | 2 |  | N/A |
| Housekeeping and Diagnostic Data Reporting |  |  |  |
| HK Parameter Report Definitions Report | 3 | 10 | Not Used |
| Diagnostic Parameter Definitions Report | 3 | 12 | Not Used |
| Housekeeping Parameter Report | 3 | 25 |  |
| Diagnostic Parameter Report | 3 | 26 | Not Used |
| Event Reporting |  |  |  |
| Event Report | 5 | 1 |  |
| Exception Report | 5 | 2 |  |
| Error/Alarm Report | 5 | 4 |  |
| Memory Management |  |  |  |
| Memory Dump, Absolute Addresses | 6 | 6 |  |
| Memory Check Report, Absolute Addresses | 6 | 10 |  |
| Function Management |  |  |  |
| Function Status Report | 8 | 6 |  |
| Time Management |  |  |  |
| Central Time Reference | 9 | 8 | Not Used |
| Time Verification Report | 9 | 9 |  |
| On-Board Scheduling | 11 |  | Not Used |
| On-Board Monitoring |  |  |  |
| Current Monitoring List Report | 12 | 9 | Not Used |
| Packet Transmission Control |  |  |  |
| Enabled Telemetry Packets Report | 14 | 4 |  |
| On-Board Storage and Retrieval | 15 |  | Not Used |
| Test Service |  |  |  |
| Connection Test Report | 17 | 2 |  |
| On-Board Control procedures | 18 |  | Not Used |
| Action/Event Service | 19 |  | Not Used |
| Information Distribution Service | 20 |  | Not Used |
| Science Data |  |  |  |
| Nominal Science Data Report | 21 | 1 |  |
| Science Type B Data Report | 21 | 2 |  |
| Diagnostic Science Data Report | 21 | 3 |  |
| Auxiliary Science Data Report | 21 | 4 |  |
| Context Saving Service | 22 |  | Not Used |

## Telemetry Packet definitions

### TC Verification Service

#### Telecommand Acceptance Report - Success (1,1)

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 15 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| TC_Packet_ID |
| TC_Packet_Sequence_Control |
| Checksum |

#### Telecommand Acceptance Report - Failure (1,2)

The structure of this packet depends on the type of error found.

##### Packet Control Errors

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| TC_Packet_ID |
| TC_Packet_Sequence_Control |
| Failure Code |
| TC_Packet_Length |
| Data_Field_Header |
| Data_Field_Error_Control |
| Parameter |
| Checksum |

##### Packet Content Error

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length=57 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| TC_Packet_ID |
| TC_Packet_Sequence_Control |
| Failure Code |
| Parameters |
| Checksum |

#### Telecommand Execution Report - Started (1,3)

This report is generated at the start of execution of a telecommand. It is only transmitted in telemetry if the corresponding bit of the Ack field is set.

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 15 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| TC_Packet_ID |
| TC_Packet_Sequence_Control |
| Checksum |

#### Telecommand Execution Report - Progress (1,5)

These reports may be generated by an executing telecommand. They are only transmitted in telemetry if the corresponding bit of the Ack filed is set.

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 17 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| TC_Packet_ID |
| TC_Packet_Sequence_Control |
| Step_Number |
| Checksum |

#### Telecommand Execution Report - Completion (1,7)

This report is generated at the successful completion of execution of a telecommand. It is only transmitted in telemetry if the corresponding bit of the Ack field is set.

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 15 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| TC_Packet_ID |
| TC_Packet_Sequence_Control |
| Checksum |

#### Telecommand Execution Report - Failure (1,8)

This report is generated at the unsuccessful completion of execution of a telecommand

The structure of this packet depends on the type of error found., but follows the general form:

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |
| 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| TC_Packet_ID |
| TC_Packet_Sequence_Control |
| Failure Code |
| Parameters |
| Checksum |

The following error Failure Codes have been defined with the parameters to be provided in the TM packet:

| Error | Failure Code | Parameters |
| --- | --- | --- |
| Illegal_Memory_ID | 0x0601 | Requested Memory_ID |
| Illegal_Start_Address | 0x0602 | Required Start Address |
| Illegal_Nsau | 0x0603 | Uplinked Nsau |
| Bad_Nsau | 0x0604 | Uplinked Nsau |
| Bad_CRC | 0x0605 | Uplinked CRC |
| Bad_Load | 0x0606 | Calculated Checksum |
| Illegal_Function_ID | 0x0801 |  |
| Illegal_Activity_ID | 0x0802 |  |
| Illegal_Table_ID | 0x0805 | Uplinked Table_ID |
| Illegal_Table_Index | 0x0806 | Uplinked Table Index |
| Bad_Data | 0x0808 | Number of 32 bit data words uplinked |
| Table_Space_Full | 0x0809 | Required Table Length |
| VM_Inactive | 0x080A | Index of VM required to stop |
| VM_Active | 0x080C | Index of VM required to run |
| Bad NData | 0x080D | Uplinked number of Data Words |
| LS_Sync_Error | 0x080E | Sync command sent |
| Illegal_FIFOFlags | 0x080F | Uplinked FIFO flag word |
| VM_Undefined_Table_ID | 0x0810 | Table_ID |
| Undefined_Table | 0x0811 | Requested Table_ID |
| EEPROM_Failed | 0x0812 | Number of errors |
| Table_Busy | 0x0813 | Requested Table ID |
| Illegal_Frame_ID | 0x0815 | Uplinked Frame_ID |
| Illegal_Select_ID | 0x0816 | Uplinked Select_ID |
| Undefined_Sel_Tanble | 0x0817 | Table ID not defined |
| Invalid_Len_Sel_Table | 0x0818 | Table size doesn’t match with Frame Length |
| Invalid_Content_Sel_Table | 0x0819 | Table doesn’t contain a valid Boolean array |
| Peak_up Error | 0x0820 | ------ |
| Illegal_HK_Packet_ID | 0x0821 | Uplinked HK_Packet_ID |
| Illegal_HK_SID | 0x0822 | Uplinked HK_SID |
| Illegal_Table_ID | 0x0823 | Uplinked Table_ID |
| Illegal_HK_Sampling Interval | 0x0824 | Required HK_Sampling_Interval (ms) |
| Undefined_HK_Table | 0x0825 | Uplinked HK Table_ID |
| Undefined_Monitoring_TableID | 0x0826 | Uplinked Monitoring_TableID |
| Report_in_Use | 0x0827 | Uplinked HK_Packet_ID |
| Undefined_HK_ID | 0x0829 | HK Packet ID requested doesn’t correspond to a currently running table |
| Function_Active | 0x0830 | Requested Function is already Active |
| Function_Stopped | 0x0831 | Requested Function is already Stopped |
| Illegal_Type | 0x0E01 | Type |
| Illegal_Subtype | 0x0E02 | Subtype |
| Illegal_SID | 0x0E03 | Packet ID |
| Bad_NPCKTS | 0x0E04 | NPCKTS |

### Device Command Distribution

Not Used

### Housekeeping and Diagnostic Data Reporting

#### Housekeeping Parameter Report  (Service 3,25)

The general packet structure is shown below. The Structure ID identifies the housekeeping packet type.

| 0 | 0 | 0 | 0 | 1 | APID |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 |
| 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| SID |
| Parameters |
| Checksum |

#### Critical Housekeeping Report (SID=0x0300)

| Location (octet) | Field Offset (bits) | Field Length (bits) | Parameter Name | CMD | Ref. | Description |
| --- | --- | --- | --- | --- | --- | --- |
| 18 | 0 | 32 | OBSID_C |  | AD03 | Observation ID |
| 22 | 0 16 | 32 16 | BBID_C BBTYPE_C |  | AD03 | Building Block ID |
| 26 | 0 | 16 | MODE_C |  |  | Observing Mode – set by command |
| 28 | 0 | 16 | STEP_C |  |  | Observation Step – set by command |
| 30 | 0 | 16 | TCRECV_C |  |  | Count of Telecommands Received |
| 32 | 0 | 16 | TCEXEC_C |  |  | Count of Telecommands Executed |
| 34 | 0 | 48 | MEMSTAT_C |  |  | Memory Check Flags – updated by background memory checking task |
| 40 | 0 | 16 | MONSTAT_C |  |  | Status of subsystems monitoring |
| 42 | 0 | 16 | EVENTSTAT_C |  |  | Status of events |
| 44 | 0 0 1 2 3 4 | 16 1 1 1 1 2 | DCUIFSTAT_C DCUIFOLAPERR_C DCU IFBCASTERR_C DCUIFREADERR_C DCUIFTOUTERR_C DCUIFCMDSTAT_C | 88000000 | RD06 | CmdIfStat Command Overlapped Forbidden Broadcast Forbidden Read SubSystem Timeout LastCmdStatus |
| 46 | 0 0 1 2 3 4 | 16 1 1 1 1 2 | MCUIFSTAT_C MCUIFOLAPERR_C MCUIFBCASTERR_C MCUIFREADERR_C MCUIFTOUTERR_C MCUIFCMDSTAT_C | 98000000 | RDO6 | CmdIfCtrl DataIfReset SubSystemRst StatusRst |
| 48 | 0 0 1 2 3 4 | 16 1 1 1 1 2 | SCUIFSTAT_C SCUIFOLAPERR_C SCUIFBCASTERR_C SCUIFREADERR_C SCUIFTOUTERR_C SCUIFCMDSTAT_C | A8000000 | RDO6 | CmdIfCtrl DataIfReset SubSystemRst StatusRst |
| 50 | 0 0 1 2 3 4 5 | 16 1 1 1 1 1 1 | PSWJFETSTAT_C PSWJFETPWR1_C PSWJFETPWR2_C PSWJFETPWR3_C PSWJFETPWR4_C PSWJFETPWR5_C PSWJFETPWR6_C | 8C120000 | RD06 | PSW_JFET_1 PSW_JFET_2 PSW_JFET_3 PSW_JFET_4 PSW_JFET_5 PSW_JFET_6 |
| 52 | 0 0 1 2 3 4 5 6 | 16 1 1 1 1 1 1 1 | PMLWJFETSTAT_C PMWJFETPWR1_C PMWJFETPWR2_C PMWJFETPWR3_C PMWJFETPWR4_C PLWJFETPWR1_C PLWJFETPWR2_C TCJFETPWR_C | 8C130000 | RDO6 | PMW_JFET_1 PMW_JFET_2 PMW_JFET_3 PMW_JFET_4 PLW_JFET_1 PLW_JFET_2 TC_JFET |
| 54 | 0 0 1 2 | 16 1 1 1 | SPECJFETSTAT_C SLWJFETPWR1_C SSWJFETPWR1_C SSWJFETPWR2_C | 8C370000 | RD06 | SLW_JFET1 SSW_JFET1 SSW_JFET2 |
| 56 | 0 0 1 2 3 4 5 6 7 8 9 10 11 | 16 1 1 1 1 1 1 1 1 1 1 1 1 | LIASTAT_C LIA01STAT_C LIA02STAT_C LIA03STAT_C LIA04STAT_C LIA05STAT_C LIA06STAT_C LIA07STAT_C LIA08STAT_C LIA09STAT_C LIA10STAT_C LIA11STAT_C LIA12STAT_C | 8C3F0012 | RD06 | PWR_STATUS, LIA 1 to LIA 12 LIA 1 +5V/+9V/-9V status LIA 2 +5V/+9V/-9V status LIA 3 +5V/+9V/-9V status LIA 4 +5V/+9V/-9V status LIA 5 +5V/+9V/-9V status LIA 6 +5V/+9V/-9V status LIA 7 +5V/+9V/-9V status LIA 8 +5V/+9V/-9V status LIA 9 +5V/+9V/-9V status LIA 10 +5V/+9V/-9V status LIA 11 +5V/+9V/-9V status LIA 12 +5V/+9V/-9V status |
| 58 | 0 | 16 | MCUERR_C | 99E90000 | RD06 | ErrorCode |
| 60 | 0 | 16 | SMECSTAT_C | 98600000 | RD06 | SMECStatus |
| 62 | 0 | 16 | BSMSTAT_C | 99000000 | RD06 | BSMStatus |
| 64 |  |  |  |  |  |  |
| 66 | 0 | 16 | SCUSTAT_C | A8800000 | RD06 | ScuStatus |
| 68 | 0 | 16 | SUBKTEMP_C | A8F00000 | RD06 | CEVTemp |
| 70 | 0 0 8 12 | 16 7 11 15 | OBSVER_C ‘j’ ‘2’ ‘1’ |  |  | SubVersion Version Issue |

#### Nominal Housekeeping Report (SID=0x0301)

The following table lists the field to be found in this report

| Location | Field Offset (bits) | Field Length (bits) | Parameter Name | CMD | Ref. | Description |
| --- | --- | --- | --- | --- | --- | --- |
| 18 | 0 | 32 | OBSID | 20010000 | AD03 | Observation ID |
| 22 | 0 16 | 32 16 | BBID BBTYPE |  | AD03 | Building Block ID |
| 26 | 0 | 16 | MODE | 10030000 |  | Observing Mode – set by command |
| 28 | 0 | 16 | STEP | 10040000 |  | Observation Step – set by command |
| 30 | 0 | 48 | THSK | 30050000 |  | Time of start of housekeeping collection |
| 36 | 0 | 48 | TRESET | 30060000 |  | Time of last reset command to the DRCU |
| 42 | 0 | 16 | TCRECV |  |  | Count of Telecommands Received |
| 44 | 0 | 16 | TCRECN | 10080000 | AD01 | Packet Sequence Control, Sequence count of latest received telecommand |
| 46 | 0 | 16 | TCEXEC |  |  | Count of Telecommands Executed |
| 48 | 0 | 16 | TCEXEN | 100A0000 | AD01 | Packet Sequence Control, Sequence count of latest executed telecommand |
| 50 | 0 | 16 | TM1N |  | AD01 | Packet Sequence Control, Sequence count of TM Packets for APID1 |
| 52 | 0 | 16 | TM2N |  | AD01 | Packet Sequence Control, Sequence count of TM Packets for APID2 |
| 54 | 0 | 16 | TM3N |  | AD01 | Packet Sequence Control, Sequence count of TM Packets for APID3 |
| 56 | 0 | 16 | TM4N |  | AD01 | Packet Sequence Control, Sequence count of TM Packets for APID4 |
| 58 | 0 | 16 | TM5N |  | AD01 | Packet Sequence Control, Sequence count of TM Packets for APID5 |
| 60 | 0 | 16 | DCUFRAMECNT |  |  | No of frames read from DCU FIFO |
| 62 | 0 | 16 | MCUFRAMECNT |  |  | No of frames read from MCU FIFO |
| 64 | 0 | 16 | SCUFRAMECNT |  |  | No of frames read from SCU FIFO |
| 66 | 0 | 48 | TSYNC |  |  | Time of last re-sync with CDMS |
| 72 | 0 0 | 48 32 | TDIFF DIFFS |  |  | Difference between current DPU time and CDMS Time at last re-sync |
| 78 | 0 | 48 | MEMSTAT |  |  | Memory Check Flags – updated by background memory checking task |
| 84 | 0 | 16 | MONSTAT |  |  | Status of subsystems monitoring |
| 86 | 0 | 16 | EVENTSTAT |  |  | Status of events |
| 88 | 0 | 16 | VMSTAT |  |  | Status of VM (table ID being executed) |
| 90 | 0 | 16 | VM1STAT |  |  | Status of VM1 (table ID being executed) |
| 92 | 0 | 16 | VM2STAT |  |  | Status of VM2 (table ID being executed) |
| 94 | 0 | 16 | VM3STAT |  |  | Status of VM3 (table ID being executed) |
| 96 | 0 | 16 | TMMODE |  |  | Telemetry Mode (Normal/Burst) |
| 98 | 0 | 16 |  |  |  |  |
| 100 | 0 | 16 |  |  |  |  |
| 102 | 0 | 16 |  |  |  |  |
| 104 | 0 | 16 |  |  |  |  |
| 106 | 0 | 16 |  |  |  |  |
| 108 | 0 | 16 |  |  |  |  |
| 110 | 0 | 16 |  |  |  |  |
| 112 | 0 | 16 |  |  |  |  |
| 114 | 0 | 16 | DPUP5V | 04180000 | RD09 | DPU monitored +5V voltage line |
| 116 | 0 | 16 | DPUP15V | 04190000 | RD09 | DPU monitored +15V voltage line |
| 118 | 0 | 16 | DPUM15V | 041A0000 | RD09 | DPU monitored –15V voltage line |
| 120 | 0 | 16 | DPUTEMP | 041B0000 | RD09 | DPU monitored temperature |
| 122 | 0 | 16 | CPULOAD | 041C0000 | RD09 | DPU Processor Workload |
| 124 | 0 | 32 | LSLOAD |  | RD09 | DPU LS Workload |
| 128 | 0 | 16 | DPUP2.5V |  | RD09 | DPU monitored +2.5V Reference voltage line |
| 130 | 0 0 1 2 3 4 | 16 1 1 1 1 2 | DCUIFSTAT DCUIFOLAPERR DCUIFBCASTERR DCU IFREADERR DCUIFTOUTERR DCUIFCMDSTAT | 88000000 | RD06 | CmdIfStat Command Overlapped Forbidden Broadcast Forbidden Read SubSystem Timeout LastCmdStatus |
| 132 | 0 0 1 2 | 16 1 1 1 | DCUIFCTRL DCUDATAIFRESET DCUSSRESET DCUIFSTATRESET | 88010000 | RD06 | CmdIfCtrl DataIfReset SubSystemRst StatusRst |
| 134 | 0 | 16 | DCUSSDEL | 88020000 | RD06 | Subsystem Delay |
| 136 | 0 | 16 | DCUDATAMODE | 8C3C0000 | RD06 | DataMode |
| 138 | 0 | 16 | DCUDATAFRMS | 8C3D0000 | RD06 | FrameCount |
| 140 | 0 | 16 | DCUDATASTAT | 8C3E0000 | RD06 | StartFrame |
| 142 | 0 | 16 | PHOTBIASDIV | 8C180000 | RD06 | PhotoBiasDiv |
| 144 | 0 | 16 | PHOTBIASMODE | 8C000000 | RD06 | PhotoBiasMode |
| 146 | 0 | 16 | PHOTMCLKDIV | 8C190000 | RD06 | PhotoMClkDiv |
| 148 | 0 | 16 | PSWBIAS | 8C010000 | RD06 | PhotoBiasAmpl for Photo SW Channels |
| 150 | 0 | 16 | PMWBIAS | 8C020000 | RD06 | PhotoBiasAmpl for Photo MW Channels |
| 152 | 0 | 16 | PLWBIAS | 8C030000 | RD06 | PhotoBiasAmpl for Photo LW Channels |
| 154 | 0 | 16 | TCBIAS | 8C040000 | RD06 | PhotoBiasAmpl for Photo TC Channels |
| 156 | 0 | 16 | PSWPHASE | 8C1A0000 | RD06 | PhaseShift for Photo SW Channels |
| 158 | 0 | 16 | PMWPHASE | 8C1B0000 | RD06 | PhaseShift for Photo MW Channels |
| 160 | 0 | 16 | PLWPHASE | 8C1C0000 | RD06 | PhaseShift for Photo LW Channels |
| 162 | 0 | 16 | TCPHASE | 8C1D0000 | RD06 | PhaseShift for Photo TCChannels |
| 164 | 0 0 1 2 3 4 5 | 16 1 1 1 1 1 1 | PSWJFETSTAT PSWJFETPWR1 PSWJFETPWR2 PSWJFETPWR3 PSWJFETPWR4 PSWJFETPWR5 PSWJFETPWR6 | 8C120000 | RD06 | PSW_JFET_1 PSW_JFET_2 PSW_JFET_3 PSW_JFET_4 PSW_JFET_5 PSW_JFET_6 |
| 166 | 0 0 1 2 3 4 5 6 | 16 1 1 1 1 1 1 1 | PMLWJFETSTAT PMWJFETPWR1 PMWJFETPWR2 PMWJFETPWR3 PMWJFETPWR4 PLWJFETPWR1 PLWJFETPWR2 TCJFETPWR | 8C130000 | RD06 | PMW_JFET_1 PMW_JFET_2 PMW_JFET_3 PMW_JFET_4 PLW_JFET_1 PLW_JFET_2 TC_JFET |
| 168 | 0 | 16 | PSWJFET1V | 8C050000 | RD06 | PSW JFET Source Voltage for Channel 1 |
| 170 | 0 | 16 | PSWJFET2V | 8C060000 | RD06 | PSW JFET Source Voltage for Channel 2 |
| 172 | 0 | 16 | PSWJFET3V | 8C070000 | RD06 | PSW JFET Source Voltage for Channel 3 |
| 174 | 0 | 16 | PSWJFET4V | 8C080000 | RD06 | PSW JFET Source Voltage for Channel 4 |
| 176 | 0 | 16 | PSWJFET5V | 8C090000 | RD06 | PSW JFET Source Voltage for Channel 5 |
| 178 | 0 | 16 | PSWJFET6V | 8C0A0000 | RD06 | PSW JFET Source Voltage for Channel 6 |
| 180 | 0 | 16 | PMWJFET1V | 8C0B0000 | RD06 | PMW JFET Source Voltage for Channel 1 |
| 182 | 0 | 16 | PMWJFET2V | 8C0C0000 | RD06 | PMW JFET Source Voltage for Channel 2 |
| 184 | 0 | 16 | PMWJFET3V | 8C0D0000 | RD06 | PMW JFET Source Voltage for Channel 3 |
| 186 | 0 | 16 | PMWJFET4V | 8C0E0000 | RD06 | PMW JFET Source Voltage for Channel 4 |
| 188 | 0 | 16 | PLWJFET1V | 8C0F0000 | RD06 | PLW JFET Source Voltage for Channel 1 |
| 190 | 0 | 16 | PLWJFET2V | 8C100000 | RD06 | PLW JFET Source Voltage for Channel 2 |
| 192 | 0 | 16 | PHOTHTRV | 8C110000 | RD06 | PhotoHeaterBias |
| 194 | 0 | 16 | TCJFETV | 8C140000 | RD06 | TC JFET Source Voltage |
| 196 | 0 | 16 | SPECBIASDIV | 8C380000 | RD06 | SpectroBiasDiv |
| 198 | 0 | 16 | SPECBIASMODE | 8C300000 | RD06 | SpectroBiasMode |
| 200 | 0 | 16 | SPECMCLKDIV | 8C390000 | RD06 | SpectroMClkDiv |
| 202 | 0 | 16 | SSWBIAS | 8C310000 | RD06 | SpectroBiasAmpl for Spectro SW Channels |
| 204 | 0 | 16 | SLWBIAS | 8C320000 | RD06 | SpectroBiasAmpl for Spectro MW Channels |
| 206 | 0 | 16 | SSWPHASE | 8C3A0000 | RD06 | PhaseShift for Spectro SW Channels |
| 208 | 0 | 16 | SLWPHASE | 8C3B0000 | RD06 | PhaseShift for Spectro LW Channels |
| 210 | 0 0 1 2 | 16 1 1 1 | SPECJFETSTAT SLWJFETPWR1 SSWJFETPWR1 SSWJFETPWR2 | 8C370000 | RD06 | SLW_JFET1 SSW_JFET1 SSW_JFET2 |
| 212 | 0 | 16 | SSWJFET1V | 8C350000 | RD06 | SSW JFET Source Voltage for Channel 1 |
| 214 | 0 | 16 | SSWJFET2V | 8C360000 | RD06 | SSW JFET Source Voltage for Channel 2 |
| 216 | 0 | 16 | SLWJFETV | 8C340000 | RD06 | SLW JFET Source Voltage |
| 218 | 0 | 16 | SPECHTRV | 8C330000 | RD06 | Spectro Heater Bias |
| 220 | 0 | 16 | TC1TEMP | 8C3F001A | RD06 | T/C 1 |
| 222 | 0 | 16 | TC2TEMP | 8C3F001C | RD06 | T/C 2 |
| 224 | 0 | 16 | TC3TEMP | 8C3F001E | RD06 | T/C 3 |
| 226 | 0 | 16 | BIASP5V | 8C3F000E | RD06 | BIAS/DAQ_IF +5V Voltage (before post regulator) |
| 228 | 0 | 16 | BIASP9V | 8C3F000F | RD06 | BIAS/DAQ_IF +9V Voltage (before post regulator) |
| 230 | 0 | 16 | BIASM9V | 8C3F0010 | RD06 | BIAS/DAQ_IF -9V Voltage (before post regulator) |
| 232 | 0 0 8 12 | 16 7 11 15 | OBSVER ‘j’ ‘2’ ‘1’ |  |  | SubVersion Version Issue |
| 234 | 0 | 16 |  |  |  |  |
| 236 | 0 | 16 |  |  |  |  |
| 238 | 0 | 16 |  |  |  |  |
| 240 | 0 | 16 |  |  |  |  |
| 242 | 0 | 16 | PLIAP5V | 8C3F0011 | RD06 | LIAP +5V Voltage (before post regulator) |
| 244 | 0 | 16 | PLIAP9V | 8C3F0012 | RD06 | LIAP +9V Voltage (before post regulator) |
| 246 | 0 | 16 | PLIAM9V | 8C3F0013 | RD06 | LIAP -9V Voltage (before post regulator) |
| 248 | 0 | 16 | SLIAP5V | 8C3F0014 | RD06 | LIAS +5V Voltage (before post regulator) |
| 250 | 0 | 16 | SLIAP9V | 8C3F0015 | RD06 | LIAS +9V Voltage (before post regulator) |
| 252 | 0 | 16 | SLIAM9V | 8C3F0016 | RD06 | LIAS -9V Voltage (before post regulator) |
| 254 | 0 | 16 |  |  |  |  |
| 256 | 0 | 16 |  |  |  |  |
| 258 | 0 | 16 | LIAP9TEMP | 8C3F0004 | RD06 | LIA_B1_TEMP, LIA board 1 temperature |
| 260 | 0 | 16 | LIAP8TEMP | 8C3F0005 | RD06 | LIA_B2_TEMP, LIA board 2 temperature |
| 262 | 0 | 16 | LIAP7TEMP | 8C3F0006 | RD06 | LIA_B3_TEMP, LIA board 3 temperature |
| 264 | 0 | 16 | LIAP6TEMP | 8C3F0007 | RD06 | LIA_B4_TEMP, LIA board 4 temperature |
| 266 | 0 | 16 | LIAP5TEMP | 8C3F0008 | RD06 | LIA_B5_TEMP, LIA board 5 temperature |
| 268 | 0 | 16 | LIAP4TEMP | 8C3F0009 | RD06 | LIA_B6_TEMP, LIA board 6 temperature |
| 270 | 0 | 16 | LIAP3TEMP | 8C3F000A | RD06 | LIA_B7_TEMP, LIA board 7 temperature |
| 272 | 0 | 16 | LIAP2TEMP | 8C3F000B | RD06 | LIA_B8_TEMP, LIA board 8 temperature |
| 274 | 0 | 16 | LIAP1TEMP | 8C3F000C | RD06 | LIA_B9_TEMP, LIA board 9 temperature |
| 276 | 0 | 16 | LIAS1TEMP | 8C3F0001 | RD06 | LIA_B10_TEMP, LIA board 10 temperature |
| 278 | 0 | 16 | LIAS2TEMP | 8C3F0002 | RD06 | LIA_B11_TEMP, LIA board 11 temperature |
| 280 | 0 | 16 | LIAS3TEMP | 8C3F0003 | RD06 | LIA_B12_TEMP, LIA board 12 temperature |
| 282 | 0 | 16 | BIASTEMP | 8C3F0000 | RD06 | BIAS_TEMP, Bias board temperature |
| 284 | 0 | 16 | DAQTEMP | 8C3F000D | RD06 | DAQ_IF_TEMP, DAQ IF board temperature |
| 286 | 0 4 5 6 7 8 9 10 11 12 13 14 15 | 16 1 1 1 1 1 1 1 1 1 1 1 1 | LIASTAT LIAS3STAT LIAS2STAT LIAS1STAT LIAP9STAT LIAP8STAT LIAP7STAT LIAP6STAT LIAP5STAT LIAP4STAT LIAP3STAT LIAP2STAT LIAP1STAT | 8C3F0017 | RD06 | PWR_STATUS, LIA 1 to LIA 12 LIA 1 +5V/+9V/-9V status (0=OK) LIA 2 +5V/+9V/-9V status (0=OK) LIA 3 +5V/+9V/-9V status (0=OK) LIA 4 +5V/+9V/-9V status (0=OK) LIA 5 +5V/+9V/-9V status (0=OK) LIA 6 +5V/+9V/-9V status (0=OK) LIA 7 +5V/+9V/-9V status (0=OK) LIA 8 +5V/+9V/-9V status (0=OK) LIA 9 +5V/+9V/-9V status (0=OK) LIA 10 +5V/+9V/-9V status (0=OK) LIA 11 +5V/+9V/-9V status (0=OK) LIA 12 +5V/+9V/-9V status (0=OK) |
| 288 | 0 0 1 2 3 4 | 16 1 1 1 1 2 | MCUIFSTAT MCUIFOLAPERR MCUIFBCASTERR MCUIFREADERR MCUIFTOUTERR MCUIFCMDSTAT | 98000000 | RD06 | CmdIfStat Command Overlapped Forbidden Broadcast Forbidden Read SubSystem Timeout LastCmdStatus |
| 290 | 0 0 1 2 | 16 1 1 1 | MCUIFCTRL MCUDATIFRESET MCUSSRESET MCUIFSTATRESET | 98010000 | RD06 | CmdIfCtrl DataIfReset SubSystemRst StatusRst |
| 292 | 0 | 16 | MCUSSDEL | 98020000 | RD06 | Subsystem Delay |
| 294 | 0 | 16 | MCUP5V | 99E00000 | RD07 | P5V |
| 296 | 0 | 16 | MCUP14V | 99E10000 | RD07 | P14V |
| 298 | 0 | 16 | MCUM14V | 99E20000 | RD07 | M14V |
| 300 | 0 | 16 | MCUP15V | 99E30000 | RD06 | P15V |
| 302 | 0 | 16 | MCUM15V | 99E40000 | RD06 | M15V |
| 304 | 0 | 16 | MCUMACTEMP | 99E50000 | RD07 | MACTemp |
| 306 | 0 | 16 | MCUSMECTEMP | 99E60000 | RD07 | SMECTemp |
| 308 | 0 | 16 | MCUBSMTEMP | 99E70000 | RD07 | BSMTemp |
| 310 |  |  |  |  |  |  |
| 312 | 0 | 16 | MCUERR | 99E90000 | RD06 | ErrorCode |
| 314 | 0 | 16 | MCUSCHEDCNTLSW | 99EA0000 | RD06 | SchedCntLSW |
| 316 | 0 | 16 | MCUSCHEDCNTMSW | 99EB0000 | RD06 | SchedCntMSW |
| 318 | 0 | 16 | MCUTM10TSAMPLE | 99C00000 | RD06 | TP10SampFreq |
| 320 | 0 | 16 | MCUFRAMESTART | 99C10000 | RD07 | FrameStart |
| 322 | 0 | 16 | MCUTM12TSAMPLE | 99C20000 | RD06 | TP12SampFreq |
| 324 | 0 | 16 | MCUFRAMES | 99C30000 | RD07 | FrameNumber |
| 326 | 0 | 16 | MCUTM14TSAMPLE | 99C40000 | RD06 | TP14SampFreq |
| 328 | 0 | 16 | MCUTM15TSAMPLE | 99C50000 | RD06 | TP15SampFreq |
| 330 | 0 | 16 | MCUTMSTATUS | 99DF0000 | RD06 | TelemetryStatus |
| 332 |  |  |  |  |  |  |
| 334 | 0 | 16 | MCUBOOTSTAT | 98200000 | RD06 | Boot Status Register |
| 336 | 0 | 16 | MCUDLOADCONF | 98210000 | RD06 | DownloadParam |
| 338 | 0 | 16 | MCUDLOADWORD | 98220000 | RD06 | DownloadWord |
| 340 | 0 | 16 | MCUDLOADPC | 98230000 | RD06 | DownloadCounter |
| 342 |  |  |  |  |  |  |
| 344 |  |  |  |  |  |  |
| 346 |  |  |  |  |  |  |
| 348 |  |  |  |  |  |  |
| 350 |  |  |  |  |  |  |
| 352 | 0 | 16 | SMECENCPWR | 98400000 | RD06 | SEncoderPwr |
| 354 | 0 | 16 | SMECLVDTPWR | 98410000 | RD06 | SLVDTPwr |
| 356 |  |  |  |  |  |  |
| 358 | 0 | 16 | SMECLATCHSTAT | 98430000 | RD06 | SlaunchLatch (commanded latch status) |
| 360 | 0 | 16 | SMECLOOPMODE | 98440000 | RD06 | SLoopMode |
| 362 | 0 | 16 | SCANSTART | 98460000 | RD06 | STrajStartPos |
| 364 | 0 | 16 | SCANEND | 98450000 | RD06 | STrajEndPos |
| 366 | 0 | 16 | SCANFSPEED | 98470000 | RD06 | SScanFwdSpeed |
| 368 | 0 | 16 | SCANS | 98480000 | RD06 | SScanNumber |
| 370 | 0 | 16 | SCANMODE | 98490000 | RD06 | STrajMode |
| 372 |  |  |  |  |  |  |
| 374 |  |  |  |  |  |  |
| 376 | 0 | 16 | SMECKP | 984A0000 | RD06 | SKp |
| 378 | 0 | 16 | SMECKD | 984B0000 | RD06 | SKd |
| 380 | 0 | 16 | SMECDFILT | 984C0000 | RD06 | SDerivFilter |
| 382 | 0 | 16 | SMECKI | 984D0000 | RD06 | SKi |
| 384 | 0 | 16 | SMECINTLIMIT | 984E0000 | RD06 | SIntegrationLimit |
| 386 | 0 | 16 | SMECINTTHRESH | 984F0000 | RD06 | SIntegration Threshold |
| 388 |  |  |  |  |  |  |
| 390 | 0 | 16 | SMECRATELIMIT | 98510000 | RD06 | SRateLimit |
| 392 | 0 | 16 | SMECDFILT2 | 98520000 | RD06 | SDerivFilter2 |
| 394 |  |  |  |  |  |  |
| 396 | 0 | 16 | SMECFFGAIN | 98540000 | RD06 | SFeedFwdGain |
| 398 | 0 | 16 | SMECFFOFFSET | 98550000 | RD06 | SFeedFwdOffset |
| 400 | 0 | 16 | SCANRSPEED | 98560000 | RD06 | SScanRevSpeed |
| 402 | 0 | 16 | SMECBEMFGAIN | 98900000 | RD06 | SMotorBEMFGain |
| 404 | 0 | 16 | SMECMOTORRES | 98910000 | RD06 | SMotorResistance |
| 406 | 0 | 16 | SMECMOTORBEMF | 98920000 | RD07 | MotorBEMF |
| 408 | 0 | 16 | SMECRATESCALE | 98930000 | RD06 | SRateScaleFactor |
| 410 |  |  |  |  |  |  |
| 412 |  |  |  |  |  |  |
| 414 |  |  |  |  |  |  |
| 416 | 0 | 16 | SMECLVDTOFFSET | 985E0000 | RD06 | ¦LVDTOffset |
| 418 | 0 | 16 | SMECLVDTSCALE | 985F0000 | RD06 | LVDTSCAle |
| 420 | 0 | 16 | SMECSTAT | 98600000 | RD06 | SMECStatus |
| 422 | 0 | 16 | SMECENCPOSN | 98610000 | RD06 | SEncoder IncrPosition |
| 424 | 0 | 16 | SMECENCSIG1 | 98620000 | RD06 | SEncoderSignal1 |
| 426 | 0 | 16 | SMECENCSIG2 | 98630000 | RD06 | SEncoderSignal2 |
| 428 | 0 | 16 | SMECENCSIG3 | 98640000 | RD06 | SEncoderSignal3 |
| 430 | 0 | 16 | SMECLVDTPOSN | 98650000 | RD06 | LVDT position |
| 432 | 0 | 16 | SMECLVDTACSIG | 98660000 | RD06 | LVDTAC |
| 434 | 0 | 16 | SMEVLVDTDCSIG | 98670000 | RD06 | LVDTDC |
| 436 | 0 | 16 | SMECTRAJPOSN | 98680000 | RD06 | TrajectoryPosition |
| 438 | 0 | 16 | SMECDACVAL | 98690000 | RD06 RD07 | SMECDACValue |
| 440 | 0 | 16 | SMECPOSNDELTA | 986A0000 | RD06 | EncLVDTPosDelta Position difference encoder/lvdt home |
| 442 | 0 | 16 | SMECENCFINEPOSN | 986B0000 | RD06 | EncoderFinePosition |
| 444 |  |  |  |  |  |  |
| 446 |  |  |  |  |  |  |
| 448 | 0 | 16 | SMECMEANSPEED | 986E0000 | RD06 | MeanSpeed |
| 450 | 0 | 16 | SMECSCANPOSNERR | 986F0000 | RD06 | MeanPositionError |
| 452 | 0 | 16 | SMECMOTORCURR | 98700000 | RD06 | SMotorCurrent |
| 454 | 0 | 16 | SMECMOTORVOLT | 98710000 | RD07 | SMotorVoltage |
| 456 |  |  |  |  |  |  |
| 458 |  |  |  |  |  |  |
| 460 |  |  |  |  |  |  |
| 462 |  |  |  |  |  |  |
| 464 |  |  |  |  |  |  |
| 466 |  |  |  |  |  |  |
| 468 |  |  |  |  |  |  |
| 470 |  |  |  |  |  |  |
| 472 |  |  |  |  |  |  |
| 474 |  |  |  |  |  |  |
| 476 |  |  |  |  |  |  |
| 478 |  |  |  |  |  |  |
| 480 |  |  |  |  |  |  |
| 482 |  |  |  |  |  |  |
| 484 |  |  |  |  |  |  |
| 486 |  |  |  |  |  |  |
| 488 |  |  |  |  |  |  |
| 490 | 0 | 16 | CHOPSENSPWR | 98C00000 | RD06 | CSensorPwr |
| 492 |  |  |  |  |  |  |
| 494 | 0 | 16 | CHOPLOOPMODE | 98C20000 | RD06 | ChopLoopMode |
| 496 | 0 | 16 | CHOPPOSN | 98C30000 | RD06 | Chop Target Position |
| 498 |  |  |  |  |  |  |
| 500 |  |  |  |  |  |  |
| 502 | 0 | 16 | BSMMODE | 98C60000 | RD06 | BSMMove |
| 504 | 0 | 16 | CHOPDERIVGAIN | 98C70000 | RD07 | CKdNed |
| 506 | 0 | 16 | CHOPKP | 98C80000 | RD06 | CKp |
| 508 | 0 | 16 | CHOPKD | 98C90000 | RD06 | CKd |
| 510 | 0 | 16 | CHOPKI | 98CA0000 | RD06 | CKi |
| 512 | 0 | 16 | CHOPINTREF | 98CB0000 | RD07 | CIntegrationRef |
| 514 | 0 | 16 | CHOPINTLIMIT | 98CC0000 | RD06 | CIntegLimit |
| 516 | 0 | 16 | CHOPFFGAIN | 98CD0000 | RD06 | CFeedFwdGain |
| 518 | 0 | 16 | CHOPFFGAINLARGE | 98CE0000 | RD07 | CFeedForward GainLarge |
| 520 | 0 | 16 | CHOPDIFFTC1 | 98CF0000 | RD06 | DiffFilterTC1 |
| 522 | 0 | 16 | CHOPDIFFTC2 | 98D00000 | RD06 | DiffFilterTC2 |
| 524 | 0 | 16 | CHOPRATELIMIT | 98D10000 | RD06 | CRateLimit |
| 526 | 0 | 16 | CHOPMOTBEMFGAIN | 98D20000 | RD06 | CMotorBEMFGain |
| 528 | 0 | 16 | CHOPMOTRES | 98D30000 | RD06 | CMotorResistance |
| 530 | 0 | 16 | CHOPMOTIND | 98D40000 | RD06 | CMotorInductance |
| 532 | 0 | 16 | CHOPFFGAINULIM | 98D50000 | RD07 | CFFgainupperlimit |
| 534 | 0 | 16 | CHOPFFGAINLLIM | 98D60000 | RD07 | CFFgainlowerlimit |
| 536 | 0 | 16 | CHOPBEMFRATEFILT1 | 98D70000 | RD06 | CBEMFRateFilter1 |
| 538 | 0 | 16 | CHOPBEMFRATEFILT2 | 98D80000 | RD06 | CBEMFRateFilter2 |
| 540 | 0 | 16 | CHOPJIGGCOUPLE | 98D9000 | RD07 | C2JCrosscoupling |
| 542 | 0 | 16 | BSMSTAT | 99000000 | RD07 | BSMStatus |
| 544 |  |  |  |  |  |  |
| 546 | 0 | 16 | CHOPPOSNERR | 99020000 | RD06 | CMeanPosError |
| 548 | 0 | 16 | CHOPSENSSIG | 99030000 | RD06 | CMagResSignal |
| 550 | 0 | 16 | CHOPDACVAL | 99040000 | RD06 | CDACValue |
| 552 | 0 | 16 | CHOPMOTORCURR | 99050000 | RD06 | CMotorCurrent |
| 554 | 0 | 16 | CHOPMOTORVOLT | 99060000 | RD06 | CVoltage |
| 556 |  |  |  |  |  |  |
| 558 | 0 | 16 | JIGGSENSPWR | 99400000 | RD06 | JSensorPwr |
| 560 |  |  |  |  |  |  |
| 562 | 0 | 16 | JIGGLOOPMODE | 99420000 | RD06 | JigLoopMode |
| 564 | 0 | 16 | JIGGPOSN | 99430000 | RD06 | JigTargetPos |
| 566 |  |  |  |  |  |  |
| 568 |  |  |  |  |  |  |
| 570 |  |  |  |  |  |  |
| 572 | 0 | 16 | JIGGDERIVGAIN | 99430000 | RD07 | JKdNeg |
| 574 | 0 | 16 | JIGGKP | 99480000 | RD06 | JKp |
| 576 | 0 | 16 | JIGGKD | 99490000 | RD06 | JKd |
| 578 | 0 | 16 | JIGGKI | 994A0000 | RD06 | JKi |
| 580 | 0 | 16 | JIGGINTREF | 994B0000 | RD06 | JIntegrationRef |
| 582 | 0 | 16 | JIGGINTLIMIT | 994C0000 | RD06 | JIntegLimint |
| 584 | 0 | 16 | JIGGFFGAIN | 994D0000 | RD06 | JFeedForwardGain |
| 586 | 0 | 16 | JIGGFFGAINLARGE | 994E0000 | RD07 | JFeedForwardGainLarge |
| 588 | 0 | 16 | JIGG DIFFTC1 | 994F0000 | RD06 | JDiffFilterTC1 |
| 590 | 0 | 16 | JIGG DIFFTC2 | 99500000 | RD06 | JdiffFilterTC2 |
| 592 | 0 | 16 | JIGGRATELIMIT | 99510000 | RD06 | JRateLimit |
| 594 | 0 | 16 | JIGGMOTBEMFGAIN | 99520000 | RD06 | JMotorBEMFGain |
| 596 | 0 | 16 | JIGGMOTRES | 99530000 | RD06 | JMotorResistance |
| 598 | 0 | 16 | JIGGMOTIND | 99540000 | RD06 | JMotorInductance |
| 600 | 0 | 16 | JIGGFFGAINULIM | 99550000 | RD07 | JFFgainupperlimit |
| 602 | 0 | 16 | JIGGFFGAINLLIM | 99560000 | RD07 | JFFgainlowerlimitr |
| 604 | 0 | 16 | JIGG BEMFRATEFILT1 | 99570000 | RD06 | JBEMFRAteFilter1 |
| 606 | 0 | 16 | JIGG BEMFRATEFILT2 | 99580000 | RD06 | JBENFRateFilter2 |
| 608 | 0 | 16 | JIGGCHOPCOUPLE | 99590000 | RD07 | J2CCrosscoupling |
| 612 |  |  |  |  |  |  |
| 614 | 0 | 16 | JIGGPOSNERR | 99820000 | RD06 | JMeanPosError |
| 616 | 0 | 16 | JIGGSENSSIG | 99830000 | RD06 | JMagREsSignal |
| 618 | 0 | 16 | JIGGDACVAL | 99840000 | RD06 | JDACValue |
| 620 | 0 | 16 | JIGGMOTORCURR | 99850000 | RD06 | JMotorCurrent |
| 622 | 0 | 16 | JIGGMOTORVOLT | 99860000 | RD07 | JVoltage |
| 624 | 0 | 16 | MCUPCKT10PARM05 | 99C60000 | RD07 | Pack10Param5 |
| 626 | 0 | 16 | MCUPCKT10PARM01 | 99C70000 | RD06 | Pack10Param1 |
| 628 | 0 | 16 | MCUPCKT10PARM02 | 99C80000 | RD06 | Pack10Param2 |
| 630 | 0 | 16 | MCUPCKT10PARM03 | 99C90000 | RD06 | Pack10Param3 |
| 632 | 0 | 16 | MCUPCKT10PARM04 | 99CA0000 | RD06 | Pack10Param4 |
| 634 | 0 | 16 | MCUPCKT12PARM01 | 99CB0000 | RD06 | Pack12Param1 |
| 636 | 0 | 16 | MCUPCKT12PARM02 | 99CC0000 | RD06 | Pack12Param2 |
| 638 | 0 | 16 | MCUPCKT12PARM03 | 99CD0000 | RD06 | Pack12Param3 |
| 640 | 0 | 16 | MCUPCKT12PARM04 | 99CE0000 | RD06 | Pack12Param4 |
| 642 | 0 | 16 | MCUPCKT12PARM05 | 99CF0000 | RD06 | Pack12Param5 |
| 644 | 0 | 16 | MCUPCKT12PARM06 | 99D00000 | RD06 | Pack12Param6 |
| 646 | 0 | 16 | MCUPCKT14PARM01 | 99D10000 | RD06 | Pack14Param1 |
| 648 | 0 | 16 | MCUPCKT14PARM02 | 99D20000 | RD06 | Pack14Param2 |
| 650 | 0 | 16 | MCUPCKT14PARM03 | 99D30000 | RD06 | Pack14Param3 |
| 652 | 0 | 16 | MCUPCKT14PARM04 | 99D40000 | RD06 | Pack14Param4 |
| 654 | 0 | 16 | MCUPCKT14PARM05 | 99D50000 | RD06 | Pack14Param5 |
| 656 | 0 | 16 | MCUPCKT14PARM06 | 99D60000 | RD06 | Pack14Param6 |
| 658 | 0 | 16 | MCUPCKT14PARM07 | 99D70000 | RD06 | Pack14Param7 |
| 660 | 0 | 16 | MCUPCKT14PARM08 | 99D80000 | RD06 | Pack14Param8 |
| 662 | 0 | 16 | MCUPCKT14PARM09 | 99D90000 | RD06 | Pack14Param9 |
| 664 | 0 | 16 | MCUPCKT14PARM10 | 99DA0000 | RD06 | Pack14Param10 |
| 666 | 0 | 16 | MCUPCKT14PARM11 | 99DB0000 | RD06 | Pack14Param11 |
| 668 | 0 | 16 | MCUPCKT14PARM12 | 99DC0000 | RD06 | Pack14Param12 |
| 670 | 0 | 16 | MCUPCKT14PARM13 | 99DD0000 | RD06 | Pack14Param13 |
| 672 | 0 | 16 | MCUPCKT14PARM14 | 99DE0000 | RD06 | Pack14Param14 |
| 674 | 0 | 16 |  |  |  |  |
| 676 | 0 0 1 2 3 4 | 16 1 1 1 1 2 | SCUIFSTAT SCUIFOLAPERR SCUIFBCASTERR SCUIFREADERR SCUIFTOUTERR SCUIFCMDSTAT | A8000000 | RD06 | CmdIfStat Command Overlapped Forbidden Broadcast Forbidden Read SubSystem Timeout LastCmdStatus |
| 678 | 0 0 1 2 | 16 1 1 1 | SCUIFCTRL SCUDATIFRESET SCUSSRESET SCUIFSTATRESET | A8010000 | RD06 | CmdIfCtrl DataIfReset SubSystemRst StatusRst |
| 680 | 0 | 16 | SCUSSDEL | A8020000 | RD06 | Subsystem Delay |
| 682 | 0 | 16 | SCUSTAT | A8800000 | RD06 | ScuStatus |
| 684 | 0 | 16 | SCUTEMPSTAT | A8850000 | RD06 | TempOnOff |
| 686 | 0 | 16 | SCUDCDCSTAT | A8870000 | RD06 | DRelOnOff |
| 688 | 0 | 16 | SCUP5V | A8D00000 | RD06 | ScuCHTp05 |
| 690 | 0 | 16 | SCUP9V | A8CF0000 | RD06 | ScuCHTp09 |
| 692 | 0 | 16 | SCUM9V | A8CE0000 | RD06 | ScuCHTn09 |
| 694 | 0 | 16 | SPHSV | A8C50000 | RD06 | SPHSHeatB |
| 696 | 0 | 16 | EVHSV | A8C40000 | RD06 | EVHSHeatB |
| 698 | 0 | 16 | TCHTRV | A8C60000 | RD06 | TCHeaterB |
| 700 | 0 | 16 | SPHTRV | A8C70000 | RD06 | SPHeaterB |
| 702 | 0 | 16 | CCUTEMP | A8C00000 | RD06 | CsuTempRd |
| 704 | 0 | 16 | TCUTEMP | A8C10000 | RD06 | TsuTempRd |
| 706 | 0 | 16 | PSUTEMP1 | A8C20000 | RD06 | PsuTmp1Rd |
| 708 | 0 0 15 | 16 8 1 | SCUFRAMECONF SCUFRAMERATE SCUFRAMETYPE | A8830000 | RD06 RD06 | FrameConf FrameRate |
| 710 | 0 | 16 | SCUFRAMES | A8840000 | RD06 | SeqLength |
| 712 | 0 | 16 | SCUFRAMESTAT | A8820000 | RD06 | FrameCtrl |
| 714 | 0 | 16 | SCUCTRL | A8810000 | RD06 | ScuContrl |
| 716 | 0 | 16 | PCALV | A8C90000 | RD06 | PhCalVolt |
| 718 | 0 | 16 | SCAL2V | A8CB0000 | RD06 | SCal2Volt |
| 720 | 0 | 16 | SCAL4V | A8CD0000 | RD06 | SCal4Volt |
| 722 | 0 | 16 | SCUCHT2.5V | A8D10000 | RD06 | ScuCHT25 |
| 724 | 0 | 16 | SCUCHTREF | A8D20000 | RD06 | ScuCHTRef |
| 726 | 0 | 16 | SCUCHTGND | A8D30000 | RD06 | ScuCHTGnd |
| 728 | 0 | 16 | PCALCURR | A8C80000 | RD06 | PhCalBias |
| 730 | 0 | 16 | SCAL2CURR | A8CA0000 | RD06 | SCal2Bias |
| 732 | 0 | 16 | SCAL4CURR | A8CC0000 | RD06 | Scal4Bias |
| 734 | 0 | 16 | PSUTEMP2 | A8C30000 | RD06 | PsuTmp2Rd |
| 736 | 0 | 16 | SUBKSTAT | A8860000 | RD06 | SubKpOnOff |
| 738 |  |  |  |  |  |  |
| 740 |  |  |  |  |  |  |
| 742 | 0 | 16 | PUMPHTRTEMP | A8E00000 | RD06 | CPHPtemp |
| 744 | 0 | 16 | PUMPHSTEMP | A8E10000 | RD06 | CPHStemp |
| 746 | 0 | 16 | EVAPHSTEMP | A8E20000 | RD06 | CEHStemp |
| 748 | 0 | 16 | SHUNTTEMP | A8E30000 | RD06 | CSHTtemp |
| 750 | 0 | 16 | SOBTEMP | A8E40000 | RD06 | SOBtemp |
| 752 | 0 | 16 | SL0TEMP | A8E50000 | RD06 | SL0temp |
| 754 | 0 | 16 | PL0TEMP | A8E60000 | RD06 | PL0temp |
| 756 | 0 | 16 | OPTTEMP | A8E70000 | RD06 | SUBtemp |
| 758 | 0 | 16 | BAFTEMP | A8E80000 | RD06 | BAFtemp |
| 760 | 0 | 16 | BSMIFTEMP | A8E90000 | RD06 | BSMtemp |
| 762 | 0 | 16 | SCAL2TEMP | A8EA0000 | RD06 | SCL2temp |
| 764 | 0 | 16 | SCAL4TEMP | A8EB0000 | RD06 | SCL4temp |
| 766 | 0 | 16 | SCALTEMP | A8EC0000 | RD06 | SCSTtemp |
| 768 | 0 | 16 | SMECIFTEMP | A8ED0000 | RD06 | FTSStemp |
| 770 | 0 | 16 | SMECTEMP | A8EE0000 | RD06 | FTSMtemp |
| 772 | 0 | 16 | BSMTEMP | A8EF0000 | RD06 | BSMMtemp |
| 774 | 0 | 16 | SUBKTEMP | A8F00000 | RD06 | CEVTemp |
| 776 | 0 | 16 | SCUTHTREF | A8F10000 | RD06 | ScuTHTRef |
| 778 | 0 | 16 | SCUTHTGND | A8F20000 | RD06 | ScuTHTGnd |
| 780 | 0 | 16 | LOSTTCBLOCK |  |  |  |
| 782 | 0 | 16 | LOSTEVBLOCK |  |  |  |
| 784 | 0 | 16 | LOSTHKBLOCK |  |  |  |
| 786 | 0 | 16 | LOSTSDBLOCK |  |  |  |
| 788 | 0 | 16 | LOSTNTBLOCK |  |  |  |

### Unused Service

Not Available

### Event Reporting

#### Event Report (5,1)

These reports provide information on events in the instrument which may impact on the scientific results, but which should have no impact on the health and safety of the instrument. These will include the reporting of anomalies which have been dealt with by the DPU

##### New Step Report

Indicates a new step in the current operation Mode. This event is issued every time the MODE or STEP Number is changed

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 29 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| EVENTID_NSR = 0x0501 |
| SID_NSR = 0x5100 |
| OBSID_NSR |
| BBID_NSR |
| EVENTCOUNT_NSR |
| MODE_NSR |
| STEP_NSR |
| Checksum |

##### Peak Up Report

This report is issued at the end of a peak up operation

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length =31 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| EVENTID_PUR = 0x0504 |
| SID_PUR = 0x5101 |
| OBSID_PUR |
| BBID_PUR |
| EVENTCOUNT_PUR |
| INSTRID_PUR |
| THETAY_PUR |
| THETAZ_PUR |
| Checksum |

##### Unallocated Block Report

The OBS failed to allocate a memory block from the VIRTUOSO Memory Pools

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 37 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| EVENTID_UBR = 0x0505 |
| SID_UBR = 0x5102 |
| OBSID_UBR |
| BBID_UBR |
| EVENTCOUNT_UBR |
| POOLID_UBR |
| SIZE_UBR |
| ALLOC_RESULT_UBR |
| TASKID_UBR |
| NPKT_UBR |
| MAXPKT_UBR |
| Checksum |

##### Unknown Command Report

In response to a command the DRCU indicated that the Command ID was not known

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 33 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| EVENTID_UCR = 0x0509 |
| SID_UCR = 0x5103 |
| OBSID_UCR |
| BBID_UCR |
| EVENTCOUNT_UCR |
| COMMAND_UCR |
| ACK_UCR |
| Checksum |

##### Forbidden Command Report

In response to a command the DRCU indicated that the Command ID was forbidden

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 33 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| EVENTID_FCR = 0x050A |
| SID_FCR = 0x5104 |
| OBSID_FCR |
| BBID_FCR |
| EVENTCOUNT_FCR |
| COMMAND_FCR |
| RESPONSE_FCR |
| Checksum |

##### Frame ID Error

When copying data frames from the FIFO to the internal science data buffer, the frame ID  is not correct.

(The DPU should also execute a procedure to resynchronise with the science data in the FIFO).

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 29 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| EVENTID_FIE = 0x0506 |
| SID_FIE = 0x5105 |
| OBSID_FIE |
| BBID_FIE |
| EVENTCOUNT_FIE |
| FRAMEID_FIE |
| FIFOID_FIE |
| Checksum |

##### Frame Length Error

When copying data frames from the FIFO to the internal science data buffer, the frame length is not correct (RD06).

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 31 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| EVENTID_FLE = 0x0507 |
| SID_FLE = 0x5106 |
| OBSID_FLE |
| BBID_FLE |
| EVENTCOUNT_FLE |
| FRAMEID_FLE |
| LENGTHRD_FLE |
| LENGTHEX_FLE |
| Checksum |

##### Frame Checksum Error

When copying data frames from the FIFO to the internal science data buffer, the Checksum word at the end of the frame is not correct.

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 31 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| EVENTID_FCE = 0x0508 |
| SID_FCE = 0x5107 |
| OBSID_FCE |
| BBID_FCE |
| EVENTCOUNT_FCE |
| FIFOID_FCE |
| CHKWORDEX_FCE |
| CHKWORDRD_FCE |
| Checksum |

##### Subsystem Timeout Error

This is issued when the DRCU responds with a timeout to a sent command.

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 33 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| EVENTID_STE = 0x050B |
| SID_STE = 0x5108 |
| OBSID_STE |
| BBID_STE |
| EVENTCOUNT_STE |
| COMMAND_STE |
| RESPONSE_STE |
| Checksum |

##### Subsystem Response Error

This is issued when there is an error in the transmission of a GET command to the DRCU, i.e. when the CID returned by the DRCU is not identical to the CID sent.

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 37 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| EVENTID_SRE = 0x050C |
| SID_SRE = 0x5109 |
| OBSID_SRE |
| BBID_SRE |
| EVENTCOUNT_SRE |
| COMMAND_SRE |
| RESPONSE_SRE |
| Checksum |

##### DPU Pool Error

This (a warning more than an error) is issued when the DPU internal memory pools (where the TM packets are stored before being sent to the 1553 I/F, it will be detailed in the ADD some time) reach a 80% occupation.

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 37 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| EVENTID_DPE = 0x050D |
| SID_DPE = 0x510A |
| OBSID_DPE |
| BBID_DPE |
| EVENTCOUNT_DPE |
| POOLID_DPE |
| NPKT_DPE |
| MAXPKT_DPE |
| TERROR_DPE |
| Checksum |

##### DPU FIFO Error

This (a warning more than an error) is issued when the DPU internal VIRTUOSO FIFOs (used to exchange messages between OBS tasks, it will be detailed in the ADD some time) reach a 80% occupation.

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 37 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| EVENTID_DFE = 0x050E |
| SID_DFE = 0x510B |
| OBSID_DFE |
| BBID_DFE |
| EVENTCOUNT_DFE |
| FIFOID_DFE |
| NMSG_DFE |
| MAXMSG_DFE |
| TERROR_DFE |
| Checksum |

##### LS Overflow Error

The number of commands send to the DRCU exceeds the maximum allowed rate.

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 29 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| EVENTID_LOE = 0x050F |
| SID_LOE = 0x510C |
| OBSID_LOE |
| BBID_LOE |
| EVENTCOUNT_LOE |
| LSLOAD_LOE |
| Checksum |

##### Unknown TM Packet Error

A TM packet ready to be sent has an unknown combination of Type/Subtype and SID

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 31 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| EVENTID_UTPE = 0x0510 |
| SID_UTPE = 0x510D |
| OBSID_UTPE |
| BBID_UTPE |
| EVENTCOUNT_UTPE |
|  | TYPE_UTPE |
| SUBTYPE_UTPE |  |
| SID_UTPE |
| Checksum |

##### No DCU Response Error

The DCU does not respond to a “SET” or “GET” command.

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 29 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| EVENTID_NDRE = 0x0520 |
| SID_NDRE = 0x510E |
| OBSID_NDRE |
| BBID_NDRE |
| EVENTCOUNT_NDRE |
| COMMAND_NDRE |
| Checksum |

##### No MCU Response Error

The MCU does not respond to a “SET” or “GET” command.

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 29 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| EVENTID_NMRE = 0x0521 |
| SID_NMRE = 0x510F |
| OBSID_NMRE |
| BBID_NMRE |
| EVENTCOUNT_NMRE |
| COMMAND_NMRE |
| Checksum |

##### No SCU Response Error

The SCU does not respond to a “SET” or “GET” command.

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 29 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| EVENTID_NSRE = 0x0522 |
| SID_NSRE = 0x5110 |
| OBSID_NSRE |
| BBID_NSRE |
| EVENTCOUNT_NSRE |
| COMMAND_NSRE |
| Checksum |

##### TC Sequence Error

This event is issued when there is a gap in the TC sequence number.

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 29 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| EVENTID_TSE = 0x0511 |
| SID_TSE = 0x5111 |
| OBSID_TSE |
| BBID_TSE |
| EVENTCOUNT_TSE |
| LAST_TC_COUNT_TSE |
| CURR_TC_COUNT_TSE |
| Checksum |

##### Out_of_Limit_Error

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length=25 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| EVENTID_OOL |
| SID_OOL = 0x5112 |
| OBSID_OOL |
| BBID_OOL |
| EVENTCOUNT_OOL |
| PARMID_OOL |
| PARMVALUE_OOL |
| Checksum |

| Error | EVENTID_OOL | Event ID – see table below |
| --- | --- | --- |
| POWER_FAILURE | 0x5100 | A monitored power rail in the DRCU is out of limits PARMID has the following values: SCUP5V = SCUP9V = SCUM9V = SCUP25V = MCUP5V = MCUP15V = MCUM15V = MCUP13V = MCUM13V = BIAS5V = BIASP9V = BIASM9V = PLIAP5V = PLIAP9V = PLIAM9V = SLIAP5V = SLIAP9V = SLIAM9V = DPU parms TBD |
| BTEMP_FAILURE | 0x5110 | TBW |
| THERM_FAILURE | 0x5120 | TBW |
| HEATER_FAILURE | 0x5130 | TBW |
| MCU_FATAL_ERROR | 0x5140 | TBW |
| CONFIG_ERROR | 0x5150 | TBW |

#### Exception Report (5,2)

These reports normally indicate an anomaly with the instrument that cannot be dealt with by the DPU and that action should be taken by the spacecraft.

##### Anomaly without parameters

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length=25 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| EVENTID_AWP |
| SID_AWP = 0x5200 |
| OBSID_AWP |
| BBID_AWP |
| EVENTCOUNT_AWP |
| Checksum |

| Error | EVENTID_AWP | Event ID – see table below |
| --- | --- | --- |
| DRCU_Anomaly | 0xC000 | OBS has detected an unrecoverable anomaly in the DRCU. The expected action is for the CDMS to switch off the DRCU. |
| DPU_Anomaly | 0xC010 | OBS has detected an unrecoverable anomaly in the DPU. The expected action is for the CDMS to switch off the DPU and DRCU. |
| Observation_Anomaly | 0xC100 | OBS has detected a problem during an observation. The expected action is for the CDMS to suspend SPIRE commanding until the instrument is ready to resume. |
| Observation_Corrected | 0xC110 | The OBS has corrected and observation anomaly - Resume SPIRE Commanding with the next subschedule. |
| Function_Unarmed | 0x0832 | Attempt to engage or disengage the SMEC Launch Latch when the function is not active. Action by the CDMS is TBD |

##### Boot ROM Memory Check

This packet is generated by the Boot ROM after checking the memory contents provided no errors are found.

Note: This packet does not conform to the format defined for Event Packets in AD01 and is TBC

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length=17 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME (0x800000000000) |
| SID? |
| SUBSID? |
| NERRORS? |
| Checksum |

#### Error/Alarm Report (5,4)

##### Memory Check Errors

Generated when the Boot Software memory check fails (ref RD10).

Note: This packet does not conform to the format defined for Event Packets in AD01

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME (0x800000000000) |
| EVENTID_MCE |
| SID_MCE=0x00FF |
| MEMID_MCE | NPAGES_MCE |
| Page IDs |
| Checksum |

| Error | EVENTID_MCE | MEMID_MCE | Event ID – see table below |
| --- | --- | --- | --- |
| PM_Error | 0x8001 | 1 | The Boot SW has detector one or more errors in the Program Memory |
| DM_Error | 0x8002 | 2 | The Boot SW has detector one or more errors in the Data Memory. |
| EEPROM_Error | 0x8003 | 3 | The Boot SW has detector one or more errors in the EEPROM |

##### Telecommand Validation Errors

Generated when the Boot Software telecommand check fails (ref RD10).

Note: This packet does not conform to the format defined for Event Packets in AD01

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 27 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME (0x800000000000) |
| EVENTID_TVE |
| SID_ TVE |
| INFO_ TVE |
| ERRCODE_ TVE |
| FCSCOMP_ TVE |
| FCSREAD_ TVE |
| CHKSUMID_ TVE |
| DMADDR_ TVE |
| Checksum |

| Error | ERRCODE _TVE | INFO _TVE | FSCCOMP _TVE | FCSREAD _TVE | CHKSUMID _TVE | DMADDR _TVE |
| --- | --- | --- | --- | --- | --- | --- |
| Data_Memory _FCS_Error | 0x0008 | Options loading memory | Computed Value | Value Read | 0x0001 | Start Address of Overlapped Memory Page |
| TC_FCS_Error | 0x0008 | 0xAAAA | Computed Value | Value Read | 0x0002 | 0xAAAA |
| TC_APID_Error | 0x000C | APID Received | 0xAAAA | 0xAAAA | 0xAAAA | 0xAAAA |
| TC_Wrong _Function_ID _Error | 0x0010 | Function ID Received | 0xAAAA | 0xAAAA | 0xAAAA | 0xAAAA |
| Data_Memory _Wrong_Function_Error | 0x0010 | TC options for loading memory | 0xAAAA | 0xAAAA | 0xAAAA | 0xAAAA |
| Packet_Type_Error | 0x000E | Type & Subtype Received | 0xAAAA | 0xAAAA | 0xAAAA | 0xAAAA |
| Packet_Subtype_Error | 0x000B | Type & Subtype Received | 0xAAAA | 0xAAAA | 0xAAAA | 0xAAAA |
| Data_Memory _Page_Overlap_Error | 0x000A | 0xAAAA | 0xAAAA | 0xAAAA | 0xAAAA | Start Address of Overlapped Memory Page |
| Data_Memory _Page_Lost_Error | 0x0009 | TC options for loading memory | 0xAAAA | 0xAAAA | 0xAAAA | Start Address of Overlapped Memory Page |
| Data_Memory _Wrong_Format_Error | 0x0007 | TC options for loading memory | 0xAAAA | 0xAAAA | 0xAAAA | Start Address of Overlapped Memory Page |
| Data_Memory _Uploading_Boundaries _Error | 0x0012 | 0xAAAA | 0xAAAA | 0xAAAA | 0xAAAA | 0xAAAA |
| Data_Memory _Wrong_Activity_Error | 0x0011 | TC options for loading memory | 0xAAAA | 0xAAAA | 0xAAAA | 0xAAAA |

##### EEPROM to PM Loading Errors

Generated when the Boot Software data transfer from EEPROM or Data Memory  to PM fails (ref RD10).

Note: This packet does not conform to the format defined for Event Packets in AD01

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 19 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME (0x800000000000) |
| EVENTID_EPMLE |
| SID_EPMLE |
| MEMTYPE | NPAGES |
| ERRCODE_EPMLE |
| Checksum |

##### DM to PM Loading Errors

Generated when the Boot Software data transfer from EEPROM or Data Memory  to PM fails (ref RD10).

Note: This packet does not conform to the format defined for Event Packets in AD01

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 19 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME (0x800000000000) |
| EVENTID_DPMLE |
| SID_DPMLE |
| MEMTYPE | NPAGES |
| ERRCODE_DPMLE |
| Checksum |

##### PM Boot Errors

Generated when the Boot Software DM-to-PM Immediate Boot fails (ref RD10).

Note: This packet does not conform to the format defined for Event Packets in AD01

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 19 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME (0x800000000000) |
| EVENTID_PMBE |
| SID_PMBE |
| MEMTYPE | NPAGES |
| ERRCODE_PMBE |
| Checksum |

### Memory Management

#### Memory Dump, Absolute Addresses

This report is issued in response to TC (6,5). Multiple packets may be generated in order to dump the requested address range.

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| MEMORYID |  |
| STARTADDR |
| NSAU |
| Data |
| CHK |
| Checksum |

#### Memory Check Report, Absolute Addresses

This report is issued in response to TC (6,9). Multiple packets may be generated in order to dump the requested address range.

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length =19 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 |
| 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| MEMORYID |  |
| STARTADDR |
| NSAU |
| CHK |
| Checksum |

Not Available

### Function Management

This report is issued in response to TC (8,5).  Three report formats are defined

#### Normal Functions Report

These correspond to Function IDs 0x01, 0x10, 0x70, 0xC0 and 0xC1

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length =15 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| FUNCTIONID | ACTIVITYID |
| SID |
| Checksum |

#### VM Functions Report

These correspond to Function IDs 0x02, 0x03, 0x04 and 0x05

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| FUNCTIONID | ACTIVITYID |
| SID |
| TABLEID |
| INDEX |
| N |
| Data |
| Checksum |

#### DPU Functions Report

These correspond to Function ID  0xCA

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length =19 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| FUNCTIONID | ACTIVITYID |
| SID |
| N |
| FRAMEID |
| SELSID |
| TABLEID |
| ………. |
| Checksum |

### Time Management

#### Time Verification Report

This report is generated in response to TC(9,7)

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 17 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 |
| 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| TDPU |
| Checksum |

Not Available

### On Board Scheduling

Not Used

### On Board Monitoring

Not Used

Not Available

### Packet Transmission Control

This report is issued in response to TC (14,3) and lists all the enabled TM packets.

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| NDEF |
| Type | Subtype |
| Packet ID |
| Type | Subtype |
| Packet ID |
| Checksum |

### On Board Storage and Retrieval

Not Used

### On Board Traffic Management

Not Used

### Test Service

This report is generated in response to TC (17,1)

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 17 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| Checksum |

### On Board Control Procedures

Not Used

### Action/Event Service

Not Used

### Information Distribution Service

Not Used

### Science Data

#### Nominal Science Data Report (21,1)

| 0 | 0 | 0 | 0 | 1 | APID |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| SID |
| OBSID |
| BBID |
| Parameters |
| Checksum |

The parameters field contains one or more blocks of science data all of the same type.  These blocks are the same as the science data frames issued by the DRCU, except for the DPU Block, which is crated by the DPU.

Normally the DPU fills the TM packet with the maximum number of blocks before the packet is made available for transmission. In the event of a flush_fifo telecommand the packet is transmitted immediately and will not be filled. The length field, with the APID and SID, allows the number of blocks in the packet to be calculated.

The possible block types are as follows:

##### Photometer Full Array Block

This block of data is inserted in the Parameter field once.

Block Length=294

FrameID=0x00

288 Detector Values

ADC_Flags

Frame_Time MSW

Frame_Time LSW

Checkword

The order of the detectors in the block is shown in Appendix D

##### Spectrometer Full Array Block

Block Length=78

FrameID=0x01

72 Detector Values

ADC_Flags

Frame_Time MSW

Frame_Time LSW

Checkword

The order of the detectors in the block is shown in Appendix D

##### SMEC Block

In order to meet the telemetry bit rate requirements, this block is normally selected (see TM(21,2)).

This is the default block contents – it may be changed by command to the MCU.

Block Length=12

FrameID=0x10

Acquisition date MSW

Acquisition date LSW

SMECENCPOSN

SMECENCFINEPOSN

SMECLVDTPOSN

CMDMOTORCURR

SMECMOTORBEMF

Transmission Time MSW

Transmission Time LSW

Checkword

##### BSM Block

This is the default block contents – it may be changed by command to the MCU.

Block Length=13

FrameID=0x12

Acquisition date MSW

Acquisition date LSW

CHOPSENSSIG

CHOPMOTORCURR

CHOPBEMF

JIGGSENSSIG

JIGGMOTORCURR

JIGGBEMF

Transmission_Time MSW

Transmission_Time LSW

Checkword

##### SCU Block

Block Length=30

FrameID=0x20

PUMPHTRTEMP

PUMPHSTEMP

EVAPHSTEMP

SHUNTTEMP

SOBTEMP

SL0TEMP

PL0TEMP

OPTTEMP

BAFTEMP

BSMIFTEMP

SCAL2TEMP

SCAL4TEMP

SCALTEMP

SMECIFTEMP

SMECTEMP

BSMTEMP

SUBKTEMP

TCHTRV

PCALCURR

PCALV

SCAL2CURR

SCAL2V

SCAL4CURR

SCAL4V

ADC _Flags

Frame_Time MSW

Frame_Time LSW

Checkword

###### SID = 0x1410:  SMEC Selected Data

Acquisition Time MSW

Aquisition Time LSW

SMECENCPOSN

SMECENCFINEPOSN

SMECLVDTPOSN

SMECMOTORBEMF

###### SID = 0x1200: Photometer Parallel Mode Selected Data

TBD

##### SID = 0x1201: Spectrometer Parallel Mode Selected Data

TBD

#### Science Type B Data Report (21,2)

| 0 | 0 | 0 | 0 | 1 | APID |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| SID |
| OBSID |
| BBID |
| Parameters |
| Checksum |

The parameters field contains one or more blocks of science data all of the same type.

These blocks are the same as the science data frames issued by the DRCU, except in the case of the Selected Data Report.

Normally the DPU fills the TM packet with the maximum number of blocks before the packet is made available for transmission. In the event of a flush_fifo telecommand the packet is transmitted immediately and will not be filled. The length field, with the APID and SID, allows the number of blocks in the packet to be calculated.

The possible block types are as follows:

##### PSW Array Block

Block Length=150

FrameID=0x02

144 Detector Values

ADC_Flags

Frame_Time MSW

Frame_Time LSW

Checkword

The order of the detectors in the block is shown in Appendix D

##### PMW Array Block

Block Length=102

FrameID=0x03

96 Detector Values

ADC_Flags

Frame_Time MSW

Frame_Time LSW

Checkword

The order of the detectors in the block is shown in Appendix D

##### PLW Array Block

Block Length=54

FrameID=0x04

48 Detector Values

ADC_Flags

Frame_Time MSW

Frame_Time LSW

Checkword

The order of the detectors in the block is shown in Appendix D

##### SSW Array Block

Block Length=54

FrameID=0x05

48 Detector Values

ADC_Flags

Frame_Time MSW

Frame_Time LSW

Checkword

The order of the detectors in the block is shown in Appendix D

##### SLW Array Block

Block Length=30

FrameID=0x06

24 Detector Values

ADC_Flags

Frame_Time MSW

Frame_Time LSW

Checkword

The order of the detectors in the block is shown in Appendix D

#### Diagnostic Science Report (21,3)

| 0 | 0 | 0 | 0 | 1 | APID |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| SID |
| OBSID |
| BBID |
| Parameters |
| Checksum |

The parameters field contains one or more blocks of science data all of the same type.  These blocks are the same as the science data frames issued by the DRCU, with theexception of the Transparent Data

Normally the DPU fills the TM packet with the maximum number of blocks before the packet is made available for transmission. In the event of a flush_fifo telecommand the packet is transmitted immediately and will not be filled. The length field, with the APID and SID, allows the number of blocks in the packet to be calculated.

The possible block types are as follows:

##### Photometer Full Test Pattern Block

This block of data is inserted in the Parameter field once.

Block Length=294

FrameID=0x09

288 Test Values

ADC_Flags

Frame_Time MSW

Frame_Time LSW

Checkword

The content of the Test Values is TBD

##### Photometer SW Test Pattern Block

Block Length=150

FrameID=0x0A

144 Test Values

ADC_Flags

Frame_Time MSW

Frame_Time LSW

Checkword

The content of the Test Values is TBD

##### Photometer MW Test Pattern Block

Block Length=102

FrameID=0x0B

96 Test Values

ADC_Flags

Frame_Time MSW

Frame_Time LSW

Checkword

The content of the Test Values is TBD

##### Photometer SW Test Pattern Block

Block Length=54

FrameID=0x0C

48 Test Values

ADC_Flags

Frame_Time MSW

Frame_Time LSW

Checkword

The content of the Test Values is TBD

##### Spectrometer Full Test Pattern Block

Block Length=78

FrameID=0x0D

72 Test Values

ADC_Flags

Frame_Time MSW

Frame_Time LSW

Checkword

The content of the Test Values is TBD

##### Spectrometer SW Test Pattern Block

Block Length=54

FrameID=0x0E

48 Test Values

ADC_Flags

Frame_Time MSW

Frame_Time LSW

Checkword

The content of the Test Values is TBD

##### Spectrometer LW Test Pattern Block

Block Length=30

FrameID=0x0F

24 Test Values

ADC_Flags

Frame_Time MSW

Frame_Time LSW

Checkword

The content of the Test Values is TBD

##### MCU Engineering Block

This block is available to transmit any MCU parameters to the ground as science telemetry. The default parameters are given in the table below. Any parameter may be replaced by command to the MCU.

Block Length=21

FrameID=0x14

Acquisition date MSW

Acquisition date LSW

SMECENCCOUNT

SMECENCSIG1

SMECENCSIG2

SMECENCSIG3

SMECLVDTDCSIG

SMECLVDTACSIG

SMECMOTORCURR

SMECMOTORVOLT

CHOPSENSSIG

CHOPMOTORCURR

CHOPMOTORVOLT

JIGGSENSSIG

JIGGMOTORCURR

JIGGMOTORVOLT

Transmission_Time MSW

Transmission_Time LSW

Checkword

##### MCU Test Pattern Block

Block Length=21

FrameID=0x15

Acquisition date MSW

Acquisition date LSW

0x5555 0xAAAA0x5554 0xAAA8 0x5550 0xAAA0 0x5541 0xAAA2 0x5505 0xAA0A 0x5414 0xA828 0x5050 0xA0A0

Transmission_Time MSW

Transmission_Time LSW

Checkword

##### SCU Test Pattern Block

Block Length=30

FrameID=0x21

Test Data (24 words)

ADC_Flags

Frame_Time MSW

Frame_Time LSW

Checkword

The content of the Test Data is TBD

##### Transparent Data Block

##### This block is used to transmit science data read directly from a FIFO without any processing of data frames.

##### It is used if an error is found in the structure of the data held in a FIFO, to dump the contents of the FIFO for diagnostic purposes.

##### Note: As the FIFO contents could be larger than could be accommodated in one TM packet. The data is sent as a group of packets using the segmentation flags (AD01 – para 4.1.1.2.1) to identify the first, intermediate and last packets.

FIFOID

INDEX

NDATA

FIFO Data

#### Auxiliary Science Data Report (21,4)

| 0 | 0 | 0 | 0 | 1 | APID |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| SID |
| OBSID |
| BBID |
| Parameters |
| Checksum |

The parameters field contains one or more blocks of science data all of the same type.

Normally the DPU fills the TM packet with the maximum number of blocks before the packet is made available for transmission. In the event of a flush_fifo telecommand the packet is transmitted immediately and will not be filled. The length field, with the APID and SID, allows the number of blocks in the packet to be calculated.

The possible block types are as follows:

##### Photometer Offsets Block

This block of data is inserted in the Parameter field once.

Block Length=294

FrameID=0x07

288 Offsets

ADC_Flags

Frame_Time MSW

Frame_Time LSW

Checkword

The order of the detector offsets in the block is shown in Appendix D

##### Spectrometer Offsets Block

Block Length=78

FrameID=0x08

72 Offsets

ADC_Flags

Frame_Time MSW

Frame_Time LSW

Checkword

The order of the detector offsets in the block is shown in Appendix D

##### Housekeeping Packet Definition

The reported parameters are those sent in the Housekeeping Packet definition command

HKPCKTID

HKSID

HKINTERVAL

HKREPEAT

TABLEID

MONITOR_TABLEID

##### Report Table Report

The parameters field contains the requested table contents.

##### Note: As the Table contents could be larger than could be accommodated in one TM packet. The data is sent as a group of packets using the segmentation flags (AD01 – para 4.1.1.2.1) to identify the first, intermediate and last packets.

TABLEID

INDEX

NDATA

Table Data

##### Context Saving Service

Not Used

# Parameters

## TC Parameters

### Parameter Definition

| Parameter Name | Service Reference | Type | Size (bits) | Conversion Curve | Constraint Table | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| Activity_ID | (8,4) | Integer | 8 | None | None |  |
| APID | (20,1) (20,2) | Integer | 11 | None | None | Application ID |
| BBID BBINTR BBTYPE BBCOUNT | (8,4) | Constant Integer Integer | 32 2 14 16 | None None None | None None None | Field is split into 3 parts: Location: Bits 0-1 Value: 2 Location: Bits 2-15 Location: Bits 16-31 |
| COUNT | (8,4) | Integer | 16 | None | None | Number of words to be reported |
| CRC | (6,2) | Unsigned Integer | 16 | None | None | Cyclic Redundancy Check - algorithm is defined in AD01 – Appendix 4 |
| Data | (6,2) (8,4) |  |  |  |  | Variable length field of any data type. Must be an integer number of 16 bits in length |
| FIFOFLAGS FIFODPU FIFODCU FIFOSCU FIFOMCU | (8,4) | Integer Integer Integer Integer | 16 1 1 1 1 | Flush Flush Flush Flush | None None None None | Flags indicating the FIFO(s) to flush Location: bit 15: DPU science buffer Location: bit 14: DCU FIFO Location: bit 13: SCU FIFO Location: bit 12: MCU FIFO |
| FRAMEID | (8,4) | Integer | 16 | None | Frame |  |
| FUNCTIONID | (8,1) (8,2) (8,4) (8,5) | Integer | 8 | Func_ID | None |  |
| HKPCKTID | (3,1) (3,3) (3,9) | Integer | 16 | None | Hsk_ID | Identifies housekeeping packet definitions |
| HKSID | (3,1) | Unsigned Integer | 16 | None | None | Unique identifier for housekeeping parameter list Value = 0x03nn where nn = a unique number (starting from 0) defining the report structure |
| HKINTERVAL | (3,1) | Unsigned Integer | 16 | None | Period | Time between each packet generated, in milliseconds |
| INDEX | (8,4) | Unsigned Integer | 16 | None | None | Offset into a table( in octets) |
| Length | (6,2) (6,5) (6,9) | Unsigned Integer | 16 | None | None |  |
| MEMORYID | (6,2) (6,5) (6,9) | Integer | 16 | Mem_ID | None | ID of Memory Area to be addressed |
| MODE | (8,4) | Unsigned Integer | 16 | None | None | Observing Mode |
| N | (8,4) | Unsigned Integer | 16 | None | N32 |  |
| NCHOP | (8,4) | Integer | 16 | None | TBD | Number of Chop science data frames to combine into one Chop Science TM Packet |
| NDATA | (8,4) | Unsigned Integer | 16 | None | N32 |  |
| NDCU | (8,4) | Integer | 16 | None | TBD | Number of DCU science data frames to combine into one Chop Science TM Packet |
| NDPU | (8,4) | Integer | 16 | None | TBD | Number of DPU science data frames to combine into one Chop Science TM Packet |
| NJIGGLE | (8,4) | Integer | 16 | None | TBD | Number of Jiggle science data frames to combine into one Chop Science TM Packet |
| NPCKTS | (14,1) (14,2) | Integer | 16 | None | None | Number of packet types to follow |
| NSAU | (6,2) (6,5) (6,9) | Integer | 16 | None | None | Number of SAUs to transfer |
| NSCU | (8,4) | Integer | 16 | None | TBD | Number of SCU science data frames to combine into one Chop Science TM Packet |
| NSMEC | (8,4) | Integer | 16 | None | TBD | Number of SMEC science data frames to combine into one Chop Science TM Packet |
| OBSID | (8,4) | Unsigned Integer | 32 | None | None | Observation ID |
| Parameters | (8,4) |  |  |  |  | Variable length field of 32 data words. |
| SID | (8,1) (8,4) (14,1) (14,2) (20,1) (20,2) | Unsigned Integer | 16 | None | None | Unique identifier for parameter list |
| STARTADDR | (6,2) (6,5) (6,9) | Unsigned Integer | 16 | None | None | Start address of memory area to be addressed |
| STEP | (8,4) | Unsigned Integer | 16 | None | None | Observation Step |
| SUBTYPE | (14,1) (14,2) | Integer | 8 | None | None | Packet Subtype |
| TABLEID | (8,4) | Integer | 16 | None | Tab_ID | Number of an OBS table |
| TABLESIZE | (8,4) | Integer | 16 | None | TBD | Table size in 32 bit words |
| TYPE | (14,1) (14,2) | Integer | 8 | None | None | Packet Type |

### Conversion Curves

| Name | Type | Raw Value | Converted Value | Comments |
| --- | --- | --- | --- | --- |
| Data_Type | Enumerated | 0 1 2 3 | 8Bits 16Bits 24Bits 32Bits |  |
| Func_ID | Enumerated | 0x01 0x02 0x03 0x04 0xC0 0xC1 0xCA | Table Cooler SCAL 300mK Ops Obs DPU | TableManagement CoolerControl SCALControl 300mKControl Operations Observations DPU |
| Info_Type | Enumerated | 0 1 2 3 | Off Target On Target Start Scan End Scan |  |
| Mem_ID | Enumerated | TBD TBD TBD | PROG DATA EEPROM |  |
| Flush | Enumerated | 0 1 | Do not flush FIFO Flush FIFO |  |

### Constraints

| Name | Type | Minimum Value | Maximum Value | Comments |
| --- | --- | --- | --- | --- |
| Bit2 | Range | 0 | 3 | Value held in lowest 2 bits of field |
| Frame | Set |  |  | Set of possible frame IDs, TBD |
| Hsk_ID | Range | 0 | 3 | Allows up to 4 housekeeping packets to be defined |
| Hsk_Value | Range | 0x00000000 | 0x000FFFFF | The value is held in lowest 20 bits of the field |
| N16 | Range | 1 | 112 | Number of 16 bit data words held in a command |
| N32 | Range | 1 | 56 | Number of 32 bit data words held in a command |
| Nsamples | Range | 1 | 32 |  |
| Period | Range | 10 | 60000 | Time period expressed as milliseconds - range is 0.01 to 60 seconds |
| Tab_ID | Range | 0 | 127 |  |

## TM  Parameters

### Parameter Definition

| Name | DRCU Name | Length (bits) | Conversion | Limits | Description |
| --- | --- | --- | --- | --- | --- |
| BBID BBINSTR BBTYPE BBCNT |  | 32 2 14 16 |  |  | Building Block ID Instrument (Bits 0,1) BB type (Bits 2-15) BB sequence count (Bits 16-31) |
| BIASTEMP | BIAS_TEMP | 8 | TBD |  | BIAS Board Temperature |
| CCUTEMP | CcuTempRd | TBD | TBD | TBD | Temperature from sensor on CCHK Board |
| CHOPACCELLIMIT | CAccelLimi | 16, TBC |  |  |  |
| CHOPACCELLOOPSF | CAccelLoopsf | 16, TBC |  |  |  |
| CHOPBEMF | CBEMF | 16, TBC | TBD |  |  |
| CHOPINTTHRESH | IntegTh | 16 |  |  | Integration threshold for the Chop PID Controller |
| CHOPKD | CKd | 16 |  |  | Derivative Gain of Chop Axis PID Controller |
| CHOPKI | CKi | 16 |  |  | Integral Gain of Chop Axis PID Controller |
| CHOPKP | CKp | 16 |  |  | Proportional Gain of Chop Axis PID Controller |
| CHOPLATCHSTAT | BSMLaunchLatch1 | 1 | LATCH |  | Chopper Axis Launch Latch Status |
| CHOPLOOPMODE | ChopLoopMode | 2 | CLOOPMODE |  | Chopper Axis Loop Mode |
| CHOPMODE | ChopMode | 2 | CHOPMODE |  | Chopping Mode |
| CHOPMOTORCURR | CMotorCurrent | 16, TBC | TBD |  |  |
| CHOPMOTORTORQUE | CMotorTorqueC | 16, TBC | TBD |  |  |
| CHOPPERIOD | ChopPeriod | 16 | PERIOD |  | Chop Cycle Period |
| CHOPICNCOEFF1 | ICnCoeff1 | 16, TBC | TBD |  |  |
| CHOPICNCOEFF2 | ICnCoeff2 | 16, TBC | TBD |  |  |
| CHOPICNCOEFF3 | ICnCoeff3 | 16, TBC | TBD |  |  |
| CHOPICNCOEFF4 | ICnCoeff4 | 16, TBC | TBD |  |  |
| CHOPOUTCOEFF1 | CoutCoeff1 | 16, TBC | TBD |  |  |
| CHOPOUTCOEFF2 | CoutCoeff2 | 16, TBC | TBD |  |  |
| CHOPOUTCOEFF3 | CoutCoeff3 | 16, TBC | TBD |  |  |
| CHOPOUTCOEFF4 | CoutCoeff4 | 16, TBC | TBD |  |  |
| CHOPPOSN | ActualPosition | 16 |  |  | Last Absolute position of the Chopper |
| CHOPPOSNERR | CMeanPositionError | 16 |  |  | Mean Position Error over a Chopper movement |
| CHOPPOSNERRLIMIT | CPositionErrorLimit | 16 |  |  | Minimum Value of Chop Position Error that causes a PID error to be reported |
| CHOPPOSN0 | Position0 | 16 |  |  | Chopper Axis Position 0 |
| CHOPPOSN1 | Position1 | 16 |  |  | Chopper Axis Position 1 |
| CHOPRATELIMIT | CRateLimit | 16, TBC |  |  |  |
| CHOPRATELOOPSF | CRateLoopsf | 16, TBC |  |  |  |
| CHOPPROFILEVAL01 | CprofileValue1 | 16, TBC | TBD |  |  |
| CHOPPROFILEVAL02 | CprofileValue2 | 16, TBC | TBD |  |  |
| CHOPPROFILEVAL03 | CprofileValue3 | 16, TBC | TBD |  |  |
| CHOPPROFILEVAL04 | CprofileValue4 | 16, TBC | TBD |  |  |
| CHOPPROFILEVAL05 | CprofileValue5 | 16, TBC | TBD |  |  |
| CHOPPROFILEVAL06 | CprofileValue6 | 16, TBC | TBD |  |  |
| CHOPPROFILEVAL07 | CprofileValue7 | 16, TBC | TBD |  |  |
| CHOPPROFILEVAL08 | CprofileValue8 | 16, TBC | TBD |  |  |
| CHOPPROFILEVAL09 | CprofileValue9 | 16, TBC | TBD |  |  |
| CHOPPROFILEVAL10 | CprofileValue10 | 16, TBC | TBD |  |  |
| CHOPPROFILEVAL11 | CprofileValue11 | 16, TBC | TBD |  |  |
| CHOPPROFILEVAL12 | CprofileValue12 | 16, TBC | TBD |  |  |
| CHOPPROFILEVAL13 | CprofileValue13 | 16, TBC | TBD |  |  |
| CHOPPROFILEVAL14 | CprofileValue14 | 16, TBC | TBD |  |  |
| CHOPPROFILEVAL15 | CprofileValue15 | 16, TBC | TBD |  |  |
| CHOPS | ChopNumber | 16 |  |  | Number of Chop Cycles to perform |
| CHOPSENSPOSN1 | CMagnetoResPos1 | 16, TBC | TBD |  |  |
| CHOPSENSPOSN2 | CMagnetoResPos2 | 16, TBC | TBD |  |  |
| CHOPSENSPWR | SensorPwr | 1 | CHOPSENS |  | Chopper axis sensor power status |
| CHOPSTAT | ChopStatus | 16, TBC | TBD |  | Contents of Chop Axis Activity Status Register |
| CHOPSTATECOEFF1 | CStateCoeff1 | 16, TBC | TBD |  |  |
| CHOPSTATECOEFF2 | CStateCoeff2 | 16, TBC | TBD |  |  |
| CHOPSTATECOEFF3 | CStateCoeff3 | 16, TBC | TBD |  |  |
| CHOPSTATECOEFF4 | CStateCoeff4 | 16, TBC | TBD |  |  |
| DAQBIAS5V | DcuDAQp05 | TBD | TBD | TBD | Voltage to DAQ Board on +5V line |
| DAQ9V | DcuDAQp09 | TBD | TBD | TBD | Voltage to DAQ Board on +9V line |
| DAQ9VN | DcuDAQn09 | TBD | TBD | TBD | Voltage to DAQ Board on -9V line |
| DAQTEMP | DAQ_I/F_TEMP | 8 | TBD |  | DAQ I/F Board Temperature |
| DCUDATAFRMS | frame | 8 | DCUFRMS |  | Number of DCU data frames to generate |
| DCUDATAMODE | mode | 5 | DCUMODE |  | DCU data collection mode |
| DCUDATASTAT | start | 1 | DCUSTAT |  | Status of DCU data frame generation |
| DCUFLAGS |  | 16 |  |  | DCU Status -TBC |
| DCUTEMP | DcuTempRd | TBD | TBD | TBD | Temperature from sensor on Distribution Board |
| DPU5V |  | 12 | TBD |  | DPU +5V line voltage |
| DPU15V |  | 12 | TBD |  | DPU +15V line voltage |
| DPU15VN |  | 12 | TBD |  | DPU -15V line voltage |
| DPUI |  | 12 | TBD |  | DPU measured input current |
| DPU_Spare1 |  | 12 | TBD |  |  |
| DPU_Spare2 |  | 12 | TBD |  |  |
| DPU_Spare3 |  | 12 | TBD |  |  |
| DPUTEMP |  | 12 | TBD |  | DPU DC-DC Converter Temperature |
| JIGGKDHIGH | KdHigh | 16, TBC |  |  | Maximum Derivative Gain of Chop Axis PID Controller? |
| JIGGKDLOW | KdLow | 16, TBC |  |  | Minimum Derivative Gain of Chop Axis PID Controller? |
| JIGGFILTHIGH | DerivFilterHigh | 16, TBC |  |  | Filtering Time Constant to calculate the derivative term of the Chop PID Controller |
| JIGGFILTLOW | DerivFilterLow | 16, TBC |  |  | Filtering Time Constant to calculate the derivative term of the Chop PID Controller |
| JIGGKIHIGH | KiHigh | 16, TBC |  |  | Maximum Integral Gain of Chop Axis PID Controller? |
| JIGGKILOW | KiLow | 16, TBC |  |  | Minimum Integral Gain of Chop Axis PID Controller? |
| JIGGKPHIGH | KpHigh | 16, TBC |  |  | Maximum Proportional Gain of Chop Axis PID Controller? |
| JIGGKPLOW | KpLow | 16, TBC |  |  | Minimum Proportional Gain of Chop Axis PID Controller? |
| JIGGLATSTAT | JiggleLaunchLatch | 1 | LATCH |  | Jiggle Axis Launch Latch Status |
| JIGGLOOPMODE | JiggleLoopMode | 2 | JLOOPMODE |  | Jiggle Axis Loop Mode |
| JIGGMEANPERR | MeanPositionError | 16, TBC |  |  | Mean Position Error over a Jiggle movement? |
| JIGGMODE | JiggleMode | 2 | JIGGMODE |  | Jiggling Mode |
| JIGGPERIOD | JigglePeriod | 16, TBC | PERIOD |  | Jiggle Cycle Period – TBD if applicable |
| JIGGPERRLIM | PositionErrorLimit | 16, TBC |  |  | Minimum Value of Chop Position Error that causes a PID error to be reported? |
| JIGGPOSN | ActualPosition | 16, TBC |  |  | Last Absolute position of the Jiggle Axis |
| JIGGPOSN0 | Position0 | 16, TBC |  |  | Jiggle Axis Position 0 |
| JIGGPOSN1 | Position1 | 16, TBC |  |  | Jiggle Axis Position 1 – TBD if applicable |
| JIGGLES | JiggleNumber | 16, TBC |  |  | Number of Jiggle Cycles to perform – TBD if applicable |
| JIGGSATNLIM | IntegrationLimit | 16, TBC |  |  | Integration Saturation Limit for the Chop PID Controller? |
| JIGGSENSPWR | SensorPwr | 1 | JIGGSENS |  | Jiggle Axis sensor power status |
| JIGGSTAT | JiggleStatus | 16, TBC | TBD |  | Contents of Jiggle Axis Activity Status Register |
| LIA01TEMP | LIA_B1TEMP | 8 | TBD |  | LIA Board 1 Temperature |
| LIA02TEMP | LIA_B2_TEMP | 8 | TBD |  | LIA Board 2 Temperature |
| LIA03TEMP | LIA_B3_TEMP | 8 | TBD |  | LIA Board 3 Temperature |
| LIA04TEMP | LIA_B4_TEMP | 8 | TBD |  | LIA Board 4 Temperature |
| LIA05TEMP | LIA_B5_TEMP | 8 | TBD |  | LIA Board 5 Temperature |
| LIA06TEMP | LIA_B6_TEMP | 8 | TBD |  | LIA Board 6 Temperature |
| LIA07TEMP | LIA_B7_TEMP | 8 | TBD |  | LIA Board 7 Temperature |
| LIA08TEMP | LIA_B8_TEMP | 8 | TBD |  | LIA Board 8 Temperature |
| LIA09TEMP | LIA_B9_TEMP | 8 | TBD |  | LIA Board 9 Temperature |
| LIA10TEMP | LIA_B10_TEMP | 8 | TBD |  | LIA Board 10 Temperature |
| LIA11TEMP | LIA_B11_TEMP | 8 | TBD |  | LIA Board 11Temperature |
| LIA12TEMP | LIA_B12_TEMP | 8 | TBD |  | LIA Board 12 Temperature |
| MCUFLAGS |  | 16 |  |  | MCU Status -TBC |
| MCUTIMEOUT | DPU_PollingTime |  |  |  | Maximum Time between commands before an IO error is reported |
| MCUTELSTAT | Telemetry | TBD | TBD |  | Define TM packets to be sent |
| MCUTELSAMP | TelemetrySampling | TBD | TBD |  | Sampling Rate of Telemetry Packets |
| MEMCHK |  | 48 | TBD |  | Memory Check Flags |
| MODE |  | 16 | TBD |  | Instrument Operating Mode |
| MONSTAT DCUMONSTAT MCUMONSTAT SCUMONSTAT |  | 16 1 1 1 | MONSTAT |  | Subsystem Monitoring Status –- indicates if the subsystem is on/off DCU Status (bit 0) MCU Status (bit 1) SCU Status (Bit 2) |
| OBSID |  | 32 |  |  | Observation ID |
| OBSLEN |  | 32 |  |  | Time since start of Observation (secs) |
| OTFERROR |  | 16, TBC | TBD |  | On Target Flag Error |
| OTFTIME |  | 48 |  |  | On Target Flag Time |
| OTF |  | 1 | OTF |  | On Target Flag |
| PHOTBIAS9V | DcuBPHp09 | TBD | TBD | TBD | Voltage to Photometer Bias Board on +9V line |
| PHOTBIAS9VN | DcuBPHn09 | TBD | TBD | TBD | Voltage to Photometer Bias Board on -9V line |
| PHOTBIASFREQ | Div_photo_bias | 9 | BIASFREQ |  | Photometry Bias frequency |
| PHOTBIASMODE | Mode_photo_bias | 8 | BIASMODE |  | Photometry bias generator mode |
| PHOTLIA5V | Dc uLPHp05 | TBD | TBD | TBD | Voltage to Photometer LIA Board on +5V line |
| PHOTLIA9V | Dc uLPHp09 | TBD | TBD | TBD | Voltage to Photometer LIA Board on +9V line |
| PHOTLIA9VN | Dc uLPHn09 | TBD | TBD | TBD | Voltage to Photometer LIA Board on -9V line |
| PHOTSAMPFREQ | Div_photo_sampl | 8 | PSAMPFREQ |  | Photometry sampling frequency |
| PHTRV | Ampl_photo_heater | 8 | HTR |  | Voltage applied to photometer heaters |
| PLWBIAS | Ampl_P500 | 8 | BIAS |  | Amplitude of bias for photometry long wave channels |
| PLWJFET1V | Ampl_P500_VSS1 | 8 | JFETV |  | Voltage applied to JFET for photometry long wave channels (group1) |
| PLWJFET2V | Ampl_P500_VSS2 | 8 | JFETV |  | Voltage applied to JFET for photometry long wave channels (group2) |
| PLWPHSE | Phase_shift_P500 | 8 | PHASE |  | Phase shift for long wave photometry channels demodulation |
| PMLWJFETSTAT PMWJFET1STAT PMWJFET2STAT PMWJFET3STAT PMWJFET4STAT PLWJFET1STAT PLWJFET2STAT | P350_JFET_1 P350_JFET_2 P350_JFET_3 P350_JFET_4 P500_JFET_1 P500_JFET_2 | 6 1 1 1 1 1 1 | JFETSTAT JFETSTAT JFETSTAT JFETSTAT JFETSTAT JFETSTAT |  | Status of JFET power for photometry medium wave channels (group1) (Bit 7) Status of JFET power for photometry medium wave channels (group2) (Bit 6) Status of JFET power for photometry medium wave channels (group3) (Bit 5) Status of JFET power for photometry medium wave channels (group4) (Bit 4) Status of JFET power for photometry long wave channels (group1) (Bit 3) Status of JFET power for photometry long wave channels (group2) (Bit 2) |
| PMWBIAS | Ampl_P350 | 8 | BIAS |  | Amplitude of bias for photometry medium wave channels |
| PMWJFET1V | Ampl_P350_VSS1 | 8 | JFETV |  | Voltage applied to JFET for photometry medium wave channels (group1) |
| PMWJFET2V | Ampl_P350_VSS2 | 8 | JFETV |  | Voltage applied to JFET for photometry medium wave channels (group2) |
| PMWJFET3V | Ampl_P350_VSS3 | 8 | JFETV |  | Voltage applied to JFET for photometry medium wave channels (group3) |
| PMWJFET4V | Ampl_P350_VSS4 | 8 | JFETV |  | Voltage applied to JFET for photometry medium wave channels (group4) |
| PMWPHSE | Phase_shift_P350 | 8 | PHASE |  | Phase shift for medium wave photometry channels demodulation |
| PSUTEMP | PsuTempRd | TBD | TBD | TBD | PSU Temperature Sensor reading |
| PSWBIAS | Ampl_P250 | 8 | BIAS |  | Amplitude of bias for photometry short wave channels |
| PSWJFET1V | Ampl_P250_VSS1 | 8 | JFETV |  | Voltage applied to JFET for photometry short wave channels (group1) |
| PSWJFET2V | Ampl_P250_VSS2 | 8 | JFETV |  | Voltage applied to JFET for photometry short wave channels (group2) |
| PSWJFET3V | Ampl_P250_VSS3 | 8 | JFETV |  | Voltage applied to JFET for photometry short wave channels (group3) |
| PSWJFET4V | Ampl_P250_VSS4 | 8 | JFETV |  | Voltage applied to JFET for photometry short wave channels (group4) |
| PSWJFET5V | Ampl_P250_VSS5 | 8 | JFETV |  | Voltage applied to JFET for photometry short wave channels (group5) |
| PSWJFET6V | Ampl_P250_VSS6 | 8 | JFETV |  | Voltage applied to JFET for photometry short wave channels (group6) |
| PSWJFETSTAT PSWJFET1STAT PSWJFET2STAT PSWJFET3STAT PSWJFET4STAT PSWJFET5STAT PSWJFET6STAT | P250_JFET_1 P250_JFET_2 P250_JFET_3 P250_JFET_4 P250_JFET_5 P250_JFET_6 | 6 1 1 1 1 1 1 | JFETSTAT JFETSTAT JFETSTAT JFETSTAT JFETSTAT JFETSTAT |  | Status of JFET power for photometry short wave channels (group1) (Bit 7) Status of JFET power for photometry short wave channels (group2) (Bit 6) Status of JFET power for photometry short wave channels (group3) (Bit 5) Status of JFET power for photometry short wave channels (group4) (Bit 4) Status of JFET power for photometry short wave channels (group5) (Bit 3) Status of JFET power for photometry short wave channels (group6) (Bit 2) |
| PSWPHSE | Phase_shift_P250 | 8 | PHASE |  | Phase shift for short wave photometry channels demodulation |
| RATE |  | 32 |  |  | Data Rate (average bits/sec over observation) |
| SCANMODE | ScanMode | 2 | SCANMODE |  | SMEC Scan Mode |
| SCANS | ScanNumber | 16 |  |  | Number of SMEC Scans to perform TBC |
| SCANSPEED | ScanSpeed | 16 |  |  | SMEC Scan Speed |
| SCANSTART | ScanStart | 16 |  |  | SMEC Scan Start Position |
| SCANSTAT | StartScan | 1 | SCANSTAT |  | SMEC Scan Status |
| SCU5V | ScuCHTp05 | 12, TBC | TBD |  | Voltage on SCU 5Vline |
| SCU9V | ScuCHTp09 | 12, TBC | TBD |  | Voltage on SCU+9Vline |
| SCU9VN | ScuCHTn09 | 12, TBC | TBD |  | Voltage on SCU -9Vline |
| SCUCAL1I | CalibraI1 | 12, TBC | TBD |  | Current in Calibrator 1 |
| SCUCAL1V | CalibraV1 | 12, TBC | TBD |  | Voltage Applied to Calibrator 1 |
| SCUCAL2I | CalibraI2 | 12, TBC | TBD |  | Current in Calibrator 2 |
| SCUCAL2V | CalibraV2 | 12, TBC | TBD |  | Voltage Applied to Calibrator 2 |
| SCUCAL3I | CalibraI3 | 12, TBC | TBD |  | Current in Calibrator 3 |
| SCUCAL3V | CalibraV3 | 12, TBC | TBD |  | Voltage Applied to Calibrator 3 |
| SCUCMDSTAT |  | TBD | TBD |  | Command Interface Control Status Word - TBD |
| SCUDATAFREQ | FrameRate | 16,TBC | TBD |  | Frame Rate |
| SCUDELAY | SubsDelay | 16,TBC | TBD |  | Subsystem Response Time |
| SCUFLAGS |  | 16 |  |  | SCU Status -TBC |
| SCUFRAMES | SeqLength | 16,TBC |  |  | Number of frames |
| SCUHHTRV | HheaterV1 | 12, TBC | TBD |  | Voltage Applied to High Power Heater |
| SCULHTR1V | LHeaterV1 | 12, TBC | TBD |  | Voltage Applied to Low Power Heater1 |
| SCULHTR2V | LheaterV2 | 12, TBC | TBD |  | Voltage Applied to Low Power Heater2 |
| SCULHTR3V | LheaterV3 | 12, TBC | TBD |  | Voltage Applied to Low Power Heater3 |
| SCUSTAT | DRelOnOff | 8 | TBD |  | Status of Distribution Board relays |
| SCUSUBKFREQ | SubKpRate | 16,TBC | TBD |  | Sampling Rate of SubK temperatures |
| SCUSUBSSTAT | SubStatus | TBD | TBD |  | Subsystem Status |
| SCUTEMPSTAT Allocation of bits TBD | TempOnOff | 12 | TBD |  | Power on status of temperature probes |
| SHTRV | Ampl_spectro_heater | 8 | HTR |  | Voltage applied to spectrometer heaters |
| SJFETSTAT SLWJFET1STAT SSWJFET1STAT SSWJFET2STAT | S-LW_JFET_1 S-SW_JFET_1 S-SW_JFET_2 | 6 1 1 1 | JFETSTAT JFETSTAT JFETSTAT |  | Status of JFET power for spectrometry long wave channels (Bit 7) Status of JFET power for spectrometry short wave channels (group1) (Bit 6) Status of JFET power for spectrometry short wave channels (group2) (Bit 5) |
| SLWBIAS | Ampl_S-LW | 8 | BIAS |  | Amplitude of bias for spectrometry long wave channels |
| SLWJFET1V | Ampl_S-LW_VSS1 | 8 | JFETV |  | Voltage applied to JFET for spectrometry long wave channels |
| SLWPHSE | Phase_shift_S-LW | 8 | PHASE |  | Phase shift for long wave spectrometry channels demodulation |
| SMECOENCPWR | EncoderPwr | 3 | TBD |  | SMEC Optical Encoder LED power |
| SMECFILTHIGH | DerivFilterHigh | 16,TBC |  |  | Filtering Time Constant to calculate the derivative term of the SMEC PID Controller |
| SMECFILTLOW | DerivFilterLow | 16,TBC |  |  | Filtering Time Constant to calculate the derivative term of the SMEC PID Controller |
| SMECSATNLIM | IntegrationLimit | 16,TBC |  |  | Integration Saturation Limit for the SMEC PID Controller? |
| SMECINITSTAT |  | TBD |  |  | Initialisation Status of SMEC |
| SMECKDHIGH | KdHigh | 16,TBC |  |  | Maximum Derivative Gain of SMEC PID Controller? |
| SMECKDLOW | KdLow | 16,TBC |  |  | Minimum Derivative Gain of SMEC PID Controller? |
| SMECKIHIGH | KiHigh | 16,TBC |  |  | Maximum Integral Gain of SMEC PID Controller? |
| SMECKILOW | KiLow | 16,TBC |  |  | Minimum Integral Gain of SMEC PID Controller? |
| SMECKPHIGH | KpHigh | 16,TBC |  |  | Maximum Proportional Gain of SMEC PID Controller? |
| SMECKPLOW | KpLow | 16,TBC |  |  | Maximum Proportional Gain of SMEC PID Controller? |
| SMECLAT1STAT | LaunchLatch1 | 1 | LATCH |  | SMEC Launch Latch1 Status |
| SMECLAT2STAT | LaunchLatch2 | 1 | LATCH |  | SMEC Launch Latch2 Status |
| SMECLOOPMODE | LoopMode | 2 | LOOPMODE |  | SMEC Control Loop Mode |
| SMECLVDTPWR | LVDTPwr | 1 | TBD |  | SMEC LVDT Oscillator On/Off |
| SMECMEANPERR | MeanPositionError | 16,TBC | TBD |  | Mean SMEC Position Error over scan |
| SMECMEANVEL | MeanSpeed | 16,TBC | TBD |  | Mean SMEC Speed over scan |
| SMECNOTCHIGH | NotchParamHigh | 16,TBC |  |  | TBW |
| SMECNOTCHLOW | NotchParamLow | 16,TBC |  |  | TBW |
| SMECPOSN | ActualPosition | 16,TBC |  |  | Last Absolute position of the SMEC |
| SMECPERRLIM | PositionErrorLimit | 16,TBC |  |  | Minimum Value of SMEC Position Error that causes a PID error to be reported? |
| SMECSTAT | SmecStatus | 16,TBC | TBD |  | Contents of SMEC Activity Status Register |
| SMECVEL | ActualVelocity | 16,TBC |  |  | Instantaneous Velocity (20Hz filtered) of the SMEC |
| SPECBIAS9V | DcuBSPp09 | TBD | TBD | TBD | Voltage to Spectrometer Bias Board on +9V line |
| SPECBIAS9VN | DcuBSPn09 | TBD | TBD | TBD | Voltage to Spectrometer Bias Board on -9V line |
| SPECBIASFREQ | Div_spectro_bias | 9 | BIASFREQ |  | Spectrometry Bias frequency |
| SPECBIASMODE | Mode_spectro_bias | 8 | BIASMODE |  | Spectrometry bias generator mode |
| SPECLIA5V | DcuLSPp05 | TBD | TBD | TBD | Voltage to Spectrometer LIA Board on +5V line |
| SPECLIA9V | DcuLSPp09 | TBD | TBD | TBD | Voltage to Spectrometer LIA Board on +9V line |
| SPECLIA9VN | DcuLSPn09 | TBD | TBD | TBD | Voltage to Spectrometer LIA Board on -9V line |
| SPECSAMPFREQ | Div_spectro_sampl | 8 | SSAMPFREQ |  | Spectrometry sampling frequency |
| SSWBIAS | Ampl_S-SW | 8 | BIAS |  | Amplitude of bias for spectrometry short wave channels |
| SSWJFET1V | Ampl_S-SW_VSS1 | 8 | JFETV |  | Voltage applied to JFET for spectrometry short wave channels (group1) |
| SSWJFET2V | Ampl_S-SW_VSS2 | 8 | JFETV |  | Voltage applied to JFET for spectrometry short wave channels (group2) |
| SSWPHSE | Phase_shift_S-SW | 8 | PHASE |  | Phase shift for short wave spectrometry channels demodulation |
| STEP |  | 16 |  |  | Number of current step in an observation |
| SUBKTEMP | SubKTempP | TBD | TBD | TBD | Temperature from SubK temperature probe |
| TRACEPERIOD | TraceSampling |  | PERIOD |  | Time period between successive Trace Values |
| TRACESIZE | TraceBuffer | 16, TBC |  |  | Trace Buffer Size |
| TRACEPARM1 | TraceParam#1 | TBD |  |  | Trace Parameter 1 |
| TRACEPARM2 | TraceParam#2 | TBD |  |  | Trace Parameter 2 |
| TRACEPARM3 | TraceParam#3 | TBD |  |  | Trace Parameter 3 |
| TRACEPARM4 | TraceParam#4 | TBD |  |  | Trace Parameter 4 |
| TRACEPARM5 | TraceParam#5 | TBD |  |  | Trace Parameter 5 |
| TRACEPARM6 | TraceParam#6 | TBD |  |  | Trace Parameter 6 |
| TC1TEMP | T/C1 | 20 | TBD |  | Thermal Control Thermistor #1 value |
| TC2TEMP | T/C2 | 20 | TBD |  | Thermal Control Thermistor #2 value |
| TC3TEMP | T/C3 | 20 | TBD |  | Thermal Control Thermistor #3 value |
| TCBIAS | Ampl_T/C | 8 | BIAS |  | Amplitude of bias for thermal control channels |
| TCEXEC |  | 16 |  |  | Number of telecommand packets executed since switch on |
| TCEXEN |  | 16 |  |  | Sequence Control word of last executeded telecommand packet |
| TCPHSE | Phase_shift_T/C | 8 | PHASE |  | Phase shift for thermal control channels demodulation |
| TCRECN |  | 16 |  |  | Sequence Control word of last received telecommand packet |
| TCRECV |  | 16 |  |  | Number of telecommand packets received since start of the OBS application. Commands to the Boot SW are not included |
| TCUTEMP | TcuTempRd | TBD | TBD | TBD | Temperature from sensor on Temp Board |
| TDPU |  | 48 |  |  | Local DPU On Board Time |
| TEMP01 | FpuTemp01 | TBD | TBD | TBD | To be replaced by correct name |
| TEMP02 | FpuTemp02 | TBD | TBD | TBD | To be replaced by correct name |
| TEMP03 | FpuTemp03 | TBD | TBD | TBD | To be replaced by correct name |
| TEMP04 | FpuTemp04 | TBD | TBD | TBD | To be replaced by correct name |
| TEMP05 | FpuTemp05 | TBD | TBD | TBD | To be replaced by correct name |
| TEMP06 | FpuTemp06 | TBD | TBD | TBD | To be replaced by correct name |
| TEMP07 | FpuTemp07 | TBD | TBD | TBD | To be replaced by correct name |
| TEMP08 | FpuTemp08 | TBD | TBD | TBD | To be replaced by correct name |
| TEMP09 | FpuTemp09 | TBD | TBD | TBD | To be replaced by correct name |
| TEMP10 | FpuTemp10 | TBD | TBD | TBD | To be replaced by correct name |
| TEMP11 | FpuTemp11 | TBD | TBD | TBD | To be replaced by correct name |
| TEMP12 | FpuTemp12 | TBD | TBD | TBD | To be replaced by correct name |
| TEMP13 | FpuTemp13 | TBD | TBD | TBD | To be replaced by correct name |
| TEMP14 | FpuTemp14 | TBD | TBD | TBD | To be replaced by correct name |
| TEMP15 | FpuTemp15 | TBD | TBD | TBD | To be replaced by correct name |
| TEMP16 | FpuTemp16 | TBD | TBD | TBD | To be replaced by correct name |
| THSK |  | 48 |  |  | DPU Time of start of last housekeeping data collection period |
| TSFTIME |  | 48 |  |  | Telescope Scan Time |
| TSF |  | 1 | TSF |  | Telscope Scan Flag |
| TSYNC |  | 48 |  |  | DPU Time of last DRCU Synchronisation |
| SCUSPARE | Reserved | TBD |  |  |  |

### Conversion Curves

| Name | Type | Raw Value | Converted Value | Units | Comments |
| --- | --- | --- | --- | --- | --- |
| BIAS | Analogue | 0 255 | 0.0 Vbmax | Volts |  |
| BIASFREQ | Derived Calculated | Raw | Eng | Hz |  |
| BIASMODE | Enumerated | 0c00 0x01 0x02 …… …… 0xFD 0xFE 0xFF | OFF DC001 DC002 …….. …….. DC253 DC252 SINE |  | Values 0x01 to 0xFE are test levels |
| CHOPMODE | Enumerated | 0 1 2 | STOP STEP TOGGLE |  | Chopping Stopped Chopping in step mode Chopping in toggle mode |
| CHOPSENS | Enumerated | 0 1 | ON OFF |  | Values TBC |
| CLOOPMODE | Enumerated | 0 1 2 | OPEN BEMF SENS |  | Loop Open Loop closed using Back EMF Loop Closed using Magnetoresistive Sensor |
| DCUFRMS | Enumerated | 0 1 2 ….. ….. 254 255 | CONT. 1 2 ….. ….. 254 255 |  |  |
| DCUMODE | Enumerated | 0x00 0x01 0x02 0x03 0x04 0x05 0x06 0x08 0x0C 0x10 0x14 0x18 0x1C | PHOT PSW PMW PLW SPEC SSW SLW PTEST STEST POFFSET SOFFSET POFFGET SOFFGET |  |  |
| DCUSTAT | Enumerated | 0 1 | OFF RUN |  |  |
| HTR | Analogue | 0 255 | 0.0 Vhmax | Volts |  |
| JFETSTAT | Enumerated | 0 1 | OFF ON |  |  |
| JFETV | Analogue | 0 255 | 0.0 VSSmax | Volts |  |
| JIGGLEMODE | Enumerated | 0 1 2 | STOP STEP TOGGLE |  | Jiggling Stopped Jiggling in step mode Jiggling in toggle mode - TBD if applicable |
| JIGGLESENS | Enumerated | 0 1 | ON OFF |  | Values TBC |
| JLOOPMODE | Enumerated | 0 1 2 | OPEN BEMF SENS |  | Loop Open Loop closed using Back EMF Loop Closed using Magnetoresistive Sensor |
| LATCH | Enumerated | 0 1 | Engaged Disengaged |  | Values TBC |
| LOOPMODE | Enumerated | 0 1 2 3 | OPEN BEMF LVDT OENC |  | Loop Open Loop closed using Back EMF Loop Closed using LVDT Loop Closed using Optical Encoder |
| MONSTAT | Enumerated | 0 1 | OFF ON |  | Subsystem off Subsystem on |
| OTF | Enumerated | 0 1 | Off Target On Target |  |  |
| PERIOD |  |  |  | mS |  |
| PHASE | Analogue | 0 255 | 0 360 | Degrees |  |
| PSAMPFREQ | Derived Calculated | Raw | Eng | Hz |  |
| SCANMODE | Enumerated | 0 1 2 3 | STOP STEP SAWTOOTH TRIANGLE |  |  |
| SCANSTAT | Enumerated | 0 1 | STOP RUN |  |  |
| SSAMPFREQ | Derived Calculated | Raw | Eng | Hz |  |
| TSF | Enumerated | 2 3 | Scanning Pointing |  |  |

### Constraints

Appendix A

This section describes the use of  the On Board Software (OBS) commands and telemetry in sufficient detail that the interface can be understood.

# Tables

Much of the data used by the OBS for operations will be held in tables. These will be used to hold, for example:

- Housekeeping packet parameter lists

- Jiggle position tables

- Command Lists

The OBS will provide for the definition of up to 128 tables, within a fixed-size memory area and will automatically move data within this memory area in order to allow update of tables, including a change in size.

By default the following table numbers are assigned and populated in the OBS, though they may be changed by command:

| Table ID | Description |
| --- | --- |
| 00 | Critical Housekeeping Report Definition |
| 01 | Nominal Housekeeping Report Definition |
| 02 | undefined |
| 03 | undefined |
| 21 | Cooler Recycle |
| 22 | Cooler Temperature Control |
| 23 | 300mK Temperature Control |
| 24 | SCAL Temperature Control |
| 31 | CHOP |
| 32 | SCAN |
| 100 | Functions |

All tables are accessed using a Table_ID and individual locations in the table are accessed by an index, specified as a number of words, offset from the beginning of the table. The word size is 32bits.

Appendix B

# Control Loops

Several control loops are executed by the On-board Software. These are all implemented as PID (Proportional, Integral, Differential) control algorithms, where the control variable (C) is adjusted to maintain the measurement variable (M) at the set point (S). The equation giving this relationship is

Where:

CN = Control variable value for sample period N

MN = Measurement Variable value at sample N

S = Required Set Point of the measurement variable

KP = Proportional Gain

KI = Integral Gain

KD = Differential Gain

n = number of samples in the integral

## Control Loop Parameters

When starting the control loop the following parameters have to be provided

- S = Required Set Point of the measurement variable

- KP = Proportional Gain

- KI = Integral Gain

- KD = Differential Gain

- n = number of samples in the integral (max 32, TBC)

- dt = the time interval between samples

- PM = The housekeeping parameter to use as the measurement variable

- PC =The housekeeping parameter to use as the control variable

It is expected that the software shall maintain a buffer containing the last n samples in order to calculate the integral term for each sample period.

If the accuracy of the measurement sampling interval cannot be guaranteed, the software will also need to maintain a buffer containing the time of each of the n samples in order to make a more accurate estimate of the integral and differential terms (the equation above assumes a fixed sampling period).

The software must ensure that the accuracy of the calculation is adequate (e.g. by use of floating point, or fixed point, math functions)

Appendix C

# Command List

This section (TBW) defines the command list entries that are available.

Appendix D

# Detector Pixel Mapping

## Phtometer SW

## Photometer MW

## Photometer LW

## Spectrometer SW

## Spectrometer LW

# Text boxes

| Error | Failure Code | Parameter |
| --- | --- | --- |
| Illegal APID | 0 | None |
| Incomplete Packet or invalid Length | 1 | Actual length of received packet |
| Incorrect Checksum | 2 | Calculated Checksum from received packet |
| Illegal Packet Type | 3 | None |
| Illegal Packet Sub-Type | 4 | None |

Note: The parameter is placed in the least significant bits of the16 bit 'parameter'  field and the most significant bits are padded with zeros

| Parameter | Comment |
| --- | --- |
| EVENTID_NSRE | 0x0522 |
| SID_NSRE | 0x5110 |
| OBSID_NSRE | Observation ID |
| BBID_NSRE | Building Block ID |
| EVENTCOUNT_NSRE | Sequential counter for TM(5,1) events |
| COMMAND_NSRE | Copy of command sent to DRCU (32bits) |

| Error | Failure Code | Parameters |
| --- | --- | --- |
| Illegal Function ID | 0x0801 | See Note |
| Illegal Activity ID | 0x0802 | See Note |

Note: The parameters field should contain the first 20 words from the 'source data' field of the received telecommand packet, unless this field is less than 20 words in length, in which case all words from the 'source data' field will be included and padded with zeros.

| APID | Packet type |
| --- | --- |
| APID1 | Critical Housekeeping Report |
| APID2 | Nominal Housekeeping Report |

| SID | Packet type | Default Period (msec) |
| --- | --- | --- |
| 0x0300 | Critical Housekeeping Report | 2000 |
| 0x0301 | Nominal Housekeeping Report | 1000 |

The reports available are identified by the APID (APID3 = Photometer, APID4 = Spectrometer) and the SID (composed of the Frame Structure (MSByte) and FrameID (LSByte)):

| APID | SID | Report |
| --- | --- | --- |
| APID3 | 0x0207 | Photometer Offsets |
| APID4 | 0x0208 | Spectrometer Offsets |
| APID5 | 0x0209 | Housekeeping Packet Definition |
| APID5 | 0x020A | Report Table Report |
| APID5 | 0x020B | VM Science Data |

Parameter

| Name | Comment |
| --- | --- |
| FUNCTIONID | Function to report on |

The reports available are identified by the APID (APID3 = Photometer, APID4 = Spectrometer and APID5 = Subsystem Data) and the SID (composed of the Frame Structure (MSByte) and FrameID (LSByte)):

| APID | SID | Report |
| --- | --- | --- |
| APID3 | 0x0309 | Photometer Test Pattern |
| APID3 | 0x030A | PSW Test Pattern |
| APID3 | 0x030B | PMW Test Pattern |
| APID3 | 0x030C | PLW Test Pattern |
| APID4 | 0x030D | Spectrometer Test Pattern |
| APID4 | 0x030E | SSW Test Pattern |
| APID4 | 0x030F | SLW Test Pattern |
| APID5 | 0x0814 | MCU Engineering |
| APID5 | 0x0915 | MCU Test Pattern |
| APID5 | 0x1121 | SCU Test Pattern |
| APID5 | 0xFF00 | Transparent Data |

The reports available are identified by the APID (APID3 = Photometer, APID4 = Spectrometer) and the SID (composed of the Frame Structure (MSByte) and FrameID (LSByte)):

| APID | SID | Report |
| --- | --- | --- |
| APID3 | 0x0102 | PSW Array |
| APID3 | 0x0103 | PMW Array |
| APID3 | 0x0104 | PLW Array |
| APID4 | 0x0105 | SSW Array |
| APID4 | 0x0106 | SLW Array |

Parameter

| Name | Value and Comments |
| --- | --- |
| FUNCTIONID | 0x01 |
| ACTIVITYID | 0x02 |
| SID | 0x0002 |
| TABLEID |  |
| INDEX | Starting offset to first word to report |
| COUNT | Number of (32 bit) words to report |

The reports available are identified by the APID (APID3 = Photometer, APID4 = Spectrometer and APID5 = Subsystem Data) and the SID (composed of the Frame Structure (MSByte) and FrameID (LSByte)):

| APID | SID | Report |
| --- | --- | --- |
| APID3 | 0x0200 | Photometer Full Array |
| APID3 | 0x1200 | Photometer Parallel Mode Selection |
| APID4 | 0x0201 | Spectrometer Full Array |
| APID3 | 0x1201 | Spectrometer Parallel Mode Selection |
| APID5 | 0x0410 | SMEC |
| APID5 | 0x1410 | SMEC Selection |
| APID5 | 0x0612 | BSM |
| APID5 | 0x0A20 | SCU |

Parameters

| Name | Value |
| --- | --- |
| FUNCTIONID | 0xCA |
| ACTIVITYID | 0x03 |
| SID | 0x0000 |

Parameters

| Name | Value |
| --- | --- |
| FUNCTIONID | 0xCA |
| ACTIVITYID | 0x04 |
| SID | 0x0000 |

| Parameter | Comment |
| --- | --- |
| EVENTID_FIE | 0x0506 |
| SID_FIE | 0x5105 |
| OBSID_FIE | Observation ID |
| BBID_FIE | Building Block ID |
| EVENTCOUNT_FIE | Sequential counter for TM(5,1) events |
| FRAMEID_FIE | The Frame ID received from the DRCU |
| FIFOID_FIE | The ID of the FIFO where the frame has been received |

| Parameter | Comment |
| --- | --- |
| TIME | This value has the msb set to indicate that the time is invalid |
| EVENTID_ TVE | 0x8004 |
| SID_ TVE | 0x0009 |
| INFO_ TVE | Information on the error – see table below |
| ERRCODE_ TVE | Error code – see table below |
| FCSCOMP_ TVE | Computed FCS – see table below |
| FCSREAD_ TVE | Read FCS – see table below |
| CHKSUMID_ TVE | Checksum error type – see table below |
| DMADDR_ TVE | Start address in DM – see table below |

Note: some parameters are not applicable for some Error Codes. In these cases the parameters are replaced by 0xAAAA

Parameters

| Name | Comments |
| --- | --- |
| FUNCTIONID | 0xCB |
| ACTIVITYID | 0x01 |
| SID | 0x0001 |

Note: The parameter is placed in the least significant bits of the16 bit 'parameter'  field and the most significant bits are padded with zeros.

| Parameter | Comment |
| --- | --- |
| EVENTID_AWP | Event ID – see table below |
| SID_AWP | 0x5200 |
| OBSID_AWP | Observation ID |
| BBID_AWP | Building Block ID |
| EVENTCOUNT_AWP | Sequential counter of events of this type/subtype |

Parameters

| Name | Value and Comments |
| --- | --- |
| FUNCTIONID | 0x01 |
| ACTIVITYID | 0x01 |
| SID | 0x0001 |
| TABLEID |  |
| TABLESIZE | Number of 32 bit words allocated to table |

Parameters

| Name | Value and Comments |
| --- | --- |
| FUNCTIONID | 0x01 |
| ACTIVITYID | 0x03 |
| SID | 0x0003 |
| TABLEID |  |
| INDEX | Start location at which to place Data |
| N | Number of 32bit words to place in table |
| Data | N (32 bit) words to be placed in the table |

Contents of the Data is dependant on the function of the table and will be specified by IFSI

Parameters

| Name | Value and Comments |
| --- | --- |
| FUNCTIONID | 0x02 |
| ACTIVITYID | 0x01 |
| SID | 0x0004 |
| N | Number of 32bit words in the command List |
| Data | N * 32 bit data words containing the command list to execute |

Parameters

| Name | Value and Comments |
| --- | --- |
| FUNCTIONID | 0x02 |
| ACTIVITYID | 0x02 |
| SID | 0x0005 |
| TABLEID | Table_ID of list to execute |
| INDEX | Index within Table at which to start |
| N | Number of data words |
| Data | N * 32 bit data words. These are the parameters passed to the VM in registers R(00) to R(N-1) |

Parameters

| Name | Value |
| --- | --- |
| FUNCTIONID | 0x02 |
| ACTIVITYID | 0x03 |
| SID | 0x0000 |

Parameters

| Name | Value and Comments |
| --- | --- |
| FUNCTIONID | 0xC1 |
| ACTIVITYID | 0x01 |
| SID | 0x0010 |
| OBSID | Observation ID (32 bits) |

Parameters

| Name | Value and Comments |
| --- | --- |
| FUNCTIONID | 0xC1 |
| ACTIVITYID | 0x02 |
| SID | 0x0011 |
| BBID | Building Block ID (32 bits) |

Parameters

| Name | Comments |
| --- | --- |
| MEMORYID | Memory Area to be addressed Value = 0 to 3 (cannot be 4) |
| STARTADDR | Start Address in SAUs |
| NSAU | Number of SAUs to be loaded |
| DATA | Data to be loaded |
| CRC | CRC Checksum of data field |

Note: The DATA field will contain the words to be written into DPU memory. 48 or 32bit words will be split into 3 or 2 16bit words and written into the DATA field of the telecommand starting from the MSB.

Parameters

| Name | Value |
| --- | --- |
| FUNCTIONID | 0xCA |
| ACTIVITYID | 0x01 |
| SID | 0x0000 |

Parameters

| Name | Value |
| --- | --- |
| FUNCTIONID | 0xCA |
| ACTIVITYID | 0x02 |
| SID | 0x0015 |
| FIFOFLAGS | 0x1000 flushes channel 0 (DCU) FIFO 0x2000 flushes channel 1 (MCU) FIFO 0x4000 flushes channel 2 (SCU) FIFO (values may be OR-ed to flush more than one FIFO) |

Parameters

| Name | Value and Comments |
| --- | --- |
| FUNCTIONID | 0xCA |
| ACTIVITYID | 0x11 |
| SID | 0x0020 |
| FRAMEID | Selection to be disabled |

Parameters

| Name | Value and Comments |
| --- | --- |
| MEMORYID | Memory Area to be addressed |
| STARTADDR | Start Address in SAUs |
| NSAU | Number of SAUs to be dumped |

Parameters

| Name | Value and Comments |
| --- | --- |
| MEMORYID | Memory Area to be addressed |
| STARTADDR | Start Address in SAUs |
| NSAU | Number of SAUs to be checked |

Parameters

| Name | Value |
| --- | --- |
| FUNCTIONID | 0x03 |
| ACTIVITYID | 0x03 |
| SID | 0x0000 |

Parameters

| Name | Value and Comments |
| --- | --- |
| FUNCTIONID | 0x03 |
| ACTIVITYID | 0x02 |
| SID | 0x0007 |
| TABLEID | Table_ID of list to execute |
| INDEX | Index within Table at which to start |
| N | Number of data words |
| Data | N * 32 bit data words. These are the parameters passed to the VM in registers R(00) to R(N-1) |

Parameters

| Name | Value and Comments |
| --- | --- |
| FUNCTIONID | 0xC1 |
| ACTIVITYID | 0x03 |
| SID | 0x0012 |
| MODE | Observing Mode |

Parameters

| Name | Value and Comments |
| --- | --- |
| FUNCTIONID | 0xC1 |
| ACTIVITYID | 0x04 |
| SID | 0x0013 |
| STEP | Observation Step |

Parameters

| Name | Value |
| --- | --- |
| FUNCTIONID | 0xC0 |
| ACTIVITYID | 0x40 |
| SID | 0x000F |
| DCUDATAMODE | DCU Data Mode |
| PIXEL | Location of reference pixel in DCU Frame |
| STARTCHOPPOSN | Initial Chop position |
| CHOPPOSNINCR | Increment in Chop position |
| NCHOPPOSNS | Number of Chop positions |
| STARTJIGGPOSN | Initial Jiggle Position |
| JIGGPOSNINCR | Increment in Jiggle position |
| NJIGGPOSNS | Number of Jiggle positions |
| CHOPOFFSET | Offset from on-source position to off-source |
| NCHOPCYCLES | Number of Chop cycles |
| CHOPCYCLEPERIOD | Period of the Chop cycle |
| NBSMFRAMES | Number of BSM frames per Chop position |
| BSMFRAMESTIME | Time between BSM frames |
| NDCUFRAMES | Number of DCU frames per Chop position |
| DCUFRAMESTIME | Time between DCU frames |
| DCUFRAMESDELAY | Delay to first DCU frame |

| Parameter | Comment |
| --- | --- |
| EVENTID_UCR | 0x0509 |
| SID_UCR | 0x5103 |
| OBSID_UCR | Observation ID |
| BBID_UCR | Building Block ID |
| EVENTCOUNT_UCR | Sequential counter for TM(5,1) events |
| COMMAND_UCR | copy of command sent to DRCU (32 bits) |
| ACK_UCR | Echo of command most significant word received by the DPU (32bits) |

Parameters

| Name | Value and Comments |
| --- | --- |
| FUNCTIONID | 0x10 |

| Parameter | Comment |
| --- | --- |
| EVENTID_PUR | 0x0504 |
| SID_PUR | 0x5101 |
| OBSID_PUR | Observation ID |
| BBID_PUR | Building Block ID |
| EVENTCOUNT_PUR | Sequential counter for TM(5,1) events |
| INSTRID_PUR | Instrument ID = 0x0002 |
| THETAY_PUR | Rotation angle about Y axis |
| THETAZ_PUR | Rotation angle about Z axis |

Parameters

| Name | Value and Comments |
| --- | --- |
| FUNCTIONID | 0xCA |
| ACTIVITYID | 0x10 |
| SID | 0x001F |
| FRAMEID | Science frame to extract data from |
| SELECTEDSID | Structure ID to use for this Selected Data Packet |
| TABLEID | Table containing the selection |

| Parameter | Comment |
| --- | --- |
| EVENTID_NMRE | 0x0521 |
| SID_NMRE | 0x510F |
| OBSID_NMRE | Observation ID |
| BBID_NMRE | Building Block ID |
| EVENTCOUNT_NMRE | Sequential counter for TM(5,1) events |
| COMMAND_NMRE | Copy of command sent to DRCU (32bits) |

Parameters

| Name | Value and Comments |
| --- | --- |
| FUNCTIONID | 0x01 |
| ACTIVITYID | 0x04 |
| SID | 0x0004 |

Parameters

| Name | Value and Comments |
| --- | --- |
| NPCKTS | Number of packets to enable |
| TYPE | Packet Type to enable |
| SUBTYPE | Packet Subtype to enable |
| PACKETID | Packet ID to enable |

Parameters

| Name | Value and Comments |
| --- | --- |
| NPCKTS | Number of packets to enable |
| TYPE | Packet Type to enable |
| SUBTYPE | Packet Subtype to enable |
| PACKETID | Packet ID to enable |

Parameters

| Name | Value and Comments |
| --- | --- |

Parameters

| Name | Value and Comments |
| --- | --- |
| FUNCTIONID | 0x04 |
| ACTIVITYID | 0x02 |
| SID | 0x0009 |
| TABLEID | Table_ID of list to execute |
| INDEX | Index within Table at which to start |
| N | Number of data words |
| Data | N * 32 bit data words. These are the parameters passed to the VM in registers R(00) to R(N-1) |

Parameters

| Name | Value |
| --- | --- |
| FUNCTIONID | 0x04 |
| ACTIVITYID | 0x03 |
| SID | 0x0000 |

Parameters

| Name | Value and Comments |
| --- | --- |
| FUNCTIONID | 0x05 |
| ACTIVITYID | 0x02 |
| SID | 0x000B |
| TABLEID | Table_ID of list to execute |
| INDEX | Index within Table at which to start |
| N | Number of data words |
| Data | N * 32 bit data words. These are the parameters passed to the VM in registers R(00) to R(N-1) |

Parameters

| Name | Value |
| --- | --- |
| FUNCTIONID | 0x05 |
| ACTIVITYID | 0x03 |
| SID | 0x0000 |

Parameters

| Name | Value and Comments |
| --- | --- |
| MEMORYID | Memory Area to be addressed |
| STARTADDR | Start Address in SAUs |
| NSAU | Number of SAUs to be dumped |
| Data | Contents of memory in increasing address |
| CHK | Checksum over the data included in this packet |

Parameters

| Name | Value and Comments |
| --- | --- |
| MEMORYID | Memory Area to be addressed |
| STARTADDR | Start Address in SAUs |
| NSAU | Number of SAUs to be checked |
| CHK | Checksum over the data included in the address range (STARTADDR to STARTADDR+NSAU) |

Parameters

| Name | Value and Comments |
| --- | --- |
| FUNCTIONID | ID of function to be reported |
| ACTIVITYID | Current Activity = 00 if function is stopped = FF if function is active and waiting |
| SID | = 0x0000 indicates no parameters |

Parameters

| Name | Value and Comments |
| --- | --- |
| NDEF | Number of sets of (Type, Subtype, SID) to follow |
| Type | Packet Type |
| Subtype | Packet Subtype |
| Packet ID | Identifier of specific groups of packets: If all packets of the given type/subtype are enabled = 0x0000 For Type = 3: this field contains the HK_Packet _ID For Type = 5: this field contains the Event ID For Type = 21: this field contains the SID |

Parameters

| Name | Value |
| --- | --- |
| FUNCTIONID | 0xCA |
| ACTIVITYID | 0x05 |
| SID | 0x0018 |
| DRCU Command MSW | Most Significant Word of DRCU command |
| DRCU Command LSW | Least Significant Word of DRCU command |

Parameters

| Name | Value |
| --- | --- |
| FUNCTIONID | 0xCA |
| ACTIVITYID | 0x06 |
| SID | 0x0000 |

Parameters

| Name | Value |
| --- | --- |
| FUNCTIONID | 0xCA |
| ACTIVITYID | 0x07 |
| SID | 0x001A |
| Start_Address | Starting address in PM (32 bits) |
| End_Address | End address in PM (32bits) |

Parameters

| Name | Value |
| --- | --- |
| FUNCTIONID | 0x70 |
| ACTIVITYID | 0x02 |
| SID | 0x0000 |

Parameters

| Name | Value |
| --- | --- |
| FUNCTIONID | 0xCA |
| ACTIVITYID | 0x09 |
| SID | 0x0000 |

| Parameter | Comment |
| --- | --- |
| EVENTID_UBR | 0x0505 |
| SID_UBR | 0x5102 |
| OBSID_UBR | Observation ID |
| BBID_UBR | Building Block ID |
| EVENTCOUNT_UBR | Sequential counter for TM(5,1) events |
| POOLID_UBR | ID of the VIRTUOSO Pool which failed to allocate block. IDs are defined in RD08 |
| SIZE_UBR | Size in Bytes of the requested memory block |
| ALLOC_RESULT_UBR | Allocation Result: Allocation Failed Allocation Timed out |
| TASKID_UBR | ID of the OBS task where failure occurred. IDs are defined in RD08 |
| NPKT_UBR | Number of packets currently present in pool |
| MAXPKT_UBR | Maximum number of packets in pool |

| Parameter | Comment |
| --- | --- |
| EVENTID_FLE | 0x0507 |
| SID_FLE | 0x5106 |
| OBSID_FLE | Observation ID |
| BBID_FLE | Building Block ID |
| EVENTCOUNT_FLE | Sequential counter for TM(5,1) events |
| FRAMEID_FLE | The Frame ID received from the DRCU |
| LENGTHRD_FLE | Frame length as read from the DRCU frame |
| LENGTHEX_FLE | Expected frame length for that frame ID |

| Parameter | Comment |
| --- | --- |
| EVENTID_FCE | 0x0508 |
| SID_FCE | 0x5107 |
| OBSID_FCE | Observation ID |
| BBID_FCE | Building Block ID |
| EVENTCOUNT_FCE | Sequential counter for TM(5,1) events |
| FIFOID_FCE | ID of the FIFO where the frame was read from |
| CHKWORDEX_FCE | XOR checksum computed on the read frame |
| CHKWORDRD_FCE | Checksum word read at the end of the received frame |

| Parameter | Comment |
| --- | --- |
| EVENTID_FCR | 0x050A |
| SID_FCR | 0x5104 |
| OBSID_FCR | Observation ID |
| BBID_FCR | Building Block ID |
| EVENTCOUNT_FCR | Sequential counter for TM(5,1) events |
| COMMAND_FCR | copy of command sent to DRCU (32 bits) |
| RESPONSE_FCR | Copy of command echo returned by DRCU (32bits) |

| Parameter | Comment |
| --- | --- |
| EVENTID_STE | 0x050B |
| SID_STE | 0x5108 |
| OBSID_STE | Observation ID |
| BBID_STE | Building Block ID |
| EVENTCOUNT_STE | Sequential counter for TM(5,1) events |
| COMMAND_STE | Copy of command sent to DRCU (32 bits) |
| RESPONSE_STE | Copy of command echo returned by DRCU (32bits) |

| Parameter | Comment |
| --- | --- |
| EVENTID_SRE | 0x050C |
| SID_SRE | 0x5109 |
| OBSID_SRE | Observation ID |
| BBID_SRE | Building Block ID |
| EVENTCOUNT_SRE | Sequential counter for TM(5,1) events |
| COMMAND_SRE | Copy of command sent to DRCU (32 bits) |
| RESPONSE_SRE | Copy of command echo returned by DRCU (32bits) |

| Parameter | Comment |
| --- | --- |
| EVENTID_DPE | 0x050D |
| SID_DPE | 0x510A |
| OBSID_DPE | Observation ID |
| BBID_DPE | Building Block ID |
| EVENTCOUNT_DPE | Sequential counter for TM(5,1) events |
| POOLID_DPE | ID of the VIRTUOSO Pool which failed to allocate block. IDs are defined in RD08 |
| NPKT_DPE | Number of packets currently present in pool |
| MAXPKT_DPE | Maximum number of packets in pool |
| TERROR_DPE | Time When Error Occurred (48 bits) |

| Parameter | Comment |
| --- | --- |
| EVENTID_DFE | 0x050E |
| SID_DFE | 0x510B |
| OBSID_DFE | Observation ID |
| BBID_DFE | Building Block ID |
| EVENTCOUNT_DFE | Sequential counter for TM(5,1) events |
| FIFOID_DFE | ID of the VIRTUOSO FIFO |
| NMSG_DFE | Number of messages currently present in FIFO |
| MAXMSG_DFE | Maximum number of messages in FIFO |
| TERROR_DFE | Time When Error Occurred (48 bits) |

| Parameter | Comment |
| --- | --- |
| EVENTID_NSR | 0x0501 |
| SID_NSR | 0x5100 |
| OBSID_NSR | Observation ID |
| BBID_NSR | Building Block ID |
| EVENTCOUNT_NSR | Sequential counter for TM(5,1) events |
| MODE_NSR | Current Mode |
| STEP_NSR | Step Number |

| Parameter | Comment |
| --- | --- |
| TIME | This value has the msb set to indicate that the time is invalid |
| EVENTID | 0x8008 |
| SID | 0x0003 |
| NERRORS | (0x0000) |

| Parameter | Comment |
| --- | --- |
| TIME | This value has the msb set to indicate that the time is invalid |
| EVENTID_MCE | Event ID - see table below |
| SID_MCE | 0x00FF |
| MEMID_MCE | Memory type (2 bits) |
| NPAGES_MCE | Number of failed memory pages (14bits) |
| Page IDs | A list of the IDs of each failed page (16 bits per ID) For EEPROM the ID may also be interpreted as an error code |

Parameters

| Name | Value and Comments |
| --- | --- |
| FUNCTIONID | 0x10 |

Parameters

| Name | Value |
| --- | --- |
| FUNCTIONID | 0x10 |
| ACTIVITYID | 0x01 |
| SID | 0x0000 |

Parameters

| Name | Value |
| --- | --- |
| FUNCTIONID | 0x10 |
| ACTIVITYID | 0xFF |
| SID | 0x0000 |

| Parameter | Comment |
| --- | --- |
| TIME | This value has the msb set to indicate that the time is invalid |
| EVENTID_EPMLE | 0x8005 |
| SID_EPMLE | 0x0001 |
| MEMTYPE_EPLME (2 bits) | EEPROM Memory = 3 |
| NPAGES_EPLME (14 bits) | Number of pages failed = 0x0001 |
| ERRCODE_EPLME | 0x1800 = Overlapping between two memory pages 0x0400 = No partition to boot 0x0800 = Total FCS Error 0x0C00 = PM FCS Error during page upload 0x1400 = Previous EEPROM test failed 0x1800 = Overlapping between two memory pages |

| Parameter | Comment |
| --- | --- |
| TIME | This value has the msb set to indicate that the time is invalid |
| EVENTID_PMBE | 0x8007 |
| SID_PMBE | 0x0001 |
| MEMTYPE_PMBE (2 bits) | Program Memory = 1 |
| NPAGES_PMBE (14 bits) | Number of pages failed = 0x0001 |
| ERRCODE_PMBE | 0x0800 = Program FCS error – the computed FCS on the whole program is wrong |

Parameters

| Name | Value |
| --- | --- |
| FUNCTIONID | 0x70 |
| ACTIVITYID | 0x03 |
| SID | 0x0000 |

Parameters

| Name | Value and Comments |
| --- | --- |
| FUNCTIONID | ID of function to be reported |
| ACTIVITYID | Current Activity = 01 when Executing a Command List = 02 when Running from a table = 03 when Halted |
| SID | 0x0860 |
| TABLEID | Table containing Command List Not applicable when ACTIVITYID = 01 |
| INDEX | Index within Table to start executing Not applicable when ACTIVITYID = 01 |
| N | Number of Data words |
| Data | N*32 bit data words |

Parameters

| Name | Value and Comments |
| --- | --- |
| FUNCTIONID | ID of function to be reported |
| ACTIVITYID | Current Activity = 10 when selecting = 11 when not selecting |
| SID | 0x0861 |
| N | Number of times FRAMEID, SELSID and TABLEID are repeated |
| FRAMEID | Science Frame data is selected from |
| SELSID | SID for the Select TM Packets |
| TABLEID | Table containing the selection information (= 0xffff if not selected) |

Note: the group FRAMID, SELSID, TABLEID are repeated 24 times in this packet

Parameters

| Name | Value |
| --- | --- |
| FUNCTIONID | 0x70 |
| ACTIVITYID | ???? |
| SID | 0x0000 |

| Parameter | Comment |
| --- | --- |
| EVENTID_LOE | 0x050F |
| SID_LOE | 0x510C |
| OBSID_LOE | Observation ID |
| BBID_LOE | Building Block ID |
| EVENTCOUNT_LOE | Sequential counter for TM(5,1) events |
| LSLOAD_LOE | Number of microsecs that the LSL was busyduring the last second |

| Parameter | Comment |
| --- | --- |
| EVENTID_UTPE | 0x0510 |
| SID_UTPE | 0x510D |
| OBSID_UTPE | Observation ID |
| BBID_UTPE | Building Block ID |
| EVENTCOUNT_UTPE | Sequential counter for TM(5,1) events |
| TYPE_UTPE | Type and subtype of unknown TM packet (copy of part of TM packet Data Field Header) |
| SUBTYPE_UTPE |  |
| SID_UTPE | SID of unknown TM packet |

| Parameter | Comment |
| --- | --- |
| EVENTID_NDRE | 0x0520 |
| SID_NDRE | 0x510E |
| OBSID_NDRE | Observation ID |
| BBID_NDRE | Building Block ID |
| EVENTCOUNT_NDRE | Sequential counter for TM(5,1) events |
| COMMAND_NDRE | Copy of command sent to DRCU (32bits) |

Parameters

| Name | Comments |
| --- | --- |
| FUNCTIONID | 0xCC |
| ACTIVITYID | 0x01 |
| SID | 0x0021 |
| HKPCKTID | HK_Packet_ID |
| HKSID |  |
| HKINTERVAL | msec |
| HKREPEAT | Number of HK frames per packet = 1 |
| TABLEID | Table_ID |

Note: The parameter is placed in the least significant bits of the16 bit 'parameter'  field and the most significant bits are padded with zeros.

Parameters

| Name | Comments |
| --- | --- |
| FUNCTIONID | 0xCC |
| ACTIVITYID | 0x02 |
| SID | 0x0022 |
| HKPCKTID | HK_Packet_ID |

Note: The parameter is placed in the least significant bits of the16 bit 'parameter'  field and the most significant bits are padded with zeros.

Parameters

| Name | Comments |
| --- | --- |
| FUNCTIONID | 0xCC |
| ACTIVITYID | 0x03 |
| SID | 0x0023 |
| HKPCKTID | HK_Packet_ID |

Note: The parameter is placed in the least significant bits of the16 bit 'parameter'  field and the most significant bits are padded with zeros.

| Parameter | Comment |
| --- | --- |
| EVENTID_TSE | 0x0511 |
| SID_TSE | 0x5111 |
| OBSID_TSE | Observation ID |
| BBID_TSE | Building Block ID |
| EVENTCOUNT_TSE | Sequential counter for TM(5,1) events |
| LAST_TC_COUNT_TSE | Previous TC PCKT SEQ Count |
| CURR_TC_COUNT_TSE | Current TC PCKT SEQ Count |

Parameters

| Name | Value and Comments |
| --- | --- |
| TDPU | Copy of the On board time held by the DPU |

| Parameter | Comment |
| --- | --- |
| EVENTID_OOL | Event ID – see table below |
| SID_OOL | 0x5112 |
| OBSID_OOL | Observation ID |
| BBID_OOL | Building Block ID |
| EVENTCOUNT_OOL | Sequential counter of events of this type/subtype |
| PARMID_OOL | Monitoring Parameter ID of parameter which has gone out of limits |
| PARMVALUE_OOL | Value of the Monitoring Parameter which has gone out of limits |

| Parameter | Comment |
| --- | --- |
| TIME | This value has the msb set to indicate that the time is invalid |
| EVENTID_DPMLE | 0x8006 |
| SID_DPMLE | 0x0001 |
| MEMTYPE_DPLME (2 bits) | Data Memory = 2 |
| NPAGES_DPLME (14 bits) | Number of pages failed = 0x0001 |
| ERRCODE_DPLME | 0x0C00 = PM FCS Error during page upload 0x1800 = Overlapping between two memory pages 0x1900 = PM Memory Page Boundaries Uploading error |