# SPIRE

| SUBJECT: | SPIRE Telemetry Data RatesSPIRE Telemetry Data Rates |
| --- | --- |
| PREPARED BY: | K.J. KingK.J. King |
| DOCUMENT No: | SPIRE-RAL-NOT-001083SPIRE-RAL-NOT-001083 |
| ISSUE: | Issue 1.0 Issue 1.0 | Date: | 25th January 200225th January 2002 |

Distribution

| Bruce Swinyard | RAL |
| --- | --- |
| John Delderfield | RAL |
| Doug Griffin | RAL |
| Sunil Sidher | RAL |

# Change Record

| ISSUE | DATE |  |
| --- | --- | --- |
| Issue 1.0 Draft 1 | 16th January | First Version |
| Issue 1.0 | 25th January | Added RD02 Updated Spectrometry Scanning to remove SCU and DPU packets Increased number of frames per packet for DCU to 4 Updated constraints to 25 packets per sec and 130kbps as shown in RD02 |

# Table of Contents

1.	Introduction	6

1.1	Scope	6

1.2	Documents	6

1.2.1	Applicable Documents	6

1.2.2	Reference Documents	6

2.	Data Rates for Observatory Functions	7

2.1	Photometric Chopping Functions	7

2.2	Photometric Non-chopping Functions	8

2.3	Spectrometry Scanning Functions	9

2.4	Spectrometry Set and Look Functions	10

Figures

Tables

Glossary

| FTS | Fourier Transform Spectrometer |
| --- | --- |
| POF | Photometry Observatory Function |
| SOF | Spectrometry Observatory Function |
| SPIRE | Spectral and Photometric Imaging Receiver |

# Introduction

This document provides estimates of the data rates expected from the different SPIRE observing modes described in the SPIRE Operating Modes document (AD01).

The data rates are based on the nominal detector and mechanism sampling rates described in AD01, combined with the science data formats described in the SPIRE Data ICD (RD01).

## Scope

The data and packet rates in this document provide the maximum rate for data generated in the nominal operating mode. In practice the actual average data rate through an observation will be less than this due to science data not being collected during change of instrument and telescope configurations and other operations (e.g. re-pointing of the telescope during raster scans).  This document does not address the estimation of actual data generated during an observation.

The estimated data rates are compared to the allowed data (and TM packet) rates given in RD02

Note: AD01 does not yet cover the SPIRE-PACS parallel mode of operation

## Documents

### Applicable Documents

| AD01 | Operating Modes for the SPIRE Instrument (SPIRE-Ral_PRJ-000320) Issue 3.0 |
| --- | --- |

### Reference Documents

| RD01 | SPIRE Data ICD (SPIRE-Ral-DOC-1078) Issue 1.0 Draft 1 |
| --- | --- |
| RD02 | Instrument Data Rates (H-P-1-ASPI-TN-0204) Issue 1.0, 15th January 2002 |

# Data Rates for Observatory Functions

Observatory functions can be split into 4 types:

- Photometry using the Beam Steering Mirror to chop the input beam between two pixels

- Photometry with no chopping, using the telescope movement to modulate the detector signals

- Spectrometry by continuously scanning the FTS mechanism

- Spectrometry chopping at a set of FTS mechanism fixed positions

The data generated for each of these four types are described below.

## Photometric Chopping Functions

For all Photometric Observatory Functions employing chopping (POF1, POF2, POF3, POF4, POF6, POF7) the maximum data rate is determined primarily by the detector data sampling rate within the chop cycle.

## Photometric Non-chopping Functions

For the Photometric Observatory Function not employing chopping (POF5) the maximum data rate is determined primarily by the detector data sampling rate, which is nominally set at 25Hz to allow for the fastest telescope scanning speed.

## Spectrometry Scanning Functions

## Spectrometry Step-and-Look Functions