| CARLO GAVAZZI SPACE S.p.A. | HSO/FIRST-DPU |
| --- | --- |
| DOCUMENT TYPE : TEST PROCEDURE | DRD : - |
| TITLE: EM PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE |
| DOCUMENT No: DPU-PR-CGS-002 | PAGE: 1 OF 66 |
| SPIRE-CGS-DOC-001087 |
| ISSUE No: 1 | DATE: 24/09/2001 |
| PREPARED BY: A. SCIORTINO |
| APPROVED BY: V. CHIAVERINI |
| THIS DOCUMENT IS SUBJECT TO THE APPROVAL OF: |
|  | YES | NO |  |
| Product Assurance | X |  |  |  |  |  |
|  |  |  |  | Approval Signature |  | Date |
| Configuration Control | X |  |  |  |  |  |
|  |  |  |  | Approval Signature |  | Date |
| Project Control |  | X |  |  |  |  |
|  |  |  |  | Approval Signature |  | Date |
| Engineering | X |  |  |  |  |  |
|  |  |  |  | Approval Signature |  | Date |
| Managing Director |  | X |  |  |  |  |
|  |  |  |  | Approval Signature |  | Date |
| CGS Program Manager | X |  |  |  |  |  |
|  |  |  | Approval Signature |  | Date |
|  | YES | NO |  |  |
| Higher Level Contractor |  |  |  |  |  |  |
|  |  |  | Approval Signature |  | Date |
| Customer |  |  |  |  |  |  |
|  |  |  | Approval Signature |  | Date |
| Data Management |  |  |  |  |  |
|  |  |  | Signature |  | Date |

| DOCUMENT CHANGE RECORD |
| --- |
| ISSUE N° | DATE | CHANGE AUTHORITY | PAGES AFFECTED | REMARKS |
| 1 | 24/09/2001 |  |  |  |

| LIST OF VALID PAGES |
| --- |
| PAGE | ISSUE N° | PAGE | ISSUE N° | PAGE | ISSUE N° | PAGE | ISSUE N° | PAGE | ISSUE N° |
| 1-1 | 1 |  |  |  |  |  |  |  |  |

Table of contents

1	SCOPE	7

2	APPLICABLE DOCUMENTS	8

3	reference documents	9

4	PARTICIPANTS REQUIRED	10

4.1	General	10

4.2	Responsibility	10

4.3	QA witness of Tests and Sign-off	10

4.4	Non-conformance and failures	10

4.5	Calibration Requirements	10

5	TEST CONDITIONS	11

6	instruments	12

7	Inspection	13

8	SET-UP	15

9	executing test	17

10	TEST SOFTWARE PACKAGE MENUS	59

11	Pin function	61

12	Printouts	64

13	DEVIATION	65

13.1	Procedure variation sheet	65

LIST OF ACRONYMS

| AD# | Applicable Document number # |
| --- | --- |
| ASI | Agenzia Spaziale Italiana |
| ATP | Authorization to proceed |
| CGS | Carlo Gavazzi Space SpA |
| CNR | Consiglio Nazionale delle Ricerche |
| CPP | Coordinated Part Procurement |
| DPU | Data Processing Board |
| DDC | Data Device Corporation |
| DPR | Dual Port Ram |
| EDAC | Error Detector And Corrector |
| EEPROM | Electrically Erasable Programmable Read Only Memory |
| EF | Empty FIFO |
| EM | Engineering Model |
| EPROM | Erasable Programmable Read Only Memory |
| EQM | Engineering Qualification Model |
| FIRST | Far Infra-Red and Sub-millimeter Telescope |
| FF | Full FIFO |
| FM | Flight Model |
| FPGA | Field Programmable Gate Array |
| FS | Flight Spare |
| FSDL | Fast Science Data Link |
| HF | Half Full FIFO |
| HIFI | Heterodyne Instrument for First |
| IFSI | Istituto per la Fisica dello Spazio Interplanetario |
| I/F | Interface |
| LSL | Low Speed Link |
| OBDH | On Board Data Handling |
| PA | Product Assurance |
| PACS | Photoconductor Array Camera and Spectrometer |
| PCB | Printed Circuit Board |
| PROM | Programmable Read Only Memory |
| PL | Payload |
| RAM | Random Access Memory |
| RD# | Reference Document number # |
| SEU | Single Event Upset |
| S/C | Spacecraft |
| SPIRE | Spectral and Photometric Imaging Receiver |
| VDU | Video Device Unit |

# SCOPE

The aim of the present document is to define a procedure to test the EM version of the “Payload & Spacecraft Interface” board to be used in the Data Processing Units, developed in the framework of the HSO/FIRST program. Particularly it must be tested each of the following functions:

- Absence of short-circuits to power supply

- Digital ground to analog ground insulation

- Power consumption

- Power-On Reset generation.

- External Hardware Reset generation

- Control Logic Reset generation

7.a	Fast Science Data Link interfaces (FSDL) (Only for HIFI)

7.b	Fast Science Data Link interfaces (FSDL) (Only for SPIRE)

8.a	Low Speed Link interface (LSL) (Only for HIFI)

8.b	Low Speed Link interface (LSL) (Only for SPIRE)

9.	Analog inputs

- MIL-STD-1553 Clock generation

- MIL-STD-1553 interface

- Control Logic Status Register

With reference to point 11, it must be emphasized that this test procedure covers only MIL-STD-1553 functional tests, without covering any verification aspect included in MIL-HBK-1553.

# APPLICABLE DOCUMENTS

The current issue of the following documents are applicable:

[AD1]:	DPU-SP-CGS-002 "Payload & Spacecraft Interface Board Specification"

[AD2]:       DPU-PL-CGS-001 “Product Assurance Plan for FIRST-DPU”

# reference documents

To test the board the user needs the current issue of the following documents:

[RD1]:	Radiation Tolerant 32/40-BIT IEEE Floating Point DSP Microprocessor Data Book 	Temic

[RD2]:		DPU-SP-CGS-001 “First CPU Board Specification”

[RD3]:	Space Level MIL-STD-1553 BC/RT/MT Advanced Communication Engine Terminal BU-61582 Data Book 	ILC Data Device Corporation 1995

[RD4]:	MIL-STD-1553 BC/RT/MT Advance Communication Engine (ACE) Data Book  ILC Data Device Corporation

[RD5]:	ACE/Mini-ACE Series BC/RT/MT Advanced Communication Engine Integrated 1553 Terminal… User's Guide  ILC Data Device Corporation

# PARTICIPANTS REQUIRED

## General

All tests shall be performed under QA surveillance in accordance with and following detailed procedure of CGS PA Plan [AD2].

The test shall be notified to the Customer as applicable.

## Responsibility

The technical responsibilities for testing and test results is of the Engineering department.

Project and test managers are responsible for the test program. The test engineer is responsible for the correct execution of the test program and for the fulfilment of the requirements, for measurement and recording and for the preparation of the test report.

QA is responsible for ensuring that all the agreed procedures are carefully observed, that test equipment and instrumentation used during testing are calibrated and within validity date, that the test results are recorded in the relative Test Report and signed by the operators and QA witness, that all non conforming condition and test results are properly documented and notified to the customer and that all requirements of applicable PA Plan, Specification and Statement Of Work pertaining to the acceptance tests, are fully satisfied.

## QA witness of Tests and Sign-off

QA inspector shall witness all tests described in this procedure and shall sign the test data sheet

## Non-conformance and failures

Any malfunction occurred during the tests shall be processed according to the Non-Conformance Procedure.

## Calibration Requirements

All instruments used for testing shall be calibrated.

Evidence of certification shall be provided by a label attached to the instruments itself, showing the calibration date, the expire date and the signature of the operator.

# TEST CONDITIONS

-	The Unit shall be tested in its defined configuration: it shall be properly mounted, all the electrical loads (if any) shall be present and the unit interface function(s) shall be simulated.

-  Unless otherwise specified, all the measurements are to be performed at the 
     following ambient conditions:

-	Temperature :		22°C ±3°C

-	Relative humidity: 		55% ±10% RH

-	Pressure	: 		Ambient

-	Cleanliness   :         	           NA

-	All tests, unless otherwise specified, shall be performed internally to CGS laboratories in a proper area.

General disposition shall be applied to maximise personnel safety from potential hazards.

-	Connectors savers shall be used to protect the Unit Under Test (UUT) interface connectors.

-   Skilled personnel shall be employed.

-	All used instruments shall meet the necessary accuracy and shall not degrade the UUT performance.

# instruments

The complete list of the instruments used during the test shall be reported in the following table. The list shall be filled up during tests and reported in Test Report.

| PROJECT: HSO/FIRST-DPU |  |
| --- | --- |
| N. | EQUIPMENT | MANUFACTURER | P/N | S/N | ACCURACY | NEXT CAL. DATE | REMARKS |

# Inspection

Before starting, the user has to check the correct setup of the board as depicted in the Picture 8-1 and verify that no short circuits are present.

# SET-UP

Connect the board as in Fig. 8-1.

Fig. 8-1

Regulate the power supply current limit follow the next table.

| VOLTAGE | LIMIT CURRENT [A] |
| --- | --- |
| +15V | 0.200 |
| -15V | 4.00 |
| +5V | 0.500 |
| +5VBU61582 | 0.900 |
| +VFIFO | 0.200 |
| +2.5V | 0.200 |

Start the program PSI-S000 Test Software Package.

# executing test

In this chapter the steps that the user has to follow are presented.

| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| --- | --- |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 1. | Check absence of shortcircuits to power supply. |  |  |  |
| 1.1 | Connect a ohmmeter between +15V and AGND (connector P1 pin C31 and P1 pin C30); measure the resistance. | >1 K( |  |  |
| 1.2 | Connect a ohmmeter between –15V and AGND (connector P1 pin C30 and P1 pin C30); measure the resistance. | >0.5 K( |  |  |
| 1.3 | Connect a ohmmeter between +5V and DGND (connector P1 pin C1 and P1 pin C32); measure the resistance. | >1 K( |  |  |
| 1.4 | Connect a ohmmeter between +2.5V and DGND (connector P1 pin C2 and P1 pin C32); measure the resistance. | >1 K( |  |  |
| 1.5 | Connect a ohmmeter between +5VBU61582 and DGND (connector P1 pin B2 and P1 pin C32); measure the resistance. | >1 K( |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 1.6 | Connect a ohmmeter between +VFIFO and DGND (connector P1 pin B2 and P1 pin C32); measure the resistance. | >1 K( |  |  |
| 2. | Check digital ground to analog ground insulation. |  |  |  |
| 2.1 | Connect a ohmmeter between DGND and AGND (connector P1 pin C32 and P1 pin C30); measure the resistance. | > 1 M( |  |  |
| 3. | Check power consumption. |  |  |  |
| 3.1 | Connect the board to the power supply inserting the amperemeter in series to the +15V power supply. |  |  |  |
| 3.2 | Supply electrical power to the board. |  |  |  |
| 3.3 | Measure the current. | < 0.120 A |  |  |
| 3.4 | Power off the board. |  |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 3.5 | Connect the board to the power supply inserting the amperemeter in series to the -15V power supply. |  |  |  |
| 3.6 | Supply electrical power to the board. |  |  |  |
| 3.7 | Measure the current. | < 3.780 A |  |  |
| 3.8 | Power off the board. |  |  |  |
| 3.9 | Connect the board to the power supply inserting the amperemeter in series to the +5V power supply. |  |  |  |
| 3.10 | Supply electrical power to the board. |  |  |  |
| 3.11 | Measure the current. | < 0.4 A |  |  |
| 3.12 | Power off the board. |  |  |  |
| 3.13 | Connect the board to the power supply inserting the amperemeter in series to the +VFIFO power supply. |  |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 3.14 | Supply electrical power to the board. |  |  |  |
| 3.15 | Measure the current. | < 0.1 A |  |  |
| 3.16 | Connect the board to the power supply inserting the amperemeter in series to the +2.5V power supply. |  |  |  |
| 3.17 | Supply electrical power to the board. |  |  |  |
| 3.18 | Measure the current. | < 0.1 A |  |  |
| 3.19 | Power off the board. |  |  |  |
| 3.20 | Power off the board. |  |  |  |
| 3.21 | Connect the board to the power supply inserting the amperemeter in series to the +5VBU61582 power supply. |  |  |  |
| 3.22 | Supply electrical power to the board. |  |  |  |
| 3.23 | Measure the current. | < 0.7 A |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 3.24 | Power off the board. |  |  |  |
| 4. | Check Power-On Reset generation. |  |  |  |
| 4.1 | Connect the probe channel 1 of the digital scope to the RES_1553 signal CN1 pin 36. Select positive slope trigger on CH1. Set acquisition mode NORMAL. |  |  |  |
| 4.2 | Power_on the board. |  |  |  |
| 4.3 | Verify the negative pulse width. | > 20 mS |  |  |
| 4.4 | Annex the printout of the waveform to the test report. |  |  |  |
| 5. | Check External Hardware Reset generation. |  |  |  |
| 5.1 | Connect the probe channel 1 of the digital scope to the /RES_1553 signal CN1 pin 36. Set acquisition mode AUTO. |  |  |  |
| 5.2 | Select from the main menu “1) HW Reset Board” |  |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 5.3 | Verify the level of the /RES_1553 signal. | Low |  |  |
| 5.4 | Hit a key on the keyboard of the PC. |  |  |  |
| 5.5 | Verify the level of the /RES_1553 signal. | High |  |  |
| 6. | Check Control Logic. |  |  |  |
| 6.1 | Select from the main menu “2) Reset Board” |  |  |  |
| 6.2 | Connect the probe channel 1 of the digital scope to the /FS0_RS signal U17 pin 22. Set acquisition mode AUTO. |  |  |  |
| 6.3 | Select from the menu “1) FSDL0 Reset” |  |  |  |
| 6.4 | Verify the level of the /FS0_RS signal. | Low |  |  |
| 6.5 | Hit a key on the keyboard of the PC. |  |  |  |
| 6.6 | Verify the level of the /FS0_RS signal. | High |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 6.7 | Connect the probe channel 1 of the digital scope to the /FS1_RS signal U16 pin 22. Set acquisition mode AUTO. |  |  |  |
| 6.8 | Select from the menu “2) FSDL1 Reset” |  |  |  |
| 6.9 | Verify the level of the /FS1_RS signal. | Low |  |  |
| 6.10 | Hit a key on the keyboard of the PC. |  |  |  |
| 6.11 | Verify the level of the /FS1_RS signal. | High |  |  |
| 6.12 | Connect the probe channel 1 of the digital scope to the /FS2_RS signal U24 pin 22. Set acquisition mode AUTO. |  |  |  |
| 6.13 | Select from the menu “3) FSDL2 Reset” |  |  |  |
| 6.14 | Verify the level of the /FS2_RS signal. | Low |  |  |
| 6.15 | Hit a key on the keyboard of the PC. |  |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 6.16 | Verify the level of the /FS2_RS signal. | High |  |  |
| 6.17 | Connect the probe channel 1 of the digital scope to the /FS3_RS signal U23 pin 22. Set acquisition mode AUTO. |  |  |  |
| 6.18 | Select from the menu “4) FSDL3 Reset” |  |  |  |
| 6.19 | Verify the level of the /FS3_RS signal. | Low |  |  |
| 6.20 | Hit a key on the keyboard of the PC. |  |  |  |
| 6.21 | Verify the level of the /FS3_RS signal. | High |  |  |
| 6.22 | Connect the probe channel 1 of the digital scope to the /RES_1553 signal CN1 pin 36. Set acquisition mode AUTO. |  |  |  |
| 6.23 | Select from the menu “5) MIL1553 Reset” |  |  |  |
| 6.24 | Verify the level of the /RES_1553 signal. | Low |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 6.25 | Hit a key on the keyboard of the PC. |  |  |  |
| 6.26 | Verify the level of the /RES_1553 signal. | High |  |  |
| 6.27 | Connect the probe channel 1 of the digital scope to the /FS0_RS, /FS1_RS, /FS2_RS, /FS3_RS and /RES_1553 signals, respectively U17, U16, U24 and U23 pin 22 and CN1 pin 36. Set acquisition mode AUTO. |  |  |  |
| 6.28 | Select from the menu “7) Software Reset” |  |  |  |
| 6.29 | Verify the level of all the /FS0_RS, /FS1_RS, /FS2_RS, /FS3_RS and /RES_1553 signals. | Low |  |  |
| 6.30 | Hit a key on the keyboard of the PC. |  |  |  |
| 6.31 | Verify the level of all the /FS0_RS, /FS1_RS, /FS2_RS, /FS3_RS and /RES_1553 signal. | High |  |  |
| 6.32 | Select from the menu “8) Return to the Main Menu” |  |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 7.a | Check Fast Science Data Link Interfaces. (Only for HIFI) |  |  |  |
| 7.a.1 | Select from the main menu “3) FSDL interfaces” |  |  |  |
| 7.a.2 | Connect the probe channel 1 of the digital scope to the FGATE0 signal U9 pin 3. |  |  |  |
| 7.a.3 | Connect the probe channel 2 of the digital scope to the FCLK0 signal U11 pin 3. |  |  |  |
| 7.a.4 | Connect the probe channel 3 of the digital scope to the FDATA signal U14 pin 3. |  |  |  |
| 7.a.5 | Set trigger to the channel 1 positive slope. Set acquisition mode NORMAL. |  |  |  |
| 7.a.6 | Connect the +/- FGATE signal from the test jig to the terminals +/- FGATE0 to the connector P2 pin B2-B3. |  |  |  |
| 7.a.7 | Connect the +/- FCLK signal from the test jig to the terminals +/- FCLK0 to the connector P2 pin A2-A3. |  |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 7.a.8 | Connect the +/- FDATA signal from the test jig to the terminals +/- FDATA to the connector P2 pin C2-C3. |  |  |  |
| 7.a.9 | Select from the menu “2) Send single data”. Select (H) for HIFI. |  |  |  |
| 7.a.10 | Verify that the waveforms are as despicted in Fig 7.a-1. |  |  |  |
| 7.a.11 | Annex the printout of the waveform to the test report. |  |  |  |
| 7.a.12 | Select from the menu “1) Reset all FSDL interfaces” |  |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |

Fig 7.a.1

| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| --- | --- |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 7.a.13 | Select from the menu “3) Send data packet”. Select (H) for HIFI. |  |  |  |
| 7.a.14 | Select from the menu “6) Read all data” and select ch 0 |  |  |  |
| 7.a.15 | Verify the data printed on the VDU of the PC. | Data with nibbles increasing from 0x00111111 to 0x00AAAAAA |  |  |
| 7.a.16 | Execute the hardcopy of the screen and annex to the test report |  |  |  |
| 7.a.17 | Connect the probe channel 1 of the digital scope to the /IRQM3 signal CN1 pin 13. |  |  |  |
| 7.a.18 | Set trigger to the channel 1 negative slope. Set acquisition mode NORMAL. |  |  |  |
| 7.a.19 | Select from the menu “4) Send half FIFO data packet”. Select (H) for HIFI. |  |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 7.a.20 | Verify the negative pulse width on /IRQM3. | >150 nS |  |  |
| 7.a.21 | Select from the menu “4) Send half FIFO data packet”. Select (H) for HIFI. |  |  |  |
| 7.a.22 | Select from the menu “2) Send single data”. Select (H) for HIFI. |  |  |  |
| 7.a.23 | Select from the menu “5) Read single data”, select ch 0 |  |  |  |
| 7.a.24 | Verify the bit 31 of the data printed on the VDU of the PC is one (1). | Data 0x80F0F0F0 |  |  |
| 7.a.25 | Select from the menu “1) Reset all FSDL interfaces” |  |  |  |
| 7.a.26 | Select from the menu “5) Read single data”. Select ch 0 |  |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 7.a.27 | Verify the bit 30 of the data printed on the VDU of the PC is one (1). | Data 0x40XXXXXX X = don’t care |  |  |
| 7.a.28 | Repeat the steps from 7.2 to 7.23 using signals FGATE1 (U9 pin 5), FCLK1 (U11 pin 5), FDATA1 (U14 pin 5) and /IRQM4 (CN1 pin 14), select channel 1;connect test jig signals FCLK1+/- on connector P2 A4 and A5, FGATE1+/- B4 and B5, FDATA1+/- C4 and C5. | OK |  |  |
| 7.a.29 | Repeat the steps from 7.2 to 7.23 using signals FGATE2 (U9 pin 11), FCLK2 (U11 pin 11), FDATA2 (u14 pin 11) and /IRQM5 (CN1 pin 15), select channel 2; connect the test jig signals FCLK2+/- on the connector P2 A6 and A7, FGATE2+/- B6 and B7, FDATA2+/- C6 and C7. | OK |  |  |
| 7.a.30 | Repeat the steps from 7.2 to 7.23 using signals FGATE3 (U9 pin 13), FCLK3 (U11 pin 13), FDATA3 (u14 pin 13) and /IRQM6 (CN1 pin 16), select channel 3; connect the test jig signals FCLK3+/- on the connector P2 A8 and A9, FGATE3+/- B8 and B9, FDATA3+/- C8 and C9. | OK |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 7.b | Check fast science data link interfaces (Only for SPIRE) |  |  |  |
| 7.b.1 | Select from the main menu “3) FSDL interfaces” |  |  |  |
| 7.b.2 | Connect the probe channel 1 of the digital scope to the FGATE0 signal U9 pin 3. |  |  |  |
| 7.b.3 | Connect the probe channel 2 of the digital scope to the FCLK0 signal U11 pin 3. |  |  |  |
| 7.b.4 | Connect the probe channel 3 of the digital scope to the FDATA signal U14 pin 3. |  |  |  |
| 7.b.5 | Set trigger to the channel 1 positive slope. Set acquisition mode NORMAL. |  |  |  |
| 7.b.6 | Connect the +/- FGATE signal from the test jig to the terminals +/- FGATE0 to the connector P2 pin B2-B3. |  |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 7.b.7 | Connect the +/- FCLK signal from the test jig to the terminals +/- FCLK0 to the connector P2 pin A2-A3. |  |  |  |
| 7.b.8 | Connect the +/- FDATA signal from the test jig to the terminals +/- FDATA to the connector P2 pin C2-C3. |  |  |  |
| 7.b.9 | Select from the menu “2) Send single data”. Select (S) for SPIRE |  |  |  |
| 7.b.10 | Verify that the waveforms are as despicted in Fig 7.b-1. |  |  |  |
| 7.b.11 | Annex the printout of the waveform to the test report. |  |  |  |
| 7.b.12 | Select from the menu “1) Reset all FSDL interfaces” |  |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |

Fig 7.b-1

| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| --- | --- |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 7.b.13 | Select from the menu “3) Send data packet”. Select (S) for SPIRE |  |  |  |
| 7.b.14 | Select from the menu “6) Read all data” and select ch 0 |  |  |  |
| 7.b.15 | Verify the data printed on the VDU of the PC. | Data with nibbles increasing from 0x00FF1111 to 0x00FFAAAA |  |  |
| 7.b.16 | Execute the hardcopy of the screen and annex to the test report |  |  |  |
| 7.b.17 | Connect the probe channel 1 of the digital scope to the /IRQM3 signal CN1 pin 13. |  |  |  |
| 7.b.18 | Set trigger to the channel 1 negative slope. Set acquisition mode NORMAL. |  |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 7.b.19 | Select from the menu “4) Send half FIFO data packet”. Select (S) for SPIRE |  |  |  |
| 7.b.20 | Verify the negative pulse width on /IRQM3. | >150 nS |  |  |
| 7.b.21 | Select from the menu “4) Send half FIFO data packet”. Select (S) for SPIRE. |  |  |  |
| 7.b.22 | Select from the menu “2) Send single data”. Select (S) for SPIRE |  |  |  |
| 7.b.23 | Select from the menu “5) Read single data”; Select ch 0 |  |  |  |
| 7.b.24 | Verify the bit 31 of the data printed on the VDU of the PC is one (1). | Data 0x8000F0F0 |  |  |
| 7.b.25 | Select from the menu “1) Reset all FSDL interfaces” |  |  |  |
| 7.b.26 | Select from the menu “5) Read sigle data”, select ch 0 |  |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 7.b.27 | Verify the bit 30 of the data printed on the VDU of the PC is one (1). | Data 0x40XXXXXX X = don’t care |  |  |
| 7.b.28 | Repeat the steps from 7.2 to 7.23 using signals FGATE1 (U9 pin 5), FCLK1 (U11 pin 5), FDATA1 (U14 pin 5) and /IRQM4 (CN1 pin 14), select channel 1;connect test jig signals FCLK1+/- on connector P2 A4 and A5, FGATE1+/- B4 and B5, FDATA1+/- C4 and C5. | OK |  |  |
| 7.b.29 | Repeat the steps from 7.2 to 7.23 using signals FGATE2 (U9 pin 11), FCLK2 (U11 pin 11), FDATA2 (u14 pin 11) and /IRQM5 (CN1 pin 15), select channel 2; connect the test jig signals FCLK2+/- on the connector P2 A6 and A7, FGATE2+/- B6 and B7, FDATA2+/- C6 and C7. | OK |  |  |
| 7.b.30 | Repeat the steps from 7.2 to 7.23 using signals FGATE3 (U9 pin 13), FCLK3 (U11 pin 13), FDATA3 (u14 pin 13) and /IRQM6 (CN1 pin 16), select channel 3; connect the test jig signals FCLK3+/- on the connector P2 A8 and A9, FGATE3+/- B8 and B9, FDATA3+/- C8 and C9. | OK |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 8.a | Check Low Speed Link Interface |  |  |  |
| 8.a.1 | Select from the main menu “4) LSL interfaces” |  |  |  |
| 8.a.2 | Connect the probe channel 1 of the digital scope to the LCK0+ signal P2 pin A18. |  |  |  |
| 8.a.3 | Connect the probe channel 2 of the digital scope to the LCK0- signal P2 pin A19. |  |  |  |
| 8.a.4 | Connect the probe channel 3 of the digital scope to the LTX0+ signal P2 pin B18 |  |  |  |
| 8.a.5 | Connect the probe channel 4 of the digital scope to the LTX0- signal P2 pin B19 |  |  |  |
| 8.a.6 | Set trigger to the channel 3 positive slope. Set acquisition mode SINGLE. |  |  |  |
| 8.a.7 | Select from the menu “2) Send single data without eco”; Select (H) for HIFI. |  |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 8.a.8 | Verify that the waveforms are as despicted in Fig 8.a-1. |  |  |  |
| 8.a.9 | Annex the printout of the waveform to the test report. |  |  |  |
| 8.a.10 | Repeat the steps from 8.2 to 8.9 using signals LCK1 (P2 pin A20, A21) and LTX1 (P2 pin B20, B21). | OK |  |  |
| 8.a.11 | Repeat the steps from 8.2 to 8.9 using signals LCK2 (P2 pin A22, A23) and LTX2 (P2 pin B22, B23). | OK |  |  |
| 8.a.12 | Repeat the steps from 8.2 to 8.9 using signals LCK3 (P2 pin A24, A25) and LTX3 (P2 pin B24, B25). | OK |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |

Fig. 8.a-1

| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| --- | --- |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 8.a.13 | Repeat the steps from 8.2 to 8.9 using signals LCK4 (P2 pin A26, A27) and LTX4 (P2 pin B26, B27). | OK |  |  |
| 8.a.14 | Repeat the steps from 8.2 to 8.9 using signals LCK5 (P2 pin A28, A29) and LTX5 (P2 pin B28, B29). | OK |  |  |
| 8.a.15 | Repeat the steps from 8.2 to 8.9 using signals LCK6 (P2 pin A30, A31) and LTX6 (P2 pin B30, B31). | OK |  |  |
| 8.a.16 | Connect the probe channel 1 of the digital scope to the LCK0+ signal P2 pin A18. |  |  |  |
| 8.a.17 | Connect the probe channel 2 of the digital scope to the LCK0- signal P2 pin A19. |  |  |  |
| 8.a.18 | Connect the Test Jig outputs to the LRX0+ signal P2 pin C18 and to the LRX0- signal P2 pin C19. |  |  |  |
| 8.a.19 | Connect the probe channel 3 of the digital scope to the LRX0 signal U8 pin 3 |  |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 8.a.20 | Select from the menu “3) Send single data with eco”; Select (H) for HIFI. |  |  |  |
| 8.a.21 | Verify that the waveforms are as despicted in Fig 8.a-2. |  |  |  |
| 8.a.22 | Annex the printout of the waveform to the test report. |  |  |  |
| 8.a.23 | Select from the menu “5) Read Status Register” |  |  |  |
| 8.a.24 | Verify the bit 1 of the data printed on the VDU of the PC is one (1) “data ready” | Data 0x0002 |  |  |
| 8.a.25 | Select from the menu “4) Read Data” | Data 0x800055aa |  |  |
| 8.a.26 | Select from the menu “5) Read Status Register” |  |  |  |
| 8.a.27 | Verify the bit 1of the data printed on the VDU of the PC is one (0) “data not ready” | Data 0x0000 |  |  |
| 8.a.28 | Repeat the steps from 8.18 to 8.27 using signals LRX1 (P2 pin C20, C21). | OK |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |

Fig. 8.a-2

| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| --- | --- |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 8.a.29 | Repeat the steps from 8.18 to 8.27 using signals LRX2 (P2 pin C22, C23). | OK |  |  |
| 8.a.30 | Select from the menu “6) Timeout Check” |  |  |  |
| 8.a.31 | Verify the output messges printed on the VDU of the PC. | TX Busy bit set… Ok Send request… Ok HK pending bit set… Ok Timeout bit set… Ok |  |  |
| 8.a.32 | Select from the menu “T) Abort Check” |  |  |  |
| 8.a.33 | Verify the output messges printed on the VDU of the PC. | TX Busy bit set… Ok Send request… Ok HK pending bit set… Ok Send request… Ok HK Aborted bit set… Ok |  |  |
| 8.b | Check Low Speed Link Interface |  |  |  |
| 8.b.1 | Select from the main menu “4) LSL interfaces” |  |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 8.b.2 | Connect the probe channel 1 of the digital scope to the LCK0+ signal P2 pin A8. |  |  |  |
| 8.b.3 | Connect the probe channel 2 of the digital scope to the LCK0- signal P2 pin A19. |  |  |  |
| 8.b.4 | Connect the probe channel 3 of the digital scope to the LTX0+ signal P2 pin B18 |  |  |  |
| 8.b.5 | Connect the probe channel 4 of the digital scope to the LTX0- signal P2 pin B19 |  |  |  |
| 8.b.6 | Set trigger to the channel 3 positive slope. Set acquisition mode SINGLE. |  |  |  |
| 8.b.7 | Select from the menu “2) Send single data without eco”; Select (S) for SPIRE. |  |  |  |
| 8.b.8 | Verify that the waveforms are as despicted in Fig 8.b-1. |  |  |  |
| 8.b.9 | Annex the printout of the waveform to the test report. |  |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 8.b.10 | Repeat the steps from 8.2 to 8.9 using signals LCK1 (P2 pin A20, A21) and LTX1 (P2 pin B20, B21). | OK |  |  |
| 8.b.11 | Repeat the steps from 8.2 to 8.9 using signals LCK2 (P2 pin A22, A23) and LTX2 (P2 pin B22, B23). | OK |  |  |
| 8.b.12 | Repeat the steps from 8.2 to 8.9 using signals LCK3 (P2 pin A24, A25) and LTX3 (P2 pin B24, B25). | OK |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |

Fig. 8.b-1

| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| --- | --- |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 8.b.13 | Repeat the steps from 8.2 to 8.9 using signals LCK4 (P2 pin A26, A27) and LTX4 (P2 pin B26, B27). | OK |  |  |
| 8.b.14 | Repeat the steps from 8.2 to 8.9 using signals LCK5 (P2 pin A28, A29) and LTX5 (P2 pin B28, B29). | OK |  |  |
| 8.b.15 | Repeat the steps from 8.2 to 8.9 using signals LCK6 (P2 pin A30, A31) and LTX6 (P2 pin B30, B31). | OK |  |  |
| 8.b.16 | Connect the probe channel 1 of the digital scope to the LCK0+ signal P2 pin A8. |  |  |  |
| 8.b.17 | Connect the probe channel 2 of the digital scope to the LCK0- signal P2 pin A19. |  |  |  |
| 8.b.18 | Connect the Test Jig outputs to the LRX0+ signal P2 pin C18 and to the LRX0- signal P2 pin C19. |  |  |  |
| 8.b.19 | Connect the probe channel 3 of the digital scope to the LRX0 signal U8 pin 3 |  |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 8.b.20 | Select from the menu “3) Send single data with eco”; Select (S) for SPIRE. |  |  |  |
| 8.b.21 | Verify that the waveforms are as despicted in Fig 8.b-2. |  |  |  |
| 8.b.22 | Annex the printout of the waveform to the test report. |  |  |  |
| 8.b.23 | Select from the menu “5) Read Status Register” |  |  |  |
| 8.b.24 | Verify the bit 1 of the data printed on the VDU of the PC is one (1) “data ready” | Data 0x0002 |  |  |
| 8.b.25 | Select from the menu “4) Read Data” | Data 0x85aa55aa |  |  |
| 8.b.26 | Select from the menu “5) Read Status Register” |  |  |  |
| 8.b.27 | Verify the bit 1of the data printed on the VDU of the PC is one (0) “data not ready” | Data 0x0000 |  |  |
| 8.b.28 | Repeat the steps from 8.18 to 8.27 using signals LRX1 (P2 pin C20, C21). | OK |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |

Fig. 8.b-2

| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| --- | --- |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 8.b.29 | Repeat the steps from 8.18 to 8.27 using signals LRX2 (P2 pin C22, C23). | OK |  |  |
| 9. | Check Analog inputs. |  |  |  |
| 9.1 | Connect the return of the Power Supply to the AGND signal P” pin A11. |  |  |  |
| 9.2 | Select from the main menu “5) Analog inputs” |  |  |  |
| 9.3 | Set the output of the Power supply to 100 mV. |  |  |  |
| 9.4 | Using the multimeter measure the output voltage of the Power Supply. | 100 mV |  |  |
| 9.5 | Connect the output signal to the AINP input P2 pin A10 and short to AGND all the unused Analog inputs. |  |  |  |
| 9.6 | Hit a key on the keyboard of the PC. |  |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 9.7 | Repeat the steps from 9.5 to 9.6 using signals AINP1, AINP2, AINP3, AINP4, AINP5 and AINP6 (P2 pin B10, C10, A12, B12, C12 and A14). |  |  |  |
| 9.8 | Execute the hardcopy of the screen and annex then output table to the test report. |  |  |  |
| 9.9 | Set the output of the Power supply to 2.5 V. |  |  |  |
| 9.10 | Using the multimeter measure the output voltage of the Power Supply. | 2.5 V |  |  |
| 9.11 | Connect the output signal to the AINP input P2 pin A10 and short to AGND all the unused Analog inputs. |  |  |  |
| 9.12 | Hit a key on the keyboard of the PC. |  |  |  |
| 9.13 | Repeat the steps from 9.11 to 9.12 using signals AINP1, AINP2, AINP3, AINP4, AINP5 and AINP6 (P2 pin B10, C10, A12, B12, C12 and A14). |  |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 9.14 | Execute the hardcopy of the screen and annex then output table to the test report. |  |  |  |
| 9.15 | Set the output of the Power supply to 4.9 V. |  |  |  |
| 9.16 | Using the multimeter measure the output voltage of the Power Supply. | 4.9 V |  |  |
| 9.17 | Connect the output signal to the AINP input P2 pin A10 and short to AGND all the unused Analog inputs. |  |  |  |
| 9.18 | Hit a key on the keyboard of the PC. |  |  |  |
| 9.19 | Repeat the steps from 9.17 to 9.18 using signals AINP1, AINP2, AINP3, AINP4, AINP5 and AINP6 (P2 pin B10, C10, A12, B12, C12 and A14). |  |  |  |
| 9.20 | Execute the hardcopy of the screen and annex then output table to the test report. |  |  |  |
| 10. | Check MIL-STD-1553 Clock generation |  |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 10.1 | Connect the probe channel 4 of the digital scope to the LTX0- signal P2 pin B19 |  |  |  |
| 10.2 | Verify the clock frequency. | 16 MHz ( 1% |  |  |
| 10.3 | Annex the printout of the waveform to the test report. |  |  |  |
| 11. | Check MIL-STD-1553 interface. |  |  |  |
| 11.1 | Start the program “BC STD-1553 Simulator”. |  |  |  |
| 11.2 | Select from the main menu “6) MIL-1553 interface”. |  |  |  |
| 11.3 | Select from the menu 1)”Configurate the unit as RT “. |  |  |  |
| 11.4 | Using ”BC STD-1553” SW Package. Send one interrogation. |  |  |  |
| 11.5 | Select from the menu”2) Read the interrogation”. |  |  |  |
| 11.6 | Verify the output messages printed on the VDU of the PC. | 1553 interface OK |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 11.7 | Select from the menu “3) Send response”. |  |  |  |
| 11.8 | Using “BC STD-1553” SW package Read response. |  |  |  |
| 11.9 | Verify the response is correctly read by the “BC STD-1553” SW package . | Ok |  |  |
| 12. | Check Control Logic Status Register. |  |  |  |
| 12.1 | Select from the main menu “7) Status Register” |  |  |  |
| 12.2 | Verify the output messages printed on the VDU of the PC. | FSDL interfaces reset Ok FSDL0 EF bit set.. Ok FSDL1 EF bit set.. Ok FSDL2 EF bit set.. Ok FSDL3 EF bit set.. Ok |  |  |
| 12.3 | Connect the Test Jigs FSDL outputs to the FSDL0 interface signals. |  |  |  |
| 12.4 | Hit a key on the keyboard of the PC. |  |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 12.5 | Verify the output messages printed on the VDU of the PC. | FSDL0 HF bit reset.. Ok Send half FIFO data … Ok FSDL0 HF bit set.. Ok FSDL0 FF bit reset.. Ok Send half FIFO data … Ok FSDL0 FF bit set.. Ok |  |  |
| 12.6 | Connect the Test Jigs FSDL outputs to the FSDL1 interface signals. |  |  |  |
| 12.7 | Hit a key on the keyboard of the PC. |  |  |  |
| 12.8 | Verify the output messages printed on the VDU of the PC. | FSDL1 HF bit reset.. Ok Send half FIFO data … Ok FSDL1 HF bit set.. Ok FSDL1 FF bit reset.. Ok Send half FIFO data … Ok FSDL1 FF bit set.. Ok |  |  |
| 12.9 | Connect the Test Jigs FSDL outputs to the FSDL2 interface signals. |  |  |  |
| 12.10 | Hit a key on the keyboard of the PC. |  |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |
| TITLE: PAYLOAD & SPACECRAFT INTERFACE BOARD TEST PROCEDURE | UNIT UNDER TEST: S/N: |
| STEP N° | TEST SEQUENCE | EXPECTED VALUE | MEASURED VALUE | REMARKS |
| 12.11 | Verify the output messages printed on the VDU of the PC. | FSDL2 HF bit reset.. Ok Send half FIFO data … Ok FSDL2 HF bit set.. Ok FSDL2 FF bit reset.. Ok Send half FIFO data … Ok FSDL2 FF bit set.. Ok |  |  |
| 12.12 | Connect the Test Jigs FSDL outputs to the FSDL3 interface signals. |  |  |  |
| 12.13 | Hit a key on the keyboard of the PC. |  |  |  |
| 12.14 | Verify the output messages printed on the VDU of the PC. | FSDL3 HF bit reset.. Ok Send half FIFO data … Ok FSDL3 HF bit set.. Ok FSDL3 FF bit reset.. Ok Send half FIFO data … Ok FSDL3 FF bit set.. Ok |  |  |
| DATE | TEST CONDUCTOR | PRODUCT ASSURANCE | CUSTOMER |

# TEST SOFTWARE PACKAGE MENUS

Main menu:

- HW Reset Board

- Reset Board

- FSDL interfaces

- LSL interfaces

- Analog inputs

- MIL-1553 interface

- Status Register

Reset Board:

- FSDL0 Reset

- FSDL1 Reset

- FSDL2 Reset

- FSDL3 Reset

- MIL1553 Reset

- LSL Reset

- Software Reset

- Return to the Main Menu

FSDL interfaces:

- Reset all FSDL interfaces

- Send single data

- Send data packet

- Send half FIFO data packet

- Read single data

- Read all data

LSL interfaces:

- Reset LSL interface

- Send single data without eco

- Send single data with eco

- Read Data

- Read Status Register

- Timeout check

- Abort Check

Analog inputs:

Not submenu are present.

MIL-1553 interface:

1)	Configurate the unit as RT.

2)	Read the interrogation.

3)	Send response.

Status Register:

Not submenu are present.

# Pin function

The pin function of the PL I/F board is shown in the Table 11-1 and Table 11-2 and Table 3.

| Pin # | Signal | Pin # | Signal | Pin # | Signal |
| --- | --- | --- | --- | --- | --- |
| 1 | +5VD | 33 | +5VD | 65 | +5VD |
| 2 | +VFIFO | 34 | +5VBU61582 | 66 | +VFPGA |
| 3 | D0 | 35 | D1 | 67 | D2 |
| 4 | D3 | 36 | D4 | 68 | D5 |
| 5 | D6 | 37 | D7 | 69 | D8 |
| 6 | D9 | 38 | D10 | 70 | D11 |
| 7 | D12 | 39 | D13 | 71 | D14 |
| 8 | D15 | 40 | D16 | 72 | D17 |
| 9 | D18 | 41 | D19 | 73 | D20 |
| 10 | D21 | 42 | D22 | 74 | D23 |
| 11 | D24 | 43 | D25 | 75 | D26 |
| 12 | D27 | 44 | D28 | 76 | D29 |
| 13 | D30 | 45 | D31 | 77 | \WR |
| 14 | A0 | 46 | A1 | 78 | A2 |
| 15 | A3 | 47 | A4 | 79 | A5 |
| 16 | A6 | 48 | A7 | 80 | A8 |
| 17 | DGND | 49 | SACK | 81 | DGND |
| 18 | A9 | 50 | A10 | 82 | A11 |
| 19 | A12 | 51 | A13 | 83 | A14 |
| 20 | A15 | 52 | A16 | 84 | A17 |
| 21 | A18 | 53 | A19 | 85 | A20 |
| 22 | A21 | 54 | A22 | 86 | A23 |
| 23 | \CS0 | 55 | \CS1 | 87 | \CS2 |
| 24 | \CS3 | 56 | \CS4 | 88 | \CS5 |
| 25 | RESERVED | 57 | \CS7 | 89 | \RD |
| 26 | IRQM3 | 58 | IRQM4 | 90 | IRQM5 |
| 27 | IRQM6 | 59 | IRQM7 | 91 | SYSCLK |
| 28 | \SYSRESETIN | 60 | RESERVED | 92 | SYSCLK |
| 29 | -15VA | 61 | -15VA | 93 | -15VA |
| 30 | AGND | 62 | AGND | 94 | AGND |
| 31 | +15VA | 63 | +15VA | 95 | +15VA |
| 32 | DGND | 64 | DGND | 96 | DGND |

Table 11-1 PL I/F board: P1 pin function

| Pin # | Signal | Pin # | Signal | Pin # | Signal |
| --- | --- | --- | --- | --- | --- |
| 1 | +5VD | 33 | RESERVED | 65 | +5VD |
| 2 | FCK0+ | 34 | FGATE0+ | 66 | FDATA0+ |
| 3 | FCK0- | 35 | FGATE0- | 67 | FDATA0- |
| 4 | FCK1+ | 36 | FGATE1+ | 68 | FDATA1+ |
| 5 | FCK1- | 37 | FGATE1- | 69 | FDATA1- |
| 6 | FCK2+ | 38 | FGATE2+ | 70 | FDATA2+ |
| 7 | FCK2- | 39 | FGATE2- | 71 | FDATA2- |
| 8 | FCK3+ | 40 | FGATE3+ | 72 | FDATA3+ |
| 9 | FCK3- | 41 | FGATE3- | 73 | FDATA3- |
| 10 | AINP0 | 42 | AINP1 | 74 | AINP2 |
| 11 | AGND | 43 | AGND | 75 | AGND |
| 12 | AINP3 | 44 | AINP4 | 76 | AINP5 |
| 13 | AGND | 45 | AGND | 77 | AGND |
| 14 | AINP6 | 46 | NOT USED | 78 | NOT USED |
| 15 | AGND | 47 | AGND | 79 | AGND |
| 16 | RTAD0 | 48 | RTAD2 | 80 | RTAD4 |
| 17 | RTAD1 | 49 | RTAD3 | 81 | RTADP |
| 18 | LCK0+ | 50 | LTX0+ | 82 | LRX0+ |
| 19 | LCK0- | 51 | LTX0- | 83 | LRX0- |
| 20 | LCK1+ | 52 | LTX1+ | 84 | LRX1+ |
| 21 | LCK1- | 53 | LTX1- | 85 | LRX1- |
| 22 | LCK2+ | 54 | LTX2+ | 86 | LRX2+ |
| 23 | LCK2- | 52 | LTX2- | 84 | LRX2- |
| 24 | LCK3+ | 53 | LTX3+ | 85 | NOT USED |
| 25 | LCK3- | 54 | LTX3- | 86 | NOT USED |
| 26 | LCK4+ | 58 | LTX4+ | 90 | SCTX/RXA+ |
| 27 | LCK4- | 59 | LTX4- | 91 | SCTX/RXA- |
| 28 | LCK5+ | 60 | LTX5+ | 92 | SCTX/RXB+ |
| 29 | LCK5- | 61 | LTX5- | 93 | SCTX/RXB- |
| 30 | LCK6+ | 62 | LTX6+ | 94 | NOT USED |
| 31 | LCK6- | 63 | LTX6- | 95 | FLAG1 |
| 32 | DGND | 64 | DGND | 96 | DGND |

Table 11-2 PL I/F board: P2 pin function

| Pin # | Signal | Pin # | Signal |
| --- | --- | --- | --- |
| 1 | NOT USED | 20 | /FS0_W2 |
| 2 | NOT USED | 21 | /FS1_W0 |
| 3 | GND | 22 | /FS1_W1 |
| 4 | NOT USED | 23 | /FS1_W2 |
| 5 | LRX0 | 24 | /FS2_W0 |
| 6 | LRX1 | 25 | /FS2_W1 |
| 7 | LRX2 | 26 | /FS2_W2 |
| 8 | LCK | 27 | /FS3_W0 |
| 9 | LTX | 28 | /FS3_W1 |
| 10 | /WR | 29 | /FS3_W2 |
| 11 | /RD | 30 | /IN_CMD |
| 12 | SACK | 31 | /READYD |
| 13 | /IRQM3 | 32 | TAG_CLK |
| 14 | /IRQM4 | 33 | /SELECT |
| 15 | /IRQM5 | 34 | RD/WR |
| 16 | /IRQM6 | 35 | /STRB |
| 17 | /IRQM7 | 36 | /RES_1553 |
| 18 | /FS0_W0 | 37 | ADC_BUSY |
| 19 | /FS0_W1 | 38 | READ/CONV_AD |

Table 3 PL I/F board: CN1 pin function

# Printouts

Printouts obtained during the test shall be reported in the test report.

# DEVIATION

In case that for any reason the test procedure has to be changed, the change shall be described in a Procedure Variation Sheet (PVS) attached to this document in Table 13-1.

The PVS shall contain:

-	Reference to the procedure to be changed

-	Reference to the relevant test, procedure page and paragraph

-	Description of the change

-	Reason for change

-	Engineering and QA signature

-	Customer signature (when required).

## Procedure variation sheet

The Procedure Variation Sheet is shown in Table 13-1.

| PROCEDURE VARIATION SHEET |
| --- |
| Test procedure Ref.: | Page revised | Para. revised |
| Description of changes: |
| Reason for changes: |
| CONCURRENCE |
| TEST COND | P.A. | ENG. | CUSTOMER |

Table 13-1