| CARLO GAVAZZI SPACE SpA |  |
| --- | --- |
| DOCUMENT TYPE: SUBSYSTEM TEST PROCEDURE |  |
| TITLE: DC / DC CONVERTER Board Test Procedure |
| DOCUMENT No: DPU-PR-CGS-003 | PAGE: 1 |
| SPIRE-CGS-DOC-001088 |
| ISSUE No: 1 | DATE: 31/08/2001 |
| PREPARED BY: L. VUCETICH |
| APPROVED BY: V CHIAVERINI |
| THIS DOCUMENT IS SUBJECT TO THE APPROVAL OF: |
|  | YES | NO |  |
| Product Assurance | X |  |  |  |  |  |
|  |  |  |  | Approval Signature |  | Date |
| Configuration Control | X |  |  |  |  |  |
|  |  |  |  | Approval Signature |  | Date |
| Project Control |  | X |  |  |  |  |
|  |  |  |  | Approval Signature | Date |
| Engineering | X |  |  |  |  |  |
|  |  |  |  | Approval Signature | Date |
| Managing Director |  | X |  |  |  |  |
|  |  |  |  | Approval Signature | Date |
| CGS Program Manager | X |  |  |  |  |  |
|  |  |  | Approval Signature | Date |
|  | YES | NO |  |  |
| Higher Level Contractor |  |  |  |  |  |  |
|  |  |  | Approval Signature | Date |
| Customer |  |  |  |  |  |  |
|  |  |  | Approval Signature | Date |
| Data Management |  |  |  |  |  |
|  |  |  | Signature | Date |

| DOCUMENT CHANGE RECORD |
| --- |
| ISSUE N° | DATE | CHANGE AUTHORITY | PAGES AFFECTED | REMARKS |
| 1 | 31/08/2001 |  |  | First Emission |

| LIST OF VALID PAGES |
| --- |
| PAGE | ISSUE N° | PAGE | ISSUE N° | PAGE | ISSUE N° | PAGE | ISSUE N° | PAGE | ISSUE N° |
| 1-1 | 1 |  |  |  |  |  |  |  |  |

TABLE OF CONTENTS

1	LIST OF ACRONYMS	6

2	scope	7

3	Documents	9

3.1	APPLICABLE DOCUMENTS	9

3.2	REFERENCE DOCUMENTS	9

4	GENERAL INFORMATION	9

5	TEST EXECUTION	11

5.1	PHYSICAL PROPERTIES VERIFICATION	11

5.2	ELECTRICAL TEST	11

5.2.1	Isolation and grounding	13

5.2.2	Push-Pull Characteristics Waveform	13

5.2.2.1	Fets Gate/Source voltage verification:	13

5.2.2.2	Switching Frequency:	16

5.2.2.3	Fets Drain Voltage and Snubber Verification:	16

5.2.2.4	Primary current limit value:	19

5.2.3	Power consumption	19

5.2.3.1	Power consumption in DPU version:	20

5.2.3.2	Power consumption in DPU+PL version:	20

5.2.4	Output Voltage Stability	21

5.2.4.1	Load regulation (static condition):	21

5.2.4.2	Load Regulation (Transient Condition)	22

5.2.4.3	Line regulation:	26

5.2.5	Ripple And Spikes	27

5.2.6	Efficiency	30

5.2.7	Start-up Verification	31

5.2.7.1	Inrush Current	31

5.2.7.2	Output Voltage soft start	34

5.2.8	Stability Verification	37

5.2.9	Input Impedance	40

5.2.10	Protection Circuitry Verification	44

5.2.10.1	Input Protection	44

5.2.10.2	Output DPU Protections	44

5.2.10.3	Unregulated PL-Outputs Protections	44

5.2.10.4	Regulated PL-Outputs Protections	45

5.2.11	Monitor Verification	46

5.3	THERMAL TEST	47

5.3.1	Low Temperature Test  (-25°)	47

5.3.1.1	Power consumption	47

5.3.1.2	Output Voltage Stability	49

5.3.1.3	Line regulation:	56

5.3.1.4	Efficiency	57

5.3.1.5	Monitors Verification	58

5.3.2	High Temperature Test  (+45°)	59

5.3.2.1	Power consumption	59

5.3.2.2	Power consumption in DPU version:	59

5.3.2.3	Power consumption in DPU+PL version:	59

5.3.2.4	Output Voltage Stability	60

5.3.2.5	Line regulation:	67

5.3.2.6	Efficiency	68

5.3.2.7	Monitors Verification	69

5.4	EMC TEST	70

5.4.1	Conducted Emission on Input Power Line	70

5.4.1.1	CE on Input Power Line, Frequency Domain, Differential Mode, NB	70

5.4.1.2	CE on Input Line, Frequency Domain, Common Mode, NB	77

5.4.1.3	Current Ripple, Time Domain, Differential Mode	81

5.4.2	Conducted Susceptibility from Input Power Line	85

5.4.2.1	CS from Input Power Line, Differential Mode, Steady State	85

5.4.2.2	CS from Input Power Line, Common Mode, Steady State	88

5.4.2.3	CS Common Mode Voltage- Steady State	90

5.4.2.4	CS Common Mode Voltage Transients	91

5.4.2.5	CS from Input Power Line – Transients due to Switching	94

5.4.3	Conducted Emissions on PL-Output Lines	97

5.4.4	Arc Discharge Susceptibility	97

5.5	VIBRATION TEST     Input Protections	97

6	Pin function	97

7	conclusion	100

# LIST OF ACRONYMS

| AD# | Applicable Document Number |
| --- | --- |
| BB | Broadband |
| CE | Conducted Emission |
| CS | Conducted Susceptibility |
| DPU | Data Processing Unit |
| EMC | Electro-Magnetic Compatibility |
| EMI | Electro-Magnetic Interference |
| FIRST | Far Infra-Red and Sub-millimeter Telescope |
| FPU | Focal Plane Unit |
| GND | Ground |
| HIFI | Heterodyne Instrument for First |
| HK | House Keeping |
| ICD | Interface Control Document |
| ICU | Instrument Control Unit |
| IID | Instrument Interface Document |
| I/F | Interface |
| LCL | Latching Current Limiter |
| OCP | Over-Current Protection |
| OVP | Over-Voltage Protection |
| NA | Not Applicable |
| NB | Narrowband |
| PA | Product Assurance |
| PACS | Photoconductor Array Camera and Spectrometer |
| PDU | Power Distribution Unit |
| PL | Payload |
| RD# | Reference Document Number |
| RE | Radiated Emission |
| RS | Radiated Susceptibility |
| RTN | Return Line |
| S/C | Spacecraft |
| SPIRE | Spectral and Photometric Imaging receiver |
| TBC | To Be Confirmed |
| TBD | To Be Determined |
| TM/TC | Telemetry & Tele-command |
| uut | Unit Under Test |

# scope

Scope of this document is to define a Test Procedure for Engineering , Qualification and Flight Models of the DC/DC board which shall be used to supply the Data Processing Unit (DPU) of the Payload Instruments HIFI, PACS and SPIRE to be developed in the framework of the FIRST program.

For the payload experiment HIFI only, the DC/DC board, besides the supply of the DPU, shall provide supplying voltages for the HIFI instrument itself. In this case the DC/DC board shall be called, in this document, as “DPU+PL version”.

The DC/DC board devoted to supply the DPU unit only, shall be called, in this document, as “DPU version”.

The sequence of Tests for each model is given in Table 2.1 .

The applicable Test Matrix which defines the applicability of the various tests for each test category is given in Table 2.2 .

| TEST | EM | QM | FM |
| --- | --- | --- | --- |
| Physical properties verification | X | X | X |
| Electrical Test | X | X (1) | X (1) |
| Thermal Test | X (2) | X | X (1) |
| EMC Test | X (1) | X | X ( 1) |
| Vibration Test |  |  |  |

Note:	(1)   Reduced Test   DEFINIRE

Note: 	(2)   These Test are valid only if components with appropriate temperature range are utilized.

TABLE 2.1 – TEST SEQUENCE

|  | TEST | EM | QM | FM |
| --- | --- | --- | --- | --- |
| 5.1 | PHISICAL PROPERTIES VERIFICATION | X | X | X |
| 5.2 | ELECTRICAL TEST | X | X | X |
| 5.2.1 | - Isolation and Grounding | X | X | X |
| 5.2.2 | - Push-Pull characteristics waveform Fet Gate/Source Voltage Switching Frequency Snubber peak voltage Controller primary current limit value and waveform. | X X X X | X X - | X X - |
| 5.2.3 | - Power Consumption | X | X | X |
| 5.2.4 | - Output Voltage Stability Load regulation Line regulation | X X | X X | X X |

TABLE 2.2 – TEST MATRIX

|  | TEST | EM | QM | FM |
| --- | --- | --- | --- | --- |
| 5.2.5 | - Ripple and Spikes | x | x | x |
| 5.2.6 | - Efficiency | x | x | x |
| 5.2.7 | - Start Up Verification Inrush Current Output Voltage soft-start Internal Power Supply Voltage | x x x | x x - | x x - |
| 5.2.8 | - Stability verification | x | x | x |
| 5.2.9 | - Input Impedance | x | x | x |
| 5.2.10 | - Protection Circuitry verification Input protection Output PDU protections Unregulated PL-Outputs Protections Regulated PL-Outputs Protections | x x x x | x x x x | x x x x |
| 5.2.11 | - Monitors Verification Output DC/DC service voltage monitors Temperature monitor | x x | x x | x x |
| 5.3 | THERMAL TEST | - | x | x |
| 5.3.1 | - Low Temperature Test (-25°) Power Consumption Output Voltage Stability Efficiency Monitors Verification | - - - - - | x x x x x | x x x - |
| 5.3.2 5.3.2.1 5.3.2.2 5.3.2.3 5.3.2.4 | - High Temperature Test (+45°) Power Consumption Output Voltage Stability Efficiency Monitors Verification | - - - - - | x x x x x | x x x - |
| 5.4 | EMC TEST | x | x | x |
| 5.4.1 | - Conducted Emission on Input Power Line CE on Input Power Line; Frequency Domain, Differential Mode, NB CE on Input Power Line; Frequency Domain, Common Mode, NB Current Ripple , Time Domain , Differential Mode | x x x | x x x | x x x |
| 5.4.2 | - Conducted Susceptibility from input Power Line CS from Input Power Line ; Differential Mode , Steady State CS from Input Power Line ; Common Mode ; Steady State CS Common Mode Voltage Steady State CS Common Mode Voltage Transient CS from Input Power Line – Transient due to Switching | - - - - - | x x x x x | x x x x x |
| 5.4.3 | - Conducted Emission on PL-Output Lines | - | x | x |
| 5.4.4 | - Arc Discharge Susceptibility | - | - | - |
| 5.5 | VIBRATION TEST | - | x | - |

TABLE 2.2 – TEST MATRIX (continued)

# Documents

The following documents were utilized to write this document:

## APPLICABLE DOCUMENTS

[AD1]:	CNR.IFSI.2000TR01 "Documento di Specifiche Tecniche per il Contratto delle Data Processing Units del Satellite First dell'ESA"    IFSI (Issue: 1 - 15/09/2000)

[AD2]:	Technical proposal CGS (Ref. S9-030 November 99)

[AD3]:	“Allegato Tecnico al Contratto ASI"

[AD4]:	 Product Assurance Plan for the FIRST DPU (DPU-PL-CGS-001 Issue 1 Jan. 2001)

[AD5]:	DC/DC Board Specification DPU-SP-CGS-004

## REFERENCE DOCUMENTS

[RD1] - 	FIRST/Planck Instrument Interface Document Part A. (Ref. SCI-PT-IIDA-04624 Issue-Rev. No. : 1/1)

[RD2] - 	FIRST/Planck Instrument Interface Document Part B - Instrument “HIFI” (Ref. SCI-PT-IIDB/HIFI-02125 Issue-Rev No. : 1/0)

# GENERAL INFORMATION

The DC/DC board ( Push-Pull topologies) must provide a set of supply voltages for to the DPU internal electronics of the payload experiments HIFI, PACS and SPIRE. For the payload experiment HIFI only, the DC/DC board must provide a further external set of supply voltages for the HIFI/FCU unit.

Therefore the board must provide, considering the DPU+PL version, the following two sets of output voltages:

- “DPU-Outputs” to supply the DPU internal electronics

- “PL-Outputs” to supply the payload instrument HIFI/FCU unit.

In the DPU version only the DPU-Outputs shall be provided.

DPU-Outputs and PL-Outputs shall be isolated from primary power side and from each other as described in [AD5]:	DC/DC Board Specification DPU-SP-CGS-004.

The DC/DC board shall switch on automatically when the input voltage is within the range established in [AD5]:DC/DC Board Specification DPU-SP-CGS-004.

Figure 4-1 DC/DC Board functional diagram (“DPU+PL version”)

# TEST EXECUTION

In the following pages the procedures to be used for test execution are described in detail and several form to be filled in are given.

Test sequence has been subdivided into five steps:

- Physical Properties Verification

- Electrical Test

- Thermal Test

- EMC Test

- Vibration Test

## PHYSICAL PROPERTIES VERIFICATION

The DC/DC board shall be located within the DPU.

The DC/DC board is implemented through one Printed Circuit Board.

The mechanical constraints and the measured value are reported in the following Table

| MEASUREMENT | NOMINAL | MEASURED |
| --- | --- | --- |
| Size (DPU+PL version) | Double Euro (160mm x 233.35mm) |  |
| Size (DPU version) | Double Euro (160mm x 233.35mm) |  |
| Overall thickness: (both versions) | 38mm |  |
| Card retainers: | Calmark series 260 |  |
| Connectors (connection to back plane): | 90°, male, DIN41612 type |  |

Table 5-1-1 Board constraints

| MEASUREMENT | NOMINAL | MEASURED |
| --- | --- | --- |
| Overall Weight (DPU+PL version) | (1000gr TBC |  |
| Overall Weight (DPU version) | (750gr TBC |  |

Table 5-1-2 Board weight

## ELECTRICAL TEST

Electrical Test to be perform on the DC/DC converter board are described in detail in this paragraph.

Before test execution complete the table 5-2-1 with instrumentation equipment data.

| Project : | Name for Test : |
| --- | --- |

Equipment required

To check and accomplish before the tests.  To complete eventually during test.

| Label of equipment (c.g.name) | Manufact. Type | Inventur No. | Next Calibration date | Accuracy | Remarks |
| --- | --- | --- | --- | --- | --- |

TABLE 5-2-1 – instrumentation equipment data

### Isolation and grounding

The Power return lines DGND and AGND shall be connected into the DC/DC board

When the output power return lines are disconnected from ground, the isolation between the output power return lines and the DC/DC board chassis shall be at least 1Mshunted by not more than 50nF (exclusive of PL-Outputs filters).

Output lines shall maintain an isolation of at least 1M( shunted with a capacity less than 5nF with respect to primary power return line before any grounding of the secondary reference is made.

With a Mega-Ohmmeter and LRC meter (for capacitive measurement ) verify the isolation.

| OUTPUT RETURNS | MEASURED PRIMARY RETURN (M( / nF) | MEASURED DC/DC CHASSIS (M( / nF) |
| --- | --- | --- |
| +5V DPU RTN |  |  |  |  |
| +2.5V DPU RTN |  |  |  |  |
| (15V DPU RTN |  |  |  |  |
| (18V_PL_RTN |  |  |  |  |
| (16V_PL_RTN |  |  |  |  |
| +8V_PL_RTN |  |  |  |  |
| +5.6V_PL_RTN |  |  |  |  |
| DGND |  |  |  |  |

### Push-Pull Characteristics Waveform

#### Fets Gate/Source voltage verification:

-	with a oscilloscope measure the fets Gate/Source voltage waveform in DPU and DPU+PL version and make hardcopy

-	Report the plots in the following figures:

figure 5.2.2.1-1, 5.2.2.1-2,)

Figure 5.2.2.1-1	Fets  Gate/source voltage DPU version

Figure 5.2.2.1-2	Fets  Gate/source voltage PL converter

#### Switching Frequency:

the DC/DC converter/s switching frequency   shall be  110kHz(10%.

| DC/DC CONVERTER | SWITCHING FREQUENCY REFERENCE VALUE (KHz) | MEASURED SWITCHING FREQUENCY (KHz) |
| --- | --- | --- |
| DPU converter |  |  |
| PL converter |  |  |

#### Fets Drain Voltage and Snubber Verification:

the maximum peak FETs Drain Voltage shall not exceed 75V.

-	With a oscilloscope verify the fets Drain Voltage waveform in DPU and DPU+PL version and make hardcopy.

-	Report the plots in the following figures:

figure 5.2.2.3-1, 5.2.2.3-2 ,)

Figure 5.2.2.3-1	Fets Drain voltage DPU version

Figure 5.2.2.3-2	Fets Drain voltage PL converter

#### Primary current limit value:

The DC/DC controller primary peak current limit value shall be set to about 3.5A .

Set  a DPU load  to a maximum value , measure the input peak current and measure the output power consumption ( about21W ).

Increase the load at 120% of maximum load ( about 25W ) and measure the input peak current and output power.

The measured in input peak current must be limited to a  limit peak current value ( 3,5A)

|  | VIN (V) | LOAD | INPUT PEAK CURRENT (A) | OUTPUT POWER (W) |
| --- | --- | --- | --- | --- |
| DPU | 28 | MAX. |  |  |
| DPU | 28 | 120% of MAX. |  |  |

Repeat this step for DPU_PL DC/DC converter section

|  | VIN (V) | LOAD | INPUT PEAK CURRENT (A) | OUTPUT POWER (W) |
| --- | --- | --- | --- | --- |
| DPU_PL | 28 | MAX. |  |  |
| DPU_PL | 28 | 120% of MAX. |  |  |

### Power consumption

Maximum overall output power of the DC/DC board in the DPU+PL version shall be 42 W ( 20%.

Maximum overall output power of the DC/DC board in the DPU version shall be 21W ( 20%.

#### Power consumption in DPU version:

With ammeter in series on positive input line, measure input current at different values of Vin and load current.

| V in (V) | I in (A) | P in (W) | Vout / Iout | Vout / Iout | Vout / Iout | Vout / Iout | Pout (W) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 26 |  |  |  |  |  |  |  |  |  |  |  |
| 28 |  |  |  |  |  |  |  |  |  |  |  |
| 29 |  |  |  |  |  |  |  |  |  |  |  |

#### Power consumption in DPU+PL version:

With ammeter in series on positive input line, measure input current at different values of Vin and load current.

| V in (V) | I in (A) | P in (W) | Vout/ Iout | Vout/ Iout | Vout / Iout | Vout / Iout | Vout / Iout | Vout / Iout | Pout (W) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 26 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 28 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 29 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

### Output Voltage Stability

#### Load regulation (static condition):

The DPU-Outputs are regulated and the electrical requirements and measured value are reported in

the following table:

| Output | Vmin [V] | Vmax [V] | Imin [mA] | Imax [mA] | Vmin measured | Vmax measured |
| --- | --- | --- | --- | --- | --- | --- |
| +5VD | 4.75 | 5.25 | 1000 | 3500 |  |  |
| +15VA | 14.25 | 15.75 | TBD | 100 |  |  |
| -15VA | -15.75 | -14.25 | TBD | 250 |  |  |
| +2.5VFPGA | 2.375 | 2.625 | TBD | 200 |  |  |

Table 5.2.4.1-1		DPU Load regulation (static condition)

The PL-Outputs electrical requirements and measured value are reported in the following table:

| Output | Vmin [V] | Vmax [V] | Imin [mA] | Imax [mA] | Vmin measured | Vmax measured |
| --- | --- | --- | --- | --- | --- | --- |
| +5.6V_PL_OUT | +5.5 | +5.8 | 0 | 240 |  |  |
| +16V_PL_OUT | +15.6 | +16.4 | 0 | 190 |  |  |
| -16V_PL_OUT | -16.4 | -15.6 | 0 | 150 |  |  |
| +8V_PL_OUT | +7 | +9 | 0 | 350 |  |  |
| +18V_PL_OUT | +17 | +20 | 0 | 330 |  |  |
| -18V_PL_OUT | -17 | -20 | 0 | 230 |  |  |

Table 5.2.4.1-2		PL Load regulation (static condition)

Vmin is the output voltage ( with max. output current) delivered when the other outlets are loaded with a min. current.

Vmax is the output voltage ( with min. output current).delivered when the other outlets are loaded with the maximun current.

#### Load Regulation (Transient Condition)

During the load variations the outlet voltage can not exceed the min./max. voltage tolerance .

-	For each outlet generate an instantaneous load variations (low to high) between 25% and 75% of maximum current.

-	Report in the following table the minimum output voltage and the recovery time .

-	Make and report the waveform hardcopy of +5VD and +5,6V_PL_OUT

| OUTLET | I low [mA] | I high [mA] | Time [ms] | Min Voltage [V] |
| --- | --- | --- | --- | --- |
| +5VD | 875 | 2625 |  |  |
| +15VA | 25 | 75 |  |  |
| -15VA | 62.5 | 187.5 |  |  |
| +2.5VFPGA | 50 | 150 |  |  |
| +5.6V_PL_OUT | 60 | 180 |  |  |
| +16V_PL_OUT | 47.5 | 142.5 |  |  |
| -16V_PL_OUT | 37.5 | 112.5 |  |  |
| +8V_PL_OUT | 87.5 | 262.5 |  |  |
| +18V_PL_OUT | 82.5 | 247.5 |  |  |
| -18V_PL_OUT | 57.5 | 172.5 |  |  |

Table 5.2.4.2-1		Load Regulation Low to High (Transient Condition)

Figure 5.2.4.2-1   Load Regulation Low to High ( Transient Condition )

-	For each outlet generate an instantaneous load variations (high to low)  between 75% and 25% of maximum current .

-	Report in the following table the minimum output voltage and the recovery time .

-	Make and report the waveform hardcopy of +5VD and +5,6V_PL_OUT

| OUTLET | I high [mA] | I low [mA] | Time [ms] | Max Voltage [V] |
| --- | --- | --- | --- | --- |
| +5VD | 2625 | 875 |  |  |
| +15VA | 75 | 25 |  |  |
| -15VA | 187.5 | 62.5 |  |  |
| +2.5VFPGA | 150 | 50 |  |  |
| +5.6V_PL_OUT | 180 | 60 |  |  |
| +16V_PL_OUT | 142.5 | 47.5 |  |  |
| -16V_PL_OUT | 112.5 | 37.5 |  |  |
| +8V_PL_OUT | 262.5 | 87.5 |  |  |
| +18V_PL_OUT | 247.5 | 82.5 |  |  |
| -18V_PL_OUT | 172.5 | 57.5 |  |  |

Table 5.2.4.2-2		Load Regulation High to Low (Transient Condition)

Figure 5.2.4.2-2	Load Regulation  High to Low ( Transient Condition )

#### Line regulation:

With multimeter measure all output voltage at minimum, Nominal and Maximum value of Input Voltage with Nominal Load current on each Secondary output. Output Voltage will be measured in correspondence of board pads or board connectors pins.

In Addition measure :

- V int. only fot DPU Version

- Auxiliary voltage V aux only for DPU+PL version.

| output | V in min 26 (V) | V in nom 28 (V) | V in max 29 (V) | NOTE |
| --- | --- | --- | --- | --- |
| V out 5V DPU |  |  |  |  |
| Vout+15V DPU |  |  |  |  |
| Vout -15V DPU |  |  |  |  |
| V out +8V PL |  |  |  |  |
| V out +18V PL |  |  |  |  |
| V out -18V PL |  |  |  |  |
| V out +5,6V PL |  |  |  |  |
| V out +16V PL |  |  |  |  |
| V out –16V PL |  |  |  |  |
| V int. |  |  |  |  |
| V aux |  |  |  |  |

Table 5.2.4.3-1		DC/DC converter Line regulation

### Ripple And Spikes

Ripple and spikes shall be measured with a representative dummy load, the dummy load shall sink a DC load current of Imax in parallel with a 20(F capacitance in series with a 10( resistance. Spikes measurements shall be performed with a 50MHz BW Oscilloscope. For ripple measurements, a 2MHz BW limitation shall be introduced. Measurements shall be performed in differential mode.

In Figure 5.2.5-1 the meaning of ripple and spikes peak to peak envelopes is shown.

Figure 5.2.5-1

Measure and report in the following table the outputs ripple and spike and print out the +5VD and +5.6V_PL_OUT  waveforms

| Output | Ripple [mVPP] | Measured | Spikes [mVpp] | Measured | Note |
| --- | --- | --- | --- | --- | --- |
| +5VD | 200 |  | 100 |  |  |
| +15VA | 400 |  | 200 |  |  |
| -15VA | 400 |  | 200 |  |  |
| +2.5VFPGA | 200 |  | 100 |  |  |
| +5.6V_PL_OUT | 140 |  | 100 |  |  |
| +16V_PL_OUT | 140 |  | 100 |  |  |
| -16V_PL_OUT | 140 |  | 100 |  |  |
| +8V_PL_OUT | 850 |  | 200 |  |  |
| +18V_PL_OUT | 1400 |  | 200 |  |  |
| -18V_PL_OUT | 1400 |  | 200 |  |  |

Table 5.2.5-1 Ripple and Spikes

Figure 5.2.5-2  Ripple and Spikes DPU converter

Figure 5.2.5-3  Ripple and Spikes PL converter

### Efficiency

The conversion efficiency shall be at least 70% at maximum output power.

With available data on Power Consumption and output voltage values at different input voltage and load current, calculate DC/DC Converter efficiency for all input and load conditions.

Efficiency  is given by:

[%]

Where Pout will be computed taking into account actual resistive loads or measured output current on each secondary output.

| DPU EFFICIENCY | VIN MIN | VIN NOM | VIN MAX |
| --- | --- | --- | --- |
| LOAD MIN |  |  |  |
| LOAD NOM |  |  |  |
| LOAD MAX |  |  |  |

| DPU+PL EFFICIENCY | VIN MIN | VIN NOM | VIN MAX |
| --- | --- | --- | --- |
| LOAD MIN |  |  |  |
| LOAD NOM |  |  |  |
| LOAD MAX |  |  |  |

### Start-up Verification

#### Inrush Current

DC/DC board inrush current due to DC/DC board switch-on shall be limited to 1.5 times the DC/DC input peak current, specified as 1.2 times the nominal current. The duration of the inrush peak shall not exceed 0.5ms. The rate of change (slope) of the inrush current shall not exceed 50mA/(sec.

-	Measure and print out the inrush current.

-	Report the waveform hardcopy in figure 5.2.7.1-1 and

| BAORD | PEAK CURRENT (A) | DURATION (ms) | RATE (mA/(sec.) |
| --- | --- | --- | --- |
| DPU |  |  |  |
| DPU+PL |  |  |  |

Figure 5.2.7.1-1	DPU Inrush current

Figure 5.2.7.1-2	DPU+PL Inrush Current

#### Output Voltage soft start

Measure and report in the following table the outputs voltages waveform and print out the +5VD and +5.6V_PL_OUT  waveforms

| OUTPUT | AMPLITUDE (V) | DURATION (ms) | NOTE |
| --- | --- | --- | --- |
| +5VD |  |  |  |
| +15VA |  |  |  |
| -15VA |  |  |  |
| +2.5VFPGA |  |  |  |
| +5.6V_PL_OUT |  |  |  |
| +16V_PL_OUT |  |  |  |
| -16V_PL_OUT |  |  |  |
| +8V_PL_OUT |  |  |  |
| +18V_PL_OUT |  |  |  |
| -18V_PL_OUT |  |  |  |

Figure 5.2.7.2-1	+5VD Output Voltage Soft Start

Figure 5.2.7.2-2	+5,6V_PL-OUT Output Voltage Soft Start

### Stability Verification

With the Set-up shown in fig. 5.2.8-1 measure and report in the following Table the Gain and Phase Margin , with Nominal load current on each Secondary output.

Print out and report the plot of Gain and Phase Margin in the following figures:

-	DPU Converter figures 5.2.8-2

-	PL Converter figures 5.2.8-3

| BAORD | GAIN (dB) | PHASE (°) |
| --- | --- | --- |
| DPU converter |  |  |
| PL converter |  |  |

Figure 5.2.8-1 Stability Verification Test Set-up

Generator Amplitude : 10mV sine

Frequency Range     : 20Hz to 50KHZ

Figure 5.2.8-2		DPU Converter Gain and Phase Margin

Figure 5.2.8-3		PL Converter Gain and Phase Margin

### Input Impedance

This test shall be performed to measure the input impedance of  DPU and DPU+PL converter.

The DC/DC board input impedance shall be 6dB higher than the power bus impedance mask.

The Power Bus Impedance mask is shown in the following figure 5.2.9-1

The measurement shall be performed at maximum output power with a test set-up as shown on figure

-	Measure the input power bus impedance envelope.

-	Report in figure 5.2.9-2the input power bus impedance envelope of DPU converter.

-	Report in figure 5.2.9-3 the input power bus impedance envelope of DPU+PL converter.

Figure 5.2.9-1		The Power Bus Impedance

Figure 5.2.9-2		DPU Input Impedance

Figure 5.2.9-3		DPU+PL Input Impedance

Figure 5.2.9-4		Test set up for input impedance measurement

### Protection Circuitry Verification

The following protections shall be implemented on the DC/DC board DPU-outputs:

#### Input Protection

The DC/DC board shall operate with nominal performance with a Input Voltage between 26(29

Only Under voltage protection is foreseen .

Decrease the input voltage power bus to about 20V and verify that DC/DC converter output voltages switch OFF , report in the following table the input under voltage and current value  .

| VIN | Iin | Pin |
| --- | --- | --- |

#### Output DPU Protections

The following protections shall be implemented on the DC/DC board DPU-Outputs:

- Over-voltage protection (OVP) on +5VD outlet. (Set at about 5.5V) (come farlo)

- Over-current protection value on +5VD, +15VA and -15VA outlets are reported in the following table:

Increase the output load current on each output voltage and report in the table the over current value

| Outlet | Threshold Current [mA] | Current measured [mA] |
| --- | --- | --- |
| +5VD | 4000(10% TBC |  |
| +15VA | 200(10% TBC |  |
| -15VA | 500(10% TBC |  |

Table 5.2.10.2-1

Each protection intervention will shutdown the DC/DC board.

#### Unregulated PL-Outputs Protections

The following protections shall be implemented on the DC/DC board Unregulated PL-Outputs:

- Over-voltage protection (OVP) on the +8V_PL_OUT, +18V_PL_OUT and -18V_PL_OUT outputs.

- The over-voltage protection are performed by series output voltage regulators

The protection characteristics are summarized in the following table.

| Outlet | Threshold Voltage [V] | V measured [V] |
| --- | --- | --- |
| +8V_PL_OUT | 10(1 |  |
| +18V_PL_OUT | 22(2 |  |
| -18V_PL_OUT | -22(2 |  |

Table 5.2.10.2-1

- Over-current protection (OCP) on the +8V_PL_OUT, +18V_PL_OUT and -18V_PL_OUT outlets as reported in the following table: ( LIMITI dei Regolatori)

| Outlet | Threshold Current [mA] | Current measured [mA] |
| --- | --- | --- |
| +8V_PL_OUT | 600(100 |  |
| +18V_PL_OUT | 600(100 |  |
| -18V_PL_OUT | 600(100 |  |

Table 5.2.10.3-2

#### Regulated PL-Outputs Protections

The following protections shall be implemented on the DC/DC board Regulated PL-Outputs:

- Over-voltage protection (OVP) with crow-bar on the +5.6V_PL_OUT, with the following characteristics :

| Output | Threshold Voltage [V] | Iclamp [A] | Vlim [V] | V measured [V] |
| --- | --- | --- | --- | --- |
| +5.6V_PL_OUT | +6.5(5% | -2…+2 | -0.7…+7 |  |
| +16V_PL_OUT | +17.2(5% | -2…+2 | -0.7…+18 |  |
| -16V_PL_OUT | -17.2(5% | -2…+2 | -18…+0.7 |  |

Table 5.2.10.4-1

Iclamp is the maximum current that the over-voltage protection should be able to handle (crowbar). The voltage on the output shall be within Vlim range when Iclamp is injected.

Note: in case of short circuit between output “hot lines” with current injection (within the range of Iclamp) from one line into the other, the output voltage shall be limited within the range established in the Vlim column.

+16V_PL_OUT and -16V_PL_OUT outputs overvoltage protection is realized by series voltage regulator.(come provarlo)

- Current limitation (CL) on the +5.6V_PL_OUT, +16V_PL_OUT and -16V_PL_OUT outlets.

The current limitation values and the measured values are reported in the following table.

| Output | Ilim [mA] | Current measured [mA] |
| --- | --- | --- |
| +5.6V_PL_OUT | 285(5% |  |
| +16V_PL_OUT | 950(5% |  |
| -16V_PL_OUT | 950(5% |  |

Table 5.2.10.4-2

Ilim is also the maximum output current for inrush currents when downstream electronics is switched ON.

To simulate the inrush current of the load connected to each Regulated PL-Output a 100(F capacitor with no significant series impedance can be used. (da testare?)

### Monitor Verification

The DC/DC board shall provide the telemetries described in the following table:

| Telemetry | Function | Accuracy | Type | Scale | Reference |
| --- | --- | --- | --- | --- | --- |
| +5V_MNT | +5VD voltage monitor | (5% | Voltage monitor Single Ended | 0V ( 0V MNT 6V ( 5V MNT | RTN_MNT1 |
| +15V_MNT | +15VA voltage monitor | (5% | Voltage monitor Single Ended | 0V ( 0V MNT 18V ( 5V MNT | RTN_MNT2 |
| -15V_MNT | -15VA voltage monitor | (5% | Voltage monitor Single Ended | 0V ( 0V MNT -18V ( 5V MNT | RTN_MNT3 |
| +TEMP_MNT | Temperature monitor | (5% | Temperature Monitor Single Ended | -50°C ( 0V MNT +80°C ( 5V MNT | RTN_MNT4 |

Table 5.2.11-1 Telemetries

Note: RTN_MNT0, RTN_MNT1, RTN_MNT2, RTN_MNT3 and RTN_MNT4 shall be connected, into the DC/DC board, to DPU-Outputs Return line.

Measure and report in the following table the measured telemetry values

| Telemetry | Measured outputs voltages | V telemetry expected [V] | V telemetry measured [V] | Error [%] |
| --- | --- | --- | --- | --- |
| +5V_MNT |  |  |  |  |
| +15V_MNT |  |  |  |  |
| -15V_MNT |  |  |  |  |
| TEMP_MNT |  |  |  |  |

Table 5.2.11-2 Telemetries

## THERMAL TEST

The DC/DC board shall be designed to be compatible with the environmental constraints summarized in the following table:

| Board operating temperature: | -25 ( +45 °C |
| --- | --- |
| Board non operating temperature: | -35 ( +85 °C |

Table 5.3-1	Thermal Environmental constraints

Note: The above mentioned temperature ranges are valid only if components with appropriate extended temperature range are utilized.

### Low Temperature Test  (-25°)

#### Power consumption

Maximum overall output power of the DC/DC board in the DPU+PL version shall be 42 W ( 20%.

Maximum overall output power of the DC/DC board in the DPU version shall be 21W ( 20%.

##### Power consumption in DPU version:

With ammeter in series on positive input line, measure input current at different values of Vin and load current.

| V in (V) | I in (A) | P in (W) | Vout / Iout | Vout / Iout | Vout / Iout | Vout / Iout | Pout (W) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 26 |  |  |  |  |  |  |  |  |  |  |  |
| 28 |  |  |  |  |  |  |  |  |  |  |  |
| 29 |  |  |  |  |  |  |  |  |  |  |  |

- Power consumption in DPU+PL version:

With ammeter in series on positive input line, measure input current at different values of Vin and load current.

| V in (V) | I in (A) | P in (W) | Vout/ Iout | Vout/ Iout | Vout / Iout | Vout / Iout | Vout / Iout | Vout / Iout | Pout (W) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 26 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 28 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 29 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

#### Output Voltage Stability

##### Load regulation (static condition):

The DPU-Outputs are regulated and the electrical requirements and measured value are reported in

The following table

| Output | Vmin [V] | Vmax [V] | Imin [mA] | Imax [mA] | Vmin measured | Vmax measured |
| --- | --- | --- | --- | --- | --- | --- |
| +5VD | 4.75 | 5.25 | 1000 | 3500 |  |  |
| +15VA | 14.25 | 15.75 | TBD | 100 |  |  |
| -15VA | -15.75 | -14.25 | TBD | 250 |  |  |
| +2.5VFPGA | 2.375 | 2.625 | TBD | 200 |  |  |

Table 5.3.1.2-1		DPU Load regulation (static condition)

The PL-Outputs electrical requirements and measured value are reported in following table:

| Output | Vmin [V] | Vmax [V] | Imin [mA] | Imax [mA] | Vmin measured | Vmax measured |
| --- | --- | --- | --- | --- | --- | --- |
| +5.6V_PL_OUT | +5.5 | +5.8 | 0 | 240 |  |  |
| +16V_PL_OUT | +15.6 | +16.4 | 0 | 190 |  |  |
| -16V_PL_OUT | -16.4 | -15.6 | 0 | 150 |  |  |
| +8V_PL_OUT | +7 | +9 | 0 | 350 |  |  |
| +18V_PL_OUT | +17 | +20 | 0 | 330 |  |  |
| -18V_PL_OUT | -17 | -20 | 0 | 230 |  |  |

Table 5.3.1.2-2		PL Load regulation (static condition)

Vmin is the output voltage ( with max. output current) delivered when the other outlet is loaded with a min. current.

Vmax is the output voltage ( with min. output current)delivered when the outlet is loaded with a current in

- Load Regulation (Transient Condition):

During the load variations the outlet voltage can not exceed the min./max. voltage tolerance .

For each outlet generate an istantaneus load variations (low to high) between 25% and 75% of maximum current.

-	Report in the following table the minimum output voltage and the recovery time.

-	Make and report the hardcopy of and in following figure:

-	+5VD waveform in figure 5.3.1.2-1.

-	+5,6V_PL_OUT waveform in figure 5.3.1.2-2.

| OUTLET | I low [mA] | I high [mA] | Time [ms] | Min Voltage [V] |
| --- | --- | --- | --- | --- |
| +5VD | 875 | 2625 |  |  |
| +15VA | 25 | 75 |  |  |
| -15VA | 62.5 | 187.5 |  |  |
| +2.5VFPGA | 50 | 150 |  |  |
| +5.6V_PL_OUT | 60 | 180 |  |  |
| +16V_PL_OUT | 47.5 | 142.5 |  |  |
| -16V_PL_OUT | 37.5 | 112.5 |  |  |
| +8V_PL_OUT | 87.5 | 262.5 |  |  |
| +18V_PL_OUT | 82.5 | 247.5 |  |  |
| -18V_PL_OUT | 57.5 | 172.5 |  |  |

Table 5.3.1.2-3		Load Regulation Low to High (Transient Condition)

Figure 5.3.1.2-1	+5VD Load Regulation Low to High ( Transient Condition )

Figure 5.3.1.2-2	+5,6V_PL_OUT Load Regulation Low to High ( Transient Condition )

For each outlet generate an instantaneous load variations (high to low)  between 75% and 25% of maximum current .

-	Report in the following table the minimum output voltage and the recovery time.

-	Make and report the hardcopy of and in following figure:

-	+5VD waveform in figure 5.3.1.2-3.

-	+5,6V_PL_OUT waveform in figure 5.3.1.2-4.

| OUTLET | I high [mA] | I low [mA] | Time [ms] | Max Voltage [V] |
| --- | --- | --- | --- | --- |
| +5VD | 2625 | 875 |  |  |
| +15VA | 75 | 25 |  |  |
| -15VA | 187.5 | 62.5 |  |  |
| +2.5VFPGA | 150 | 50 |  |  |
| +5.6V_PL_OUT | 180 | 60 |  |  |
| +16V_PL_OUT | 142.5 | 47.5 |  |  |
| -16V_PL_OUT | 112.5 | 37.5 |  |  |
| +8V_PL_OUT | 262.5 | 87.5 |  |  |
| +18V_PL_OUT | 247.5 | 82.5 |  |  |
| -18V_PL_OUT | 172.5 | 57.5 |  |  |

Table 5.3.1.2-4		Load Regulation High to Low (Transient Condition)

Figure 5.3.1.2-3	+5VD Load Regulation  High to Low ( Transient Condition )

Figure 5.3.1.2-4	+5,6V_PL_OUT Load Regulation  High to Low ( Transient Condition )

- Line regulation:

With multimeter measure all output voltage at minimum, Nominal and Maximum value of Input Voltage with Nominal Load current on each Secondary output. Output Voltage will be measured in correspondence of board pads or board connectors pins.

In Addition measure :

-	Vint only fot DPU Version

-	auxiliary voltage V aux only for DPU+PL version.

| output | V in min 26 (V) | V in nom 28 (V) | V in max 29 (V) | NOTE |
| --- | --- | --- | --- | --- |
| V out 5V DPU |  |  |  |  |
| Vout+15V DPU |  |  |  |  |
| Vout -15V DPU |  |  |  |  |
| V out +8V PL |  |  |  |  |
| V out +18V PL |  |  |  |  |
| V out -18V PL |  |  |  |  |
| V out +5,6V PL |  |  |  |  |
| V out +16V PL |  |  |  |  |
| V out –16V PL |  |  |  |  |
| V int. |  |  |  |  |
| V aux |  |  |  |  |

Table 5.3.1.2-5		DC/DC converter Line regulation

#### Efficiency

The conversion efficiency shall be at least 70% at maximum output power.

With available data on Power Consumption and output voltage values at different input voltage and load current, calculate DC/DC Converter efficiency for all input and load conditions.

Efficiency  is given by:

[%]

Where Pout will be computed taking into account actual resistive loads or measured output current on each secondary output.

| DPU EFFICIENCY | VIN MIN | VIN NOM | VIN MAX |
| --- | --- | --- | --- |
| LOAD MIN |  |  |  |
| LOAD NOM |  |  |  |
| LOAD MAX |  |  |  |

| DPU+PL EFFICIENCY | VIN MIN | VIN NOM | VIN MAX |
| --- | --- | --- | --- |
| LOAD MIN |  |  |  |
| LOAD NOM |  |  |  |
| LOAD MAX |  |  |  |

#### Monitors Verification

The DC/DC board shall provide the telemetries described in the following table:

| Telemetry | Function | Accuracy | Type | Scale | Reference |
| --- | --- | --- | --- | --- | --- |
| +5V_MNT | +5VD voltage monitor | (5% | Voltage monitor Single Ended | 0V ( 0V MNT 6V ( 5V MNT | RTN_MNT1 |
| +15V_MNT | +15VA voltage monitor | (5% | Voltage monitor Single Ended | 0V ( 0V MNT 18V ( 5V MNT | RTN_MNT2 |
| -15V_MNT | -15VA voltage monitor | (5% | Voltage monitor Single Ended | 0V ( 0V MNT -18V ( 5V MNT | RTN_MNT3 |
| +TEMP_MNT | Temperature monitor | (5% | Temperature Monitor Single Ended | -50°C ( 0V MNT +80°C ( 5V MNT | RTN_MNT4 |

Table 5.3.1.4-1 	Telemetries

Note: RTN_MNT0, RTN_MNT1, RTN_MNT2, RTN_MNT3 and RTN_MNT4 shall be connected, into the DC/DC board, to DPU-Outputs Return line.

Measure and report in the following table the measured telemetry values

| Telemetry | Measured outputs voltages | V telemetry expected [V] | V telemetry measured [V] | Error [%] |
| --- | --- | --- | --- | --- |
| +5V_MNT |  |  |  |  |
| +15V_MNT |  |  |  |  |
| -15V_MNT |  |  |  |  |
| TEMP_MNT |  |  |  |  |

Table 5.4.1.4-2		telemetry values

### High Temperature Test  (+45°)

#### Power consumption

Maximum overall output power of the DC/DC board in the DPU+PL version shall be 42 W ( 20%.

Maximum overall output power of the DC/DC board in the DPU version shall be 21W ( 20%.

- Power consumption in DPU version:

With ammeter in series on positive input line, measure input current at different values of Vin and load current.

| V in (V) | I in (A) | P in (W) | Vout / Iout | Vout / Iout | Vout / Iout | Vout / Iout | Pout (W) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 26 |  |  |  |  |  |  |  |  |  |  |  |
| 28 |  |  |  |  |  |  |  |  |  |  |  |
| 29 |  |  |  |  |  |  |  |  |  |  |  |

- Power consumption in DPU+PL version:

With ammeter in series on positive input line, measure input current at different values of Vin and load current.

| V in (V) | I in (A) | P in (W) | Vout/ Iout | Vout/ Iout | Vout / Iout | Vout / Iout | Vout / Iout | Vout / Iout | Pout (W) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 26 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 28 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 29 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

#### Output Voltage Stability

- Load regulation (static condition):

The DPU-Outputs are regulated and the electrical requirements and measured value are reported in the following table:

| Output | Vmin [V] | Vmax [V] | Imin [mA] | Imax [mA] | Vmin measured | Vmax measured |
| --- | --- | --- | --- | --- | --- | --- |
| +5VD | 4.75 | 5.25 | 1000 | 3500 |  |  |
| +15VA | 14.25 | 15.75 | TBD | 100 |  |  |
| -15VA | -15.75 | -14.25 | TBD | 250 |  |  |
| +2.5VFPGA | 2.375 | 2.625 | TBD | 200 |  |  |

Table 5.3.2.2-1		DPU Load regulation (static condition)

The PL-Outputs electrical requirements and measured value are reported in following table:

| Output | Vmin [V] | Vmax [V] | Imin [mA] | Imax [mA] | Vmin measured | Vmax measured |
| --- | --- | --- | --- | --- | --- | --- |
| +5.6V_PL_OUT | +5.5 | +5.8 | 0 | 240 |  |  |
| +16V_PL_OUT | +15.6 | +16.4 | 0 | 190 |  |  |
| -16V_PL_OUT | -16.4 | -15.6 | 0 | 150 |  |  |
| +8V_PL_OUT | +7 | +9 | 0 | 350 |  |  |
| +18V_PL_OUT | +17 | +20 | 0 | 330 |  |  |
| -18V_PL_OUT | -17 | -20 | 0 | 230 |  |  |

Table 5.3.2.2-2		PL Load regulation (static condition)

Vmin is the output voltage ( with max. output current) delivered when the other outlet is loaded with a min. current.

Vmax is the output voltage ( with min. output current)delivered when the outlet is loaded with a current in

- Load Regulation (Transient Condition)

During the load variations the outlet voltage can not exceed the min./max. voltage tolerance .

For each outlet generate an istantaneus load variations (low to high) between 25% and 75% of maximum current.

-	Report in the following table the minimum output voltage and the recovery time.

-	Make and report the hardcopy of and in following figure:

-	+5VD waveform in figure 5.3.2.2-1.

-	+5,6V_PL_OUT waveform in figure 5.3.2.2-2.

| OUTLET | I low [mA] | I high [mA] | Time [ms] | Min Voltage [V] |
| --- | --- | --- | --- | --- |
| +5VD | 875 | 2625 |  |  |
| +15VA | 25 | 75 |  |  |
| -15VA | 62.5 | 187.5 |  |  |
| +2.5VFPGA | 50 | 150 |  |  |
| +5.6V_PL_OUT | 60 | 180 |  |  |
| +16V_PL_OUT | 47.5 | 142.5 |  |  |
| -16V_PL_OUT | 37.5 | 112.5 |  |  |
| +8V_PL_OUT | 87.5 | 262.5 |  |  |
| +18V_PL_OUT | 82.5 | 247.5 |  |  |
| -18V_PL_OUT | 57.5 | 172.5 |  |  |

Table 5.3.2.2-3		Load Regulation Low to High (Transient Condition)

Figure 5.3.2.2-1	+5VD Load Regulation Low to High ( Transient Condition )

Figure 5.3.2.2-2	+5,6V_PL_OUT Load Regulation Low to High ( Transient Condition )

For each outlet generate an instantaneous load variations (high to low)  between 75% and 25% of maximum current

-	Report in the following table the minimum output voltage and the recovery time.

-	Make and report the hardcopy of and in following figure:

-	+5VD waveform in figure 5.3.2.2-3.

-	+5,6V_PL_OUT waveform in figure 5.3.2.4-4.

| OUTLET | I high [mA] | I low [mA] | Time [ms] | Max Voltage [V] |
| --- | --- | --- | --- | --- |
| +5VD | 2625 | 875 |  |  |
| +15VA | 75 | 25 |  |  |
| -15VA | 187.5 | 62.5 |  |  |
| +2.5VFPGA | 150 | 50 |  |  |
| +5.6V_PL_OUT | 180 | 60 |  |  |
| +16V_PL_OUT | 142.5 | 47.5 |  |  |
| -16V_PL_OUT | 112.5 | 37.5 |  |  |
| +8V_PL_OUT | 262.5 | 87.5 |  |  |
| +18V_PL_OUT | 247.5 | 82.5 |  |  |
| -18V_PL_OUT | 172.5 | 57.5 |  |  |

Table 5.3.2.2-4		Load Regulation High to Low (Transient Condition)

Figure 5.3.2.2-3		+5VD Load Regulation  High to Low ( Transient Condition )

Figure 5.3.2.4-4	+5,6V_PL_OUT Load Regulation  High to Low ( Transient Condition )

- Line regulation:

With multimeter measure all output voltage at minimum, Nominal and Maximum value of Input Voltage with Nominal Load current on each Secondary output. Output Voltage will be measured in correspondence of board pads or board connectors pins.

In Addition measure :

-	Vin only fot DPU Version

-	Auxiliary voltage Vaux only for DPU+PL version.

| output | V in min 26 (V) | V in nom 28 (V) | V in max 29 (V) | NOTE |
| --- | --- | --- | --- | --- |
| V out 5V DPU |  |  |  |  |
| Vout+15V DPU |  |  |  |  |
| Vout -15V DPU |  |  |  |  |
| V out +8V PL |  |  |  |  |
| V out +18V PL |  |  |  |  |
| V out -18V PL |  |  |  |  |
| V out +5,6V PL |  |  |  |  |
| V out +16V PL |  |  |  |  |
| V out –16V PL |  |  |  |  |
| V int. |  |  |  |  |
| V aux |  |  |  |  |

Table 5.3.2.2-5		DC/DC converter Line regulation

#### Efficiency

The conversion efficiency shall be at least 70% at maximum output power.

With available data on Power Consumption and output voltage values at different input voltage and load current, calculate DC/DC Converter efficiency for all input and load conditions.

Efficiency  is given by:

[%]

Where Pout will be computed taking into account actual resistive loads or measured output current on each secondary output.

| DPU EFFICIENCY | VIN MIN | VIN NOM | VIN MAX |
| --- | --- | --- | --- |
| LOAD MIN |  |  |  |
| LOAD NOM |  |  |  |
| LOAD MAX |  |  |  |

| DPU+PL EFFICIENCY | VIN MIN | VIN NOM | VIN MAX |
| --- | --- | --- | --- |
| LOAD MIN |  |  |  |
| LOAD NOM |  |  |  |
| LOAD MAX |  |  |  |

#### Monitors Verification

The DC/DC board shall provide the telemetries described in the following table:

| Telemetry | Function | Accuracy | Type | Scale | Reference |
| --- | --- | --- | --- | --- | --- |
| +5V_MNT | +5VD voltage monitor | (5% | Voltage monitor Single Ended | 0V ( 0V MNT 6V ( 5V MNT | RTN_MNT1 |
| +15V_MNT | +15VA voltage monitor | (5% | Voltage monitor Single Ended | 0V ( 0V MNT 18V ( 5V MNT | RTN_MNT2 |
| -15V_MNT | -15VA voltage monitor | (5% | Voltage monitor Single Ended | 0V ( 0V MNT -18V ( 5V MNT | RTN_MNT3 |
| +TEMP_MNT | Temperature monitor | (5% | Temperature Monitor Single Ended | -50°C ( 0V MNT +80°C ( 5V MNT | RTN_MNT4 |

Table 5.3.2.4-1		Telemetries

Note: RTN_MNT0, RTN_MNT1, RTN_MNT2, RTN_MNT3 and RTN_MNT4 shall be connected, into the DC/DC board, to DPU-Outputs Return line.

Measure and report in the following table the measured telemetry values

| Telemetry | Measured outputs voltages | V telemetry expected [V] | V telemetry measured [V] | Error [%] |
| --- | --- | --- | --- | --- |
| +5V_MNT |  |  |  |  |
| +15V_MNT |  |  |  |  |
| -15V_MNT |  |  |  |  |
| TEMP_MNT |  |  |  |  |

Table 5.3.2.4-2		Telemetries values

## EMC TEST

### Conducted Emission on Input Power Line

#### CE on Input Power Line, Frequency Domain, Differential Mode, NB

| Type of measur. | : | Differential mode |
| --- | --- | --- |

| Frequency range Emission type | : : | 30 Hz ÷ 50 MHz Narrowband |
| --- | --- | --- |

| Measured line | : | Input power lines |
| --- | --- | --- |

This test shall be performed to measure the current ripple appearing on input power lines in frequency domain.

The measurement shall be performed at maximum output power with a test set-up as shown on figure 5.4.1.1-1

-	Take measurement of the ambient noise and make hardcopy (positive input line)

-	Switch-on the UUT, repeat the measurements and make hardcopy (positive input line)

For the highest emissive mode the applied voltage shall be the worst case among the range from 26V-29V

-	Repeat the above test for return line.

-	Report the plots in the following figures:

figure 5.4.1.1-3, 5.4.1.1-4, 5.4.1.1-5, 5.4.1.1-6)

Figure 5.4.1.1-1	test set up for conduced emission frequency domain DM

Narrow-Band conducted emission Differential Mode in the frequency range 30Hz(50MHz generated by the DC/DC board on the input power line shall not exceed the following adjustable limit:

A)	For Nominal DC input current less than 1A, use the curve in figure 5.4.1.1-2

B)	For Nominal DC input current greater than 1A, increase the level (in dB(A) of the curve in                figure 5.4.1.1-2 by 10*Log[I (A)]. I(A) is the nominal input current in Ampere.

Figure 5.4.1.1-2	limit for CEP-Differential mode

Figure 5.4.1.1-3		Hardcopy of the UUT CEP on the positive input line

Figure 5.4.1.1-4		Hardcopy of the ambient noise on the return input line

Figure 5.4.1.1-5		Hardcopy of the UUT CEP on the return input line

Figure 5.4.1.1-6		Hardcopy of the ambient noise on the positive input line

#### CE on Input Line, Frequency Domain, Common Mode, NB

| Type of measur. | : | Common mode |
| --- | --- | --- |

| Frequency range Emission type | : : | 10 KHz ÷ 50 MHz Narrowband |
| --- | --- | --- |

| Measured line | : | Input power lines |
| --- | --- | --- |

This test shall be performed to measure the current ripple appearing on input power lines in frequency domain.

The measurement shall be performed at maximum output power with a test set-up as shown on figure 5.4.1.2-2

-	Take measurement of the ambient noise and make hardcopy

-	Switch-on the UUT, repeat the measurements and make hardcopy

For the highest emissive mode the applied voltage shall be the worst case among the range from 26V-29V

-	Report the plots in the following figures:

figure 5.4.1.2-3, 5.4.1.2-4)

Narrow-Band conducted emission Common Mode in the frequency range 10kHz 50MHz generated by the DC/DC board on the input power line shall not exceed the following adjustable limit:

- For nominal DC input current less than 1A, use the curve of figure 5.4.1.2-1 as shown.

- For nominal DC input current greater than 1A, increase the level (in dB(A) of the curve in                 figure 5.4.1.2-1 by 10*log[I(A)]. I(A) is the nominal input current in Ampere.

Figure 5.4.1.2-1

Figure 5.4.1.2-2	test set up for conduced emission frequency domain CM

Figure 5.4.1.2-3		Hardcopy of the ambient noise on the input line

Figure 5.4.1.2-4		Hardcopy of the UUT CEP on the input line

#### Current Ripple, Time Domain, Differential Mode

| Type of measur. | : | Differential mode |
| --- | --- | --- |

| Bandwidth | : | 50 MHz |
| --- | --- | --- |

| Measured line | : | Input power lines |
| --- | --- | --- |

This test shall be performed to measure the exported spikes from the equipment on the input power lines in time domain.

The measurement shall be performed at maximum output power with a test set-up as shown on figure 5.4.1.3-1

-	Place the current probe on positive power lead of the power line.

-	Record the current ripple and make hardcopy

-	Place the current probe on return power lead of the power line.

-	Record the current ripple and make hardcopy

-	Report the plots in the following figures:

figure 5.4.1.3-2, 5.4.1.3-3)

The current ripple and spikes on the input power line of the DC/DC board shall not exceed the following adjustable limits:

A) 	For nominal DC input current less than 1A:

Ripple: less than 20mApp.

Spikes, including ripple: less than 60mApp.

B) 	For nominal DC input current greater than 1A:

Ripple: multiply 20mApp by a factor (I(A), I(A) is the nominal input current in Ampere.

Spikes, including ripple: multiply 60mApp by a factor (I(A), I(A) is the nominal input current in Ampere.

Ripple and spikes shall be measured on both the primary and return lines with at least 50MHz bandwidth.

Figure 5.4.1.3-1	test set up for conduced emission time domain

Figure 5.4.1.3-2		Hardcopy of the current ripple on positive power lead of the power line

Figure 5.4.1.3-3	Hardcopy of the current ripple on return power lead of the power line

### Conducted Susceptibility from Input Power Line

#### CS from Input Power Line, Differential Mode, Steady State

This test shall be performed to verify the immunity of the UUT to sine wave differential mode noise injected on power lines.

| The measurement shall be performed at maximum output power with a test set-up as shown on figure 5-4-2-2 and figure |  |  |
| --- | --- | --- |

# Text boxes

CH.

CH.

HSO/FIRST-DPU

dddd

ddddddd

dd

Probe

Probee

V1

V2

GEN

Power

Supply

To PWM

To OUT

DC/DC CONVERTER

Amp.

Adapt.

CH.

probe

GAIN / PHASE

ANALYZER

+

-

+ +

-

Feedback Loop

Il grafico non sembra descrivere le caratteristiche del disturbo da indurre ma, piuttosto, una maschera per accettare o meno gli effetti del disturbo!

Ma allora che cosa bisogna iniettare?

Chamber ground plane

Insulating plane

dc/dc board

Amplifier

Signal generator

Bus 28v generator

+28V line

+28V rtn

220Vac / 50Hz

220Vac / 50Hz

Dedicated test equipment

OUT line

OUT rtn

Dc/dc chassis

Oscilloscope

(differential probe CH1-CH2)

Chamber ground plane

Insulating plane

dc/dc board

Amplifier

Signal generator

Bus 28v generator

+28V line

+28V rtn

220Vac / 50Hz

220Vac / 50Hz

Dedicated test equipment

OUT line

OUT rtn

Dc/dc chassis

Oscilloscope

(differential probe CH1-CH2)

DEFINIRE