SPIRE Filters

Failure Modes Effects & Criticality Analysis (FMECA) Report

SPIRE Ref.: SPIRE-QMW-PRJ-001115

Cardiff Ref.: HSO-CDF-RP-031

Issue: 2.0

Prepared by: Peter Hargrave

Last Modified on: 25 January 2002

Approved by:

Distribution list

Update history

| Date | Version | Remarks |
| --- | --- | --- |
| 31/08/01 | 1.0 | First Issue for DDR |
| 25/01/02 | 2.0 | First configuration controlled issue |

List of Acronyms

| Term | Meaning | Term | Meaning |
| --- | --- | --- | --- |
| AD | Applicable Document | IR | Infrared |
| ADC | Analogue to Digital Converter | IRD | Instrument Requirements Document |
| AIV | Assembly, Integration and Verification | IRTS | Infrared Telescope in Space |
| AME | Absolute Measurement Error | ISM | Interstellar Medium |
| AOCS | Attitude and Orbit Control System | JFET | Junction Field Effect Transistor |
| APART | Arizona's Program for the Analysis of Radiation Transfer | ISO | Infrared Space Observatory |
| APE | Absolute Pointing Error | LCL | Latching Current Limiter |
| ASAP | Advanced Systems Analysis Program | LIA | Lock-In Amplifier |
| ATC | Astronomy Technology Centre, Edinburgh | LVDT | Linear Variable Differential Transformer |
| AVM | Avionics Model | LWS | Long Wave Spectrometer (an instrument used on ISO) |
| BDA | Bolometer Detector Array | MAC | Multi Axis Controller |
| BFL | Back Focal Length | MAIV | Manufacturing, Assembly, Integration and Verification |
| BRO | Breault Research Organization | MCU | Mechanism Control Unit = HSMCU |
| BSM | Beam Steering Mirror | MGSE | Mechanical Ground Support Equipment |
| CBB | Cryogenic Black Body | M-P | Martin-Puplett |
| CDF | Cardiff, Department of Physics & Astronomy | NEP | Noise Equivalent Power |
| CDMS | Command and Data Management System | NTD | Neutron Transmutation Doped |
| CDMU | Command and Data Management Unit | OBS | On-Board Software |
| CDR | Critical Design Review | OGSE | Optical Ground Support Equipment |
| CEA | Commissariat a l’Energie Atomique | OMD | Observing Modes Document |
| CMOS | Complimentary Metal Oxide Silicon | OPD | Optical Path Difference |
| CoG | Centre of Gravity | PACS | Photodetector Array Camera and Spectrometer |
| CPU | Central Processing Unit | PCAL | Photometer Calibration source |
| CQM | Cryogenic Qualification Model | PFM | Proto-Flight Model |
| CVV | Cryostat Vacuum Vessel | PID | Proportional, Integral and Differential (used in the context of feedback control loop architecture) |
| DAC | Digital to Analogue Converter | PLW | Photometer, Long Wavelength |
| DAQ | Data Acquisition | PMW | Photometer, Medium Wavelength |
| DCU | Detector Control Unit = HSDCU | POF | Photometer Observatory Function |
| DDR | Detailed Design Review | PROM | Programmable Read Only Memory |
| DM | Development Model | PSW | Photometer, Short Wavelength |
| DPU | Digital Processing Unit = HSDPU | PUS | Packet Utilisation Standard |
| DSP | Digital Signal Processor | RAL | Rutherford Appleton Laboratory, |
| DQE | Detective Quantum Efficiency | RD | Reference Document |
| EDAC | Error Detection and Correction | RMS | Root Mean Squared |
| EGSE | Electrical Ground Support Equipment | SCAL | Spectrometer Calibration Source |
| EM | Engineering Model | SCUBA | Submillimetre Common User Bolometer Array |
| EMC | Electro-magnetic Compatibility | SED | Spectral Energy Distribution |
| EMI | Electro-magnetic Interference | SMEC | Spectrometer Mechanics |
| ESA | European Space Agency | SMPS | Switch Mode Power Supply |
| FCU | FCU Control Unit = HSFCU | SOB | SPIRE Optical Bench |
| FIR | Far Infrared | SOF | Spectrometer Observatory Function |
| FIRST | Far Infra-Red and Submillimetre Telescope | SPIRE | Spectral and Photometric Imaging Receiver |
| FOV | Field of View | SRAM | Static Random Access Memory |
| F-P | Fabry-Perot | SSSD | SubSystem Specification Document |
| FPGA | Field Programmable Gate Array | STP | Standard Temperature and Pressure |
| FPU | Focal Plane Unit | SVM | Service Module |
| FS | Flight Spare | TBC | To Be Confirmed |
| FTS | Fourier Transform Spectrometer | TBD | To Be Determined |
| FWHM | Full Width Half maximum | TC | Telecommand |
| GSFC | Goddard Space Flight Center | URD | User Requirements Document |
| HK | House Keeping | UV | Ultra Violet |
| HOB | Herschel Optical Bench | WE | Warm Electronics |
| HPDU | Herschel Power Distribution Unit | ZPD | Zero Path Difference |
| HSDCU | Herschel-SPIRE Detector Control Unit |  |  |
| HSDPU | Herschel-SPIRE Digital Processing Unit |  |  |
| HSFCU | Herschel-SPIRE FPU Control Unit |  |  |
| HSO | Herschel Space Observatory |  |  |
| IF | Interface |  |  |
| IID-A | Instrument Interface Document - Part A |  |  |
| IID-B | Instrument Interface Document - Part B |  |  |
| IMF | Initial Mass Function |  |  |

Table of Contents

1.	Scope	5

2.	Documents	5

2.1.	Applicable documents	5

2.2.	Reference documents	5

3.	Details of the analysis	5

# Scope

This document presents the results of the FMECA carried out on the SPIRE filters.

# Documents

## Applicable documents

All applicable documents are listed in the AD chapter of the CIDL (HSO-CDF-LI-029).

## Reference documents

# Details of the analysis

A failure modes effects and criticality analysis has been performed on all functional elements of the filters which can cause failure effects within the experiment or cause damage to, or interfere with, the proper functioning of the SPIRE instrument or Herschel spacecraft.

Each failure effect identified has been given a criticality category according to the definition below:

- Category 1:	The failure effect is not confined to the subsystem.  When this failure results also in loss or degradation of the instruments function this shall be stated.

- Category 2:	The failure results in loss or degradation of the subsystems function but the effect is confined to the subsystem.

- Category 3: 	Minor internal subsystem failures.

The following attributes have been added to the criticality category as appropriate:

-	"R", if the design contains a redundant item which can perform the same function

-	"SH", if the failure effect causes a safety hazard

-	"SPF" if the failure is caused by a single point failure.

The following failure modes have been considered: -

Failure during operation

Degradation or out of tolerance operation

Mechanical failure

Design specifications, descriptions functional diagrams etc. used in the preparation of the FMECA shall be attached or referenced.

Table 1 Results of FMECA of the filters subsystem.

| FAILURE MODES EFFECTS AND CRITICALITY ANALYSIS (FMECA) Product: SPIRE Instrument Project/Phase: Herschel System/Subsystem/Equipment: Filters, beam splitters & dichroics Mission phase/Operational Mode: Space Flight Prepared by: P.Hargrave Approved by: Date: 25/08/01 Document reference: Issue: |
| --- |
| Id number | Item/ block | Function | Failure mode | Failure cause | Failure effects a. Local effects b. End effects | Severity | Failure detection method/ observable symptoms | Compensation provisions | Correction actions | Remarks |
| 000.001 | CFIL1 | Common input filter. Attenuates out-of-band radiation | Delamination | Manufacturing error | Loss in transmission. Additional in-band fringing. Decreased instrument sensitivity | 1 | Detected as loss in transmission in the photometer. Any fringing could be observed in the spectrometer. | None | None | Very unlikely – delamination would occur in first few thermal cycles of qualification tests. |
| 000.002 |  |  | Cracking | Differential thermal contraction | Negligible impact on performance Negligible impact on performance | 3 | None | None | None | Never observed before, but possible. |
| 000.003 |  |  | Slippage in clamp / warping | Incorrect mounting | None None | 3 |  |  |  |  |
| 000.004 |  |  | Falls from clamp | Incorrect mounting, cracking. | Reduction in blocking. Increased background on all detectors. Possibility of damage to other Herschel Instruments and SPIRE subsystems. | 1 | Increased background loading on all detectors | None | None | Highly unlikely. Never observed before. This filter and mount will undergo rigorous qualification tests. |
| 001.001 | 4K blockers | Attenuates out-of-band radiation | Delamination | Manufacturing error | Loss in transmission. Additional in-band fringing. Decreased instrument sensitivity | 1 | Detected as loss in transmission in the photometer. Any fringing could be observed in the spectrometer. | None | None | Very unlikely – delamination would occur in first few thermal cycles of qualification tests. |
| 001.002 |  |  | Cracking | Differential thermal contraction | Negligible impact on performance Negligible impact on performance | 3 | None | None | None | Never observed before, but possible. |
| 001.003 |  |  | Slippage in clamp / warping | Incorrect mounting | None None | 3 |  |  |  |  |
| 001.004 |  |  | Falls from clamp | Incorrect mounting, cracking. | Reduction in blocking. Increased background on detectors. Possibility of damage to other SPIRE subsystems. | 1 | Increased background loading on photometer or spectrometer detectors (depending on which filter is lost) | None | None | Highly unlikely. Never observed before. Filters and mounts will undergo rigorous qualification tests. |
| 002.001 | 2K Blockers | Attenuates out-of-band radiation | Delamination | Manufacturing error | Loss in transmission. Additional in-band fringing. Decreased instrument sensitivity | 1 | Detected as loss in transmission in the photometer. Any fringing could be observed in the spectrometer. | None | None | Very unlikely – delamination would occur in first few thermal cycles of qualification tests. |
| 002.002 |  |  | Cracking | Differential thermal contraction | Negligible impact on performance Negligible impact on performance | 3 | None | None | None | Never observed before, but possible. |
| 002.003 |  |  | Slippage in clamp / warping | Incorrect mounting | None None | 3 |  |  |  |  |
| 002.004 |  |  | Falls from clamp | Incorrect mounting, cracking. | Reduction in blocking. Increased background on detectors. Possibility of damage to other SPIRE subsystems. | 1 | Increased background loading on photometer or spectrometer detectors (depending on which filter is lost) | None | None | Highly unlikely. Never observed before. Filters and mounts will undergo rigorous qualification tests. |
| 003.001 | 300mK Blockers | Attenuates out-of-band radiation | Delamination | Manufacturing error | Loss in transmission. Additional in-band fringing. Decreased instrument sensitivity | 1 | Detected as loss in transmission in the photometer. Fringing could be observed in the spectrometer if it were either of the spectrometer edge definers which failed in this mode. | None | None | Very unlikely – delamination would occur in first few thermal cycles of qualification tests. |
| 003.002 |  |  | Cracking | Differential thermal contraction | Negligible impact on performance Negligible impact on performance | 3 | None | None | None | Never observed before, but possible. |
| 003.003 |  |  | Slippage in clamp / warping | Incorrect mounting | None None | 3 | None | None | None |  |
| 003.004 |  |  | Falls from clamp | Incorrect mounting, cracking. | Reduction in blocking. Increased background on detectors. Possibility of damage to other SPIRE subsystems. | 1 | Increased background loading on photometer or spectrometer detectors (depending on which filter is lost) | None | None | Highly unlikely. Never observed before. Filters and mounts will undergo rigorous qualification tests. |
| 004.001 | 300mK Edge definers | Defines low pass edge of band. | Delamination | Manufacturing error | Loss in transmission. Additional in-band fringing. Loss of edge definition. Decreased instrument sensitivity. Poorly defined detector channels. | 1 | Detected as loss in transmission in the photometer. Fringing could be observed in the spectrometer if it were either of the spectrometer edge definers which failed in this mode. | None | None | Very unlikely – delamination would occur in first few thermal cycles of qualification tests. |
| 004.002 |  |  | Cracking | Differential thermal contraction | Negligible impact on performance Negligible impact on performance | 3 | None | None | None | Never observed before, but possible. |
| 004.003 |  |  | Slippage in clamp / warping | Incorrect mounting | Warping Possibility of degradation of BDA performance | 1 | None | None | None | Highly unlikely. All 300mK filters are qualified through many thermal cycles using an Invar BDA interface replica. Any warping is very unlikely to damage the BDA. |
| 004.004 |  |  | Falls from clamp | Incorrect mounting, cracking. | Reduction in blocking. Increased background on detectors. Possibility of damage to other SPIRE subsystems. | 1 | Increased background loading on photometer or spectrometer detectors (depending on which filter is lost) | None | None | Highly unlikely. Never observed before. Filters and mounts will undergo rigorous qualification tests. |
| 005.001 | Dichroics | Splits photometric bands. Acts as mirror for wavelengths below edge, transmits longer wavelengths | Delamination | Manufacturing error | Loss in transmission. Additional in-band fringing. Loss of edge definition. Decreased instrument sensitivity for transmitted channels. Poorly defined detector channels. | 1 | Detected as loss in transmission in the photometer MW or LW channels. | None | None | Very unlikely – delamination would occur in first few thermal cycles of qualification tests. |
| 005.002 |  |  | Cracking | Differential thermal contraction | Negligible impact on performance Negligible impact on performance | 3 | None | None | None | Never observed before, but possible. |
| 005.003 |  |  | Warping | Incorrect mounting. Differential thermal contraction. | Warping Loss of spatial purity for reflected channel. No loss of performance for transmitted channel. | 1 | Spatial comparison of photometer channel images | None | None | Highly unlikely. The dichroics are mounted in substantial rings to maintain flatness. |
| 005.004 |  |  | Falls from clamp | Incorrect mounting. | Reduction of blocking and possible partial obscuration for transmitted channels. Loss of reflected channel. | 1 |  | None | None | Highly unlikely. Never observed before. Filters and mounts will undergo rigorous qualification tests. |
| 006.001 | Beam dividers | Transmits 50%, and reflects 50% of incident energy, independent of frequency (in SPIRE band) | Splitting of Mylar substrate | Manufacturing error | Loss of performance over part of element. Degraded performance for beam dividers – ripples introduced to transmission/reflection curve | 1 |  | None | None | This failure mode would appear after the first few thermal cycles and therefore would be eliminated by qualification |
| 006.002 |  |  | Warping | Incorrect mounting | Beam divider loses flatness Loss of frequencies according to degree of warp. Higher frequencies affected first. High degree of warp – lose whole spectrometer. Smaller degree of warp – lose ability to perform high-resolution scan. | 1 |  | None | None | The beam dividers are mounted in substantial rings to maintain flatness. |