Mechanism Control Unit

Failure Mode Effects And Critically Analysis

DRAFT ISSUE TO BE COMPLETED

| Prepared by : | Date : |
| --- | --- |
| Didier Ferrand | 20/09/2001 |
| Checked by : | Date : |
| Dominique Pouliquen | 20/09/2001 |

Document change record

________

| Issue - rev. | Date | Modifications |
| --- | --- | --- |
| draft1 | 20-09-00 | All : first draft |

Distribution list

________

| Jean Louis Auguères | CEA | X |  |
| --- | --- | --- | --- |
| Christophe Cara | CEA | X |  |
| Colin Cunningham | ROE | X |  |
| Brian Stobie | ROE | X |  |
| Ian Pain | ROE | X |  |
| Didier Ferrand | LAM | X |  |
| Michel Jevaud | LAM | X |  |
| Patrick Levacher | LAM | X |  |
| Dominique Pouliquen | LAM | X |  |
| Bruce Swinyard | RAL | X |  |
| Ken King | RAL | X |  |

Acronyms

________

AD		Applicable Document

AVM		Avionics Model

BOL		Begin Of Life

BSM		Beam Steering Mirror

CQM		Cryogenic Qualification Model

EGSE		Electrical Ground Support Equipment

EOL		End of Life

ESA		European Space Agency

FIRST		Far Infra Red and Sub-millimeter Telescope

FM		Flight Model

FPU		Focal Plane Unit

FTS		Fourier Transform Spectrometer

FTSE		FTS warm Electronics

FTSP		FTS Preamplifier for the position encoder signals

H/K		House Keeping

H/W		Hardware

I/F		Interface

LAM		Laboratoire Astrophysique de Marseille

MAC		Multi Axes Controller

MCU		Mechanism Control Unit

N/A		Not Applicable

RAL		Rutherford Appleton Laboratory

RD		Reference Document

ROE		Royal Observatory of Edinburgh

S/C		Spacecraft

SM		Spare Model

SMEC		Spectrograph MEChanism

S/W		Software

TBC		To Be Confirmed

TBD		To Be Define

TBW		To Be Written

TC		Tele-Command

TM		TeleMetry

WE		Warm Electronics

Table of contents

________

1	Introduction	5

1.1	Purpose and Scope	5

1.2	Applicable and reference documents	5

1.2.1	Applicable documents	5

1.2.2	Reference documents	5

2	SYSTEM OVERVIew/SCOPE	6

3	FMECA	7

# Introduction

## Purpose and Scope

The purpose of this document is to describe the potential failure effects of the MCU electronics and software.

## Applicable and reference documents

### Applicable documents

| AD1 | Operating Modes for the SPIRE Instrument (SPIRE-RAL-DOC-000320) |
| --- | --- |
| AD2 | FIRST/Planck Packet Structure Interface Control Document (SCI-PT-IF-07527) |
| AD3 | Spire Spectrometer Mirror Mechanism Subsystem Specification (SPIRE-LAM-PRJ-000460) |
| AD4 | FIRST / Planck Instrument Interface Document Part B (SCI-PT-IIDB/SPIRE-02124) |
| AD5 | DRCU Electrical Interface Control Document (SAp-SPIRE-CCa-24-00) |
| AD6 | SPIRE Instrument Requirements Specification (IRD) (SPIRE-RAL-PRJ-000034) |

### Reference documents

| RD1 | MCU Design Description |
| --- | --- |

# SYSTEM OVERVIew/SCOPE

The MCU is part of the DRCU and has electrical (Main Power Supplies) and mechanical (Electronics Cabinet) interfaces with it.

The MCU is dedicated to the control and monitoring of the following 3 axis of the SPIRE instrument:

- the Spectrometer Mechanism (SMEC). The control is typically based on a scan at a configurable speed, but can be set-up on the basis of a step position control in case of use of the step and integrate mode of the instrument.

- the Chopper and Jiggle axis of the Beam Steering Mirror subsystem. The control is a position step control pattern.

The MCU control electronics includes:

- the MAC Board : common digital control board based on a 21020 DSP including :

- 3 DACs for SMECm and BSMm motor control,

- 1 multiplexed 16 bits ADC for SMEC and BSM analogue signal acquisitions,

- 8 logical inputs

- 12 logical outputs.

- a SMEC Board : analogue electronics for the power amplification of the actuators and acquisition electronics for sensors pre-amplification and conditioning of the SMEC subsystem

- a BSM Board : analogue electronics for the power amplification of the actuators and acquisition electronics for sensors pre-amplification and conditioning of the BSM subsystem

The design is described in the MCU Design Description document (RD1).

# FMECA

| Subsystem/ Component in failure | Failure description | Failure Cause | Identification mean | Failure Effect | Recovering Compensation provision |
| --- | --- | --- | --- | --- | --- |
| Interface electronics | No command can be received | Open connection Driver internal failure | the DPU has no command handshake | MCU out of control All motion stopped and the MAC automatically resets after time-out | Switch to redundant |
|  | Bad command/parameter | Glitch on the line Invalid parameter | Checksum/No recognition of a command | None because the command is verified | Stop of the scan Status report Switch to stand-by mode waiting for another control mode operation |
| DSP and related interface components | Control algorithm diverging | Bad PID parameter configuration | software limits (maximum position error and maximum speed) | Increase of the actuator command up to limitation | Stop of the scan Status report Switch to stand-by mode waiting for another control mode operation |
|  | No control on the DSP | Glitch in the program memory | Watchdog by bus Control FPGA | DSP out of control | Emergency stop on watchdog action and reset by Bus Control FPGA |
| Motor and related PWR amp | Short cut in the motor coil | Internal Failure | I Motor=Iref=Imeas. Backemf=0 | Limitation of current and motion stop after detection | Use of the redundant board + motor coil. |
|  | Motor coil open | Internal failure | Imot=Imeasured=0 Backemf=12V | Motion stopped | Use of the redundant board + motor coil. |
|  | Harness open | Internal failure or no connected | Imot=Imeasured=0 Backemf=0 | Motion stopped | Use of the redundant board + motor coil. |
|  | Measure resistance open | Internal failure of V->I Resistance | Imot=0 Imeasured=high Backemf=0 | Motion stopped | Use of the redundant board + motor coil. |
| Optical encoder and related acquisition electronics | Loss of some individual incremental pulses during closed loop operation | Encoder misaligment | Difference between fiducial mark and position counter | Perturbation on the trajectory | Status report Adjust the position counter on next scan or switch to LVDT/Open loop control degraded mode |
|  | Total loss of incremental encoder pulses | Encoder internal failure | id. | Error vs ramp reference increase -> Increase of the actuator command due to integral effect and position ramp increase -> Excessive motion speed up to speed limitation. -> Emergency stop. | Stop of the scan Status report Switch to stand-by mode waiting for another control mode operation |
|  | Glitch on the absolute position counter (decreasing) |  | Additional position switch on the mechanics | The scan goes to hardware limits | Flyback operation and reset of the absolute position counter |
|  | Glitch on the absolute position counter (increasing) |  | The scan ends before the nominal scan length parameter, and a difference between fiducial mark and position counter occurs at the end of flyback | The scientific scan is not achieved completely | Status report Readjust the position counter on next scan |