# Introduction

This note takes the Naming Convention Specification (AD01) for the Herschel/Planck System Database (HPSDB) and applies it to the SPIRE instrument to provide a recommended naming convention for the SPIRE Mission Implementation Base (MIB), which will be provided conforming to the SCOS2000 Database Import ICD (RD01).

The SPIRE MIB has to allow for definition of parameters from the SPIRE EGSE and other test equipment (e.g. TFCS), which is not delivered. Conventions for naming of these parameters will follow the same format as for instrument parameters. Information specifically related to these parameters is included in this document in blue type.

## Documentation

### Applicable Documents

| AD01 | Herschel/Planck Naming Convention Specification (H-P-1-ASPI-SP-0141), Issue 01/00 |
| --- | --- |

### Reference Documents

| RD01 | SCOS2000 Database Import ICD (S2K-MKS-ICD-0001-TOS-GCI), Issues 5.0 |
| --- | --- |
| RD02 | ASPI comments to version 1.0 of this note (email from F. Chatte, 15th February 2002) |
| RD03 | TFCS Requirements Document (SPIRE-RAL-DOC-001172) |

# Naming Convention

The SPIRE MIB contains Monitor and Command packets, Monitor and Command parameters plus the corresponding calibration curves and displays (command sequences, verification stages, parameter sets, parameter range sets, etc are TBD)

The following naming convention shall be used:

| Item | SCOS field name(s) | Name (alternative, see RD02) | Convention (see AD01) |
| --- | --- | --- | --- |
| Command packet | CCF_CNAME CDF_CNAME PTV_CNAME | SCiiippp | 4580 |
| Command parameter | CPC_PNAME CDF_PNAME | SPiiippp | 5130 |
| Command num calibration | CCA_NUMBR CCS_NUMBR | tttnnnrrr (sss) | 5370 |
| Command txt calibration | PAF_NUMBR PAS_NUMBR | tttnnnrrr (sss) | 5370 |
| Monitor packet | PID_SPID TPCF_SPID PLF_SPID | tttnnnnppp | 4380 |
| Monitor parameter | PCF_NAME OCF_NAME OCP_NAME PLF_NAME PTV_PARNAM | SMiiippp | 5130 |
| Numerical calibration | CAF_NUMBR CAP_NUMBR | tttnnnrrr (sss) | 5370 |
| Textual calibration | TXF_NUMBR TXP_NUMBR | tttnnnrrr (sss) | 5370 |
| Polynomial calibration | MCF_IDENT | tttnnnrrr (sss) | 5370 |
| Numerical display | DPF_NUMBE DPC_NUMBE | SAiiippp | 6100 |
| Graphical display | GPF_NUMBE GPC_NUMBE | SGiiippp | 6110 |
| Scrolling display | SPF_NUMBE SPC_NUMBE | SLiiippp | 6130 |

Where:

- iii is the Theoretical Parameter Identifier. The contents of this field are dependent on the parameters available, but a format is proposed: The first character is the Subsystem ID (See section 3.1) and the third character is the Parameter Unit ID (See section 3.5).

- nnn and nnnn are running numbers starting at zero and incrementing

- ttt is the System Element number (see section 3.1)

- rrr is the Real Element number (see section 3.3)

- ppp is the Position Identifier  (see section 3.2)

- sss is the Alternative Identifier (see section 3.4)

# Identifiers

Identifiers are defined in AD01 with SPIRE allocated particular numbers and characters for the various fields. This section defines how these are used in the SPIRE naming convention.

## System Elements

Each distinct type of subsystem in the instrument (called a System Element Type) is assigned a unique number and a set of identifiers corresponding to the subsystems it contains:

| System Element Type | Subsystem ID(s) | Number |
| --- | --- | --- |
| OBS | T (Telemetry) 0 (Operations) | 480 |
| DPU | D (Data) | 490 |
| DCU | B (Bias) D (Data/DAQ) L (LIA) P (Photometer) 2 (Photometer SW) 3 (Photometer MW) 5 (Photometer LW) 8 (Photometer MW+LW) T (Thermal Control) S (Spectrometer) 0 (Spectrometer SW) 1 (Spectrometer LW) | 500 |
| MCU | D (Data) C (Chop Axis) J (Jiggle Axis) S (SMEC) T (Trace) L (Latch) | 510 |
| SCU | D (Data/DAQ) C (Calibrator) H (Htr) K (SubK) T (Temperature) P (Photometer Bias) S (Spectrometer Bias) L (Photometer LIA) M (Spectrometer LIA) | 520 |
| EGSE | C (CDMS Simulator) D (DRCU Simulator) E (Engineering Simulator) S (Shutter) | 528 |
| TFCS | B (Black Body) C (Cryostat) F (FTS) M (Beam Monitor) L (Laser) H (Chopper) P (Power Supply) T (Telescope Simulator) | 529 |

## Position Identifiers

Each ‘real’ model of the instrument is composed of a set of System Elements. This may include more than one System Element of any given type. Each distinct System Element for each instrument model is assigned a unique number. This unique number is also used as the Position Identifier.

|  | Model |
| --- | --- |
| System Element | AVM | QM | FM | FS |
| OBS | 480 | 480 | 480 | 480 |
| DPU | 4901 4912 | 4901 4912 | 4901 4912 | 4901 4912 |
| DCU | 500 | 500 | 500 | 500 |
| MCU | 510 | 510 | 510 | 510 |
| SCU | 520 | 520 | 520 | 520 |

1. Valid for prime element

2. Valid for redundant element

## Real Element Numbers

These numbers identify individual configurations of each System Element (there may be more than one configuration if, for example, electronic boards have to be exchanged during testing). The table below gives the Real Element Number for the first configuration of the System Element. They should be incremented by 1 for each new configuration.

|  | Model |
| --- | --- |
| System Element | AVM | QM | FM | FS |
| OBS | 100 | 300 | 500 | 700 |
| DPU | 1001 2002 | 3001 4002 | 5001 6002 | 7001 8002 |
| DCU | 100 | 300 | 500 | 700 |
| MCU | 100 | 300 | 500 | 700 |
| SCU | 100 | 300 | 500 | 700 |

1. Valid for prime element

2. Valid for redundant element

## Alternative IDs

This number will be used to identify Calibration Curves if SCOS2000 is incapable of handling 8 character field names. The following assignment is made.

| System Element Type | Range of values |
| --- | --- |
| OBS | 500-549 |
| DPU | 550-599 |
| DCU | 600-649 |
| MCU | 650-699 |
| SCU | 700-749 |

## Parameter Unit IDs

This number will be part of the Theoretical Parameter Identifier, identifying the parameter units.

| Parameter Unit ID | Parameter Unit |
| --- | --- |
| A | Current (Amps) |
| B | Limit (Boundaries) |
| E | Error |
| F | Status (Flag) |
| H | Frequency (Hertz) |
| K | Temperature (Kelvin) |
| L | Lower Limit |
| M | Mode |
| N | Number, Count |
| P | Position |
| R | Phase (Radians) |
| S | Speed, Velocity |
| T | Time, Period |
| U | Upper Limit |
| V | Voltage (Volts) |
| W | Power (Watts) |