# DISTRIBUTION LIST

| SPIRE-Project | Doug Griffin |  |
| --- | --- | --- |
|  | Bruce M. Swinyard |  |
|  | Matt Griffin |  |
| UK ATC | Colin Cunningham |  |
|  | Gillian Wright |  |
|  | Ian Pain |  |
|  | Brian Stobie |  |
|  | Tom Paul |  |
|  | Ian Laidlaw |  |
| UoC | Peter Hargrave |  |
| MSSL | Berend Winter |  |
| LAM | Didier Ferrand |  |
|  | Dominique Pouliquen |  |
|  | Patrick Levacher |  |

# Record of Issue

| Date | Index | Remarks |
| --- | --- | --- |
| 10 Jan 2002 | 0.1 | Creation of the document (break out from Design description presented art DDR) |
| 7. Feb.02 | 1.0 | Minor updates and first Issue |

# Table of contents

DISTRIBUTION LIST	1

Record of Issue	1

Table of contents	2

1.	Documents	3

1.1	Applicable documents	3

1.2	Reference documents	3

1.3	Glossary	4

2.	ICD Philosophy	5

3.	BSM ICD Master Reference Table	5

4.	Description of ICD contents	8

4.1	Top level system	8

4.2	Structural interface	8

4.3	PCAL interface	8

4.4	Launch latch interface	8

4.5	Optical interface	8

4.5.1	Finish	8

4.5.2	Mirror Interfaces	8

4.5.3	Baffle Interface	8

4.6	Harness	9

4.7	BSM warm electronics (BSMe)	9

5.	Note on ICD drawing numbers	9

DISTRIBUTION LIST	1

Record of Issue	1

Table of contents	2

1.	Documents	3

1.1	Applicable documents	3

1.2	Reference documents	3

1.3	Glossary	4

2.	Interface Control Documents	5

2.1	ICD Philosophy	5

2.2	BSM ICD Master Reference Table	5

2.3	Description of ICD contents	8

2.3.1	Top level system	8

2.3.2	Structural interface	8

2.3.3	PCAL interface	8

2.3.4	Launch latch interface	8

2.3.5	Optical interface	8

2.3.6	Harness	8

2.3.7	BSM warm electronics (BSMe)	9

2.4	Note on ICD drawing numbers	9

# Documents

## Applicable documents

|  | Title | Author | Reference | Date |
| --- | --- | --- | --- | --- |
| AD2 | BSM ICD drawing | I.Pain | ATC drawing number: SPIRE-BSM-021-002-001 | 7.Feb.02 |
| AD3 | ICD drawing: Structure: BSM | MSSL | Drg No A2/5264/907 issue 6 |  |
| AD4 | ICD Structure - Mechanical I/F | B.Winter | MSSL/SPIRE/SP004.11 (formerly SPIRE-MSS-PRJ-00617) | 29.Nov.01 |
| AD5 | SPIRE Harness Definition | D.K.Griffin | SPIRE-RAL-PRJ-000608 v0.3 | 30.May.01 |
| AD6 | TBD (harness run mechanical details) |  | TBD |  |
| AD7 | Master Assembly Icd 3d Model And 2d Views (Blank) |  | SPI-BSM-PRJ-0713-a | TBW |
| AD8 | Structure, Thermometry ICD | I Pain | SPI-BSM-PRJ-0713-b | 7 Feb 2001 |
| AD9 | PCAL ICD | I Pain | SPI-BSM-PRJ-0713-c | 19 Jul 2001 |
| AD10 | Launch Latch ICD | I Pain | SPI-BSM-PRJ-0713-d | 20 Jul 2001 |
| AD11 | Optics ICD |  | SPI-BSM-PRJ-0713-e | TBW |
| AD13 | MCU ICD | B Stobie | SPI-BSM-PRJ-0713-f | 20 Jul 2001 |
| AD14 | FPU Simulator ICD |  | SPI-BSM-PRJ-0713-g | TBW |
| AD15 | Instrument Simulator ICD |  | SPI-BSM-PRJ-0713-h | TBW |

## Reference documents

|  | Title | Author | Reference | Date |
| --- | --- | --- | --- | --- |
| RD 1 | Thermal Configuration Control Document | S.Heys | SPIRE-RAL-PRJ-000560 | 18.Apr.01 |

## Glossary

| AD | Applicable Document | MAC | Multi-Axis Controller |
| --- | --- | --- | --- |
| CEA | Commissariat à l' Energie Atomique | MCE | Mechanism Control Electronics |
| CDR | Critical Design Review | MGSE | Mechanical Ground Support Equipment |
| CNES | Centre National des Etudes Spatiales | MPIA | Max Planck Institute for Astronomy |
| CoG | Center of Gravity | MSSL | Mullard Space Science Laboratory |
| CQM | Cryogenic Qualification Model | NA | Not Applicable |
| DDR | Detailed Design Review | OGSE | Optical Ground Support Equipment |
| DESPA | Département des Etudes SPAtiales | PFM | ProtoFlight Model |
| DM | Development Model | RAL | Rutherford Appleton Laboratory |
| DRCU | Digital Read-out and Control Unit | RD | Reference Document |
| EGSE | Electrical Ground Support Equipment | BSM | Beam Steering Mirror |
| Herschel | Far InfraRed Space Telescope | UK ATC | United Kingdom Astronomy Technology Centre |
| FPU | Focal Plane Unit | BSM | Beam Steering Mirror |
| FS | Flight Spare model | SPIRE | Spectral and Photometric Imaging REceiver |
| LAM | Laboratoire d'Astrophysique de Marseille | TBC | To Be Confirmed |
| FTS | Fourier Transform Spectrometer | TBD | To Be Defined |
|  |  | WE | Warm Electronics |

# ICD Philosophy

The BSM interfaces with other subsystems in the SPIRE instrument. The interface to each sub-system is specified in the relevant Interface Control Document. For each ICD there will be:

- An ICD document.

- Where required, an ICD drawings (or equivalent electronic design information) with distinct drawing numbers. A copy of the drawings will be included within the document, probably in postscript or pdf format.

All these ICD’s are will be collected internally by the ATC, and issued as a single document SPI-BSM-PRJ-0713. as an annex to this document (the BSM Design Description.)  Each ICD sub-document annex will be self-contained, with a version number and date controlled internally.

# BSM ICD Master Reference Table

This section presents a table showing:

- which institute UK ATC interfaces to,

- the relevant documents the interfacing institute is supplying to the rest of SPIRE,

- which UK ATC documents their ICD information is fed from.

Whenever UK ATC update and release interface information with any party we will update the relevant annex and the master table, as well as the design description document.master (this document).

Although this may leads to multiple updates of the design descriptionBSM ICD to all parties, this is felt essential in order to ensure the design and interfaces are kept in lock-step.

Table 1:  BSM interface master reference table

| ID | Sub-System | Organization responsible | External ICD document | Internal ATC ICD document | Internal ATC ICD drawing/ file |
| --- | --- | --- | --- | --- | --- |
| 1 | BSM-SPIRE | RAL | Instrument Requirements Document (IRD). SPIRE-RAL-PRJ-000034 v0.30 May.00 | SPIRE-ATC-PRJ-000713 | SPIRE-BSM-021-001-001 |
| 2.1 | Structure – BSM 2D drawing | MMSL | MSSL/SPIRE/SP004.11 (formerly SPIRE-MSS-PRJ-00617) Drg No A2/5264/907 issue 6 | SPIRE-ATC-PRJ-000713 | SPIRE-BSM-021-002-001 |
| 2.2 | Structure – BSM 3D solid | MMSL |  |  | SPIRE-BSM-021-002-002 (IGES file) |
| 2.3 | Thermometry | RAL | TBD |  | SPIRE-BSM-021-002-003 |
| 3 | Photometer Calibration Source - BSM | UoW, Cardiff | TBD | SPIRE-ATC-PRJ-000713 | SPIRE-BSM-021-003-001 |
| 4 | Launch Latch – BSM | LAM (TBC) | Spectrometer mirror mechanism design description LAM.SPI.PJT.NOT.200008 Ind 3 | SPIRE-ATC-PRJ-000713 | SPIRE-BSM-021-004-001 |
| 5.1 | Optics – external finish | LAM | Optical System Design Description SPIRE-LAM-PRJ-000447 Draft 1 18.Dec.00 | SPIRE-ATC-PRJ-000713 | SPIRE-BSM-021-005-001 |
| 5.2 | Optics – BSM | RAL | ??? |  | SPIRE-BSM-021-005-002 |
| 5.3 | Baffles – BSM | RAL | ??? |  | SPIRE-BSM-021-005-003 |
| 6 | Cryo-Harness | RAL / MSSL | SPIRE Harness Definition. SPIRE-RAL-PRJ-000608 Issue: 0.3 30.May.01 Harness routing : TBD (MSSL) | SPIRE-ATC-PRJ-000713 | SPIRE-BSM-021-006-001 |
| 7.1 | MCU-BSM | LAM | ??? | SPIRE-ATC-PRJ-000713 | SPIRE-BSM-021-007-001 |
| 7.2 | On Board Software - BSM | LAM | ??? |  | SPIRE-BSM-021-007-002 |
| 8 | Photometer Bolometer Arrays - BSM | MSSL | ICD Structure - Mechanical I/F SPIRE-MSS-PRJ-000xxx v1.0 April 2001 | Sub-System Specification EMC/ exported vibration ??? |  |
| 9 | Spectrometer Bolometer Arrays - BSM | MSSL | ICD Structure - Mechanical I/F SPIRE-MSS-PRJ-000xxx v1.0 April 2001 | Sub-System Specification EMC/ exported vibration ??? |  |
| 10 | FPU Simulator - BSM | TBD | TBD | SPIRE-ATC-PRJ-000713 |  |
| 11 | Instrument Simulator - BSM | TBD | TBD | SPIRE-ATC-PRJ-000713 |  |

# Description of ICD contents

The paragraph numbers below refer to the ICD numbers in table 1 above, eg 4.1refers to interface '1', etc.

## Top level system

This is the ATC’s top-level assembly including optical bench, optical beams, cryo-harness, thermal strap, thermometry  and any other system level interfaces. A multi-sheet drawing (SPIRE-BSM-021-001-001), is used to show all relevant interfaces clearly, though many of these items will be themselves references to other institutions files (e.g. RAL IGES optical beams).

This document is mainly used for internal consistency checks of external data supplied from a variety of sources, and may not necessarily be formally communicated to any one external party. It may however, tie in well with the IRD or IID-B.

## Structural interface

- The main structural interface drawing (SPIRE-BSM-021-002-001), includes a layout of the BSM assembly (SPIRE-BSM-020-001) showing the principal dimension, to the mirror surface from the interface, as well as the shoe dimensions, mounting details and the full space envelope. 3d information views would also be shown.  A mass estimate, CoG, MoI, principle resonant modes are also included.

- Additionally, a full IGES or STEP interface file is allocated a distinct ICD number (SPIRE-BSM-021-002-002) and will be treated as the master 3D interface with MSSL.

- Thermometry.

## PCAL interface

PCAL interface drawing - a toleranced space envelope sketch of PCAL, also indicating distance from an optical reference point (possibly cross-referenced to one of the other ICD's). Also shows Mass, nominal CoG,, details connector position.

## Launch latch interface

This comprises a toleranced space envelope sketch. Also shows Mass, nominal CoG and electrical information. Depending on procurement process selected (TBD) this could alternately be treated as a straight procurement-to-drawing and the ICD deleted.

## Optical interface

### Finish

Specifies the external optical finish of BSM assembly.

### Mirror Interfaces

This shows mirror position (toleranced dimensions tying into the BSM subsystem spec), size, range of travel, surface finish (or calls mirror part drawing for this - we don't want it to appear twice!).

### Baffle Interface

This shows baffle shape and position (toleranced dimensions tying into the BSM subsystem spec), surface finish (or calls mirror part drawing for this - we don't want it to appear twice!). We may call 'back' on the top level SPIRE-BSM-021-001 for any issues to do with optical beams supplied as IGES files by RAL.

## Harness

Harness interface and grounding scheme. We probably also absorb an electrical drawing into the Pro/E or pro-intralink scheme here

## BSM warm electronics (BSMe)

- Warm electronics drawings and model.

- Software interfaces to drive BSMe with MCU

# Note on ICD drawing numbers

These are contained within the same drawing management system as the main models, but are identified distinctly by drawing description/title and also be an allocated number set.

For a given build the design data is : SPIRE-BSM-bb0-aaa-ccc

Where bb = build (e.g. Development model = 02), 0 identifies design data, aaa = assembly, ccc = component

However for an ICD the scheme is: SPIRE-BSM-bb1-iii-fff

Where bb = build (e.g. Development model = 02), 1 identifies interface data, iii = interface ID, fff = ICD file

Annexes - Table of Contents

A.	MASTER ASSEMBLY ICD 3D MODEL AND 2D VIEWS (BLANK)

B.	STRUCTURE, THERMOMETRY

C.	PCAL

D.	LAUNCH LATCH

E.	OPTICS (BLANK)

F.	MCU

G.	FPU SIMULATOR (BLANK)

H.	INSTRUMENT SIMULATOR (BLANK)

# Footnotes

.i.e. responsible for feeding ICD info upwards to SPIRE system design