| Prepared by |  |  |  |
| --- | --- | --- | --- |
|  | A.J. Matheson | Date |  |
| Checked by |  |  |  |
|  | D.J. Parker | Date |  |
| Approved by |  |  |  |
|  | D.L. Smith | Date |  |

# Distribution

| RAL | J. Payne |
| --- | --- |
|  | M. Ferlet |
|  | K. King |
|  | T. Lim |
|  | S. Sidher |
|  | B. Swinyard |
| Cardiff | P. Hargrave |

# Document Change Record

| Issue | Date | Affected Pages | Description |
| --- | --- | --- | --- |
| Draft 2 | 28/11/2001 | All | Incorporation of comments on Draft 1 |
| Draft 3 | 12/02/2002 | All | Changes by D.L. Smith |
| Draft 4 | 25/02/2002 | All | Changes by D.L. Smith following meeting with Dave Parker and Ken King |

CONTENTS

Distribution	2

Document Change Record	2

1.	SCOPE OF DOCUMENT	4

2.	DOCUMENTS	4

2.1	Applicable Documents	4

3.	Acronyms	4

4.	Introduction	5

5.	General Requirements	7

5.1	System	7

5.2	Data Logging	7

5.3	Display	7

5.4	Monitoring	9

5.5	Interface to EGSE	9

5.5.1	TFCS Telemetry	9

5.5.2	TFCS Commands	9

6.	Phase A Requirements	10

6.1	Cryostat Monitoring and Control	10

6.1.1	Temperature Logging and Monitoring	10

6.1.2	Cryogen Level	11

6.1.3	Pressure	11

6.1.4	Cryostat temperature control	13

6.1.5	Interface to EGSE	13

6.2	Cold Blackbody	15

6.2.1	Cold Blackbody Software Requirements	15

6.2.2	EGSE Interface	16

6.3	Telescope Simulator	18

6.3.1	System Description	18

Axis	19

6.3.2	Software Requirements	21

6.3.3	EGSE Interface	21

6.4	Instrument Monitoring	23

6.4.1	Heater Power	23

6.4.2	Temperature Monitoring	23

7.	Phase B Requirements	25

7.1	Instrument Power Supply	25

7.2	Beam Monitor	25

7.3	Chopper	25

7.4	Laser Line Selection	25

7.5	Fourier Transform Spectrometer	25

# SCOPE OF DOCUMENT

This document specifies the requirements for the SPIRE Test Facility Control System (TFCS).  Both the user and software requirements are incorporated in this document.

The TFCS will be developed in two phases.  The first, phase A, will cover all the functions that are required for the cryostat commissioning and the STM instrument tests.  Phase B will cover the remaining functions that are required for the CQM instrument tests.  This release of this document will reflect these development phases.

# DOCUMENTS

## Applicable Documents

| Ref | Document | Doc. No. | Date |
| --- | --- | --- | --- |
| AD1 | SPIRE Test Facility Requirements Specification | SPIRE-RAL-PRJ-000463 |  |
| AD2 | Herschel EGSE Packet Router ICD | SRON-G/EGSE/ICD/2001-xxx |  |
| AD3 | TFCS TM/TC Packet ICD | SPIRE-RAL-DOC- |  |
| AD4 | SPIRE STM Thermal Balance Test Specification | Draft 2 | 27-Jan-2002 |

# Acronyms

| CBB | Cold BlackBody |
| --- | --- |
| CQM | Cryogenic Qualification Model |
| EGSE | Electrical Ground Support Equipment |
| FIR | Far InfraRed |
| FTS | Fourier Transform Spectrometer |
| ICD | Interface Control Document |
| PFM | Proto-Flight Model |
| SPIRE | SPectrometer and Infrared REceiver |
| STM | Structural Test Model |
| TFCS | Test Facility Control System |
| VI | Virtual Instrument |

# Introduction

This section gives a brief description of the Test Facility Control System, TFCS.  The TFCS will provide control and monitoring for the SPIRE calibration cryostat and sources.  The key functions will be to:

- Monitor the cryostat temperatures, vacuum pressure and the cryogen levels.

- Control the temperatures within the cryostat, namely the 1.7K, 4.2K and 10K stages.

- Monitor the cold-blackbody temperatures

- Control the cold-blackbody heater

- Control the cold-blackbody flip mirror and heat shunt.

- Control and monitor the telescope simulator

- Monitor the output of the beam monitor.

- Record the selected laser wavelength.

- Set and read back the chopper frequency.

- Provide a 28V power supply to the instrument.

- Display parameters

- Log the data to a file

- Receive telecommand packets from the SPIRE EGSE to control the TFCS subsystems

- Send telemetry packets from the TFCS subsystems to the SPIRE EGSE.

In addition to the above capabilities, it shall be possible to

- Monitor and log the STM instrument temperatures

- Control and monitor the Fourier Transform Spectrometer, FTS.

It is not necessary that these be performed by the TFCS, but they will have some of the functions and interfaces.

The TFCS will be used for the complete operational cycle of the test cryostat:

- Pump-down

- Cool-down

- Instrument testing (thermal, performance tests, calibration)

- Warm Up

- Let-up to air

In all phases the cryostat temperatures and cryogen levels will be logged automatically and will be displayed on a computer screen as required. The vacuum pressure must be recorded and displayed throughout the tests except during instrument testing where the pressure gauge head could be a potential source of stray light and affect the instrument performance.  However, periodic checks of the vacuum pressure will still be required to confirm that vacuum is being maintained.

The cold blackbody will be used as source of known radiance for performance and calibration tests.  The blackbody will be nominally at 4K when not in use and heated up to 30K when used.  A flip mirror will allow SPIRE to view the blackbody cavity.  A heat shunt will be employed so that the blackbody plate can be returned to 4K.

The telescope simulator will present SPIRE with an f8.68 beam representative of the Herschel telescope.  Due to restrictions on space within the test laboratory, the full SPIRE field of view cannot be completely filled.  To ensure that the calibration can be performed for all SPIRE detectors, a series of moving fold mirrors is used to scan the image of a point source across the field of view, while maintaining the focus.  A control law has been defined that will be used as the basis of the control software.

A Fourier Transform Spectrometer is being developed by Cardiff University and will be used to measure the spectral response of SPIRE.  The TFCS user requirements for the FTS will not be defined in this issue of the URD.

The output of the telescope simulator will be picked off by a beam splitter and measured using a reference detector (probably a Golay cell).  The output of the detector will be measured and recorded by the TFCS to allow correlation with the SPIRE measurements.

The wavelength selection of the FIR laser will be performed Manually with a Fabry Perot.  The TFCS will allow the selected wavelength to be entered and recorded by the EGSE.

# General Requirements

## System

All functions of the TFCS will be performed from a single Pentium III PC running Windows NT-4.

The TFCS PC shall have sufficient expansion slots to incorporate

- A GPIB, IEEE-488 interface card

- 2 (TBC) National Instruments data acquisition cards.

- TBD additional serial ports.

The TFCS PC shall have a network link to the SPIRE EGSE.

The TFCS shall be configured so that it can either be controlled as a stand-alone system or remotely from SCOS-2000.

The TFCS shall be time synchronised to the SPIRE EGSE.

The TFCS software shall be written in LabVIEW 6i™.

## Data Logging

All TFCS data must be recorded to a log file.

It shall be possible to stop and restart data logging at any time.

A new log file shall be generated whenever logging restarts.

Existing log files must not be overwritten when logging is started/restarted.

It shall be possible to concatenate data from several log-files.

## Display

The temperatures, heater settings and measured powers, vacuum pressures and cryogen levels and cold-blackbody mirror position and heat shunt position shall be displayed for real-time and archived data for the full SPIRE test period.

The display will be configurable by the user to show data from parameters of interest over a selected time range.  The configuration settings shall include as a minimum:

- The parameters to be displayed

- Graphical or Text output

- The output format (precision, linestyle, colour)

- Display type (Linear or Logarithmic)

- Time/Date range

- Time/Date resolution

- Parameter range

- Parameter resolution

- Alarm limits

It shall be possible to call up displays independently of whether the TFCS is operating as a stand-alone system, or from the TFCS.

The configurations of the displays shall be saved to an editable text file so that a particular display format can be reused.

It shall be possible to produce an electronic copy of the display  (i.e. pdf file)

It shall be possible to play back data through display system.

Temperature data will be compiled into a data packet for transmission to the rest of the EGSE systems.

## Monitoring

It shall be possible for the user to define upper and lower alarm settings.

The TFCS shall monitor all parameters and check for out of limits conditions.

An audible alarm shall be triggered in the case of a parameter being out of limits.

## Interface to EGSE

### TFCS Telemetry

The data from all of the TFCS subsystems will be incorporated into telemetry packets to be sent to the SPIRE EGSE by the packet router.  The format and content of the telemetry packets will be defined in the TFCS TM/TC Packet ICD (AD3).

### TFCS Commands

Telecommands issued by SCOS-2000 to the TFCS subsystems will be sent via the packet router.  The format and content of the telecommand packets will be defined in the TFCS TM/TC Packet ICD (AD3).

# Phase A Requirements

## Cryostat Monitoring and Control

### Temperature Logging and Monitoring

#### Thermometers

Table 1 below specifies the positions, type, measurement range, accuracy and resolution of cryostat thermometers.  The accuracy of the sensors is determined by the sensor characteristics, the calibration and the performance of the monitoring units.  The TFCS shall ensure that the full measurement ranges are covered and that the temperatures are recorded to at least the resolutions stated in the Table 1.

Table 1: Cryostat thermometer locations, type, measurement range, accuracy and resolution

| Sensor | Location | Type | Temp Range (K) | Accuracy | Resolution |
| --- | --- | --- | --- | --- | --- |
| No. |  |  | min | max | (+/- K) | (K) |
| 1 | 77K Shield | Endcap 1 | Si Diode | 60 | 325 | 1 | 0.1 |
| 2 |  | Endcap 2 | Si Diode | 60 | 325 | 1 | 0.1 |
| 3 |  | Filter Flange |  | 60 | 325 | 1 | 0.1 |
| 4 | 10K Shield | Inlet Pipe | Si Diode | 4.2 | 325 | 0.1 | 0.01 |
| 5 |  | Outlet Pipe | Si Diode | 4.2 | 325 | 0.1 | 0.01 |
| 6 |  | Endcap 1 | Si Diode | 4.2 | 325 | 0.1 | 0.01 |
| 7 |  | Endcap 2 | Si Diode | 4.2 | 325 | 0.1 | 0.01 |
| 8 |  | Cylinder End 1 | Si Diode | 4.2 | 325 | 0.1 | 0.01 |
| 9 |  | Cylinder Centre | Si Diode | 4.2 | 325 | 0.1 | 0.01 |
| 10 |  | Cylinder End 2 | Si Diode | 4.2 | 325 | 0.1 | 0.01 |
| 11 |  | Filter Flange | Si Diode | 4.2 | 325 | 0.1 | 0.01 |
| 12 | 10K Support | Vacuum Vessel Standoff 1 | Si Diode | 4.2 | 325 | 0.1 | 0.01 |
| 13 | Frame | Vacuum Vessel Standoff 2 | Si Diode | 4.2 | 325 | 0.1 | 0.01 |
| 14 |  | Vacuum Vessel Standoff 3 | Si Diode | 4.2 | 325 | 0.1 | 0.01 |
| 15 |  | Vacuum Vessel Standoff 4 | Si Diode | 4.2 | 325 | 0.1 | 0.01 |
| 16 | HOB | Phot JFET Enclosure | Si Diode | 4.2 | 325 | 0.1 | 0.01 |
| 17 | Simulator | Spec JFET Enclosure | Si Diode | 4.2 | 325 | 0.1 | 0.01 |
| 18 |  | FPU Foot 1Interface | Si Diode | 4.2 | 325 | 0.1 | 0.01 |
| 19 |  | FPU Foot 2 Interface | Si Diode | 4.2 | 325 | 0.1 | 0.01 |
| 20 |  | FPU Foot 3 Interface | Si Diode | 4.2 | 325 | 0.1 | 0.01 |
| 21 |  | Harness Sink - RF Filters | Si Diode | 4.2 | 325 | 0.1 | 0.01 |
| 22 |  | Harness Sink - Phot JFET | Si Diode | 4.2 | 325 | 0.1 | 0.01 |
| 23 |  | Harness Sink - Spec JFET | Si Diode | 4.2 | 325 | 0.1 | 0.01 |
| 24 | 4.2K Stage | Vessel Top | Cernox | 1.4 | 325 | 0.05 | 0.001 |
| 25 |  | Vessel Bottom | Cernox | 1.4 | 325 | 0.05 | 0.001 |
| 26 |  | FPU Level 1 Strap interface | Cernox | 1.4 | 325 | 0.05 | 0.001 |
| 27 | 1.7K Stage | Vessel - Bottom | Cernox | 1.4 | 325 | 0.01 | 0.001 |
| 28 |  | FPU Box Strap interface | Cernox | 1.4 | 325 | 0.01 | 0.001 |
| 29 |  | FPU Pump Strap interface | Cernox | 1.4 | 325 | 0.01 | 0.001 |
| 30 |  | FPU Evap Strap interface | Cernox | 1.4 | 325 | 0.01 | 0.001 |
| 31 |  | Vessel – Top | Cernox | 1.4 | 325 | 0.01 | 0.001 |

#### Conditioning

Lakeshore type 218 units will be used to monitor the temperature sensors. Each unit is designed to monitor up to 8 thermometers of both types specified in Table 1.  The monitoring units will be remotely controlled from the TFCS via an IEEE 488 interface.

#### Logging Requirements

The temperatures of all the thermometers listed in table 1 shall be automatically recorded by the TFCS.  The update rate will be every 16 seconds (TBC) for all sensors.

All temperatures shall be logged and monitored continuously throughout the tests.

No other process on the TFCS may interrupt temperature logging unless a specific instruction has been sent.

### Cryogen Level

The cryostat will have two level sensors, one for liquid nitrogen and one for liquid helium.

#### Sensors

The cryogen level sensors will be supplied and installed by AS Scientific.

A series of 4x100 platinum resistance thermometers (PT100) will be used to give a coarse indication of the level of liquid nitrogen.  At 77K the PT100 resistance is 20.2 and increases with temperature.  To avoid false readings when the sensor is above the liquid and in gas, a 100mA current to ensure that the resistance has some self-heating.  The measured voltage will be between 2V and 10V.

The liquid helium sensor consists of a superconductive wire in a stainless steel sheath.  The portion of the wire above the helium remains resistive while the portion below the liquid surface will be superconducting, i.e. 0. The voltage across the wire is proportional to the fraction of the wire above the surface.  Typically a 100mA current is applied across the probe to give a voltage between 0 and 40V depending on the normal wire resistance.

#### Data Logging

The level sensors will be polled every 16 seconds (TBC).

No other process on the TFCS may interrupt the level logging and monitoring unless a specific instruction has been sent.

The liquid nitrogen and helium levels shall be logged and monitored continuously throughout the tests.

There will be no automatic filling of LN2 or He.

### Pressure

Pressure monitoring will be provided for the pump-down and let-up phases, and periodically at non-critical times during instrument tests.

#### Sensors and Conditioning

The pressure inside the cryostat will be measured using compact Pirani gauges (Pfeiffer Vacuum TPR265) and a compact full range gauge (Pfeiffer Vacuum PKR251) connected to a dual-channel measurement & control unit for compact gauges (Pfeiffer Vacuum TPG262). The Measurement & control unit has an RS232 interface connector and can be driven from a serial port on the TFCS PC.

Table 2: Pressure gauges and ranges

| Sensor Type | Range | Accuracy | Resolution |
| --- | --- | --- | --- |
| Pirani | 1bar ( 5 x 10-4 mbar | 10% of value | 1% of value |
| FullRange | 1bar ( 10-8 mbar | 10% of value | 1% of value |

#### Software

The pressure gauges will be polled every second (TBC).

No other process on the TFCS may interrupt the pressure monitoring unless a specific instruction has been sent.

The pressure readings shall be logged and monitored continuously throughout the tests except when the SPIRE instrument is switched on.

It shall be possible to disable the pressure monitoring without affecting the overall logging system (i.e. temperature, levels…).  When the pressure monitoring is disabled the pressure gauges must be switched off.

It shall be possible to reactivate the pressure gauges and monitoring without having to restart the overall logging system.

The rate of change of vacuum pressure shall be calculated and displayed.

### Cryostat temperature control

#### Heaters

Table 3: Location of cryostat heaters

| Heater No. | Location | Resistance | Temperature Range | StabilitymK/ hr | Power Dissipation |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Min | Max |  | Nom | Max |
| 1 | L0 Interface plate – 1 | 50 | 1.6 | 2.2 | TBD | TBD | TBD |
| 2 | L0 Interface plate – 2 | 50 | 1.6 | 2.2 | TBD | TBD | TBD |
| 3 | L0 Interface plate – 3 | 50 | 1.6 | 2.2 | 9 | TBD | TBD |
| 4 | L1 Interface plate | 50 | 4.2 | 7.0 | 120 | TBD | TBD |
| 5 | Shield | TBD | 9.0 | 15.0 | 70 | TBD | TBD |
| 6 | HOB Simulator | TBD | 9.0 | 15.0 | 70 | TBD | TBD |

### Interface to EGSE

#### Telemetry

The parameters listed in Table 4 shall be transmitted to SCOS-2000 as telemetry packets.

Table 4: Cryostat parameters to be transmitted to SCOS-2000

| Ref: | Parameter Name |
| --- | --- |
| 1 | Date |
| 2 | Time |
| 3 | Temperature Logging Enabled/Disabled |
| 4 | Pressure Logging Enabled/Disabled |
| 5 | Cryogen level logging Enabled/Disabled |
| 6 | Pirani Gauge Pressure |
| 7 | Full Range Gauge Pressure |
| 8 | N2 Level |
| 9 | He Level |
| 10 | 77K Shield Endcap 1 Temperature |
| 11 | 77K Shield Endcap 2 Temperature |
| 12 | 77K Shield Filter Flange Temperature |
| 13 | 10K Shield Inlet Pipe Temperature |
| 14 | 10K Shield Outlet Pipe Temperature |
| 15 | 10K Shield Endcap 1 Temperature |
| 16 | 10K Shield Endcap 2 Temperature |
| 17 | 10K Shield Cylinder End 1Temperature |
| 18 | 10K Shield Cylinder Centre Temperature |
| 19 | 10K Shield Cylinder End 2 Temperature |
| 20 | 10K Shield Filter Flange Temperature |
| 21 | Vacuum Vessel Standoff 1 Temperature |
| 22 | Vacuum Vessel Standoff 2 Temperature |
| 23 | Vacuum Vessel Standoff 3 Temperature |
| 24 | Vacuum Vessel Standoff 4 Temperature |
| 25 | HOB Sim Phot JFET Enclosure Temperature |
| 26 | HOB Sim Spec JFET Enclosure Temperature |
| 27 | HOB Sim FPU Foot 1Interface Temperature |
| 28 | HOB Sim FPU Foot 2 Interface Temperature |
| 29 | HOB Sim FPU Foot 3 Interface Temperature |
| 30 | HOB Sim Harness Sink - RF Filters Temperature |
| 31 | HOB Sim Harness Sink - Phot JFET Temperature |
| 32 | HOB Sim Harness Sink - Spec JFET Temperature |
| 33 | 4K Vessel Top Temperature |
| 34 | 4K Vessel Bottom Temperature |
| 35 | 4K FPU Level 1 Strap interface Temperature |
| 36 | 1.7K Vessel - Bottom Temperature |
| 37 | 1.7K FPU Box Strap interface Temperature |
| 38 | 1.7K FPU Pump Strap interface Temperature |
| 39 | 1.7K FPU Evap Strap interface Temperature |
| 40 | 1.7K Vessel – Top Temperature |
| 41 | Level 0 Interface 1 Set Point Temperature |
| 42 | Level 0 Interface 1 Set Point Temperature |
| 43 | Level 0 Interface 1 Set Point Temperature |
| 44 | Level 1 Interface Set Point Temperature |
| 45 | 10K Shield Set Point Temperature |
| 46 | HOB Simulator Heater Power |
| 47 | Level 0 Heater 1 Power |
| 48 | Level 0 Heater 2 Power |
| 49 | Level 0 Heater 3 Power |
| 50 | Level 1 Heater Power |
| 51 | 10K Shield Heater Power |
| 52 | HOB Simulator Heater Power |

#### Telecommands

Table 5: Commands to be sent from SCOS-2000 to the TFCS to control the cryostat control, logging and monitoring

| Ref: | Commands | Parameters |
| --- | --- | --- |
| 1 | Activate/Disable temperature logging | Activate/Deactivate |
| 2 | Activate/Disable cryogen level logging | Activate/Deactivate |
| 3 | Activate/Disable pressure logging | Activate/Deactivate |
| 4 | Set interface n temperature | Temperature |

#### Events

Table 6: Cryostat control, logging and monitoring events to be sent to SCOS-2000

| Ref: | Event | Parameters |
| --- | --- | --- |
| 1 | Command Accepted | Command Name |
| 2 | Command Rejected | Command Name |
| 3 | Command Execution Successful | Command Name |
| 4 | Command Execution Failure | Command Name |
| 6 | Monitoring Limit Exceeded | Sensor Location Value |

## Cold Blackbody

Figure 1: Schematic of the cold-blackbody control and monitoring

The cold black body and its interface electronics are provided by Cardiff University.

- 3 temperature sensors

- Heater

- Flip Mirror

- Heat switch

An electronics box will be provided by Cardiff with a standard interface to a National Instruments board.

### Cold Blackbody Software Requirements

A LabVIEW 6i™ VI will be provided by Cardiff that will control and monitor the Cold Blackbody electronics.  The VI will have an interface to the TFCS software to enable commands and data to be sent and received by the TFCS.  An interface specification for the VI and control electronics will be provided by Cardiff.

The parameters to be passed to the cold-blackbody VI from the TFCS are:

Heater power level (mW)

Flip mirror position (open/closed)

Heat shunt position (open/closed)

The parameters to be sent to the TFCS from the blackbody VI are:

Measured temperatures (3)

Measured heater power (mW)

Actual flip mirror position (open/closed)

Actual heat shunt position (open/closed)

It shall be possible to set the cold-blackbody heater power, flip mirror position and heat shunt position from the SPIRE EGSE.

No other process on the TFCS may interrupt the cold-blackbody control and monitoring unless a specific instruction has been sent.

The temperatures, heater power, mirror and heat shunt positions shall be logged and monitored continuously throughout the tests.

### EGSE Interface

#### Telemetry

The parameters listed in Table 7 shall be transmitted to SCOS-2000 as telemetry packets.

Table 7: Cold blackbody parameters to be transmitted to SCOS-2000

| Ref: | Parameter Name |
| --- | --- |
| 1 | Date |
| 2 | Time |
| 3 | Flip Mirror Status |
| 4 | Heat Shunt Status |
| 5 | Cold Blackbody Temperature 1 |
| 6 | Cold Blackbody Temperature 2 |
| 7 | Cold Blackbody Temperature 3 |
| 8 | Cold Blackbody Heater Power |

#### Commands

Table 8: Commands to be sent from SCOS-2000 to the TFCS to control the cold-blackbody

| Ref: | Commands | Parameters |
| --- | --- | --- |
| 1 | Activate/Disable Cold Blackbody Logging | Activate/Deactivate |
| 2 | Open/Close Flip Mirror | Open/Close |
| 3 | Open/Close Heat Shunt | Open/Close |
| 4 | Set cold blackbody power | Power setting |

#### Events

Table 9: Cold blackbody control, logging and monitoring events to be sent to SCOS-2000

| Ref: | Event | Parameters |
| --- | --- | --- |
| 1 | Command Accepted | Command Name |
| 2 | Command Rejected | Command Name |
| 3 | Command Execution Successful | Command Name |
| 4 | Command Execution Failure | Command Name |
| 6 | Monitoring Limit Exceeded | Sensor Location Value |

## Telescope Simulator

### System Description

Figure 2: Optical Design of the SPIRE Telescope Simulator

The purpose of the telescope simulator is to present the SPIRE instrument with an F8.68 optical beam representative of the Herschel telescope beam (see Figure 2).  In order to keep the point-source aberration free over the SPIRE FOV range, and to keep the simulator imaging simple, the design allows only one point source to be imaged at the spire focal surface.  To point source is scanned across the FOV in azimuth and elevation by two of the fold mirrors, F2 and F3.  To correct for the non-planar focal surface of SPIRE, two of the mirrors F1 and F2 are mounted on a translation stage in a trombone arrangement. The motions of these mirrors are defined by a set of complex control laws that have been produced by the SSTD Optics group.  At the time of writing, the control law for two degrees of freedom have been tested.  The control law will be tested for the full system will be tested once the optical layout has been installed.

The telescope simulator motors are driven from a Newport MM4006 multi axis motion controller capable of controlling up to 6 axes.  The first four axes will drive the azimuth and elevation of the two fold mirrors and the fifth axis will be used for the focus control actuator. The configuration is given in Table 10 below.  Communication between the MM4006 and TFCS can be either via an RS232 or GPIB.   Labview drivers have been supplied for both options.

Table 10: Configuration of telescope simulator motion controller

| Axis | Movement | Motor | Drive Card |
| --- | --- | --- | --- |
| 1 | Fold 2 – Azimuth | Newport 850-G Actuator | OPT-7D |
| 2 | Fold 2 – Elevation | Newport 850-G Actuator | OPT-7D |
| 3 | Fold 3 – Azimuth | Newport 850-G Actuator | OPT-7D |
| 4 | Fold 3 – Elevation | Newport 850-G Actuator | OPT-7D |
| 5 | Focus Adjustment | Newport M-ILS Translation Stage | OPT-7J |

Tim Grundy has been prototyping the control laws using the MM4006 controller using Labview to control the experiment and IDL to analyse the measurements.  The basic concept of the system is that the control laws have been defined using an optical ray-tracing model (Zeemax).  The output is a look-up table that used by the Labview software so that the mirrors can be moved by the correct amount for a given beam position, see Figure 3.  For the prototype, the table comprises a set of actuator positions for a complete scan sequence.  The actual telescope simulator will require a table consisting of actuator positions for each SPIRE detector position (this will be large!).

Figure 3: Schematic of Telescope Simulator Control System

### Software Requirements

#### Control

It shall be possible to move the image of a point source by the telescope simulator to a given detector position x,y.

It shall be possible to scan the image of a point source across a range of SPIRE detectors.

It shall be possible to automatically find the centre of movement of the telescope simulator actuators.

It shall be possible to reset the co-ordinates of the actuator positions to a defined setting (e.g. zero mm)

It shall be possible to remotely switch-on/off the Newport MM4006 controller.

#### Display

The TFCS shall provide a real-time display of the commanded and actual positions of the actuators.

The TFCS shall indicate the commanded and estimated pixel co-ordinates.

The TFCS shall indicate the status of the Newport MM4006 controller.

The TFCS shall indicate the scanning mode:

- Move to detector x,y

- Scan from x1,y1 to x2,y2

- Centering actuators.

An audible alarm shall sound if an actuator end-stop has been reached.

### EGSE Interface

#### Telemetry

| Ref: | Parameter Name |
| --- | --- |
| 1 | Date |
| 2 | Time |
| 3 | Fold Mirror 2 Commanded Azimuth |
| 4 | Fold Mirror 2 Measured Azimuth |
| 5 | Fold Mirror 2 Commanded Elevation |
| 6 | Fold Mirror 2 Measured Elevation |
| 7 | Fold Mirror 3 Commanded Azimuth |
| 8 | Fold Mirror 3 Measured Azimuth |
| 9 | Fold Mirror 3 Commanded Elevation |
| 10 | Fold Mirror 3 Measured Elevation |
| 11 | Translation Stage Commanded Position |
| 12 | Translation Stage Measured Position |

#### Commands

| Ref: | Commands | Parameters |
| --- | --- | --- |
| 1 | Switch On/Off MM4006 controller | ON/OFF |
| 2 | Center actuators |  |
| 3 | Set actuator position | Actuator no. Position (mm) |
| 4 | Move to detector position x,y | x y |
| 5 | Scan from detector x1,y1 to x2,y2 | x1 y1 x2 y2 |

#### Events

Table 11: Telescope simulator control, logging and monitoring events to be sent to SCOS-2000

| Ref: | Event | Parameters |
| --- | --- | --- |
| 1 | Command Accepted | Command Name |
| 2 | Command Rejected | Command Name |
| 3 | Command Execution Successful | Command Name |
| 4 | Command Execution Failure | Command Name |
| 6 | Motor end stop reached | Stepper motor number |

## Instrument Monitoring

The SPIRE STM instrument will not have any control and monitoring electronics apart from the cooler EGSE.  Therefore it will be necessary to provide some EGSE for the STM thermal tests.  The STM will not have any active mechanisms other than the CQM cooler and therefore the only requirement is to provide power to a number of heaters and temperature monitoring.

### Heater Power

Standard laboratory power supplies will supply the power to the instrument heaters.  There will be no remote control of these units.  A list of the STM heaters are provided in Table 12.

Table 12: STM Heater Locations

| Heater No. | Location | Resistance | Temperature Range | StabilitymK/ hr | Power Dissipation |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Min | Max |  | Nom | Max |
| 1 | BSM | TBD | TBD | TBD | TBD | TBD | TBD |
| 2 | SMECm | TBD | TBD | TBD | TBD | TBD | TBD |
| 3 | SCAL | TBD | TBD | TBD | TBD | TBD | TBD |
| 4 | PCAL | TBD | TBD | TBD | TBD | TBD | TBD |

### Temperature Monitoring

A duplicate of the TFCS cryostat temperature logging and monitoring system will perform temperature monitoring of the STM instrument.  The main difference will be a PICOWATT, AC resistance bridge (TBD) to measure the temperatures of the 300mK stage.  This unit has an IEEE-488 interface and comes with Labview drivers.  The STM instrument thermometers are defined in listed in Table 13 below.  Sensors 1 to 22 are the flight sensors. Sensors 23 to 42 are additional sensors required to monitor the temperature of the STM FPU and JFET chassis during thermal balance testing.

Table 13: STM Instrument Thermometers

| Sensor | Location | Type | Temp Range (K) | Accuracy | Resolution |
| --- | --- | --- | --- | --- | --- |
| No. |  |  | min | max | (+/- K) | (K) |
| 1 | Level 2: | JFET Phot module 1 | Cernox | 10 | 100 | 1.000 | 0.500 |
| 2 |  | JFET Spec module 1 | Cernox | 10 | 120 | 1.000 | 0.500 |
| 3 | Level 1: | HSFPU Optical Bench | Cernox | 3 | 100 | 0.050 | 0.025 |
| 4 |  | M3,5,7 Optical Sub Bench | Cernox | 3 | 100 | 0.010 | 0.010 |
| 5 |  | Input Baffle | Cernox | 3 | 100 | 0.010 | 0.010 |
| 6 |  | BSM/SOB I/F(SOB side) | Cernox | 3 | 100 | 0.010 | 0.010 |
| 7 |  | SCAL Structure | Cernox | 3 | 100 | 0.010 | 0.010 |
| 8 |  | Cooler Pump | Cernox | 3 | 100 | 0.025 | 0.025 |
| 9 |  | Cooler Evap | Cernox | 0.2 | 5 | 0.001 | 0.001 |
| 10 |  | Cooler Pump Heat Switch | Cernox | 1 | 50 | 0.005 | 0.005 |
| 11 |  | Cooler Evap Heat Switch | Cernox | 1 | 50 | 0.005 | 0.005 |
| 12 |  | Cooler Shunt | Cernox | 0.2 | 5 | 0.001 | 0.001 |
| 13 |  | SCAL 4% | Cernox | 10 | 80 | 0.005 | 0.005 |
| 14 |  | SCAL 2% | Cernox | 10 | 80 | 0.005 | 0.005 |
| 15 |  | BSM | Cernox | 3 | 20 | 0.010 | 0.010 |
| 16 |  | SMEC | Cernox | 3 | 20 | 0.010 | 0.010 |
| 17 |  | SMEC/SOB I/F | Cernox | 3 | 100 | 0.050 | 0.025 |
| 18 | Level 0: | Photometer Level 0 Encl. | Cernox | 1 | 10 | 0.002 | 0.002 |
| 19 |  | Spectrometer Level 0 Encl. | Cernox | 1 | 10 | 0.002 | 0.002 |
| 20 | 300mK: | 300mK PH Busbar 1 | Cernox | 0.2 | 5 | 0.001 | 0.001 |
| 21 |  | 300mK PH Busbar 2 | Cernox | 0.2 | 5 | 0.001 | 0.001 |
| 22 |  | 300mK SP Busbar 3 | Cernox | 0.2 | 5 | 0.001 | 0.001 |
| 23 | Level 2: | Phot JFET Chassis | Cernox | 3 | 100 | 0.050 | 0.025 |
| 24 |  | Spec JFET Chassis | Cernox | 3 | 100 | 0.050 | 0.025 |
| 25 | Level 1: | Shutter Vane | Cernox | 3 | 100 | 0.010 | 0.010 |
| 26 |  | FPU Structure +Y | Cernox | 3 | 100 | 0.050 | 0.025 |
| 27 |  | FPU Structure -Y | Cernox | 3 | 100 | 0.050 | 0.025 |
| 28 |  | FPU Structure +X | Cernox | 3 | 100 | 0.050 | 0.025 |
| 29 |  | FPU Structure -X | Cernox | 3 | 100 | 0.050 | 0.025 |
| 30 |  | FPU Structure +Z | Cernox | 3 | 100 | 0.050 | 0.025 |
| 31 |  | FPU Structure -Z | Cernox | 3 | 100 | 0.050 | 0.025 |
| 32 |  | SOB +X | Cernox | 3 | 100 | 0.050 | 0.025 |
| 33 |  | SOB -X | Cernox | 3 | 100 | 0.050 | 0.025 |
| 34 |  | SOB +Z | Cernox | 3 | 100 | 0.050 | 0.025 |
| 35 |  | SOB -Z | Cernox | 3 | 100 | 0.050 | 0.025 |
| 36 | Level 0: | Photometer Level 0 Encl. | Cernox | 1 | 10 | 0.002 | 0.002 |
| 37 |  | Spectrometer Level 0 Encl. | Cernox | 1 | 10 | 0.002 | 0.002 |
| 38 | 300mK: | Ph SW BDA | Cernox | 0.2 | 5 | 0.001 | 0.001 |
| 39 |  | Ph MW BDA | Cernox | 0.2 | 5 | 0.001 | 0.001 |
| 40 |  | Ph LW BDA | Cernox | 0.2 | 5 | 0.001 | 0.001 |
| 41 |  | Sp SW BDA | Cernox | 0.2 | 5 | 0.001 | 0.001 |
| 42 |  | Ph LW BDA | Cernox | 0.2 | 5 | 0.001 | 0.001 |

# Phase B Requirements

## Instrument Power Supply

## Beam Monitor

| Ref: | Parameter Name |
| --- | --- |
| 1 | Date |
| 2 | Time |
| 3 | Detector Signal |

## Chopper

| Ref: | Parameter Name |
| --- | --- |
| 1 | Date |
| 2 | Time |
| 3 | Commanded frequency |
| 4 | Measured frequency |

## Laser Line Selection

| Ref: | Parameter Name |
| --- | --- |
| 1 | Date |
| 2 | Time |
| 3 | Selected Wavelength |

## Fourier Transform Spectrometer

| Ref: | Parameter Name |
| --- | --- |
| 1 | Date |
| 2 | Time |
|  | …. |
|  | …. |
|  | …. |