Total Pages : 67

|  | System Database Specification Naming Convention Specification H-P-1-ASPI-SP-0141 Product Code : 00000 |  |
| --- | --- | --- |

|  | HERSCHEL / PLANCK TEAM | Date | Signature |
| --- | --- | --- | --- |
| Rédigé par/Written by | F. CHATTE | 01/02/02 |  |
| Vérifié par/Verified by | P. RIDEAU |  |  |
| Vérifié par/Verified by | JY. CHARNIER |  |  |
| Vérifié par/Verified by | C. MASSE |  |  |
| Approbation/Approved | J.J. JUILLET |  |  |

Entité Emettrice : Alcatel Space - Cannes

(détentrice de l’original) :

ENREGISTREMENT DES EVOLUTIONS / CHANGE RECORDS

| ISSUE | DATE | § : DESCRIPTION DES EVOLUTIONS § : CHANGE RECORD | REDACTEUR AUTHOR |
| --- | --- | --- | --- |
| 01/00 | 01/02/02 | issue 01 - Revision 00 | F. Chatte |

TABLE OF CONTENTS

1.	SCOPE	7

2.	Documents	8

2.1	Applicable documents	8

2.2	Reference documents	8

2.3	Acronyms	8

2.4	Definition	8

3.	General IDEntifier Requirements	9

4.	IDEntifier Requirements	11

4.1	Configuration	11

4.2	Telemetry packets	13

4.3	Telecommand packets	17

4.4	1553 messages	21

4.5	OBDH interfaces	24

4.6	Parameters	26

4.7	Curves	28

4.8	Displays	29

5.	General allocation requirement	32

6.	Detail allocation requirements	33

6.1	Subsystems	33

6.2	Type of system elements	34

6.3	Position	35

7.	attributes requirements	38

7.1	Application ID	38

7.1.1	Short description	38

7.1.2	Long description	38

7.2	Software parameter identifier	38

8.	Annex 1 : Compliance matrix with RD1	39

9.	Summary	50

9.1	Configuration	50

9.2	Telemetry packets	52

9.3	Telecommand packets	55

9.4	1553 messages	59

9.5	OBDH interfaces	62

9.6	Parameeters	64

9.7	Curves	66

9.8	Displays	66

List of figures

None

List of tables

None

# SCOPE

The scope of this document is to provide the naming convention to apply for the identifiers attached to all items which will be manipulated all among the Herschel / Planck project from engineering up to operation and which will be defined in the Herschel /Planck System DataBase (HPSDB).

This naming convention is aimed mainly to prevent identifier duplication at spacecraft real model level.

In addition, this naming convention shall support commonality between Herschel and Planck (for instance common subsystem (RF, …), common boxes (QRS, CCS, …)) and between the different models of a same spacecraft (AVM, SVM, PFM, …), this will allow to have common items allowing common development for AIT (TM and TC identifiers, test sequences, synoptics, …) or operation (TM and TC identifiers, displays, …) or software (TM and TC identifiers, …).

As last aim, this naming convention shall make the identifier as readable as possible.

Chapter 2 provides the applicable and reference documents. RD1 document in annex 4 provide a provisional naming convention limited to one spacecraft model (PFM) definition and not supporting all the spacecraft model definitions used during development phases.

Chapter 3 provides the general identifier requirements : possible subtypes, authorised characters, …

Chapter 4 provides the detail identifier requirements, each requirement is linked with an AD1 requirement.

Chapter 5 provides the general allocation requirements : mainly range of allocated value per subsystem.

Chapter 6 provides the detailed allocation requirements.

Chapter 7 provides some additional requirements to be applied on some attributes (APID, labels, …).

The requirements have the following format :

Requirement identifier :

5 characters set to "NMCVT" to identify requirements applicable to NaMing ConVenTion,

4 decimal digits to uniquely identified NMCNV requirement,

One character set to "C" to identify that the requirements apply to both Herschel and Planck,

requirement title,

Verification method : one character set to "I" to indicate that the validation method will be done by inspection (mainly via HPSDB checks or automatic generation).

Text of the requirement.

# Documents

In case of conflict between this document and other document (mainly RD1), this document has precedence.

## Applicable documents

| AD1 | H-P-1-ASPI-SP-0082 | Herschel / Planck System database specification |
| --- | --- | --- |

## Reference documents

| RD1 | SCI-PT-RS-07360 | Operations Interface Requirement Document (Annex 4) |
| --- | --- | --- |
| RD2 | S2K-MCS-ICD-0001-TOS-GCI | SCOS-2000 database import ICD |
| RD3 | SCI-PT-ICD-07527 | Packet structure interface control document (PSICD) |

## Acronyms

Refer to AD1

## Definition

Refer to AD1.

# General IDEntifier Requirements

The identifiers are coded using the identifier subtypes defined in the following requirements.

NMCVT-0100-C	- 	Identifier type							-	I

The identifier type shall be defined as any character string able to include one or several occurrences of the following identifier characters :

[0-9]	(decimal digits),

[A-H]	(characters from "A" to "H", but only upper case),

[J-N]	(characters from "J" to "N", but only upper case),

[P]		(character "P", but only upper case),

[R-Z]	(characters from "R" to "Z", but only upper case),

[_]		(underscore),

[+]		(plus),

[-]		(minus, dash),

[.]		(dot).

Note :

- Characters "I", "O" and "Q" by default are excluded in order to minimise the likelihood of transcription errors when these are typed manually, however they can be used if specifically authorised (type of system element, system element model, …).

NMCVT-0110-C	- 	Identifier subtype							-	I

The identifier subtypes are identifier type with length and other potential limitations and shall be :

IDCHnnF with

"ID" for identifier type,

"CH" for any authorised character,

"nn" for the identifier length (01-99),

"F" for fixed length

IDE201F (function specifier for parameter - refer to RD1-A4.3) :

Length = 1,

Enumerated data :

.	"B"	Spare (at function specifier level),

.	"D"	for synthetic (derived) parameters,

.	"E"	Spare (at function specifier level),

.	"H"	Spare (at function specifier level),

.	"J"	Spare (at function specifier level),

.	"K"	for constant parameter (not compliant with RD1 due to TC identifier function),

.	"M"	for TM parameters,

.	"N"	Spare (at function specifier level),

.	"P"	for command parameter,

.	"R"	Spare (at function specifier level),

.	"Z"	for system parameter,

.	"U"	for user parameter,

.	"W"	Spare (at function specifier level),

IDINnnF with

"ID" for identifier type,

"IN" for any decimal digit string,

"nn" for the identifier length (01-99),

"F" for fixed length

Note :

- Some other limitations can be added in the corresponding requirements.

- For IDE201F, the other allowed letter are for other items than parameter (TC, sequence, …).

- For IDINnnF, the greater value (9, 99, 999, …) is reserved for "pseudo" definition.

# IDEntifier Requirements

The following requirements are directly linked to AD1 requirements. In order to insure the traceability with [AD1] document, the NMCVT requirements numbering is the one of the HPSDB requirements (for instance NMCVT-1234-C requirement refer to HPSDB-1234-C requirement in AD1).

## Configuration

NMCVT-4030-C	- 	Type of system elements						-	I

"Type of system element" identifier shall :

Be of IDCH11F subtype,

Be unique.

For instance :"01234567890", "CDMU_______", "CDMU_SW_h__", "TWTA_______", "CCS________"

Note : Letters "I", "O" and "Q" are allowed

NMCVT-4040-C	- 	Type of system element number					-	I

"Type of system element" number identifier shall :

Be of IDIN03F subtype,

Be unique.

For instance :"012", "000", "998"

note : Used in some identifier (when there is no length constraint) as three first character (structure, …).

NMCVT-4050-C	- 	Real elements							-	I

"Real element" identifier shall :

Be of IDCH14F subtype with the following limitations :

From first up to eleventh character is "type of system element" identifier (IDCH11F - refer to NMCVT-4030-C),

From twelfth upto fourteenth character is "real element" number (IDIN03F - refer to NMCVT-4060-C),

Be unique.

For instance :"01234567890012",  "CDMU_______007", "CDMU_SW_h__001", "TWTA_______002", "CCS________003"

NMCVT-4060-C	- 	real element number						-	I

"Real element" number shall :

Be of IDIN03F

Be unique for a "type of system element".

For instance : "012", "998"

Note : used for instanciation at real element generation (curve, …)

NMCVT-4075-C	- 	Elements direct definition						-	I

"element direct definition" identifier shall :

Be of IDCH14F subtype with the following limitations :

From first up to eleventh character is "pseudo type of system element" identifier (IDCH11F - refer to NMCVT-4030-C),

From twelfth upto fourteenth character is "pseudo real element" number (IDIN03F - refer to NMCVT-4060-C),

Be unique.

For instance :"01234567890999",  "CDMU_______999", "CDMU_SW_h__999", "TWTA_______999", "CCS________999"

NMCVT-4100-C	- 	System element models						-	I

"System element model" identifier shall :

Be of IDCH10F subtype

Be unique.

For instance : "H_01234567", "P_PLM_____", "H_PFM_____", "X_AVM1____"

Note : Characters "I", "O" and "Q" are allowed.

NMCVT-4111-C	- 	System element models direct definition			-	I

"System element model direct definition" identifier shall :

Be of IDCH10F subtype

Be unique.

For instance : "H_01234567", "P_PLM_____", "H_PFM_____", "X_AVM1____"

Note : Characters "I", "O" and "Q" are allowed.

NMCVT-4113-C	- 	Subsystems								-	I

"Subsystem" identifier shall :

Be of IDCH01F subtype,

Be unique for a "system element model".

For instance : "A", "C", "Z"

NMCVT-4117-C	- 	Position								-	I

"Position" identifier shall :

Be of IDIN03F subtype,

Be unique for a "system element model".

For instance : "000", "998", "012"

Note : used for instanciation at system element model generation (parameter identifier, Telecommand packet identifier, …)

NMCVT-4120-C	- 	Real models								-	I

"Real model" identifier shall :

Be of IDCH12F subtype with the following limitations :

From first up to tenth character is "system element model" identifier (IDCH10F - refer to NMCVT-4100-C),

From eleventh up to twelfth character is "real model" number (IDIN02F - refer to NMCVT-4130-C),

Be unique.

For instance : "H_0123456701", "P_PLM_____02", "H_PFM_____98", "X_AVM1____25"

NMCVT-4130-C	- 	Real model number						-	I

"Real model" number shall :

Be of IDCH02F subtype

Be unique for a "system element model".

For instance : "01", "98"

Note : could (it is not in the current status of HPSDB) for any instanciation at "real mode"l generation.

## Telemetry packets

NMCVT-4305-C	- 	TM packet standard template					-	I

"TM packet standard template" identifier shall :

be of IDCH10F subtype with the following limitations :

First character is "pseudo subsystem" identifier (IDCH01F- refer to NMVCT-4113-C),

Second character is "X",

From third up to sixth character is "TMSD" (to refer to TM packet standard template),

From seventh up to tenth character is IDIN04F (Unique for "YXTMSD"),

Be unique.

For instance : "ZXTMSD0123", "ZXTMSD9998", "ZXTMSD0250"

NMCVT-4320-C	- 	TM packet PSICD template					-	I

"TM packet PSICD template" identifier shall :

Be of IDCH10F subtype with the following limitations :

First character is "pseudo subsystem" identifier (IDCH01F- refer to NMVCT-4113-C),

Second character is "X",

From third up to sixth character is "TMPS" (to refer to TM packet PSICD template),

From seventh up to eighth character is IDIN02F (Type),

From ninth up to tenth character is IDIN02F (Subtype),

Be unique.

For instance : "ZXTMPS0123", "ZXTMPS9998", "ZXTMPS0250"

NMCVT-4340-C	- 	Theoretical TM packet 						-	I

"Theoretical TM packet" identifier shall :

Be of IDIN07F subtype with the following limitations :

From first up to third character is "type of system element" number (IDIN03F - refer to NMCVT-4040-C),

From fourth up to seventh character IDIN04F,

Be unique for a "type of system element".

For instance : "0120123", "9989998", "0250250"

NMCVT-4360-C	- 	Theoretical TM structure 						-	I

"Theoretical TM structure" identifier shall :

Be of IDCH11F subtype with the following limitations :

From first up to third character is "type of system element" number (IDIN03F - refer to NMCVT-4040-C),

From fourth up to seventh character is "TMST" (to refer to TM structure),

From eighth up to eleventh character is IDIN04F,

Be unique for a "type of system element".

For instance : "012TMST0123", "998TMST9998", "025TMST0250"

NMCVT-4374-C	- 	Theoretical TM packet group 					-	I

"Theoretical TM packet group" identifier shall :

Be of IDCH11F subtype with the following limitations :

From first up to third character is "type of system element" number (IDIN03F - refer to NMCVT-4040-C),

From fourth up to seventh character is "TMGR" (to refer to TM group),

From eighth up to eleventh character is IDIN04F,

Be unique for a "type of system element".

For instance : "012TMGR0123", "998TMGR9998", "025TMGR0250"

NMCVT-4380-C	- 	Real TM packet 							-	I

"Real TM packet" identifier shall :

Be of IDIN10F subtype with the following limitations :

From first up to seventh character is "theoretical TM packet" identifier (IDIN07F - refer to NMCVT-4340-C),

From eighth up to tenth character is "position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "0120123012", "9989998998", "0250250025"

NMCVT-4400-C	- 	Real TM structure 							-	I

"Real TM structure" identifier shall :

Be of IDCH14F subtype with the following limitations :

From first up to eleventh character is "theoretical TM" structure identifier (IDCH11F - refer to NMCVT-4360-C),

From twelfth up to fourteenth character is "position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "012TMST0123012", "998TMST9998998", "025TMST0250025"

NMCVT-4420-C	- 	Real TM packet group 						-	I

"Real TM packet group" identifier shall :

Be of IDCH14F subtype with the following limitation :

From first up to eleventh character is "theoretical TM packet group" identifier (IDCH11F - refer to NMCVT-4374-C),

From twelfth up to fourteenth  character is "position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "012TMGR0123012", "998TMGR9998998", "025TMGR0250025"

NMCVT-4440-C	- 	TM packet direct definition 					-	I

"TM packet direct definition" identifier shall :

Be of IDIN10F subtype with the following limitations :

From first up to seventh character is "pseudo theoretical TM packet" identifier (IDIN07F - refer to NMCVT-4340-C)

From eighth up to tenth character is "pseudo position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a real model.

For instance : "9990123999", "9999998999", "9990250999"

NMCVT-4450-C	- 	TM structure direct definition					-	I

"TM structure direct definition" identifier shall :

Be of IDCH14F subtype with the following limitations :

From first up to eleventh character is "pseudo theoretical TM structure" identifier (IDCH11F - refer to NMCVT-4360-C),

From twelfth up to fourteenth character is "pseudo position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "999TMST0123999", "999TMST9998999", "999TMST0250999"

NMCVT-4455-C	- 	TM packet group direct definition				-	I

"TM packet group direct definition" identifier shall :

Be of IDCH14F subtype with the following limitations :

From first up to eleventh character is "pseudo theoretical TM packet group" identifier (IDCH11F - refer to NMCVT-4374-C),

From twelfth up to fourteenth character is "pseudo position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "999TMGR0123999", "999TMGR9998999", "999TMGR0250999"

## Telecommand packets

NMCVT-4505-C	- 	TC packet standard template					-	I

"TC packet standard template" identifier shall :

be of IDCH10F subtype with the following limitations :

First character is "pseudo subsystem" identifier (IDCH01F- refer to NMVCT-4113-C),

Second character is "X" (RD1),

From third up to sixth character is "TCSD" (to refer to TC packet standard template),

From seventh up to tenth character is IDIN04F (Unique for "YXTCSD")

Be unique.

For instance : "ZXTCSD0123", "ZXTCSD9998", "ZXTCSD0250"

NMCVT-4520-C	- 	TC packet PSICD template					-	I

"TC packet PSICD template" identifier shall :

Be of IDCH10F subtype with the following limitations :

First character is "pseudo subsystem" identifier (IDCH01F- refer to NMVCT-4113-C),

Second character is "X" (RD1),

From third up to sixth character is "TCPS" (to refer to TC packet PSICD template),

From seventh up to eighth character is IDIN02F (type),

From ninth up to tenth character is IDIN02F (subtype),

Be unique.

For instance : "ZXTCPS0123", "ZXTCPS9998", "ZXTCPS0250"

NMCVT-4540-C	- 	Theoretical TC packet 						-	I

"Theoretical TC packet" identifier shall :

Be of IDCH04F subtype with the following limitations :

First character is "C",

From second up to fourth character is IDCH03F,

Be unique for a "type of system element".

For instance : "C012", "CABC", "C998", "C025"

NMCVT-4560-C	- 	Theoretical TC structure 						-	I

"Theoretical TC structure" identifier shall :

Be of IDCH11F subtype with the following limitations :

From first up to third character is "type of system element" number (IDIN03F - refer to NMCVT-4040-C),

From fourth up to seventh character is "TCST" (to refer to TC structure),

From eighth up to eleventh is IDIN04F,

Be unique for a "type of system element".

For instance : "012TCST0123", "998TCST9998"

NMCVT-4574-C	- 	Theoretical TC packet group 					-	I

"Theoretical TC packet group" identifier shall :

Be of IDCH11F subtype with the following limitations :

From first up to third character is "type of system element" number" (IDIN03F - refer to NMCVT-4040-C),

From fourth up to seventh character is "TCGR" (to refer to TC group),

From eighth up to eleventh character is IDIN04F

Be unique for a "type of system element".

For instance : "012TCGR0123", "998TCGR9998", "025TCGR0250"

NMCVT-4580-C	- 	Real TC packet 							-	I

"Real TC packet" identifier shall :

Be of IDCH08F subtype with the following limitations :

First character is "subsystem" identifier (IDCH01F - refer to NMCVT-4113-C),

From second up to fith character is "theoretical TC packet identifier" (IDCH04F - refer to NMCVT-4540-C),

From sixth up to eighth character is "position identifier" (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "AC012012", "ACABC012", "YC998998", "HC025025"

NMCVT-4600-C	- 	Real TC structure 							-	I

"Real TC structure" identifier shall :

Be of IDCH14F subtype with the following limitations :

From first up to eleventh character is "theoretical TC structure" identifier (IDCH11F - refer to NMCVT-4560-C),

From twelfth up to fourteenth character is "position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "012TCST0123012", "998TCST9998998", "025TCST0250025"

NMCVT-4620-C	- 	Real TC packet group 						-	I

"Real TC packet group" identifier shall :

Be of IDCH14F subtype with the following limitation :

From first up to eleventh character is "theoretical TC packet group" identifier (IDCH11F - refer to NMCVT-4574-C),

From twelfth up to fourteenth  character is "position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "012TCGR0123012", "998TCGR9998998", "025TCGR0250025"

NMCVT-4640-C	- 	TC packet direct definition 					-	I

"TC packet direct definition" identifier shall :

Be of IDCH08F subtype with the following limitations :

First character is "pseudo subsystem" identifier (IDCH01F - refer to NMCVT-4113-C),

From second up to fith character is "pseudo theoretical TC packet identifier" (IDCH04F - refer to NMCVT-4540-C)

From sixth up to eighth character is "pseudo position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a real model.

For instance : "ZC012999", "ZCABC999", "ZC998999", ZC025999"

NMCVT-4650-C	- 	TC structure direct definition					-	I

"TC structure direct definition" identifier shall :

Be of IDCH14F subtype with the following limitations :

From first up to eleventh character is "pseudo theoretical TC structure" identifier (IDCH11F - refer to NMCVT-4560-C),

From twelfth character up to fourteenth character is "pseudo position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "999TCST0123999", "999TCST9998999", "999TSST0250999"

NMCVT-4655-C	- 	TC packet group direct definition 				-	I

"TC packet group direct definition" identifier shall :

Be of IDCH14F subtype with the following limitation :

From first up to eleventh character is " pseudo theoretical TC packet group" identifier (IDCH11F - refer to NMCVT-4574-C),

From twelfth up to fourteenth  character is "pseudo position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "999TCGR0123999", "999TCGR9998999", "999TCGR0250999"

NMCVT-4660-C	- 	Command sequence						-	I

"Command sequence" identifier shall :

Be of IDCH08F subtype with the following limitations :

First character is "subsystem" identifier (IDCH01F- refer to NMVCT-4113-C),

Second character is "S",

From third up to fifth character is IDCH03F,

From sixth up to eighth character is "position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "AS012012", "ASABC012", "YS998998", "HS025025"

NMCVT-4680-C	- 	Command sequence formal parameter			-	I

"Command sequence formal parameter" identifier shall :

Be of IDCH08F subtype with the following limitations :

First character is "subsystem" identifier (IDCH01F- refer to NMVCT-4113-C),

Second character is "F",

From third up to fifth character is IDCH03F,

From sixth up to eighth character is "position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "AF012012", "AFABC012", "YF998998", "HF025025"

NMCVT-4685-C	- 	Command parameter set						-	I

"Command parameter set" identifier shall :

Be of IDCH08F subtype with the following limitations :

First character is "subsystem" identifier (IDCH01F- refer to NMVCT-4113-C),

Second character is "T",

From third up to fifth character is IDCH03F,

From sixth up to eighth character is "position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "AT012012", "ATABC012", "YT998998", "HT025025"

NMCVT-4690-C	- 	Command parameter set value					-	I

"Command parameter set value" identifier shall :

Be of IDCH08F subtype with the following limitations :

First character is "subsystem" identifier (IDCH01F- refer to NMVCT-4113-C),

Second character is "V",

From third up to fifth character is IDCH03F,

From sixth up to eighth character is "position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "AV012012", "AVABC012", "YV998998", "HV025025"

NMCVT-4660-C	- 	Command parameter range check				-	I

"Command parameter range check" identifier shall : TBD (N4 in RD2)

For instance : TBD

## 1553 messages

NMCVT-4705-C	- 	1553 message template						-	I

"1553 message template" identifier shall

be of IDCH10F subtype with the following limitations :

First character is "pseudo subsystem" identifier (IDCH01F- refer to NMVCT-4113-C),

Second character is "X",

From third up to sixth character is "BUSD" (to refer to 1553 message template),

From seventh up to tenth character is IDIN04F (Unique for "YXBUSD"),

Be unique.

For instance : "ZXBUSD0123", "ZXBUSD9998", "ZXBUSD0250"

NMCVT-4725-C	- 	1553 status word							-	I

"1553 status word" identifier shall

be of IDCH10F subtype with the following limitations :

First character is "subsystem" identifier (IDCH01F- refer to NMVCT-4113-C),

Second character is "X",

From third up to sixth character is "BUSW" (to refer to 1553 status word),

From seventh up to eighth character is IDIN02F (RT address),

From ninth character up to tenth character is IDIN02F (subaddress),

Be unique.

For instance : "DXBUSW0123", "AXBUSW9998", "AXBUSW2525"

NMCVT-4740-C	- 	Theoretical 1553 message					-	I

"Theoretical 1553 message" identifier shall :

Be of IDIN11F subtype with the following limitations :

From first up to third character is "type of system element number (IDIN03F - refer to NMCVT-4040-C),

From fourth up to seventh character is "BUMG" (to refer to 1553 message),

Eighth character is IDCH01F ("A" for Acquisition, "C" for Command),

From ninth up to eleventh is IDIN03F,

Be unique for a "type of system element".

For instance : "012BUMGA012", "998BUMGC998", "025MUMGC025"

NMCVT-4760-C	- 	Theoretical 1553 structure 					-	I

"Theoretical 1553 structure" identifier shall :

Be of IDCH11F subtype with the following limitations :

From first up to third character is "type of system element" number (IDIN03F - refer to NMCVT-4040-C),

From fourth up to seventh character is "BUST" (to refer to 1553 structure),

Eighth character is IDCH01F ("A" for Acquisition, "C" for Command),

From ninth up to eleventh is IDIN03F,

Be unique for a "type of system element".

For instance : "012BUSTA012", "998BUSTC998", "025BUMGC025"

NMCVT-4774-C	- 	Theoretical 1553 message group 				-	I

"Theoretical 1553 message group" identifier shall :

Be of IDCH11F subtype with the following limitations :

From first up to third character is "type of system element" number (IDIN03F - refer to NMCVT-4040-C),

From fourth up to seventh character is "BUGR" (to refer to 1553 group),

Eighth character is IDCH01F ("A" for Acquisition, "C" for command),

From ninth up to eleventh character is IDIN03F

Be unique for a "type of system element".

For instance : "012BUGRA012", "998BUGRC998", "025BUGRC025"

NMCVT-4780-C	- 	Real 1553 message 						-	I

"Real 1553 message" identifier shall :

Be of IDIN14F subtype with the following limitations :

From first up to eleventh character is "theoretical 1553 message" identifier" (IDIN11F - refer to NMCVT-4740-C)

From twelfth up to fourteenth character is "position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "012BUMGA012012", "998BUMGC998998", "025MUMGC025025"

NMCVT-4800-C	- 	Real 1553 structure 						-	I

"Real 1553 structure" identifier shall :

Be of IDCH14F subtype with the following limitations :

From first up to eleventh character is "theoretical 1553 structure" identifier (IDCH11F - refer to NMCVT-4760-C),

From twelfth character up to fourteenth character is "position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "012BUSTA012012", "998BUSTC998998", "025BUMGC025025"

NMCVT-4820-C	- 	Real 1553 message group 					-	I

"Real 1553 message group" identifier shall :

Be of IDCH14F subtype with the following limitation :

From first up to eleventh character is "theoretical 1553 message group" identifier (IDCH11F - refer to NMCVT-4774-C),

From twelfth up to fourteenth  character is "position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "012BUGRA012012", "998BUGRC998998", "025BUGRC025025"

NMCVT-4840-C	- 	1553 message direct definition					-	I

"1553 message direct definition" identifier shall :

Be of IDIN10F subtype with the following limitations :

From first up to seventh character is "pseudo 1553 message" identifier (IDIN07F - refer to NMCVT-4740-C)

From eighth up to tenth character is "pseudo position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "999BUMGA012999", "999BUMGC998999", "999MUMGC025999"

NMCVT-4850-C	- 	1553 structure direct definition 					-	I

"1553 message structure direct definition" identifier shall :

Be of IDCH14F subtype with the following limitations :

From first up to eleventh character is "pseudo 1553 structure" identifier (IDCH11F - refer to NMCVT-4760-C),

From twelfth character up to fourteenth character is "pseudo position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "999BUSTA012999", "999BUSTC998999", "999BUMGC025999"

NMCVT-4860-C	- 	1553 message group direct definition 				-	I

"1553 message group direct definition" identifier shall :

Be of IDCH14F subtype with the following limitation :

From first up to eleventh character is "pseudo 1553 message group" identifier (IDCH11F - refer to NMCVT-4774-C),

From twelfth up to fourteenth  character is "pseudo position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "999BUGRA012999", "999BUGRC998999", "999BUGRC025999"

## OBDH interfaces

NMCVT-4974-C	- 	Theoretical OBDH interrogation					-	I

"Theoretical OBDH" identifier shall :

Be of IDIN11F subtype with the following limitations :

From first up to third character is "type of system element number" (IDIN03F - refer to NMCVT-4040-C),

from fourth up to seventh character is "DHIN" (to refer to OBDH interrogation),

Eighth character is IDCH01F ("C" for Command),

From ninth up to eleventh character IDIN03F,

Be unique for a "type of system element".

For instance : "012DHINC012", "998DHINC998", "025DHINC025"

NMCVT-4990-C	- 	Theoretical OBDH interrogation group 			-	I

"Theoretical OBDH interrogation group" identifier shall :

Be of IDCH11F subtype with the following limitations :

From first up to third character is "type of system element number" (IDIN03F - refer to NMCVT-4040-C),

From fourth up to seventh character is "DHGR" (to refer to OBDH group),

Eighth character is IDCH01F ("C" for command),

From ninth up to eleventh character is IDIN03F,

Be unique for a "type of system element".

For instance : "012DHGRC012", "998DHGRC998", "025DHGRC025"

NMCVT-5020-C	- 	Real OBDH interrogation 					-	I

"Real OBDH interrogation" identifier shall :

Be of IDIN14F subtype with the following limitations :

From first up to eleventh character is "theoretical OBDH interrogation" identifier (IDIN11F - refer to NMCVT-4974-C)

From twelfth up to fourteenth character is "position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "012DHINC012012", "998DHINC998998", "025DHINC025025"

NMCVT-5044-C	- 	Real OBDH interrogation group 				-	I

"Real OBDH interrogation group" identifier shall :

Be of IDCH14F subtype with the following limitation :

From first up to eleventh character is "theoretical OBDH interrogation group" identifier (IDCH11F - refer to NMCVT-4990-C),

From twelfth up to fourteenth  character is "position" identifier (IDIN03F - refer to NMCVT-4117-C"),

Be unique for a "real model".

For instance : "012DHGRC012012", "998DHGRC998998", "025DHGRC025025"

NMCVT-5060-C	- 	OBDH interrogation direct definition				-	I

"OBDH interrogation direct definition" identifier shall :

Be of IDIN14F subtype with the following limitations :

From first up to eleventh character is "pseudo OBDH interrogation" identifier (IDIN11F - refer to NMCVT-4974-C)

From eighth up to tenth character is "pseudo position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "999DHINC012999", "999DHINC998999", "999DHINC025999"

NMCVT-5080-C	- 	OBDH interrogation group direct definition 			-	I

"OBDH interrogation group direct definition" identifier shall :

Be of IDCH14F subtype with the following limitation :

From first up to eleventh character is "pseudo OBDH interrogation group" identifier (IDCH11F - refer to NMCVT-4990-C),

From twelfth up to fourteenth  character is "pseudo position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "999DHGRC012999", "999DHGRC998999", "999DHGRC025999"

## Parameters

NMCVT-5110-C	- 	Theoretical parameter 						-	I

"Theoretical parameter" identifier shall :

Be of IDCH04F subtype with the following limitations :

First character is IDE201F,

From second up to fourth character is IDCH03F,

Be unique for a "type of system element".

For instance : "M012", "PABC", "D998", "U025"

NMCVT-5126-C	- 	Theoretical parameter group		 			-	I

"Theoretical parameter group" identifier shall :

Be of IDCH11F subtype with the following limitations :

From first up to third character is "type of system element number" (IDIN03F - refer to NMCVT-4040-C),

From fourth up to seventh character is "PAGR" (to refer to parameter group),

Eighth character is IDCH01F ("A"' for Acquisition, "C" for Command, "U" for User, "Z" for System), "D" for Derived, "W" for Condition)

From ninth up to eleventh character is IDIN03F,

Be unique for a "type of system element".

For instance : "012PAGRC012", "998PAGRU998", "025PAGRW025"

NMCVT-5130-C	- 	Real parameter 							-	I

"Real parameter" identifier shall :

Be of IDCH08F subtype with the following limitations :

First character is subsystem identifier (IDCH01F - refer to NMCVT-4113-C),

From second up to fifth character is "theoretical parameter" identifier (IDCH04F - refer to NMCVT-5110-C),

From sixth character up to eighth character is "position identifier" (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "AM012012", "DPABC012", "YD998998", "HU025025"

NMCVT-5150-C	- 	Parameter direct definition 					-	I

"Parameter direct definition" identifier shall :

Be of IDCH08F subtype with the following limitations :

First character is "pseudo subsystem" identifier (IDCH01F - refer to NMCVT-4113-C), (TBC : could be subsystem identifier),

From second up to fifth character is "pseudo theoretical parameter" identifier (IDCH04F - refer to NMCVT-5110-C),

From sixth up to eighth character is "pseudo position identifier" (IDIN03F - refer to NMCVT-4117-C),

Be unique for a real model.

For instance : "ZM012999", "ZPABC999", "ZD998999", "ZU025999"

NMCVT-5160-C	- 	Real parameter group 						-	I

"Real parameter group" identifier shall :

Be of IDCH14F subtype with the following limitation :

From first up to eleventh character is "theoretical parameter group" identifier (IDCH11F - refer to NMCVT-5126-C),

From twelfth up to fourteenth  character is "position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "012PAGRC012012", "998PAGRU998998", "025PAGRW025025"

NMCVT-5175-C	- 	Parameter group direct definition 				-	I

"Parameter group direct definition" identifier shall :

Be of IDCH14F subtype with the following limitation :

From first up to eleventh character is "pseudo parameter group" identifier (IDCH11F - refer to NMCVT-5126-C),

From twelfth up to fourteenth  character is "pseudo position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "999PAGRC012999", "999PAGRU998999", "999PAGRW025999"

## Curves

NMCVT-5360-C	- 	Theoretical curve		 					-	I

"Theoretical curve" identifier shall :

Be of IDIN06F subtype with the following limitations :

From first up to third character is "type of system element" number (IDIN03F - refer to requirement NMCVT-4040-C),

fourth to sixth character is IDIN03F (unique for "type of system element"),

Be unique for a "type of system element".

For instance : "012012", "998998", "025025"

Note : to identify uniquely a curve the type (Analogue or digital) and subtype (for analogue only : polynomial or discrete)  of curve shall be provided - In order to be in line with RD1.

NMCVT-5370-C	- 	Real curve		 						-	I

"Real curve" identifier shall :

Be of IDIN09F subtype with the following limitations :

from first to sixth character is "theoretical curve" identifier (IDIN06F - refer to 5360-C),

From seventh to ninth character is "real element" number (IDIN03F - refer to NMCVT-4060-C),

Be unique for a "real element".

For instance : "012012012", "998998998", "025025025"

NMCVT-5380-C	- 	Curve direct definition						-	I

"Curve direct definition" identifier shall :

Be of IDIN09F subtype with the following limitations :

from first to sixth character is "pseudo theoretical curve" identifier (IDIN06F - refer to 5360-C),

From seventh to ninth character is "pseudo real element" number (IDIN03F - refer to NMCVT-4060-C),

Be unique for a "real element".

For instance : "999012999", "999998999", "999025999"

## Displays

The following naming convention for displays is such that the implementation of theoretical displays and direct definition (even if not specified in HPSDB specification) will be possible (the two last characters always reflect the "position number") as it is for TC packets or parameters (8 characters).

NMCVT-6100-C	- 	Alphanumeric display						-	I

"Alphanumeric display" identifier shall :

Be of IDCH08F subtype with the following limitations :

First character is "subsystem" identifier (IDCH01F- refer to NMVCT-4113-C),

Second character is "A",

From third up to fifth character is IDCH03F,

From sixth up to eighth character is "position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "AA012012", "AAABC012", "YA998998", "HA025025"

NMCVT-6110-C	- 	Graphic display							-	I

"Graphic display" identifier shall :

Be of IDCH08F subtype with the following limitations :

First character is "subsystem" identifier (IDCH01F- refer to NMVCT-4113-C),

Second character is "G",

From third up to fifth character is IDCH03F,

From sixth up to eighth character is "position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "AG012012", "AGABC012", "YG998998", "HG025025"

NMCVT-6120-C	- 	Alphanumeric mimic display					-	I

"alphanumeric mimic display" identifier shall :

Be of IDCH08F subtype with the following limitations :

First character is "subsystem" identifier (IDCH01F- refer to NMVCT-4113-C),

From second up to third character is "AM",

From fourth up to fifth character is IDCH02F,

from sixthto eighth character is "position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "AAM01012", "AAMAB012", "YAM98998", "HAM25025"

NMCVT-6125-C	- 	Mimic display diagram						-	I

"Mimic display diagram" identifier shall :

Be of IDCH08F subtype with the following limitations :

First character is "subsystem" identifier (IDCH01F- refer to NMVCT-4113-C),

From second up to third character is "AD",

From fourth up to fifth character is IDCH02F,

from sixth up to eighth character is "position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "AAD01012", "AADAB012", "YAD98998", "HAD25025"

NMCVT-6130-C	- 	Scrolling display							-	I

"Scrolling display" identifier shall :

Be of IDCH08F subtype with the following limitations :

First character is "subsystem" identifier (IDCH01F- refer to NMVCT-4113-C),

Second character is "L",

From third up to fifth character is IDCH03F,

From sixth up to eighth character is "position" identifier (IDIN03F - refer to NMCVT-4117-C),

Be unique for a "real model".

For instance : "AL012012", "ALABC012", "YL998998", "HL025025"

# General allocation requirement

TBW

# Detail allocation requirements

## Subsystems

NMCVT-7500-C	- 	Subsystem identifiers allocation					-	I

The subsystem identifiers allocation shall be as follows :

Subsystem identifier		Herschel			Planck

"A"				AOCMS			AOCMS

"B"				ACC software			ACC software

"C"				RCS				RCS

"D"				CDMS				CDMS

"E"				CDMS software		CDMS software

"F"				Frame structure		Frame structure

"G" 			Spare				Spare

"H"				HIFI				HFI

"J" 				System				System

"K" 				Kryo				Spare

"L" 				Spare				LFI

"M" 			Radiation monitor		Radiation monitor

"N" 			Spare				Spare

"P"				PACS				Spare

"R"				Radio frequency (TT&C)	Radio frequency (TT&C)

"S"				SPIRE				Sorption cooler

"T"				Thermal control		Thermal control

"U"				Spare				Spare

"V"				Visual monitor camera	Visual monitor camera

"W"				Electrical power		Electrical power

"X"				STR software			Spare

"Y"				EGSE				EGSE

"Z"				Pseudo subsystem		Pseudo subsystem

## Type of system elements

The following list has to be completed.

NMCVT-7510-C	- 	Type of system element allocation				-	I

The type of system element identifier and corresponding type of system element number allocation shall be as follows (As far as it is not sure that the element described hereafter will be in fact composed of several type of system elements (mainly for instruments) the allocated number are given as range - in addition, for information, is provided the number of real corresponding equipment per spacecraft model and the associated subsystem) :

Type of system		Type of system			Element number for

element  identifier	element number		Herschel	Planck 		Subsystem

"ACC"		[001-009]			1		1		A

"GYRO"		[010-019]			1		0		A

"STR"		[020-029]			2		0		A

"RWE"		[030-039]			1		0		A

"RW"		[040-049]			4		0		A

"SAS-H"		[050-059]			2		0		A

"FSS"		[060-069]			2		0		A

"QRS"		[070-079]			2		2		A

"STR_MAPPER"	[080-089]			0		1		A

"AAD"		[090-099]			0		1		A

"SAS-P"		[100-109]			0		3		A

"ACC_SW_H"	[110-119]			1		0		B

"ACC-SW_P"	[120-129]			0		1		B

"RCS_H"		[130-139]			1		0		C

"RCS_P"		[140-149]			0		1		C

"CDMU"		[150-159]			1		1		D

"CDMU_SW_H"	[160-169]			1		0		E

"CDMU_SW_P"	[170-179]			0		1		E

"FRAME_STR"	[180-189]			TBD		TBD		F

"HIFI"		[190-239]			1		0		H

"HFI"		[240-289]			0		1		H

"SYSTEM"		[290-299]			TBD		TBD		J

"CRYO_ELEC"	[300-309]			1		0		K

"CRYOSTAT"	[310-319]			1		0		K

"LFI"		[320-369]			0		1		L

"RAD_MON"	[370-379]			TBD		TBD		M

"PACS"		[380-429]			1		0		P

"LGA"		[430-439]			2		3		R

"MGA"		[440-449]			1		1		R

"RFDN"		[450-459]			1		1		R

"TWTA"		[460-469]			2		2		R

"TRSP"		[470-479]			2		2		R

"SPIRE"		[480-529]			1		0		S

"SRP_COOLER"	[530-559]			0		1		S

"THERMAL_H"	[600-749]			1		0		T

"THERMAL_P"	[750-899]			0		1		T

"VISUAL_MON"	[560-564]			TBD		TBD		V

"PCDU"		[565-569]			1		1		W

"BATTERY"		[570-574]			1		1		W

"SOLAR_AR_H"	[575-579]			1		0		W

"SOLAR_AR_P"	[580-584]			0		1		W

"STR_SW"		[585-589]			1		0		X

EGSE		[900-998]			1		1		Y

"PSEUDO"		[999-999]			1		1		Z

## Position

NMCVT-7510-C	- 	Position allocation							-	I

The "position" identifier of different "type of system elements" belonging to a "system element model" shall be allocated as follows (A range, identical to the one provided for "type of system element" number is provided for each element and for the same reason - In addition, this table provides the 1553 bus and OBDH address) :

CDMS		CDMS		ACC		ACC

Type of system		Position		Bus 1553	Bus OBDH	Bus 1553	Bus OBDH

element  identifier	Number		address	address	address	address

"ACC"		[001-009]

"GYRO"		[010-019]

"STR1"		[020-029]

"STR2"		[020-029]

"RWE"		[030-039]

"RW1"		[040-049]

"RW2"		[040-049]

"RW3"		[040-049]

"RW4"		[040-049]

"SAS-H1"		[050-059]

"SAS-H2"		[050-059]

"FSS1"		[060-069]

"FSS1"		[060-069]

"QRS1"		[070-079]

"QRS2"		[070-079]

"STR_MAPPER"	[080-089]

"AAD"		[090-099]

"SAS-P1"		[100-109]

"SAS-P2"		[100-109]

"SAS-P3"		[100-109]

"ACC_SW	"	[110-129]

"RCS"		[130-149]

"CDMU"		[150-159]

"CDMU_SW"	[160-179]

"FRAME_STR"	[180-189]

"HIFI"		[190-239]

"HFI"		[240-289]

"SYSTEM"		[290-299]

"CRYO_ELEC"	[300-309]

"CRYOSTAT"	[310-319]

"LFI"		[320-369]

"RAD_MON"	[370-379]

"PACS"		[380-429]

"LGA1"		[430-439]

"LGA2"		[430-439]

"LGA3"		[430-439]

"MGA"		[440-449]

"RFDN"		[450-459]

"TWTA1"		[460-469]

"TWTA2"		[460-469]

"TRSP1"		[470-479]

"TRSP2"		[470-479]

"SPIRE"		[480-529]

"SRP_COOLER"	[530-559]

"THERMAL"		[600-899]

"VISUAL_MON"	[560-564]

"PCDU"		[565-569]

"BATTERY"		[570-574]

"SOLAR_AR"	[575-584]

"STR_SW"		[585-589]

EGSE		[900-998]

"PSEUDO"		[999-999]

# attributes requirements

## Application ID

NMCVT-7500-C	- 	Application identifier allocation					-	I

The application identifiers allocation shall be as follows per subsystem :

According to RD3 annexe 3.

NMCVT-7600-C	- 	Description 								-	I

The descriptions (long and short) shall :

Consist of 26 letters of upper and lower case english alphabet A-Z, digits 0-9, 'space', plus and minus signs,

Not contain a quote, double quote, accent, comma, colon, full-stop, and semi-colon,

Not contain any special or non-printing character and in particular the under score unless it is absolutely necessary to define the data item,

Be as readable as possible,

Have an understandable abbreviations and acronyms,

Not be left empty.

### Short description

NMCVT-7610-C	- 	Short description							-	I

TBW

### Long description

NMCVT-7620-C	- 	Long description							-	I

TBW

## Software parameter identifier

NMCVT-7800-C	- 	Software parameter identifier					-	I

"Software parameter" identifier shall :

Be of IDIN05F (limited to 65535) subtype with the following limitations :

Generated by software SDE and reloaded inside HPSDB.

Be unique for a "software (CDMU or ACC) and real model".

# Annex 1 : Compliance matrix with RD1

| RD1 | Naming convention | Compliance | Remarks |
| --- | --- | --- | --- |
| General Conventions There shall be logically distinct databases for Herschel and Planck – this implies that the same naming conventions may be may be used for both Herschel and Planck. The naming convention will not provide the means for the logical distinction. |  | C | Supported by AD1 |
| A4.1 Field width constraints See AD-8. |  | PC | To be detailed during HPSDB development |
| A4.2 Descriptions Many tables in AD-8 include a descriptive field. This should be human-readable and gives further information on the record. The description provided for any data item should: Consist of 26 letters of upper and lower case English alphabet A-Z, digits 0-9 and ‘space’,and the plus and minus signs; Not contain a quote, double-quote, accent, comma, colon, full-stop or semi-colon; Not contain any special or non-printing character and in particular the under score unless it is absolutely necessary to define the data item; Be as readable as possible; Have understandable abbreviations and acronyms; Not be left empty. | NMCVT-7600-C | C |  |
| A4.3 Subsystem identifiers Subsystem identifiers are used to uniquely identify the relevant spacecraft subsystem for the data item in question. For the Herschel-Planck project the following identifiers have been defined (TBC when system definition complete): | NMCVT-4113-C | C | The following subsystems have been added : "C" for RCS "K" for Herschel CRYO "Y" for EGSE "Z" for pseudo (due to HPSDB) |
| A + B for Attitude and Orbit Control Subsystem (AOCS) | NMCVT-7500-C | PC | A : compliant B : not compliant |
| D + E for On-Board Data Handling Subsystem (CDMS) | NMCVT-7500-C | PC | D : compliant E : Not compliant |
| J for system | NMCVT-7500-C | C | To be clarify |
| W for Electrical Power Subsystem (PS or EPSS) | NMCVT-7500-C | C |  |
| R for Radio Frequency Subsystem (TT&C) | NMCVT-7500-C | C |  |
| T for Thermal Control Subsystem (TCS) | NMCVT-7500-C | C |  |
| M for Radiation Monitor | NMCVT-7500-C | C | To be clarify |
| V for Visual Monitor Camera | NMCVT-7500-C | C |  |
| F for Frame- structure etc. | NMCVT-7500-C | C | To be clarify |
| A for ACC Software Parameters | NMCVT-7500-C | NC | Set to B instead of A |
| C for CDMS Software Parameters | NMCVT-7500-C | NC | Set to E instead of C |
| X for Star Tracker Software Parameters | NMCVT-7500-C | C |  |
| H for HIFI | NMCVT-7500-C | C |  |
| P for PACS | NMCVT-7500-C | C |  |
| S for SPIRE | NMCVT-7500-C | C |  |
| H for HFI | NMCVT-7500-C | C |  |
| L for LFI | NMCVT-7500-C | C |  |
| S for Sorption Cooler Subsystem | NMCVT-7500-C | C |  |
| The Char 8 fields shall have the following format: The first character shall be a sub-system identifier selected from the above list as appropriate. The second character shall be a function specifier, as indicated in the following table. The remaining characters shall consist of the digits 0-9 inclusive and the 23 uppercase letters of the English alphabet (A-Z without the letters O, Q, or I, to minimise the likelihood of transcription errors when these are typed manually). |  | PC | The plus, minus, underscore, dash and dot characters are also allowed (NMCVT-0100-C) according to RD2 chapter 3.3 third bullet. |
| Parameter identifier (ground) : PCF_NAME Char 8 M, C,D (C for Constants D for Synthetic Parameters) | NMCVT-5130-C | PC | Other function specifier have been added (NMCVT-0110-C - Subtype IDE201F) : "K" for constante ("C" is used for TC" "Z" for system parameters "U" for user parameters The "type of data" is the sixth character instead of eighth. |
| Parameter identifier (on-board) PCF_PID N10 | NMCVT-7800-C | C | Warning : in RD3 (PSICD) the software parameter is coded on 16 bits so cannot be grater than 65535 (N5). |
| Monitoring numerical curve identifier CAF_NUMBR N4 | NMCVT-5370-C | NC | N9 instead of N4 |
| monitoring texte curve identifier TXF_NUMBR N4 | NMCVT-5370-C | NC | N9 instead of N4 |
| monitor plynomial curve identifier MCF_IDENT N4 | NMCVT-5370-C | NC | N9 instead of N4 |
| Monitor packet identifier (fixed length) PID_SPID N10 | NMCVT-4380-C | C |  |
| Monitor packet identifier (variable length) PID_TPSD N10 | NMCVT-4380-C | C |  |
| Alphanumeric display DPF_NUMBE Char8 A (AM - Displays created to feed data for a Mimic shall use Function Specifier AM) | NMCVT-6100-C | C |  |
| Grphic display identifier GPF_NUMBE Char8 G | NMCVT-6110-C | C |  |
| Scrolling display identifier SCF_NUMBE Char8 L | NMCVT-6130-C | C |  |
| TC packet header TCP_ID Char8 X | NMCVT-4505-C | C | To be confirmed |
| TC packet header parameter PCPC_PNAME Char8 Y | NMCVT-5130-C | PC | Defined as any other parameters |
| TC packet identifier CCF_CNAME Char8 C | NMCVT-4580-C | C |  |
| Command parameter CPC_PNAME Char8 P | NMCVT-5130-C | C |  |
| Command sequence CSF_NAME Char8 S | NMCVT-4660-C | C |  |
| Command sequence formal parameter CSP_FPNAME Char8 F |  | C |  |
| Verification stage identifier CVS_ID N5 |  | PC | Via expected effect of TC |
| Command parameter set PST_NAME Char8 T |  | C |  |
| Command parameter set value PSV_PVSID Char8 V |  | C |  |
| Command numerical curve CCA_NUMBR N4 | NMCVT-5370-C | NC | N9 instead of N4 |
| Command textual curve PAF_NUMBR N4 | NMCVT-5370-C | NC | N9 instead of N4 |
| Command sequence parameter range check PRF_NUMBR N4 |  | NC | As for curve the N4 length is too limited. |
| N10 => Ten digit number N such that 0 < N < 2 32 -1 |  | NC | Non-duplication guaranty by HPSDB instanciations |
| N5 => Five digit number 00000 - 32767 |  | NC | Non-duplication guaranty by HPSDB instanciations |
| N4 => Four digit number 0001 - 9999 |  | NC | Non-duplication guaranty by HPSDB instanciations |
| Char8 => Eight Character alphanumeric identifier intended for Human use. | NMCVT-0110-C | C |  |
| N4 : 1 000 - 1 999 HIFI HFI |  | NC | Non-duplication guaranty by HPSDB instanciations |
| N4 : 2 000 - 2 999 PACS LFI |  | NC | Non-duplication guaranty by HPSDB instanciations |
| N4 : 3 000 - 3 999 SPIRE Sorption Cooler Subsystem |  | NC | Non-duplication guaranty by HPSDB instanciations |
| N4 : 4 000 - 8 999 Alcatel |  | NC | Non-duplication guaranty by HPSDB instanciations |
| N4 : 9 000 - 9 999 ESOC |  | NC | Non-duplication guaranty by HPSDB instanciations |
| N5 : 00 001- 02 999 HIFI HFI |  | NC | Non-duplication guaranty by HPSDB instanciations |
| N5 : 03 000- 05 999 PACS LFI |  | NC | Non-duplication guaranty by HPSDB instanciations |
| N5 : 06 000 - 08 999 SPIRE Sorption Cooler Subsystem |  | NC | Non-duplication guaranty by HPSDB instanciations |
| N5 : 09 000 - 19 999 Alcatel |  | NC | Non-duplication guaranty by HPSDB instanciations |
| N5 : 20 000 - 29 999 ESOC |  | NC | Non-duplication guaranty by HPSDB instanciations |
| N10 : 10 000 000 -19 999 999 HIFI HFI |  | NC | Non-duplication guaranty by HPSDB instanciations |
| N10 : 20 000 000 -29 999 999 PACS LFI |  | NC | Non-duplication guaranty by HPSDB instanciations |
| N10 : 30 000 000 -39 999 999 SPIRE Sorption Cooler Subsystem |  | NC | Non-duplication guaranty by HPSDB instanciations |
| 40 000 000 - 79 999 999 Alcatel |  | NC | Non-duplication guaranty by HPSDB instanciations |
| 80 000 000 - 99 999 999 ESOC |  | NC | Non-duplication guaranty by HPSDB instanciations |
| Experience indicates that it can also be very useful to indicate the type of data being communicated by a telemetry item or the destination of a command. For example T for a temperature, V for a voltage, C for a current, D for a discrete hardware measurement, W for a software parameter if a separate identifier has not been made available. This type information should be the final character of the Designator, when supplied. | NMCVT-0110-C | NC | Impossible to comply with this request (not mandatory) and some identifier length too short (TC packet, Parameters, …) |
| A4.4 Telemetry Packet Packet identifiers shall be allocated on the basis of the source of the packet. Example 10000003 could be defined by HIFI | NMCVT-4380-C | NC | Non-duplication guaranty by HPSDB instanciations |
| A4.5 Command Master Function Number: Example: AC0001 (Command number for the AOCS subsystem) | NMCVT-4580-C | C | Warning : the example looks wrong : 6 characters. |
| A4.5.1 Command Parameter Reference Number, (PREF): Example: AP0001 (Command parameter for the AOCS subsystem) Please note that the command parameter name is not used to link it to any given command packet because they can be used in many different packets and therefore are not unique across them. They are unique within their own table and therefore no two-command parameters can share the same name. | NMCVT-5130-C | C | Warning : the example looks wrong : 6 characters and no "type of parameter". |
| A4.5.2 Command Sequences: Command sequences shall be identified the subsystem identifier and the letter S for sequence. For example AS123 is a sequence for the AOCS subsystem. Example: AS001svt | NMCVT-4660-C | C | Warning : the example looks wrong : 6 characters. |
| A4.6 Telemetry Parameters A telemetry parameter shall be the relevant subsystem code letter and followed by the data type. Example: AM1234 | NMCVT-5130-C | C | Warning : the example looks wrong : 6 characters. |
| A4.6.1 Derived or Synthetic Parameters: Derived parameters shall be identified by the subsystem identifier followed by the letter D (Derived or Synthetic) followed by a four-digit unique number derived parameter type designator T and a four-digit unique number and.) Where T can be: S – Saved (Supported by the system) H - Hard coded (Needs C++ complier.) D – Dynamic (Most common. Supported directly by the editor application) Example: ADD0004 (Leading zeros are required) ADS1234 All synthetic parameters must be defined in the telemetry database. | NMCVT-5130-C | PC | Warning : requirement unclear, but potential modification of naming convention for "T" code" ??? Warning : the example looks wrong : 6 characters. |
| A4.6.3 Constant Parameters: Constant parameters shall be identified by the subsystem identifier followed by the letter C (Constant) followed by a four-digit unique number. (i.e. AC1234) | NMCVT-5130-C | C | Warning : the example looks wrong : 6 characters. |
| A4.7.1 Alphanumeric Displays (AND): AND naming shall use the subsystem identifier followed by the letter A (e.g. AA1234) | NMCVT-6100-C | C | Warning : the example looks wrong : 6 characters. |
| A4.7.2 Graphical Displays (GRD): GRD naming shall use the subsystem identifier followed by the letter G (e.g. AG1234) | NMCVT-6110-C | C | Warning : the example looks wrong : 6 characters. |
| A4.7.3 Mimic Alphanumeric Displays: Mimic alphanumeric displays (One Mimic alphanumeric display must be defined for each Mimic Diagram created) use the subsystem identifier followed by AM (e.g. AAM1234). | NMCVT-6120-C | C | Warning : the example looks wrong : 6 characters. |
| A4.7.4 Mimic Display Diagrams (MDD): MDD naming shall use the subsystem identifier followed by the function specifier AD (i.e. AAD1234) | NMCVT-6125-C | C | Warning : the example looks wrong : 6 characters. |
| A4.7.5 Scrolling Log Displays (SLD): SLD naming shall use the subsystem identifier followed by the function specifier L followed by a four-digit number (i.e. AL1234) | NMCVT-6130-C | C | Warning : the example looks wrong : 6 characters. |
| A4.8 Convention to be used for Procedures: Subsystem Identifier TBC:. AOC for AOCS DHS for CDMS EPS for Power TCS for TCS TTC for RF part of command, telemetry and tracking RM for Radiation Monitor VMC for Visual Monitoring Camera OBS for On-Board Software procedures SYS for Systems Procedures MPP for Mission Planning Procedures PAC for PACS HIF for HIFI SPI for SPIRE HFI for HFI LFI for LFI SOR for Sorption Cooler System |  | NC | Not covered by HPSDB tool |
| A4.8.1 Flight Control Procedures, FCP: FCP's shall be referenced using a four-digit number preceded by FCP_ and the relevant subsystem identifier followed by 'underscore' (i.e. FCP_AOC_1234) Note: leading zeros are required (i.e. FCP_AOC_0001) |  | NC | Not covered by HPSDB tool |
| A4.8.2 Contingency Recovery Procedures: CRP's shall be referenced using four digit number preceded by CRP_ and the relevant subsystem identifier followed by underscore' (i.e. CRP_AOC_1234) Note: leading zeros are required (i.e. CRP_AOC_0001) |  | NC | Not covered by HPSDB tool |
| A4.8.3 Timelines: The character string TDoyFfNn shall identify Timelines as follows: Where: T = Timeline Doy = Day of Year Ff = File number Nn = Version number |  | NC | Not covered by HPSDB tool To be clarify. |

# Summary

## Configuration

NMVCT-4030-C

| Type of system element |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| IDCH11F |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4040-C

| Type of system element |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| IDIN03F |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4050-C

| real element |  |  |
| --- | --- | --- |
| Type of system | Real element |  |  |
| IDCH11F | IDIN03F |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4060-C

| Real element number |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| IDIN03F |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4075-C

| Element direct definition |  |  |
| --- | --- | --- |
| Type of system | Pseudo real element |  |  |
| IDCH11F | 9 | 9 | 9 |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4100-C

| System element model |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| IDCH10F |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4111-C

| System element model direct definition |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| IDCH10F |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4113-C

| Subsyst. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| IDCHO1F |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4117-C

| Position |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| IDIN03F |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4120-C

| real model |  |  |  |  |
| --- | --- | --- | --- | --- |
| System element model | real model |  |  |  |  |
| IDCH10F | IDIN02F |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4130-C

| Real model |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| IDIN02 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

## Telemetry packets

NMVCT-4305-C

| TM packet standard template |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Subsyst. |  |  |  |  |  |  |  |  |  |
| Z | X | T | M | S | D | IDIN04F |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4320-C

| TM packet PSICD template |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Subsyst. |  |  | type | subtype |  |  |  |  |  |  |
| Z | X | T | M | P | S | IDIN02F | IDIN02F |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4340-C

| Theoretical TM packet |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Type of system element |  |  |  |  |  |  |  |  |  |  |
| IDIN03F | IDIN04F |  |  |  |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4360-C

| Theoretical TM structure |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| type of system element |  |  |  |  |  |  |  |
| IDIN03F | T | M | S | T | IDIN04F |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4374-C

| Theoretical TM packet group |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| type of system element |  |  |  |  |  |  |  |
| IDIN03F | T | M | G | R | IDIN04F |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4380-C

| Real TM packet |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Theoretical TM packet | Position |  |  |  |  |  |  |
| Type of system element |  |  |  |  |  |  |  |  |
| IDIN03F | IDIN04F | IDIN03F |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4400-C

| Real TM structure |  |  |
| --- | --- | --- |
| Theoretical TM structure | Position |  |  |
| type of system element |  |  |  |  |  |
| IDIN03F | T | M | S | T | IDIN04F | IDIN03F |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4420-C

| Real TM packet group |  |  |
| --- | --- | --- |
| Theoretical TM packet group | Position |  |  |
| type of system element |  |  |  |  |  |
| IDIN03F | T | M | G | R | IDIN04F | IDIN03F |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4440-C

| TM packet direct definition |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Pseudo theoretical TM packet | Pseudo position |  |  |  |  |  |  |
| Pseudo type of system elem. |  |  |  |  |  |  |  |  |
| 9 | 9 | 9 | IDIN04F | 9 | 9 | 9 |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4450-C

| TM structure direct definition |  |  |
| --- | --- | --- |
| Pseudo theoretical TM structure | Pseudo position |  |  |
| Pseudo type of system elem. |  |  |  |  |  |
| 9 | 9 | 9 | T | M | S | T | IDIN04F | 9 | 9 | 9 |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4455-C

| TM packet group direct definition |  |  |
| --- | --- | --- |
| Pseudo theoretical TM packet group | Pseudo position |  |  |
| Pseudo type of system elem. |  |  |  |  |  |
| 9 | 9 | 9 | T | M | G | R | IDIN04F | 9 | 9 | 9 |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

## Telecommand packets

NMVCT-4505-C

| TC packet standard template |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Subsyst. |  |  |  |  |  |  |  |  |  |
| Z | X | T | C | S | D | IDIN04F |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4520-C

| TC packet PSICD template |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Subsyst. |  |  | type | subtype |  |  |  |  |  |  |
| Z | X | T | C | P | S | IDIN02F | IDIN02F |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4540-C

| Theoretical TC packet |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Function |  |  |  |  |  |  |  |  |  |  |  |  |  |
| C | IDCH03F |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4560-C

| Theoretical TC structure |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| type of system element |  |  |  |  |  |  |  |
| IDIN03F | T | C | S | T | IDIN04F |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4574-C

| Theoretical TC packet group |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| type of system element |  |  |  |  |  |  |  |
| IDIN03F | T | C | G | R | IDIN04F |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4580-C

| Real TC packet |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Subsyst. | Theoretical TC packet | Position |  |  |  |  |  |  |  |  |
|  | Function |  |  |  |  |  |  |  |  |  |  |
| IDCH01F | C | IDCH03F | IDIN03F |  |  |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4600-C

| Real TC structure |  |  |
| --- | --- | --- |
| Theoretical TC structure | Position |  |  |
| type of system element |  |  |  |  |  |
| IDIN03F | T | C | S | T | IDIN04F | IDIN03F |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4620-C

| Real TC packet group |  |  |
| --- | --- | --- |
| Theoretical TC packet group | Position |  |  |
| type of system element |  |  |  |  |  |
| IDIN03F | T | C | G | R | IDIN04F | IDIN03F |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4640-C

| TC packet direct definition |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Pseudo theoretical TC packet |  |  |  |  |  |  |  |  |
| Ps. SS | Function |  | Pseudo position |  |  |  |  |  |  |  |  |
| Z | C | IDCH03F | 9 | 9 | 9 |  |  |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4650-C

| TC structure direct definition |  |  |
| --- | --- | --- |
| Pseudo theoretical TC structure | Pseudo position |  |  |
| Pseudo type of system elem. |  |  |  |  |  |
| 9 | 9 | 9 | T | C | S | T | IDIN04F | 9 | 9 | 9 |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4655-C

| TC packet group direct definition |  |  |
| --- | --- | --- |
| Pseudo theoretical TC packet group | Pseudo position |  |  |
| Pseudo type of system elem. |  |  |  |  |  |
| 9 | 9 | 9 | T | C | G | R | IDIN04F | 9 | 9 | 9 |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4660-C

| Command sequence |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Subsyst. |  | Position |  |  |  |  |  |  |  |  |
|  | Function |  |  |  |  |  |  |  |  |  |  |
| IDCH01F | S | IDCH03F | IDIN03F |  |  |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4680-C

| Command sequence formal parameter |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Subsyst. |  | Position |  |  |  |  |  |  |  |  |
|  | Function |  |  |  |  |  |  |  |  |  |  |
| IDCH01F | F | IDCH03F | IDIN03F |  |  |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4685-C

| Command parameter set |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Subsyst. |  | Position |  |  |  |  |  |  |  |  |
|  | Function |  |  |  |  |  |  |  |  |  |  |
| IDCH01F | T | IDCH03F | IDIN03F |  |  |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4690-C

| Command parameter set value |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Subsyst. |  | Position |  |  |  |  |  |  |  |  |
|  | Function |  |  |  |  |  |  |  |  |  |  |
| IDCH01F | V | IDCH03F | IDIN03F |  |  |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4695-C

TBD

## 1553 messages

NMVCT-4705-C

| 1553 message template |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Ps. SS |  |  |  |  |  |  |  |  |  |
| Z | X | B | U | S | D | IDIN04F |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4725-C

| 1553 status word |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Subsyst. |  |  | RT address | Subaddress |  |  |  |  |  |  |
| IDCH01F | X | B | U | S | W | IDIN02F | IDIN02F |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4740-C

| Theoretical 1553 message |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Type of system element |  | A/C |  |  |  |  |  |  |
| IDIN03F | B | U | M | G | IDCH01F | IDIN03F |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4760-C

| Theoretical 1553 structure |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| type of system element |  | A/C |  |  |  |  |  |  |
| IDIN03F | B | U | S | T | IDCH01F | IDIN03F |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4774-C

| Theoretical 1553 message group |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| type of system element |  | A/C |  |  |  |  |  |  |
| IDIN03F | B | U | G | R | IDCH01F | IDIN03F |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4780-C

| Real 1553 message |  |  |
| --- | --- | --- |
| Theoretical 1553 message | Position |  |  |
| Type of system element |  | A/C |  |  |  |  |
| IDIN03F | B | U | M | G | IDCH01F | IDIN03F | IDIN03F |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4800-C

| Real 1553 structure |  |  |
| --- | --- | --- |
| Theoretical 1553 structure | Position |  |  |
| type of system element |  | A/C |  |  |  |  |
| IDIN03F | B | U | S | T | IDCH01F | IDIN03F | IDIN03F |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4820-C

| Real 1553 message group |  |  |
| --- | --- | --- |
| Theoretical 1553 message group | Position |  |  |
| type of system element |  | A/C |  |  |  |  |
| IDIN03F | B | U | G | R |  | IDIN03F | IDIN03F |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4840-C

| 1553 message direct definition |  |  |
| --- | --- | --- |
| Pseudo theoretical 1553 message | Pseudo position |  |  |
| Pseudo type of system elem. |  | A/C |  |  |  |  |
| 9 | 9 | 9 | B | U | M | G | IDCH01F | IDIN03F | 9 | 9 | 9 |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4850-C

| 1553 structure direct definition |  |  |
| --- | --- | --- |
| Pseudo theoretical 1553 structure | Pseudo position |  |  |
| Pseudo type of system elem. |  | A/C |  |  |  |  |
| 9 | 9 | 9 | B | U | S | T | IDCH01F | IDIN03F | 9 | 9 | 9 |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4860-C

| 1553 message group direct definition |  |  |
| --- | --- | --- |
| Pseudo theoretical 1553 message group | Pseudo position |  |  |
| Pseudo type of system elem. |  | A/C |  |  |  |  |
| 9 | 9 | 9 | B | U | G | R | IDCH01F | IDIN03F | 9 | 9 | 9 |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

## OBDH interfaces

NMVCT-4974-C

| Theoretical OBDH interrogation |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Type of system element |  | A/C |  |  |  |  |  |  |
| IDIN03F | D | H | I | N | C | IDIN03F |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-4990-C

| Theoretical OBDH interrogation group |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| type of system element |  | A/C |  |  |  |  |  |  |
| IDIN03F | D | H | G | R | C | IDIN03F |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-5020-C

| Real OBDH interrogation |  |  |
| --- | --- | --- |
| Theoretical OBDH interrogation | Position |  |  |
| Type of system element |  | A/C |  |  |  |  |
| IDIN03F | D | H | I | N | C | IDIN03F | IDIN03F |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-5044-C

| Real OBDH interrogation group |  |  |
| --- | --- | --- |
| Theoretical OBDH interrogation group | Position |  |  |
| type of system element |  | A/C |  |  |  |  |
| IDIN03F | D | H | G | R | C | IDIN03F | IDIN03F |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-5060-C

| OBDH interrogation direct definition |  |  |
| --- | --- | --- |
| Pseudo theoretical OBDH interrogation | Pseudo position |  |  |
| Pseudo type of system elem. |  | A/C |  |  |  |  |
| 9 | 9 | 9 | D | H | I | N | C | IDIN03F | 9 | 9 | 9 |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-5080-C

| OBDH interrogation group direct definition |  |  |
| --- | --- | --- |
| Pseudo theoretical OBDH interrogation group | Pseudo position |  |  |
| Pseudo type of system elem. |  | A/C |  |  |  |  |
| 9 | 9 | 9 | D | H | G | R | C | IDIN03F | 9 | 9 | 9 |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

## Parameeters

NMVCT-5110-C

| Theoretical parameter |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Function |  |  |  |  |  |  |  |  |  |  |  |  |  |
| IDE201F | IDCH03F |  |  |  |  |  |  |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-5126-C

| Theoretical parameter group |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| type of system element |  | A/C |  |  |  |  |  |  |
| IDIN03F | P | A | G | R | IDCH01F | IDIN03F |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-5130-C

| Real parameter |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Subsyst.. | Theoretical parameter | Position |  |  |  |  |  |  |  |  |
|  | Function |  |  |  |  |  |  |  |  |  |  |
| IDCH01F | IDE201F | IDCH03F | IDCIN3F |  |  |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-5150-C

| Parameter direct definition |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Pseu. SS | Pseudo theoretical parameter | Pseudo position |  |  |  |  |  |  |  |  |
|  | Function |  |  |  |  |  |  |  |  |  |  |
| Z | IDE201F | IDCH03F | 9 | 9 | 9 |  |  |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-5160-C

| Real parameter group |  |  |
| --- | --- | --- |
| Theoretical parameter group | Position |  |  |
| type of system element |  | A/C |  |  |  |  |
| IDIN03F | P | A | G | R | IDCH01F | IDIN03F | IDIN03F |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-5175-C

| Parameter group direct definition |  |  |
| --- | --- | --- |
| Pseudo theoretical parameter group | Pseudo position |  |  |
| Pseudo type of system elem. |  | A/C |  |  |  |  |
| 9 | 9 | 9 | P | A | G | R | IDCH01F | IDIN03F | 9 | 9 | 9 |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

## Curves

NMVCT—5360C

| Theoretical curves |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Type of system element number |  |  |  |  |  |  |  |  |  |  |  |
| IDIN03F | IDIN03F |  |  |  |  |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT—5370C

| Real curves |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Theoretical curve | Real element number |  |  |  |  |  |  |  |
| Type of system element number |  |  |  |  |  |  |  |  |  |
| IDIN03F | IDIN03F | IDIN03F |  |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-5380-C

| Curves direct definition |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Pseudo theoretical curve | Pseudo real element number |  |  |  |  |  |  |  |
| Pseudo Type of system element nb |  |  |  |  |  |  |  |  |  |
| 9 | 9 | 9 | IDIN03F | 9 | 9 | 9 |  |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

## Displays

NMVCT-6100-C

| Alphanumeric display |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Subsyst. | Function |  | Position |  |  |  |  |  |  |  |  |
| IDCH01F | A | IDCH03F | IDIN03F |  |  |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-6110-C

| Graphic display |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Subsyst. | Function |  | Position |  |  |  |  |  |  |  |  |
| IDCH01F | G | IDCH03F | IDIN03F |  |  |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-6120-C

| Alphanumeric mimic display |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Subsyst. | Function |  | Position |  |  |  |  |  |  |  |  |
| IDCH01F | A | M | IDCH02F | IDIN03F |  |  |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-6125-C

| Mimic diagram display |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Subsyst. | Function |  | Position |  |  |  |  |  |  |  |  |
| IDCH01F | A | D | IDCH02F | IDIN03F |  |  |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

NMVCT-6030-C

| Scrolling display |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Subsyst. | Function |  | Position |  |  |  |  |  |  |  |  |
| IDCH01F | L | IDCH03F | IDIN03F |  |  |  |  |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |

End of the document

# Text boxes

HERSCHEL / PLANCK