# DRCU Frequency Plan - 4/02/02                           SPIRE-SAP-NOT-001175

P. Levacher / C. Cara

| SPIRE Unit / | Frequency Source | Frequency Range | W-form | Signal Level | Comment |
| --- | --- | --- | --- | --- | --- |
| subsystem |  | Lower | Upper |  |  |  |  |
| DCU | Cmd IF Clock | 312 kHz |  | Rect. | 0 | 5 V | Differential RS422 – Continuous |
|  | Data IF Clock | 1MHz | 2.5 MHz | Rect | 0 | 5 V | Differential RS422 |
|  | Master Clock | 10 MHz |  | Rect |  | 5 V | Crystal Oscillator – Internal to unit |
|  | Bolometer Bias | 50 Hz | 300 Hz | Sine | 0 | 100 mV | Differential – Highly sensitive signal |
|  | T/C Bias | 50 Hz | 300 Hz | Sine | 0 | 500 mV | Differential – Highly sensitive signal |
| MCU | Cmd IF Clock | 312 kHz |  | Rect. | 0 | 5 V | Differential RS422- Continuous |
|  | Data IF Clock | 1MHz | 2.5 MHz | Rect | 0 | 5 V | Differential RS422 |
|  | Master Clock | 40 MHz |  | Rect |  | 5 V | Crystal Oscillator – Internal to unit |
|  | DSP Clock | 20 MHz |  | Rect |  | 5 V | Master clock / 2 Internal to unit |
|  | LVDT excitation | 2.5 kHz |  | Sine |  | 3 V | Differential +/- 20 % |
|  | DAC change | 3.0 kHz | 10 kHz | Random |  | 10 V | Internal to unit |
|  | Position encoder | 0 | 2.5 kHz | Sine |  | 3 mV | Differential 250 Hz at nominal speed |
| SCU | Cmd IF Clock | 312 kHz |  | Rect. | 0 | 5 V | Differential RS422- Continuous |
|  | Data IF Clock | 1MHz | 2.5 MHz | Rect | 0 | 5 V | Differential RS422 |
|  | Master Clock | 10 MHz |  | Rect |  | 5 V | Crystal Oscillator – Internal to unit |
|  | 300 mK TS Bias | 20 Hz |  | Rect |  | 6 mV | Tr/Tf = 1ms Highly sensitive signal |
|  | Photo Stimulus | 0 | 5 Hz | Rect |  |  |  |
| PSU | DC/DC switching frequency | 131 kHz TBC |  |  |  |  | Free runing - ± 10% - internal to unit |