Herschel-SPIRE

Interface Control Document

BDA

SPIRE-JPL-PRJ-001181

| James J. Bock | Matthew J. Griffin |
| --- | --- |
| SPIRE Co-Investigator | SPIRE Principle Investigator |
| Jet Propulsion Laboratory, Pasadena, USA | Cardiff University, Wales, UK |
| Bruce Swinyard | John Delderfield |
| Spire Instrument Scientist | SPIRE Systems Engineeer |
| Rutherford Appleton Laboratory, Oxfordshire, UK | Rutherford Appleton Laboratory, Oxfordshire, UK |
| Gerald Lilienthal | Kenneth J. King |
| U.S. SPIRE Detector Project Element Manager | SPIRE Project Manager |
| Jet Propulsion Laboratory, Pasadena, USA | Rutherford Appleton Laboratory, Oxfordshire, UK |

Document Change Record

| Revision /Status | Modifications |
| --- | --- |
| Rev | Date | Approved by |  |
| 1.0 |  |  |  |
| Draft 2.0 | 10/29 |  | Filling in the holes |
| Draft 3.0 | 11/1/01 |  | Added more info to all pages |
| JD | 14/11/01 |  |  |
| LH | Feb 4, ‘02 |  | Extensively revised |

Table of Contents

1	Scope	4

2	Applicable Documents	4

3	Applicable ICDs	4

4	Reference Documents	4

5	List of Acronyms	5

6	Functional Interface	6

6.1	Functional Description	6

7	Mechanical Interface	7

7.1	Fastener Data	7

7.2	Electrical Connector Mechanical Identification	8

7.2.1	BDAs	8

7.2.2	JFET modules.	9

7.2.3	FPU RF Filter(s)	10

8	BDA Mechanical Structural Integrity	11

8.1	PART DESCRIPTION:	11

8.2	FEA SUMMARY	11

8.2.1	FEA APPROACH	12

9	Thermal Interface	Error! Bookmark not defined.

9.1	BDA assembly conduction.	Error! Bookmark not defined.

9.2	Cross-section (mm2) of materials for BDA-to-FPU cables:	15

9.3	Cross-section (mm2) of materials for FPU-to-JFET cables:	15

10	Electrical Interface	16

11	Material and Process Description	17

11.1	Materials Identification and Usage List__Non Metallic	17

11.2	Materials Identification and Usage List__Metallic Materials	20

Materials Identification and Usage List - Processes	21

11.4	Materials Identification and Usage List - Procedures	22

11.5	Electronic Parts	23

# Scope

The purpose of this document is to complete the information about SPIRE instrument interfaces which are not included in the Interface Control Drawings listed as Applicable ICDs.  These Interface Control Drawings shall take precedence if they conflict with this document.  All this interface information is transferred under ITAR agreement between JPL and PPARC and between ESA and NASA according to the following restrictions:

Restrictions for ESA:

This technical data is export controlled under U.S. law and is being transferred by JPL to ESA for use exclusively on the Herschel SPIRE project.  The information may not be used for any other purposes, and shall not be re-transferred or disclosed to any other party without the prior written approval of NASA.

Restrictions for PPARC:

This technical data is export controlled under U.S. law and is being transferred by JPL to PPARC pursuant to the NASA / PPARC Letter of Agreement which entered into force on December 2, 1999.  This technical data is transferred to PPARC for use exclusively on the NASA/PPARC SPIRE on FIRST cooperative project, may not be used for any other purpose, and shall not be re-transferred or disclosed to any other party without the prior written approval of NASA.

# Applicable Documents

| Item | Doc. Number | Document Name |
| --- | --- | --- |
| AD1 | SCI-PT-IIDB/SPIRE-02124 | Herschel/Planck Instrument Interface Doc. Part B |
| AD2 | SPIRE-RAL-PRJ-000608 | Harness Definition Document |
| AD3 | SPIRE-RAL-PRJ-000617 | ICD Structure - Mechanical I/F |
| AD3 | SPIRE-RAL-DWG-000646 | SPIRE Instrument Block Diagram |
| AD4 | SPIRE-JPL-PRJ-000456 | Detector Subsystem Specification Document |

# Applicable ICDs

| Item | Doc. Number | Document Name |
| --- | --- | --- |
| ICD1 | 10209721 | BDA, Interface Control Drawing |
| ICD2 | 10209722 | JFET Module, Interface Control Drawing |
| ICD3 | 10209723 | FPU RF Filter, Interface Control Drawing |
| ICD4 | 10209725 | Wiring Diagram, Interface Control Drawing |
| ICD5 | 10209726 | Thermal Control, Interface Control Drawing |

# Reference Documents

| Item | Doc. Number | Document Name |
| --- | --- | --- |
| REF1 |  | Wire length and routing ICD (MSSL) |
| REF2 |  | Sub-millimeter filter materials (Cardiff) |
| REF3 |  | The SPIRE Instrument for Herschel |

# List of Acronyms

| AD | Applicable Document |
| --- | --- |
| BDA | Bolometer Detector Assembly |
| Co-I | Co-Investigator |
| CQM | Cryogenic Qualification Model |
| ESA | European Space Agency |
| FEA | Finite Element Analysis |
| Herschel | Name for Far Infrared and Submillimeter Telescope |
| HSJFP | Herschel SPIRE J-FET Unit (Photometer) |
| HSJFS | Herschel SPIRE J-FET Unit (Spectrometer) |
| HSDCU | Herschel SPIRE Detector Control Unit |
| HSFCU | Herschel SPIRE FPU Control Unit |
| FPU | Focal Plane Unit |
| FS | Flight Spare |
| FTS | Fourier Transform Spectrometer |
| GSE | Ground Support Equipment |
| ICD | Interface Control Document |
| IID-A | Instrument Interface Document (Part A) |
| IID-B | Instrument Interface Document (Part B) |
| JFET | Junction Field Effect Transistor |
| JPL | JET Propulsion Laboratory |
| MoU | Memorandum of Understanding |
| NASA | National Aeronautics and Space Agency |
| PA | Product Assurance |
| PDR | Preliminary Design Review |
| PFM | Proto-Flight Model |
| PI | Principal Investigator |
| PPARC | Particle Physics and Astronomy Research Council |
| QMW | Queen Mary and Westfield College |
| RAL | Rutherford Appleton Laboratory |
| RD | Reference Document |
| SPIRE | Spectral and Photometric Imaging Receiver |
| SVM | Service Module |
| TBC | To Be Confirmed |
| TBD | To Be Decided |

# Functional Interface

## Functional Description

SPIRE, the Spectral and Photometric Imaging Receiver, is a bolometer camera and spectrometer for ESA's Herschel satellite.  Herschel will give the scientific community access to a large space-borne far-infrared and submillimeter telescope equipped with a suite of instruments for imaging photometry and spectroscopy. As Herschel is an observatory mission, the design and scientific performance of its payload is a matter for oversight by ESA on behalf of the scientific community. ESA has established the Herschel Science Team to oversee and monitor the development and scientific optimisation of Herschel. Matters affecting significantly the scientific performance of SPIRE must be referred to the Herschel Science Team.

The design and scientific capabilities of SPIRE are described in more detail in The SPIRE Instrument for Herschel [REF5]. The main elements of the SPIRE instrument are shown schematically in Figure 1.

Figure 1:  Functional block diagram of SPIRE

For a more detailed picture see [AD3].

## Mechanical Interfaces

The mechanical mounting and interface features for each assembly are shown in their individual Interface Drawings, ICD1-3.

## Fastener Data

Unified threadform screws are MMSL(UK) provided, but all the reminder of these items are JPL furnished.

Each Bolometer Detector Array (BDA) is secured in place using 4 No. 6-32 UNF screws, 4 No. 6 washers, and torqued as specified in [REF6].  Note that torques depend on design of MSSL side of interface.

Each BDA bolts to the 300 mK thermal strap by 2 M2.0 screws, a Belleville spring stack, and torque to 0.21 NM as per [REF6]

Each JFET Module Assembly is secured in place using 10 M2.5 screws, 6 M2.5 washers, and torque to 0.46 NM on threaded inserts.  Through holes are torqued as specified in [REF7].

The RF Filter Module Assembly may be secured in place with 4 ST12391-1 studlocks and torqued to 2 in-lbs as per [REF8].

## Dynamic stability

The suspended parts of the BDA have 1mm of permitted movement from their nominal position before hitting bump stops. This is not to imply that they should ever make such a contact.

However the suspended parts can statically in 0g be up to 0.5mm in x, y, and/or z away from nominal w.r.t. the 1.7K housings.

The bump stops are not set up to be 1mm from the actual static position .  Therefore, 1.5mm movement in X, Y and Z is needed as a dynamic envelope around the 300mK parts shown in the drawings.

Clearly the BDA suspensions act symmetrically about their suspended centres of mass.  Since the Kevlar tension remains at ~30 lbs weight, ~130 Newtons, analysis estimates that the suspended part moves **TBC mm in the direction of a one G static force applied to its C. of G. without rotation to first order.  The mass of the suspended part of each BDA can to a very good approximation be obtained by taking the overall mass tabulated in sheets 5-7 of [ICD1] and subtracting **TBC grams, where **TBC=the mass of the 1.7K assembly.

## Electrical Connector Mechanical Identification

### BDAs

Each BDA has six possible connector positions J1-J6 as shown in [ICD1].  Not all the positions are used on every BDA, and the unused ones shall either be R.F. tight blanked or not machined through in the first place.

For each of the 5 BDA types, sheets 5-7 of [ICD1] show a data table which, amongst other information, identifies the BDA type number for each wavelength and photometer/spectrometer, and defines which out of J1 to J6 are used.  Locations J1-J6 are labelled with epoxy ink, see materials list.  Pin one locations will be noted on the ICD drawing.

All BDA connectors are Nanonics type STM 051 M6SN

### JFET modules.

JPL’s JFET Filter modules are assembled into two RAL provided racks, two modules making the HSJFS for the spectrometer and six making the HSFFP for the photometer.  Electrically all JFET modules are nominally identical, each containing two JFET membrane PCBs, excepting the matter of which JFET pair(s) are selected to be unused.  Connectors are as follows and will be enumerated on the rack by RAL.  Serial numbers for the JFETs will be labelled with epoxy ink, see the materials list.  This configuration follows [AD3].  Wiring diagram for JFETS is shown on ICD #10209725.

| BDA | Fharness | JFET Rack I/P | JFET Unit/J | JFET Rack O/P | C harness |
| --- | --- | --- | --- | --- | --- |
| PSW J1 | 1 | HSJFP J29 | P1 J06/J01/J02 | HSJFP J1/2 | 9 |
| PSW J2 | 2 | HSJFP J30 | P2 J08/J03/J04 | HSJFP J3/4 | 9 |
| PSW J3 | 3 | HSJFP J31 | P3 J06/J01/J02 | HSJFP J5/6 | 8 |
| PSW J4 | 4 | HSJFP J32 | P4 J08/J03/J04 | HSJFP J7/8 | 8 |
| PSW J5 | 5 | HSJFP J33 | P5 J06/J01/J02 | HSJFP J9/10 | 7 |
| PSW J6 | 6 | HSJFP J34 | P6 J08/J03/J04 | HSJFP J11/12 | 7 |
| PLW J5 | 7 | HSJFP J35 | P7 J06/J01/J02 | HSJFP J13/14 | 6 |
| PLW J6 | 8 | HSJFP J36 | P8 J08/J03/J04 | HSJFP J15/16 | 6 |
| PMW J1 | 9 | HSJFP J37 | P9 J06/J01/J02 | HSJFP J17/18 | 5 |
| PMW J2 | 10 | HSJFP J38 | P10 J08/J03/J04 | HSJFP J19/20 | 5 |
| PMW J3 | 11 | HSJFP J39 | P11 J06/J01/J02 | HSJFP J21/22 | 4 |
| PMW J4 | 12 | HSJFP J40 | P12 J08/J03/J04 | HSJFP J23/24 | 4 |
| SSW J5 | 13 | HSJFS J11 | S1 J06/J01/J02 | HSJFS J1/2 | 2 |
| SSW J6 | 14 | HSJFS J12 | S2 J08/J03/J04 | HSJFS J3/4 | 2 |
| SLW J5 | 15 | HSJFS J13 | S3 J06/J01/J02 | HSJFS J5/6 | 1 |
| Tcontrol | 28 | HSJFS J14 | S4 J08/J03/J04 | HSJFS J7 | 2 to I4+ |

Reading in the same sequence as the table, the JFET 15way filtered connectors HSJFP 41-46, HSJFP 47-52, HSJFS 15-16 couple to HSJFP 25&27, HSJFP26&28 and HSJFS9&10 respectively using three JPL supplied copper harnesses that may be left connected to the racks.  These route the JFET power, bias and heater wiring.

### FPU RF Filter(s)

JPL’s RF Filter Modules are assembled into one RAL provided rack.  This rack will hold all 12 modules.  Electrically all RF modules are nominally identical servicing a single 37 way MDM connector pair.  Connectors will be shown on the assembled rack.   RAL will provide for the labelling of the modules in the housing.  JPL will enumerate serial numbers on the modules upon delivery using epoxy ink, see materials list.  Wiring diagram for RF Filters is shown on ICD #10209723.

# BDA Mechanical Structural Integrity

To state the matter simply, JPL has satisfied its engineers that the elements suspended within BDA units will remain in place before and after launch and thus the unit will comply with [ICD1].  The situation is as follows.

## PART DESCRIPTION:

The BDA comprises two sections.  The first a 1.7 Kelvin outer structure, which mounts to the SPIRE detector boxes via adaptor plates. The components of the 1.7 Kelvin structure are the Flexure Ring, Invar Suspension Rings, and four Vespel Posts.

The second section is a 300milli-Kelvin inner structure consisting of the Top Ring, Spacers, Bottom Ring, Cover Plate, and the Feedhorn.  It is thermally isolated from first by two Kevlar suspension cables.  Kevlar was chosen for its low thermal conductance and high strength.  This inner structure includes the silicon bolometric thermal detectors.

The Kevlar suspension cable is preloaded to ~30 pounds weight ±20 pounds at room temperature according to JPL internal procedures.  This includes verification of the tension achieved at room temperature.  The design gives a nominally constant tension in the Kevlar cables during thermal transition.

## FEA SUMMARY

The BDA is analyzed to the Design and Manufacture requirements specified in the Detector  Subsystem Specification document (Ref. 1).  The specification states that the BDA is to survive a 100G qualification quasi-static load in conjunction with load derived from a room temperature to 90 Kelvin thermal transition.   Although the requirement states the minimum temperature during qualification testing is to be 90 Kelvin, this analysis uses the thermal transition to the flight operating temperature of .3 Kelvin.  This was done to access the structural integrity of the BDA when subjected to flight thermal loading.

The major structural components all exhibited positive margins of safety with +.35 for the Flexure Ring being the lowest.  Likewise, all fasteners, alignment pins, and shear pins exhibited positive margins of safety with +1.02 being the lowest for the shear pins that connect the Flexure Ring to the top Invar Suspension Ring.  All joints exhibited factors of safety in excess of one, with 1.15 being the lowest for the pulley-to-Bottom Ring connection.

### FEA APPROACH

A finite element model was created to solve for stress in each structural component, quantify loads in each joint and fastener, and determine the mass participation/frequency for each resonant mode.  MSC/NASTRAN was used in solving for the aforementioned items.

#### FEA  Load Case Results

The following table summarizes the output of the FEA analysis.

TTable 1: Margin of Safety Summary for BDA parts

Table 2: Fastener Margin of Safety Summary

Table 3: Joint Factor of Safety Summary

# Thermal Interface

This information is in addition to that in {ICD6].

The following are physical interface data so the BDAs that meet their thermal load values given in [AD4].

## BDA assembly conduction.

The area to length aspect ratios (A/L in mm) of materials linking the BDA 300mK sections to the 1.7K sections, the first three being electrical harnesses, are as follows:-

| Array | Constantin | Kapton | Adhesive | Kevlar |
| --- | --- | --- | --- | --- |
| P/LW | < 1.9 x10-3 [1.5 x10-3] | < 0.06 [0.05] | < 0.04 [0.02] | < 0.25 [0.15] |
| P/MW | < 3.9 x10-3 [3.1 x10-3] | < 0.13 [0.11] | < 0.09 [0.04] | < 0.25 [0.15] |
| P/SW | < 5.8 x10-3 [4.6 x10-3] | < 0.19 [0.16] | < 0.13 [0.06] | < 0.25 [0.15] |
| S/LW | < 1.0 x10-3 [0.8 x10-3] | < 0.03 [0.03] | < 0.02 [0.01] | < 0.25 [0.15] |
| S/SW | < 1.9 x10-3 [1.5 x10-3] | < 0.06 [0.05] | < 0.04 [0.02] | < 0.25 [0.15] |

[] refer to nominal values

The average thermal length is 33 mm for the electrical harnesses and, 23 mm for Kevlar suspensions.

## Cross-section (mm2) of materials for BDA-to-FPU cables:

Manganin		Stainless		PFA

.329			1.168			2.65

## Cross-section (mm2) of materials for FPU-to-JFET cables:

Manganin		Stainless		PFA			Constantin RF shield

.329			1.168			2.65

# Electrical Interface

This information is in addition to that given in JPL’s [ICD3] and  [ICD5].

The overall configuration of BDAs, JFEts and harnesses is given in [AD2].

Each BDA electrical bolometer signal is a differential signal taken directly from the ends of the bolometer element. A quiet symmetric AC voltage bias, accurately symmetrical about ground, is supplied to each detector array.  The bolometer elements are each current biased from this AC bias by two 300mK 10Mresistors from a resistor array integral within the BDA.  The A-side of each signal is connected to the positive AC bias polarity, and the B-side is connected to the negative polarity.

16 cables carry bolometer signals, detector bias and ground between the BDAs and the JFET modules.  Each of these cables are divided into two sections, one running from the JFET module to the 4 K wall of the FPU, and one running from the FPU to the BDA.  The two sections connect electrically at the FPU wall.  The cables must be RF shielded from the JFET module to the FPU wall to maintain the electrical continuity of the Faraday cage.

The JFET module provides differential power amplification at a little less than unity voltage gain for the bolometer signals.  The electrical interface consists of input signals from the bolometers, and output signals to the ESA-supplied cryo-harness.  The JFET modules require power (Vdd, Vss) and heater supply for operation.  The module also passes detector bias and ground along to the bolometers.  The JFET module is electrically integral to the cryogenic Faraday cage, and thus provides RF filtering of all electrical connection passing through the Faraday cage.  The RF filters are integral to the JFET module.

JPL is also providing cables connecting the 15-way MDM inputs from the JFET modules to the ESA cryoharness.  The wiring of these cables is defined in [AD2].

The electrical interface shown in drawing 10209725 describes the wiring of detector channels through the BDA nano connector interface, BDA-to-JFET cables, through JFET amplifiers, out to the 25-way MDM output connectors on the JFET module.  All shielding and ground connections are specified in this drawing.  This ICD must be consistent with the Harness Definition Document.

JPL is also providing RF filter modules for filtering cables at the cryogenic Faraday cage required by other subsystems.  The electrical interface for the RF filter modules is shown in drawing 10209723.

# Material and Process Description

## Materials Identification and Usage List__Non Metallic

| Item No. | Material Description/ Brand Name Supplier | Application | Material Specifications | Thermal Vacuum Stability(%) | JPL Rating1 | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Vespel, Dupont SP1 Unloaded | Structural Support |  | TML = 1.09 VCM= 0.00 WVR=0.40 | 1 |  |
| 2 | Vespel, Dupont SP3 Molybdenium Loaded | Snubber |  | TML = VCM = WVR = |  | Need to get material’s data |
| 3 | Kevlar 29 Yarn, Dupont Braided. Denier???? | Tension Member |  | TML =3.13 VCM=0.19 WVR=1.76 | 3 | Thermal vacuum bakeout required. Is a bakeout currently planned? How much material will be used? |
| 4 | Stycast 2850 FT | Adhesive |  | TML = VCM= WVR= | ? | Need to get materials data |
| 5 | EC2216 | Adhesive |  | TML =0.97 VCM=0.02 WVR=0.32 | 2 | Do not use material if hardware will be exposed to temperatures greater than 80°C |
| 6 | JFET boards (polyimide) |  |  | TML = VCM= WVR= |  |  |
| 7 | RF filter connector potting |  |  | TML = VCM= WVR= |  |  |
| 8 | Diallyl Phthalate | Connector Insulator | MIL-M-14G Type SDG-F |  |  |  |
| 9 | Chomerics EMI/EMP Gasket | RF gasket material | MIL-G-83528 Type A |  |  |  |
| 10 | Teflon | Wire Insulation | ST 11478 |  |  |  |
| 11 | Epoxy | Cable potting. | TBD | TML = VCM= WVR= |  |  |
| 12 | Epoxy ink |  |  | TML = VCM= WVR= |  |  |
| 13 | Urlane 5750A/B | Conformal Coating | BS515376 | TML = VCM= WVR= |  |  |
| 14 | Silicon |  |  | TML = VCM= WVR= |  |  |
| 15 | Silicon Nitride |  |  | TML = VCM= WVR= |  |  |
| 16 | Germanium |  |  | TML = VCM= WVR= |  |  |
| 17 | Kapton | Rigid Flex Cable Insulation | IPC-FC-232C/1 | TML = VCM= WVR= |  |  |
| 18 | Acrylic adhesive | Fabricate Rigid Flex Cable | IPC-FC-232C/1 | TML = VCM= WVR= |  |  |
| 19 | Polyimide Resin Glass Base | Fabricate Rigid Flex Cable | IPC-4101/40 | TML = VCM= WVR= |  |  |
| 20 | Solder mask | Fabricate Rigid Flex Cable | BS502673 | TML = VCM= WVR= |  |  |
| 21 | Armstrong C7/W | Via Fill | D8208 | TML = VCM= WVR= |  |  |
| 22 | Sub-millimeter filter materials |  | Cardiff | TML = VCM= WVR= |  | Explicit materials the responsibility of Cardiff. |
| 23 | Epoxy | Array to backshort |  | TML = VCM= WVR= |  |  |
| 24 | Epoxy | Feedhorn | Custom Microwave | TML = VCM= WVR= |  |  |
| 25 | Assorted electronics bits (thin resistors, ferrite in inductors, etc…) |  |  | TML = VCM= WVR= |  |  |

1) 1 - acceptable, 2 - qualified acceptable, 3 - provisionally acceptable, 4 - unacceptable

## Materials Identification and Usage List__Metallic Materials

| Item No. | Material Description/ Condition | Application | Material Specifications | Stress Corrosion Cracking Rating | JPL Rating1 | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Invar 36 | Structural Elements | ASTM B753-T36 | A | 1 |  |
| 2 | Al 7075 T73 | Structural Elements | SAE-AMS-QQ-A-225/9 | 1 | 1 |  |
| 3 | Al 6061 T651 | Structural Elements | SAE-AMS-QQ-A-250/11 | 1 | 1 |  |
| 4 | A286 Stainless???? | Fasteners |  | 1 | 1 |  |
| 5 | 303 CRES | Fasteners | AMS 5738 | 1 | 1 |  |
| 6 | Copper, 99.999% pure | Thermal Strap |  | A | 1 | Sort out annealing and keeping pure. |
| 7 | CDA 172 | Clamps | B194 | 1 | 1 |  |
| 8 | Gold | Protective Plating | MIL-G-45204 |  |  |  |
| 9 | Nickel | Under Plating | QQ-N-290 |  |  |  |
| 10 | Indium | NTD Ge bonds |  |  |  |  |
| 11 | Phosphor Bronze |  |  |  |  |  |
| 12 | Copper | Wire Harness | ST 11478 |  |  |  |
| 13 | Manganin |  |  |  |  |  |
| 14 | Constantin |  |  |  |  |  |
| 15 | CRES Wire Braid | Cable Shield | AMS 5738 |  |  |  |
| 16 | BeCu | Connector Contacts | C17200 |  |  |  |
| 17 | Al | Connector shell | QQ-A-200/8 |  |  |  |
| 18 | SN63 Solder | Cable Assembly | QQ-S-571 |  |  |  |
| 19 | Nichrome | JFET source and load Resistors |  |  |  | Vacuum deposited oxide. |
| 20 | Aluminium | wirebonds | Purchase Order |  |  |  |
| 21 | Gold | wirebonds | Purchase Order |  |  |  |
|  | Copper , Electroplate | Feed Horn | MIL-C-14550 |  |  |  |

1) 1 - acceptable, 2 - qualified acceptable, 3 - provisionally acceptable, 4 - unacceptable

## Materials Identification and Usage List - Processes

| Item No. | Process | Specification | Materials Processed | Application | Rat-ing1 | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Gold Plating | MIL-G-45204, Class 3, Type 3 | Invar 36 | Corrosion Protection, Thermal Conduction | 1 |  |
| 2 | Gold Plating | MIL-G-45204, Class 3, Type 3 | Copper | Thermal Conduction | 1 |  |
| 3 | Passivation | FS 505146 | 303 CRES | Passivation | 1 |  |
| 4 | Bonding | D-8208, Section 3.17, FP513414 | Solithane 113/C113-300 Filled Polyurethane | Spot Bonding of Component Parts | 1 |  |
| 5 | Bonding | BS515871, D-8208, Section 3.17 | Scotch Weld 2216 B/A with Filler | Spot Bonding of Component Parts | 1 |  |
| 6 | Workmanship | FS504040 | ALL | Workmanship Standards for Mechanical Parts and Material | 1 |  |
| 7 | Torque | ES504255 | Fasteners | Torque Requirements, Threaded Fasteners | 1 | American Nation Standard |
| 8 | Solder Joint | D-8208, Section 3.14, FP513414 | Cables/Connectors | Solder Joint | 1 |  |
| 9 | Installation | D-8208, Section 3.12, FP513414 | Connectors | Connector Installation – Rectangular Miniature |  |  |
| 10 | Nickel plating | QQ-N-290 | Invar 36 | Corrosion Protection, Thermal Conduction |  |  |
| 11 | Annealing | BS506336 | Invar 36 | Stress relief |  |  |
| 12 | Parts vacuum bake out | AIDS | All Parts and Assemblies | Out gassing |  |  |
| 13 | Wire bonding | Mil-STD-883 | Gold | JFET and Detector Assembly |  |  |
| 14 | Wire bonding | Mil-STD-883 | Al | JFET Assembly |  |  |
| 15 | Torque | ES517040 |  | Torque Requirements, Threaded Fasteners |  | Metric fasteners |

1 - acceptable, 2 - qualified acceptable, 3 - provisionally acceptable, 4 – unacceptable

## Materials Identification and Usage List - Procedures

| Item No. | Process | Specification | Materials Processed | Application |  | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Bolometer Array Lithography | AIDS/Traveller | Silicon | Bolometer Fabrication |  |  |
| 2 | Bolometer Array chip attachment and etch | AIDS/Traveller |  | Bolometer Assembly |  |  |
| 3 | JFET lithography | AIDS/Traveller |  | JFET Substrate Fabrication |  |  |
| 4 | JFET die attach and etch | AIDS/D8208 |  | JFET Module Assembly |  |  |
| 5 | Load resistor lithography | AIDS/Traveller |  | Load Resistor Fabrication |  |  |
| 6 | Back short fabrication | AIDS/Traveller |  | Detector Assembly |  |  |
| 7 | BDA suspension assembly | AIDS/D8208 |  | BDA Assembly |  |  |
| 8 | Detector sub-assembly | AIDS/D8208 |  | BDA Assembly |  |  |
| 9 | BDA integration | AIDS/D8208 |  | BDA Assembly |  |  |
| 10 | JFET module assembly | AIDS/D8208 |  | JFET Module Assembly |  |  |
| 11 | Kapton cable assembly | AIDS/D8208 |  | Detector Assembly |  |  |
| 12 | BDA-JFET cable assembly | Purchase Order/Drawing |  | SPIRE Optical Bench |  |  |
| 13 | Back harness cable assembly | AIDS/D8208 |  | SPIRE Optical Bench |  |  |
| 14 | RF filter assembly | Purchase Order/Drawing |  | SPIRE Optical Bench |  |  |

## Electronic Parts

| Part Name | Part Number | Specification | Remarks |
| --- | --- | --- | --- |
| Surface mount resistors |  |  |  |
| JFET | U401 |  | Balanced N-channel JFET die |
| Micro D Connector | M83513/01* | Mil-C-83513 |  |
| Filter Connector | FMD-2D-1N5PM | Mil-C-83513 | Supplier Cristek |
| Jumper Connector |  |  |  |
| Nanonics connectors |  | Mil-C-83513 | Supplier Nanonics |