# SPIRE

| SUBJECT: | CDMS Simulator Data ICDCDMS Simulator Data ICD |
| --- | --- |
| PREPARED BY: | K.J. KingK.J. King |
| DOCUMENT No: | SPIRE-RAL-DOC-001196SPIRE-RAL-DOC-001196 |
| ISSUE: | Draft 2Draft 2 | Date: | 14th March 200214th March 2002 |
| APPROVED BY: |  | Date: |  |

Distribution

# Change Record

| ISSUE | DATE |  |
| --- | --- | --- |
| Draft 1 | 19th July 2001 | Original Draft |
| Draft 2 | 14th March 2002 | Update for first version of CDMS Simulator |

# Table of Contents

1.	Introduction	8

1.1	Scope	8

1.2	Structure of the Document	8

1.3	Documents	8

1.3.1	Applicable Documents	8

1.3.2	Reference Documents	9

2.	The Packet Interface	10

2.1	Packet Structures	10

2.1.1	Telecommand Packets	10

2.1.2	Telemetry Packets	10

2.2	APIDs	11

2.3	Packet Transfer Protocol	11

3.	Telecommand Packets	12

3.1	Telecommand Packet Types	12

3.2	Telecommand Packet Definition	13

3.2.1	Telecommand Verification Service	13

3.2.2	Device Command Distribution	13

3.2.3	Housekeeping and Diagnostic Data Reporting	13

3.2.4	13

3.2.5	Event Reporting	13

3.2.6	Memory Management	13

3.2.7	13

3.2.8	Function Management	13

3.2.9	Time Management	16

3.2.10	16

3.2.11	On-Board Scheduling	16

3.2.12	On-Board Monitoring	16

3.2.13	16

3.2.14	Packet Transmission Control	16

3.2.15	On-Board Storage and Retrieval	16

3.2.16	On-Board Traffic Management	16

3.2.17	Test Service	16

3.2.18	On-Board Control Procedures	16

3.2.19	Action/Event Service	17

3.2.20	Information Distribution Service	17

3.2.21	Science Data	17

3.2.22	Context Saving Service	17

4.	Telemetry Packets	18

4.1	Telemetry Packet Types	18

4.2	Telemetry Packet Definitions	19

4.2.1	TC Verification Service	19

4.2.2	Device Command Distribution	20

4.2.3	Housekeeping and Diagnostic Data Reporting	21

4.2.4	21

4.2.5	Event Reporting	22

4.2.6	Memory Management	22

4.2.7	22

4.2.8	Function Management	22

4.2.9	Time Management	23

4.2.10	23

4.2.11	On-Board Scheduling	23

4.2.12	On-Board Monitoring	23

4.2.13	23

4.2.14	Packet Transmission Control	23

4.2.15	On-Board Storage and Retrieval	23

4.2.16	23

4.2.17	Test Service	24

4.2.18	On-Board Control Procedures	24

4.2.19	Action/Event Service	24

4.2.20	Information Distribution Service	24

4.2.21	Science Data	24

4.2.22	Context Saving Service	24

5.	Parameters	25

5.1	TC Parameters	25

5.1.1	Parameter Definition	25

5.1.2	Conversion Curves	26

5.1.3	Constraints	26

5.2	TM  Parameters	27

5.2.1	Parameter Definition	27

5.2.2	Conversion Curve	28

5.2.3	Constraints	28

Figures

Tables

Table 2-1 Table of APIDs	11

Table 3-1 Telecommand Packet Types	12

Table 4-1 Telemetry Packet Types	18

Glossary

| APID | Application ID |
| --- | --- |
| DPU | Digital Processing Unit |
| OBS | On-Board Software |
| SID | Structure ID |
| SPIRE | Spectral and Photometric Imaging REceiver |
| SVM | Service Module |

# Introduction

The CDMS Simulator is used to simulate the interface of the Herschel spacecraft CDMS towards the SPIRE DPU. In this role it passes commands it receives from the SPIRE EGSE to the DPU and collects telemetry from the DPU and passes this to the other SPIRE EGSE systems. In this respect it is 'transparent ' to telecommand and telemetry packets passing between the SPIRE EGSE and the instrument. However, it is necessary in some circumstances for the EGSE to control the configuration of the CDMS Simulator and it is also required that the CDMS Simulator provide telemetry on the status of its configuration during the coarse of a test. This ICD describes how this is achieved.

All telemetry data produced by the EGSE systems will follow the same standards as is used in the Herschel Spacecraft and Ground Segment systems (this allows easier transition from the testing to the operational environments). The data is generated in the form of TM Source Packets conforming to the ESA Packet Utilisation Standards (RD01, RD02, RD03), but the set of supported packet types within the Herschel project is restricted. This restricted set is defined in the Herschel Packet Structure ICD (AD01).  The CDMS Simulator utilises a reduced set of telemetry packet types and this document details the contents of each of these.

The Operations Interface Requirements Document (AD03) defines how the units on the spacecraft  (and hence the CDMS Simulator and EGSE) interact. The CDMS Simulator meets these requirements

## Scope

This document defines the packet types and their contents that will be accepted and generated by the CDMS Simulator during Instrument -Level Testing (ILT).  These packets conform to the formats given in the Packet Structure ICD (AD01) and the Ground Segment to Instruments ICD (AD02). They also provide for the functionality described in the CDMS Simulator User Manual (RD04).

## Structure of the Document

Section 2 describes the packet interface used between  instrument and the spacecraft. This includes the general format of the packets used by the SPIRE instrument for telecommanding and telemetry  (from AD01), the allocation of Application IDs used by the instrument and the functionality of the packet  transfer protocol of the instrument/spacecraft interface (from AD01, appendix 9) that is used by the instrument.

Section 3 defines the format and content of each of the telecommand packets accepted by the CDMS Simulator. Section 4 defines the corresponding information for the telemetry packets generated by the CDMS Simulator. A description of how these packets are handled by the Simulator is given in RD04.

Section 5 defines, in detail, the parameters used in the telecommand and telemetry packets.

## Documents

### Applicable Documents

| AD01 | Herschel/Planck Packet Structure Interface Control Document (SPIRE-ESA-DOC-000433), Issue 2.0 (draft2) |
| --- | --- |
| AD02 | Herschel/Planck Operations Interface Requirements Document (SPIRE-ESA-DOC-000188), Issue 2.0 (draft3) |
| AD03 | Herschel Science Ground Segment to Instruments Interface Control Document (FIRST-FSC-DOC-0200), Issue 1.0 |
| AD04 | Packet Router ICD (SRON-G/HIFI/ICD/2001-001), Issue 1.1 |

### Reference Documents

| RD01 | Packet Telemetry Standard (ESA PSS-04-106), Issue 1, 1998 |
| --- | --- |
| RD02 | Packet Telecommand Standard (ESA PSS-04-107), Issue 2, 1992 |
| RD03 | Telemetry and Telecommand Packet Utilisation Standard (ECSS-E-70/41) Draft 04, April 1999 |
| RD04 | CDMS Simulator Users Manual, TBW |

# The Packet Interface

## Packet Structures

The following packet structures are shown as a set of 16 bit words, contained in two consecutive octets in the packet structure (all packets are composed of an even number of octets). The most significant octet of each word comes before the least significant in the packet. The least significant bit of each word is on right of each field:

|  | MS Octet | LS Octet |  |
| --- | --- | --- | --- |
| Most Significant Bit | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Least Significant Bit |

### Telecommand Packets

The following figure gives the general structure of a TC Packet (after AD01)

| Packet Header | Packet ID | 0 | 0 | 0 | 1 | 1 | APID |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | Sequence Control | 1 | 1 | Src | Count |
|  | Length | Length |
| Data Field | Data Field Header | 0 | 0 | 0 | 0 | Ack | 0 | Type |
|  |  | Sub-Type | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | Source Data |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  | D | A | T | A |  |  |  |  |  |  |
|  | Error Control | Checksum |

Src,Count, Length, TIME and Checksum are defined in AD01

Ack is the most significant 3 bits of Ack as defined in AD01

Type and Sub-Type define the packet type and are also defined in AD01

### Telemetry Packets

The following figure gives the general structure of a TM Packet (after AD01)

| Packet Header | Packet ID | 0 | 0 | 0 | 0 | 1 | APID |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | Sequence Control | 1 | 1 | Count |
|  | Length | Length |
| Data Field | Data Field Header | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Type |
|  |  | Sub-Type | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | TIME |
|  | Source Data |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  | D | A | T | A |  |  |  |  |  |  |
|  | Error Control | Checksum |

Count, Length, TIME and Checksum are defined in AD01

Type and Sub-Type define the packet type and are also defined in AD01

## APIDs

The Application ID is used to identify the source or destination of a telemetry packet. SPIRE has been allocated  APIDs for different types of packet (see AD1) as well as for EGSE equipment. The APID(s) to be used by the SPIRE CDMS Simulator are given in the following table:

| ID | Telemetry types | APID (hex) |
| --- | --- | --- |
| APID1 | Telecommands, Telecommand Verification and Events | 7F6 |
| APID2 | Periodic Housekeeping | 7F6 |
| APID3 | Science Data | 7F6 |

Table 2-1 Table of APIDs

## Packet Transfer Protocol

The packets are transferred between the CDMS Simulator and the EGSE following the Packet Router ICD.

# Telecommand Packets

This section defines all the telecommand packets accepted by the SPIRE CDMS Simulator.

## Telecommand Packet Types

The Packet Structure ICD (AD1) defines many types of service that can be provided by an Application. The following table shows the telecommand packet types that will be accepted by the SPIRE CDMS Simulator.

| Description | Service Type | Service Sub-Type | Comments |
| --- | --- | --- | --- |
| Telecommand Verification Service | 1 |  | N/A |
| Device Command Distribution | 2 |  | Not Used |
| Housekeeping and Diagnostic Data Reporting | 3 |  | Not Used |
| Event Reporting | 5 |  | N/A |
| Memory Management | 6 |  | Not Used |
| Function Management |  |  |  |
| Start Function | 8 | 1 |  |
| Stop Function | 8 | 2 |  |
| Perform Activity of Function | 8 | 4 |  |
| Report Function Status | 8 | 5 | Not Used |
| Time Management |  |  |  |
| Synchronise User | 9 | 3 | Not Used (TBC) |
| Enable Time Synchronisation | 9 | 4 | Not Used |
| Time Code | 9 | 5 | Not Used |
| Verify User Time | 9 | 6 |  |
| Enable Time Verification | 9 | 7 | Not Used |
| Synchronise Central Time Reference | 9 | 10 | Not Used |
| On-Board Scheduling | 11 |  | Not Used |
| On-Board Monitoring | 12 |  | Not Used |
| Packet Transmission Control | 14 |  | Not Used |
| On-Board Storage and Retrieval | 15 |  | Not Used |
| On-Board Traffic Management | 16 |  | Not Used |
| Test Service |  |  |  |
| Perform Connection Test | 17 | 1 |  |
| On-Board Control procedures | 18 |  | Not Used |
| Action/Event Service | 19 |  | Not Used |
| Information Distribution Service | 20 |  | Not Used |
| Science Data | 21 |  | N/A |
| Context Saving Service | 22 |  | Not Used |

Table 3-1 Telecommand Packet Types

## Telecommand Packet Definition

### Telecommand Verification Service

Not Applicable

### Device Command Distribution

Not Used

### Housekeeping and Diagnostic Data Reporting

Not Used

Not Available

### Event Reporting

Not Applicable

### Memory Management

Not Used

Not Available

### Function Management

#### Start Function (Service 8,1)

Not Used

#### Stop Function (Service 8,2)

Not Used

#### (Service 8,3)

Not Available

#### Perform an Activity of a Function (Service 8,4)

All command packets of this type and subtype may give rise to the following Errors:

| Error | TM Service | Error Code | Description |
| --- | --- | --- | --- |
| Illegal_Activity_ID | (1,2) | 0x0802 | Activity_ID not known |

##### Function 0xC1 Observations, Activity 0x01: Set Observation ID

This command sets the value for the Observation ID, which is included in all telemetry packets to allow them to be ingested into the HCSS database. This command clears the current BBID value to zero (TBC).

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 11 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| OBSID |
| Checksum |

##### Function 0xC1 Observations, Activity 0x02: Set Building Block ID

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Src | Count |
| Length = 11 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| BBID |
| Checksum |

##### Function 0xCB, CDMS Simulator, Activity 0x01: Select Buslist

Changes the Buslist being used. The change may happen immediately or at a given time. The set of Buslists available is defined in a configuration file of the CDMS Simulator.

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | 0 | 0 | 0 | Count |
| Length = 15 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| BUSLISTID |
| BLTIME |
| Checksum |

##### Function 0xCB, CDMS Simulator, Activity 0x02: Select Bus Medium

Changes the 1553 bus medium being used. The change may happen immediately or at a given time.

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | 0 | 0 | 0 | Count |
| Length = 15 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| FUNCTIONID | ACTIVITYID |
| BUSID |
| BMTIME |
| Checksum |

### Time Management

#### Verify User Time (Service 9,6)

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | 0 | 0 | 0 | Count |
| Length = 7 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 0 | 0 | 0 | 1 | 1 | APID1 |
| Checksum |

Not Available

### On-Board Scheduling

Not Used

### On-Board Monitoring

Not Used

Not Available

### Packet Transmission Control

Not Used

### On-Board Storage and Retrieval

Not Used

### On-Board Traffic Management

Not Used

### Test Service

#### Perform Connection Test (Service 17,1)

| 0 | 0 | 0 | 1 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | 0 | 0 | 0 | Count |
| Length = 5 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Checksum |

### On-Board Control Procedures

Not Used

### Action/Event Service

Not Used

### Information Distribution Service

Not Used

### Science Data

Not Applicable

### Context Saving Service

Not Used

# Telemetry Packets

This section defines all the TM packets that will be produced by the SPIRE CDMS Simulator.

## Telemetry Packet Types

The Packet Structure ICD (AD1) defines many types of service that can be provided by an Application. The following table shows the telemetry packet types that will be produced by the SPIRE CDMS Simulator.

| Description | Service Type | Service Sub-Type | Comments |
| --- | --- | --- | --- |
| Telecommand Verification Service |  |  |  |
| Telecommand Acceptance Report - Success | 1 | 1 |  |
| Telecommand Acceptance Report - Failure | 1 | 2 |  |
| Telecommand Execution Report - Started | 1 | 3 | Not Used |
| Telecommand Execution Report - Progress | 1 | 5 | Not Used |
| Telecommand Execution Report - Completed | 1 | 7 | Not Used |
| Telecommand Execution Report - Failure | 1 | 8 | Not Used |
| Telecommand Contents Report | 1 | 9 | Not Used |
| Device Command Distribution | 2 |  | N/A |
| Housekeeping and Diagnostic Data Reporting |  |  |  |
| HK Parameter Report Definitions Report | 3 | 10 | Not Used |
| Diagnostic Parameter Definitions Report | 3 | 12 | Not Used |
| Housekeeping Parameter Report | 3 | 25 |  |
| Diagnostic Parameter Report | 3 | 26 | Not Used |
| Event Reporting |  |  |  |
| Event Report | 5 | 1 | TBD |
| Exception Report | 5 | 2 | Not Used |
| Error/Alarm Report | 5 | 4 | TBD |
| Memory Management | 6 |  | Not Used |
| Function Management | 8 |  | Not Used |
| Time Management |  |  |  |
| Central Time Reference | 9 | 8 |  |
| Time Verification Report | 9 | 9 | Not Used |
| On-Board Scheduling | 11 |  | Not Used |
| On-Board Monitoring | 12 |  | Not Used |
| Packet Transmission Control | 14 |  | Not Used |
| On-Board Storage and Retrieval | 15 |  | Not Used |
| Test Service |  |  |  |
| Link Connection Report | 17 | 2 |  |
| On-Board Control procedures | 18 |  | Not Used |
| Action/Event Service | 19 |  | Not Used |
| Information Distribution Service | 20 |  | Not Used |
| Science Data |  |  |  |
| Nominal Science Data Report | 21 | 1 | Not Used |
| Science Type B Data Report | 21 | 2 | Not Used |
| Diagnostic Science Data Report | 21 | 3 | Not Used |
| Auxiliary Science Data Report | 21 | 4 | Not Used |
| Context Saving Service | 22 |  | Not Used |

Table 4-1 Telemetry Packet Types

## Telemetry Packet Definitions

### TC Verification Service

#### Telecommand Acceptance Report - Success (1,1)

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 15 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| TC_Packet_ID |
| Packet Sequence Control |
| Checksum |

#### Telecommand Acceptance Report - Failure (1,2)

The structure of this packet depends on the type of error found.

##### Packet Control Errors

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 19 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| TC_Packet_ID |
| TC_Packet_Sequence_Control |
| Failure Code |
| Parameter |
| Checksum |

##### Packet Content Error

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| TC_Packet_ID |
| Packet_Sequence_Control |
| Failure Code |
| Parameters |
| Checksum |

### Device Command Distribution

Not Applicable

### Housekeeping and Diagnostic Data Reporting

#### Housekeeping Parameter Report  (Service 3,25)

The general packet structure is shown below. The Structure ID identifies the housekeeping packet type.

| 0 | 0 | 0 | 0 | 1 | APID2 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 |
| 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| SID |
| Parameters |
| Checksum |

#### Nominal Housekeeping Report (SID=0x0301)

The following table lists the fields to be found in this report

| Location (msb) | Length (bits) | Parameter Name |
| --- | --- | --- |
| octet | bit |  |  |
| 18 | 0 | 32 | OBSID |
| 22 | 0 | 32 | BBID |
| 26 | 0 | 16 | BUSID |
| 28 | 0 | 16 | BUSLISTID |
| 30 | 0 | 32 | TCN |
| 34 | 0 | 32 | TMN |
| 38 | 0 | 16 | BUSACT |
| 40 | 0 | 16 | BUSSTAT |

Not Available

### Event Reporting

#### Event Report (5,1)

TBD

#### Exception Report (5,2)

##### RT Not Responding

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length=21 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| SID = 0x0501 |
| OBSID |
| BBID |
| RTID |
| Checksum |

Others TBD

### Memory Management

Not Used

Not Available

### Function Management

Not Used

### Time Management

#### Central Time Reference (Service 9,4)

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 17 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| CDMS Time |
| Checksum |

Not Available

### On-Board Scheduling

Not Used

### On-Board Monitoring

Not Used

Not Available

### Packet Transmission Control

Not Used

### On-Board Storage and Retrieval

Not Used

Not Available

### Test Service

#### Link Connection Report (Service 17,2)

| 0 | 0 | 0 | 0 | 1 | APID1 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Count |
| Length = 11 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| TIME |
| Checksum |

### On-Board Control Procedures

Not Used

### Action/Event Service

Not Used

### Information Distribution Service

Not Used

### Science Data

Not Used

### Context Saving Service

Not Used

# Parameters

## TC Parameters

### Parameter Definition

| Parameter Name | Service Reference | Type | Size (bits) | Conversion Curve | Constraint Table | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| ACTIVITYID | (8,4) | Integer | 8 | None | None |  |
| APID | (20,1) (20,2) | Integer | 11 | None | None | Application ID |
| BBID BBINTR BBTYPE BBCOUNT | (8,4) | Constant Integer Integer | 32 2 14 16 | None None None | None None None | Field is split into 3 parts: Location: Bits 0-1 Value: 2 Location: Bits 2-15 Location: Bits 16-31 |
| BLTIME | (8,4) | Integer | 48 | None | None | Time to change buslist (Zero = immediately) |
| BMTIME | (8,4) | Integer | 48 | None | None | Time to change bus medium (Zero = immediately) |
| BUSID | (8,4) | Integer | 16 | Bus_ID | None | Identifier of the Bus |
| BUSLISTID | (8,4) | Integer | 16 | None | None | Identifier of the Buslist |
| CRC | (6,2) | Unsigned Integer | 16 | None | None | Cyclic Redundancy Check - algorithm TBD |
| FUNCTIONID | (8,1) (8,2) (8,4) (8,5) | Integer | 8 | Func_ID | None |  |
| Length | (6,2) (6,5) (6,9) | Unsigned Integer | 16 | None | None |  |
| OBSID | (8,4) | Unsigned Integer | 32 | None | None | Observation ID |
| SID | (8,1) (8,4) (20,1) (20,2) | Unsigned Integer | 16 | None | None | Unique identifier for parameter list Values are TBD |

### Conversion Curves

| Name | Type | Raw Value | Converted Value | Comments |
| --- | --- | --- | --- | --- |
| Bus_ID | Enumerated | 0 1 | A B |  |
| Func_ID | Enumerated | 0xC1 0xCB | Obs CDMS | Observations CDMS Simulator |

### Constraints

## TM  Parameters

### Parameter Definition

| Name | Length (bits) | Conversion | Limits | Description |
| --- | --- | --- | --- | --- |
| BBID BBINTR BBTYPE BBCOUNT | 32 2 14 16 | None None None | None None None | Field is split into 3 parts: Location: Bits 0-1 Value: 2 Location: Bits 2-15 Location: Bits 16-31 |
| BUSACT | 16 | BUSACT | None | Bus Activity Status |
| BUSID | 16 | BUSID | None | Bus Identifier |
| BUSLISTID | 16 | None | None | Bus List Identifier |
| BUSSTAT | 16 | BUSSTAT | None | Bus Status |
| OBSID | 32 | None | None | Observation ID |
| RTID | 16 | RTID | None | RT Identifier |
| TCN | 32 | None | None | Number of Telecommand packets transferred to the instrument |
| TMN | 32 | None | None | Number of Telemetry packets transferred from the instrument |

### Conversion Curve

| Name | Type | Raw Value | Converted Value | Units | Comments |
| --- | --- | --- | --- | --- | --- |
| BUSACT | Enumerated | 0 1 | DEAD ALIVE |  |  |
| BUSID | Enumerated | 0 1 | A B |  |  |
| BUSSTAT | Enumerated | 0 1 | STOPPED RUNNING |  |  |
| RTID | Enumerated | 0 1 2 | TBD |  | The RTID identifies the instrument (or subsystem) |

### Constraints

# Text boxes

| Parameter | Type | Value |
| --- | --- | --- |

| Parameter | Comment |
| --- | --- |
| RTID | Number of RT affected |

| SID | Packet type | Default Frequency (msec) |
| --- | --- | --- |
| 0x0301 | Nominal Housekeeping Report | 1000 |

Parameters

| Name | Value and Comments |
| --- | --- |
| FUNCTIONID | 0xC1 |
| ACTIVITYID | 0x02 |
| BBID | Building Block ID (32 bits) |

| Parameter | Value and Comments |
| --- | --- |
| FUNCTIONID | 0xCB |
| ACTIVITYID | 0x01 |
| BUSLISTID | Buslist ID (16 bits) |
| BLTIME | Time at which to change the Buslist (Zero means immediately) |

| Error | Failure Code | Parameters |
| --- | --- | --- |
| Illegal or inconsistent Application Data | 5 | See Note |
| Other TBD errors | 16-255 | See Note |
| Illegal_Function_ID | 0x0801 | See Note |
| Illegal_Activity_ID | 0x0802 | See Note |

Note: The parameters for each error are TBD, but as a suggestion this field should contain the first 20 words from the 'source data' field of the received telecommand packet, unless this field is less than 20 words in length, in which case all words from the 'source data' field will be included.

| Parameter | Value and Comments |
| --- | --- |
| FUNCTIONID | 0xCB |
| ACTIVITYID | 0x02 |
| BUSID | Bus Medium ID |
| BUSTIME | Time at which to change the Bus Medium (Zero means immediately) |

| Parameter | Type | Value |
| --- | --- | --- |

| Error | Failure Code | Parameter |
| --- | --- | --- |
| Illegal APID | 0 | TC_Packet_APID |
| Incomplete Packet or invalid Length | 1 | TC_Packet_Length |
| Incorrect Checksum | 2 | TC_Packet_Checksum |
| Illegal Packet Type | 3 | TC_Packet_Type |
| Illegal Packet Sub-Type | 4 | TC_Packet_Sub-Type |

Note: The parameter is placed in the least significant bits of the16 bit 'parameter'  field and the most significant bits are padded with zeros

Parameters

| Name | Value and Comments |
| --- | --- |
| FUNCTIONID | 0xC1 |
| ACTIVITYID | 0x01 |
| BBID | Observation ID (32 bits) |