Work Package:	Detectors and Cold Electronics                         SPIRE-JPL-REP-001213

| 1. Subsystem Progress Since Project Inception |
| --- |
| Subsystem has progressed through the CDR stage successfully this summer. We have received approval for moving forward into the implementation phase. Action items from the CDR will be addressed individually and closed out thorough memos distributed to the originators and the project files. We are in the process of building our CQM and STM hardware. |
| 2. Subsystem Progress This Month |
| Completed PLW array lithography. Lost our JFET fabrication engineer (left JPL). We have embarked on the process of training a new one. Began assembly of the QM BDA. We have received the Thermal Cycle Dewar and are in the process of installing it. Finished 4K measurements of the load resistor module successfully. |
| 3. Problem Areas | Remedial Action |
| We have found it necessary to modify the design of the capstan which is used to preload and secure the kevlar suspension bands. Although the kevlar is being pretensioned, the final adjustment length needed is longer than expected. | Redesigned capstan to be installed. A design review is scheduled to cover this and some other minor changes to the BDA design. This review will take place on the 25th of February. |
| 4. Engineering Activities |
| 5. Design Changes |
| As described above. |
| 6. PA/QA Activities |
| Completed the FMECA. |
| 7. Subsystem Management Issues |
| None |
| 8. Actions Requiring Immediate Attention |
| ICD for wiring harness is critical. |
| 9. Status of Previous Actions |
| None |
| 10. Activities Yet to be Achieved |
| Completion of the assembly of the first BDA units (QM and CQM). |
| 11. Milestones | Status |
| March 1, 02 | QM BDA Assembled |  |
| 13. Schedule Changes |
| Pending with objective being no changes to delivery schedule. |

This technical data is export controlled under U.S. law and is being transferred by JPL to PPARC pursuant to the NASA / PPARC Letter of Agreement which entered into force on December 2, 1999.  This technical data is transferred to PPARC for use exclusively on the NASA/PPARC SPIRE on FIRST cooperative project, may not be used for any other purpose, and shall not be re-transferred or disclosed to any other party without the prior written approval of NASA.